SG Network System Requirements Specification

UCAiug

Mm/dd/yyyy

Document History

Revision History

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 1.01 |  |  | Documented shell created | n |
| 1.02 | 2/16/10 | MKG | Result from 2/16/10 conference call | n |

Preface

Authors

The following individuals and their companies are members of the OpenSG SG-Network Task Force Core Development Team and contributed substantially to the drafting of the SG-Network System Requirement Specification:

Ron Cunningham, American Electric Power

Matt Gillmore, Consumers Energy

Bill Godwin, Progress Energy

Michael Northern, Deloitte Consulting LLP

Don Sturek, Pacific Gas & Electric

Vincent Bemmel, Trilliant

Paul Duffy, Cisco

Claudio Lima, Sonoma Innovations

Bill Leslie, Longboard Technologies

Jerry Armes, Micronet Communications

Gary Stuebing, Duke Energy

Acronyms and Abbreviations

| Aggregation | Practice of summarizing certain data and presenting it as a total without any PII identifiers |
| --- | --- |
| AMI | Advanced Metering Infrastructure |
| AMS | Asset management system |
| Anonymize | A process of transformation or elimination of PII for purposes of sharing data |
| ASAP-SG | Advanced Security Acceleration Project-Smart Grid |
| B2B | Business to Business |
| BAN | Business Area Network |
| CIM | Common Information Model. A structured set of definitions that allow different Smart Grid domain representatives to communicate important concepts and exchange information easily and effectively. |
| CIP | Critical Infrastructure Protection |
| CSWG | Cyber Security Working Group |
| DA | Distribution Automation |
| De-identify | A form of anonymization that does not attempt to control the data once it has had PII identifiers removed, so it is at risk of re-identification. |
| DER | Distributed Energy Resources |
| DHS | Department of Homeland Security |
| DMS | Distribution Management System |
| DNP | Distributed Network Protocol |
| DOE | Department of Energy |
| DOMA | Distribution Operations Model and Analysis |
| DR | Demand Response |
| DSDR | Distribution Systems Demand Response |
| DSM | Demand Side Management |
| EMS | Energy management system |
| EPRI | Electric Power Research Institute |
| ES | Electric Storage |
| ESB | Enterprise service bus |
| ESI | Energy Services Interface |
| ET | Electric Transportation |
| EUMD | End Use Measurement Device |
| EV/PHEV | Electric Vehicle/Plug-in Hybrid Electric Vehicles. Cars or other vehicles that draw electricity from batteries to power an electric motor. PHEVs also contain an internal combustion engine. |
| EVSE | Electric Vehicle Service Element |
| FERC | Federal Energy Regulatory Commission |
| FIPS | Federal Information Processing Standard Document |
| FLIR | Fault Location, Isolation, Restoration |
| G&T | Generations and Transmission |
| GAPP | Generally Accepted Privacy Principles. Privacy principles and criteria developed and updated by the AICPA and Canadian Institute of Chartered Accountants to assist organizations in the design and implementation of sound privacy practices and policies. |
| GIS | Geographic Information System |
| GPRS | General Packet Radio Service |
| HAN | Home Area Network. A network of energy management devices, digital consumer electronics, signal-controlled or enabled appliances, and applications within a home environment that is on the home side of the electric meter. |
| HMI | Human-Machine Interface |
| I2G | Industry to Grid |
| IEC | International Electrotechnical Commission |
| IED | Intelligent Electronic Device |
| ISA | International Society of Automation |
| ISO | Independent System Operator |
| ISO/IEC27001 | International Organization for Standardization/International Electrotechnical Commission Standard 27001. A auditable international standard that specifies the requirements for establishing, implementing, operating, monitoring, reviewing, maintaining and improving a documented Information Security Management System within the context of the organization's overall business risks. It uses a process approach for protection of critical information. |
| IT | Information Technology |
| LAN | Local Area Network |
| LMS | Load management system |
| LMS/DRMS | Load Management System/ Distribution Resource Management System |
| MDMS | Meter Data Management System |
| MFR | Multi-Feeder Reconnection |
| MSW | Meter service switch |
| NERC | North American Electric Reliability Corporation |
| NIPP | National Infrastructure Protection Plan |
| NIST | National Institute of Standards and Technology |
| NISTIR | NIST Interagency Report |
| NMS | Network management system |
| OECD | Organization for Economic Cooperation and Development. A global governmental forum of 30+ market democracies for comparison of policy experiences, good practices, and coordination of domestic and international policies. It is one of the world’s largest and most reliable sources of comparable statistical, economic and social data. |
| OMS | Outage Management System |
| OWASP | Open Web Application Security Project |
| PAP | NIST Smart Grid interoperability Priority Action Plan |
| Personal Information | Information that reveals details, either explicitly or implicitly, about a specific individual’s household dwelling or other type of premises. This is expanded beyond the normal "individual" component because there are serious privacy impacts for all individuals living in one dwelling or premise. This can include items such as energy use patterns or other types of activities. The pattern can become unique to a household or premises just as a fingerprint or DNA is unique to an individual. |
| PEV | Plug-In Electric Vehicle |
| PI | Process Information |
| PIA | Privacy Impact Assessment. A process used to evaluate the possible privacy risks to personal information, in all forms, collected, transmitted, shared, stored, disposed of, and accessed in any other way, along with the mitigation of those risks at the beginning of and throughout the life cycle of the associated process, program or system. |
| PII | Personally Identifying Information |
| R&D | Research and Development |
| RTO | Regional Transmission Operator |
| RTU | Remote Terminal Unit |
| SCADA | Supervisory Control and Data Acquisition |
| SGIP | Smart Grid Interoperability Panel |
| SGIP-CSWG | SGIP – Cyber Security Working Group |
| SP | Special Publication |
| SSP | Sector-specific Plans |
| T/FLA | Three/Four Letter Acronym |
| VVWS | Volt-VAR-Watt System |
| WAMS | Wide-Area Measurement System |
| WAN | Wide Area Network |
| WASA | Wide Area Situational Awareness |
| WLAN | Wireless Local Area Network |
| WMS | Work Management System |

| MDMS | AMS | EMS | DSM | Event / OMS | DMS | LMS | SCADA | GIS | NMS | Head End | CIS | CIS |  |  |  |  |  |  |  | DAP | Meter Meter | Meter NIC | ESI | Meter SW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Definitions

Asset Management System – A system(s) of record for assets managed in the Smart Grid.  Management context may change(e.g. financial, network)

Capacitor Bank – This is a device used to add capacitance as needed at strategic points in a distribution grid to better control and manage VARs and thus the Power Factor and they will also affect voltage levels.

Distribution Systems Demand Response – A system used to reduce load during peak demand.  Strictly used for Distribution systems only.

Data Aggregation Point – This device is a logical actor that represents a transition in most AMI networks between Wide Area Networks and Neighborhood Area Networks.  (e.g. Collector, Cell Relay, Base Station, Access Point, etc)

Distribution Management System – A system that monitors, manages and controls the electric distribution system.

Demand Side Management – A system that co-ordinates demand response / load shedding messages indirectly to devices (e.g. Set point adjustment)

Field Force – Employee working in the service territory that may working Smart Grid devices.

Energy Services Interface – Provides security and, often, coordination functions that enable secure interactions between relevant Home Area Network Devices and the Utility.  Permits applications such as remote load control, monitoring and control of distributed generation, in-home display of customer usage, reading of non-energy meters, and integration with building management systems.  Also provides auditing/logging functions that record transactions to and from Home Area Networking Devices.

Voltage Regulator – This device is in effect an adjustable ratio transformer positioned at strategic points in a distribution grid and is utilized to better manage and control the voltage as it changes along the distribution feeder.

Medium Voltage Sensor – A device used to measure and report electrical properties (such as voltage, current, phase angle or power factor, etc.) on a medium voltage distribution line.

Last Gasp – Concept of an energized device within the Smart Grid detecting power loss and sending a broadcast message of the event.

Load Management System – System that controls load by sending messages directly to device (e.g. On/Off)

Low Voltage Sensor – A device used to measure and report electrical properties (such as voltage, current, phase angle or power factor, etc.) at a low voltage customer delivery point.

Network Management System – A system that manages Fault, Configuration, Auditing/Accounting, Performance and Security of the communication.  This system is exclusive from the electrical network.

Recloser (non-Team) – A device used to sense fault conditions on a distribution line and trip open to provide protection.  It is typically programmed to automatically close (re-close) after a period of time to test if the fault has cleared.  After several attempts of reclosing it can be programmed to trip open and stop trying to reclose until reset either locally or under remote control.

Recloser (Team) – A device that can sense fault conditions on a distribution line and to communicate with other related reclosers (the team) to sectionalize the fault and provide a coordinated open/close arrangement to minimize the effect of the fault.

Motorized Switch – A device under remote control that can be used to open or close a circuit.

Fault Detector – A device used to sense a fault condition and can be used to provide in indication of the fault.

Intelligent Fault Detector – A device that can sense a fault and can provide more detailed information on the nature of the fault, such as capturing an oscillography trace.

Phase Measuring Unit – A device capable of measuring the phase of the voltage or current waveform relative to a reference.

Outage Management System – A system that receives out power system outage notifications and correlates where the power outage occurred

Regional Transmission Operator – RON

Transformer (MV-to-LV) – A standard point of delivery transformer.  In the Smart Grid context is it assumed there will be a need to measure some electrical or physical characteristics of this transformer such as voltage (high and/or low side) current, MV load, temperature, etc.

Common Web Portal – Web interface for Regional Transmission Operator, customers, retail electric providers and transmission distribution service provider to function as a clearing house for energy information.  Common used in deregulated markets.

Web Portal – Interface between energy customers and the system provider.  Could be the utility or third party

Aggregator – SEE FERC OPERATION MODEL

Sub Meter – Premise based meter used for Distributed Energy Resources and PHEV.  This device may be revenue grade.

Programmable Communicating Thermostat – A device within the premise that has communication capabilities and controls heating, ventilation and cooling systems.

Substation Controller – Distributed processing device that has supervisory control or coordinates information exchanges from devices within a substation from a head end system.

Data Collector – See Substation Controller

Neighborhood Area Network – Also called FAN.  A network comprised of all communicating components within a distribution domain.

Enterprise Service Bus – Enterprise service bus (ESB) consists of a software architecture used to construct integration services for complex event-driven and standards-based messaging to exchange meter or grid data. The ESB is not limited to a specific tool set rather it is a defined set of integration services.

Remote Terminal Unit – Aggregator of multiple serialized devices to a common communications interface

VAR – Volt-Amperes Reactive; – In an AC power system the voltage and current measured at a point along the delivery system will often be out of phase with each other as a result the combined effects of the resistive and reactive (i.e. the capacitance and inductive) characteristics of the delivery system components and the load.  The phase angle difference at a point along the delivery system is an indication of how well the inductive and capacitive effects are balanced at that point.  The real power passing that point is the product of the magnitude of the Voltage and Current and the Cosine of the angle between the two.  The VAR parameter is the product of the magnitude of the Voltage and Current and the Sine of the angle between the two.  The magnitude of the VAR parameter is an indication of the phase imbalance between the voltage and current waveforms.

Power Factor – A quantity that relates to efficiency of the electrical delivery system for delivering real power to the load.  Numerically, it is the Cosine of the phase angle between the voltage and current waveforms.  The closer the power factor is to unity the better the inductive and capacitive elements of the circuit are balanced and the more efficient the system is for delivering real power to the load(s).

SG-Network Requirements Gathering process

The SG-Network task force derived functional requirements from the following process:

- Listing of pertinent use cases

- Identification of Actors within use cases

- Gap analysis by mapping actors to use cases

- Defining Functional Requirements

  - Requirement actor to actor

  - Estimated payload

  - Expected latency

  - Expected Reliability

  - Security Requirements

    - Low, Medium, High per NISTIR 7628

  - Implications of failure

- Architectural reference diagram

  - Illustrative diagram of requirements

Architecture Reference Model

Requirements

References