DRAFT Proposed Content updates to Section 3 (as input from SG-Network, Ron Cunningham’s revisions) based on the ref document http://collaborate.nist.gov/twiki-sggrid/pub/SmartGrid/PAP02Wireless/NIST_Priotity_Action_Plan_2_r04.pdf

The specific sections or portions of section 3 being updated are highlighted in yellow in the 6 page extraction “NIST_Priotity_Action_Plan_2_r04-sect3markups.pdf” from that base pdf document above.

- - - - - - - - - - - - - - - - - - - - - - -- - - - - - - -- - - - - -- - -- - - - -- - -- - - -- - - - - -- -

3 Smart Grid Conceptual Model and Business Functional Requirements

This section includes several sets of information that attempts to provide an overview of the major set of Smart Grid business functional domains, actors, interfaces and separately detailed business functional and volumetric requirements with a focus on documenting and quantifying the application payloads that may traverse a Smart Grid deployment.

3.1 Smart Grid Conceptual Reference Diagrams

In this section a few illustrative diagrams are included to help the reader of this document understand the content. Links to these files are also provided.

Figure 1 – Smart Grid Conceptual Reference Diagram

Figure 2 – OpenSG_SG Network TF Smart Grid Conceptual Reference Diagram

The latest set of OpenSG_SG Communications_SG Network Task Force reference diagrams are located at

http://osgug.ucaiug.org/UtiliComm/Shared%20Documents/Latest_Release_Deliverables/Diagrams/

3.2 List of Actors

The table below maps the actors included in the SG Network Task Force reference diagram Figure 2 and the NIST reference diagram Figure1. The SG Network Task Force high level list of actors are further qualified by domain and sub-domain as used in documenting the Smart Grid business functional and volumetric requirements.

| SG Network Reference Diagram Descriptor (Actor) | SG Network Ref Diagram Domain Name | Related NIST Diagram Descriptor (Actor) |
| --- | --- | --- |
| Field Tools |  |  |
| Generators | Bulk Generation | Generators |
| Market Services Interface | Bulk Generation | Market Services Interface |
| Plant Control Systems | Bulk Generation | Plant Control Systems |
|  | Customer | Electric Storage |
| Customer EMS | Customer | Customer EMS |
| DERs (Solar, Wind, premise generation sources) | Customer | Distributed Generation |
| ESI (Broadband) | Customer | Energy Services Interface |
| ESI (In Meter) | Customer | Energy Services Interface |
| EVSE / EUMD | Customer | Customer Equipment |
| HVAC | Customer | Customer Equipment |
| IHD (In Home Device) | Customer | Customer Equipment |
| Load Control Device | Customer | Customer Equipment |
| PCT | Customer | Thermostat |
| PHEV | Customer | Electric Vehicle |
| Phone/Email/Txt/Web | Customer | Customer Equipment |
| Smart Appliances | Customer | Appliances |
| Smart Meter | Customer | Meter |
| Sub-Meter | Customer | Customer Equipment |
| Two Way Meter | Customer | Meter |
| Capacitor Bank | Distribution | Field Device |
| Circuit Breaker | Distribution | Field Device |
| Recloser | Distribution | Field Device |
| Sectionalizer | Distribution | Field Device |
| Switch | Distribution | Field Device |
| Voltage Regulator | Distribution | Field Device |
| DAC (Distributed Application Controller) | Distribution / Transmission | Substation Controller |
| Distributed Generation | Distribution / Transmission | Distributed Generation |
| Distributed Storage (Substation to 4-6 residential customer per size) | Distribution / Transmission | Storage System |
| FAN Gateway | Distribution / Transmission |  |
| Field Sensors | Distribution / Transmission | Field Device |
| RTU | Distribution / Transmission | Data Collector |
| Substation Devices | Distribution / Transmission | Substation Device |
| Energy Market Clearinghouse | Markets | Energy Market Clearinghouse |
| Retailer/Wholesaler | Markets | Aggregator/Retail Energy Provider |
| RTO/ISO | Markets | RTO/ISO |
| Aggregator | Markets / Service Providers | Aggregator |
|  | Operations | Asset Mgmt |
|  | Operations | WAMS |
| AMI Head-End | Operations | Metering System |
| Analytic DB | Operations |  |
| Distr. SCADA FEP | Operations | Distr. SCADA |
| DSM | Operations | Demand Response |
| EMS | Operations | Utility EMS |
| Event/OMS | Operations |  |
| GIS | Operations |  |
| GL / Accts Payable / Receivable | Operations |  |
| LMS | Operations |  |
| MDMS | Operations | MDMS |
| NMS | Operations |  |
| RTO SCADA | Operations | RTO SCADA |
| Trans. SCADA FEP | Operations | Trans. SCADA FEP |
| Utility DMS | Operations | DMS |
| Utility EMS | Operations | EMS |
| Work Management System | Operations |  |
| Bill Payment Orgs/Banks | Service Provider | Other |
| Common Web Portal-Jurisdictional | Service Provider | Other |
| Home/Building Manager | Service Provider | Home/Building Manager |
| Internet/Extranet Gateway | Service Provider |  |
| ODW | Service Provider |  |
| REP CIS/Billing | Service Provider | Retail Energy Providers Billing |
| REP CIS/Billing | Service Provider | Retail Energy Providers CIS |
| Utility CIS/Billing | Service Provider | Utility CIS |
| Utility CIS/Billing | Service Provider | Utility Billing |
| Web Portal | Service Provider |  |

3.3 Smart Grid Use Cases

From the Interoperability Knowledge Base (IKB)

http://collaborate.nist.gov/twikisggrid/in/view/SmartGrid/InteroperabilityKnowledgeBase#Use_Cases

Use Cases come in many shapes and sizes. With respect to the IKB, fairly comprehensive Use Case descriptions are used to expose functional requirements for applications of the Smart Grid. In order to provide this depth, these Use Cases contain the following:

Narrative -- a description in prose of the application represented including all important details and participants described in the context of their activities.

Actors -- identification of all the persons, devices, subsystems, software applications that collaborate to make the Use Case work

Information Objects -- defines the specific aggregates of information exchanged between Actors to implement the Use Case

Activities/Services -- description of the activities and services this Use Case relies on or implements

Contracts/Regulations -- what contractual or regulatory constraints govern this Use Case

Steps -- the step by step sequence of activities and messaging exchanges required to implement the Use Case

http://collaborate.nist.gov/twiki-sggrid/bin/view/SmartGrid/IKBUseCases

Contains use cases following this description

SG-Network Task Force performed an exercise to research and list all pertinent use cases that involve network communication to help satisfy the OpenSG input requirements into the NIST PAP 2 tasks.  Use cases from several sources e.g. Southern California Edison Use Cases, Grid Wise Architectural Console use cases, EPRI and others were researched. The following table summarizes the use cases SG-Network Task Force has currently in scope for this work effort

| Smart Grid Use Case | Requirements in Release 4.0 of the Requirements Table, Or Planned for later Release |
| --- | --- |
| Accounting Mgmt | Yes |
| Configuration mgmt | Yes |
| Direct Load Control | Yes |
| Distributed Storage | Yes |
| DSDR - Centralized Control | Yes |
| Fault Clear Isolation Reconfigure | Yes |
| Fault mgmt | Yes |
| Meter Events | Yes |
| Meter Read | Yes |
| Pre-Pay Metering | Yes |
| Service Switch | Yes |
| Customer Info / Messaging | Partial |
| Demand Response | Partial |
| Distribution automation support | Partial |
| Outage Restoration Mgmt | Partial |
| PHEV | Partial |
| Premise Network Admin | Partial |
| Security mgmt | Partial |
| System updates | Partial |
| Volt/VAR Management | Partial |
| Distributed GEN | Planned |
| Field Force tools | Planned |
| Performance Mgmt | Planned |
| Pricing TOU / RTP/ CPP | Planned |
| Transmission automation support | Planned |

The current released version of the System Requirements Specification (SRS) document is located at

http://osgug.ucaiug.org/UtiliComm/Shared%20Documents/Latest_Release_Deliverables/

in the file named “SG Network System Requirements Specification v3.doc”

The textual SRS documents follow more the previously discussed use case documentation efforts, but include summarization of the network and volumetric requirements as discussed in section 3.4. Future releases of this SRS document will be posted as SG-Network Task Force continues it’s documentation efforts. A release 4 of the SRS is currently being created.

3.4 Smart Grid Business Functional and Volumetric Requirements

There are many smart grid user applications (use cases). Many have text describing the user applications (see IKB) , but few contain quantitative requirements, which are necessary to design communications protocols or assess or plan communication networks. OpenSG_SG Communications_SG Network Task Force took on the task to document the Smart Grid business functional and volumetric requirements for input into the NIST PAP 2 tasks and to help fill this requirements void. The current SG-Network business functional and volumetric requirements are located at

http://osgug.ucaiug.org/UtiliComm/Shared%20Documents/Latest_Release_Deliverables/

in the file named “SG Network System Requirements Specification v4.0.xls”

The document referenced below, was prepared for the requirement authors, but also can be used by the consumer of the Requirements Table to better understand what is and is not included and how to interpret that data.

http://osgug.ucaiug.org/UtiliComm/Shared%20Documents/Latest_Release_Deliverables/

in the file named “rqmts-documentation-instructions-r1.1.doc”

The Requirement Table consists of several major sets of information by use case:

- Use case business functional requirement statements are documented as individual information flows e.g. specific application payload requirement sets. This is comparable to what many use case tools capture as information flows and/or sequence diagram flows.

- To the baseline business requirements were added the:

  - volumetric attributes (the when, how often, with what availability, latency, application payload size)

  - an assignment of the security confidentiality, integrity, availability needs for that application payload

- Payload requirement sets, which are grouped rows in the table that contain all the detailed actor to actor passing of the same application payloads in a sequence that follows the main data flow from that payloads originating actor to primary consuming actor(s) across multiple communication paths that a deployment might use. The payload requirements sets will always contain a parent (main) actor to actor row and most will contain child (detailed) rows for that requirement set.

- Payload communication path (information or data flow) alternatives that a given smart grid deployment might use.

To effectively use the business functional and volumetric requirements, the consumer (user) of the Requirements Table must:

- select which use cases and payloads are to be included

- select which communication path scenario (alternative) is to be used for each of the main information/data flows from originating actor to target consuming actor

- specify the size (quantity and type of devices) of the smart grid deployment

- perform other tweaks to the payload volumetrics to match that smart grid deployments’ needs

The current Requirements Table as a spreadsheet is not very conducive to performing these tasks. SG-Network Task Force is building a database that will be made available to assist in performing several of the tasks mentioned above. When finalized, it will be made available for use.

The process of requirements gathering has been evolutionary in nature.  The SG Network Task Force has defined over 1400 (as of release 4.0) functional and volumetric requirements while reviewing the use cases listed above. The group intends to continue to release versions of requirements over time in order to keep scope and focus attainable yet giving consumers of this information something to work with and provide feed back.

3.4.1 Smart Grid User Applications’ Quantitative Requirements

An earlier release of the Requirements Table e.g. “SG Network System Requirements Specification v2.1 (March 12, 2010), contained sufficient data for consideration as a partial list of Smart Grid user applications’ quantitative requirements to PAP 2. This version contained three user applications: meter reading, PHEV, and service switching along with their quantitative requirements.

Subsequent releases of the Requirements Table from SG-Network have also be made available to PAP 2 for their use.