## Distributed Customer Storage

### Overview

The Distributed Customer Storage use cases focus on the function and role of the electric grid storage devices that are those deployed along distribution feeder circuits/laterals for the purposes of: peak load shaving, voltage support, power quality, demand control, interruption protection on a specific Distribution feeder circuit and/or specific clusters of customers served by that feeder circuit versus the larger capacity Distributed Storage devices co-located with distribution substations which is a different use case. There are three main scenarios described in this section:

- Dispatch Distributed Customer Storage

- Islanded Distribution Customer Storage

- Capped Customer Energy Usage

For each scenario, the currently documented payload business application requirements are described. Prior to the scenario descriptions, the Reference Architecture and Possible Communication Paths diagrams and Actors list are provided from which each of the scenarios are subsets.

#### Reference Architecture with Domains, Actors and Interfaces

#### Possible communication paths

### Actors

| Actor | Description |
| --- | --- |
| 2-Way Meter - Electr | A bi-directional communication device used to perform measurement of electrical energy usage for residential use. |
| AMI Head-End(j) | The AMI head end is responsible for the operation and coordination of AMI system components. It represents the central nervous system of the AMI system. The “(j) qualifier indicates that there may be multiple vendor implementations in the utility’s operations. |
| Analytic DB | A database used in Operations that contains the detailed electrical grid device(s) state and measured values for further engineering analysis and/or application use. |
| Cust. EMS | A customer owned energy management system used to manage energy with a premises. |
| DAC - Ops/Regnl | Distribution Application Control system hosted in either the Utilities Operations or Regional Data Centers to run a specific Distribution application |
| DAC – sub | Distribution Application Control system hosted in a Distribution Substation to run a specific Distribution application |
| DAPjm | This device is a network gateway logical actor between Wide Area Networks and the Neighborhood Area Networks. (e.g. Collector, Cell Relay, Base Station, Access Point, etc) that make up the “AMI Network” or “Field Area Network”. The “jm” qualifier indicates that there may be multiple vendor implementations of AMI Head-End(J) in the utility’s operations with the associated DAPs. The “m” qualifier indicates the m`th occurrence of the DAP on AMI Network managing the network traffic for a specific geography of the network. |
| Distr. Cust. Storage | Distributed Customer Storage is a storage device sized to meet typical distribution substation circuit loads and is typically located at or near a distribution substation or in smaller capacities out in customer/premise neighborhoods |
| Distr. SCADA FEP | Distribution Supervisory Control and Data Acquisition Front End Processor |
| DMS | Distribution Management System - A system that monitors, manages and controls the electric distribution system. |
| ESI - 3rd Party | An ESI, owned by the Customer and not provided by the Utility, which enables secure interactions between HAN Devices Registered on its network and the service provider e.g. REP. The 3rd Party ESI functionality may reside in the Customer EMS or customer's |
| ESI - In Meter | An ESI, owned by the Utility and resides in the Utility meter, which enables secure interactions between HAN Devices Registered on its network and the Utility AMI. |
| ESI - Utility | An ESI, owned by the Utility, which enables secure interactions between HAN Devices Registered on its network and the Utility AMI. The Utility ESI functionality may reside in the Customer EMS or customer broadband router. |
| FAN gateway - field | Field Area Network gateway device located in the field, that provides the interface between the Feeder Line device communication modules and the Wide Area Network connection. |
| FAN gateway - sub | Field Area Network gateway device located in the substation, that provides the interface between the Feeder Line device communication modules and the Substation network connection. |
| Feeder Circuit Breaker | A device used in the substation that is used per a specific configuration to protect distribution equipment. |
| Internet / Extranet gateway(s) - Utility | These are gateways used to connect internal utility networks with external networks. |
| IPD | In Premise Display |
| LMS – Utility | Load management system - System that controls load by sending messages directly to device (e.g. On/Off) |
| MDMS | The application responsible for the collection and retrieval of all relevant customer information for purposes of billing and facilitating interaction. |
| OMS | A system that receives power system outage notifications and correlates the geographic location of the power outage |
| RTU | Remote Terminal Unit - Aggregator of multiple serialized devices to a common communications interface |

### Scenarios

#### Scenario: 	Dispatch Distributed Customer Storage

Narrative

The Utility has need to provide for any combination of: peak load shaving, voltage support, power quality, demand control on a specific Distribution feeder circuit and/or specific clusters of customers served by that feeder circuit. This scenario includes both the discharge of the Distributed Customer Storage devices to accomplish the needs above and to charge the Distributed Customer Storage devices after their discharge. The DAC is the actor carrying out these functions as directed and programmed by Distribution Operations.

Business Objectives

| Originating Actor | Destination Actor | Latency | Reliability | Payload Size - bytes | Payload Name |
| --- | --- | --- | --- | --- | --- |
| DAC - sub | Feeder Circuit Breaker | < 2 sec | > 99.5% | 25 | circuit-brk_device_status_cmd |
| Feeder Circuit Breaker | DAC - sub | < 2 sec | > 99.5% | 50 | circuit-brk_status_resp-data |
| Sub-Totals | < 4 sec | > 99% | 75 |  |
| DAC - sub | Distr. Cust. Storage | < 5 sec | > 99.5% | 25 | distr_cust_storage_status_cmd |
| Distr. Cust. Storage | DAC - sub | < 5 sec | > 99.5% | 50 | distr_cust_storage_status_resp-data |
| Sub-Totals | < 10 sec | > 99% | 75 |  |
| DAC - sub | DAC - Ops/Regnl, DMS, Analytic DB | < 4 sec | > 99.5% | 50 | distr_cust_storage_status_resp-data |
| DAC - sub | Distr. Cust. Storage | < 5 sec | > 99.5% | 25 | distr_cust_storage_discharge_cmd |
| Distr. Cust. Storage | DAC - sub | < 5 sec | > 99.5% | 25 | distr_cust_storage_discharge_cmd_ack |
| Sub-Totals | < 10 sec | > 99% | 50 |  |
| DAC - sub | Distr. Cust. Storage | < 5 sec | > 99.5% | 25 | distr_cust_storage_charge-rate_cmd |
| Distr. Cust. Storage | DAC - sub | < 5 sec | > 99.5% | 25 | distr_cust_storage_charge-rate_cmd_ack |
| Sub-Totals | < 10 sec | > 99% | 50 |  |

Implications and Rationale

| Functional Domain | Expected Potential Impact | Rationale |
| --- | --- | --- |
| Bulk Generation |  |  |
| Customer |  |  |
| Distribution | X | Missed or inaccurate information about the state of the circuits and the Distr Customer Storage devices may lead to missed opportunities to improve the circuit and customer electric service objectives OR potential harm to feeder circuits and devices |
| Markets |  |  |
| Operation | X | Missed or inaccurate information about the state of the circuits and the Distr Customer Storage devices may lead to missed opportunities to improve the circuit and customer electric service objectives from other Distribution Applications or Operations |
| Service Providers |  |  |
| Transmission |  |  |

#### Scenario: 	Islanded Distributed Customer Storage

Narrative

This scenario covers the situation where power has been lost to the portion of a feeder circuit that has attached Distributed Customer Service devices that can provide for temporary finite amount of power for a limited amount of time. This scenario is also premised on a close affinity between the customer loads that can be sourced from the deployed Distributed Customer Storage devices and the 2-way Meter – Electr.

Business Objectives

| Originating Actor | Destination Actor | Latency | Reliability | Payload Size - bytes | Payload Name |
| --- | --- | --- | --- | --- | --- |
| Distr. Cust. Storage | DAC - sub, Distr. SCADA FEP | < 8 sec | > 99.5% | 50 | distr_cust_storage_in-island-mode_alarm |
| Distr. SCADA FEP | DAC - Ops/Regnl, DMS, OMS, Analytic DB | < 4 sec | > 99.5% | 50 | distr_cust_storage_in-island-mode_alarm |
| Distr. Cust. Storage, DAC - Ops/Regnl | LMS - Utility | < 6 sec | > 98% | 50 | distr_cust_storage_in-island-mode_alarm |
| LMS - Utility | IPD, Cust. EMS, MDMS | < 12 sec | > 98% | 50 - 150 | on_distr-cust-strg_alarm |
| Sub-Totals | < 22 sec | > 96% | 100 - 200 |  |
| Distr. Cust. Storage | DAC - sub, Distr. SCADA FEP | < 8 sec | > 99.5% | 50 | distr_cust_storage_out-of-island-mode_alert |
| Distr. SCADA FEP | DAC - Ops/Regnl, DMS, OMS, Analytic DB | < 4 sec | > 99.5% | 50 | distr_cust_storage_out-of-island-mode_alert |
| Distr. Cust. Storage, DAC - Ops/Regnl | LMS - Utility | < 6 sec | > 98% | 50 | distr_cust_storage_out-of-island-mode_alert |
| LMS - Utility | IPD, Cust. EMS, MDMS | < 12 sec | > 98% | 50 - 150 | off_distr_cust_strg_alert1 |
| Sub-Totals | < 22 sec | > 96% | 100 - 200 |  |

Implications and Rationale

| Functional Domain | Expected Potential Impact | Rationale |
| --- | --- | --- |
| Bulk Generation |  |  |
| Customer | X | Missed or inaccurate information about the state of available energy available, may lead to additional customer complaints separate from a complete outage |
| Distribution | X | Missed or inaccurate information about the state of the Distributed Customer Storage devices or 2-Way Meter -Electr may lead to reduced time that customer is provided some amount of energy/load |
| Markets |  |  |
| Operation | X | Missed or inaccurate information about the state of the circuits and the Distr Customer Storage devices may lead to missed opportunities to improve the circuit and customer electric service objectives or recognizing the need to check for customer outages on that circuit |
| Service Providers |  |  |
| Transmission |  |  |

#### Scenario: 	Capped Customer Energy Usage

Narrative

This scenario covers the situation where power has been lost to the portion of a feeder circuit that has attached Distributed Customer Service devices that can provide for temporary finite amount of power for a limited amount of time. This scenario is also premised on a close affinity between the customer loads that can be sourced from the deployed Distributed Customer Storage devices and the 2-way Meter – Electr. for placing the meter into a capped energy/load usage mode and then to take the meter out of that capped energy/load usage after power has been restored.

Business Objectives

| Originating Actor | Destination Actor | Latency | Reliability | Payload Size - bytes | Payload Name |
| --- | --- | --- | --- | --- | --- |
| LMS - Utility | 2-Way Meter - Electr | < 12 sec | > 98% | 25 | meter_capped_kwh_mode_cmd |
| 2-Way Meter - Electr | LMS - Utility | < 12 sec | > 98% | 25 | meter_capped_kwh_mode_cmd_ack |
| 2-Way Meter - Electr | IPD, Cust. EMS, MDMS | < 12 sec | > 98% | 50 - 150 | meter_in_capped_kwh_mode_alert |
| Sub-Totals | < 36 sec | > 94 % | 100 - 200 |  |
| LMS - Utility | 2-Way Meter - Electr | < 12 sec | > 98% | 25 | meter_capped_kwh_mode_cancel_cmd |
| 2-Way Meter - Electr | LMS - Utility | < 12 sec | > 98% | 25 | meter_capped_kwh_mode_cancel_cmd_ack |
| 2-Way Meter - Electr | IPD, Cust. EMS, MDMS | < 12 sec | > 98% | 50 - 150 | meter_out_of_capped_kwh_mode_alert |
| Sub-Totals | < 36 sec | > 94 % | 100 - 200 |  |

Implications and Rationale

| Functional Domain | Expected Potential Impact | Rationale |
| --- | --- | --- |
| Bulk Generation |  |  |
| Customer | X | Missed or inaccurate information about the state of available energy available, may lead to additional customer complaints separate from a complete outage |
| Distribution | X | Missed or inaccurate information about the state of the Distributed Customer Storage devices or 2-Way Meter -Electr may lead to reduced time that customer is provided some amount of energy/load or customer is returned to full enrgy/load service functionality |
| Markets |  |  |
| Operation | X | Missed or inaccurate information about the state of the circuits and the Distr Customer Storage devices may lead to missed opportunities to improve the circuit and customer electric service objectives or recognizing the need to check for customer outages on that circuit |
| Service Providers |  |  |
| Transmission |  |  |

# Footnotes

this is a new requirement row and payload incremental to Requirements Table R5.1