Table of Contents

Preface	5

Introduction	5

Background	5

Purpose	5

Scope	5

OpenSG Compliance & Interoperability (CIP)	6

Scope of the CIP	6

Device Certification Program Overview	8

Process	8

End Product and Module	9

Self Certification	11

Testing Compliant Portion	11

Certification Program Manager (CPM)	13

Approved Device Certification Body (ADCB)	13

Technical Advisory Board (TAB)	15

Lead Laboratory (LL)	16

Approved Device Certified Laboratory (ADCL)	16

Certificate Authority (CA)	17

Certification Requirements Status List (CRSL)	18

Logo Program Administration and Operations	21

Certified Product Listing	21

Digital Certificates	21

Compliance Folder	21

Logo Certificate	22

Removal of Products from Certified Product List	22

Changes to Certified Products	22

Determining Class of Change	22

Module Policy	23

Inheritance of Compliant Portion of Modules	24

Integrated Products and Re-Branded Products	24

Certification Process Exceptions	25

Process Problem Resolution	25

Process Dispute Resolution	26

Jurisdiction	26

Certification Requirement Waiver Process	29

Monitoring of Logo Certified Product Validity	29

Corrective and Preventive Action	29

Selection and Maintenance of Logo Certification Program Golden Units	30

Test Harness	31

Validation of Test Harness	31

Submittal Process	31

Evaluation Process	31

List of Tables

Error! No table of figures entries found.

List of Figures

Definitions

CRSL:  Certification Reference Status List

Primary Test Categories

Reference Primary Test Category Tests

CA:  Certificate Authority

ADCB:  Approved Device Certification Body

ADCL:  Approved Device Certification Laboratory

CPM:  Certification Program Manager

LL:  Lead Lab

TAB:  Technical Advisory Board

# Preface

  - Introduction

### Background

The electric energy utility industry has sponsored the Open Smart Grid (OpenSG) Conformity Working Group organization, Edge Conformance Task Group (OpenSG Edge TG), under the auspices of the Utility Common Architecture Group (UCA Group).  This OpenSG Edge TG is tasked with the job of defining the necessary requirements for assuring conformance and interoperability of various devices and technologies in OpenHAN, OpenADR, and OpenADE specifications.

The GridWise Council, sponsored by NIST, also address issues of Edge device interoperability and testing.  This document aims to be inclusive of the GridWise Council work products, while maintaining a clear focus on utility infrastructure and industry requirements.

  - Purpose

This document descibes the Compliance and Interoperability Program (CIP) required by OpenSG.  The purpose of this document is to promote industry-centered robust product and system certification programs to test for the stringent requirements of the technical specifications from OpenHAN, OpenADR, and OpenADE.  It is the intent of this document to become the basic foundation of standards organization testing and certification programs that would be deemed acceptable to the utility industry.

  - Scope

This document covers the entire framework description of the CIP.  The CIP follows the Guiding Principles  Document issued by the OpenSG Edge Conformance TG, and implements the following key policy factors:.

-Testing and certification experiences of communication protocol stacks point to Best Practice Structure of testing as described in the Guiding Principles document.

-The importance of accumulated experience of testing institutions is recognized.  Of particular importance are: coexistence with interferers, interoperability at application layers but with various physical layers and interconnections thereof, and enforcement of standards based interoperability.

In general, the CIP framework shall consist of a basic two parts, with one part being the CIP Program Operations and Administration, while the other is the CIP Requirements & Policy.   A Steering Committee shall oversee the entire program and liaise with OpenSG on the suitability of the specific CIP Program.

# OpenSG Compliance & Interoperability (CIP)

  - Scope of the CIP

The scope of this program is to certify products and systems per agreed to PICS to

-relevant mandatory and optional conformance feature sets of

the communication stack physical layer

-relevant mandatory and optional conformance feature set of the protocol stack

-interoperability of devices within the device class,

and service level and application interfaces relevant to the application profiles

-interoperability with applications and service level interfaces from other network domains within

the smart grid communication infrastructure

-conformance to metrics for product and system performance as specified by business, regulatory, 			and user requirements per the GWAC stack framework

The relevant PICS documents are required to incorporate the SRS documents from OpenHAN, OpenADR, and OpenADE as appropriate.  Product and System Certification shall require applicants to sign a Declaration of Conformity (DoC) document prior to a Certification by the relevant industrial organization.

The certification process applies to deployable end products and reference designs such as, but not limited to, Smart Meters, Energy Service Interfaces and openHAN compliant Smart Energy 2.0 device implementations (PCT, IHD, LCD, etc.).  The certification process also addresses complete radio, PLC, wireline, and/or radio-PLC-wireline modules and reference designs which may be integrated into other end products, typically without further modification, and therefore without further certification (See section Inheritance).  Re-certification of certified device versions (evolving devices) and variants (adaptations) are also addressed (Section:  Revisions).  The certification program does not certify incomplete implementations (SW/HW components, subcomponents, subunits) of devices and applications, for example an implementation of part of the protocol stack.

The certification process is also applied to application software and systems consuming services at interfaces with the smart grid communication infrastructure.  These may include OpenADR and OpenADE client / server services, including Demand Response DRAS, Demand Response Client, portal services.  Re-certification of certified application software and system versions and variats are also addressed (Section: Revision). The certification program does no certify incomplete implementations that do not implement mandatory set of features.

In the event of discrepancies or errors in the Standard, Specifications or Certificaiton testing, an industry Lead Laboratory (LL) will notify all affected companies regarding needed remediation activities.  In the event of invalid test an industry WG shall review the test result and procedures followed.  If corrective action is needed the industry WG in cooperation with the LL will determine the course of action and notify all affected companies of its determination.

If a product is certified and later the registered company is no longer a viable entity, the certificate remains active but use of relevant logo stops and the listing is removed.

The context diagram of Figure 2 gives a pictorial representation of the general communication infrastructure involved in the Smart Grid.

Figure 2.	Context Diagram

  - Device Certification Program Overview

### Process

An OpenHAN device industry manufacturer seeking an OpenHAN compliant technology certification, such as ZigBee Smart Energy 2.x (ZEP2.x) , of a new device first completes an application for a Device Certification (see section TBD for details; a new device may be an End Product or a Module).  This member selects an Approved Device Certification Laboratory (ADCL).  The member seeking certification for a product or module shall contract with the ADCL and the assigned Apppointed Device Certification Body (ADCB) for evaluation, testing, and certification services.  The application process is the first step in the booking process.  It shall not possible to test and obtain a device certification at the LL.

The instance of the OpenHAN technology, such as ZEP2.x, provides a PICS proforma including all the features (Mandatory and optional) that  Certified product or module may support.

The applicant supplies:

-Two product or module samples with supporting components (i.e. batteries, cables, chargers, notebook 	computers and associate hardware/software, etc. as needed to facilitate the evaluation)

-Signed and dated Laboratory Nondisclosure Agreement and Information Pack (soft copies preferred)

-User documentation

-Completed PICS proforma

-Completed PIXIT proforma.  The PIXIT proforma will be provided by ADCL at the beginning

of the testing project

-Completed Declaration of Conformity - this must be finalized prior to certification but after

testing is completed.

-Test reports for category C tests - supplied as available prior to certification

-A completed Signed Certification Mark License Agreement to permit use of the logo upon

successful completeion of Certification - to be completed prior to certification.

Where applicant seeks to certify more than one bill of material, product/module samples for each bill of material shall be provided.  Based on a review of the differences between bill of materials, the ADCL may waive this requirement.

The ADCL with the ADCB reviews the application, and determines test requirements based on the supplied PICS according to the current Certification Requirements Status List (CRSL).

The Compliant Portion of the proposed Certified Device shall be described precisely so that subsequent product change applications can determine whether a product/module change is Class I (outside Compliant Portion) or Class II (within Compliant Portion).  When feasible, product model number, hardware version number and software version number shall be associated with the Compliant Portion rather than a higher level assembly.  If the Compliant Portion is to be integrated into another end product, or if other Class I change is envisioned, the application shall describe the applicable hardware and software environment of the Compliant Portion sufficiently so that compliance can be ensured.

Certification Testing ensures that a IUT meets all Certificaiton Criteria according to the vendors submitted PICS which determines through a mapping table which specific test cases in the currenlty applicable CRSL form the test plan that must be passed in accordance with the categories defined in section TBD.  The whole process shall be done by a ADCL.  Tests include the following “Primary Test Categories”:

PhyCT- Physical Conformance Testing

PCT-Protocol Conformance Testing

DIOT-Device Interoperability Testing

NIOT-Network InteroperabilityTesting

PhyPT-Physical Device Performance Testing

Testing requirements for a particualr device are determined by the PICS and the applicable Certification Requirements Status List (CRSL) which identifies the current status of each applicable test and certification requirement.  A PIXIT proforma is used to configure the implementation under test (IUT) in the test bed properly in order to run the test plan.  Applicable tsts shall be performed and documented as required by their category. Test categories are defined in seciton TBD.  During the testing process each vendor has restriced access to the ADCL’s web site for tracking and monitoring the progress of the testing of their equipment.

The ADCL shall ensure that all testing requirements are satisfied by the particular hardware and software version certified.  In general, no product change is permitted during certificaiton, except as expressly required by a Test Procedure wihin an appliable test case.  The ADCL may permit cettain limited change if the ADCL (a) has high confidence that such a change will not compromise the integrity of prior test results, or (b) repeats all test cases which might be impacted.  Any product/module change introduced during certificaiton shall be documented and strictly managed by ADCL.  See Annex A guidelines on determining required retesting based on product changes.

When a produt successfully completes all the required testing, test reports are assembled into a Compliance Folder.  See Section TBD and Annex for Compliance Folder details.

The ADCB shall review the application and relevant certification documentation, including PICS, to determine that

- the vendor supplied product satisfies all current certification requirements;

- All mandatory PICS items are supported;

- the entire Compliant Portion is contained wihitn the elements described;

- the hardware and software environment containing the Compliant Portion is sufficiently described to ensure compliance is maintained in that environment; and

- the Declaration of Comformity is complete and accurate.

After the ADCB has determined that all necessary certification requirements are satisfied and the certification listing fee is paid, the ADCB shall submit the Compliant Portion to the Certified Product/Module List along with necessary supporitng information (See section TBD) and shall add the product/module in which the Complaint Portion was evaluated to the End Product List.

A Compliant Portion is defined as an exact hardware and firmware/software configuration, and any deviation thereof represents a Class I or Class II change.  For example, an Device Module may be an Compliant Portion, as well as a particular microcontroller model with a specific firmware build.

Once the product or module is certified, the Certificate Authority (CA) issues a digital certificate to be programmed into the devices, for use in joining a utility smart grid network.

### End Product and Module

      - General

A certified device describes a Compliant Portion certified within a particular end product or module.  The listing member company may intend to apply the certified Compliant Portion to a family of similar end product models or module, either initially or subsequent to the intial listing.

Furthermore, the member company is allowed to sell the Compliant Portion for integration, resulting in end products offered by another member company if the Compliant Portion is listed as a Certified Module (See Section TBD).

Performance may be impacted by integration of a Complaint Portion into a different end product, and testing will typically be required when the end product differs or when the end product manfuacturer (integrator) is different from the Compliant Portion manufacturer according to Class I, Class II, or Class III change rules by a ADCB.

An End Product is an integration intended for end user distribution containing Compliant Portion.  Every End Product shall be listed on the End Product List.

Integration of a Compliant Portion into an end product different from the end product in which it was certified, may impact the performance, for example if the antenna placement or environment changes, or if the host environment is otherwise different.  Such integration shall be considered within the Class I, Class II, and Class III change rules by a ADCB.

A member seeking to list a End Product shall complete an online application for Certification.  An End Product application shall reference the Module or Compliant Portion of a Certified Product integrated into the End Product if the member wishes to claim abbreviated certification process.

When integrating a Module, an application for End Product certification shall declare that the hardware and firmware/software environment containing the module complies fully withthat required by the Module, and provide supporting documentation as needed. Such integration shall be considered within the Class I, Class II, and Class III change rules by a ADCB.

When integrating a Compliant Portion that is not a Module, an application for End Product certificaiton shall describe any variation form the specific End Product in which the applicable Complant Portion was certified. Such integration shall be considered within the Class I, Class II, and Class III change rules by a ADCB.

An End Product application may cover a family of end product models, provided the compliant poortion is identical, and the applcation shall describe the end product familty in a sufficientl detail to permit evaluation of potential impact of product family variations on performance including radiated performance.

A End Product application is reviewed by ADCB to determine testing requirements with reference to section XX and Annex A, “Certification Program Class I/II/III Change Guidelines”.  Indicated testing shall be performed and documented in the End Product Compliance Folder.  After the ADCB has determined that all necessary certification requirements have been met and the SE log fee is paid, the ADCB shall submit the end product into the End Product List along with necessary supporting documentation.

It is allowed to start certification testing for an end product before the initial product completes its certification conditional that the end product does not complete certification before the inital product completes and obatins its certificate.  In all cases the end product must follow the rules and policies as defined in sections TBD.

A certificate is issued for each End Product and Module Listing.

      - Change to End Product or Module

A change to an End Product or Module shall be reviewed by a ADCB.  When a listed product is changed, the member responsible for the listing shall complete an application for Certification online.

A Change application shall include the following:

-identify pertinent End Product or Module record,

-amended Compliant Portion or End Product / Module description as applicable

-amended PICS if applicable

-product change description, and

-executed revised Declaration of Conformity

The product/module change description shall be sufficient to determine the scope of testing required to determine that the change device is compliant.

The ADCB may request additional information as needed to complete the review.  The ADCB shall determine additional testing required.  Se section TBD and Annex A for details.

      - Certification Requirements

Product/module certification is associated with (a) a category (i.e. tbd or tbd), (b) a particular System Profile Release nubmer and version and (c) one or more Certification Profiles(s).  To certify a product/module, a vendor completes the applicable PICS forms.

In the PICS, the vendor stipulates the SE functions supported by the product/module to be certified.  The completed PICS is used to generate a list of applicable Test Cases based on the test case mapping table (contact the ADCB for a copy) within the online Cert System.

The list of applicable test cases is used in conjunction with the current CRSL to determine which test cases shall be performed.  See section TBD for dtailed information on the CRSL.

### Self Certification

TBD

### Testing Compliant Portion

The End Product or Module is subject to testing for its proposed compliant portion.  The testing involves layers, from the physical all the way to the network interfaces.

      - Physical Conformance (PhyCT):  Radio, PLC, wireline

Physical Conformance Testing assesses the compliance of the physical layers of an implementation seeking certification to the applicable base or core specification of the mandatory and optional features of  the physical transport layer PHY (IEEE 802.15.4, IEEE 802.11, etc), as applicable to the type of End Product or module.

Typically, Physical (RF, wireline, or PLC) Conformance Testing is not concerned with and does not cover assessment of performance, reliability or robustness of the entity under test, unless explicitly stated as a conformance requirement in the conformance testing specification.

Physical Conformance Testing does not add constraints to those stated in the core specifications and consists of a series of tests against the physical conformance requirments stated in the applicable radio/plc/wireline conformance testing specification.

A radio/plc conformance requirement is an elementary piece of the core specification stating what a SE implementation seeking certification is reqiured to do or not to do.

An implementation is found as conformant with the physical layer core specifications when it satisfies all the selected physical layer conformance requirements contained in the CRSL based upon completing the required tests and executing the DoC.

For example, the radio physical layer conformance requirements of ZigBee devices are derived from the basic IEEE802.15.4 radio layer specification over the operational temperature and humidity range of the device as declared in the PIXIT, and include:  power spectral mask and density, center frequency and tolerance, sensitivity/packet error rate, modulation/demodulation, error vector magnitude, adjacent and alternate channel rejection, turnaround time, clear channel assessment, energy detection, and link quality indication.

An implementation is found as conformant with the physical conformance related core specifications when it satisfies all the selected physical conformance rquirements contained in the CRSL based upon completing the required tests and executing the DoC.

      - Protocol Conformance Testing (PCT)

Protocol Conformance Testing assesses the compliance of the protocols implementing the MAC layer and Network Layer of the implementation seeking certification to the applicable base and core specification (IEEE802.15.4:2006 and ZigBee IP for ZigBee, HomePlug SE Specification for HomePlug, IEEE802.11b/g for Wi-Fi).

Protocol Conformance Testing does not add constraints to those stated in the core specifications and consist of a series of tests against the protocol conformance requirements stated in the applicable protocol conformance testing specification.

A protocol conformance requirement defines the core specification stating what an implementation seeking certification is required or not to support.

For example, The ZigBee-related protocol conformance requirements are derived from the IEEE802.15.4 MAC layer and ZigBee IP specification along with the PICS and PIXIT documents relating to those MAC and NWK layers.  These include:  ....

An implementation is found as conformant with the protocol-related core specifications when it satisfies all the selected protocol conformance requirements contained in the CRSL based upon completing the required tests and executing the DoC.

      - Interoperability Testing (IOT)

Interoperability is key to customer acceptance.  Interoperability testing for Logo Certification requires a minimum of three different golden unit vendor devices.  The interoperability configuration scenario must include at least two different physical layer chipset vendors. Each end product/module must demonstrate interoperability with at least three different certified Energy Service Interface (ESI) if it is not an ESI; if an ESI, it shall demonstrate interoperability with at least three different PCT and IHD combination.  This enables the basic  network interoperability.

Additional to the above requirement, each product/module must demonstrate interoperability with at least two different certified end product/module (from at least two vendors) and at least one device should be the reference unit selected by industry WG.  This enables general market device interoperability.

Interoperability testing is enhanced as more vendor equipment is made available from different vendors.

Interoperability tests are described in TBD

The interoperability certification test bed is available at each ADCL for all currently required interoperability tests.  The tests shall include all relevant profile device roles and application functionality declared in the PICS and PIXIT, and test for:  trust center policy, network management policy, commissioning and installation, power failure/start-up, use cases, stress cases, over-the-air download.

A implementation is found as conformant with the interoperability core specifications when it satisfies all the selected interoperability requirements contained in the CRSL based upon completing the required tests and executing the DoC.

      - Physical Performance Testing (PhyPT)

Physical Performance Testing (PhyPT) requirements provide physical layer performance metrics intended to determine the limits of performance of  End Products and modules, for example in an over-the-air (RF) environment.  In such case, tests are intended to determine the transmitter and receiver performance and sensitivity in normal operation in the presence of  far-field (for RF case) interferers causing transceiver desensitivity.  PhyPT tests are critical in that they provide necesssary infomration on the radiation pattern of the device as used, and the effect of interaction factors between the radiated field and the circuitry of the device.

The PhyPT shall include the following based on the PIXT and PICS declarations:  range and directionality (link budget and sensitivity verification), and immunity/desensitivity to known interferers.

PhyPT is required for the Certification of End Product/module.  The test report will be included in the Compliance Folder and test results become part of the Compliant Portion of the end product/module.  It is the intent of industry WG to conduct a regression analysis across the applicable Certification profiles on data collected during PhyPT.  Industry WG will then request an approval of a baseline criteria for example, Smart Energy 2.0 for future PhyPT testing.

      - Network Conformance Testing (NCT)

Network Conformance Testing (NCT) complements PhyCT, PCT, IOT as a system level conformance testing for end-to-end from the utility head end to the HAN network.

(to be continued)

### Certification Program Manager (CPM)

CPM is an individual appointed by the industry program to act as the administrator of the Logo Certification Program.  His/her task is to oversee the day-to-day operations and needs of the certification program, and act as the interface between the industry and the program.  His/her taskes involve:

Chairing the TAB

Coordinating problem resolution in the Logo Certification Program

Communicating important items to the industry

Signing off on the Logo Certifications

(to be continued)

### Approved Device Certification Body (ADCB)

ADCB is a personal qualification scheme installed by the logo program, and part of the Approved Device Certification Program.  Each appointed ADCB is entrusted with the authority to submit products as Certified, without further review.  This special trust depends upon both the competence and the integreity of each ADCB.  The ADCB appointment is renewed yearly by the ADCB contingent upon the following yearly recognition maintenance requirements and any additional requirements the logo program deems necessary.  The ADCB may seek monetary compensation to clients for services rendered to clients and organizations as part of sanctioned ADCB function.

      - Definition

The ADCB are individuals appointed by the logo porgram to certify that an End Product or module satisfies all certification criteria to be a Certified Product.  ADCB is an individual who is typically, but not necessarily, affiliated with an ADCL(s).  ADCB shall not be both a) responsible for performing tests, generating and/or signing off on a test report for a specific certification project, and b) responsible for assessing and certifying the results for submittal as a  Certified Product, for the same specific certification project.  In other words, ADCB may test for projects he/she is not responsible for certifying.

      - Sanctioned Activities and Responsibilities

ADCB submits product listings through the Certification Tool to the Certification Program Manager for listing Certified Products, after a review of the Compliance Folder and other documents by checking completeness, correctness, and consistency of the materials.  ADCB may assist the Member to determine tests required through the use of the Test Plan Generator, preparing documentation, and completing all requirements for the listing.  At the time of completion of the certification assessment, the ADCB shall deliver a Certified Product Notice certifying that product has satisfied all Certification Criteria and is ready for listing.  This notification will be generated by the Cert system when the ADCB updates the status of the corresponding certification project.

The ADCB is knowledgeable about the application profile and its certification criteria.  The ADCB notifies the industry WG Program manager when all listing requirements are met, and gives a certification date and a member defined listing date of the product with the express permission of the Member.  The ADCB enters the product information on the Certified Products List when authorized by the Member for a specific listing date.

Confidentiality is a key part of the ADCB activity.  For this reason, the ADCB will operated under the NDA.  The ADCB is responsible for verifying the authenticity of documents submitted and used in Product Certification.

With respect to the Certification program, the ADCB serves under priviledge granted by the logo program, and hence answers foremost to the Program Manager above any immediate management authority the ADCB may be operating under.  Any deviation is grounds for withdrawal of ADCB status.

      - Qualifications:  Recognition Process for ADCB

The ADCB holds a position of high trust.  Recognition as ADCB is therefore both subjective and revocable.  ADCB recognition is based upon an applicant’s compliance with criteria listed on this CPRM as well as additional information gained by logo program throughout the applicant evaluation process.

Applications for ADCB recognition shall be submitted to the Certification Program Manager.  The applicants shall directly address each requirement listed below in a manner that allows the responses to be easily compared with each requirement.  The Certification Program Manager will forward completed ADCB applications to the logo program consideration.  The logo program will determine whether additional evidence or interview(s) are needed and will instruct the  Certification Program Manager to so notify the applicant.

      - ADCB Requirements

The ADCB shall have the following minimum qualifications

-at least 3 years relevant professional work experience

-at least 2 years of relevant engineering related work experience in at least one of the following areas

-edge device planning and project management

-edge device design in physical, protocol, or application layers

-edge device evaluation and testing

-edge device regulatory testing

-edge device regulatory certification

-where ADCB is part of a larger organization, the organziational arrangements should be such that departments having conflicting interests, such as production, commerical marketing, or financing do not adversely influence ADCB compliance with the requirements of the Certification Program

-ADCB shall have arrangements that ensure that ADCB is free from any internal or external commerical, financial, or other pressures and influences that may adversely affect the quality of work

-authority to reject test resulsts based on non-conformance

-capable of maintaining confidential information

-at least 1 year of edge device technical or qualification working active group participation

-relevant degree in engineering or sciences, or equivalent

-ability to speak, read, write English at college level

-ability to compose a logical non-technical position and argument based on technical issues

-be available for participation in industry WG participation

-complete a  Certification Program / ADCB introductory course session held by CPM

-complete, with satisfactory results, the application and questionnaire for ADCB recognition

-complete an interview with the  CPM and logo program, or proxy thereof, for ADCB recognition

-participate in Technical Advisory Board (TAB) once recognized as ADCB

Furthermore, each ADCB applicant acknowledges that continued recognition is contingent upon the applicant’s maintaining both the complete trust of the program and the original ADCB requirements met by the applicant.  The logo program reserves the right to suspend any ADCB recognition at any time, without warning.  This includes, but is not limited to, changes in employment status and failure to maintain competence in the applicable  specifications,  test specifications, and  certification policies.  It is not necessary for the program to provide any specific reason for withdrawal of ADCB priviledges.

The ADCB shall annually declare in writing to the program:

-that no changes in the ADCB’s conformance with the recognition requirements have occurred,

-how the ADCB continues as an active participant in the certification program, and

-how the ADCB maintains competence in the SE specifications, and SE certification policies

Note that ADCB appointment does not guarantee the validity of ADCB’s action (logo program cannot be held liable for any claims against a ADCB).

### Technical Advisory Board (TAB)

      - Definition

The TAB consists of Certification Program Manager, ADCBs, ADCL representatives, Lead Laboratory representative, in additional to other relevant technical experts from manufacturers.  The TAB exists as an ongoing operations entity separate from the  industry WG.  The TAB provides specific informational and operational recommendations to the program.  Its function is advisory for feedback and improvements of the process of Certification program through the Program Manager.    TAB shall seek to enhance the expertise and technical competence of its members in matters relating to edge product certification and testing.

      - Activities

The typical purposes of the TAB include:

-to address technical issues relating to conformance and interoperability testing of End Products and modules; including issues relating to test specificaitons, test requirements, test procedures, validated test equipment and validated test cases.

-to produce advisory notes for use by ADCBs covering aspects related to test cases, guidance on test configurations, applicablility of test cases especially during transitional peridos, and new testing techiques in order to iprove the practical iplementations of the certification process.

-to review and decide on Test Case Waiver submissions, subject to review by the Lead Laboratory

-to provide a forum for free discusion of new ideas, developments, and advanced testing techniques relating to test requirements, methods, and equipment

-to provide an environment that will improve the practical and theoretical knowledge of members relating to the testing of End products and modules.

The primary function of the TAB is to advise and counsel the logo program in matters relating to product certification requirements and testing, including prolmes relating to test specifications, procedures, and equipment.  A secondary function is the free exchange of knowledge among members.  To help these functions the TAB will act as the input and source of knowledge on problems to the testing of End products and modules and on the certification process for the benefit of the entire  Certification Program and the Lead Laboratory.

### Lead Laboratory (LL)

      - Definition

The Lead Laboratory is appointed by the program as the operational arm of technical development, resolution, and ongoing repository of competence for the entire Certification Program.  The LL is a test laboratory charged with the investigation of test methods, test equipment, and inputs from the TAB.  The purpose of the LL is to maintain a center of core competence to uphold a robust Certification Program, and to normalize the trustworthiness of test results from the various ADCLs.

      - Activities

The following activities are included in the LL scope of activities:

-Evaluation of test procedures, test cases, and test suites proposed by the industry WG before final approval

-Coordinating and managing interoperability events for development, and certification readiness of upcoming specifications and products

-Evaluation and development of test systems used by the ADCL and industry at large

-Proxy as technical operations arm of the Certification Program manager and program

-Evaluation of ADCL for continued competence in testing for End Products and modules

-Coordinating and facilitating the output of TAB and resulting requests and requirements from the Certification Program Manager and/or program

-Serve as the operational arm of technical issues resolution, as necessary, for issues forwarded by TAB, and WG.

-In general to functional as center of excellence in technical matters related to the Certification Program, and to deploy that competence to the ADCLs

-The LL shall not commerically compete with existing ADCLs for testing and certification services.

      - Selection

The LL is selected and appointments renewed or revoked at the discretion of the Steering Committee.

### Approved Device Certified Laboratory (ADCL)

      - Definition

The Approved Device Certified Laboratory (ADCL) is a commercial or non-commercial testing laboratory focussed on delivering testing services as part of the Logo Certification Program.  The ADCL is charged with the responsibility of serving the logo program companies, to provide a clear and concise pass / fail result for  Logo Testing based on the CRSL and the applicable test and technical specifications.    The ADCL status is granted by the logo program based on recommendation from the WG.  The ADCL designation is a privilege which can be revoked at any time by the logo program based on defined process of removal.  Appointments are subject to evaluation and renewed biannually.

      - Activities

The following activities are included in the ADCL scope of activities:

-timely implementation and maintenance of test procedures and test systems used in logo testing program

-participation and active contribution to industry WG and TAB

-provide testing services in accordance with the CRSL to the logo program member companies

-promptly address any issues identified by member companies, LL, TAB, WG, or logo program

-maintain competent personnel

-abide by the Service Level Agreement (SLA) defined with the logo program, and in force between the ADCL, member companies, and the logo program

      - Selection

It is the intent of the WG to make selection recommendations based on the following:

-Overall result of both evaluation and audits of candidate ADCL

-Geographic diversity of ADCL locations in the  Certification Program

-Fostering competition for service and technical excellence

-Basic organizational and technical strength

-Good management practices

-Recognized accreditations, including ISO Guide 17025 from an internationally recognized accreditation 		body under the ISO/IEC standarization structure

-Facilitating baseline business viability

-Commitment and ability to add value to the logo program organization through technical participation in 		working groups and advisory boards

-Experience in similar services

-Competent personnel

-Value brought to the logo program in general

-Work with ADCB and submit to the ADCB the results for review

-Capability or readiness to implement the following, both technically and budgetarily

-edge device physical layer conformance testing

-edge device protocol layer conformance testing

-edge device interoperability testing

-edge device network testing

-edge device physical layer performance testing

The industry WG will develop a complete evaluation procedure and documentation to assist ADCL selection according to the above set of criteria.

### Certificate Authority (CA)

      - Definition

The Certificate Authority (SECA) is a commercial or non-commercial organization focussing on issuing the digital certificates for the Logo Certified Products.  The CA is charged with the responsibility of serving the program member companies, to provide digital certificates to be embedded in to edge products, for use in certificate based key establishment security feature (CBKE).    The CA status is granted by the logo program.  The CA designation is a privilege which can be revoked at any time by the logo program based on defined process of removal.  Appointments are subject to evaluation and renewed biannually.

      - Activities

The following activities are included in the CA scope of activities:

-timely issuance of digital certificates to Logo certified products

-management and control of digital certificate issuance system

-ensuring that the digital certificates issued are current and valid

-maintain competent personnel

-abide by the Service Level Agreement (SLA) defined with the logo program, and in force between the CA, member companies, and the logo program

### Certification Requirements Status List (CRSL)

      - Definition

The Logo Certification Program currently certifies devices on 3 levels of conformance and interoperability test specifications.  The corresponding PICS documents specify the mandatory and optional requirements for all the test specification documents.  The Certification  Requirements Status List (CRSL) specify the testing requirements at any given time, and gives guidance to ADCL and ADCB on testing and recommendation for certifications.  The CRSL is maintained by the LL.

CRSL versions include changes to the test requirements and test specifications. Requirements for certification are set by the CRSL version effective on the date that the device is certified.

A CRSL Interim Release includes the results of the CCB process, and introduces new requirements that will become active in future CRSL Major Releases.  A (x.0.0) of the CRSL shall occur twice annually.  A public interim release of the CRSL (x.y.0) shall occure no more frequently than once per month.

Requirements upgraded in Major Release (x.0.0) shall be available in an interim release of the Major Release (x-1.y.0) effective 45 days prior to Major Release (x.0.0).  Vendors have 90 days to submit their equiment for certification to be tested against this major release.

IUT undergoing certification testing when the next major release becomes effective have 45 days to complete testing.  Test requirements are defined by the major release under which the IUT is submitted.  Test cases which become active after the next major release are not required.

      - CRSL Structure

The CRSL defines the current status of each test case in a list.  The list contains the following information:

- Designator - test case identifier

- Name - descriptive text from the test specification

- Current requirement -

- Test specification number and version

- Test Case Category

- Available date: date at which the test case may be used as the indicated Test Case Category

- Active date:  date at which the test case shall be use d at the indicated Test Case Category

- Associated notes

- Previously published requirement

- -Test specification number and version

- -Test Case Category

- -Status

- -Active date

- -Associated notes

- Informative

- -Test Case Priority

- -Test Platform:  Validated test platforms for both the current and previous test case

The following applies for each test case requirement:

- Prior to the Available date of the current requirement, the previously published requirement shall apply.

- From the Available date until the active date of the current requirement, the vendor shall choose to apply either the previously published requirement or the current requirement.

- From the Active date, the current requirement shall apply.

Issue of an update to the CRSL is managed and approved by the industry WG.  Updates to the CRSL include changes to test case categories to reflect the addition of new validated test cases, the downgrade of previous validated test cases, and the revalidation of downgraded test cases.  The LL shall implement the CRSL updates.

      - Test Case Categories

The Logo Certification Program assigns each test case from the test specification a Test Case Category.  A test case is validated when a validated test platform is available, and required for implementation.

        - Category A

The device shall pass each Category A test case at the ADCL on a validated test platform.  These are the validated test cases.  A test report shall be generated according to ISO Guide 17025.

        - Category B

The device shall pass each Category B test case at the ADCL.  Pass/Fail verdict is assigned and the test reported generated according to ISO Guide 17025.  These are typically test cases that have been verfiied and can be executed with unambiguous results, but for which test case validation is incomplete.

        - Category C

The device shall pass each Category C test case either at the manufacturer or the ADCL.  In case the test is done by the manufacturer, a test report shall be submitted to the ADCL.  Pass/Fail verdict shall be assigned.

        - Category D

Test cases may be downgraded from A or B or C by the LL, but must be revalidated and reinstated to its prior status without delay, upon resolution of any issues.

        - Category E

The device shall perform Category D tests at the ADCL and a test report generated.  However there is no Pass/Fail verdict assigned.

        - Category I

Test cases planned for further development and listed for informational purpose.

        - Category P

Test case planned for validation or awaiting approval but currently listed for informational purposes.

      - Test Case Category Transition

A Test Case Category for  a test case may or may not change over time.  Test Case Status is communicated using the CRSL Interim and Major release.  The following list describes, in part, the typical assignment and re-assignment of test case categories:

- All test cases start as Category I.

- Test cases selected from development are moved to Category P in the next major release.

- If a test case upgrade proposal from Category B to Category A is accepted for inclusion in the next Interim Release of the CRSL, the following rule shall apply

- -The upgrade is effective immediately

- -Testing underway may (test start date prior to upgrade) may continue their certification testing without regression testing.

- The initial Available Date shall not precede the CRSL publication date.  Teset cases may be immediately downgraded temporarily to Category D in specific circumstances under the authority of LL and reinstated without delay, maintaining the original active date if the reinstatement does not occur past the original active date.  Test cases are not necessarily downgraded due to a single test platform losing validated status.

- All other category transsitions (upgrades) are effective at the next Major Release of the CRSL.

# Logo Program Administration and Operations

  - Certified Product Listing

When the Logo Certification criteria are satisfied, and with the agreement of the vendor, the ADCB shall post the product / module onto the Logo Certified Product registry with the following information:

- Product Name

- Certified Edge Device Type

- Certification Number

- Date of Certification

- CRSL date

- CRSL associated version number

- Detailed product informationin text form (not more than 200 words)

- Product image in jpg format no larger than 300 x 300 pixels

- Company logo in jpg format no larger than 300 x 300 pixels

The ADCB shall ensure, prior to completing the product certification process, that the equipment vendor is still a member in good standing with the logo program, and that the certification testing fee and certifcation logo fee are collected per certification.  With the explicit agreement of the applicant, the ADCB will enter the data into the Logo Certified Product registry and create an electronic Logo Certification Certificate from this data.

### Digital Certificates

Once a product enters the Logo Certified Product registry, the CA shall generate a digital certificate for that product and issue it to the applicant.

### Compliance Folder

The SE Compliance Folder shall provide the actual Record of Work for conformance to the certification process.  Theminimum required information is listed below.  For additional information, see Annex TBD.

Minimum contents in the Compliance Folder:

- Member name

- Exact model number

- Exact kit number if applicable (i.e. variant number)

- Hardware version and change history

- Software version and change history

- CRSL version number

- PICS

- PIXIT

- Test Report

- Applicable waivers and their descriptions and reasons, and any change requests

- Declaration of Conformance

All vendors shall maintain a duplicate set of Compliance Folder for their certified product.  The logo program, at its discretion, order additional reviews of the Compliance Folder.  Any such additional Compliance Folder reviews shall be at the expense of the logo program and be conducted by a mutually agreeable third party contractor that is neither an employee of another manufacturer.

Additional Compliance Folder Review will occur only when the industry WG has indications of repeated problems with the Logo Certified product of the vendor.  Under such circumstances, the industryWG chair shall sign a NDA to this effect.

### Logo Certificate

After the Logo Certified product is listed in the Logo Certified Product List, the Certification Program Manager shall issue a hard copy of the Certification to the vendor with special heavy stock paper and embossed in gold seal.

### Removal of Products from Certified Product List

The primary contact for the particualr product posted on the Logo Certified Product List may request that the Council remove prudcts from public view anytime.  The removal request should be sent to the Certification Program Manager.  This action only affects the public view of the product on the List.

### Changes to Certified Products

Any change to a certified product falls under one of two classes:  Class I or Class II.

### Determining Class of Change

All devices put on the market shall meet the requirements for which the product has been certified.  The Logo Certified Product List registers products/modules having a specific hardware and software version.  The product manufacturer is responsible to ensure that the Compliant Portion of all production units are identical to the certified version in all material aspects.

Any change to the Compliant Portion of the Logo Certified Product shall be documented in the Compliance Folder of the manufacturer, and the manufacturer shall notify the ADCB of those changes.  The manufacturer may initially classify the class of change; however the classification noted by the ADCB shall be the class of record.  The ADCB shall determine what additional testing is required, according to the Annex TBD guidelines and documentation provided.

      - Class I Changes

A Class I change is a product change that has no impact to the hardware or software within the Compliant Portion and no change to the declared functionality in the PICS.

For Class I change, no testing is required.  For any change in the product name or product version, the Compliant Folder will be revised to reflect the change, and the ADCB is responsible to effect the cahnge in the Logo Certified Product List.

      - Class II Changes

A Class II change is a software or hardware change to the Compliant Portion or to the functionality declared in the PICS.

The member shall supply the ADCB with the detailed change description, and estimated impact to the results of the tests implemented according to the CRSL in effect at the time of the certification testing at ADCL   The member may add a proposal on the scope of required re-testing.

The recertification testing is done by the ADCL using the current CRSL.  Based on the technical evaluation of the supplied change documentation, the ADCB may determine that certain prior test results may be reused.

The test requirements shallb e determined by ADCB based on the current CRSL.  Test reports from the former certification testing may be reused in portions or in its entirety depending on the test requirements and judgement of the ADCL.

Based on the review of product change documentation, the ADCB shall determin test cases to be conducted on the product.

The ADCB may require additional informaiton as necessary to determine test cases to be conducted.

      - Re-certification versus Change to Certification

The change classification to a certified product  is determined by the impact of that change on the Compliant Portin as shown in the table below.

| Class Category | Definition | Re-certification | Responsibilities |
| --- | --- | --- | --- |
| I | Software and/or Hardware change outside the Compliant Portion | No | Manufacturer is responsible for any testing, and informational changes and any test results are recorded in the Compliance Folder. |
| II | Software and/or Hardware change affecting the Compliant Portion | Yes | Any and all tests are to be performed by the ADCL. Changes and test results need to be recorded in the Compliance Folder |

For Class I changes, any testing are responsibility of the member, and testing can be conducted by the manufacturer, or by ADCL.  Test results shall be recorded in the Compliance Folder.  For Class II changes, any and all tests are to be performed by the ADCL.

### Module Policy

A Logo Certified Product may be designated as a Module at the option of the member responsible for the listing.  Desiginating the Logo Certified Product as a Module facilitates the reuse of the Module in a broader range of  End Products.  Certification requirements for the Module include all requirements for the Logo Certified Product, and additionally information described in this section.

A Module is a hardware and software combination that constitutes a Compliant Portion when installed within a specified hardware and software environment.  Typically, a Module will include a software driver, hardware module, and antenna.  Annex TBD gives an informative guideline on Modules.

The description of the Module on the Logo Certified Product List shall identify:

- hardware and software comprising the entire Compliant Portion,

- description essentional to operation of the module,

- hardware and software versions certified.

To certify a Module, the ADCB shall determine that

- the vendor supplied product satisfies all current certification requirements,

- the entire Compliant Portion is contained within the Module,

- the hardware and software environment required for the Module is sufficiently specified to ensure adherence of the Compliant Portion to the certified conditions.

The same Product change rules apply to Modules.

### Inheritance of Compliant Portion of Modules

When a certified Module is incorporated into a product, the integrator may change the antenna front end to the module.  The integrated product may be certified as a End Product when the ADCB determines that a ADCL RPT test yields results with acceptable outcomes.  Exception applies when there are no changes to the antenna front end, housing, or any characteristics impacting the Compliant Portion.

An example for a streamlined process for OEMs using a previsouly certified Module is shown in the table below as a guide.

| Vendor | Scenario | Required Testing | Approximate Cost | Documents |
| --- | --- | --- | --- | --- |
| Module Vendor | Initial Certification | PhyCT, RCT, IOT, PhyPT, NCT | Full certification testing cost and logo fee | All test reports and Compliance Folder |
| End Product Vendor | Initial Certification using a certified Module | PhyPT | PhyPT test cost and logo fee | PhyPT test report and Compliance Folder, plus a reference to Compliance Folder of Module |

### Integrated Products and Re-Branded Products

During its life cycle in the market, certified products may at times be integrated into larger systems, or re-branded without the Compliant Portion undergoing any material change.  In order to maintain traceability of the certified product through the market place, and to ensure that Compliant Portion certified status is indeed maintained, it is necessary to manage the integration and re-branding processes.

Using a new brand name for a previously certified product is allowed without additional logo fee if a new listing is not requested.  However, in such cases, the product shall bare clearly the original certification ID.  If a new listing is requested, a logo listing fee shall be charged, and a replica record created in the Logo Certified Product list with the new brand information.

Additionally, original design manufacturers (ODM) may design, manufacture, and certify a product or module for a second client company.  In such cases, the client company is responsible to create a new listing request for the product to be Logo Certified Product under the client company.

Any change in the Compliant Portion shall be processed under the change classifications scheme detailed in TBD.

  - Certification Process Exceptions

While the present Certification Program Reference Manual attempts to cover all contingencies that may occur during the Certification Program, inevitably, new needs and issues continually arise, and the program shall install processes to enable a flexibility in the program for continaul improvement.

In general contingencies will occur that interrupt the planned certification process.  These contingencies may occur at various steps along the device testing and certification process, and can generally be categorized into two characters:

- Problems arising in the course of executing the certification process:  Process Problem

- Problems arising due to strong and quantifiable objection by members: Disputes

The following describes the nominal process to handle such contingencies.

### Process Problem Resolution

There can arise may potential problems within the Logo Certification Process that can cause significant delays in certification of a vendors product.  These problems include, but are not limited to

- Test Harness issues,

- Interoperability issues between optional or conditional features of vendor devices,

- Specification issues, etc.

The following creates a process framework to provide at a minimum, a predictable path to resolution for any potential problem that may arise.

      - Change Request Process

In order to provide a solution to a problematic component of the certification process, the Teering Council provides its members the possibility to go through the Certification Change Request process (CCR).  The CCR process is based on three steps:  generation, evaluation, and resolution.

- CCR generation:  Vendor issues a CCR describing the problem and the test cases, PICS, specifications affected by this problem to the ADCB.  The ADCB is responsible to review the CCR and consult with the LL.

- CCR evaluation:  LL, along with the ADCB evaluates the CCR and endorses or rejects the CCR.  In the case of endorsing the CCR, the LL shall recommend a resolution. The endorsement is forwarded to the TAB.  The process shall take place within 5 business days from reception of the CCR.

- CCR resolution:  The LL has further 5 business days to implement any technical resolution to the CCR under the LL’s direct control and implement any necessary CRSL revisions. The TAB shall locate, as necessary a sponsor within the industry WG to affect any change in the SE technical specifications by the CCB process to institute a permanent fix to the problem.

      - CCR

The following describes the submittal and template for the Certification Change Request (CCR).

To be continued.

### Process Dispute Resolution

All disputes relating to product certification shall be resolved by the following process.

      - Overview

Disputes not immediately affecting the certification process, but nonetheless are deemed serious enough for a vendor to raise, can be processed in a procedural way.  The following is essentially a formalized disupute resolution, when other alternatives methods of are not available.

      - Binding Resolution

### Jurisdiction

A vendor may initiate a dispute resolution proceeding in accordance with this section for a dispute that relates to a certified feature or aspect of a Certified Product.

      - Informal Dispute Resolution

Prior to initiating formal dispute resolution the member  shall seek in good faith to resolve disputes informally.

        - Dispute Resolution Demand

If parties are unable to resolve the dispute within 30 days after the parties commenced informal efforts to resolve the dispute, either party may demand formal dispute resolution by delivering a demand in writing to the other party and to the Certification Program Manager.

        - Hearing by Dispute Resolution Committee

Each dispute brought pursuant to this section shall be heard by a dispute resolution committee defined by these rules.  The decidion fot he Dispute Resolution Committee shall be final and binding to both parties with respect to all certification matters.  The Dispute Resolution Committee is formed by the Certification Program Manager at his/her discretion.

        - Dispute Resolution Fee

Before the Dispute Resolution Committee considers the dispute, the party demanding adjudication of the dispute shall pay a non-refundable processing fee of $TBD.  The Certification Program Manager and the Dispute Resolution Committee shall not act unless the fee has been paid.  Where the final decision is deemed favorable to the party demanding adjudication, the fee shall be reimbursed.

        - Hearing Schedule

Upon receipt of the demand notice for the dispute resolution and payment of the processing fee, the Certification Program Manager shall promptly set up the Dispute Resolution Committee and send a copy of notice to parties involved via email with acknowledgement.  This notice shall define a “Notice Date” for purpose of calculating all further actions in the dispute resolution process.

If the decision fo the Dispute Resolution Committee requires action by a product manufacturer in order to bring a Certified Product into conformity with applicable certification requirements, the manufacturer shall either implement those changes with ninety days of the Notice Date, or submit a schedule that is deemed acceptable by the Dispute Resolution Committee and commence diligent efforts to implement the change in accordance with the imposed or submitted timeline.

        - Revocation of Certification

If the Dispute Resolution Committee deems that a manufacturer has failed to implement corrections as required by the binding resolution within the imposed or submitted timeline, and the Committee determines that no viable corrective action plan is in progress to resolve the dispute, the Dispute Resolution Committee can recommend to the Certification Program Manager that the product in question may be removed from the Logo Certified Product List.  The Certification Program Manager may then remove the product from the Logo Certified Product List until the Dispute Resolution Committee deems that the manufacturer has rectified the problem.

      - Dispute Resolution Committee

        - Composition

The Dispute Resolution Committee shall have the following composition:

TBD

        - Committee Actions

In considering a dispute, teh Dispute Resolution Committee shall consider the materials presented by each party involved to the dispute, and may in addition consier such other materials and information as it deems appropriate to settle the dispute.

A copy of all asssociated documents used in resolving the dispute sahll be mainted by the vendor and ADCB in the Compliance Folder.

        - Committee Decisions

The Dispute Resolution Committee shall decide on matters by a majority vote.

        - Role of Certification Working Group

All decisions of the Dispute Resolution Committee shall be binding and final upon the parties, provided however that it becomes evident that the dispute may be related to a flaw in the certification test or the certification process.  In that case, the Dispute Resolution Committee or either party in the dispute may request the matter by transferred to the industry WG for consideration.

      - Special Cases

TBD

  - Certification Requirement Waiver Process

The waiver process allows a manufacturer to apply for a dispensation (exception) from a specific certification requirement that the manufacturer is unable to meet and that will prevent or delay certification.  The waiver process is intended to be used in cases where a manufacturer believes it has a justifiable reason that a waiver should be granted.  The waiver process is not intended to deal with test harnss or test case problems that are preventing a device from achieving certification.  Such issues are dealt with the CCR process.

Waiver requests are reviewed by an independent body, the Waiver Review Board (WRB)  which reviews and takes decisions on waiver requests.  This body must be independent of the manufacturer submitting the waiver request, and have no conflict of interest with respect to the waiver request application for the device.  Waiver requests are confidential and are not shared between manufacturers.

Waiver requests are submitted to the Certification Program Manager through the ADCB, using the Waiver Template (see Annex TBD).  The Program Manager forwards the request to the Waiver Review Board for consideration.  Waivers are reviewed on a case by case basis.  Submission of a waiver request does not guarantee consideration nor approval of the waiver request by the WRB.  A waiver request can be submitted at any time in the certification testing process and the process can be applied for both inital and re-certification of Logo Certified Products.

  - Monitoring of Logo Certified Product Validity

The LL is the organization primarily responsible to police the continued validity of Logo Certified Products and Modules in the market.

LL is responsible to compile an ongoing verification record of Logo Certified products out in the market.  All such records are submitted to the CPM at intervals defined between the LL and CPM.  The LL shall furnish requested details of the verification to the CPM upon request.

CPM is responsible to take mitigative, corrective and preventive action to the non-compliant Member, ADCB, and the ADCL involved using the following procedure outlined, upon discovery of a certified product that breaches the original certified condition of the product.

The ADCB shall take full responsibility to drive and manage the mitigation, correction, and preventative action on the part of the Member, ADCL, and self.

### Corrective and Preventive Action

CPM shall discuss with the involved ADCB the issuance in writing of the Mitigation, Corrective, and Preventive Action Request (MCPAR), to the ADCB, the non-compliant Member and the ADCL.  The MCPAR shall indicate the following:

Detail on the observed breach of certification requirements

Assigns ADCB as party responsible to close the open action items identified on the MCPAR

Orders  Member to account for units already in the market

Orders ADCB, ADCL, Member to institute corrective action of this event and preventive action of similar 		events

Order ADCB and ADCL to work with Member to mitigate the impact of released devices

Order ADCB and ADCL to institute coorective action for this event, and preventive action to forestall 		future similar events

After set date, obtain the report on the corrective and preventive action from Member, ADCB and ADCL

CPM shall evaluate validity and effectiveness of the response.

ADCB shall monitor the corrective and preventive action after a set time indicated by response on the 		MCPAR. When subsequent verification determines that corrective and preventive actions are 		effective, ADCB shall report to CPM, and the case can be closed; if it is found to be 	insufficient, CPM shall initiate complete review of ADCB and ADCL appointed status.

  - Selection and Maintenance of Logo Certification Program Golden Units

The Logo Certification Program shall maintain at least two Golden Unit implementations of each device type from the industry.  The Golden Units are reference devices that are voluntarily submitted by manufacturers, and satisfy the following criteria:

- Golden Units are Logo Certified Products

- Golden Units have sponsoring ADCB as point of contact for handling adminstrative issues related to the Golden Units as it concerns  Logo Certification processes.

- Golden Units are furnished to the ADCLs by the manufacturer

- Golden Unit manufacturers participate in interoperability test events of the Logo Certification Program, as it relates to the device types.

# Test Harness

In order to institute a stable Logo Certification Program, a reliable testing program is essential.  One basis of such a program is the use of well defined “test harness” with known performance envelope.  Any such test harness shall be officially “validated” by the CPM as capable of performing the required testing.  All ADCL are required to use validated test harnesses to peform Logo Certification testing.

The Application Profile devices requires testing through the following five stages as described in Chapter 2.2:

PhyCT- Physical Radio/PLC/wireline Conformance Testing

PCT-Protocol Conformance Testing

IOT-Interoperability Testing

NCT-Network Conformance Testing

PhyPT-Physical Performance Testing

All test harnesses tasked to perform the five stage test (the test harness may or may not be able to run then entire set) need to be able to complete the entire set of tests as described in the applicable CRSL.

Once a test harness(es) is validated to perform the CRSL tests, all such instances of the test harness at ADCL need to be monitored for continual validity of the entire Logo Certification Program.  Therefore,  it is critical that tests be repeatable and reproducible (gage R&R), i.e. repeated measurement results are consistent, and that those measurements are reproducible by other laboratories that may be using different test harnesses.  The Certification Program shall maintain a specific level of gage R&R of less than or equal to 10% across all ADCL for specific representative tests in the five categories of testing.  The representative tests (reference primary category tests) shall be selected by the LL on an ongoing basis, and performed across the ADCL at least once a year.  The nature of the gage R&R method requires that the primary reference tests be parametric in nature, and the test results be well defined number based on those parameter measurements.  The specific measurement and system analysis (MSA) applied for the primary reference test shall be developed by LL.

  - Validation of Test Harness

### Submittal Process

A test harness subject to consideration as part or whole of a validated test system for Logo Certification shall satisfy the following submittal criteria:

- be available for commercial purchase by testing laboratories and Member companies

- support the Test Control Interface (TCI) for relevant Primary Test Categories and protocol layers

- include scripting capability for automated test runs

- supply test cases in accordance with the CRSL; implementation must be at least one complete test category out of five Primary Test Categories

- as appropriate, subject to calibration cycles

The CPM shall review the test harness submittal for the above minimum submittal criteria (may be outsourced to LL), to be an eligible candidate system of detailed evaluation for validation as an official Logo Certification Test Harness.

### Evaluation Process

A test harness, accepted for consideration as part or whole of a validated test system for Logo Certification, shall undergo technical evaluation by the LL, and the LL is responsible to sign-off on the technical viability of the system as a test harness for the industry.

The validation process shall at minimum involve the following steps:

- Execution of the relevant CRSL scope, through the TCI, as implemented for the Primary Test Category of the test harness, and obtaining the expected results with the Golden Units designated by the CPM for the Product Logo Certification Program.

- Examination of the upper tester and lower test logs, along with the over-the-air results, to determine the proper recording and evaluation of the test result.

- Test harness shall exhibit a gage R&R of relevant reference Primary Test Category tests of less than 5%.

- Test harness shall exhibt a gage R&R of relevant reference Primary Test Category tests of less than 10% between homogenous and heterogenous test harness set-ups at different laboratory locations (i.e. in ADCLs).

Note that the procedure to perform the Gage R&R using the reference Primary Test Category tests are the responsibility of the LL.