OpenSG Edge Conformance Task Group

OpenHAN – Abstract Test Cases

Rev 0 - Work in Progress

October 20, 2010

Table of Contents

Disclaimer	5

Change History	5

1.	Introduction	6

1.1.	Purpose	6

1.2.	Scope	6

1.3.	Acronyms and Abbreviations	6

1.3.1.	Testing Methodology	6

1.4.	Terminology	6

1.5.	Other Considerations and References	7

2.	Pre-requisites	8

2.1.	Implementation Under Test	8

2.2.	HAN Device Functionality	8

3.	Implementation Conformance Statements	10

3.1.	Abbreviations and special symbols	10

3.2.	ICS Proformas - Applications	10

3.2.1.	Logical Device Type	10

3.2.2.	Application Control	11

3.2.3.	Application Measurement and Monitoring	14

3.2.4.	Application Processing	14

3.2.5.	Application Human-Machine Interface	14

3.3.	ICS Proformas – Communications Requirements	15

3.3.1.	Communications Interface Support	15

3.3.2.	Commissioning	15

3.3.3.	Control	15

3.4.	ICS Proformas – Security Requirements	15

3.4.1.	Access	15

3.4.2.	Integrity	15

3.4.3.	Accountability	15

3.4.4.	Registration	15

3.4.5.	Enrollment	15

3.5.	ICS Proformas – Performance Requirements	16

3.6.	ICS Proformas – Operations, Maintenance and Logistics Requirements	16

4.	Test Methodology	17

4.1.	Example for U-Snap Load Control module	17

4.1.1.	Justification	17

4.1.2.	Description	17

4.2.	Example for In Home Display - Conformance Testing	18

4.2.1.	Justification	18

4.2.2.	Description	18

4.3.	Example for EMS with multiple physical interfaces	19

4.3.1.	Justification	20

4.3.2.	Description	20

5.	Abstract Test Cases	21

5.1.	Application	21

5.1.1.	Application Control	21

5.1.2.	Application Measurement and Monitoring	21

5.1.3.	Application Processing	21

5.1.4.	Application Human-Machine Interface	21

5.2.	Communications	21

5.3.	Security	21

5.4.	Performance	21

5.5.	Operations, Maintenance and Logistics	21

List of Tables

Table 1: Logical HAN Device Types	9

Table 3: Logical Device Type	11

Table 3: Communications Interfaces	15

List of Figures

Figure 1: System Component Overview	8

Figure 2: Wi-Fi USNAP Module	17

Figure 3: ZigBee SEP2.0/802.15.4 In Home Display	18

Figure 4 EMS	19

Disclaimer

This document is work in progress. It is anticipated that there will be updates resulting from further work within OpenSG and the work of the SGIP Test and Certification committee.

Change History

| Date | Rev | Change | By |
| --- | --- | --- | --- |
| October 20 2010 | R0: Work in Progress | Initial document | Phil Beecher |

Introduction

Purpose

The purpose of this document is to define the context, test methodologies and test cases for products claiming compliance with OpenHAN which can then be used as a basis for creating a comprehensive Conformance and Interoperability test program.

Scope

This document describes the Abstract Test Cases for OpenHAN.  It summarises the Methodology and Context  for the product / device / implementation under test and provides the Proforma background information including PICS, PIXIT etc ...

Acronyms and Abbreviations

Testing Methodology

See R2 for full definition and context w.r.t. Test Method

ASP: Abstract Service Primitive

IUT: Implementation Under Test

PCO: Point of Control and Observation

PDU: Protocol Data Unit

PICS: Protocol implementation comformance statement

PIXIT: Protocol Implementation Extra Information for Testing

SUT: System Under Test

UT: Upper Tester, behaves as a User of the Implementation Under Test

Terminology

Device: A device is a product which incorporates hardware, typically including communications hardware which is included as part of the compliant portion. A device will usually be deployed at the edge of the utility network.

System: Part or whole instance of product functionality, usually associated with software portion of product

Product: Hardware and/or software implementation to be tested for compliance / interoperability

Module: Hardware and software implementation that incorporates a compliant portion

Other Considerations and References

[R1] UCAIug Home Area Network System Requirements Specification Version 2.0 – August 30, 2010

[R2] X291 OSI Conformance Testing Methodology and Framework for Protocol Recommendations for ITU-T Applications – Abstract Test Suite Specification available from:

http://www.itu.int/rec/dologin_pub.asp?lang=e&id=T-REC-X.291-199504-I!!PDF-E&type=items

Pre-requisites

Implementation Under Test

Figure 1 shows an Overview of the System Components to be considered.  The service interfaces are shown as.  Note that HAN devices also include a service interface.  In the case for OpenHAN, the Implementation Under Test will implement functionality as shown in the Residential Customer domain.

Figure 1: System Component Overview

HAN Device Functionality

The OpenHAN SRS v2.0 identifies Logical HAN device types as shown in Table 1.  The functionality for each logical device type (optional and mandatory features) is described in Section 3 of R1 OpenHAN SRS V2.0 and summarized in the ICS proformas in 3

|  | Logical Device | Primary Functionality |
| --- | --- | --- |
| 1 | Energy Services Interface (ESI) | Network Control and Coordination |
| 2 | Utility ESI | Network Control and Coordination |
| 3 | Programmable Communicating Thermostat (PCT) | HVAC Control |
| 4 | In-Home Display (IHD) | Display of Energy Information |
| 5 | Energy Management System (EMS) | Controlling end-device energy |
| 6 | Load Control | Resource Control |
| 7 | AMI meter | Energy Measurement |
| 8 | HAN Non-Electric Meter | Resource Measurement |
| 9 | Smart Appliance | Intelligent Response |
| 10 | Electric Vehicle Supply Equipment (EVSE) | Charging a PEV |
| 11 | Plug-in Electric Vehicle (PEV) | Electric transportation |
| 12 | End-Use Measurement Device (EUMD) | Metering of an end-device load |

Table 1: Logical HAN Device Types

Implementation Conformance Statements

Abbreviations and special symbols

Notations for requirement status:

M	Mandatory

O	Optional

O.n	Optional, but support of at least one of the group of options labeled O.n is required

N/A	Not applicable

X	Prohibited

Item Number: Status	Status is conditional on support of item number

ICS Proformas - Applications

This section defines the proformas for the Implementation Conformance Statements for the Applications Requirements.

Logical Device Type

| Item number | Item description | Reference | Status | Support Y/N |
| --- | --- | --- | --- | --- |
| LDT1 | Is this device capable of acting as an Energy Services Interface (ESI)? | R1.Table1:1 | O.1 |  |
| LDT2 | Is this device capable of acting as a Utility ESI? | R1.Table1:2 | O.1 |  |
| LDT3 | Is this device capable of acting as Programmable Communicating Thermostat? | R1.Table1:3 | O.1 |  |
| LDT4 | Is this device capable of acting as an In-Home Display? | R1 Table1:4 | O.1 |  |
| LDT5 | Is this device capable of acting as Energy Management System? | R1 Table1:5 | O.1 |  |
| LDT6 | Does this device support Load Control Functionality? | R1 Table1:6 | O.1 |  |
| LDT7 | Is this device capable of acting as AMI Meter ? | R1 Table1:7 | O.1 |  |
| LDT8 | Is this device capable of acting as a HAN non-electric meter? | R1 Table1:8 | O.1 |  |
| LDT9 | Is this device capable of acting as a Smart Appliance? | R1 Table1:9 | O.1 |  |
| LDT10 | Is this device capable of acting as Electric Vehicle Supply Equipment (EVSE) ? | R1 Table1:10 | O.1 |  |
| LDT11 | Does this device behave as Plug-in Electric Vehicle (PEV) | R1 Table1:11 | O.1 |  |
| LDT12 | Is this device capable of acting as an End-Use Measurement Device (EUMD) | R1 Table1:12 | O.1 |  |

Table 3: Logical Device Type

Application Control

| Item number | Item description | Reference | Status | Support Y/N |
| --- | --- | --- | --- | --- |
| AC1 | HAN device shall accept control signals from one or more authorized parties | R1.Table3:1 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:M LDT7:N/A LDT8:N/A LDT9:M LDT10:M LDT11:M LDT12:N/A |  |
| AC2 | HAN device shall limit or reduce energy consumption in response to control signal receipt | R1,Table3:2 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:M LDT7:N/A LDT8:N/A LDT9:M LDT10:M LDT11:M LDT12:N/A |  |
| AC3 | HAN device shall resume previous operational state (as appropriate) following receipt of Control Signal that cancels, expires or overrides a previous Control Signal in effect | R1,Table3:3 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:M LDT7:N/A LDT8:N/A LDT9:M LDT10:M LDT11:M LDT12:N/A |  |
| AC4 | HAN device shall acknowledge receipt of Control Signal when requested | R1,Table3:4 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:M LDT7:N/A LDT8:N/A LDT9:M LDT10:M LDT11:M LDT12:N/A |  |
| AC5 | HAN device shall acknowledge execution of Control | R1,Table3:5 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:M LDT7:N/A LDT8:N/A LDT9:M LDT10:M LDT11:M LDT12:N/A |  |
| AC6 | HAN device shall acknowledge execution failure of Control Signal (i.e. exceptions) | R1,Table3:6 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:M LDT7:N/A LDT8:N/A LDT9:M LDT10:M LDT11:M LDT12:N/A |  |
| AC7 | HAN device shall communicate any consumer or device-initiated overrides or delays in response | R1, Table3:7 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:M LDT7:N/A LDT8:N/A LDT9:M LDT10:M LDT11:M LDT12:N/A |  |
| AC8 | HAN device shall implement its response to a control signal at a specific future time as set forth in the control signal | R1 Table 3:8 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:0 LDT7:N/A LDT8:N/A LDT9:0 LDT10:M LDT11:M LDT12:N/A |  |
| AC9 | HAN device shall resume previous operational state (as appropriate) following expiration of a control signal | R1 Table 3:9 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:0 LDT7:N/A LDT8:N/A LDT9:0 LDT10:M LDT11:M LDT12:N/A |  |
| AC10 | HAN device shall support randomization of scheduled control signal start ad stop times to prevent unnecessary stress on the electric grid | R1 Table 3:10 | LDT1:N/A LDT2:N/A LDT3:M LDT4:N/A LDT5:M LDT6:0 LDT7:N/A LDT8:N/A LDT9:0 LDT10:M LDT11:M LDT12:N/A |  |

Application Measurement and Monitoring

[Note: Insert tables here for Measurement and Monitoring Requirements]

Application Processing

[Note: Insert tables here for Processing Requirements]

Application Human-Machine Interface

[Note: Insert tables here for HMI Requirements]

ICS Proformas – Communications Requirements

Communications Interface Support

| Item number | Item description | Reference | Status | Support Y/N |
| --- | --- | --- | --- | --- |
| CIF1 | Does this device include 802.15.4 /ZIP Interface? | tbc | O.1 |  |
| CIF2 | Does this device include an 802.11/Wi-Fi Interface? | tbc | O.1 |  |
| CIF3 | Does this device include a HomePlug interface? | tbc | O.1 |  |
| CIFS4 | Others? | tbc | O.1 |  |

Table 3: Communications Interfaces

Commissioning

[Note: Insert tables here for Communications Options]

Control

[Note: Insert tables here for Communications Options]

ICS Proformas – Security Requirements

Access

[Note: Insert table here for Security Access Options]

Integrity

[Note: Insert table here for Security Integrity Options]

Accountability

[Note: Insert table here for Security Accountability Options]

Registration

[Note: Insert table here for Security Registration Options]

Enrollment

[Note: Insert table here for Security Enrollment Options]

ICS Proformas – Performance Requirements

[Note: Insert table here for Performance Options]

ICS Proformas – Operations, Maintenance and Logistics Requirements

[Note: Insert table here for OML Options]

Test Methodology

Example for U-Snap Load Control module

The following diagram shows the test methodology where the Implementation Under Test is a USNAP module that incorporates Load Control Functionality with SEP2.0 and a Wi-Fi/802.11 compatible radio.

Justification

The test methodology chosen is the Local Test Method. The Local Test Method is used because:

- The upper service boundary of the IUT is a standardized hardware interface that can be used for the Testing purpose. (see R2, 11.3.2. c)

- The specification of the hardware upper interface of the IUT (i.e. the USNAP interface) fully defines the mapping between the relevant ASP and PDUs and the realization of the interface. (see R2, 11.3.2. d)

- The Upper Tester can be completed located within the Test System (see R2, 11.3.2. e)

Description

- The X-Service-Provider is the 802.11 Radio Interface.

- X-Service-Provider acts as PCO (observation using Wireshark or similar)

- The X-ASPs are actually Physical Layer PDUs – see R2 I.2 a) and b)

- The lower tester is part of the test harness and implements an 802.11 wireless interface, a method of generating frames to be transmitted and receiving and processing frames as part of the Test Control Program coordination.

- P1 -Pn PDUs are the data frames transmitted over air in 802.11 frames (P1).  P1- Pn layers include 802.11 PHY and MAC, IPv6, UDP, http, XML.

Example for In Home Display - Conformance Testing

Figure 3 shows the test methodology where the Implementation Under Test is an In Home Display (IHD) with ZigBee SEP2.0 implementation and a single Communications interface supporting 802.15.4 / ZigBee ZIP.

Justification

The test methodology chosen is the Distributed Test Method (R2 11.3.3). The Distributed Test Method is used because:

- The upper service boundary of the IUT is a human user interface that is used for the Testing purpose. (see R2, 11.3.3. c)  No requirements are placed on the realization of the interface in SUT.

- Because the upper interface of IUT is a human user interface, the human operator of the SUT fulfills all/some of the requirements of the TCP (see R2, 11.3.3. g)

Description

The test system implements a test harness in which:

- The X-Service interface is implemented as 802.15.4-2006 operating at 2.4GHz (Channel Page 0)

- The Lower Tester (LT) is included as a component of the test harness and incorporates an ESI emulation comprising

  - 802.15.4 PHY and MAC, Zigbee IP, etc

- P1 to Pn PDUs are sent in 802.15.4 data frames transmitted between IUT and Lower Tester.  P1 == 802.15.4 PHY frames, Pn compresies 802.15.4 frames, 6loWpan, ZIP, UDP, http, XML

- The Upper Tester is a human Test System Operator interacting with keypad / display device

- The Y-Abstract Service Primitive (ASP) interface comprises the IHD display device and push buttons

- The Test Coordination Procedure, TCP, comprises an automated test program as part of the Test System, with a HMI to allow the Test System Operator to control the test procedure and observe the results.

Example for EMS with multiple physical interfaces

The following diagram shows the test methodology for interoperability testing where the Implementation Under Test is an EMS with Wi-Fi and 802.15.4 Physical layer interfaces.  In this case the EMS will be required to communicate with multiple HAN devices concurrently using multiple physical interfaces.

Justification

The test methodology chosen is a General Model for Multi Party Testing. This Test Method is used because:

i) The IUT is required to communicate with multiple other real devices on multiple communications interfaces.

Description

The test system implements a test harness in which:

- 1st X-Service interface is implemented as 802.15.4-2006 operating at 2.4GHz (Channel 0)

- 2nd X-Service Interface is implemented as 802.11 Radio Interface

- X-Services PCO Observation is achieved using Wireshark or similar

- Lower Testers 1 and 2 emulate HAN network devices, e.g. Load Control Devices.

- Upper Testers 1 and 2 emulate Control Functions e.g. Utility signals / 3rd Party service provider signals

Abstract Test Cases

Application

Application Control

[Note: Insert test cases for Application Control Requirements as defined in 3.2.2]

Application Measurement and Monitoring

[Note: Insert test cases for Measurement and Monitoring Requirements]

Application Processing

[Note: Insert test cases for Processing Requirements]

Application Human-Machine Interface

[Note: Insert test cases for HMI Requirements]

Communications

[Note: Insert test cases for Communications Requirements]

Security

[Note: Insert test cases for Security Requirements]

Performance

[Note: Insert test cases for Communications Requirements]

Operations, Maintenance and Logistics

[Note: Insert test cases for OML Requirements]

# Text boxes

policy

Figure 2: Wi-Fi USNAP Module

Test System

SUT

X-Service-Provider

TCP

IUT

P1 to Pn

PDUs

X-ASPs

PCO ASPs

UT

LT

Figure 3: ZigBee SEP2.0/802.15.4 In Home Display

SUT

Test System

X-Service-Provider

TCP

IUT

P1 to Pn

PDUs

X-ASPs

Y-ASPs

UT

LT

Figure 4 EMS

LT2

LT1

PCO

PCO

UT2

X-Service-Providers

(802.11 and 802.15.4)

IUT

(P)-PDUs

X-ASPs

Y-ASPs

UT1

(P)-PDUs

PCO

Lower Tester

Control Function

Test Coordination Procedures