OpenADE 1.0 System Requirements Specification

Version: Draft v0.4

Release Date: 1/20/2010

Acknowledgements

The following individuals and their companies are members of the UCAIug OpenSG and have contributed and/or provided support to the work of the OpenADE System Requirements Specification:

- …

The OpenADE Task Force wishes to thank all of the above-mentioned individuals and their companies for their support of this important endeavor, as it sets a key foundation for interoperable Smart Grid of the future.

Document History

Revision History

Date of this revision: Oct. 29, 2009

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 0.1 | 10/16/09 | Steve Van Ausdall | Initial draft “shell”. | N |
| 0.2 | 10/29/09 | Steve Van Ausdall | Added data elements | N |
| 0.4 | 1/20/09 | Steve Van Ausdall | Resolved comments from Arthur Salwin | Y |

Open Issues Log

Last updated: Oct. 29, 2009

| Issue Number | Issue Date | Provided By | Summary of the Issue |
| --- | --- | --- | --- |

Contents

1	Introduction	6

1.1	Purpose	6

1.2	Scope	7

1.3	Acronyms and Abbreviations	8

1.4	External Considerations and References	8

1.5	Document Overview	8

2	Architecture Overview	11

2.1	Architecture Vision	11

2.2	Architecture Guiding Principles	12

2.3	Architectural Considerations	12

3	OpenADE Systems Architecture	14

3.1	OpenADE Business Architecture View	14

3.2	Integration Requirements Specification	16

3.2.1	Functional Requirements – Business Processes	16

3.2.2	Functional Requirements – Integration Services	16

3.2.3	Technical Requirements – Integration Services	16

3.3	OpenADE Application Architecture View	19

3.4	OpenADE Data Architecture View	20

3.4.1	Consumption Data Requirements	20

3.4.2	Meter Reading and Event View	21

3.5	OpenADE Technical Architecture View	22

3.5.1	Security Standards	22

3.5.2	Service Patterns	23

3.5.3	Governance	24

4	Appendices	25

4.1	Terms and Definitions	25

List of Figures

Figure 1.  OpenADE component diagram showing the scope of the service definition effort.	7

Figure 2.  The Open Group Architecture Framework (TOGAF) architecture development cycle.	9

Figure 3.  OpenADE Stakeholders Overview	11

Figure 4.  Overview of Business Process Flows	14

Figure 5.  Overview diagram of Logical Components	15

Figure 6.  Services that are provided or consumed by OpenADE Provider component.	19

Figure 7.  Class relationship diagram representing the meter reading and related events.	22

# Introduction

Open Automatic Data Exchange (OpenADE) is an industry-led initiative under the Open Smart Grid (OpenSG) subcommittee within the UCA International Users Group (UCAIug).  The OpenADE Task Force defines systems requirements, policies and principles, best practices, and services, required for information exchange and control between 3rd Party energy usage data service providers (3rd Party), and public utility web services, and customers. OpenADE, as an open user group forum, is developing a set of utility-ratified requirements and specifications for utilities and 3rd Parties to adopt and implement.  The end-state of this effort will contribute to the development of open and interoperable utility data sharing applications.  Please see the OpenADE Charter for additional information.

The OpenADE group is organized with three sub-groups:

- Use Case Team: to develop common business process models and functional requirements.

- SRS Team: to develop overall systems architecture principles, integration requirements and specifications.

- Service Definition Team: to develop standards-based, platform independent integration services that support the business processes, adhere to the architecture principles and patterns, and are open and support extensible interoperability.

The main goal of the task force is to work with utilities and 3rd Parties to develop requirements and specifications necessary to enable 3rd Parties to gain access to consumer usage.  This will be achieved by defining and making the following OpenADE related items available to the market:

- Common business processes and functional requirements

- Common architecture principles and patterns

- Common information requirements and model

- Common integration services (functional & informational)

- Tested interoperability between vendor products

Our current charter can be found on Smartgridipedia, at http://www.smartgridipedia.org/index.php/OpenADE_Charter.

## Purpose

The purpose of this document is to provide both the functional and technical guidance and requirements needed to serve as the “rules of engagement” for messaging and data exchange to achieve interoperability.  This would lead to open and interoperable components that can be delivered with different vendor products and/or solutions within the scope of OpenADE.  The functional requirements will be driven by business processes and the technical requirements will be driven by desired architectural principles and best practices.

## Scope

The scope of OpenADE 1.0 SRS includes authorization and transfer of consumer consumption. Future functional scope may include prices and billing related information.  The SRS defines the logical components and business functions in order to identify the interfaces that must be specified to enable interoperability across different implementations, for many utilities to many 3rd Parties.  It includes architectural aspects and specific requirements.  The inputs include OpenADE use cases, as well as industry best practices and standards, including information models and other specifications.

Figure 1.  OpenADE component diagram showing the actors and components.

OpenADE SRS does not include the following items that are typically a part of solution architecture.  Some of them are or have been addressed by other parts of the OpenSG initiative.  Others will need to be dealt with specifically for each implementation.

- Network and hardware infrastructure architecture

- Operational architecture

- Testing methodology and architecture

- Internal application architecture

## Acronyms and Abbreviations

This subsection provides a list of all acronyms and abbreviations required to properly interpret the OpenSG OpenADE System Requirements Specification.

| ADE | Automatic Data Exchange |
| --- | --- |
| SRS | System Requirements Specification |
| SDO | Standards Development Organization |
| CIM | IEC TC57 Common Information Model |
| TOGAF | The Open Group Architecture Framework |
| UML | Unified Modeling Language |
| DDL | Data Definition Language |
| XSD | XML Schema |
| WSDL | Web Services Definition Language |
| ESM | Enterprise Semantic Model |
| WS-I | Web Service – Interoperability (W3C) |
| OASIS | Organization for the Advancement of Structured Information Standards |

## External Considerations and References

The work of OpenADE SRS is dependent upon the best practices available from the following entities and standards organizations:

- Internet Standards (TBD)

          - TCP/IP, HTTPS, OAuth, AtomPub

- IEC TC57 Working Group 14 (IEC 61968) (Common Information Model)

- Additional Standards TBD

## Document Overview

TOGAF 9.0 defines four architecture domains that are commonly accepted as subsets of overall enterprise architecture, all of which TOGAF is designed to support, see Figure 2:

- Architecture Vision defines overall architecture guiding principles, goals and objectives and desired traits.

- The Business Architecture defines the business strategy, governance, organization, and key business processes.

- The Information Systems Architecture, including the following.

  - The Data Architecture describes the structure of an organization's logical and physical data assets and data management resources.

  - The Application Architecture provides a blueprint for the individual application systems to be deployed, their interactions, and their relationships to the core business processes of the organization.

- The Technology Architecture describes the logical software and hardware capabilities that are required to support the deployment of business, data, and application services. This includes IT infrastructure, middleware, networks, communications, processing, standards, etc.

Figure 2.  The Open Group Architecture Framework (TOGAF) architecture development cycle.

As such, the document will be structured as follows:

Section 2 describes the overall Architecture Vision for the system, including Guiding Principles, Architectural Considerations, and the OpenADE Reference Model, all relevant to providing a consistent framework within which the four architecture components can be developed.

Section 3 provides details on the following:

- Business Architecture:  This will refer to work products produced by the Use Case and Service Definition Teams of OpenADE, which includes the list of use cases and integration requirements and business services at the functional level.

- Data Architecture:  This provides the technical level requirements relative to how the OpenADE data should be modeled and represented consistently across all integration services to ensure semantic interoperability.

- Application Architecture: This provides the technical level requirements relative to how applications are modeled as logical components, and what services each logical component may provide or consume. This should be an instantiation of the business services identified within the Business Architecture.

- Technology Architecture: This provides the technical level requirements relative to how services will interact with each other to support end-to-end AMI business processes.

Section 4 contains the Appendices, which includes terms and definitions, logical components list, integration requirements list, and integration services view.

# Architecture Vision

The following diagram gives an overview of the key stakeholders. Key elements of this problem space are that we want to enable a 3-way authorization handshake, and allow for many-to-many data transfers between many utilities and 3rd Parties.

Figure 3.  OpenADE Stakeholders Overview

## Architectural Goals and Guiding Principles

Architecture guiding principles are rules of engagement designed to ensure that all aspects of the implementation fit within a well-defined framework.  These principles, discussed and agreed upon with all stakeholders of the OpenADE, are used to drive the architectural approach and patterns to be implemented.  These principles should not be taken lightly as they imply what and how the overall goals of OpenADE will be met.  Each of the principles has a level of effort and cost implications for utilities and 3rd Parties looking to adopt this specification.  Adherence to these principles can be adjusted for specific cases driven by time and budget constraints.  These exceptions should be approved by all stakeholders and must be documented.

- Exchanges of data cross enterprise boundaries

  - Industry best practices must be followed

  - The most interoperable and widely supported technologies must be used to ensure adoption regardless of development and deployment platforms used

  - Security and privacy of customer information is of utmost importance, since transfers must use public networks, and sensitive customer information may be exchanged across enterprise boundaries

- Recommendations must promote and enable interoperability

  - Many utilities need to be interoperable with many 3rd Parties, so everyone must use the same protocols and application messages in order to ensure compatibility

  - Recommendations must be specific and prescriptive, actionable and testable

- Must meet the goals of several different types of stakeholders

  - Requires an open process to allow discussion and negotiation of the recommendation

- Forwards and backwards version compatibility is needed

  - Existing implementations must remain operational when either side adds future extensions

## Architectural Considerations

OpenADE as a system needs to be architected with requirements that cover the entire spectrum of business, technical, and market needs.  The following list of architecture attributes will be used as guidelines for OpenADE systems requirements development.

- System quality attributes discernable at runtime

  - Performance, Security, Availability, Functionality, Usability, Scalability

- System quality attributes requiring assessment for evaluation

  - Modifiability, Portability, Reusability, Integrability, Testability

- Business Qualities

  - Time to market; Cost; Projected life time of the system; Targeted market; Rollout schedule; Extensive use of legacy system

- Qualities directly related to the architecture

  - Conceptual integrity; Correctness and completeness; Useability

# OpenADE Systems Architecture

## OpenADE Business Architecture View

The primary business flows include configuration, registration, and authorization of 3rd Party providers, and exchange of authorized data, as shown in the following diagram.

Figure 4.  Overview of Business Process Flows

The business architecture is the primary topic covered in the “Business and User Requirements” document, where additional use cases and requirements are located.

#### Logical Components List

Logical Components are used in this document to organize interfaces (integration services) for OpenADE.  These functional components may be mapped to specific physical components for a particular implementation. Following is a table listing all major logical components that will provide some functions to support ADE business processes.  All services will be organized accordingly.

| # | Acronym | Logical Components | Description / Key Business Functions | Notes | Map to IEC 61968-9 |
| --- | --- | --- | --- | --- | --- |
|  |  | Utility |  |  |  |
|  |  | 3rd Party |  |  |  |
|  |  | Customer |  |  |  |
|  |  | Authorizing Entity |  |  |  |

The following diagram shows the components involved in data exchanges.

Figure 5.  Overview diagram of Logical Components

## Integration Requirements Specification

### Functional Requirements – Business Processes

The business processes that have been developed as part of OpenADE are listed as follows.  Note that the “OpenADE Business and User Requirements” contains the details of each business process (use case).

- ADE Discovery

  - 3rd Party and Utility agree to SLAs and configure OpenADE services

  - 3rd Party retrieves listing of supported operations with extensions and versions

  - Utility retrieves listing of supported operations with extensions and versions

  - 3rd Party and Utility subscribe to notifications

- ADE Authorization

  - Consumer Grants Permission

  - Consumer Extends Permission

  - Consumer Terminates Permission

- ADE Publication

  - 3rd Party Requests or Subscribes to Consumer Data

  - Utility Provides Consumer Data to 3rd Party

### Functional Requirements – Integration Services

Using a consistent methodology to identify integration requirements from the use cases list above, the Services Definitions Team identified the following requirements.

The goals of the service definition specification are as follows.

- Access control shall be possible to enforce given an authenticated (certified) access request token and associated secret key.

| Use Case Scenario | Integration Requirement | Functional Description of the Service | Operation Pattern | Service Name | Service Provider |
| --- | --- | --- | --- | --- | --- |
|  |  | Requested from service consumer (3rd Party) to service provider (Utility) to obtain an unauthorized request token. |  | Request Token | Utility |
|  |  | 3rd Party passes unauthorized request token to service provider for authorization. (Redirect) |  | User Authorization | Utility |
|  |  | After grant or deny, verification code is returned to service consumer. |  | Consumer Callback | 3rd Party |
|  |  | Service consumer requests access token with signed request from 3rd Party. Token is returned if successful in the response. |  | Access Token | Utility |

### Technical Requirements – Integration Services

Integration services that are well defined, understood and managed are the linchpin of an open and interoperable implementation between the utility enterprise and other business entities.  Following is a list of guiding principles for integration services design:

- Common protocol and business semantics should be used to achieve loose coupling of end-point service (directly or indirectly)

- Services should be representative of a unique unit of work and reusable across business functions.

- Services should be reusable across common practices of utilities.

- Service design should be driven by business requirements and reflected in the architecture.

- Service design should be governed with a common approach and framework to achieve conceptual integrity.

- Services should be abstract, precise (no overloading, but allow for polymorphic services), atomic but composable, testable, etc.

- Integration layer is preferable (but not required) to achieve guaranteed delivery, managed integration, etc. and to enable process orchestration and complex event processing where necessary.

- Services to support B2B integration scenarios shall be identified to allow for more specific security and Service Lever Agreement (SLA) implementation requirements.

- Service level agreement should be defined to support key architecture qualities: security, reliability, performance, availability, scalability, data quality, information fidelity, etc.

Based upon the above-mentioned guiding principles for services design, here is the table of integration services attributes to be defined for each of the business and physical services of OpenADE.  The collection of the services attributes constitutes the integration technical requirements of OpenADE.

| Integration Services Attribution Name | Description |
| --- | --- |
| Service Identifier | Unique identifier for each service that is provided by a logical component. |
| Service Name | Name of the service |
| Business Scenario Identifier | The business process from which the service is derived and supports. |
| Integration Requirement Identifier | Unique identifier for the integration requirement upon which the service was identified. |
| Integration Requirement Name | The name of the integration requirement. |
| Service Status | The status of the service (Active, Inactive, ?) |
| Service Version | The version of the service. (A version mechanism needs to be developed, which may contain a timestamp on when it is operational.) |
| Interaction Pattern | Identify a desired interaction pattern for this service: fire-forget, request-reply, etc. |
| Interaction Type | Type of interaction (real time, batch, event driven) |
| Service Choreography | Define the need for complex service interaction between provider and consumer, or participate in a stateful business process. |
| Service Operation | Applied service patterns for service operation (such as create, created, etc. see patterns section). |
| Information Object | The associated information object for the service for input and/or output. |
| Service Message Size | The average size of each message or file. |
| Service Message Volume | The average number of messages or files per time interval. |
| Service Frequency | The frequency of each transmission for batch type interactions (e.g. as needed, hourly, daily, weekly) |
| Service Peak Factor | Peak payload size and peak volume, and peaking factor. |
| Service Availability | Availability requirements to support business process and business continuity. |
| Service Level Security | Service level security requirements for authentication and authorization. |
| Data Level Security | Payload security requirements to drive encryption at whole message level or element/attribute level. |
| Service Owner | The owner of the definition of the service. |
| IEC 61968 Message Type | The corresponding IEC 61968 message type (XSD) name for the Information Object, if applicable. |

In addition to these “OpenADE Service” definitions, the Authorization process will use the OAuth web authorization delegation specification. Usage of that standard for this purpose is detailed in the next section.

#### Use of Open Authorization

(Content pending decision from task force on this topic)

In addition to the

## OpenADE Application Architecture View

OpenADE application architecture view provides a list of Logical Components and the integration services they either provide or consume.  A utility or a vendor could map their actual application portfolio for their ADE solution and derive at the services that their physical applications will need to provide or consume.

The following diagram shows, from a Logical Component point of view, the integration services they either provide or consume.  They also show the corresponding Logical Components and their related services. This logical view of application services does not imply a point-to-point service interaction, but rather indicates the functional provider-consumer relationship.  Following is an example of services provided and consumed by the “Utility Web Portal” component.

The diagrams only include those Logical Components that have services identified.  As more use cases and services are identified, they will be updated accordingly.

Figure 6.  Services that are provided or consumed by OpenADE Provider component.

## OpenADE Data Architecture View

Based on OpenADE use cases, five semantic model views are provided:

- Authorization Request

- Authorization

- Consumption Readings Request

- Consumption Readings Notification

- Consumption Readings

The published XML Schemas for OpenADE services have the detailed attributes and data types associated with each of the entities listed in the diagrams below.

### Consumption Data Requirements

The list of logical data elements needed for the main “Consumption Readings” publication contains the following items.

| Data Element | Description | CIM Element |
| --- | --- | --- |
| Utility Identifier | Used to distinguish between data elements from different utilities | ServiceSupplier name |
| User Resource | A key value, generated during the authorization process, to be used by the utility and 3rd party to represent a user / service point combination. | CustomerAuthorization |
| Service Point Name | An identifier (name) for the (metered) point at which the commodity was delivered to the customer. | ServiceDeliveryPoint name |
| Service Type | The type of commodity related to the readings, such as energy, gas, water, etc. | ServiceCategory kind |
| Meter Readings Start Time | The date and time of the beginning of the period during which the readings apply. | MeterReading startTime |
| Meter Readings End Time | The date and time of the end of the period during which the readings apply. | MeterReading endTime |
| Reading Type | The type of measurement represented by the value of the reading (e.g. energy, voltage, pressure) | ReadingType kind |
| Interval Duration | Number of seconds within each reading interval. | ReadingType intervalLength |
| Interval Reading | The number of measured units delivered, for this interval. | IntervalReading value |
| Reading Units | The units of the reading value (e.g. W, Wh, V) | ReadingType unit |
| Reading Source | Where the reading originated: from the meter, or calculated during VEE (estimate / actual) | MeasurementValueSource name |
| Reading Date / Time or Interval | The start or end time of each individual reading, or which interval within the block. | MeasurementValue timeStamp or IntervalReading sequenceNumber (new) |

To help understand how the elements relate to each other, the following shows a preview of what selected sections of a typical message might look like.

[…]	(header, etc. will go here)

<MeterReading>

<endTime>2009-06-23T00:00:00-07:00</endTime>

<startTime>2009-06-22T00:00:00-07:00</startTime>

[…] (user resource, etc. will go here)

<IntervalReading>

<MeasurementValueSource>

<name>ACTUAL</name>

</MeasurementValueSource>

<value>2.716549</value>

<sequenceNumber>24</sequenceNumber>

</IntervalReading>

</IntervalReadingList>

<ReadingType>

<kind>ENERGY</kind>

<intervalLength>3600</intervalLength>

<unit>Wh</unit>

</ReadingType>

</IntervalBlock>

[…] (full message could contain multiple MeterReading elements)

Note that some extensions may have been included in the above that are not shown in the logical data model diagram in the next section, but these will be in sync when the actual message structure is built.

### Meter Reading and Event View

This view is a center piece of ADE data architecture on meter reading and events. It provides a view of the logical data model used to construct the following messages:

- MeterReading

- ActivityRecord

Figure 7.  Class relationship diagram representing the meter reading and related events.

## OpenADE Technical Architecture View

Given a large variety of integration technologies that exist in the market place and in the utility enterprises, it would be up to each utility to implement the OpenADE systems requirements specification that fit with their chosen technology infrastructure and architecture goals.  However, regardless of the technologies, the following architectural issues are important and needs to be addressed when it comes to achieving interoperability.

### Security Standards

A major component of OpenADE is ensuring that protected resources, including data, can and will be secured to prevent unauthorized access. This responsibility originates with the utility, where the data is obtained, and is passed to 3rd Party providers when customers authorize their use of specific utility data. To ensure that data is not provided to unauthorized parties, the following security measures are to be used.

(Content requires discussion with task force)

### Service Patterns

Service naming standards are important to achieve a level of “plug & play” at the run time environment.  It implies the semantics of the service and its operations.

The OpenADE services naming convention has the following rules:

- Information Object – Collection of entities to describe an object in a business context.

- Service Name – Service naming convention follows the information object in a business process for an interface definition.

- Operation Name – Operation name indicates a specific action that will be performed to the Information Object. Here is a list of operation naming patterns utilizing IEC 61989 verbs (See IEC61968-1 Specification for details):

- The following verbs are used for service/operation provided by the master system that owns the Information Object to entertain the request for the specified action implied by the verb.

    - Create

    - Change

    - Cancel

    - Close

    - Delete

- The following verbs are used for service/operation provided by systems that are interested in receiving the Information Object as the result of the specified action implied by the verb.  This can be invoked by the master system or an intermediary to supply the Information Object.

    - Created

    - Changed

    - Closed

    - Canceled

    - Deleted

- The following verbs are used for query type services provided by the master system of the Information Object.

    - Get

    - Show

    - Reply

- The following verbs are not used within OpenADE.

    - Subscribe

    - Unsubscribe

### Governance

Governance defines the rules by which parties participating in interoperability (integration, or data exchange) efforts can change the interfaces and components providing and consuming them, in order to maintain efficient operation. For OpenADE, governance includes guidelines recommended for addition or extension of standard interfaces, as well as modifications to or extensions to become part of the standard.

(Content on this topic needs to be discussed)

#### Extensions

This section describes how extensions are to be made, to allow additional data elements to be added by individual implementations, as well as for the next version of the recommendation, so that existing providers and consumers can continue to operate with or without those additions.

(Content on this topic needs to be discussed)

# Appendices

## Terms and Definitions

This subsection provides the definitions of all terms required to properly interpret the OpenSG OpenADE SRS.

| Term | Definition |
| --- | --- |
| Advanced Metering | Technology that allows two-way communications between the utility and the meter. This communication enables the ability to analyze energy consumption resulting in more efficient demand response systems. |
| Advanced Metering Infrastructure (AMI) | The infrastructure built around advanced metering allowing the utility and consumer to communicate in real time with respect to energy consumption. Based on the information collected, the utility is able to obtain an accurate reading of demands, while consumers are able to modify their usage to save energy. |
| Automated Meter Reading | Automated meter reading is a subcategory of AMI which allows for communication devices to transfer data from a meter to the utility or from a meter to the 3rd Party. |
| Business Service Provider | Software delivered over the internet as web services. The platform for integrating these web services is the enterprise service bus. |
| Daily Consumption | The amount of energy a customer uses in a 24 hour period. This information is used to drive business intelligence solutions. |
| Energy Data Management | Analyzing meter data for consumption by backend systems. Often times these backend systems will measure load, calculate demand response, billing intervals, etc. |
| ESB | Enterprise Service Bus. The ESB provides the features necessary for a service oriented architecture implementation by providing a place to host all of the web services. |
| IEC | The International Electrotechnical Commission (IEC). The IEC TC57 maintains an electric utility focused information model called CIM (Common information model). |
| IEC 61968 | International standards for Energy Distribution Managements Systems, respectively, specify a Common Information Model (CIM) for utility data exchange, Applications Programming Interfaces (API) for application integration (GID), and XML messaging standards. |
| Logical Data Model | A representation of an organization’s data based upon entities and attributes of those entities. A logical data model is often a logical representation of a business' integration or business requirements. |
| Meter Bus (M-bus) | Allows for the interconnecting of many different utility measuring units (gas, electric, water, etc.) The M-Bus acts as the central station for these different utilities to communicate with. |
| Meter Data Management | A system for storing, processing, consuming and analyzing large quantities of meter data. |
| Smart Grid | The term smart grid represents the digital upgrade of our distribution and long distance transmission grid allowing for increased energy efficiency as well as a boost in optimization of current systems. |
| SLA | Service Level Agreement: the part of a service contract where the level of the services are agreed upon between two systems. |
| Smart Meters | Meters with extra functionality that allow for more accurate and useful meter readings. This extra functionality allows the meter to collect usage data and transmit this data back to the utility over a network. |
| SOA | Service oriented architecture – The concept of grouping business functionality around business processes. These services are than packaged as interoperable services. A SOA architecture allows for the transmission of data between multiple systems as they participate in multiple business processes. |
| SOAP | Simple Object Access Protocol (XML protocol) – A protocol for exchanging xml messages for web services in a service oriented architecture implementation. |
| Supervisory Control and Data Acquisition (SCADA) | SCADA systems monitor and control the electric power generation, transmission, and distribution. |
| UML | Unified Modeling Language is a general purpose modeling language commonly used for object/data modeling. |
| WSDL | Web Services Description Language is an xml format used to describe web services and the messages that interface with the web services. |
| XML | Extensible Markup Language – general purpose markup language for creating custom mark-up languages. |
| XSD | A description describing a specific xml document focusing primarily on the restraints and structure of that xml document. |
| Utility Sub Metering | An implementation that allows for a multi tenant property to bill tenants for individual energy usage. This is most commonly implemented in apartments and condominiums. |

| CIM Term | Definition |
| --- | --- |
| ActivityRecord | Records activity for an Asset, Location, Document, PowerSystemResource, Organization or ErpContact (e.g., operator, market participant, etc.) at a point in time. An activity may be for an event that has already occurred or for a planned activity. The PowerSystemResource relationship records events regarding the logical function being provided by the resource in the electrical network (independent of the particular asset providing the function). The Asset relationship records history about the particular equipment, independent of where it is currently being used in the electrical network. The Location relationship records events associated with the geographical location. The Customer relationship records history regarding the customer independent of the logical network or particular assets being used to serve the customer. |
| EndDeviceAsset | This type of AssetContainer performs one or more EndDevice functions. One type of EndDeviceAsset is a Meter Asset which can perform metering, load management, connect/disconnect, accounting functions, etc. Some EndDeviceAssets, such as ones monitoring and controlling air conditioner, refrigerator, pool pumps may be connected to a MeterAsset. All EndDeviceAssets may have communication capability defined by the associated ComFunction(s). An EndDeviceAsset may be owned by a consumer, a service provider, utility or otherwise. |
| IntervalBlock | Used within a MeterReading to identify a time sequence of Readings of the same ReadingType. |
| IntervalReading | Data captured at regular intervals of time. Interval data could be captured as incremental data, absolute data, or relative data. The source for the data is usually a tariff quantity or an engineering quantity. Data is typically captured in time-tagged, uniform, fixed-length intervals of 5, 10, 15, 30, or 60 minutes. Interval Data is sometimes also called "Interval Data Readings" (IDR). |
| Location | The place, scene, or point of something where someone or something has been, is, and/or will be at a given moment in time. It may be the spatial location of an actual or planned structure or set of point-oriented structures (as a substation, structure, building, town, etc.), which may be defined as a point or polygon. It may also be the path of a underground or overhead conductor. |
| Meter | This is generic logical meter object. |
| MeterAsset | The physical asset that performs the metering role of the ServiceDeliveryPoint. Used for measuring consumption and detection of events. |
| MeterAssetModel | Documentation for a type of a meter asset of a particular product model made by a manufacturer (Organisation). These types of meters are used to measure power consumption. There are typically many instances of an asset associated with a single asset model. |
| MeterReading | Used to convey quantities that are measured by a meter. |
| MeterReadingPurpose | The purpose of the meter reading, such as initial reading, final reading, peridic reading, demand reading, etc. This information is often used to distinguish final and initial readings when there is a tenancy change at a service location. |
| MeterTypeAsset | Documentation for a generic meter that may be used for design purposes. Rather than being associated with CustomerMeter, it is associated with EnergyConsumer as it may be used for many applications, such as tie line metering, in addition to customer metering. |
| Reading | Used to convey a specific value measured by a meter or other asset. Each Reading is associated with a specific ReadingType. |
| ReadingQuality | The quality of a specific reading. Note that more than one Quality may be applicable to a given Reading Value. This field is not necessary unless problems or unusual conditions occur because Quality for each Reading Value is assumed to be 'Good' unless stated here otherwise. |
| ReadingType | Used to identify the type of data that is conveyed by a specific Reading. |
| ServiceDeliveryPoint | There can be multiple service points at a single ServiceLocation, each one identified as a ServiceDeliveryPoint. They deliver service in accordance with a CustomerAgreement. |
|  | A service point exists within a ServiceLocation and is used at the place where a meter may be installed. Properties include: |

# Comments

Remove Portal distinction