OpenADE 1.0 Service Definition - Common

Version: Draft v0.94

Release Date: 7/13/2010

Acknowledgements

The following individuals and their companies have contributed and/or provided support to the work of the OpenADE 1.0 Service Definition - Common:

- Chad Maglaque from Microsoft

- Charles Spirakis from Google

- Dave Mollerstuen from Tendril Networks

- Debbie Tillman from SCE

- Gerald Gray from CIMple Integrations

- Jeffrey Kenward from DTE Energy

- Jeremy McDonald from SCE

- Mark Ortiz from Consumers Energy

- Mamta Shetty from SCE

- Shawn Hu from Xtensible Solutions / SCE

- Steve Van Ausdall from Xtensible Solutions / SCE

- Wayne Dennison from Xtensible Solutions / SCE

The OpenADE Task Force wishes to thank all of the contributors to OpenADE, especially the above-mentioned individuals and their companies for their support of this important endeavor, as it sets a key foundation for an interoperable Smart Grid.

Document History

Revision History

Date of this revision: July. 13, 2010

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 0.5 | 2/25/10 | Steve Van Ausdall | Initial draft discussion version. | N |
| 0.6 | 3/1/10 | Steve Van Ausdall | Additional details about defined resources | N |
| 0.8 | 4/8/10 | Steve Van Ausdall | Simplified, following approved plan | N |
| 0.9 | 4/15/10 | Steve Van Ausdall | Addressed comments raised in walkthrough and from Jeff Kenward. | N |
| 0.92 | 4/22/10 | Steve Van Ausdall | Additional changes from SD team | Y |
| 0.93 | 6/17/10 | Wayne Dennison Steve Van Ausdall | Additional Cleanup and Updates from F2F meeting and Review, new schema structure from PAP10 | Y |
| 0.94 | 7/13/2020 | Wayne Dennison | Updated Schema and streamlined service operation documentation. | N |

Open Issues Log

Last updated: July. 13, 2010

| Issue | Issue Date | Provided By | Summary of the Issue |
| --- | --- | --- | --- |

Contents

1	Introduction	7

1.1	Rights / Management / Governance	7

1.1.1	Intellectual Property Rights	7

1.1.2	CIM Object Models	7

1.1.3	Service Resource Definitions	8

1.2	Referenced Specifications	8

1.3	Referenced Guidance	8

1.4	Namespaces	8

2	Resources	8

2.1	Security	9

2.1.1	Authentication	9

2.1.2	Authorization	9

2.2	Message document format	9

2.3	Payload entities	9

2.3.1	Usage File Format	11

3	Technological Concerns	12

3.1	Event Notification	12

4	Discovery	12

5	Metadata	12

6	Versioning	12

7	Extensibility	13

8	Concurrency	13

9	Functional Areas	13

9.1	Common	13

10	Service Resource Definitions	13

10.1	Energy Usage Information	13

10.1.1	CustomerAgreement	14

10.1.2	CustomerAuthorisation	14

10.1.3	DateTimeInterval	14

10.1.4	Direction  «enumeration»	14

10.1.5	EnergyUsageInformation	14

10.1.6	IntervalReading	14

10.1.7	MeterAsset	15

10.1.8	MeterReading	15

10.1.9	ReadingKind  «enumeration»	15

10.1.10	ReadingQuality	15

10.1.11	ReadingType	15

10.1.12	ServiceCategory	16

10.1.13	ServiceDeliveryPoint	16

10.1.14	ServiceKind  «enumeration»	16

10.1.15	ServiceSupplier	16

10.1.16	SupplierKind  «enumeration»	16

10.1.17	UnitMultiplier  «enumeration»	17

10.1.18	UnitSymbol  «enumeration»	17

10.1.19	Customer	17

10.2	Physical Schema Diagrams	17

11	Appendix A	20

11.1	Consumption XSD and Example	20

12	Appendix B	20

12.1	SUBSEQUENT ASSOCIATED REFERENCE DOCUMENTATION	20

List of Figures

Figure 1: Batch Payload Logical UML Data Model Diagram	9

Figure 2: OpenADE Schema – Overview	17

Figure 4: OpenADE Schema – Expanded 2	19

# Introduction

Access to energy management resources is of paramount interest to consumers and Smart Grid service providers. In order to provide access to customer data, energy service providers and 3rd Party consumers can use this best practice recommendation in order to develop early implementations. As the standards development organizations recommend alterations, stakeholders will decide how to handle these changes.

OpenADE represents the internet data service provided by energy service providers (Utilities). It is the goal of OpenSG to promote interoperability by providing an easy to use, simple set of commonly available technologies. Toward this goal, our direction is to define XML formats for payload data which can be used with; A resource-oriented architecture or service-oriented architecture.

This document is focused on the common payload definition. For information on service operations, refer to Appendix B.

## Rights / Management / Governance

### Intellectual Property Rights

This document and the information contained herein is provided on an "AS IS" basis. UCAIug DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY OWNERSHIP RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

UCAIug requests any party that believes it has a patent claim that would necessarily be infringed by implementations of this UCAIug work, to notify UCAIug immediately, so that fair and reasonable licensing terms can be negotiated. UCAIug invites any party aware of applicable undisclosed patent claims to contact the UCAIug. UCAIug may include such claims on its website, but disclaims any obligation to do so.

UCAIug takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this UCAIug recommendation, can be obtained from the UCAIug. UCAIug makes no representation that any information or list of intellectual property rights will at any time be complete, or that any claims in such list are, in fact, Essential Claims.

### CIM Object Models

Information on the management of rights and governance for IEC can be found at the page below.
http://www.iec.ch/tctools/patent-guidelines.htm

The recommendations herein build on work owned by the IEC. Required extensions identified in this recommendation will be submitted to the IEC, and will be tracked for inclusion in the model.

### Service Resource Definitions

If necessary, UCAIug is willing to work with standards development organizations to incorporate additional aspects of this recommendation into a standard, including the specification of how to use profiled (restricted) CIM objects within different environments, and possibly the information object definitions themselves.

## Referenced Specifications

- [1] OpenADE B&UR 1.0 - http://osgug.ucaiug.org/sgsystems/OpenADE/Shared%20Documents/Forms/AllItems.aspx?RootFolder=%2fsgsystems%2fOpenADE%2fShared%20Documents%2fBusiness%20and%20User%20Requirements

- [2] OpenADE SRS 1.0 - http://osgug.ucaiug.org/sgsystems/OpenADE/Shared%20Documents/Forms/AllItems.aspx?RootFolder=%2fsgsystems%2fOpenADE%2fShared%20Documents%2fSRS

- [3] IEC CIM (TC 57 61968/61970) - http://tc57.iec.ch

- [4] IEC TC57 WG14 61968-1-2 – Profile for use of CIM with WS-I Basic Profile

## Referenced Guidance

- [G1] 3PDA – Security Profile for Third Party Data Access (ASAP-SG)
http://osgug.ucaiug.org/utilisec/Shared%20Documents/Forms/AllItems.aspx?RootFolder=%2futilisec%2fShared%20Documents%2fThird%20Party%20Data%20Access%20Security%20Profile

## Namespaces

The subject of namespaces is important, because the namespace identifies the domain managing the definitions of protocol resources and formats. OpenSG proposes to use the format below for the namespace.

http://osgug.ucaiug.org/ns/2010/06/oade

Extensions to the schema that are backwards and forwards compatible will not change the namespace, but will include a version number inside the definition.

# Resources

Some of the design decisions are being driven by the desire to provide an interface for the available data objects. For Example; objects could be exposed as resources and have operations which specify URL’s and Object ID’s (though they may not be required). Note: Alignment with the ZigBee Alliance Smart Energy Profile 2.0 is of interest, along with other related industry efforts, as documented in NAESB PAP10 recommendations.

Since this document is the first to define the general-purpose conventions, several resources were identified allowing consumers access to the resources they want. However, this document is not intended to provide details of all resources and service operations, but the currently identified resources are available in Appendix B for reference.  The following “data” objects are currently in scope, as defined in [1] OADE-B&UR and [2] OADE-SRS. They will be delivered via client services in a set of (chunked) batch XML files.

- MeterReading – Represents a collection of readings associated with a specific user key and meter point

  - IntervalReading – A durational measurement

  - Reading – An instantaneous measurement (future)

- ReadingType – Represents a type of reading (e.g. hourly kWh) used by a MeterReading

- ServiceSupplier – The supplier of utility service

- CustomerAgreement – Represents the agreement for service at a location

- Customer – The identifier for the customer associated with the data

- CustomerAuthorisation – Represents the agreement to share data with the 3rd Party

- ServiceDeliveryPoint – The logical point at which the readings were obtained

- MeterAsset – The physical measurement device that captured the readings

## Security

Because these services define resources that could be used to cause damage, access must be restricted to only those data objects that have been authorized. Security guidance is specified in [G1] 3PDA.

### Authentication

Authentication is a process through which an identity is proven. Users may have an identity at each domain involved in sharing their data, or they may use a federated identity managed at a separate domain. These identities are associated at each domain with specific authorizations. OpenADE does not require a specific method for authentication, but does require an authentication method which provides a reliable, secure way for customers to protect access to their information.

### Authorization

Authorization is the process of requesting and granting access to protected user resources. OpenADE shall allow for the creation and management of user access details.  Consumer Request Parameters are addressed in subsequent documentation, please refer to Appendix B for additional information.

## Message document format

“Message document” refers to the type of XML returned by resource requests. This initial release of OpenADE uses CIM-based XML, according to the schema provided.

## Payload entities

Payload entities will conform to the message document schema. They will contain an XML representation of CIM classes.

The batch payload defined allows a number of object instances to be included in a single transfer. Subscription will be automatic, as defined in the implemented profile, based on the resources authorized by the user. For profile details (subsequent associated reference documentation) please refer to Appendix B for additional information.  All data elements are “create or update” so that if the ID does not exist, then the representation should be interpreted as a new instance of the type containing the ID. If the ID has been transferred previously, then it should be interpreted as an update to the fields specified, and elements not specified should not be modified.

A logical view of the schema for the initial payload structure is shown below. An XSD is provided as well in Appendix A. The model is also posted to the OpenADE Sharepoint. This model was developed during initial PAP10 harmonization efforts, and will be submitted to and refined within NAESB Smart Grid PAP10 Task Force. It contains structures from ZigBee Alliance Smart Energy Profile 2.0, for OpenADE internet services to eventually be accessed from devices or applications within the HAN environment. The model below is a restricted subset of the full PAP10 model.

Figure 1: Batch Payload Logical UML Data Model Diagram

### Usage File Format

Domain data objects build on the IEC CIM model. In general, complex type schema elements will be named using the CIM class. For listings of fields, see the details for each resource, defined in Section 10. The XSD for the format is included in the archive in Section 11.1, Consumption XSD and Example.

An example is shown below.

<?xml version="1.0" encoding="UTF-8"?>

<m:EnergyUsageInformation xsi:schemaLocation="http://osgug.ucaiug.org/ns/2010/06/ade OpenADE-Schema.xsd" xmlns:m="http://osgug.ucaiug.org/ns/2010/06/ade" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

<ServiceSupplier>

<ID>123</ID>

<Customer>

<ID>12345678910</ID>

<CustomerAgreement>

<ID>56421587</ID>

<CustomerAuthorisation>

<validityInterval>

<end>2011-12-17T00:00:00Z</end>

<start>2010-12-17T00:00:00Z</start>

</validityInterval>

</CustomerAuthorisation>

<ServiceDeliveryPoint>

<ID>85945261</ID>

<MeterAsset>

<ID>19283746</ID>

</MeterAsset>

<MeterReading>

<ID>1</ID>

<IntervalReading>

<endTimeStamp>2010-12-17T11:00:00Z</endTimeStamp>

<ReadingQuality>

<quality>interpolated</quality>

</ReadingQuality>

<timeStamp>2010-12-17T10:00:00Z</timeStamp>

<value>0.0035</value>

</IntervalReading>

<ReadingType>

<ID>1001</ID>

</ReadingType>

</MeterReading>

<name>Guest House</name>

<ServiceCategory>

<kind>electricity</kind>

</ServiceCategory>

</ServiceDeliveryPoint>

</CustomerAgreement>

</Customer>

<kind>utility</kind>

<name>Utility Company</name>

</ServiceSupplier>

<ReadingType>

<ID>1001</ID>

<defaultQuality>validated</defaultQuality>

<direction>delivered</direction>

<kindReading>energy</kindReading>

<multiplier>k</multiplier>

<name>Energy Delivered kWh</name>

<unitSymbol>Wh</unitSymbol>

</ReadingType>

</m:EnergyUsageInformation>

# Technological Concerns

This section contains guidance for the general scenarios below.

## Event Notification

Clients will gain access to user data as specified in Appendix B followed by transfer of published data resources.

# Discovery

Discovery of available resources, retrieval of the supported operations and resource types are  not specified in this document.  Supporting documentation of Service Operation documentation may include these details.  Refer to Appendix B for additional information

# Metadata

No metadata publication is specified in this document, but supporting documentation of Service Operation documentation may include this information. Refer to Appendix B for additional information.

# Versioning

As additional capabilities are added to the interface definition, the minor version number of the definition will be incremented. If compatibility with existing counterparts must be broken, the namespace and the major version number will be updated, as per [9] 61968-1-2. Namespaces shown below are temporary, and will be updated as determined by the participants.

<xs:schema targetNamespace="http://osgug.ucaiug.org/ns/2010/06/oade" xmlns:m="http://osgug.ucaiug.org/ns/2010/06/oade" xmlns:xs="http://www.w3.org/2001/XMLSchema" elementFormDefault="qualified" version="1.0">

# Extensibility

To enable backwards and forwards compatibility, schema validation should be turned off in operational systems to allow new schema elements to pass without update or rebuild. Previous incarnations are not capable of 100% guaranteed anticipation of future elements. As such, these unrecognized elements shall be ignored.   Also, additional platform-specific handling features should be implemented to support compatibility.

# Concurrency

No data shall be directly editable by clients, so concurrency controls are not included in this document.

# Functional Areas

## Common

The flows in this section represent general-purpose functions which are necessary for all protected resource publications. Please note, operations to support 3rd Party registration, certificate transfer, and test of configuration were judged to be premature for this initial version, as such, these operational steps will require manual processes, and volume/quantity of steps will be low. They may be specified in a future release.

Refer to Appendix B for additional information such as definition of the methods to be used to transfer payload data

# Service Resource Definitions

For details of available profiles, extensions, initiations, authorization, access methods and how to incorporate these details, please refer to Appendix B.

## Energy Usage Information

This data resource represents a collection of readings, related to a specific reading type at a specific service delivery point and metering device. Meters may provide readings of different values, such as KWh and Voltage. Each could be authorized separately or as a group by the user. Individual meter readings are represented by IntervalReadings, which represent a measurement over a specified time interval, or Reading for instantaneous measurements.

The structure presented here is similar to the schema developed within IEC 61968-9, however it is not directly compatible, due to the need for some additional data elements and structural differences. It is, however, conformant to the more general CIM UML model. Extensions to the model are marked with [ADE Extension] in the description.

### CustomerAgreement

Agreement between the Customer and the ServiceSupplier to pay for service at a specific ServiceLocation. It records certain billing information about the type of service provided at the ServiceLocation and is used during charge creation to determine the type of service.

| Name | Type | Description |
| --- | --- | --- |
| ID | string | A Model Authority issues mRIDs. Given that each Model Authority has a unique id and this id is part of the mRID, then the mRID is globally unique. |

### CustomerAuthorisation

Holds an authorisation for access to specific user-private data granted to a 3rd Party service provider. [OpenADE Extension - Specialization of "Agreement"]

| Name | Type | Description |
| --- | --- | --- |
| validityInterval | DateTimeInterval | Date and time interval this agreement is valid (from going into effect to termination). |

### DateTimeInterval

Interval of date and time.

| Name | Type | Description |
| --- | --- | --- |
| end | dateTime | Date and time that this interval ended. |
| start | dateTime | Date and time that this interval started. |

### Direction  «enumeration»

| Name | Type | Description |
| --- | --- | --- |
| delivered |  |  |
| received |  |  |
| net |  |  |

### EnergyUsageInformation

### IntervalReading

Data captured at regular intervals of time. Interval data could be captured as incremental data, absolute data, or relative data. The source for the data is usually a tariff quantity or an engineering quantity. Data is typically captured in time-tagged, uniform, fixed-length intervals of 5, 10, 15, 30, or 60 minutes.

Note: Interval Data is sometimes also called "Interval Data Readings" (IDR).

| Name | Type | Description |
| --- | --- | --- |
| endTimeStamp | dateTime | End interval timestamp |
| timeStamp | dateTime | The start date and time of an interval reading |
| value | float | Value in type of float |

### MeterAsset

Physical asset that performs the metering role of the ServiceDeliveryPoint. Used for measuring consumption and detection of events.

| Name | Type | Description |
| --- | --- | --- |
| ID | string | Object identifier |

### MeterReading

Set of values obtained from the meter.

| Name | Type | Description |
| --- | --- | --- |
| ID | string | Object identifier |

### ReadingKind  «enumeration»

Kind of reading.

| Name | Type | Description |
| --- | --- | --- |
| energy |  |  |

### ReadingQuality

Quality of a specific reading value or interval reading value. Note that more than one Quality may be applicable to a given Reading. Typically not unsed unless problems or unusual conditions occur (i.e., quality for each Reading is assumed to be 'Good' unless stated otherwise in associated ReadingQuality).

| Name | Type | Description |
| --- | --- | --- |
| quality | string | Quality, to be specified if different than 'Good'. |

### ReadingType

Type of data conveyed by a specific Reading.

| Name | Type | Description |
| --- | --- | --- |
| ID | string | A Model Authority issues mRIDs. Given that each Model Authority has a unique id and this id is part of the mRID, then the mRID is globally unique. |
| defaultQuality | string | Characteristics of a data value conveyed by a specific Reading, which allow an application to understand how a specific Reading is to be interpreted. |
| direction | Direction | Specifies the direction of flow of the measurement. |
| kindReading | ReadingKind | Kind of reading. |
| multiplier | UnitMultiplier | Multiplier for 'unit'. |
| name | string | Name of an attribute. |
| unitSymbol | UnitSymbol | Unit in symbol |

### ServiceCategory

Category of service provided to the customer.

| Name | Type | Description |
| --- | --- | --- |
| kind | ServiceKind | Kind of service. |

### ServiceDeliveryPoint

Logical point on the network where the ownership of the service changes hands. It is one of potentially many service points within a ServiceLocation, delivering service in accordance with a CustomerAgreement. Used at the place where a meter may be installed.

| Name | Type | Description |
| --- | --- | --- |
| ID | string | A Model Authority issues mRIDs. Given that each Model Authority has a unique id and this id is part of the mRID, then the mRID is globally unique. |
| name | string | Name of an attribute. |

### ServiceKind  «enumeration»

Kind of service.

| Name | Type | Description |
| --- | --- | --- |
| electricity |  |  |

### ServiceSupplier

Organisation that provides services to Customers.

| Name | Type | Description |
| --- | --- | --- |
| ID | string | Unique identifier of this service supplier. |
| kind | SupplierKind | Kind of supplier. |
| name | string | The human-readable name for the service supplier. |

### SupplierKind  «enumeration»

Kind of supplier.

| Name | Type | Description |
| --- | --- | --- |
| utility |  |  |
| retailer |  |  |
| other |  |  |

### UnitMultiplier  «enumeration»

The unit multipliers defined for the CIM

| Name | Type | Description |
| --- | --- | --- |
| k |  | Kilo 10**3 |

### UnitSymbol  «enumeration»

The units defiend for usage in the CIM

| Name | Type | Description |
| --- | --- | --- |
| VArh |  | Reactive energy in volt ampere reactive hours |
| Wh |  | Real energy in what hours |

### Customer

Organisation receiving services from ServiceSupplier.

| Name | Type | Description |
| --- | --- | --- |
| ID | string |  |

## Physical Schema Diagrams

The XML schema for this resource is shown below.

Figure 2: OpenADE Schema – Overview

Figure 3: OpenADE Schema – Expanded 1

Figure 4: OpenADE Schema – Expanded 2

# Appendix A

## Consumption XSD and Example

The files embedded below are the XML Schema Definition (XSD) described in this document, and the sample XML.

# Appendix B

## SUBSEQUENT ASSOCIATED REFERENCE DOCUMENTATION

The service Operation files embedded below are derivatives of; This document and decisions made while considering the content of this document. Considerable community input and effort has been expended towards attaining the overall architectural concept (providing access to customer data) and Extensions which were considered viable during the authoring of this document.  Additional community input and consensus building is expected during the lifespan of this document.

- “OpenSG OpenADE SD – REST”  - The REST document which clarifies on Demand access to resources.

- “OpenSG OpenADE SD – Web Services”  -  Extensions to support WS-I Basic Profile web service operations.