OpenADE 1.0 Service DEFINITION - Web ServiceS Extension

Version: Draft v0.2

Release Date: 4/8/2010

Acknowledgements

The following individuals and their companies have contributed and/or provided support to the work of the OpenADE 1.0 Service Definition  - WS* Extension:

- Chad Maglaque from Microsoft

- Charles Spirakis from Google

- Dave Mollerstuen from Tendril Networks

- Gerald Gray from CIMple Integrations

- Mark Ortiz from Consumers Energy

- Shawn Hu from Xtensible Solutions / SCE

- Steve Van Ausdall from Xtensible Solutions / SCE

The OpenADE Task Force wishes to thank all of the contributors to OpenADE, especially the above-mentioned individuals and their companies for their support of this important endeavor, as it sets a key foundation for an interoperable Smart Grid.

Document History

Revision History

Date of this revision: Apr. 8, 2010

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 0.1 | 4/8/10 | Gerald R. Gray | Initial draft discussion version. | N |
| 0.2 | 4/14/10 | Gerald R. Gray | Added example wsdls and xsds provided by Shawn Hu. | N |

Open Issues Log

Last updated: Apr. 8, 2010

| Issue | Issue Date | Provided By | Summary of the Issue |
| --- | --- | --- | --- |

Contents

1	Introduction	7

1.1	Rights / Management / Governance	7

1.1.1	Intellectual Property Rights	7

1.1.2	CIM Object Models	7

1.1.3	Service Definitions	8

1.2	Referenced Standards	8

1.3	Referenced Guidance	8

1.4	Namespaces	8

2	service	8

2.1	Service Format / syntax	9

2.2	Message document format	9

2.3	Payload entities	9

2.3.1	resources	9

3	Patterns	10

3.1	Creating, Updating, Deleting	10

3.2	Query, request and response (Retrieve) formats	10

3.2.1	Format	10

3.2.2	Category	10

3.2.3	Reference Expansion	10

3.2.4	Sorting	11

3.2.5	Filtering	11

3.2.6	Iteration	11

3.2.7	Conditional Retrieval	11

3.3	Event Notification	11

3.4	Batch transfers	11

4	Discovery	12

5	Metadata	12

6	Extensibility	12

7	Versioning	12

8	Concurrency	12

9	Functional Areas	12

9.1	Common	12

9.1.1	Discover Resource- (Sequence diagram)	13

9.2	Metering Consumption	13

9.2.1	Consumption Request - (Sequence diagram)	13

9.2.2	Consumption Subscribe - (Sequence diagram)	14

10	Resource Definitions	14

10.1	Resource Definition	15

10.2	Web Service Details	15

10.2.1	Collection (Feed)	15

10.2.2	Category	15

10.2.3	Resources	16

10.2.4	Authorization	16

10.2.5	Access Token	16

10.2.6	Notification	16

11	Traceability	17

11.1	TBD	17

12	appendix	17

12.1.1	Consumption WSDL	17

12.1.2	Output Data	18

12.1.3	Consumption XSD	20

List of Figures

Figure 1: Discover Service Resources Sequence Diagram	13

Figure 2: MeterReading Request Sequence Diagram	13

Figure 3: Subscribe Sequence Diagram	14

Figure 4: Web Service Interfaces	14

Figure 5: Use of CIM objects within feeds	15

# Introduction

This document contains only the extensions necessary to the OpenADE Core specification to build a WS*implementation of the OpenADE Requirements Specification.   The “OpenSG OpenADE SD – Core” document should be thought of as the parent of this document, filling in sections not addressed in the Core specification.

These extensions define a collection of services as a discoverable, stateless data service, using SOAP over HTTPS to send and receive requests and information in XML.  This architecture provides secure access to scalable methods and data resources hosted by the provider, while maintaining concurrency and integrity. All data is secured at the user level, so that access to individual operations can be provided or revoked to external services, and other users’ data will still be protected.

## Rights / Management / Governance

### Intellectual Property Rights

This document and the information contained herein is provided on an "AS IS" basis. UCAIug DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY OWNERSHIP RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

UCAIug requests any party that believes it has a patent claim that would necessarily be infringed by implementations of this UCAIug work, to notify UCAIug immediately, so that fair and reasonable licensing terms can be negotiated. UCAIug invites any party aware of applicable undisclosed patent claims to contact the UCAIug. UCAIug may include such claims on its website, but disclaims any obligation to do so.

UCAIug takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this UCAIug recommendation, can be obtained from the UCAIug. UCAIug makes no representation that any information or list of intellectual property rights will at any time be complete, or that any claims in such list are, in fact, Essential Claims.

### CIM Object Models

The recommendations herein build on work owned by the IEC. Required extensions identified in this recommendation will be submitted to the IEC, and will be tracked for inclusion in the model.

Information on the management of rights and governance can be found at the page below.
http://www.iec.ch/tctools/patent-guidelines.htm

### web Service Definitions

If necessary, UCAIug is willing to work with standards development organizations to incorporate additional aspects of this recommendation into standards, including the specification of how to use profiled (restricted) CIM objects within the SOAP over HTTP environment, and possibly the web service definitions themselves.

## Referenced Standards

- [1] IEC CIM (TC 57 61968/61970) - http://tc57.iec.ch

- [2] OAuth - http://oauth.net/

- [3] WS Basic Profile Version 1.0 http://www.ws-i.org/Profiles/BasicProfile-1.0-2004-04-16.html

## Referenced Guidance

- [G1] OpenADE B&UR 1.0 - http://osgug.ucaiug.org/sgsystems/OpenADE/Shared%20Documents/Forms/AllItems.aspx?RootFolder=%2fsgsystems%2fOpenADE%2fShared%20Documents%2fBusiness%20and%20User%20Requirements

- [G2] OpenADE SRS 1.0 - http://osgug.ucaiug.org/sgsystems/OpenADE/Shared%20Documents/Forms/AllItems.aspx?RootFolder=%2fsgsystems%2fOpenADE%2fShared%20Documents%2fSRS

- [G3] 3PDA – Security Profile for Third Party Data Access (ASAP-SG)

- [G4] OpenSG OpenADE SD – Core

- [G5] UDDI: www.uddi.org

- [G6] SOAP: http://www.w3.org/TR/SOAP/

## Namespaces

The subject of namespaces is important, because the namespace identifies the domain managing the definitions of protocol resources and formats. OpenSG proposes to use a temporary namespace until the final destination is identified. In any case, namespaces already defined elsewhere and used directly within reference service definitions will remain where they are, and will reference the identified body.

The proposed temporary namespace for definitions to be submitted to standards is below.

http://osgug.ucaiug.org/ns/2010/wsoade

# web services

Service Oriented Architecture is nothing new; in fact the web we are all familiar with today provides service-oriented access to Internet resources. Web services and SOAP are a mature, scalable, and reliable way to interconnect information systems.

Since this document is the first to define the general-purpose conventions, several resources were identified to allow consumers to gain access to the resources they want. These extensions are listed below.

- Authorization – To exchange tokens for authorizations

- Subscription – To register for notifications

In addition, the following “data” resources are currently in scope, as defined in [1] OADE-B&UR and [2] OADE-SRS.

- ReadingType – Represents a type of reading represented by MeterReading

- MeterReading – Represents a collection of readings associated with a specific ReadingType

The scope of this web services is the Web Services Basic Profile (BP).

“The WS-I Basic, a specification from the Web Services Interoperability industry consortium (WS-I), provides interoperability guidance for core Web Services specifications such as SOAP, WSDL, and UDDI. The profile uses Web Services Description Language (WSDL) to enable the description of services as sets of endpoints operating on messages.

To understand the importance of WSI-BP, note that it defines a much narrower set of valid services than the full WSDL schema. Many common platforms (listed below) support WSI-BP but do not support services outside of it. Compare the WSDL 1.1 specification to the subset permitted in WSI-BP.”

Source:  Wikipedia.org

## Service Format / syntax

This profile assumes SOAP over HTTP.  The Simple Object Access protocol (SOAP) is defined at http://www.w3.org/TR/SOAP/ thusly:

A SOAP (Simple Object Access Protocol) message is an XML document that consists of a mandatory SOAP envelope, an optional SOAP header, and a mandatory SOAP body. The element names are exactly as quoted (XML is case-sensitive), and their rules are as follows:

The “Envelope” is the top element of the XML document representing the message. It MUST be present in a SOAP message, and it MAY contain namespace declarations as well as additional attributes. If present, such additional attributes MUST be namespace-qualified. Similarly, the element MAY contain additional sub elements. If present, these elements MUST be namespace-qualified and MUST follow the Body element.

The “Header” element is a mechanism for adding features to a SOAP message without prior agreement between the communicating parties. SOAP defines a few attributes that can be used to indicate who should deal with a feature and whether it is optional or mandatory. It is optional and, if present, it MUST be the first immediate child element of an Envelope element. It MAY contain a set of header entries, each being an immediate child element of the Header element, and each of which MUST be namespace-qualified.

The “Body” element is a container for information intended for the ultimate recipient of the message. It MUST be present in a SOAP message and MUST be an immediate child element of an Envelope element. It MUST directly follow the Header element if present. Otherwise it MUST be the first immediate child element of the Envelope element. The element MAY contain a set of body entries, each being an immediate child element of the Body element. Immediate child elements of the Body element MAY be namespace-qualified.

## Message document format

Blah blah blah

More blah blah blah to follow.

## Payload entities

Payload entities will be specializations (subclasses) of the message document entry. They will therefore inherit all elements defined in the message document entry, as well as implement an XML schema representation of a CIM class defining additional schema elements.

Feed payloads will contain a list of references to resource entries that match the request query criteria.

The batch payload defined in the Core document allows a number of documents or resource requests to be included in a single request. Possibly a flag could be passed as an input parameter to feed resources to specify to include full representations instead of just references.

### resources

Domain data objects build on the IEC CIM model. In general, resources will be named using the CIM class as the resource part of the URI. Collections are returned if no specific entry ID is specified in the resource. For listings of fields, see the details for each resource, defined in Section 10.

An example is shown below.

Note that this is a preliminary draft for discussion purposes.

<?xml version="1.0" encoding="UTF-8"?>

<entry xmlns="http://www.w3.org/2005/Atom"

xmlns:m="http://osgug.ucaiug.org/ns/2010/aoade"

xml:lang="en">

<id>https://data.utility.com/rs/MeterReading/fj2ofj8</id>

<category term="m:MeterReading"/>

<m:mRID>fj2ofj8</m:mRID>

<m:IntervalReading>

<m:beginTimeStamp>2001-12-17T09:30:47Z</m:beginTimeStamp>

<m:endTimeStamp>2001-12-17T10:30:47Z</m:endTimeStamp>

<m:value>3.14159E0</m:value>

</m:IntervalReading>

<m:IntervalReading>

<m:beginTimeStamp>2001-12-17T10:30:47Z</m:beginTimeStamp>

<m:endTimeStamp>2001-12-17T11:30:47Z</m:endTimeStamp>

<m:value>3.14159E0</m:value>

</m:IntervalReading>

<link rel=’ReadingType’ href=”https://data.utility.com/rs/ReadingType/7.6.7.1.0.12.0.0.0.3.72’>

<link rel=’ServiceDeliveryPoint’ href=”https://data.utility.com/rs/ServiceDeliveryPoint/98374’>

</entry>

# Patterns

This section contains guidance and decisions on how message exchanges flow for the general scenarios below. In general, the constructs and operations defined in ________ shall be used, including requests for Services, Workspaces, Collections, Members, Categories, and Media Types. Extensions are generally refined subsets of the full specifications detailed in _________, and full implementations should not break clients who only implement these recommendations.

## Creating, Updating, Deleting

The POST method is to be used for creation of new entries, PUT is to be used for updates to existing entries, and DELETE is to be used to delete an entry.

## Query, request and response (Retrieve) formats

This section specifies the input parameters that can be passed to GET method operations for format, category, reference expansion, sorting, filtering, and iteration through list items.

_______ defines several useful query constructs for consideration in addition to those below, in Section 2.2.3.6 Query Options.

### Format

The default, and only required format, will be CIM-extended _________.

### Category

Specification of the category of entries is accomplished using the Atom element “term”, and if needed could be supported as a qualifier in queries by accepting category terms as inputs. In general, each CIM object class will become a category of entry, so that the representations of entries can be specified with a schema.

### Reference Expansion

By default, feed queries will return a list of resource links. If the reference expansion flag is set, entries returned will be expanded to contain their full representation.

(Need to determine if nested expansion is necessary / possible, and if so, how to specify to what level)

### Sorting

Ability to specify the sort order of resulting query / request entries is not necessary - subsequent processing of received data can display or rearrange data however desired. However, ordering of entries shall remain consistent across requests, so that an iterator can be used to page through results.

### Filtering

Filtering requires inputs that allow the specification of the resource name and/or path, as well as a range of publication or update date/times. Properties of the entry element (defined by its category type) could be defined to be acceptable by default as filter terms for the associated resource. Need to determine if it is feasible to implement all, or if identification is necessary of only the filter terms required for specific use cases. Possibly usage patterns could determine the need for indexing, etc.

If a specific entry ID is specified, that entry is returned.

### Iteration

Iteration inputs allow consumers to request a subset of entries or references at a time, and then page through them for processing. Inputs include the starting entry index, and number of entries per page.

Query results may require additional terms for iteration.

### Conditional Retrieval

Blah blah blah…check for applicability…

## Event Notification

The publish / subscribe pattern is not used in the Web Services model.  (How do we notify when data from the utility is ready?)

## Batch transfers

If desired, a feed for each data service consumer could be provided through which all subscribed content would be returned in a single request (or series of large chunks). This mechanism should allow any resource type to be included within a single feed. It may be possible to implement this as a regular feed request with reference expansion specified.

# Discovery

Universal Description, Discovery, and Integration (UDDI) is a specification designed to allow businesses to enter details about themselves and the services they provide in a registry. Searches can be typically be performed by company name, specific service, or types of service. This allows companies providing or needing web services to discover each other, define how they interact over the Internet, and share information in a standardized fashion.

Since a WSDL defines the XML grammar for describing services as collections of communication endpoints capable of exchanging messages, utilizes and third parties can publish WSDLs for services they provide and links to the WSDLs are usually offered in a company’s profile in a UDDI registry.

# Metadata

This may not be applicable in the web services model…

# Extensibility

…

Extensions to the CIM objects will be associated with specific versions of the namespace, specified in the version attribute of the schema element.

# Versioning

As additional capabilities are added to the interface definition, a specification of the version of the definition will be needed to help in service discovery negotiation. This should not change the namespace of any definitions.

# Concurrency

In order to ensure data integrity, clients may only update resources if they are updating the current version of the resource. If an update request fails due to conflict (not current version), the client must request the latest version, apply changes to that representation, and retry the update.

…

# Functional Areas

## Common

The flows in this section represent general-purpose functions that are needed for all protected resource publications.

### Discover Resource- (Sequence diagram)

Addresses OpenSG OpenADE 1.0 SRS 3.2.1, bullet 1.2, 1.3

Figure 1: Discover Service Resources Sequence Diagram

## Metering Consumption

### Consumption Request - (Sequence diagram)

Addresses OpenSG OpenADE 1.0 SRS 3.2.1, bullet 3.1, 3.2

Figure 2: MeterReading Request Sequence Diagram

### Consumption Subscribe - (Sequence diagram)

Addresses OpenSG OpenADE 1.0 SRS 3.2.1, bullet 3.1

Figure 3: Subscribe Sequence Diagram

# service Definitions

The following diagram provides an overview of the service resources defined. Of course, the service consumer also has to implement client requests for required interfaces, in order to access the resources provided by the provider.

Figure 4: Web Service Interfaces

The following table lists the resources defined for OpenADE.

| Logical Resource Name | Consumer Operation | Implementer | Description |
| --- | --- | --- | --- |
| Resource | GET /rs/Resource | Utility | Get supported service resources and extensions |
| Auth Access Token | GET /rs/<Key>/AccessToken | Utility | Get the authorized request token |
| Reading Type | GET /rs/<Key>/ReadingType | Utility | Get meter reading types defining readings units and lengths |
| Meter Reading | GET /rs/<Key>/MeterReading | Utility | Get meter readings – may be interval or instantaneous |
| Notification | POST /rs/<Key>/Notification | Both | Get notifications such as user modified authorization |

## service Definition

All web services with beginning with /ws/ support the patterns in Section 3, returning a (possibly expanded) collection of data resource stream entries. Individual entries can be managed using ____, _____, and _____. Permissions may be set according to policy, but guidance is provided regarding the typical configuration in resource details following this table.

The UML diagram below shows a proposed method of linking CIM object types to a syndication collection container such as______.

Figure 5: Use of CIM objects within feeds

IdentifiedObject is the top-most generalization (superclass) of most CIM classes. By generalizing this with the feed “Entry” element, all CIM IdentifiedObjects become valid Entry elements. In addition to the use of IdentifiedObject as a specialization of an Entry, CIM classes used as resources shall also have category terms defined for them within service workspace collections, so that entries can use the term element to denote their type and link to schema.

## Web Service Details

Many of the resources below are necessary to support initial setup and authorization. Implementations shall conform to referenced specifications for details on these interfaces. Clarifications and refinements made to support these service resources are denoted where necessary.

All resources are to be implemented as collections, with the elements listed in the sections below. Additional allowed values may be specified, and will be included here as necessary.

Collections consist of feeds, and exhibit behavior as defined in _______.

Examples of the consumption wsdl, and associated consumption and output data xsds can be found in the Appendix.

### Authorization

This resource is used to post the signed authorization for the associated token to the 3rd Party.

| Schema | Use | Element |
| --- | --- | --- |
| Authorization | Input | oauth_token |
| Authorization | Input | oauth_verifier |

### Access Token

This resource allows the 3rd Party to get the authorized request token. A different key is created for each authorized resource, so in the case of Meter Readings, individual service point channels would have separate keys.

| Schema | Use | Element |
| --- | --- | --- |
| AccessToken | Output | realm |
| AccessToken | Output | oauth_consumer_key |
| AccessToken | Output | oauth_token |
| AccessToken | Output | oauth_signature_method |
| AccessToken | Output | oauth_timestamp |
| AccessToken | Output | oauth_nonce |
| AccessToken | Output | oauth_verifier |
| AccessToken | Output | oauth_signature |

### Notification

Notifications are to be used to announce the creation or modification of resources. Based on the design pattern chosen for each information exchange, notification may or may not be required.

| Schema | Use | Element |
| --- | --- | --- |
| Notification | GET Output | Resource List |

# Traceability

## TBD

# appendix

### Consumption WSDL Example

<?xml version="1.0" encoding="utf-8"?>

<xs:schema xmlns:m="http://www.smartgridipedia.org/2009/11/Consumption" xmlns:xs="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.smartgridipedia.org/2009/11/Consumption" elementFormDefault="qualified" attributeFormDefault="unqualified" version="1.0">

<xs:element name="Consumption" type="m:Consumption"/>

<xs:complexType name="Consumption">

<xs:sequence>

<xs:element name="MeterReading" type="m:MeterReading_Type" minOccurs="0" maxOccurs="unbounded"/>

<xs:element name="ReadingType" type="m:ReadingType_Type" minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

<xs:simpleType name="String_type">

<xs:restriction base="xs:string"/>

</xs:simpleType>

<xs:simpleType name="AbsoluteDateTime_type">

<xs:restriction base="xs:dateTime"/>

</xs:simpleType>

<xs:simpleType name="Float_type">

<xs:restriction base="xs:float"/>

</xs:simpleType>

<xs:simpleType name="ReadingKind_type">

<xs:restriction base="xs:normalizedString">

<xs:enumeration value="time"/>

<xs:enumeration value="voltage"/>

<xs:enumeration value="voltageAngle"/>

<xs:enumeration value="volume"/>

<xs:enumeration value="current"/>

<xs:enumeration value="currentAngle"/>

<xs:enumeration value="date"/>

<xs:enumeration value="demand"/>

<xs:enumeration value="energy"/>

<xs:enumeration value="other"/>

<xs:enumeration value="phaseAngle"/>

<xs:enumeration value="power"/>

<xs:enumeration value="powerFactor"/>

<xs:enumeration value="pressure"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="UnitSymbol_type">

<xs:restriction base="xs:normalizedString">

<xs:enumeration value="A"/>

<xs:enumeration value="deg"/>

<xs:enumeration value="F"/>

<xs:enumeration value="g"/>

<xs:enumeration value="H"/>

<xs:enumeration value="h"/>

<xs:enumeration value="Hz"/>

<xs:enumeration value="Hz-1"/>

<xs:enumeration value="J"/>

<xs:enumeration value="J/s"/>

<xs:enumeration value="kg/J"/>

<xs:enumeration value="m"/>

<xs:enumeration value="m2"/>

<xs:enumeration value="m3"/>

<xs:enumeration value="min"/>

<xs:enumeration value="N"/>

<xs:enumeration value="none"/>

<xs:enumeration value="C"/>

<xs:enumeration value="ohm"/>

<xs:enumeration value="Pa"/>

<xs:enumeration value="rad"/>

<xs:enumeration value="S"/>

<xs:enumeration value="s"/>

<xs:enumeration value="s-1"/>

<xs:enumeration value="V"/>

<xs:enumeration value="V/VAr"/>

<xs:enumeration value="VA"/>

<xs:enumeration value="VAh"/>

<xs:enumeration value="VAr"/>

<xs:enumeration value="VArh"/>

<xs:enumeration value="W"/>

<xs:enumeration value="W/Hz"/>

<xs:enumeration value="W/s"/>

<xs:enumeration value="Wh"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="ServiceKind_type">

<xs:restriction base="xs:normalizedString">

<xs:enumeration value="electricty"/>

<xs:enumeration value="gas"/>

<xs:enumeration value="heat"/>

<xs:enumeration value="internet"/>

<xs:enumeration value="other"/>

<xs:enumeration value="rates"/>

<xs:enumeration value="refuse"/>

<xs:enumeration value="sewerage"/>

<xs:enumeration value="time"/>

<xs:enumeration value="tvLicence"/>

<xs:enumeration value="water"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="UnitMultiplier_type">

<xs:restriction base="xs:normalizedString">

<xs:enumeration value="c"/>

<xs:enumeration value="d"/>

<xs:enumeration value="G"/>

<xs:enumeration value="k"/>

<xs:enumeration value="M"/>

<xs:enumeration value="m"/>

<xs:enumeration value="micro"/>

<xs:enumeration value="n"/>

<xs:enumeration value="none"/>

<xs:enumeration value="p"/>

<xs:enumeration value="T"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="Seconds_Type">

<xs:restriction base="xs:float"/>

</xs:simpleType>

<xs:simpleType name="abstractElementRef_type">

<xs:restriction base="xs:string"/>

</xs:simpleType>

<xs:complexType name="ReadingTypeRef_type">

<xs:attribute name="ref" type="xs:string"/>

</xs:complexType>

<xs:complexType name="IntervalReading_Type">

<xs:sequence>

<xs:element name="timeStamp" type="m:AbsoluteDateTime_type"/>

<xs:element name="value" type="m:Float_type"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="ReadingType_Type">

<xs:sequence>

<xs:element name="mRID" type="m:String_type"/>

<xs:element name="intervalLength" type="m:Seconds_Type"/>

<xs:element name="kind" type="m:ReadingKind_type"/>

<xs:element name="unit" type="m:UnitSymbol_type"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="ServiceDeliveryPoint_Type">

<xs:sequence>

<xs:element name="mRID" type="m:String_type" minOccurs="0"/>

<xs:element name="name" type="m:String_type" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="MeterReading_Type">

<xs:sequence>

<!--<xs:element name="valuesInterval" type="m:DateTimeInterval_Type" minOccurs="0"/> -->

<xs:element name="CustomerAgreement" type="m:CustomerAgreement_Type"/>

<xs:element name="IntervalBlocks" type="m:IntervalBlock_Type" maxOccurs="unbounded"/>

<!-- <xs:element name="Readings" type="m:Reading_Type" minOccurs="0" maxOccurs="unbounded"/> -->

<!--			<xs:element name="ServiceDeliveryPoint" type="m:ServiceDeliveryPoint_Type" minOccurs="0"/> -->

</xs:sequence>

</xs:complexType>

<xs:complexType name="Reading_Type">

<xs:sequence>

<xs:element name="timeStamp" type="m:AbsoluteDateTime_type" minOccurs="0"/>

<xs:element name="value" type="m:Float_type" minOccurs="0"/>

<xs:element name="ReadingType" type="m:ReadingTypeRef_type"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="IntervalBlock_Type">

<xs:sequence>

<xs:element name="IntervalReadings" type="m:IntervalReading_Type" minOccurs="0" maxOccurs="unbounded"/>

<xs:element name="ReadingType" type="m:ReadingTypeRef_type"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="CustomerAgreement_Type">

<xs:sequence>

<xs:element name="mRID" type="m:String_type"/>

<xs:element name="CustomerAuthorization" type="m:CustomerAuthorization_Type"/>

<xs:element name="ServiceCategory" type="m:ServiceCategory_Type"/>

<xs:element name="ServiceSupplier" type="m:ServiceSupplier_Type"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="CustomerAuthorization_Type">

<xs:sequence>

<xs:element name="mRID" type="m:String_type"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="ServiceCategory_Type">

<xs:sequence>

<xs:element name="kind" type="m:ServiceKind_type"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="ServiceSupplier_Type">

<xs:sequence>

<xs:element name="mRID" type="m:String_type"/>

<xs:element name="name" type="m:String_type"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="DateTimeInterval_Type">

<xs:sequence>

<xs:element name="end" type="m:AbsoluteDateTime_type" minOccurs="0"/>

<xs:element name="start" type="m:AbsoluteDateTime_type" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

</xs:schema>

### Output Data example

<?xml version="1.0" encoding="UTF-8"?>

<xs:schema xmlns="http://www.smartgridipedia.org/2009/05/OutputData" xmlns:xs="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.smartgridipedia.org/2009/05/OutputData" elementFormDefault="qualified" attributeFormDefault="unqualified" version="1.0">

<xs:element name="Error" type="Error"/>

<xs:complexType name="Error">

<xs:annotation>

<xs:documentation>Errors in a service call</xs:documentation>

</xs:annotation>

<xs:sequence>

<xs:element name="errorCode" type="xs:string">

<xs:annotation>

<xs:documentation>error code</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="reason" type="xs:string" minOccurs="0">

<xs:annotation>

<xs:documentation>description of the error</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="details" type="xs:string" minOccurs="0">

<xs:annotation>

<xs:documentation>content about the error</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="stackTrace" type="xs:string">

<xs:annotation>

<xs:documentation>stack trace</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Location" type="Location" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

<xs:element name="Location" type="Location"/>

<xs:complexType name="Location">

<xs:annotation>

<xs:documentation>Identifies the pipeline and the stage where the error occurred </xs:documentation>

</xs:annotation>

<xs:sequence>

<xs:element name="node" type="xs:string" minOccurs="0">

<xs:annotation>

<xs:documentation>Name of the Pipeline/Branch/Route node where error occurred</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="pipeline" type="xs:string" minOccurs="0">

<xs:annotation>

<xs:documentation>Name of the Pipeline where error occurred (if applicable)</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="stage" type="xs:string" minOccurs="0">

<xs:annotation>

<xs:documentation>Name of the Stage where error occurred (if applicable)</xs:documentation>

</xs:annotation>

</xs:element>

</xs:sequence>

</xs:complexType>

<xs:element name="OutputData" type="Output"/>

<xs:complexType name="Output">

<xs:annotation>

<xs:documentation>This captures an event happened during a service transaction. This can be used to represent receipt acknowledgment and  error information</xs:documentation>

</xs:annotation>

<xs:sequence>

<xs:element name="result" type="xs:string">

<xs:annotation>

<xs:documentation>Event result. This represents the outcome of a service invocation.</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="creationTime" type="xs:dateTime">

<xs:annotation>

<xs:documentation>Event creation time</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="description" type="xs:string" minOccurs="0">

<xs:annotation>

<xs:documentation>Event description</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Error" type="Error" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

</xs:schema>

### Receive Consumption XSD example

<?xml version="1.0" encoding="UTF-8"?>

<wsdl:definitions name="ReceiveConsumptionUsage"

targetNamespace="http://www.openade.org/2010/04/ConsumptionUsage.wsdl"

xmlns:http="http://schemas.xmlsoap.org/wsdl/http/"

xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/"

xmlns:wsdl="http://schemas.xmlsoap.org/wsdl/"

xmlns:xs="http://www.w3.org/2001/XMLSchema"

xmlns="http://schemas.xmlsoap.org/wsdl/"

xmlns:wsi="http://ws-i.org/schemas/conformanceClaim/"

xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/"

xmlns:tm="http://microsoft.com/wsdl/mime/textMatching/"

xmlns:mime="http://schemas.xmlsoap.org/wsdl/mime/"

xmlns:tns="http://www.openade.org/2010/04/ConsumptionUsage.wsdl"

xmlns:typeOrig="http://www.smartgridipedia.org/2009/11/Consumption"

xmlns:typeIn="http://www.smartgridipedia.org/2009/11/ConsumptionIn"

xmlns:typeOut="http://www.smartgridipedia.org/2009/05/OutputData">

<wsdl:documentation>A web service for Consumption data transaction</wsdl:documentation>

<wsdl:types>

<xs:schema targetNamespace="http://www.smartgridipedia.org/2009/11/ConsumptionIn">

<xs:import namespace="http://www.smartgridipedia.org/2009/11/Consumption" schemaLocation="Consumption.xsd"/>

<xs:element name="CreatedConsumption" type="typeOrig:Consumption"/>

<xs:element name="ChangedConsumption" type="typeOrig:Consumption"/>

</xs:schema>

<xs:schema>

<xs:import namespace="http://www.smartgridipedia.org/2009/05/OutputData" schemaLocation="OutputData.xsd"/>

</xs:schema>

</wsdl:types>

<wsdl:message name="CreatedConsumptionInput">

<wsdl:part name="CreatedConsumption" element="typeIn:CreatedConsumption"/>

</wsdl:message>

<wsdl:message name="ChangedConsumptionInput">

<wsdl:part name="ChangedConsumption" element="typeIn:ChangedConsumption"/>

</wsdl:message>

<wsdl:message name="outputData">

<wsdl:part name="outputData" element="typeOut:OutputData"/>

</wsdl:message>

<wsdl:message name="faultReturn">

<wsdl:part name="faultInfor" element="typeOut:OutputData">

<wsdl:documentation>fault information</wsdl:documentation>

</wsdl:part>

</wsdl:message>

<wsdl:portType name="Consumption">

<wsdl:operation name="CreatedConsumption">

<wsdl:documentation>CreatedConsumption</wsdl:documentation>

<wsdl:input name="CreatedConsumptionInput" message="tns:CreatedConsumptionInput"/>

<wsdl:output name="CreatedConsumptionOutput" message="tns:outputData"/>

<wsdl:fault name="faultInfor" message="tns:faultReturn"/>

</wsdl:operation>

<wsdl:operation name="ChangedConsumption">

<wsdl:documentation>ChangedConsumption</wsdl:documentation>

<wsdl:input name="ChangedConsumptionInput" message="tns:ChangedConsumptionInput"/>

<wsdl:output name="ChangedConsumptionOutput" message="tns:outputData"/>

<wsdl:fault name="faultInfor" message="tns:faultReturn"/>

</wsdl:operation>

</wsdl:portType>

<wsdl:binding name="Consumption_Binding" type="tns:Consumption">

<soap:binding style="document" transport="http://schemas.xmlsoap.org/soap/http"/>

<wsdl:operation name="CreatedConsumption">

<wsdl:documentation>CreatedConsumption binding</wsdl:documentation>

<soap:operation soapAction="http://www.openade.org/2010/04/ConsumptionUsage.wsdl/CreatedConsumption" style="document"/>

<wsdl:input name="CreatedConsumptionInput">

<soap:body use="literal"/>

</wsdl:input>

<wsdl:output name="CreatedConsumptionOutput">

<soap:body use="literal"/>

</wsdl:output>

<wsdl:fault name="faultInfor">

<soap:fault name="faultInfor" use="literal"/>

</wsdl:fault>

</wsdl:operation>

<wsdl:operation name="ChangedConsumption">

<wsdl:documentation>ChangedConsumption binding</wsdl:documentation>

<soap:operation soapAction="http://www.openade.org/2010/04/ConsumptionUsage.wsdl/ChangedConsumption" style="document"/>

<wsdl:input name="ChangedConsumptionInput">

<soap:body use="literal"/>

</wsdl:input>

<wsdl:output name="ChangedConsumptionOutput">

<soap:body use="literal"/>

</wsdl:output>

<wsdl:fault name="faultInfor">

<soap:fault name="faultInfor" use="literal"/>

</wsdl:fault>

</wsdl:operation>

</wsdl:binding>

<wsdl:service name="ReceiveConsumptionUsage">

<wsdl:port name="Consumption_Port" binding="tns:Consumption_Binding">

<soap:address location="http://www.openade.org/2010/04/ConsumptionUsage.wsdl"/>

</wsdl:port>

</wsdl:service>

</wsdl:definitions>