OpenADE 1.0 Service Definition

Version: Draft v0.5

Release Date: 2/16/2010

Acknowledgements

The following individuals and their companies have contributed and/or provided support to the work of the OpenADE Service Definition:

- TBD

The OpenADE Task Force wishes to thank all of the above-mentioned individuals and their companies for their support of this important endeavor, as it sets a key foundation for an interoperable Smart Grid.

Document History

Revision History

Date of this revision: Feb. 25, 2010

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 0.5 | 2/25/10 | Steve Van Ausdall | Initial draft discussion version. | N |

Open Issues Log

Last updated: Feb. 16, 2010

| Issue | Issue Date | Provided By | Summary of the Issue |
| --- | --- | --- | --- |

Contents

1	Introduction	6

1.1	Rights / Management / Governance	6

1.1.1	CIM Object Models	6

1.1.2	Service Resource Definitions	6

1.2	Referenced Standards	6

1.3	Referenced Guidance	7

1.4	Namespaces	7

2	Resources	7

2.1	Security	7

2.1.1	Authentication	7

2.1.2	Authorization	8

2.2	URI Format / syntax	8

2.3	Status / return codes	8

2.4	Message document format	8

2.5	Payload entities	9

2.5.1	resource types / valid values	9

3	Patterns	9

3.1	Creating, Updating, Deleting	9

3.2	Query, request and response (Retrieve) formats	9

3.2.1	Format	10

3.2.2	Category	10

3.2.3	Reference Expansion	10

3.2.4	Sorting	10

3.2.5	Filtering	10

3.2.6	Iteration	11

3.2.7	Conditional Retrieval	11

3.3	Event Notification (pub/sub)	11

3.4	Batch transfers	11

4	Discovery	11

5	Metadata	11

6	Extensibility	11

7	Versioning	12

8	Concurrency	12

9	Functional Areas	12

9.1	Common	12

9.1.1	Register - (Sequence diagram)	12

9.1.2	Discover - (Sequence diagram)	13

9.1.3	Authorize - (Sequence diagram)	13

9.1.4	Modify Authorization - (Sequence diagram)	14

9.2	Metering Consumption	14

9.2.1	Consumption Request - (Sequence diagram)	14

9.2.2	Consumption Subscribe - (Sequence diagram)	15

10	Traceability	15

10.1	Sequences / Resources to SRS req's	15

10.2	Data elements to Referenced standards	15

10.3	Data Elements to interface X	15

List of Figures

No table of figures entries found.

# Introduction

Access to energy management resources is of paramount interest to Smart Grid service and device vendors. In order to provide access to customer data, energy services providers can implement these reference standards proposals and get access to early implementations. As the standards development organizations recommend alterations, stakeholders will decide how to handle these changes. If possible, all changes will be made as enhancements, so that existing implementations can continue to function or be upgraded independently of others.

OpenADE represents the internet data service provided by energy services providers. Many “Third Party” entities may also implement these services, to allow other uses not directly envisioned, though any enhancements to allow additional scenarios should be shared with the group and discussed as extensions.

It is the goal of OpenSG to promote interoperability by providing an easy to use, simple set of commonly available technologies. Toward this end, in line with the direction of the industry in ZigBee / HomePlug Alliance SEP 2.0, our direction is to define these services as a discoverable, stateless data service, using internet protocols to send and receive requests and information. A resource oriented architecture is proposed, similar to efforts elsewhere in the world such as web of internet things. This architecture uses RESTful HTTP to provide secure access to methods and data resources hosted by the provider. All data is secured at the user level, so that access to individual operations can be provided or revoked to external services, and other users data will still be protected.

## Rights / Management / Governance

### CIM Object Models

### Service Resource Definitions

## Referenced Standards

- OpenADE B&UR 1.0 - http://osgug.ucaiug.org/sgsystems/OpenADE/Shared%20Documents/Forms/AllItems.aspx?RootFolder=%2fsgsystems%2fOpenADE%2fShared%20Documents%2fBusiness%20and%20User%20Requirements

- OpenADE SRS 1.0 - http://osgug.ucaiug.org/sgsystems/OpenADE/Shared%20Documents/Forms/AllItems.aspx?RootFolder=%2fsgsystems%2fOpenADE%2fShared%20Documents%2fSRS

- IEC CIM - http://tc57.iec.ch

- Atom Publishing Protocol – http://www.w3.org/2007/app

- OAuth - http://oauth.net/

- GData - http://code.google.com/apis/gdata/docs/2.0/reference.html

- OData - http://www.odata.org/docs/[MC-APDSU].htm

- PubSubHubbub - http://code.google.com/p/pubsubhubbub/

## Referenced Guidance

TBD

## Namespaces

The subject of namespaces is important, because the namespace identifies the domain managing the definitions of protocol resources and formats. OpenSG proposes to use a temporary namespace until the final destination is identified. In any case, namespaces already defined elsewhere and used directly within reference service definitions will remain where they are, and will reference the identified body.

# Resources

Resource Oriented Architecture is nothing new; in fact the web we are all familiar with today provides restful (browser) access to internet resources. When you specify the Address URL of a page, you are providing the address of that resource that you requested. This architecture provides similar operations for external data consumer applications to request data and methods. Generally, data is made available as a feed, which is an agreement about how to query, create, update, request, and delete entries (individual object records, which have a defined schema according to their type).

Since this document is the first to define the general-purpose conventions, several resources were identified to allow consumers to gain access to the resources they want. These include the objects below.

- Register

- Discover

- Authorization

- Notification

- Subscription

In addition, the following “data” resources are currently in scope, as defined in OADE-B&UR and OADE-SRS.

- ConsumptionData

## Security

Because these services define resources that could be used to cause damage, access must be restricted to only those requests that have been authorized. Open Authorization is proposed as the method for requesting and acquiring these authorizations.

### Authentication

Authentication is a process through which an identity is proven. This identity is associated with specific authorizations. OpenADE does not require a specific method, but does require that the authentication method provides a reliable, secure way for customers to manage access to their information.

### Authorization

Authorization is the process of requesting and granting access to protected user resources. OpenADE proposes the use of OAuth to allow for the creation and management of revocable access keys.

Neither GData nor OData specify the authorization mechanism, but both support OAuth.

## URI Format / syntax

The URIs of the resources defined in OpenADE take the general form below. The <baseURL> does not need to be the same across different implementations, since resource addresses include the entire string.

http://<baseURL>/<resource>?<query>

Resource requests require inputs of user, key, and resource object. Additional path elements may be required for some resources. Resources may be a list (feed) or an individual entry.

The query section may contain additional inputs to affect processing, specified as a list of name=value pairs.

## Status / return codes

The normal HTTP response codes are to be used, as specified below. (From GData)

| Code | Explanation |
| --- | --- |
| 200 OK | No error. |
| 201 CREATED | Creation of a resource was successful. |
| 304 NOT MODIFIED | The resource hasn't changed since the time specified in the request's If-Modified-Since header. |
| 400 BAD REQUEST | Invalid request URI or header, or unsupported nonstandard parameter. |
| 401 UNAUTHORIZED | Authorization required. |
| 403 FORBIDDEN | Unsupported standard parameter, or authentication or authorization failed. |
| 404 NOT FOUND | Resource (such as a feed or entry) not found. |
| 409 CONFLICT | Specified version number doesn't match resource's latest version number. |
| 410 GONE | Requested change history is no longer available on the server. Refer to service-specific documentation for more details. |
| 500 INTERNAL SERVER ERROR | Internal error. This is the default code that is used for all unrecognized errors. |

## Message document format

“Message document” refers to the type of XML returned by resource requests. The two reference definitions, OAuth and GData both use an extended version of the Atom Publishing Protocol (AtomPub) to fulfill this need.

In addition to the recommended format, it is possible to support additional representations. An input can be accepted to provide RSS or other formats, but these additional formats are all optional, and will only be considered for this specification if needed.

## Payload entities

Payload entities will be specializations (subclasses) of the message document entry. They will contain all elements defined in the message document entry, as well as reference to a CIM type, where additional schema elements will be defined.

Feed payloads will contain a list of references to resource entries that match the request query criteria.

In addition, a batch payload is needed, to allow a number of documents or resource requests to be included in a single request. Possibly this could be an input parameter to feed resources to specify to include full representations instead of just references.

### resource types / valid values

In addition to the authorization resources described in OAuth, and additional common resources, the following CIM object definition is proposed to be used for the definition of consumption data fields.

/MeterReading/MeterReadingID/IntervalReading

A simple example is shown below. (Note that this format is still in early draft form)

<?xml version="1.0" encoding="UTF-8"?>

<entry xmlns="http://www.w3.org/2005/Atom"

xmlns:cim="http://osgug.ucaiug.org/ns/cim"

xml:lang="en">

<id>https://data.utility.com/sep/key/H3kP8F3z/MeterReading/hh39GPwfa/IntervalReading/2F8dhz9f</id>

<cim:readingStartTime>2010-07-24T16:00:00Z</cim:readingStartTime>

<cim:readingEndTime>2010-07-24T17:00:00Z</cim:readingEndTime>

<cim:value>2.042</cim:value>

</entry>

# Patterns

This section contains guidance and decisions on how message exchanges flow for the general scenarios below.

## Creating, Updating, Deleting

The POST method is to be used for creation of new entries, PUT is to be used for updates to existing entries, and DELETE is to be used to delete an entry.

## Query, request and response (Retrieve) formats

This section specifies the input parameters that can be passed to GET method operations for format, category, reference expansion, sorting, filtering, and iteration through list items.

OData defines several useful query constructs for consideration, in Section 2.2.3.6 Query Options.

### Format

The default, and only required format, will be CIM-extended AtomPub feed / entry XML.

Additional formats to be considered include RSS 2.0 and JSON.

Also to be considered is a representation of the service resource description, in Atom XML format.

OData defines several additional capabilities for definition of formats, including 2.2.1 Abstract Data Model and Conceptual Schema Definition Language. We would need to determine platform and tool support for these extensions. Could XSD be used to define the structure of entries of different category / types?

GData does not appear to link resources to a specific type, but includes all defined elements in a domain-specific namespace. (For example, PowerMeter does define elements for measurement quantities, etc.)

### Category

Specification of the category of entries is accomplished using the Atom element “term”, and if needed could be supported as a qualifier in queries by accepting category terms as inputs. For OpenADE, the main data element, MeterReading could have categories for different types of readings, interval vs. instantaneous, or a lower level specification such as hourly energy consumption vs. gas or water consumption. In general, each CIM object class will become a category, so that the representations of entities of the same category will have all applicable fields.

### Reference Expansion

By default, feed queries will return a list of resource links. If the reference expansion flag is set, entries returned will be expanded to contain their full representation.

(Need to determine if nested expansion is necessary / possible, and if so, how to specify to what level)

OData uses an m:inline extension to the atom:link element for this purpose.

### Sorting

Ability to specify the sort order of resulting query / request entries is not necessary - subsequent processing of received data can display or rearrange data however desired. However, ordering of entries shall remain consistent across requests, so that an iterator can be used to page through results.

### Filtering

Filtering requires inputs that allow the specification of the resource name and/or path, as well as a range of publication or update date/times. Properties of the entry element (defined by its category type) could be defined to be acceptable by default as filter terms for the associated resource. Need to determine if it is feasible to implement all, or if identification is necessary of only the filter terms required for specific use cases. Possibly usage patterns could determine the need for indexing, etc.

If a specific entry ID is specified, that entry is returned.

In GData, “most queries are simply full text search queries”.

### Iteration

Iteration inputs allow consumers to request a subset of entries or references at a time, and then page through them for processing. Inputs include the starting entry index, and number of entries per page.

Query results may require additional terms for iteration. GData uses some openSearch terms.

### Conditional Retrieval

GData uses If-None-Match in HTTP header to retrieve entries only if they have changed.

## Event Notification (pub/sub)

The publish / subscribe pattern is incredibly useful, and is implemented mostly by AtomPub. However, there is no mechanism defined in AtomPub to notify subscribers of new feed entries. This requires them to “poll” for new data, and while this is sufficient in many cases, some business processes require ability to notify in order to achieve reduced latency in client updates.

PubSubHubbub defines a mechanism for this purpose, and is worth consideration for use in this specification.

## Batch transfers

If desired, a feed for each data service consumer could be provided through which all subscribed content would be returned in a single request (or series of large chunks). This mechanism should allow any resource type to be included within a single feed. It may be possible to implement this as a regular feed request with reference expansion specified.

GData describes batch processing here http://code.google.com/apis/gdata/docs/batch.html.

# Discovery

Discovery of available services and resources is specified in OData, “limited capability negotiation” using DataServiceVersion (section 2.2.5.3) and MaxDataServiceVersion (section 2.2.5.7).

# Metadata

A “Resource” resource shall allow retrieval of the representation of all available resources, and the currently implemented version of each. AtomPub (http://www.w3.org/2007/app) defines a “workspace” for this.

# Extensibility

AtomPub is specified to be extensible, and implementations should be able to function even with different versions of client or server.

Extensions to the CIM objects will be associated with specific versions of the namespace, specified in the version attribute of the schema element.

# Versioning

GData uses ETags for versioning / concurrency management.

# Concurrency

See GData Resource Versioning http://code.google.com/apis/gdata/docs/2.0/reference.html#ResourceVersioning for one possible mechanism for preventing conflicting updates.

# Functional Areas

## Common

### Register - (Sequence diagram)

Addresses OpenSG OpenADE 1.0 SRS 3.2.1, bullet 1.1

Figure: 1: Register

### Discover - (Sequence diagram)

Addresses OpenSG OpenADE 1.0 SRS 3.2.1, bullet 1.2, 1.3

Figure: 2: Discover

### Authorize - (Sequence diagram)

Addresses OpenSG OpenADE 1.0 SRS 3.2.1, bullet 2.1

Figure: 3: Authorize

### Modify Authorization - (Sequence diagram)

Addresses OpenSG OpenADE 1.0 SRS 3.2.1, bullet 2.2, 2.3

Figure: 4: Modify Authorization

## Metering Consumption

### Consumption Request - (Sequence diagram)

Addresses OpenSG OpenADE 1.0 SRS 3.2.1, bullet 3.1, 3.2

Figure: 5: Consumption Request

### Consumption Subscribe - (Sequence diagram)

Addresses OpenSG OpenADE 1.0 SRS 3.2.1, bullet 3.1

Figure: 6: Consumption Subscribe

# Traceability

## Sequences / Resources to SRS req's

## Data elements to Referenced standards

## Data Elements to interface X