Roles:

Resource Owner

A Resource Owner produces and owns the resource and resource information managed by a customer or intermediary. A resource is a dispatchable entity. A typical Resource Owner would be an electric utility customer and a typical example of resource information owned by the customer is their electricity usage data and resource availability and capabilities.

Virtual Top Node (VTN) (something? initiator?; like resource custodian / resource manager; controlling entity)

Within the context of a paired interaction with a Virtual End Node, the Virtual Top Node manages the interaction with entities that manage and interact with DR resources. Examples of a VTN are the Utility, ISO/RTO, DR Aggregator. The VTN would be the source of a DR Signal that is sent to a VEN.

Virtual End Node (VEN) (third party?)

Within the context of a paired interaction with a Virtual Top Node, the Virtual End Node manages the interaction with DR Resources based on the interaction with the VTN. Examples of a VEN are a DR Resource, Facility Management System, Energy Management System or a DR Aggregator. In the example of a DR Aggregator as a VEN, the same party would, in turn, act as a VTN that interacts with other Virtual End Nodes.

VEN as Intermediary (third party?)

A Virtual End Node Intermediary is a 3rd party VEN that manages the Resources of a Resource Owner. Examples of a VEN Intermediary are a Facility Manager.

Use Cases as defined for NAESB document – “Requirements Specifications for Retail Standard DR Signals - for NIST PAP09”.

[Use Case list does not include DR Program Administration, DR Bidding, Direct Load Control, and Settlement.]

- VEN Registers DR Resource with VTN for DR Program

- VEN Modifies DR Resource with VTN for DR Program

- VEN Removes DR Resource with VTN for DR Program

- VTN Notifies VEN of New DR Event

- VEN Requests VTN for New DR Event (Pull or Callback Model)

- VTN Notifies VEN of Modified DR Event

- VEN Requests VTN for Modified DR Event (Pull or Callback Model)

- VTN Notifies VEN of Canceled DR Event

- VEN Confirms VTN for Received DR Event

- VEN Notifies VTN of Opt-out for DR Event

- VEN Notifies VTN of Resource Performance (Feedback)

- Resource Owner  Designates 3rd Party VEN as Intermediary

- Resource Owner Terminates 3rd Party VEN as Intermediary