## 2.1 Some background definitions/context needed

DR Event is defined in 3.4.1	Temporal Model of a DR Event for SRS cited below.

Amazingly enough DR Program is not defined in the SRS. The DR Program is the contract terms that define the rules and expectations for participation. I don’t think much of that matters for this analysis except that it should be understood that much of the details of the rules of engagement in the interaction patterns is pre-defined as part of a contract and other supporting details between the customer and the Utility or Aggregator.

## 2.2 Role Definitions

All roles are defined in the following sub-sections.

### Demand Response (DR) Controlling Entity

This role that represents all the different entities that may need to manage and interact with wholesale and/or retail DR resources and includes the following actors: ISO/RTO, Distribution Company, Load Serving Entity, DR Aggregator and others. Different actors may function as the DR Controlling Entity at different points in the process of administering a DR Event. The DR Controlling Entity may represent a single actor, such as a Utility Distribution Company in the business role of a Load Serving Entity. A DR Controlling Entity may also represent a hierarchy of entities, such as an ISO/RTO dispatching DR instructions to a Transmission Operator, who in turn sends the dispatch instructions on to a UDC, who sends instructions to a DR Aggregator, who then directs a specific DR Resource to execute the instruction. This can be modeled as a recursive relationship with DR Controlling Entity which represents each of these actors in an integration role. The goal is to minimize the number of different logical components and hence the number of different services and message payloads that need to be defined through reuse of the standard services and payload definitions.

This concept is elaborated more extensively in a recent EPRI report titled Concepts to Enable Advancement of Distributed Energy Resources. The terminology for the interaction parties varies depending on the source. For the purposes of this analysis, the roles and definitions used are those defined in “OpenADR 1.0 System Requirements Specification v1.0” developed by the OpenSG OpenADR Task Force. [probably need to move  the sources used to the beginning]

Demand Response (DR) Resource

A DR resource is a virtual representation of one or more assets or physical devices capable of shedding or managing load in response to a triggering event. A DR Resource may consist of multiple assets or devices that have been aggregated to form a larger load shedding capacity or energy resource.

For example, an apartment building with multiple electricity consumers is one large Resource composed of the aggregated the total load shedding capacity of all the assets or devices in the apartment building. A DR Resource may also consist of different types of generation assets such as a wind Turbine and an electric motor that work in combination to meet DR program obligations.

Demand Response (DR) Asset

A DR Asset is an end device that is capable of shedding or managing load in response to Demand Response Events, Energy or Ancillary Services, Price Signals or other system events (e.g. under frequency detection). The DR Asset can be controlled by an end device control through Direct Load Control or Demand Response Load Control.

# Use Case 1: Demand Response Resource Registers with a Demand Response Controlling Entity

Use Case Description: A party with ownership, controlling interest or administrative responsibilities for a Resource communicates operational information about the Resource to a controlling entity. This includes information about the capabilities, availability, and constraints regarding the Resource’s ability to shed load or generate power.

For example the owner of a DR resource may wish to declare their inability to shed load due to summer shutdown or may wish to reduce the available capacity of a Resource due to equipment maintenance or other causes.

.

Preconditions:

- The DR Resource and DR Controlling Entity have all of the necessary network connections available.

- The party with ownership, controlling interest or administrative responsibilities for the Resource has enrolled in a Demand Response Program that is administered by the DR Controlling Entity.

Minimal Guarantees:

- The DR Resource does not reveal any information to another party that would allow that party to provide any false information to a DR Controlling Entity attributed to the DR Resource.

- The DR Controlling Entity processes only valid data

- The DR Resource sends data to the DR Controlling Entity unaltered.

Success Guarantees:

- The DR Resource has registered with the DR Controlling Entity prior to a call for performance under the terms of the DR Program and provided all Resource information necessary to participate in a DR Event.

Trigger:

The trigger for this use case could be an operator initiated trigger or the result of a pre-configured device configured to participate in a DR Program.

Diagram: Use Case 1:  Register DR Resource

Main Success Scenario:

1:  The DR Resource sends a registration request to create, updated, or remove a profile to the DR Controlling Entity.

2: The DR Controlling Entity assesses the validity of the Resource registration request .

3: The DR Controlling Entity send a reply based on the results of the assessment

4: The DR Controlling Entity has a profile of the performance characteristics needed to dispatch the DR Resource.

# Use Case 2: DR Controlling Entity Notifies DR Resource of DR Event

Use Case Description: This interaction is used to dispatch DR Resources.  The dispatch can convey an objective, price or direct load control. The objective is expressed as a load or generation value (e.g. shed 100kW) for the load profile of the DR Resource for a specific interval or series of intervals. The price message expresses the price for an interval or intervals as an absolute real time price or a price relative to the current tariff price. The direct load control message includes an on/off or set point (e.g. set thermostat to 80 degrees).

Although the Event Notification message can contain one or more of the three signal types, this Use Case is broken out into separate Use Cases for each signal type for the purposes of a properly segmented security analysis.

Preconditions:

- The DR Resource and DR Controlling Entity have all of the necessary network connections available.

- The party with ownership, controlling interest or administrative responsibilities for the Resource has enrolled in a Demand Response Program that is administered by the DR Controlling Entity.

- The DR Resource is successfully registered with the DR Controlling Entity as defined in Use Case 1.

Minimal Guarantees:

- The DR Controlling Entity does not reveal any information that could allow another party to present false identification, or intercept or alter future messages sent to the DR Resource.

- The DR Resource processes only valid data.

- The DR Controlling Entity sends data to the DR Resource unaltered.

Success Guarantees:

- The DR Resource receives an Event notification and is able to respond and perform load-shed or generation based on the content and intentions of the DR Event signal.

Trigger:

The trigger for this use case could beIndi from multiple sources depending on the span of control of the DR Controlling Entity and the DR Program definition. The originating Event message could be a manual response from a Market Operator based on forecasted or current conditions. The event could be a manual or automated response to a program rule regarding time of day and outside air temperature, or any number of options. If the DR Controlling Entity is a DR Aggregator, it could be a manual or automated response to an event signal from a Market Operator.

Diagram: Use Case 2:  DR Event Notification

[Don’t know what the second interaction is. Remove it and the acks.]

Main Success Scenario:

1: A DR Controlling Entity sends a DR Event Notification (a.k.a DR Dispatch) to the DR Resource. [A DR Event Notification could be for a new DR Event notifice, or an update or cancellation of a pending or current DR Event.]

2: The DR Resource receives the DR Event Notification.

3:The DR Resource optionally sends a reply with an affirmative acknowledgement or failure message.

4: The DR Resource takes action to reduce load or generate power.

5: The DR Resource is able to provide feedback on expected performance as defined in a later Use Case.

# Use Case 3: DR Controlling Entity Notifies DR Resource of DR Event - Objective

Use Case Description: This interaction is used to dispatch DR Resources using a signal with an objective.  The objective is expressed as a load or generation value (e.g. shed 100KW) for the load profile of the DR Resource for a specific interval or series of intervals.

Preconditions:

- The DR Resource and DR Controlling Entity have all of the necessary network connections available.

- The party with ownership, controlling interest or administrative responsibilities for the Resource has enrolled in a Demand Response Program that is administered by the DR Controlling Entity.

- The DR Resource is successfully registered with the DR Controlling Entity as defined in Use Case 1.

Minimal Guarantees:

- The DR Controlling Entity does not reveal any information that could allow another party to present false identification, or intercept or alter future messages sent to the DR Resource.

- The DR Resource processes only valid data.

- The DR Controlling Entity sends data to the DR Controlling Entity unaltered

Success Guarantees:

- The DR Resource receives an Event notification and is able to respond and perform load-shed or generation based on the content and intentions of the DR Event signal.

Trigger:

The trigger for this use case could be from multiple sources depending on the span of control of the DR Controlling Entity and the DR Program definition. The originating Event message could be a manual response from a Market Operator based on forecasted or current conditions. The event could be a manual or automated response to a program rule regarding time of day and outside air temperature, or any number of options. If the DR Controlling Entity is a DR Aggregator, it could be a manual or automated response to an event signal from a Market Operator.

Diagram: Use Case 3:  DR Event Notification - Objective

[Don’t know what the second interaction is. remove it and the acks]

Main Success Scenario:

1: The DR Controlling Entity sends a DR Event Notification with Objectives to a DR Resource.

2: The DR Resource receives the DR Event Notification with Objectives.

3: The DR Resource optionally sends a reply with an affirmative acknowledgement or failure message.

4: The DR Resource takes action to reduce load or generate power.

5: The DR Resource is able to provide feedback on expected performance as defined in a later Use Case.

# Use Case 4: DR Controlling Entity Notifies DR Resource of DR Event – Price (Broadcast)

Use Case Description: This interaction is used to broadcast a price to DR Resources. The price is broadcast to Resources for a specific time interval or with a start time indicating that this is the price until another broadcast.

Preconditions:

- The DR Resource and DR Controlling Entity have all of the necessary network connections available.

- The party with ownership, controlling interest or administrative responsibilities for the Resource has enrolled in a Demand Response Program that is administered by the DR Controlling Entity.

- The DR Resource is successfully registered with the DR Controlling Entity as defined in Use Case 1.

Minimal Guarantees:

- The DR Controlling Entity does not reveal any information that could allow another party to present false identification, or intercept or alter future messages sent to the DR Resource.

- The DR Resource processes only valid data.

- The DR Controlling Entity sends data to the DR Resource unaltered.

Success Guarantees:

- The DR Resource receives price notification and is able to respond and perform load-shed or generation based on the current price conditions and best economic interests of the DR Resource.

Trigger:

The trigger for this use case could be from multiple sources depending on the span of control of the DR Controlling Entity and the DR Program definition. It could be a manual or automated process.

Diagram: Use Case 4:  DR Event Notification – Price (Broadcast)

[change to single interaction with DR entities]

Main Success Scenario:

1: A DR Controlling Entity broadcasts a DR Event Price message to multiple DR Resources.

2: The DR Resource receives the DR Event Price message.

2: The DR Resource optionally takes action to reduce load or generate power.

# Use Case 5: DR Controlling Entity Notifies DR Resource of DR Event – Direct Load Control

Use Case Description:

The direct load control message includes an on/off or set point (e.g. set thermostat to 80 °). A Direct Load Control message is sent to a specific device end device control that is capable of controlling a specific device. The role associated with the controlling device is a DR Asset.

Preconditions:

- The DR Resource and DR Asset have all of the necessary network connections available.

- The party with ownership, controlling interest or administrative responsibilities for the DR Asset has enrolled in a Demand Response Program that is administered by the DR Controlling Entity.

Minimal Guarantees:

- The DR Controlling Entity does not reveal any information that could allow another party to present false identification, or intercept or alter future messages sent to the DR Asset.

- The DR Asset processes only valid data.

- The DR Controlling Entity sends data to the DR Asset unaltered.

Success Guarantees:

- The DR Asset accepts and acts on the requested direct load control command, such as turning off a device or reaching a desired setpoint.

.

Trigger:

The trigger for this use case could be from multiple sources depending on the span of control of the DR Controlling Entity and the DR Program definition. The originating Event message could be a manual or automated message.

Diagram: Use Case 5:  DR Event Notification – Direct Load Control

[get rid of ack.]

Main Success Scenario:

1: The DR Controlling Entity sends and Event Nofication to a DR Asset.

2: The DR Asset receives the DR Event Notifcation.

3: The DR Resource optionally acknowledges the receipt of a DR Event Notification. [The acknowledgement of an Event is optional depending on the interaction agreement between the parties]

2: The DR Asset takes action based on the Direct Load Control Command (e.g. turn off, change to a setpoint, etc.).

# Use Case 6: DR Resource Requests New DR Event from DR Controlling Entity (Pull or Callback Model)

Use Case Description: This interaction is used to dispatch DR Resources based on a request from the DR Resource.  The dispatch is the same as in Use Case 3.

Preconditions:

- The DR Resource and DR Controlling Entity have all of the necessary network connections available.

- The party with ownership, controlling interest or administrative responsibilities for the Resource has enrolled in a Demand Response Program that is administered by the DR Controlling Entity.

- The DR Resource is successfully registered with the DR Controlling Entity as defined in Use Case 1.

Minimal Guarantees:

- The DR Resource does not reveal any information that would allow another party to present false identification or intercept messages as a DR Resource.

- The DR Controlling Entity only processes valid requests.

- The DR Resource sends data to the DR Controlling Entity unaltered.

Success Guarantees:

- The DR Resource receives an Event notification and is able to respond and perform based on the content and intentions of the DR Event signal.

Trigger:

The trigger for this use case is a request from the DR Resource. The request is sent based on the temporal aspects of the specific Demand Response Program and enrollment agreements between the DR Controlling Entity and DR Resource. For example, for a day-ahead program the request is sent for the next day’s event. [May be some smoke here.]

.

Diagram: Use Case 6:  DR Resource Requests DR Controlling Entity for New DR Event

Main Success Scenario:

1: The DR Resource requests a DR Event Notification from the DR Controlling Entity.

2: The DR Controlling Entity responds with the Event Notification.

3: The DR Resource optionally sends a reply with an affirmative acknowledgement or failure message.

4: The DR Resource takes action to reduce load or generate power.

5: The DR Resource acknowledges receipt of the DR Event Notification.

6: The DR Resource is able to provide feedback on expected performance as defined in a later Use Case.

# Use Case 7: DR Resource Opts-Out of DR Event(s)

Use Case Description: This interaction is used by the DR Resource to notify the DR Controlling Entity that it is opting to not participate events for a schedule of time intervals.

Preconditions:

- The DR Resource and DR Controlling Entity have all of the necessary network connections available.

- The party with ownership, controlling interest or administrative responsibilities for the Resource has enrolled in a Demand Response Program that is administered by the DR Controlling Entity.

- The DR Resource is successfully registered with the DR Controlling Entity as defined in Use Case 1.

Minimal Guarantees:

- The DR Resource does not reveal any information that could allow another party to present false identification, or intercept or alter future messages sent to the DR Controlling Entity.

- The DR Controlling Entity processes only valid data.

- The DR Resource sends data to DR Controlling Entity unaltered.

Success Guarantees:

- The DR Controlling Entity is able to determine which current or future events that the DR Resource will participate in.

Trigger:

The  DR Resource sends opt-outs as availiablity is determined.

Diagram: Use Case 7: DR Resource Opts-Out of a DR Event

(need to remove asset interaction)

Main Success Scenario:

1: The DR Resource decides to opt-out of events or for a period of time.

4: The DR Resource sends an Opt-out notice to the DR Controlling Entity.

5: The DR Controlling Entity acknowledges receipt of the Opt-out.

# Use Case 8: DR Resource Notifies DR Controlling Entity of Event Performance (Feedback)

Use Case Description: This interaction is used by the DR Resource to notify the DR Controlling Entity if the Resources status or state of the Resource during the event. The feedback is provided continuously during the event in intervals agreed upon by the parties. The performance feedback contains information such as the load profile response characterization of the DR Resource in response to getting the DR signal and information about the near real time electricity usage of the DR Resource.

Preconditions:

- The DR Resource and DR Controlling Entity have all of the necessary network connections available.

- The party with ownership, controlling interest or administrative responsibilities for the Resource has enrolled in a Demand Response Program that is administered by the DR Controlling Entity.

- The DR Resource is successfully registered with the DR Controlling Entity as defined in Use Case 1.

- The DR Resource has been notified of a DR Event.

- The DR Controlling Entity and DR Resoruce have agreed on a feedback schedule. The Feedback of performance is provided only during the requested performance interval of the DR Resource.

Minimal Guarantees:

- The DR Resource does not reveal any information that could allow another party to present false identification, or intercept or alter future messages sent to the DR Controlling Entity.

- The DR Controlling Entity processes only valid data.

- The DR Resource sends data to the DR Controlling Entity unaltered.

Success Guarantees:

- The DR Controlling Entity receives continuous and timely (real time or near real time) feedback from the DR Resource during the entire Event performance window.

Trigger:

The trigger for this use case is based on an agreed upon reporting interval.

Diagram: Use Case 8: DR Resource Notifies DR Controlling Entity of Event Performance (Feedback)

Main Success Scenario:

1: A DR Resource sends a Feedback message to a DR Controlling Entity.

2: The DR Controlling Entity Receives a Feedback message from a DR Resource.

3:The DR Controlling Entity stores DR Resource event performance data for use in subsequent analysis by the DR Controlling Entity.

[These are use cases added when analyzing using 3PDA.  Not sure if we still need to deal with them. In these cases the Resource Owner has contracted with an Energy Management Service Provider that is given some level of control over the assets that make up the resource. The interaction patterns remain the same as above.]

- Resource Owner  Designates 3rd Party VEN as Intermediary

- Resource Owner Terminates 3rd Party VEN as Intermediary

# Footnotes

Concepts to Enable Advancement of Distributed Energy Resources: White Paper on DER. EPRI, Palo Alto, CA : 2010. 1020432

# Comments

Add minimal gaurantees for both parties.

Counterpart for DRCE ends up in a known (valid?) state. Each party agrees on the outcome.

?other

could be altenate scenario - for interaction with known execption to business rules  to which there is a reply of failure. Capture rollback condition or no action condition.

And acknowleged. Provide proof that this is successful.

Failed. What do we need to make sure happened if failed. Protect information – DR Controlling Entity does not reveal information that would allow spoof of future message.

What to make sure what hold true if fails.

“no undersiered manipulation o load takes place”.

But at least…

Indications that this use case succeeded. i.e. dropped load/gen power.

Failed. What do we need to make sure happened if failed. Protect information – DR Controlling Entity does not reveal information that would allow spoof of future message.

What to make sure what hold true if fails.

“no undersiered manipulation o load takes place”.

But at least…

Indications that this use case succeeded. i.e. dropped load/gen power.

Failed. What do we need to make sure happened if failed. Protect information – DR Controlling Entity does not reveal information that would allow spoof of future message.

What to make sure what hold true if fails.

“no undersiered manipulation o load takes place”.

But at least…

Indications that this use case succeeded. i.e. dropped load/gen power.

Failed. What do we need to make sure happened if failed. Protect information – DR Controlling Entity does not reveal information that would allow spoof of future message.

What to make sure what hold true if fails.

“no undersiered manipulation o load takes place”.

But at least…

Indications that this use case succeeded. i.e. dropped load/gen power.