OpenADR 1.0 System Requirements Specification

Version: Draft v0.3

Issued for review prior to Draft 1 on: 5/2/2010

[Draft 1] Release Date: 05/04/2010

Acknowledgements

The following individuals and their companies have contributed and/or provided support to the work of the OpenADR System Requirements Specification:

The OpenADR Task Force wishes to thank all of the above-mentioned individuals and their companies for their support of this important endeavor, as it sets a key foundation for an interoperable Smart Grid.

Document History

Revision History

Date of this revision: April 13, 2010

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 0.1 | 4/13/2010 | Bruce Bartell | Initial draft “shell” based on OpenADE SRS | N |
| 0.2 | 4/20/2010 | Bruce Bartell | Updated through sections 3.2.1 | N |
| 0.2 | 4/30/2010 | Bruce Bartell | Updated through sections 3.2.2 | N |
| 0.2 | 5/1/2010 | Ed Koch | Scope update and comments for F2F | N |

Open Issues Log

Last updated: April 13, 2010

As issues are addressed in new versions of this document, they are removed from this list.

| Issue Date | Provided By | Summary of the Issue |
| --- | --- | --- |

Contents

1	Introduction	6

1.1	Purpose	6

1.2	Scope	7

1.2.1	Scope of This Release	7

1.2.2	Scope of Subsequent Releases	7

1.3	Acronyms and Abbreviations	8

1.4	External Considerations and References	9

1.4.1	RFC 2119 Keyword interpretation	9

1.5	Document Overview	10

2	Architecture Vision	12

2.1	Architectural Goals and Guiding Principles	13

2.2	Architectural Considerations	13

3	OpenADR Systems Architecture	15

3.1	OpenADR Business Architecture View	15

3.2	Integration Requirements Specification	18

3.2.1	Functional Requirements – Business Processes	18

3.2.2	Functional Requirements – Integration Services	20

Draft 1	29

3.2.3	Technical Requirements – Integration Services	29

3.3	OpenADR Application Architecture View	29

3.4	OpenADR Data Architecture View	30

3.4.1	DR Signal Data Requirements [PAPs contain summary of data requirements]	30

3.4.2	DR Management Data Requirements	30

3.5	OpenADR Technical Architecture View	31

3.5.1	Networking Standards	31

3.5.2	Security Standards	31

3.5.3	Service / Resource Patterns	31

3.6	Governance	33

4	Appendices	34

4.1	Terms and Definitions	34

List of Figures

Figure 1.  OpenADR component diagram showing the actors and components.	8

Figure 2.  The Open Group Architecture Framework (TOGAF) architecture development cycle.	10

Figure 3.  OpenADR Stakeholders Overview	15

Figure 4.  Overview of Business Process Flows	16

Figure 5.  Overview of Business Process Flows Using Logical Components.	21

Figure 6.  Overview diagram of Logical Components	22

# Introduction

The Open Smart Grid Open Automated Demand Response (OpenADR) is an industry-led initiative under the Open Smart Grid (OpenSG) subcommittee within the UCA International Users Group (UCAIug).  The OpenADR Task Force defines systems requirements, policies and principles, best practices, and services, required for business and data requirements for standardizing control and pricing signals for Demand Response (DR) and Distributed Energy Resources (DER) as part of the Smart Grid implementation. OpenADR, as an open user group forum, is developing a set of utility-ratified requirements and specifications for utilities and 3rd Parties to adopt and implement.  The end-state of this effort will contribute to the development of open and interoperable Demand Response solutions.

This will be achieved by defining and making the following OpenADR related items available to the market:

- Common business processes and functional requirements

- Common architecture principles and patterns

- Common information requirements and model

- Common integration services (functional & informational)

## Purpose

The purpose of this document is to provide both the functional and technical guidance and requirements needed to serve as the “rules of engagement” for messaging and data exchange to achieve interoperability.  This would lead to open and interoperable components that can be delivered with different vendor products and/or solutions within the scope of OpenADR.  The functional requirements will be driven by business processes and the technical requirements will be driven by desired architectural principles and best practices.

## Scope

The SRS focuses on the requirements to support the interactions and exchange of information for the purposes of Demand Response (DR) and includes the exchanges of DR related information between various entities such as Utilities, Independent System Operators (ISO’s), Aggregators, Energy Service Providers and end use customers. The scope of OpenADR SRS includes standardizing dispatch, control and pricing signals for DR and Distributed Energy Resources (DER) as part of the Smart Grid implementation as defined in the Open ADR Functional Requirements and Use Case Document  (OpenSG).

Demand Response is defined as the temporary modification of customer energy usage for a defined duration which is triggered by some condition on the grid such as reliability or market conditions. These  DR events result in the exchange of “DR signals” between service providers such as Utilities, ISO’s, Aggregators, ESP’s, etc. and their customers. The information in the DR signals causes modifications to the end users load profiles. The requirements in the SRS are from the perspective of the enterprise systems of the service providers that are publishing the DR signals to their customers (i.e. Utility). This is in contrast to the customer’s systems or perspective which is covered in other efforts such as OpenHAN and SEP. The thing that all the various efforts have in common is the need to exchange the DR related information in some standardized form. Furthermore this SRS does not cover many of the administrative aspects of managing a DR program such as measurement and verification and settlement.  The SRS is focused on only those aspects of DR management that is required to facilitate the exchange of DR signals with their customers.

The SRS defines the logical components and business functions in order to identify the interfaces that must be specified to enable interoperability across different implementations, for many utilities to many 3rd Parties.  It includes architectural aspects and specific requirements.  The inputs include OpenADR use cases, as well as industry best practices and standards, including information models and other specifications.

### Scope of This Release

OpenADR SRS 1.0 addresses the following functional areas:

- Direct Load Control Signals

- Dispatching of Load Profiles

- DR Related Pricing Signals

- DER applications (limited to the context of grid-connected DR)

- DR Program Management

  - Program and Customer Registration

  - DR Resource Registration

### Scope of Subsequent Releases

- Utility internal systems integration for DR purposes

- DR Bidding

  - DR Bid to Supply (Retail Offers)

  - DR Bid to Buy

Figure 1.  OpenADR component diagram showing the actors and components.

The OpenADR SRS does not include the following items that are typically a part of solution architecture.  Some of them are or have been addressed by other parts of the OpenSG initiative.  Others will need to be dealt with specifically for each implementation.

- Network and hardware infrastructure architecture

- Operational architecture

- Testing methodology and architecture

- Internal application architecture

## Acronyms and Abbreviations

This subsection provides a list of all acronyms and abbreviations required to properly interpret the OpenSG OpenADR System Requirements Specification.

| Acronym | Name |
| --- | --- |
| ADE | Automatic Data Exchange |
| AMI | Advanced Metering Infrastructure |
| CIM | IEC TC57 Common Information Model |
| EMS | Energy Management System |
| ESI | Energy System Interface; Energy Services Interface |
| HAN | Home Area Network |
| IETF | Internet Engineering Task Force |
| IHD | In-Home Display |
| PHEV | Plug-In Hybrid Electric Vehicle |
| SDO | Standards Development Organization |
| SEP 2.0 | Smart Energy Profile |
| SLA | Service Level Agreement |
| SRS | System Requirements Specification |
| TOGAF | The Open Group Architecture Framework |

## External Considerations and References

The work of the OpenADR SRS is dependent upon the requirements defined in the following sources:

- Open ADR Functional Requirements and Use Case Document  (OpenSG)

- Requirements Specifications for Wholesale Standard DR Signals - for NIST PAP09

- Requirements Specifications for Retail Standard DR Signals - for NIST PAP09

- OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION - Public Interest Energy Research (PIER), California Energy Commission

- Requirements Specifications for Common Electricity Product and Pricing Definition - for NIST PAP03

- Requirements Specifications for Common Scheduling Mechanism for Energy Transactions - for NIST PAP04

- ZigBee Smart Energy Profile™ 2.0 Technical Requirements Document

- Energy Information Standards (EIS) Alliance Customer Domain Use Cases

The work of OpenADR SRS is dependent upon the best practices available from the following entities and standards organizations:

- IETF Internet Suite - Internet Standards, including the following

          - [RFC-793] IETF Transmission Control Protocol (TCP)

          - [RFC-791] IETF Internet Protocol (IP)

          - [RFC-2616] Hypertext Transfer Protocol -- HTTP/1.1

- [IEC-61968] IEC TC57 Working Group 14 (IEC 61968) (Common Information Model)

- [ASAP-SG-3P] Security Profile for Third Party Access (ASAP-SG)

### RFC 2119 Keyword interpretation

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this document are to be interpreted as described in RFC 2119.

## Document Overview

TOGAF 9.0 defines four architecture domains that are commonly accepted as subsets of overall enterprise architecture, all of which TOGAF is designed to support, see Figure 2:

- Architecture Vision defines overall architecture guiding principles, goals and objectives and desired traits.

- The Business Architecture defines the business strategy, governance, organization, and key business processes.

- The Information Systems Architecture, including the following.

  - The Data Architecture describes the structure of an organization's logical and physical data assets and data management resources.

  - The Application Architecture provides a blueprint for the individual application systems to be deployed, their interactions, and their relationships to the core business processes of the organization.

- The Technology Architecture describes the logical software and hardware capabilities that are required to support the deployment of business, data, and application services. This includes IT infrastructure, middleware, networks, communications, processing, standards, etc.

Figure 2.  The Open Group Architecture Framework (TOGAF) architecture development cycle.

As such, the document will be structured as follows:

Section 2 describes the overall Architecture Vision for the system, including Guiding Principles, Architectural Considerations, and the OpenADR Reference Model, all relevant to providing a consistent framework within which the four architecture components can be developed.

Section 3 provides details on the following:

- Business Architecture:  This will refer to work products produced by the Use Case and Service Definition Teams of OpenADR, which includes the list of use cases and integration requirements and business services at the functional level.

- Data Architecture:  This provides the technical level requirements relative to how the OpenADR data should be modeled and represented consistently across all integration services to ensure semantic interoperability.

- Application Architecture: This provides the technical level requirements relative to how applications are modeled as logical components, and what services each logical component may provide or consume. This should be an instantiation of the business services identified within the Business Architecture.

- Technology Architecture: This provides the technical level requirements relative to how services will interact with each other to support end-to-end AMI business processes.

Section 4 contains the Appendices, which includes terms and definitions, logical components list, integration requirements list, and integration services view.

# Architecture Vision

The Architecture Vision articulates the Architectural Goals and Principles that enables the business goals and addresses the stakeholder concerns and objectives. As stated in the Introduction, the goal is the development of open and interoperable Demand Response solutions.

## Architectural Goals and Guiding Principles

Architecture guiding principles are rules of engagement designed to ensure that all aspects of the implementation fit within a well-defined framework.  These principles, discussed and agreed upon with all stakeholders of the OpenADR, are used to drive the architectural approach and patterns to be implemented.  These principles should not be taken lightly as they imply what and how the overall goals of OpenADR will be met.  Each of the principles has a level of effort and cost implications for utilities and 3rd Parties looking to adopt this specification.  Adherence to these principles can be adjusted for specific cases driven by time and budget constraints.  These exceptions should be approved by all stakeholders and must be documented.

- Exchanges of data cross enterprise boundaries

  - Industry best practices must be followed

  - The most interoperable and widely supported technologies should be used to ensure adoption regardless of development and deployment platforms used

  - The technologies chosen shall be well specified, with active communities and tools and/or frameworks available. For example, WS-I, or RESTful in conjunction with AtomPub, OData or GData. [Restful vs. SOAP is an open item?]

  - Technologies chosen shall be compatible and interoperable with technologies specified for access to HAN resources. [which resources?]

  - Security and privacy of customer information is of utmost importance, since transfers must use public networks, and sensitive customer information may be exchanged across enterprise boundaries.

- Recommendations must promote and enable interoperability

  - Many utilities need to be interoperable with many 3rd Parties, so there are significant efficiency savings possible by defining a common interface for the OpenADR message exchanges. Therefore, recommendations must be specific and prescriptive, actionable and testable

- Must meet the goals of several different types of stakeholders

  - Requires an open process to allow discussion and negotiation of the recommendation

- Forwards and backwards version compatibility is needed

  - Existing implementations must remain operational when either side adds future extensions

## Architectural Considerations

OpenADR as a system needs to be architected with requirements that cover the entire spectrum of business, technical, and market needs.  The following list of architectural attributes will be used as guidelines for OpenADR systems requirements development.

- System quality attributes discernable at runtime

  - Performance - Services SHALL provide and consume data in a timely manner

  - Security –

    - Parties involved in any DR event SHALL be authenticated and authorized;

    - Command/message exchanged between parties involved in any DR event SHALL be secure from end to end.

    - Results of the DR event execution SHALL be auditable.

  - Authorization – Protected resources SHALL be authorized individually by the user(s) associated with those resources.

  - Availability – Services SHALL be highly available

  - Functionality – SHALL meet the functional needs of customers and regulators

  - Usability – SHALL require only commonly available tools and technologies

  - Scalability – SHALL be able to add additional servers to meet performance

- System quality attributes requiring assessment for evaluation

  - Modifiability – SHALL allow additions without affecting existing systems

  - Portability – SHALL be possible to implement on a variety of platforms

  - Reusability – SHALL use standard industry object representations

  - Integrability – SHALL be possible to map to a variety of other interfaces

  - Testability – SHALL be possible to perform testing using a variety of methods

- Business Qualities

  - Cost – SHALL not be cost-prohibitive

  - Projected life time of the system – SHALL allow growth

- Qualities directly related to the architecture

  - Conceptual integrity – Semantics of defined elements SHALL be consistent across objects that use those elements

  - Correctness and completeness - Is aligned with common application architectures and addresses all considerations required for interoperability.

Note that desired, minimum and maximum levels for performance, availability, functionality, acceptable use, and other characteristics will likely be specified and negotiated in Service Level Agreements (SLAs) between 3rd Parties and Utilities. Regulators may also require certain service levels. Each side will likely have some number of terms required for use of their services. This is not part of the standardization effort, just a note to prepare for these agreements.

# OpenADR Systems Architecture

## OpenADR Business Architecture View

The key stakeholders to be addressed by the business architecture are shown in the figure below.  The stakeholders all perform business roles and represent a subset of the Actors from the use cases which fill business roles in the OpenADR business processes, as described in the Open ADR Functional Requirements and Use Case Document.

Figure 3.  OpenADR Stakeholders Overview

The primary business flows include DR Program Administration, Bidding, and Execution as shown in the following diagram. The swim lanes represent business roles and the blocks within the swim lanes correspond to a business process carried out by that business role. Business roles are related to the Actors identified earlier; however, in some cases multiple different Actors may carry out the same business role. For example, an ISO/RTO, Utility Distribution Company (UDC), Load Serving Entity, or DR Aggregator can all perform the business role of Controlling Entity.  The business processes shown are those that involve the exchange of information between business roles.

Figure 4.  Overview of Business Process Flows

The Business Roles used in the Business Process Flow are summarized from the Use Cases and represent activities performed at the business level. Section 3.2.2 Functional Requirements – Integration Services maps these business roles into integration roles as described in that section.

Following is a table listing all major Business Roles that will provide some functions to support ADR business processes.

| Business Role | Description / Key Business Functions | Map to NIST |
| --- | --- | --- |
| Load Serving Entity | A role which carries the responsibility of serving end-users and selling electric energy to end-users. (PAPs) The entity that is responsible for serving the Electricity Customers Electricity needs. An LSE may also perform the role of DR Aggregator. (Base Use Case) |  |
| Electricity Consumer | The end users of electricity. May also generate, store, and manage the use of energy. Traditionally, three customer types are discussed, each with its own domain: home, commercial/building, and industrial. | Utility Customer |
| Energy Service Provider | A business entity that provides energy services to end users in a deregulated retail market. (NAESB Use Cases) | Service Provider |
| Demand Response Provider (DRP) | An entity or role with the responsibility to coordinate demand resources to deliver demand response services. A DRP includes entities that have acquired curtailment rights from electricity consumers, and manage the aggregation of capacity that is curtailable as an eligible energy or capacity resource for participating in Demand Response programs. (PAP09 Retail dated 2/11/2010 v 1.5) |  |
| DR Asset Owner | The entity that is responsible for the DR Resource or Asset in the retail market. |  |
| DR Controlling Entity | This is a generalized actor class and represents all the different entities that may need to manage and interact with wholesale and/or retail DR resources. It includes the following actors: ISO/RTO, Distribution Company, Load Serving Entity, DR Aggregator. (PAP09 Retail dated 2/11/2010 v 1.5) |  |
| DR Asset | An energy resource that is capable of shedding load in response to Demand Response Events, Electricity Price Signals or other system events (e.g. under frequency detection). Examples of Demand Response Assets are: Smart Appliances, entire buildings that are under the control of an Energy Management System, Electric Vehicles. (PAP09 Retail dated 2/11/2010 v 1.5) |  |
| DR Resource | A DR resource is a virtual representation of one or more DR assets. It is similar to a DR Asset in that it is capable of shedding load in response to a triggering event. Unlike a DR Asset, which is autonomous, a DR Resource may consist of multiple DR Assets that have been aggregated to form a larger capacity or energy resource. An apartment building with multiple electricity consumers, each one having one or more DR Assets may be considered one large DR Resource by aggregating the total load shedding capacity of all the DR Assets in the apartment building and representing the sum total of this capacity as one DR Resource. A DR Resource may also consist of different types of Assets (e.g., a wind Turbine and an electric motor that work in combination to meet DR program obligations). (PAP09 Retail dated 2/11/2010 v 1.5) |  |
| System and Market Operator | A System Operator is a Balancing Authority, Transmission Operator, or Reliability Coordinator whose responsibility is to monitor and control an electric system in real time (based on NERC definition). The System Operator is responsible for initiating Demand Response Events (e.g., Advance Notifications, Deployment, and Release/Recall instructions). The Market Operator manages the bulk electricity market and produces prices for various products. ISO New England and PJM Interconnection are examples of Market and System Operators that perform this function. (PAP09 Retail dated 2/11/2010 v 1.5) |  |

## Integration Requirements Specification

### Functional Requirements – Business Processes

The business processes that have been developed as part of OpenADR are listed as follows.  Note that the requirements documents summarized in section 1.4 External Considerations and References contain the details of each business process (use case).

The following requirements are identified based the use cases defined in Open ADR Functional Requirements and Use Case Document (OpenSG) and Requirements Specifications for Retail Standard DR Signals - for NIST PAP09, Functional Specifications section of  the Open Automated Demand Response Communications Specification.

- Administrate DR Programs

  - Create DR Program

  - Update DR Program

  - Remove DR Program

- Administrate Customer for DR

  - Register / Enroll Customer for DR Program

  - Update Customer Identity

  - Remove Customer from DR Program

- Administrate DR Resource

  - Administrate Distribution DR Resource

  - Update DR Resource

  - Register DR Resource

- Administrate DR Asset (Direct)

  - Register DR Asset

  - Update DR Asset

  - Remove DR Asset

- DR Bidding

  - DR Bid to Supply (Retail Offers)

  - DR Bid to Buy

- Execute DR Event

  - Notify DR Event (Retail)

  - Advanced Notification for DR (Retail)

  - Update a DR Event (Retail)

  - Cancel a DR Event (Retail)

  - DR Resource Confirmation (Retail)

  - Broadcast DR Message (Price Plus Information)

  - Dispatch DR Instructions (Retail)

    - DR Direct Load Control (Retail)

    - Monitor DR Event (DR Resource)

    - Monitor DR Event (DR Asset)

  - DR Event Execution

    - DR Execution - Retail Time Pricing (RTP)

    - DR Execution - Notification Based

    - DR Execution - Direct Load Control (DLC)

  - Operational Coordination

    - Post DR Event Management

    - Post DR Event M&V / Settlement (No Open Retail)

    - Post DR Event M&V / Settlement (Open Retail)

### Functional Requirements – Integration Services

#### Logical Components

Logical Components are used in this document to organize interfaces (integration services) for OpenADR.  These logical components represent IT systems which exchange information to carry out the business processes and implement the use cases identified earlier. They may be mapped to specific physical components for a particular implementation. The Logical Components in some cases consolidate multiple Business Roles/Actors to represent entities which perform a common integration role in exchanging information. For example, a DR Controlling Entity is a generalized actor class which represents all the different entities that may need to manage and interact with wholesale and/or retail DR resources. It represents actors such as an ISO/RTO, Distribution Company, Load Serving Entity, and DR Aggregator.

Following is a table listing all major logical components that will provide some functions to support ADR business processes.  All services will be organized accordingly.

| Logical Components | Description / Key Business Functions | Map to NIST |
| --- | --- | --- |
| Electricity Consumer | The end users of electricity. May also generate, store, and manage the use of energy. Traditionally, three customer types are discussed, each with its own domain: home, commercial/building, and industrial. | Utility Customer |
| DR Asset Owner | The entity that is responsible for the DR Resource or Asset in the retail market. |  |
| DR Controlling Entity | This is a generalized actor class and represents all the different entities that may need to manage and interact with wholesale and/or retail DR resources. It includes the following actors: ISO/RTO, Distribution Company, Load Serving Entity, DR Aggregator. (PAP09 Retail dated 2/11/2010 v 1.5) |  |
| DR Asset | An energy resource that is capable of shedding load in response to Demand Response Events, Electricity Price Signals or other system events (e.g. under frequency detection). Examples of Demand Response Assets are: Smart Appliances, entire buildings that are under the control of an Energy Management System, Electric Vehicles. (PAP09 Retail dated 2/11/2010 v 1.5) |  |
| DR Resource | A DR resource is a virtual representation of one or more DR assets. It is similar to a DR Asset in that it is capable of shedding load in response to a triggering event. Unlike a DR Asset, which is autonomous, a DR Resource may consist of multiple DR Assets that have been aggregated to form a larger capacity or energy resource. An apartment building with multiple electricity consumers, each one having one or more DR Assets may be considered one large DR Resource by aggregating the total load shedding capacity of all the DR Assets in the apartment building and representing the sum total of this capacity as one DR Resource. A DR Resource may also consist of different types of Assets (e.g., a wind Turbine and an electric motor that work in combination to meet DR program obligations). (PAP09 Retail dated 2/11/2010 v 1.5) |  |
| System and Market Operator | A System Operator is a Balancing Authority, Transmission Operator, or Reliability Coordinator whose responsibility is to monitor and control an electric system in real time (based on NERC definition). The System Operator is responsible for initiating Demand Response Events (e.g., Advance Notifications, Deployment, and Release/Recall instructions). The Market Operator manages the bulk electricity market and produces prices for various products. ISO New England and PJM Interconnection are examples of Market and System Operators that perform this function. (PAP09 Retail dated 2/11/2010 v 1.5) |  |

The following figure represents the Business Process Flows consolidated using the Logical Components.

Figure 5.  Overview of Business Process Flows Using Logical Components.

The following diagram shows the logical components involved in data exchanges. The exchanges are identified at a high level in order to show the major types of functions carried out.

Figure 6.  Overview diagram of Logical Components

Note that a DR Controlling Entity may represent a single Actor, such as a Utility Distribution Company in the business role of a Load Serving Entity. However, a DR Controlling Entity may also represent a hierarchy of entities, such as an ISO/RTO dispatching DR instructions to a Transmission Operator, who in turn sends the dispatch instructions on to a UDC, who sends instructions to a DR Aggregator, who then directs a specific DR Resource to execute the instruction. This can be modeled as a recursive relationship with DR Controlling Entity which represents each of these Actors in an integration role. The goal is to minimize the number of different logical components and hence the number of different services and message payloads that need to be defined through reuse of the standard services and payload definitions.

This concept is elaborated more extensively in a recent EPRI report titled Concepts to Enable Advancement of Distributed Energy Resources. This approach is made possible as we shift from designing control systems which issue direct load controls to system viewed as a grid resource which “has the ability to handle to handle a situation in an effective manner”, where the “how” of the response is replaced by a description of the situation requiring a change in energy consumption, leaving it to the final DR Resource to know how to control DR Assets to effect the desired change in energy use. The concept put forward by the EPRI report is called the REC-VEN concept, where the REC (Resource Energy Controller) determines when and why to send specific grid messages to the resources it manages, which are represented as a VEN (Virtual End Node). A VEN can in turn also function as a REC to another VEN which is lower down in the control hierarchy – thus the recursive nature of a REC-VEN object.

In the diagram above, the DR Controlling Entity can be thought of as a REC-VEN object, thus representing all the entities in series from the System and Market Operator to the DR Resource. This is modeled by adding a recursive relation to a DR Controlling Entities, so that the DR Controlling Entity in the diagram represents one or more entities. This approach ensures a scalable architecture for all future Smart Grid developments.

#### Integration Services

The following Integration Services were derived from the Use Cases, Business Processes, and Functional Specifications documents defined earlier (Section 3.2.1) and represent the services needed to carry out the necessary data exchanges between logical components. The source of the requirement is defined in the “Requirements Source” column. Since the Service names are based the PAP09 Retail and OpenADR Use Case documents, only the remaining requirements sources are cited individually.

Each service is assigned a priority within the current release or defined for a future release as defined in the “Priority/Release” column.

[Still includes some references to UDC and LSE, need to determine if they are acting as DR Controlling Entity or as UDC or LSE.]

| Use Case Scenario | Service Name | Service Provider | Functional Description of the Service | Priority/ Release | Requirements Source |
| --- | --- | --- | --- | --- | --- |
| Create DR Program | Created DR Program | DR Controlling Entity | DR Program is created and published. |  | OADRS 7.1.3 |
| Update DR Program | Update DR Program | DR Controlling Entity | DR Program is updated and updates published. |  | OADRS 7.1.3 |
| Cancel DR Program | Cancelled DR Program | DR Controlling Entity | DR Program is terminated and notice published. |  | OADRS 7.1.3 |
| Register Customer for DR Program | Register Customer for a DR Program | Customer | Register a Customer for a DR Program. Customer registers with DR Controlling Entity (Utility or DRP). |  | OADRS 7.1.3 |
| Update Customer for DR Program | Update Customer for a DR Program | Customer | Updates to Customer registration information are provided for Utility or DRP. |  | OADRS 7.1.3 |
| Remove Customer from DR Program | Cancel Customer for DR Program | Customer | Customer notifies Utility or DRP of cancellation/removal from DR program. (Contingent on contractual obligations) |  | OADRS 7.1.3 |
| Register DR Resource | Register DR Resource | DR Resource Owner | The Resource is registered and associated with a Customer and DR Program |  |  |
| Remove DR Resource | Remove DR Resource | DR Resource Owner | The Resource is removed (message format only specifies Resource ID and Effective Date/Time) Removed from Program or totally?, probably need 2 messages or program status update. |  |  |
| Register DR Asset | Register DR Asset | DR Asset Owner or Customer | The Asset is registered and associated with a Customer and DR Program |  |  |
| Update DR Asset | Update DR Asset | DR Asset Owner | The Asset is updated. |  |  |
| Remove DR Asset | Remove DR Asset | DR Asset Owner | The Asset is removed (message format specifies Resource ID and Contract) Removed from Program or totally?, probably need 2 messages or program status update. |  |  |
| DR Bidding |  |  | Process currently out of scope | Phase II | OADRS 7.1.2 |
| DR Event Advance Notification | Notify DR Event | DR Controlling Entity | DR Controlling Entity provides the advance notification of a DR Event to a DR Resource to provide scheduled Operation Mode and Event Information |  | OADRS 7.1.1 |
| DR Event Advance Notification | Confirm DR Resource for Event | DR Resource | DR Resource opts in/out for DR Event. Response to DR Event Advance Notification and Update DR Event. |  | OADRS 7.1.1 |
| Update DR Event | Update DR Event | DR Controlling Entity | Update of Event Notice for Resource. |  | OADRS 7.1.1 |
| Cancel DR Event | Cancel DR Event | DR Controlling Entity | Cancellation notice from DR Controlling Entity to DR Resource. |  | OADRS 7.1.1 |
| DR Broadcast Message (Price Plus) | Broadcast DR Message | DR Controlling Entity | DR Broadcast Message to DR Resource for Pricing Information. (May include other attributes of Energy Delivery) Directly from SO or MO or LSE or through DR Controlling Entity. |  |  |
| Dispatch DR Instructions (Retail) | Dispatch DR Instruction | DR Controlling Entity | DR Controlling Entity provides specific objectives to the DR Resource. |  |  |
| Dispatch DR Instructions (Retail) | Confirm DR Resource | DR Resource | DR Resource Confirms DR Instruction (opt in/out ?) |  | OADRS 7.3.1 |
| DR Direct Load Control (Retail) | Created Direct Load Control | DR Controlling Entity | Direct interactions between the DR Service Provider and a specific DR Asset for the purposes of putting that asset into a specific load control state (e.g., to turn it on or off). In this case, the DR Asset is a DR Resource with only one DR Asset, and thus, the interaction is directly with the DR Asset. |  | SEP2TRD 10.4 |
| Monitor DR Event (DR Resource) | Monitor DR Event (DR Resource) | DR Resource | Response from DR Resource to DR Controlling Entity used to monitor a DR Resource's behavior. It may be executed as a result of the DR Resource receiving a DR signal or it may be conducted continuously. |  | SEP2TRD 10.4 |
| Monitor DR Event (DR Asset) | Publish DR Asset Status | DR Asset | Response from DR Asset to DR Controlling Entity used to monitor a DR Asset's behavior. It may be executed as a result of the DR Asset receiving a DR signal or it may be conducted continuously. |  | SEP2TRD 10.4 |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Forecast Load By Circuit | DR Controlling Entity | DR Controlling Entity provides Load Forecast to UDC and MO. [Content undefined] |  |  |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Broadcast Locational Wholesale Price | SO or MO | Wholesale Locational Price Information provided by the SO or MO to the LSE |  |  |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Broadcast Locational Retail Price | LSE | Retail Locational Price Information provided by the LSE to the Customer and DR Controlling Entity after aggregation and uplift. |  | EIS-UC-19,ID3 |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Update Load Forecast (Forecast DR) | DR Controlling Entity | DR Controlling Entity provides Load Forecast adjusted by expected DR to LSE. |  | EIS-ID15 (Customer to DRCE) |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Update Load Forecast by Circuit (Forecast DR by Circuit) | DR Controlling Entity | DR Controlling Entity provides Load Forecast by Circuit adjusted by expected DR to UDC. |  |  |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Schedule Approved, No violations | UDC | UDC approves DR Schedule based on check against circuit limits |  |  |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Suggested Schedule Adjustment | UDC | UDC sends suggested schedule adjustments based on circuit limits. (Process for reprocessing schedule is not defined) |  |  |
| DR Execution – Notification Based | Load Forecast | DR Controlling Entity | DR Controlling Entity provide Load Forecast to SO/MO |  |  |
| DR Execution – Notification Based | Load Forecast by Circuit | DR Controlling Entity | DR Controlling Entity provides Load Forecast by Circuit to UDC |  |  |
| DR Execution – Notification Based | DR Capability | Customer | Customer notifies DRP of DR Capability |  |  |
| DR Execution – Notification Based | DR Nomination | DR Controlling Entity | DR Controlling Entity Nominates DR Capability to LSE and SO/MO |  |  |
| DR Execution – Notification Based | DR Dispatch Instructions | SO/MO | SO/MO sends DR Dispatch Instructions to DRP and LSE |  |  |
| DR Execution – Notification Based | DR Schedule by Circuit | DR Controlling Entity | DR Controlling Entity provides DR Schedule by Circuit to UDC. |  |  |
| DR Execution – Notification Based | Schedule Approved, No violations | UDC | UDC approves DR Schedule based on check against circuit limits |  |  |
| DR Execution – Notification Based | Suggested Schedule Adjustment | UDC | UDC sends suggested schedule adjustments based on circuit limits. (Process for reprocessing schedule is not defined) |  |  |
| DR Execution – Notification Based | Final DR Schedule | DR Controlling Entity | DR Controlling Entity sends final DR Schedule to LSE based on Approved Schedules. |  |  |
| DR Execution – Notification Based | Notify Customer of DR Schedule | DR Controlling Entity | DR Controlling Entity Notifies Customer of DR Schedule |  |  |
| DR Execution – Direct Load Control (DLC) | DR Capability | Customer | Customer notified DRP of DR capability. |  |  |
| DR Execution – Direct Load Control (DLC) | DR Capability Aggregated by Network Location | DR Controlling Entity | DR Controlling Entity provides DR Capability aggregated by network location to UDC. |  |  |
| DR Execution – Direct Load Control (DLC) | DR Capability Aggregated by Location | DR Controlling Entity | DR Controlling Entity provides DR Capability aggregated by network location to SO/MO. |  |  |
| DR Execution – Direct Load Control (DLC) | DR Dispatch Instructions | SO/MO | SO/MO sends DR Dispatch Instructions to DRP and LSE |  |  |
| DR Execution – Direct Load Control (DLC) | Advisory Information on pending DR | DR Controlling Entity | DR Controlling Entity send advisory to LSE of pending DR Event |  |  |
| DR Execution – Direct Load Control (DLC) | DR Control Schedule by Circuit | DR Controlling Entity | DR Controlling Entity provides DR Schedule by Circuit to UDC. |  |  |
| DR Execution – Direct Load Control (DLC) | Schedule Approved, No violations | UDC | UDC approves DR Schedule based on check against circuit limits and notifies DRP. |  |  |
| DR Execution – Direct Load Control (DLC) | Suggested Schedule Adjustment | UDC | UDC sends suggested schedule adjustments based on circuit limits to DRP. (Process for reprocessing schedule is not defined) |  |  |
| DR Execution – Direct Load Control (DLC) | Control Signal | DR Controlling Entity | DR Controlling Entity send control signal to Customer asset. |  |  |
| DR Execution – Direct Load Control (DLC) | Telemetry Data | Customer Asset | Customer Asset provides telemetry data to DR Controlling Entity. |  |  |
| DR Execution – Direct Load Control (DLC) | Aggregated DR Telemetry | DR Controlling Entity | DR Controlling Entity provides aggregated telemetry data to SO/MO |  |  |
| Post DR Event M&V / Settlement (Open Retail) | Request Meter Read | LSE | LSE requests meter read from Customer Resource |  |  |
| Post DR Event M&V / Settlement (Open Retail) | Created Meter Read | Resource | Resource provides meter read to LSE |  |  |
| Post DR Event M&V / Settlement (Open Retail) | Created Meter Read | LSE | LSE provides meter read to DR Controlling Entity |  |  |
| Post DR Event M&V / Settlement (Open Retail) | Created Billing | DR Controlling Entity or LSE | DR Controlling Entity or LSE provides Billing information to Customer. |  |  |
| Post DR Event M&V / Settlement (No Open Retail) | Request Meter Read | LSE | LSE requests meter read from Customer Resource |  |  |
| Post DR Event M&V / Settlement (No Open Retail) | Created Meter Read | Resource | Resource provides meter read to LSE (Read interval must match interval of DR Event) |  |  |
| Post DR Event M&V / Settlement (No Open Retail) | Created Billing | LSE | LSE provides Billing information to Customer. |  |  |

### Draft 1

### Technical Requirements – Integration Services

Integration services that are well defined, understood and managed are the linchpin of an open and interoperable implementation between the utility enterprise and other business entities.  Following is a list of guiding principles for integration services design:

- Common protocol and business semantics SHALL be used to achieve loose coupling of end-point service (directly or indirectly)

- Services SHALL be representative of a unique unit of work and reusable across business functions.

- Services SHALL be reusable across common practices of utilities.

- Service design SHALL be driven by business requirements and reflected in the architecture.

- Service design SHALL be governed with a common approach and framework to achieve conceptual integrity.

- Service level agreement should be defined to support key architecture qualities: security, reliability, performance, availability, scalability, data quality, information fidelity, etc.

## OpenADR Application Architecture View

- Audit information SHOULD be maintained, so that a report could be produced containing details (who, what, when, etc.) about authorizations, transfers, and other significant events.

## OpenADR Data Architecture View

Based on OpenADR use cases, the following data objects have been identified. The OpenADR services SHALL implement methods to make requests related to these objects.

- xxx Messages

  - functions.

### DR Signal Data Requirements [PAPs contain summary of data requirements]

| Data Element | Description |
| --- | --- |

### DR Management Data Requirements

| Data Element | Description |
| --- | --- |

Note that some extensions may have been included in the above that are not shown in the logical data model diagram in the next section, but these will be in sync when the actual message structure is built.

## OpenADR Technical Architecture View

Given a large variety of integration technologies that exist in the market place and in the utility enterprises, it would be up to each utility to implement the OpenADR systems requirements specification that fit with their chosen technology infrastructure and architecture goals.  However, regardless of the technologies, the following architectural issues are important and needs to be addressed when it comes to achieving interoperability.

### Networking Standards

- OpenADR services SHALL be provided via TCP/IP (internet) networks. (See [RFC-1122])

- OpenADR services SHALL be exposed primarily using the HTTPS protocol. (See [RFC-1123])

- OpenADR services MAY support Secure FTP. Since OpenADR requires HTTPS, FTP is only an option if both parties implement and agree to use FTP. (Note that requiring support is in discussion.)

### Security Standards

A major component of OpenADR is ensuring that protected resources, including data, can and will be secured to prevent unauthorized access. This responsibility originates with the utility, where the data is obtained, and is passed to 3rd Party providers when customers authorize their use of specific utility data. To ensure that data is not provided to unauthorized parties, the constraints and controls documented in [ASAP-SG-3P] are to be complied with for OpenADR installations.

Using the terminology specified in the ASAP-SG Third Party Data Access document, the customer is the Resource Owner, the Data Service Provider is the Resource Custodian. (The 3rd Party is still called the Third Party)

### Service / Resource Patterns

Service and/or resource naming standards are important to achieve a level of “plug & play” at the run time environment.  It implies the semantics of the service and its operations.

The OpenADR services naming convention has the following rules:

- Information Object – Collection of entities (classes and attributes) to describe an object in a business context.

- Service / Resource Name – Service naming convention follows the information object in a business process for an interface definition.

- Operation Name – Operation name indicates a specific action that will be performed to the Information Object. Here is a list of operation naming patterns utilizing IEC 61989 verbs (See IEC61968-1 Specification for details):

- The following verbs are used for service/operation provided by the master system that owns the Information Object to entertain the request for the specified action implied by the verb.

    - Create

    - Change

    - Cancel

    - Close

    - Delete

- The following verbs are used for service/operation provided by systems that are interested in receiving the Information Object as the result of the specified action implied by the verb.  This can be invoked by the master system or an intermediary to supply the Information Object.

    - Created

    - Changed

    - Closed

    - Canceled

    - Deleted

- The following verbs are used for query type services provided by the master system of the Information Object.

    - Get

    - Show

- The following verbs are not used within OpenADR.

    - Subscribe

    - Unsubscribe

## Governance

Governance defines the rules by which parties participating in interoperability (integration, or data exchange) efforts can change the interfaces and components providing and consuming them, in order to maintain efficient operation. For OpenADR, governance includes guidelines recommended for addition or extension of standard interfaces, as well as modifications to or extensions to become part of the standard.

- Changes shall be made to be backwards compatible (optional additions only), to allow existing implementations to continue to operate.

- Participants are encouraged to submit extensions to the working group as business requirements, with additional recommendations as necessary, to be discussed, ratified, and added to periodic updates.

# Appendices

## Terms and Definitions

This subsection provides the definitions of all terms required to properly interpret the OpenSG OpenADR SRS.

| Term | Definition |
| --- | --- |
| Advanced Metering Infrastructure (AMI) | The infrastructure built around advanced metering allowing the utility and consumer to communicate in real time with respect to energy consumption. Based on the information collected, the utility is able to obtain an accurate reading of demands, while consumers are able to modify their usage to save energy. |
| Daily Consumption | The amount of energy a customer uses in a 24 hour period. This information is used to drive business intelligence solutions. |
| Data Service Provider | The utility, or organization acting on behalf of the utility, that is providing the OpenADE service. |
| IEC | The International Electrotechnical Commission (IEC). The IEC TC57 maintains an electric utility focused information model called CIM (Common information model). |
| IEC 61968 | International standards for Energy Distribution Managements Systems, respectively, specify a Common Information Model (CIM) for utility data exchange, Applications Programming Interfaces (API) for application integration (GID), and XML messaging standards. |
| Logical Data Model | A representation of an organization’s data based upon entities and attributes of those entities. A logical data model is often a logical representation of a business’ integration or business requirements. |
| SLA | Service Level Agreement: the part of a service contract where the level of the services are agreed upon between two systems. |

| CIM Term | Definition |
| --- | --- |
| IntervalBlock | Used within a MeterReading to identify a time sequence of Readings of the same ReadingType. |
| IntervalReading | Data captured at regular intervals of time. Interval data could be captured as incremental data, absolute data, or relative data. The source for the data is usually a tariff quantity or an engineering quantity. Data is typically captured in time-tagged, uniform, fixed-length intervals of 5, 10, 15, 30, or 60 minutes. Interval Data is sometimes also called “Interval Data Readings” (IDR). |
| MeasurementValueSource | MeasurementValueSource describes the alternative sources updating a MeasurementValue. User conventions for how to use the MeasurementValueSource attributes are described in the introduction to IEC 61970-301. |
| MeterReading | Used to convey quantities that are measured by a meter. |
| Reading | Used to convey a specific value measured by a meter or other asset. Each Reading is associated with a specific ReadingType. |
| ReadingType | Used to identify the type of data that is conveyed by a specific Reading. |
| ServiceDeliveryPoint | There can be multiple service points at a single ServiceLocation, each one identified as a ServiceDeliveryPoint. They deliver service in accordance with a CustomerAgreement. |

# Footnotes

The OpenADR Task Force of the Open Smart Grid Users Group acknowledges the work coordinated by the Demand Response Research Center and funded by the California Energy Commission (Energy Commission), Public Interest Energy Research (PIER) Program in development of the Open Automated Demand Response Communications Specification, also known as OpenADR or Open Auto-DR. For the purposes of this document the specification will be cited using the full title. The term OpenADR SRS or SRS refers to the OpenSG OpenADR System Requirements Specification.

Requirements Specifications for Wholesale Standard DR Signals - for NIST PAP09, Requirements Specifications for Retail Standard DR Signals - for NIST PAP09

Concepts to Enable Advancement of Distributed Energy Resources : White Paper on DER. EPRI, Palo Alto, CA : 2010. 1020432.

Abbreviation for OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION

Abbreviation for ZigBee Smart Energy Profile™ 2.0 Technical Requirements Document

Abbreviation for Energy Information Standards (EIS) Alliance Customer Domain Use Cases

# Comments

I think this is an important aspect of scoping the SRS properly and we should discuss at the face to face.

We should discuss the scope of this at the face to face.

There are some architectural requirements  I want to make sure are captured somewhere in the document, but I’m still unsure  where they fit in.  We will discuss them at the f2f and afterwards can decide how best to integrate them into this document.