OpenADR 1.0 System Requirements Specification

Version: Draft v0.4

Issued for review prior to Draft 1 on: 5/2/2010

[Draft 1] Release Date: 05/04/2010

Acknowledgements

The following individuals and their companies have contributed and/or provided support to the work of the OpenADR System Requirements Specification:

The OpenADR Task Force wishes to thank all of the above-mentioned individuals and their companies for their support of this important endeavor, as it sets a key foundation for an interoperable Smart Grid.

Document History

Revision History

Date of this revision: April 13, 2010

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 0.1 | 4/13/2010 | Bruce Bartell | Initial draft “shell” based on OpenADE SRS | N |
| 0.2 | 4/20/2010 | Bruce Bartell | Updated through sections 3.2.1 | N |
| 0.2 | 4/30/2010 | Bruce Bartell | Updated through sections 3.2.2 | N |
| 0.3 | 5/1/2010 | Ed Koch | Scope update and comments for F2F | N |
| 0.4 | 5/7/2010 | Bruce Bartell | Incorporate feedback from OSG Quarterly |  |
| 0.4 | 5/14/2010 | Bruce Bartell | Added Integration Service Messages based on Entity, Priorities. |  |
| 0.4 | 5/18/2010 | Bruce Bartell | Added attributes & definitions for Priority 1 messages |  |

Open Issues Log

Last updated: April 13, 2010

As issues are addressed in new versions of this document, they are removed from this list.

| Issue Date | Provided By | Summary of the Issue |
| --- | --- | --- |

Contents

1	Introduction	6

1.1	Purpose	6

1.2	Scope	7

1.2.1	Scope of This Release	7

1.2.2	Scope of Subsequent Releases	8

1.3	Acronyms and Abbreviations	9

1.4	External Considerations and References	9

1.4.1	RFC 2119 Keyword interpretation	10

1.5	Document Overview	10

2	Architecture Vision	12

2.1	Architectural Goals and Guiding Principles	13

2.2	Architectural Considerations	13

3	OpenADR Systems Architecture 	15

3.1	OpenADR Business Architecture View	15

3.2	Integration Requirements Specification	18

3.2.1	Functional Requirements – Business Processes	18

3.2.2	Functional Requirements – Integration Services	21

3.2.3	Technical Requirements – Integration Services	26

3.3	OpenADR Application Architecture View	26

3.4	OpenADR Data Architecture View	27

3.4.1	DR Dispatch Signal Data Requirements	29

3.4.2	DR Event Data Requirements	33

3.4.3	Asset / Resource Status (State)	36

3.4.4	DR Resource	37

3.4.5	DR Asset	43

3.4.6	Demand Response Program	45

3.4.7	Demand Response Customer Agreement	47

3.5	OpenADR Technical Architecture View	48

3.5.1	Networking Standards	48

3.5.2	Security Standards	48

3.5.3	Service / Resource Patterns	48

3.6	Governance	50

4	Appendices	51

4.1	Terms and Definitions	51

4.2	Integration Services – Detailed Messages by Use Case	52

List of Figures

Figure 1.  OpenADR component diagram showing the actors and components.	8

Figure 2.  The Open Group Architecture Framework (TOGAF) architecture development cycle.	11

Figure 3.  OpenADR Stakeholders Overview	15

Figure 4.  Overview of Business Process Flows	16

Figure 5.  Overview of Business Process Flows Using Logical Components.	22

Figure 6.  Overview diagram of Logical Components	23

Figure 7.  REC-VEN Operations 3	24

# Introduction

The Open Smart Grid Open Automated Demand Response (OpenADR) is an industry-led initiative under the Open Smart Grid (OpenSG) subcommittee within the UCA International Users Group (UCAIug).  The OpenADR Task Force defines systems requirements, policies and principles, best practices, and services, required for business and data requirements for standardizing control and pricing signals for Demand Response (DR) and Distributed Energy Resources (DER) as part of the Smart Grid implementation. OpenADR, as an open user group forum, is developing a set of utility-ratified requirements and specifications for utilities and 3rd Parties to adopt and implement.  The end-state of this effort will contribute to the development of open and interoperable Demand Response solutions.

This will be achieved by defining and making the following OpenADR related items available to the market:

- Common business processes and functional requirements

- Common architecture principles and patterns

- Common information requirements and model

- Common integration services (functional & informational)

## Purpose

The purpose of this document is to provide both the functional and technical guidance and requirements needed to serve as the “rules of engagement” for messaging and data exchange to achieve interoperability.  This would lead to open and interoperable components that can be delivered with different vendor products and/or solutions within the scope of OpenADR.  The functional requirements will be driven by business processes and the technical requirements will be driven by desired architectural principles and best practices.

## Scope

The SRS focuses on the requirements to support the interactions and exchange of information for the purposes of Demand Response (DR) and includes the exchanges of DR related information between various entities such as Utilities, Independent System Operators (ISO’s), Aggregators, Energy Service Providers and end use customers. The scope of OpenADR SRS includes standardizing dispatch, control and pricing signals for DR and Distributed Energy Resources (DER) as part of the Smart Grid implementation as defined in the Open ADR Functional Requirements and Use Case Document  (OpenSG).

Demand Response is defined as the temporary modification of customer energy usage for a defined duration which is triggered by some condition on the grid such as reliability or market conditions. These DR events result in the exchange of “DR signals” between service providers such as Utilities, ISO’s, Aggregators, ESP’s, etc. and their customers. The information in the DR signals causes modifications to the end users load profiles. The requirements in the SRS are from the perspective of the enterprise systems of the service providers that are publishing the DR signals to their customers (i.e. Utility). This is in contrast to the customer’s systems or perspective which is covered in other efforts such as OpenHAN and SEP. The thing that all the various efforts have in common is the need to exchange the DR related information in some standardized form. Furthermore this SRS does not cover many of the administrative aspects of managing a DR program such as measurement and verification and settlement.  The SRS is focused on only those aspects of DR management that is required to facilitate the exchange of DR signals with their customers.

The SRS defines the logical components and business functions in order to identify the interfaces that must be specified to enable interoperability across different implementations, for many utilities to many 3rd Parties.  It includes architectural aspects and specific requirements.  The inputs include OpenADR use cases, as well as industry best practices and standards, including information models and other specifications.

### Scope of This Release

OpenADR SRS 1.0 addresses the following functional areas:

- Direct Load Control Signals

- Dispatching of Load Profiles

- DR Related Pricing Signals

- DER applications (limited to the context of grid-connected DR)

- DR Program Management (Limited to data required to support DR Signals)

  - Program and Customer Registration

  - DR Resource Registration

### Scope of Subsequent Releases

- Utility internal systems integration for DR purposes

- DR Bidding

  - DR Bid to Supply (Retail Offers)

  - DR Bid to Buy

Figure 1.  OpenADR component diagram showing the actors and components.

The OpenADR SRS does not include the following items that are typically a part of solution architecture.  Some of them are or have been addressed by other parts of the OpenSG initiative.  Others will need to be dealt with specifically for each implementation.

- Network and hardware infrastructure architecture

- Operational architecture

- Testing methodology and architecture

- Internal application architecture

## Acronyms and Abbreviations

This subsection provides a list of all acronyms and abbreviations required to properly interpret the OpenSG OpenADR System Requirements Specification.

| Acronym | Name |
| --- | --- |
| ADE | Automatic Data Exchange |
| ADR | Automated Demand Response |
| AMI | Advanced Metering Infrastructure |
| CIM | IEC TC57 Common Information Model |
| DLC | Direct Load Control |
| DR | Demand Response |
| EMS | Energy Management System |
| ESP | Energy Service Provider |
| ESI | Energy System Interface; Energy Services Interface |
| HAN | Home Area Network |
| IETF | Internet Engineering Task Force |
| IHD | In-Home Display |
| ISO | Independent System Operator |
| IT | Information Technology |
| M&V | Measurement and Verification |
| NERC | North American Electric Reliability Corporation |
| PHEV | Plug-In Hybrid Electric Vehicle |
| RTO | Regional Transmission Organization |
| RTP | Real Time Pricing |
| SDO | Standards Development Organization |
| SEP 2.0 | Smart Energy Profile |
| SLA | Service Level Agreement |
| SRS | System Requirements Specification |
| TOGAF | The Open Group Architecture Framework |

## External Considerations and References

The work of the OpenADR SRS is dependent upon the requirements defined in the following sources:

- Open ADR Functional Requirements and Use Case Document  (OpenSG)

- Requirements Specifications for Wholesale Standard DR Signals - for NIST PAP09

- Requirements Specifications for Retail Standard DR Signals - for NIST PAP09

- OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION - Public Interest Energy Research (PIER), California Energy Commission

- Requirements Specifications for Common Electricity Product and Pricing Definition - for NIST PAP03

- Requirements Specifications for Common Scheduling Mechanism for Energy Transactions - for NIST PAP04

- ZigBee Smart Energy Profile™ 2.0 Technical Requirements Document

- Energy Information Standards (EIS) Alliance Customer Domain Use Cases

The work of OpenADR SRS is dependent upon the best practices available from the following entities and standards organizations:

- IETF Internet Suite - Internet Standards, including the following

          - [RFC-793] IETF Transmission Control Protocol (TCP)

          - [RFC-791] IETF Internet Protocol (IP)

          - [RFC-2616] Hypertext Transfer Protocol -- HTTP/1.1

- [IEC-61968] IEC TC57 Working Group 14 (IEC 61968) (Common Information Model)

- [ASAP-SG-3P] Security Profile for Third Party Access (ASAP-SG)

### RFC 2119 Keyword interpretation

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this document are to be interpreted as described in RFC 2119.

## Document Overview

TOGAF 9.0 defines four architecture domains that are commonly accepted as subsets of overall enterprise architecture, all of which TOGAF is designed to support, see Figure 2:

- Architecture Vision defines overall architecture guiding principles, goals and objectives and desired traits.

- The Business Architecture defines the business strategy, governance, organization, and key business processes.

- The Information Systems Architecture, including the following.

  - The Data Architecture describes the structure of an organization's logical and physical data assets and data management resources.

  - The Application Architecture provides a blueprint for the individual application systems to be deployed, their interactions, and their relationships to the core business processes of the organization.

- The Technology Architecture describes the logical software and hardware capabilities that are required to support the deployment of business, data, and application services. This includes IT infrastructure, middleware, networks, communications, processing, standards, etc.

Figure 2.  The Open Group Architecture Framework (TOGAF) architecture development cycle.

As such, the document will be structured as follows:

Section 2 describes the overall Architecture Vision for the system, including Guiding Principles, Architectural Considerations, and the OpenADR Reference Model, all relevant to providing a consistent framework within which the four architecture components can be developed.

Section 3 provides details on the following:

- Business Architecture:  This will refer to work products produced by the Use Case and Service Definition Teams of OpenADR, which includes the list of use cases and integration requirements and business services at the functional level.

- Data Architecture:  This provides the technical level requirements relative to how the OpenADR data should be modeled and represented consistently across all integration services to ensure semantic interoperability.

- Application Architecture: This provides the technical level requirements relative to how applications are modeled as logical components, and what services each logical component may provide or consume. This should be an instantiation of the business services identified within the Business Architecture.

- Technology Architecture: This provides the technical level requirements relative to how services will interact with each other to support end-to-end AMI business processes.

Section 4 contains the Appendices, which includes terms and definitions, logical components list, integration requirements list, and integration services view.

# Architecture Vision

The Architecture Vision articulates the Architectural Goals and Principles that enables the business goals and addresses the stakeholder concerns and objectives. As stated in the Introduction, the goal is the development of open and interoperable Demand Response solutions.

## Architectural Goals and Guiding Principles

Architecture guiding principles are rules of engagement designed to ensure that all aspects of the implementation fit within a well-defined framework.  These principles, discussed and agreed upon with all stakeholders of the OpenADR, are used to drive the architectural approach and patterns to be implemented.  These principles should not be taken lightly as they imply what and how the overall goals of OpenADR will be met.  Each of the principles has a level of effort and cost implications for utilities and 3rd Parties looking to adopt this specification.  Adherence to these principles can be adjusted for specific cases driven by time and budget constraints.  These exceptions should be approved by all stakeholders and must be documented.

- Exchanges of data cross enterprise boundaries

  - Industry best practices must be followed

  - The most interoperable and widely supported technologies should be used to ensure adoption regardless of development and deployment platforms used

  - The technologies chosen shall be well specified, with active communities and tools and/or frameworks available. For example, WS-I, or RESTful in conjunction with AtomPub, OData or GData.

  - Technologies chosen shall be compatible and interoperable with technologies specified for access to HAN resources.

  - Security and privacy of customer information is of utmost importance, since transfers must use public networks, and sensitive customer information may be exchanged across enterprise boundaries.

- Recommendations must promote and enable interoperability

  - Many utilities need to be interoperable with many 3rd Parties, so there are significant efficiency savings possible by defining a common interface for the OpenADR message exchanges. Therefore, recommendations must be specific and prescriptive, actionable and testable

- Must meet the goals of several different types of stakeholders

  - Requires an open process to allow discussion and negotiation of the recommendation

- Forwards and backwards version compatibility is needed

  - Existing implementations must remain operational when either side adds future extensions

## Architectural Considerations

OpenADR as a system needs to be architected with requirements that cover the entire spectrum of business, technical, and market needs.  The following list of architectural attributes will be used as guidelines for OpenADR systems requirements development.

- System quality attributes discernable at runtime

  - Performance - Services SHALL provide and consume data in a timely manner

  - Security –

    - Parties involved in any DR event SHALL be authenticated and authorized;

    - Command/message exchanged between parties involved in any DR event SHALL be secure from end to end.

    - Results of the DR event execution SHALL be auditable.

  - Authorization – Protected resources SHALL be authorized individually by the user(s) associated with those resources.

  - Availability – Services SHALL be highly available

  - Functionality – SHALL meet the functional needs of customers and regulators

  - Usability – SHALL require only commonly available tools and technologies

  - Scalability – SHALL be able to add additional servers to meet performance

- System quality attributes requiring assessment for evaluation

  - Modifiability – SHALL allow additions without affecting existing systems

  - Portability – SHALL be possible to implement on a variety of platforms

  - Reusability – SHALL use standard industry object representations

  - Integrability – SHALL be possible to map to a variety of other interfaces

  - Testability – SHALL be possible to perform testing using a variety of methods

- Business Qualities

  - Cost – SHALL not be cost-prohibitive

  - Projected life time of the system – SHALL allow growth

- Qualities directly related to the architecture

  - Conceptual integrity – Semantics of defined elements SHALL be consistent across objects that use those elements

  - Correctness and completeness - Is aligned with common application architectures and addresses all considerations required for interoperability.

Note that desired, minimum and maximum levels for performance, availability, functionality, acceptable use, and other characteristics will likely be specified and negotiated in Service Level Agreements (SLAs) between 3rd Parties and Utilities. Regulators may also require certain service levels. Each side will likely have some number of terms required for use of their services. This is not part of the standardization effort, just a note to prepare for these agreements.

# OpenADR Systems Architecture

## OpenADR Business Architecture View

The key stakeholders to be addressed by the business architecture are shown in the figure below.  The stakeholders all perform business roles and represent a subset of the Actors from the use cases which fill business roles in the OpenADR business processes, as described in the Open ADR Functional Requirements and Use Case Document.

Figure 3.  OpenADR Stakeholders Overview

The primary business flows include DR Program Administration, Bidding, and Execution as shown in the following diagram. The swim lanes represent business roles and the blocks within the swim lanes correspond to a business process carried out by that business role. Business roles are related to the Actors identified earlier; however, in some cases multiple different Actors may carry out the same business role. For example, an ISO/RTO, Utility Distribution Company (UDC), Load Serving Entity, or DR Aggregator can all perform the business role of Controlling Entity.  The business processes shown are those that involve the exchange of information between business roles.

Figure 4.  Overview of Business Process Flows

The Business Roles used in the Business Process Flow are summarized from the Use Cases and represent activities performed at the business level. Section 3.2.2 Functional Requirements – Integration Services maps these business roles into integration roles as described in that section.

Following is a table listing all major Business Roles that will provide some functions to support ADR business processes.

| Business Role | Description / Key Business Functions | Map to NIST | Map to LBNL |
| --- | --- | --- | --- |
| Load Serving Entity | A role which carries the responsibility of serving end-users and selling electric energy to end-users. (PAP09 Retail dated 2/11/2010 v 1.5) The entity that is responsible for serving the Electricity Customers Electricity needs. An LSE may also perform the role of DR Aggregator. (Base Use Case) | Load Serving Entity |  |
| Electricity Consumer | The end users of electricity. May also generate, store, and manage the use of energy. Traditionally, three customer types are discussed, each with its own domain: home, commercial/building, and industrial. | Utility Customer | Participant |
| Energy Service Provider | A business entity that provides energy services to end users in a deregulated retail market. (NAESB Use Cases) | Service Provider |  |
| Demand Response Provider (DRP) | An entity or role with the responsibility to coordinate demand resources to deliver demand response services. A DRP includes entities that have acquired curtailment rights from electricity consumers, and manage the aggregation of capacity that is curtailable as an eligible energy or capacity resource for participating in Demand Response programs. (PAP09 Retail dated 2/11/2010 v 1.5) |  |  |
| DR Asset Owner | The entity that is responsible for the DR Resource or Asset in the retail market. |  |  |
| DR Controlling Entity | This is a generalized actor class and represents all the different entities that may need to manage and interact with wholesale and/or retail DR resources. It includes the following actors: ISO/RTO, Distribution Company, Load Serving Entity, DR Aggregator. (PAP09 Retail dated 2/11/2010 v 1.5) |  |  |
| DR Asset | An energy resource that is capable of shedding load in response to Demand Response Events, Electricity Price Signals or other system events (e.g. under frequency detection). Examples of Demand Response Assets are: Smart Appliances, entire buildings that are under the control of an Energy Management System, Electric Vehicles. (PAP09 Retail dated 2/11/2010 v 1.5) |  |  |
| DR Resource | A DR resource is a virtual representation of one or more DR assets. It is similar to a DR Asset in that it is capable of shedding load in response to a triggering event. Unlike a DR Asset, which is autonomous, a DR Resource may consist of multiple DR Assets that have been aggregated to form a larger capacity or energy resource. An apartment building with multiple electricity consumers, each one having one or more DR Assets may be considered one large DR Resource by aggregating the total load shedding capacity of all the DR Assets in the apartment building and representing the sum total of this capacity as one DR Resource. A DR Resource may also consist of different types of Assets (e.g., a wind Turbine and an electric motor that work in combination to meet DR program obligations). (PAP09 Retail dated 2/11/2010 v 1.5) |  | DRAS Client |
| System and Market Operator | A System Operator is a Balancing Authority, Transmission Operator, or Reliability Coordinator whose responsibility is to monitor and control an electric system in real time (based on NERC definition). The System Operator is responsible for initiating Demand Response Events (e.g., Advance Notifications, Deployment, and Release/Recall instructions). The Market Operator manages the bulk electricity market and produces prices for various products. ISO New England and PJM Interconnection are examples of Market and System Operators that perform this function. (PAP09 Retail dated 2/11/2010 v 1.5) |  |  |

## Integration Requirements Specification

### Functional Requirements – Business Processes

The business processes that have been developed as part of OpenADR are listed as follows.  Note that the requirements documents summarized in section 1.4 External Considerations and References contain the details of each business process (use case).

The following requirements are identified based the use cases defined in Open ADR Functional Requirements and Use Case Document (OpenSG) and Requirements Specifications for Retail Standard DR Signals - for NIST PAP09, Functional Specifications section of  the Open Automated Demand Response Communications Specification.

- Administrate DR Programs (Limited to data required to support DR Signals)

  - Create DR Program

  - Update DR Program

  - Remove DR Program

- Administrate Customer for DR (Limited to data required to support DR Signals)

  - Register / Enroll Customer for DR Program

  - Update Customer Attributes

  - Remove Customer from DR Program

- Administrate DR Resource (Limited to data required to support DR Signals)

  - Administrate Distribution DR Resource

  - Update DR Resource

  - Register DR Resource

- Administrate DR Asset (Direct Load Control)

  - Register DR Asset

  - Update DR Asset

  - Remove DR Asset

- DR Bidding

  - DR Bid to Supply (Retail Offers)

  - DR Bid to Buy

- Execute DR Event

  - Notify DR Event

    - Includes Advanced Notification for DR

  - Update a DR Event

  - Cancel a DR Event

  - DR Resource Confirmation

  - Broadcast DR Message (Price Plus Information)

  - Dispatch DR Objectives

    - DR Direct Load Control

    - Monitor DR Event (DR Resource)

    - Monitor DR Event (DR Asset)

  - DR Event Execution

    - DR Execution - Real Time Pricing (RTP)

    - DR Execution - Notification Based (includes Advance Notification)

    - DR Execution - Direct Load Control (DLC)

  - Operational Coordination

    - Post DR Event Management (out of scope, handled by other groups: AMI and if only meter reads and billing?)

    - Post DR Event M&V / Settlement (No Open Retail)

    - Post DR Event M&V / Settlement (Open Retail)

### Functional Requirements – Integration Services

#### Logical Components

Logical Components are used in this document to organize interfaces (integration services) for OpenADR.  These logical components represent IT systems which exchange information to carry out the business processes and implement the use cases identified earlier. They may be mapped to specific physical components for a particular implementation. The Logical Components in some cases consolidate multiple Business Roles/Actors to represent entities which perform a common integration role in exchanging information. For example, a DR Controlling Entity is a generalized actor class which represents all the different entities that may need to manage and interact with wholesale and/or retail DR resources. It represents actors such as an ISO/RTO, Distribution Company, Load Serving Entity, and DR Aggregator.

Following is a table listing all major logical components that will provide some functions to support ADR business processes.  All services will be organized accordingly.

| Logical Components | Description / Key Business Functions | Map to NIST | Map to LBNL |
| --- | --- | --- | --- |
| Electricity Consumer | The end users of electricity. May also generate, store, and manage the use of energy. Traditionally, three customer types are discussed, each with its own domain: home, commercial/building, and industrial. | Utility Customer |  |
| DR Asset Owner | The entity that is responsible for the DR Resource or Asset in the retail market. |  |  |
| DR Controlling Entity | This is a generalized actor class and represents all the different entities that may need to manage and interact with wholesale and/or retail DR resources. It includes the following actors: ISO/RTO, Distribution Company, Load Serving Entity, DR Aggregator. (PAP09 Retail dated 2/11/2010 v 1.5) |  |  |
| DR Asset | An energy resource that is capable of shedding load in response to Demand Response Events, Electricity Price Signals or other system events (e.g. under frequency detection). Examples of Demand Response Assets are: Smart Appliances, entire buildings that are under the control of an Energy Management System, Electric Vehicles. (PAP09 Retail dated 2/11/2010 v 1.5) |  |  |
| DR Resource | A DR resource is a virtual representation of one or more DR assets. It is similar to a DR Asset in that it is capable of shedding load in response to a triggering event. Unlike a DR Asset, which is autonomous, a DR Resource may consist of multiple DR Assets that have been aggregated to form a larger capacity or energy resource. An apartment building with multiple electricity consumers, each one having one or more DR Assets may be considered one large DR Resource by aggregating the total load shedding capacity of all the DR Assets in the apartment building and representing the sum total of this capacity as one DR Resource. A DR Resource may also consist of different types of Assets (e.g., a wind Turbine and an electric motor that work in combination to meet DR program obligations). (PAP09 Retail dated 2/11/2010 v 1.5) |  |  |
| System and Market Operator | A System Operator is a Balancing Authority, Transmission Operator, or Reliability Coordinator whose responsibility is to monitor and control an electric system in real time (based on NERC definition). The System Operator is responsible for initiating Demand Response Events (e.g., Advance Notifications, Deployment, and Release/Recall instructions). The Market Operator manages the bulk electricity market and produces prices for various products. ISO New England and PJM Interconnection are examples of Market and System Operators that perform this function. (PAP09 Retail dated 2/11/2010 v 1.5) |  |  |

The following figure represents the Business Process Flows consolidated using the Logical Components.

Figure 5.  Overview of Business Process Flows Using Logical Components.

The following diagram shows the logical components involved in data exchanges. The exchanges are identified at a high level in order to show the major types of functions carried out.

Figure 6.  Overview diagram of Logical Components

Note that a DR Controlling Entity may represent a single Actor, such as a Utility Distribution Company in the business role of a Load Serving Entity. However, a DR Controlling Entity may also represent a hierarchy of entities, such as an ISO/RTO dispatching DR instructions to a Transmission Operator, who in turn sends the dispatch instructions on to a UDC, who sends instructions to a DR Aggregator, who then directs a specific DR Resource to execute the instruction. This can be modeled as a recursive relationship with DR Controlling Entity which represents each of these Actors in an integration role. The goal is to minimize the number of different logical components and hence the number of different services and message payloads that need to be defined through reuse of the standard services and payload definitions.

This concept is elaborated more extensively in a recent EPRI report titled Concepts to Enable Advancement of Distributed Energy Resources. This approach is made possible as we shift from designing control systems which issue direct load controls to system viewed as a grid resource which “has the ability to handle to handle a situation in an effective manner”, where the “how” of the response is replaced by a description of the situation requiring a change in energy consumption, leaving it to the final DR Resource to know how to control DR Assets to effect the desired change in energy use. The concept put forward by the EPRI report is called the REC-VEN concept, where the REC (Resource Energy Controller) determines when and why to send specific grid messages to the resources it manages, which are represented as a VEN (Virtual End Node). A VEN can in turn also function as a REC to another VEN which is lower down in the control hierarchy.

Figure 7.  REC-VEN Operations 3

In the diagram above, the DR Controlling Entity can be thought of as a VEN-REC object, thus representing all the entities in series from the System and Market Operator to the DR Resource. This is modeled by adding a recursive relation to a DR Controlling Entities, so that the DR Controlling Entity in the diagram represents one or more entities. This approach ensures a scalable architecture for all future Smart Grid developments.

#### Integration Services

The following Integration Services were derived from the Use Cases, Business Processes, and Functional Specifications documents defined earlier (Section 3.2.1) and represent the services needed to carry out the necessary data exchanges between logical components. The data required for the data exchange is defined in Section 3.4.1 Data Architecture View.

Specific Service Operations and Resource Patterns are defined as part of the OpenADR Service Definition document and the associated artifacts. The operations are defined based on the methods defined in Section 3.4 OpenADR Data Architecture View.

A detailed list of individual messages in Use Case Context is provided in Section 4.2.

| Use Case Scenario | Service Name | Provider | Functional Description of the Service | Priority/ Release | Requirements Source |
| --- | --- | --- | --- | --- | --- |
| Administrate DR Program | DR Program | DR Controlling Entity | Administrate DR Program that is created, published, Changed, and Canceled. | 3 |  |
| Administrate Customer for DR | DR Customer Agreement | DR Controlling Entity | Customer is Registered for, Updated or Removed from a DR Program. | 3 |  |
| Administrate DR Resource | DR Resource | DR Resource Owner | DR Resource is registered and associated with a DR Program and Customer. The Resource is updated and/or removed from DR Program. | 2 |  |
| Administrate DR Asset | DR Asset | DR Asset Owner | DR Asset is registered and associated with a DR Resource. The Resource is updated and/or removed from DR Program. | 2 |  |
| Execute DR Event | DR Event | DR Controlling Entity | DR Event information is sent to participants in prior to the DR Event start based on defined intervals, Updated, and/or Canceled | 1 |  |
| Execute DR Event | DR Dispatch Signal | DR Controlling Entity | DR Dispatch Signal is a polymorphic message type that supports Direct Load Control, DR Instructions (Objectives), Price Schedule | 1 |  |
| Execute DR Event – Operational Coordination | Forecast Demand | DR Controlling Entity | Multiple levels of aggregated DR Demand and Telemetry data is provided for the purpose of coordinating a DR Event and to provide checks against circuit limits. Needs more complete definition. This is a combination of descriptions from the section on Operational Coordination. | 4 |  |
| Execute DR - Event Monitoring / Confirmation | Asset / Resource Status (State) | DR Resource or Asset | The DR Resource or Asset (in the event of DLC) provides status for opt in / out or other state that impacts Demand Response. The Status message may be as a confirmation reply to a DR Signal or as an update resulting from a state/status change or in response to a Get message. | 1 |  |
| Post DR Event – M&V / Settlement | Meter Read & Billing |  | The process and messages used for settlement of a DR event are the same as defined in the UtilityAMI AMI-ENT System Requirements Specification, UtilityAMI AMI-ENT Task Force. The meter read interval is determined by the interval of DR Event participation. | 5 |  |
| DR Bidding |  |  |  | 6 |  |

### Technical Requirements – Integration Services

Integration services that are well defined, understood and managed are the linchpin of an open and interoperable implementation between the utility enterprise and other business entities.  Following is a list of guiding principles for integration services design:

- Common protocol and business semantics SHALL be used to achieve loose coupling of end-point service (directly or indirectly)

- Services SHALL be representative of a unique unit of work and reusable across business functions.

- Services SHALL be reusable across common practices of utilities.

- Service design SHALL be driven by business requirements and reflected in the architecture.

- Service design SHALL be governed with a common approach and framework to achieve conceptual integrity.

- Service level agreement should be defined to support key architecture qualities: security, reliability, performance, availability, scalability, data quality, information fidelity, etc.

## OpenADR Application Architecture View

- Audit information SHOULD be maintained, so that a report could be produced containing details (who, what, when, etc.) about authorizations, transfers, and other significant events.

- OpenADR Application Architecture SHALL provide measures that protect and defend information and information systems by ensuring their availability, integrity, authentication, confidentiality, and non-repudiation.

## OpenADR Data Architecture View

Based on OpenADR use cases, the following data objects have been identified. The OpenADR services SHALL implement methods to make requests related to these objects.

- Demand Response Program

  - Create

  - Update

  - Terminate

- Customer Agreement for DR

  - Register Customer for DR Program

  - Update Customer for DR Program

  - Remove Customer from DR Program

- Asset (End Device)

  - Register Asset for DR Program

  - Update Asset for DR Program

  - Remove Asset from DR Program

- Resource (Device Group)

  - Register Resource for DR Program

  - Update Resource for DR Program

  - Remove Resource from DR Program

- Demand Response Event

  - Advance Notification

  - Update Event

  - Cancel Event

- Demand Response Dispatch Signal

  - Types:

    - Direct Load Control Signal

    - Demand Response Instructions / Objectives (DR Dispatch)

    - Price Signal / Schedule

  - Updates

  - Cancel

- Forecast Demand

- Asset / Resource Status (Monitor Demand Response Event)

  - Response to Signal

  - Get Status/State

  - Continuous Response

### DR Dispatch Signal Data Requirements

| DR Dispatch Signal is a polymorphic message type that supports Direct Load Control, DR Instructions (Objectives), Price Schedule. The message is defined for all DR Dispatch types, Price Plus, Objectives, Direct Load Control | Map to |
| --- | --- |
| Data Element | Description | PAP09 Retail | OADRCS |
|  |  | PAP09 Wholesale | Map to SEP 2.0 TRD |
|  | All DR Dispatch Types |  |  |
| Dispatch (Event) Type | Identifies the type of the DR Dispatch |  | EventInfoType. EventInfoTypeID |
| DR Program Name | An identifier of the program for which a DR event was issued. | DR Program Name | UtilityProgram.name |
|  |  |  | DR event name |
| DR Resource ID | An identifier of the DR Resource for which a dispatch is intended. | DR Resource ID |  |
| Event ID | An identifier for the DR event that was created when the DR event was first issued. | Event ID | eventIdentifier |
|  |  |  | DR event ID |
| Event Modification Number | A modification number for the DR event. This is used to indicate if the DR Event has been modified by the Utility. Each time it is modified, this number is incremented. | Event Modification Number | eventModNumber |
| Event Schedule | Schedule for the DR Event periods, which includes the following: • Notification date/time • Event start date/time • Event end date/time. | Event Schedule | EventInfoInstance. Values .value .startTime |
|  |  |  | DR event start date/time DR event end date/time DR event duration |
| Test Event Flag | This attribute signifies whether this is a test event or not. Test events may be issued by the Utility/ISO like other DR Events. | Test Event Flag |  |
|  | Price Plus Information |  |  |
| Currency | Identifier used to interpret the price element. MUST follow ISO 4217 standard. | Currency |  |
| Duration | The amount of time for which this price is valid, commencing at the Effective-Date-Time specified. A value of zero means price is valid until next price broadcast override. Specified in decimal notation where integers represent minutes and decimals represent fractions of minutes. For example: 5 indicates that prices will be published every 5 minutes .5 indicates that prices will be published every 30 seconds | Duration | duration |
| Effective-Date-Time | The date and time which the price is in effect. In ISO 8601 standard format. The date and time interval which the price is in effect. | Effective-Date-Time |  |
| Location | An identifier used to indicate an area which this price is in effect. A value of "null" indicates that the price is in effect for all areas. | Location |  |
| Location-type | A value used to interpret the value contained in the Location element. Examples of Location-type include: Zone Node Zip-code USNG | Location-type |  |
| Message-Exchange-Pattern | The means by which price information is communicated to any party that is interested in receiving this information. The following are valid options: In-Only Robust In-Only In-Out Refer to http://www.w3.org/TR/wsdl20-adjuncts/#patterns for complete descriptions. [WSDL specific requirement?] | Message-Exchange-Pattern |  |
| Price | Expressed in decimal notation with a precision up to 6 decimal places. Prices MAY be either positive or negative. Single of multiple valued price (e.g., for energy, demand, etc.) | Price |  |
| Product-Identifier | Identifies the type of product (e.g. energy, regulation, etc.) which this price pertains. Contains an enumeration of various products that may be offered. Extensibility MUST be supported in order to accommodate multiple jurisdictions and markets. | Product-Identifier |  |
| Publishing-Interval | Indicates the frequency with which price information is expected to be published. Specified in decimal notation where integers represent minutes and decimals represent fractions of minutes. For example: 5 indicates that prices will be published every 5 minutes .5 indicates that prices will be published every 30 seconds | Publishing-Interval |  |
| Source-Authentication | The recipient of a "Price Message" must have some assurance that the message was produced by a reliable, authoritative party. This will require some ability to validate the authenticity of the source and integrity of the data (e.g. digital signature applied to a price message). | Source-Authentication |  |
| TimeStamp | Indicates the Date and Time when this information was published. MUST follow ISO 8601 standard representation. | TimeStamp |  |
| Unique-Identifier | An identifier used to identify the message. Should be expressed as a URI in accordance with http://www.w3.org/TR/uri-clarification/#uri-schemes | Unique-Identifier |  |
| Unit-of-Measure | Indicates the unit of measure for which the price pertains. MUST be complaint with the International System of Units as defined by NIST SP 330, ref: http://physics.nist.gov/Pubs/SP330/sp330.pdf Examples of NIST compliant units of measure include: kWh MWh | Unit-of-Measure |  |
|  | DR Objectives / Instructions |  |  |
| Dispatch Instructions | A collection of dispatch instructions that is associated with a DR event. An instance of such instructions represents a specific type of instruction that was defined specifically for the DR program. Each type of instruction may have a schedule of values that are valid across the entire period for which the DR event is active. Therefore, a single type of instruction may have multiple values, each of which are valid during a different time period during the event. Each type of instruction has the following attributes when it is defined: • name • Instruction type. The following instruction types should be supported: • LOAD_LEVEL - Amount of load based on an enumeration, i.e., moderate, high, etc • LOAD_AMOUNT - Fixed amount of load to shed in kW • LOAD_PERCENTAGE - Percentage of load to shed, i.e., 10%. | Dispatch Instructions | EventInfoTypeID EventInfoValue |
|  | Direct Load Control |  |  |
| DR Resource ID | An identifier of the DR Resource for which the control is intended. | DR Resource ID |  |
| Status Check | A signal to inquire the DR resource status to be sent back | Status Check |  |
| Pending DLC Notification | A signal indicating a pending DLC operation – A multi-value signal indicating the start time, duration, and the magnitude (kW, or resource specific options) of the control. | Pending DLC Notification |  |
| DR Control Command | This may include multiple parameters Schedule for the DR initiation, or termination, and type/level of control. Please note that the control signal may be sent to a building EMS or a smart device with a multi-function control capability. | DR Control Command |  |
| Source-Authentication | This is for authentication of the control signal. | Source-Authentication |  |
| Unique-Identifier | An identifier used to identify the message. | Unique-Identifier |  |
| Event Duration | Event Duration (definition in “price” signal is also an interval ) |  |  |
|  |  |  | DR event duration |
|  | Demand Response Program Type |  |  |
|  |  |  | DR event type |
| DR Group | Abstraction for management of group communications or the data for a group of related devices. Commands can be issued to all of the devices that belong to a group using a defined group address. |  |  |
|  |  |  | DR group (utility enrollment group) |
|  |  |  | Optional SEP 2.0 HAN Device IDs HAN Device Class Heating Temperature offset/setpoint Cooling Temperature offset/setpoint Load adjustment offset Duty cycle Event control DR event cancel control Cancel effective date/time |

### DR Event Data Requirements

| An Event consists of the time periods, deadlines, and transitions during which Demand Resources perform. (PAP09 Wholesale) | Map to |
| --- | --- |
| Data Element | PAP09 Retail | PAP09 Retail | OADRCS |
|  |  | PAP09 Wholesale | Map to SEP 2.0 TRD |
| Event ID | An identifier for the DR Event that was created when the DR event was first issued. This should be a globally unique identifier for each Service Provider. | Event ID | eventIdentifier |
|  |  | Event ID |  |
| Service Provider ID | An identifier for the Service Provider issuing the DR event. [Original Issuer? Or sender of this event message?] [Could be ID of multiple actors or component types] | Service Provider ID | accountID |
| DR Program ID | An identifier of the program for which a DR event was issued. | DR Program ID | UtilityProgram.name |
| DR Resource Group ID | A group to which a DR Resource belongs. This can be used for multi-cast notifications. [Need more definition; a construct to group resources makes sense, but would it be needed in as a message element for events] | DR Resource Group ID |  |
| DR Resource ID | An identifier of the DR Resource for which an Event is intended. [Could be any node in the VEN chain? Or a specific Resource?] | DR Resource ID | drasClientID |
| DR Resource Operation Mode (Schedule) | Operation modes are representations of how the DR Resource should respond to the Event Data that is part of an event. Operation modes allow DR logic to be implemented within the DR Service Provider and allow the DR Resource to respond to a much simpler representation of the DR Event data. Operation modes are simple enumerations of the values that may be scheduled during the DR Event active period. The possible values are the following: NORMAL - This value is used to signify that no response to the DR Event is necessary by the DR Resource. MODERATE - This value is typically used to signify a moderate level of response by the DR Resource. HIGH- This value is typically used to signify a high level of response by the DR Resource. SPECIAL- This value is typically used to signify a circumstance special to the DR Resource. | DR Resource Operation Mode (Schedule) | operationModeValue |
| DR Resource Specifications | This specifies which DR Assets within a DR Resource should be used, and can be specified in the following fashion: Geographic location Grid location DR Asset group ID | DR Resource Specifications | Location gridLocation coordinate participantlist.groups |
| DR Resource Type ID | A program specific field that can be used to identify a type of DR Resource within a DR program. | DR Resource Type ID |  |
| Event Data | A collection of information that is associated with a DR event. An instance of such information represents a specific type of information that was defined to exist for DR events when the program was first developed and implemented. For example, a DR program may have been developed and implemented to use real-time pricing as the values that are sent when DR events are issued. In that case, the information would be prices. Furthermore, each type of information may have a schedule of values that are valid across the entire period for which the DR event is active. Therefore, a single type of information may have multiple values, each of which are valid during a different time period during the event. Each type of information has the following attributes when it is defined: name data type. The following data types should be supported: PRICE_ABSOLUTE - Price number PRICE_RELATIVE - Change in price PRICE_MULTIPLE - Multiple of current price LOAD_LEVEL - Amount of load based on an enumeration, i.e. moderate, high, etc LOAD_AMOUNT - Fixed amount of load to shed in kW LOAD_PERCENTAGE - Percentage of load to shed, i.e. 10% GRID_RELIABILITY - Number signifying the reliability of the grid. | Event Data | EventInfoTypeID EventInfoValue EventInfoInstance.EventInfoTypeName EventInfoInstance.value |
| Event Schedule | A Schedule for the DR Event periods that includes the following: • Notification date/time • Event start date/time • Ramp time (potentially randomized) • Event end date/time (possibly specified as the duration). | Event Schedule | UtilityDREvent.EventTiming & EventInfoInstance. EventInfoValue.StartTime |
|  |  | Event Day Event Start Time Event End Time |  |
| Test Event Flag | This attribute signifies whether this is a test event or not. Test events may be issued by the Utility/ISO like other DR audit events. | Test Event Flag | testEvent |
| Event Modification Number | This is Modification number of the DR event. It is used to indicate that the DR Event has been modified by the Utility. Each time a DR Event is modified, this number is incremented. | Event Modification Number | eventModNumber |
| Modification reason code | The reason the event was modified. | Modification reason code | Extension of EventState? |
| Cancellation reason code | The reason the event is being cancelled. | Cancellation reason code |  |
| (Cancel) Effective date/time | The date and time a cancellation takes effect. | (Cancel) Effective date/time |  |
| Event State | This represents the state of a single DR Event. There will be one of these sent for each DR Event that is either pending or active. If there are no DR Events pending or active then there will be one of these sent with the EventStatus field of the simpleDRModeData set to "NONE". Note that when the EventStatus is set to NONE then some of the elements and attributes of this entity are not applicable. See the documentation for each element and attribute to see which are not applicable when the EventStatus is set to NONE. |  | eventState |
|  |  | Event Status |  |
|  | PAP09 Wholesale includes attributes for Baseline Calculation and other. |  |  |
| Baseline Dates | Dates of days used to calculate the Energy Baseline |  |  |
| Baseline Exclusion Dates | Dates of days Excluded from the calculation of the Energy Baseline |  |  |
|  |  | Baseline Exclusion Dates |  |
| Energy Baseline Value | Calculated Energy Baseline |  |  |
|  |  | Energy Baseline Value |  |
| Energy Baseline Timestamp | Timestamp of Energy Baseline |  |  |
|  |  | Energy Baseline Timestamp |  |
| Reporting Interval | Interval size required for Reporting |  |  |
|  |  | Reporting Interval |  |

### Asset / Resource Status (State)

| Asset/Resource Status (State) is a confirmation message that is sent by a DR Resource to the Service Provider as a result of receiving a DR Signal form the Service Provider. It may be used as an acknowledgement of the receipt of the DR signal, but it may also contain various information used to signify how the DR Resource will respond to the DR Signal. | Map to |
| --- | --- |
| Data Element | Description | PAP09 Retail | OADRCS |
|  |  | PAP09 Wholesale | Map to SEP 2.0 TRD |
| DR Resource ID | The identifier of the DR Resource. | DR Resource ID |  |
| Exception Conditions | This is used to report that the load controller may not behave as commanded because of a variety of conditions including: Faults in device Customer override. | Exception Conditions |  |
| Load Control State | The state of the load, which includes both commanded states and user settings. This may include a schedule of future states if a particular control algorithm for the load controller is being executed. | Load Control State | ResponseSchedule |
|  |  |  | Req[DRLC-3] No specific data requirement |
| Operational Constraints | Constraints on how the load may be controlled. This may include limits on the state of the load controller as well as schedules upon those constraints. | Operational Constraints |  |
| DR Assets Characteristics | The expected response characteristics of each DR Asset that is part of the DR Resource. These may be needed for aggregated DR Assets and may be as simple as whether a DR Asset is participating or its actual load profile. For each DR Asset, the following should be given: Location of Asset, either geographic or grid location Asset schedule of participating Asset load profile (schedule). | DR Assets Characteristics |  |
| DR Resource Load Profile Response | The load profile response characterization of the DR Resource in response to getting the DR signal. | DR Resource Load Profile Response |  |
| Notification Received Acknowledgement | This is an acknowledgement of the receipt of a DR notification or dispatch. It should include any necessary provisions for non-repudiation. | Notification Received Acknowledgement |  |
| Opt in/out | This is used to temporarily opt in/out of DR Events and to override the normal operational constraints. The opt-in/out can be specified using the following criteria: All events in a program indefinitely Specific DR Event All events in a specific time period. In addition, there may be a schedule associated with the opt in/out state. | Opt in/out | OptOutState |
|  |  |  | Req[DRLC-1] No specific data requirement |

### DR Resource

| A DR Resource is a group of Assets (Response Method Aggregations) that represents a dispatchable entity. | Map to |
| --- | --- |
| Data Element | Description | PAP09 Retail | OADRCS |
|  |  | PAP09 Wholesale | Map to SEP 2.0 TRD |
| DR Resource Identifier | This identifies the DR Resource that is being registered. | DR Resource Identifier |  |
|  |  | Resource ID |  |
| DR Asset group ID |  | DR Asset group ID | participantlist.groups |
| Resource Type | Type of Resource. Valid types are: load reduction, generation, combination. |  |  |
|  |  | Resource Type |  |
| Resource Qualification Test Date | Date the Resource demonstrated its ability to deliver a product or service |  |  |
|  |  | Resource Qualification Test Date |  |
| Requalification Test Date | Date the Resource will retest its ability to deliver a product or service |  |  |
|  |  | Requalification Test Date |  |
| Available-Capacity | The total amount of power (megawatts) available from the asset/resource, expressed in integer format representing the amount of kilowatts available. | Available-Capacity |  |
| Customer Identifier | This is a customer identifier (e.g., account number) that signifies the owner of the DR Resource to the Utility. | Customer Identifier | participantID |
| The following attributes are applicable to a DR Resource as enrolled in a DR Program. |  |  |
| DR Program Identifier | This identifies the DR program in which a DR Resource is participating. | DR Program Identifier | program |
|  |  | Program ID |  |
| DR Resource Qualification | This shows the qualification of a DR resource for certain type(s) of DR programs | DR Resource Qualification |  |
| DR Resource Operational Constraints | These are constraints that define the amount load that can be made available during a DR event and includes the following: Minimum load Maximum load. | DR Resource Operational Constraints |  |
| DR Resource Schedule Constraints | These are a set of constraints that specify when the DR Resource will be available. It may contain such information as: Time of day schedule constraints Black out dates Maximum consecutive days of participation Maximum duration of DR event participation Minimum duration of DR event participation Max number of times per day the DR Resource may be called Minimum advanced notification necessary. Provide details if DR asset or DR resource is in any other DR programs (wholesale and retail) | DR Resource Schedule Constraints | programConstraint |
| Effective-Start-Date-Time | The start date and time which an asset/resource is available. | Effective-Start-Date-Time |  |
|  |  | Effective Enrollment Date |  |
| Program Enrollment Status | Status of the Program Enrollment for the Facility or Resource |  |  |
|  |  | Program Enrollment Status |  |
| Location | An identifier to indicate the location of the asset/resource. | Location | locationInformation |
|  |  | PAP09 Wholesale (Mandatory) Address1 Address2 City Facility State/Province Facility Zip/Postal Code Facility Country GPS Coordinates Weather Station Zone ID Zone (from CIM) Electrical Node ID Electrical Node Name Electrical Node Type PNode PNode ID |  |
| Location-type | A value used to interpret the value contained in the Location element. Examples of Location-type include: Zone Node Zip-code. | Location-type |  |
| Maximum-Duration | The maximum amount of time the asset/resource is capable of delivering power (megawatts), this may be expressed in hours using decimal notation. For example, a value of 0.5 indicates a maximum duration of 30 minutes which the asset/resource can reduce power consumption by the level indicated in Available Capacity. | Maximum-Duration | programConstraint. maxEventDuration |
| Message-Exchange-Pattern | The means by which price information is communicated to any party that is interested in receiving this information. The following are valid options: In-Only Robust In-Only In-Out. Refer to http://www.w3.org/TR/wsdl20-adjuncts/#patterns for complete descriptions. | Message-Exchange-Pattern |  |
| Minimum-Duration | The minimum amount of time that an Asset/Resource Owner is willing to allow the resource/asset to be utilized during a DR event. It may be expressed in decimal format representing hours. For example, a value of 1.5 indicates that an asset/resource must be utilized for no less than one hour and 30 minutes during any DR event. | Minimum-Duration |  |
| Parent-Resource ID | This is used by an Asset to indicate that it "belongs to" a particular Resource. Assets may be aggregated into a Resource, but are not required to be so aggregated. Resources are autonomous and may not be aggregated. | Parent-Resource ID |  |
| Report-type | This indicates the type of report being issued by the Asset or Resource Owner. This is an enumerated value containing one of the following: REGISTRATION (to register a new asset/resource) CHANGE (refers to permanent changes) RETIREMENT. | Report-type |  |
| Response-time | The amount of time before an asset/resource is capable of meeting its full performance, in response to a request by a Service Provider to shed load, expressed as minutes in decimal format. | Response-time |  |
| Source-Authentication | The recipient must have some assurance that the message was produced by a reliable, authoritative party. This will require some ability to validate the authenticity of the source and integrity of the data (e.g., digital signature applied to a price message). | Source-Authentication | clientAuthentication |
| Hourly-Capacity-Availability | The amount of capacity available for interruption by hour for the period defined by the effective start/end date, expressed in kW or MW with appropriate precision. | Hourly-Capacity-Availability |  |
| Monthly-Capacity-Availability | The average capacity available for interruption by month for the period defined by the effective start/end date, expressed in Megawatts with appropriate precision. | Monthly-Capacity-Availability |  |
| Temporary Opt-Out | This is used to temporarily opt out of DR Events and to override the normal operational constraints. The opt-out can be specified using the following criteria: All events in a program indefinitely Specific DR Event All events in a specific time period. Other triggered programs for which an asset or DR resource is already called upon (reduce double counting of available capacity) | Temporary Opt-Out |  |
| Removal Effective Date/time | Date/time when the DR resource is no longer available. Date of Termination of Enrollment | Removal Effective Date/time |  |
|  |  | Enrollment End Date |  |
| Resource / DR Program Attributes from PAP09 Wholesale |  |  |
| Lead Time | Time between the advanced notification and deployment |  |  |
|  |  | Lead Time |  |
| Day Ahead Flag | Flag set if the Resource will be participating in the Day-Ahead market |  |  |
|  |  | Day Ahead Flag |  |
| Real Time Flag | Flag set if the Resource will be participating in the Real-Time market |  |  |
|  |  | Real Time Flag |  |
| Self-Schedule Flag | Flag set if the Resource is Self-Deploying |  |  |
|  |  | Self-Schedule Flag |  |
| Response Method Type | Type of Response Method |  |  |
|  |  | Response Method Type |  |
| Response Method ID | Identifier assigned to the Response Method |  |  |
|  |  | Response Method ID |  |
| Response Method Name | Name of the Response Method |  |  |
|  |  | Response Method Name |  |
| Response Method Value | Value of the Response Method |  |  |
|  |  | Response Method Value |  |
| Verified Capability | Audited Capability |  |  |
|  |  | Verified Capability |  |
| Verified Capability Factor | Ratio of the Verified Capability to the qualified capability |  |  |
|  |  | Verified Capability Factor |  |
| Performance Evaluation Method Type Code | Code representing the Type of Measurement |  |  |
|  |  | Performance Evaluation Method Type Code |  |
| Performance Evaluation Method | Method used to Evaluate the Performance of a Resource |  |  |
|  |  | Performance Evaluation Method |  |
| Mandatory General Asset/Resource Attributes from PAP09 Wholesale |  |  |
| Loss Factor Type | Type of Loss Factor |  |  |
|  |  | Loss Factor Type |  |
| Loss Factor (value) | Loss Factor |  |  |
|  |  | Loss Factor |  |

### DR Asset

| DR Asset - A logical entity that has a reportable interval level consumption, e.g. a site may also be a physical entity that may have its own meter, a neighborhood of homes that has a net meter, or an estimate of consumption of an aggregation of retail customers. Referred to as Response Method Aggregation (RMA) in PAP09 Wholesale. | Map to |
| --- | --- |
| Data Element | Description | PAP09 Retail | OADRCS |
|  |  | PAP09 Wholesale | SEP 2.0 TRD |
| DR Asset Identifier | The unique identifier and name of the DR Assets. | DR Asset Identifier |  |
|  |  | Response Method Aggregation ID |  |
| DR Asset group ID | Grouping of Assets that can respond to the same DR Signal within a DR Resource. (See DR Resource Specification) | DR Asset group ID |  |
| Asset Operator | The business entity that operates the DR assets | Asset Operator |  |
| Asset Owner | The business entity that owns the DR assets | Asset Owner |  |
| Asset Physical Location | The location of where the DR assets reside | Asset Physical Location | locationInformation |
| Authorized Asset Servicers | The authorized service providers of the operation and maintenance of DR assets | Authorized Asset Servicers |  |
| Date of Registration and Last Update | Date of which the DR Assets registered for DR purpose. | Date of Registration and Last Update |  |
| State of Registration Process | The state/status of the registration process of the DR assets. | State of Registration Process |  |
| DR Asset Administrator | System and Operator Distribution Utility Load Serving Entity Service Providers | DR Asset Administrator |  |
| DR Asset Availability and Status | Run Status, Set point, Override status, etc. | DR Asset Availability and Status |  |
| DR Asset Physical Capabilities | Ramp Up/Down Rate, Maximum Capacity | DR Asset Physical Capabilities |  |
| DR Asset Product | Manufacturer, Model, Version, Date of Manufacturer | DR Asset Product |  |
| DR Asset Type | (DG, renewable, storage, curtailable or interruptible load) | DR Asset Type |  |
| DR Resources | The identifier of DR resources that the DR Assets belong to. | DR Resources |  |
| Authorized Asset Servicers | The authorized service providers of the operation and maintenance of DR assets | Authorized Asset Servicers |  |
| DR Asset Availability and Status | Run Status, Set point, Override status, etc. | DR Asset Availability and Status |  |
| Contractual Agreements | Contractual agreement under which the DR assets could be removed. | Contractual Agreements |  |
| Third Party Participation | The identification of third parties involved in the removal of DR assets. | Third Party Participation |  |

### Demand Response Program

| A Demand Response Program is a program that is created to provide incentive to customers to reduce or shift demand. | Map to |
| --- | --- |
| Data Element | Description | PAP09 Retail | OADRCS |
|  |  | PAP09 Wholesale | Map to SEP 2.0 TRD |
| Program ID | Identifier assigned to the Program | DR Program Identifier |  |
|  |  | Program ID |  |
| Program Name | Name of the Program |  | UtilityProgram.name |
|  |  | Program Name |  |
| Event Window | This is a start and end time (time of day) that specifies a window within which a DR event may be issued for this program. |  | ProgramConstraint.EventWindow.startTime & endTime |
| Event Window Filter | Determines how the resource behaves if an issued DR event is not within the Event Window. Values: ACCEPT, REJECT, FORCE, RESTRICT. |  | ProgramConstraint.EventWindowFilter |
| Maximum Event Duration | Maximum amount of time a DR Event can be active. |  | ProgramConstraint.maxEventDuration |
| Maximum Event Duration Filter | Determines how the resource behaves if an issued DR event exceeds the Maximum Duration. Values: ACCEPT, REJECT, FORCE, RESTRICT. |  | ProgramConstraint.maxEventDurationFilter |
| Notification Window | The minimum and maximum time prior to a DR event being active that notification of the event can be given to the participant. |  | ProgramConstraint.notificationWindow |
| Notification Filter | Determines how the resource behaves if an issued DR event notification is not within the Notification Window. Values: ACCEPT, REJECT, FORCE, RESTRICT. |  | ProgramConstraint.notificationFilter |
| Black Out Date/Times | List of date/times during which a DR Event cannot be issued. |  | ProgramConstraint.blackoutDateTimes |
| Black Out Filter | Determines how the resource behaves if an issued DR event occurs in the Black Out Window. Values: ACCEPT, REJECT, FORCE, RESTRICT. |  | ProgramConstraint.blackoutFilter |
| Valid Date Times | Date/times during which a DR Event may be issued. If undefined then it is assumed that the DR Event may be issued at any time except as specified by the other constraints. |  | ProgramConstraint.validDateTimes |
| Maximum Consecutive Days | Maximum number of consecutive days that a DR Event can be issued. |  | ProgramConstraint.maxConsecutiveDays |
| Maximum Consecutive Days Filter | Determines how the resource behaves if an issued DR event exceeds Max Consecutive Days. Values: ACCEPT, REJECT, FORCE, RESTRICT. |  | ProgramConstraint.maxConsecutiveDaysFilter |
| Event Data | A collection of information that is associated with a DR event. An instance of such information represents a specific type of information that was defined to exist for DR events when the program was first developed and implemented. For example, a DR program may have been developed and implemented to use real-time pricing as the values that are sent when DR events are issued. In that case, the information would be prices. Furthermore, each type of information may have a schedule of values that are valid across the entire period for which the DR event is active. Therefore, a single type of information may have multiple values, each of which are valid during a different time period during the event. Each type of information has the following attributes when it is defined: name data type. The following data types should be supported: PRICE_ABSOLUTE - Price number PRICE_RELATIVE - Change in price PRICE_MULTIPLE - Multiple of current price LOAD_LEVEL - Amount of load based on an enumeration, i.e. moderate, high, etc LOAD_AMOUNT - Fixed amount of load to shed in kW LOAD_PERCENTAGE - Percentage of load to shed, i.e. 10% GRID_RELIABILITY - Number signifying the reliability of the grid. | Event Data | EventInfoType |
| Schedule Type | This specifies how a schedule may be associated with the DR event information is defined and may take on the following values: NONE – There is no schedule and thus Event Data does not change values during the entire DR event ACTIVE state. DYNAMIC–The time schedule is not fixed during configuration, but can be set when the DR event is issued. STATIC–The schedule is fixed when the DR program is configured. |  | EventInfoType.scheduleType |
| Schedule | If the Schedule Type is STATIC, this is the configured schedule. A schedule is a sequence of time slots that are valid over the entire ACTIVE period of a DR event. |  | EventInfoType.Schedule |
| Enumerations | This is a list that defines a fixed set of values that the Event instance may take. If defined, the Event instance is an enumeration and can take on any of the values in the list. If left undefined, the Event instance can take on any contiguous value between the minimum Value and maximum Value. |  | EventInfoType.enumerations |

### Demand Response Customer Agreement

| A Demand Response Program is a program that is created to provide incentive to customers to reduce or shift demand. | Map to |
| --- | --- |
| Data Element | Description | PAP09 Retail | OADRCS |
|  |  | PAP09 Wholesale | Map to SEP 2.0 TRD |
| Program ID | Identifier assigned to the Program | DR Program Identifier |  |
|  |  | Program ID |  |
| Customer Identifier | This is a customer identifier (e.g., account number) that signifies the owner of the DR Resource to the Utility. | Customer Identifier | participantID |

## OpenADR Technical Architecture View

Given a large variety of integration technologies that exist in the market place and in the utility enterprises, it would be up to each utility to implement the OpenADR systems requirements specification that fit with their chosen technology infrastructure and architecture goals.  However, regardless of the technologies, the following architectural issues are important and needs to be addressed when it comes to achieving interoperability.

### Networking Standards

- OpenADR services SHALL be provided via TCP/IP (internet) networks. (See [RFC-1122])

- OpenADR services SHALL be exposed primarily using the HTTPS protocol. (See [RFC-1123])

- OpenADR services MAY support Secure FTP. Since OpenADR requires HTTPS, FTP is only an option if both parties implement and agree to use FTP. (Note that requiring support is in discussion.)

### Security Standards

A major component of OpenADR is ensuring that protected resources, including data, can and will be secured to prevent unauthorized access. This responsibility originates with the utility, where the data is obtained, and is passed to 3rd Party providers when customers authorize their use of specific utility data. To ensure that data is not provided to unauthorized parties, the constraints and controls documented in [ASAP-SG-3P] are to be complied with for OpenADR installations.

Using the terminology specified in the ASAP-SG Third Party Data Access document, the customer is the Resource Owner, the Data Service Provider is the Resource Custodian. (The 3rd Party is still called the Third Party)

### Service / Resource Patterns

Service and/or resource naming standards are important to achieve a level of “plug & play” at the run time environment.  It implies the semantics of the service and its operations.

The OpenADR services naming convention has the following rules:

- Information Object – Collection of entities (classes and attributes) to describe an object in a business context.

- Service / Resource Name – Service naming convention follows the information object in a business process for an interface definition.

- Operation Name – Operation name indicates a specific action that will be performed to the Information Object. Here is a list of operation naming patterns utilizing IEC 61989 verbs (See IEC61968-1 Specification for details):

- The following verbs are used for service/operation provided by the master system that owns the Information Object to entertain the request for the specified action implied by the verb.

    - Create

    - Change

    - Cancel

    - Close

    - Delete

- The following verbs are used for service/operation provided by systems that are interested in receiving the Information Object as the result of the specified action implied by the verb.  This can be invoked by the master system or an intermediary to supply the Information Object.

    - Created

    - Changed

    - Closed

    - Canceled

    - Deleted

- The following verbs are used for query type services provided by the master system of the Information Object.

    - Get

    - Show

- The following verbs are not used within OpenADR.

    - Subscribe

    - Unsubscribe

Event messages shall support both support both “push” and “pull” operations patterns.

## Governance

Governance defines the rules by which parties participating in interoperability (integration, or data exchange) efforts can change the interfaces and components providing and consuming them, in order to maintain efficient operation. For OpenADR, governance includes guidelines recommended for addition or extension of standard interfaces, as well as modifications to or extensions to become part of the standard.

- Changes shall be made to be backwards compatible (optional additions only), to allow existing implementations to continue to operate.

- Participants are encouraged to submit extensions to the working group as business requirements, with additional recommendations as necessary, to be discussed, ratified, and added to periodic updates.

# Appendices

## Terms and Definitions

This subsection provides the definitions of all terms required to properly interpret the OpenSG OpenADR SRS.

| Term | Definition |
| --- | --- |
| Advanced Metering Infrastructure (AMI) | The infrastructure built around advanced metering allowing the utility and consumer to communicate in real time with respect to energy consumption. Based on the information collected, the utility is able to obtain an accurate reading of demands, while consumers are able to modify their usage to save energy. |
| Demand Response | Demand Response is defined as the temporary modification of customer energy usage for a defined duration which is triggered by some condition on the grid such as reliability or market conditions. |
| IEC | The International Electrotechnical Commission (IEC). The IEC TC57 maintains an electric utility focused information model called CIM (Common information model). |
| IEC 61968 | International standards for Energy Distribution Managements Systems, respectively, specify a Common Information Model (CIM) for utility data exchange, Applications Programming Interfaces (API) for application integration (GID), and XML messaging standards. |
| Logical Data Model | A representation of an organization’s data based upon entities and attributes of those entities. A logical data model is often a logical representation of a business’ integration or business requirements. |
| SLA | Service Level Agreement: the part of a service contract where the level of the services are agreed upon between two systems. |

## Integration Services – Detailed Messages by Use Case

The list of Integration Services defined in section 3.2.2.2 was derived from the sequence interaction defined in the supporting Use Cases. This subsection is a detailed list of each interaction / message in the context of the supporting Use Case.

The source of the requirement is defined in the “Requirements Source” column. Since the Service names are based the PAP09 Retail and OpenADR Use Case documents, only the remaining requirements sources are cited individually.

Each service is assigned a priority within the current release or defined for a future release as defined in the “Priority/Release” column.

| Use Case Scenario | Service Name | Provider | Functional Description of the Service | Priority/ Release | Requirements Source |
| --- | --- | --- | --- | --- | --- |
| Create DR Program | Created DR Program | DR Controlling Entity | DR Program is created and published. |  | OADRCS 7.1.3 Program Services |
| Update DR Program | Updated DR Program | DR Controlling Entity | DR Program is updated and updates published. |  | OADRCS 7.1.3 |
| Cancel DR Program | Cancelled DR Program | DR Controlling Entity | DR Program is terminated and notice published. |  | OADRCS 7.1.3 |
| Register Customer for DR Program | Register Customer for a DR Program | DR Controlling Entity | Register a Customer for a DR Program. Customer registers with DR Controlling Entity (Utility or DRP). |  | OADRCS 7.1.3 |
| Update Customer for DR Program | Update Customer for a DR Program | DR Controlling Entity | Updates to Customer registration information are provided for Utility or DRP. |  | OADRCS 7.1.3 |
| Remove Customer from DR Program | Cancel Customer for DR Program | DR Controlling Entity | Customer notifies Utility or DRP of cancellation/removal from DR program. (Contingent on contractual obligations) |  | OADRCS 7.1.3 |
| Register DR Resource | Register DR Resource | DR Controlling Entity | The Resource is registered and associated with a Customer and DR Program |  |  |
| Remove DR Resource | Remove DR Resource | DR Controlling Entity | The Resource is removed from DR Program. |  |  |
| Register DR Asset | Register DR Asset | DR Controlling Entity | The Asset is registered and associated with a Customer and DR Program |  |  |
| Update DR Asset | Update DR Asset | DR Controlling Entity | The Asset is updated. |  |  |
| Remove DR Asset | Remove DR Asset | DR Controlling Entity | The Asset is removed from DR Program |  |  |
| DR Bidding |  |  | Process currently out of scope | Phase II | OADRCS 7.1.2 |
| DR Event Advance Notification | Notify DR Event | DR Controlling Entity | DR Controlling Entity provides the advance notification of a DR Event to a DR Resource to provide scheduled Operation Mode and Event Information |  | OADRCS 7.1.1 |
| DR Event Advance Notification | Confirm DR Resource for Event | DR Resource | DR Resource opts in/out for DR Event. Response to DR Event Advance Notification and Update DR Event. |  | OADRCS 7.1.1 |
| Update DR Event | Update DR Event | DR Controlling Entity | Update of Event Notice for Resource. |  | OADRCS 7.1.1 |
| Cancel DR Event | Cancel DR Event | DR Controlling Entity | Cancellation notice from DR Controlling Entity to DR Resource. |  | OADRCS 7.1.1 |
| DR Broadcast Message (Price Plus) | Broadcast DR Message | DR Controlling Entity | DR Broadcast Message to DR Resource for Pricing Information. (May include other attributes of Energy Delivery) |  |  |
| Dispatch DR Instructions (Retail) | Dispatch DR Instruction | DR Controlling Entity | DR Controlling Entity provides specific objectives to the DR Resource. |  |  |
| Dispatch DR Instructions (Retail) | Confirm DR Resource | DR Resource | DR Resource Confirms DR Instruction (with opt in/out) Non-repudiation required. |  | OADRCS 7.3.1 |
| DR Direct Load Control (Retail) | Created Direct Load Control | DR Controlling Entity | Direct interactions between the DR Service Provider and a specific DR Asset for the purposes of putting that asset into a specific load control state (e.g., to turn it on or off). In this case, the DR Asset is a DR Resource with only one DR Asset, and thus, the interaction is directly with the DR Asset. |  | SEP2TRD 10.4 |
| Monitor DR Event (DR Resource) | Monitor DR Event (DR Resource) | DR Resource | Response from DR Resource to DR Controlling Entity used to monitor a DR Resource's behavior. It may be executed as a result of the DR Resource receiving a DR signal or it may be conducted continuously. |  | SEP2TRD 10.4 |
| Monitor DR Event (DR Asset) | Publish DR Asset Status | DR Asset | Response from DR Asset to DR Controlling Entity used to monitor a DR Asset's behavior. It may be executed as a result of the DR Asset receiving a DR signal or it may be conducted continuously. |  | SEP2TRD 10.4 |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Forecast Load By Circuit | DR Controlling Entity | DR Controlling Entity provides Load Forecast to UDC and MO. [Content undefined] | Low compared to execution phase |  |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Broadcast Locational Wholesale Price | SO or MO | Wholesale Locational Price Information provided by the SO or MO to the LSE | Work with wholesale guys, touchpoint |  |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Broadcast Locational Retail Price | LSE | Retail Locational Price Information provided by the LSE to the Customer and DR Controlling Entity after aggregation and uplift. | touchpoint | EIS-UC-19,ID3 |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Update Load Forecast (Forecast DR) | DR Controlling Entity | DR Controlling Entity provides Load Forecast adjusted by expected DR to LSE. | Open issue on how modeled (PAP03) gap | EIS-ID15 (Customer to DRCE) |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Update Load Forecast by Circuit (Forecast DR by Circuit) | DR Controlling Entity | DR Controlling Entity provides Load Forecast by Circuit adjusted by expected DR to UDC. |  |  |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Schedule Approved, No violations | UDC | UDC approves DR Schedule based on check against circuit limits |  |  |
| DR Execution – Real Time Pricing (RTP) / Dynamic Price Based | Suggested Schedule Adjustment | UDC | UDC sends suggested schedule adjustments based on circuit limits. (Process for reprocessing schedule is not defined) |  |  |
| DR Execution – Notification Based | Load Forecast | DR Controlling Entity | DR Controlling Entity provide Load Forecast to SO/MO |  |  |
| DR Execution – Notification Based | Load Forecast by Circuit | DR Controlling Entity | DR Controlling Entity provides Load Forecast by Circuit to UDC |  |  |
| DR Execution – Notification Based | DR Capability | Customer | Customer notifies DRP of DR Capability (Same as Status/State) |  |  |
| DR Execution – Notification Based | DR Nomination | DR Controlling Entity | DR Controlling Entity Nominates DR Capability to LSE and SO/MO From PAP09 Retail – “The DR capabilities are specified by the DR Provider to the System Operator based on a DR Program, a price curve, or other nomination protocol.” Message attributes include Dispatch instructions. |  |  |
| DR Execution – Notification Based | DR Dispatch Instructions | SO/MO | SO/MO sends DR Dispatch Instructions to DRP and LSE |  |  |
| DR Execution – Notification Based | DR Schedule by Circuit | DR Controlling Entity | DR Controlling Entity provides DR Schedule by Circuit to UDC. |  |  |
| DR Execution – Notification Based | Schedule Approved, No violations | UDC | UDC approves DR Schedule based on check against circuit limits |  |  |
| DR Execution – Notification Based | Suggested Schedule Adjustment | UDC | UDC sends suggested schedule adjustments based on circuit limits. (Process for reprocessing schedule is not defined) |  |  |
| DR Execution – Notification Based | Final DR Schedule | DR Controlling Entity | DR Controlling Entity sends final DR Schedule to LSE based on Approved Schedules. |  |  |
| DR Execution – Notification Based | Notify Customer of DR Schedule | DR Controlling Entity | DR Controlling Entity Notifies Customer of DR Schedule |  |  |
| DR Execution – Direct Load Control (DLC) | DR Capability | Customer | Customer notified DRP of DR capability. |  |  |
| DR Execution – Direct Load Control (DLC) | DR Capability Aggregated by Network Location | DR Controlling Entity | DR Controlling Entity provides DR Capability aggregated by network location to UDC. |  |  |
| DR Execution – Direct Load Control (DLC) | DR Capability Aggregated by Location | DR Controlling Entity | DR Controlling Entity provides DR Capability aggregated by network location to SO/MO. |  |  |
| DR Execution – Direct Load Control (DLC) | DR Dispatch Instructions | SO/MO | SO/MO sends DR Dispatch Instructions to DRP and LSE |  |  |
| DR Execution – Direct Load Control (DLC) | Advisory Information on pending DR | DR Controlling Entity | DR Controlling Entity send advisory to LSE of pending DR Event |  |  |
| DR Execution – Direct Load Control (DLC) | DR Control Schedule by Circuit | DR Controlling Entity | DR Controlling Entity provides DR Schedule by Circuit to UDC. |  |  |
| DR Execution – Direct Load Control (DLC) | Schedule Approved, No violations | UDC | UDC approves DR Schedule based on check against circuit limits and notifies DRP. |  |  |
| DR Execution – Direct Load Control (DLC) | Suggested Schedule Adjustment | UDC | UDC sends suggested schedule adjustments based on circuit limits to DRP. (Process for reprocessing schedule is not defined) |  |  |
| DR Execution – Direct Load Control (DLC) | Control Signal | DR Controlling Entity | DR Controlling Entity send control signal to Customer asset. |  |  |
| DR Execution – Direct Load Control (DLC) | Telemetry Data | Customer Asset | Customer Asset provides telemetry data to DR Controlling Entity. |  |  |
| DR Execution – Direct Load Control (DLC) | Aggregated DR Telemetry | DR Controlling Entity | DR Controlling Entity provides aggregated telemetry data to SO/MO |  |  |
| Post DR Event M&V / Settlement (Open Retail) | Request Meter Read | LSE | LSE requests meter read from Customer Resource |  |  |
| Post DR Event M&V / Settlement (Open Retail) | Created Meter Read | Resource | Resource provides meter read to LSE |  |  |
| Post DR Event M&V / Settlement (Open Retail) | Created Meter Read | LSE | LSE provides meter read to DR Controlling Entity |  |  |
| Post DR Event M&V / Settlement (Open Retail) | Created Billing | DR Controlling Entity or LSE | DR Controlling Entity or LSE provides Billing information to Customer. |  |  |
| Post DR Event M&V / Settlement (No Open Retail) | Request Meter Read | LSE | LSE requests meter read from Customer Resource |  |  |
| Post DR Event M&V / Settlement (No Open Retail) | Created Meter Read | Resource | Resource provides meter read to LSE (Read interval must match interval of DR Event) |  |  |
| Post DR Event M&V / Settlement (No Open Retail) | Created Billing | LSE | LSE provides Billing information to Customer. |  |  |

# Footnotes

The OpenADR Task Force of the Open Smart Grid Users Group acknowledges the work coordinated by the Demand Response Research Center and funded by the California Energy Commission (Energy Commission), Public Interest Energy Research (PIER) Program in development of the Open Automated Demand Response Communications Specification, also known as OpenADR or Open Auto-DR. For the purposes of this document the specification will be cited using the full title. The term OpenADR SRS or SRS refers to the OpenSG OpenADR System Requirements Specification.

Requirements Specifications for Wholesale Standard DR Signals - for NIST PAP09, Requirements Specifications for Retail Standard DR Signals - for NIST PAP09

Concepts to Enable Advancement of Distributed Energy Resources: White Paper on DER. EPRI, Palo Alto, CA : 2010. 1020432.

Abbreviation for OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION

Abbreviation for OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION

Abbreviation for OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION

Abbreviation for OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION

Abbreviation for OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION

Abbreviation for OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION

Abbreviation for OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION

Abbreviation for OPEN AUTOMATED DEMAND RESPONSE COMMUNICATIONS SPECIFICATION

Abbreviation for ZigBee Smart Energy Profile™ 2.0 Technical Requirements Document

Abbreviation for Energy Information Standards (EIS) Alliance Customer Domain Use Cases

# Comments

There are some architectural requirements  I want to make sure are captured somewhere in the document, but I’m still unsure  where they fit in.  We will discuss them at the f2f and afterwards can decide how best to integrate them into this document.

1. Ssuggest merge LSE into Energy Service Provider. 
2. Suggest add System/Market Operator to Figure 4 as new swimlane and add process to initiate DR Event for SMO.

3. Suggest we discuss if all the Business Processes shown in Section 3.2.1 are adequately represented in Figure 4.

Suggest this LSE be thought of more as a Logical Component, and for purposes of this table we combine with Energy Service Provider and remove LSE from the table and from Figure 4, overview of business process flows.

Suggest this LSE be thought of more as a Logical Component, and for purposes of this table we combine with Energy Service Provider and remove LSE from the table and from Figure 4, overview of business process flows.

I think Ed suggested this would be better named Dispatch DR Objectives rather than Instructions. Also I wonder if DR Direct Load Control should be under Dispatch DR Instructions at all, since it is more in the nature of a control command and probably should be under only DR Event Execution.

It seems to me the distinction between Dispatch DR Instructions and DR Event Execution is not clear.

# Text boxes

DR
Controlling
Entity