OpenADR 1.0 Service Definition - Common

Version: Draft R0.9

Release Date: 10/21/2010

Acknowledgements

The following individuals and their companies have contributed and/or provided support to the work of the OpenADR 1.0 Service Definition - Common:

- Gerald Gray, Guiding Principle Consulting

- Bruce Bartell, Xtensible Solutions

- Ed Koch, Honeywell

- John Mani, Commverge

- Phil Davis,

- Shawn Hu, Xtensible Solutions

The OpenADR Task Force wishes to thank all of the contributors to OpenADR, especially the above-mentioned individuals and their companies for their support of this important endeavor, as it sets a key foundation for an interoperable Smart Grid.

Document History

Revision History

Date of this revision: Apr. 22, 2010

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 0.1 | 08/17/2010 | GRGray | Stubbed out the integration requirements identified in the OpenADR SRS | N |
| 0.2 | 09/02/2010 | GRGray | Updating issues and data elements based on the contribution of the IRC Wholesale model | N |
| 0.3 | 09/09/2010 | GRGray | Updated issue resolution based on Service Definition team meeting 9/9/2010 | N |
| 0.35 | 09/16/2010 | GRGray | Updated issue resolution and action items based on Service Definition team meeting, 9/16/2010 | N |
| 0.36 | 09/20/2010 | GRGray | Added figures showing the UML of DR Event Pricing and AssetResourceStatus message payloads | N |
| 0.5 | 09/27/2010 | GRGray | Updated all data elements tables, added UML diagrams for all message payloads, and added sections for DR Event – Opt Out, DR Event – Price “Plus”, and DR Event - Objectives. This is the baseline document; all changes will be noted from this point forward. | N |
| 0.5 | 10/1/2010 | BBartell | Updated message descriptions. | Y |
| 0.9 | 10/21/2010 | GGray | Updated UML images, finalized document for OpenSG Review | Y |

Open Issues Log

Last updated: Sep. 14, 2010

| Issue | Issue Date | Provided By | Summary of the Issue |
| --- | --- | --- | --- |
| 1 | 8/27/2010 | GRGray | DR Asset: Asset Location Type : Using servicelocation and PNode. Is support for others, (Zone, PositionPoint, CircuitSection) required? Resolution: Yes. There is a need to include both geographic location information as well as grid location information |
| 2 | 8/27/2010 | GRGray | DR Asset: DR Asset Physical Location : related to issue above; Resolution: Same as above. |
| 3 | 8/27/2010 | GRGray | DR Asset: State of Registration process: Is this status different from Enrollment.programEnrollmentStatus? Offer.dispatchStatus and Offer.commitStatus Resolution: Yes |
| 4 | 9/03/2010 | GRGray/BBartell | DR Asset: Need to make sure that the enum for commitStatus and dispatchStatus are complete; Populate list and send to IRC for confirmation. Action Item: Updated enumerations. |
| 5 | 9/03/2010 | GRGray/BBartell | DR Asset: Is EndDeviceAsset.CorporateCode sufficient for Manufactuer? Is EndDeviceAsset.utcNumber sufficient for model and version? Resolution: Yes for both elements. |
| 6 | 9/03/2010 | GRGray/BBartell | DR Asset: DR Asset Type – does DR Asset need its own type or is an association to Resource.resourceType how this should be controlled? Resolution: DR Asset Type is fundamentally different than the type being identified in DR Resource so this element is required. |
| 7 | 9/03/2010 | GRGray/BBartell | DR Event: DR Program Name, same issue with resource, have CIM:DemandResponseProgram inherit from IRC:Program Resolution: IRC : Program class is now going to inherit from identifiedObject, this gives us both the mRID from identifiedObject as well as ProgramID and ProgramName and solves the problem of inheriting from a single parent rule in the CIM (DemandResponseProgram already inherits from identifiedObject so it was inappropriate to inherit from a different class). |
| 8 | 9/03/2010 | GRGray/BBartell | DR Event: Service Point ID; need to have SP (MP) inherit from identifiedObject to pickup mRID Action Item: IRC now has SP inherit from identifiedObject |
| 9 | 9/03/2010 | GRGray/BBartell | DR Event: DemandResponseEvent already inherits from identifiedObject, can mRID be used instead of the separate attribute eventID? Meant to refer to some instance of an event, if event is modified the event ID must remain consistent. Proposed Resolution: Replace EventID with mRID |
| 10 | 9/03/2010 | GRGray/BBartell | DR Event: Event Modification, Event Modification Reason, Event Modification date/time need to be added to the IRC reference model Resolution: These attributes have been added to the IRC Reference model used in the repository. |
| 11 | 8/30/2010 | GRGray | DR Event: Location identifier calls for Location.corporateCode or ResourceGroup.mRID; which is it or should both be supported. Proposed Resolution: Location ID appears to be superfluous as once the Location Type is populated, the value of the type is known. This “may” be removed from DR Event payload, but be applicable in the DR Event – Pricing payload Action Item: Discussion item for OpenSG meeting |
| 15 | 9/03/2010 | GRGray/BBartell | DR Resource: Temporary opt-out is not in the IRC model, is IRC:Offer.dispatchStatus the appropriate element to track opt-out? Resolution: Yes. However, there needs to be an enumerator list to ensure it is fully populated, see action item related to issue #4. |
| 16 | 9/07/2010 | GRGray | AssetResourceStatus: Are "operational constraints" the same as Load Profile Response element requirement? Resolution: AssetResourceStatus payload is going to be refactored to eliminate redundant data elements from the DR Asset or DR Resource use cases. |
| 17 | 9/07/2010 | GRGray | AssetResourceStatus: Which part of DR Asset Characteristics are required since we already know this in the DR Asset, DR Resource message exchanges, i.e. Asset Location (added below)? Resolution: AssetResourceStatus payload is going to be refactored to eliminate redundant data elements from the DR Asset or DR Resource use cases. |
| 18 | 9/07/2010 | GRGray | AssetResourceStatus: Is Load Profile response the same as DR Resource Schedule constraints? Is this duplication required? Resolution: AssetResourceStatus payload is going to be refactored to eliminate redundant data elements from the DR Asset or DR Resource use cases. |
| 19 | 9/07/2010 | GRGray | AssetResourceStatus: "DR Asset Physical Capabilities" is the same as the DR Asset payload - is this duplication required? |
| 20 | 9/07/2010 | GRGray | AssetResourceStatus: "There is a common Reply.xsd that each two-way MEP will use. Is this sufficient for the purpose of this element? Shouldn't this requirement be matched with the DR Event - Dispatch use case scenario?" Resolution: AssetResourceStatus payload is going to be refactored to eliminate redundant data elements from the DR Asset or DR Resource use cases. |
| 21 | 9/07/2010 | GRGray | AssetResourceStatus: Is this the same Temporary Opt-Out that has been captured by the DR Resource requirements? Does it have the same issue (using IRC:Offer.dispatchStatus to track opting in/out)? Resolution: AssetResourceStatus payload is going to be refactored to eliminate redundant data elements from the DR Asset or DR Resource use cases. |
| 22 | 9/08/2010 | GRGray | AssetResourceStatus: Load Control State - Scheduling and control algorithms are not handled by this element - do we need to add additional elements for this status message? Scheduling may be handled by the DR Resource Load Profile element, (see related issue) Resolution: AssetResourceStatus payload is going to be refactored to eliminate redundant data elements from the DR Asset or DR Resource use cases. |
| 23 | 9/08/2010 | BBartell | AssetResourceStatus: Usage Information - IntervalReading.value What is ""near real time?"", is this a meter read value or something device specific?" IntervalReadingValue is fairly specific to metering with association needto IntervalBlock, ReadingType, Metering,… Resolution: AssetResourceStatus payload is going to be refactored to eliminate redundant data elements from the DR Asset or DR Resource use cases. |
| 24 | 9/10/2010 | GRGray/BBartell | DR Event – Direct Load Control : Simple Signal Level – does not exist in any model – what should this be mapped to? Resolution: Add enum attribute to EndDeviceControl. Added enumeration to the SEP2 EndDeviceControl class that was used in the generation of the DREvent – Direct Load Control CIM profile. |
| 25 | 9/10/2010 | GRGray/BBartell | DR Event – Direct Load Control : Criticality Level – does not exist in any model – what should this be mapped to? Resolution: SEP: EndDeviceControl.drProgramLevel |
| 26 | 9/29/2010 | GRGray | DR Event : Location is pertinent from an SO to a DR Controlling Entity, but it is not pertinent from a DR Controlling Entity to a Resource/Asset in term of triggering a DR Event |

Contents

1	Introduction	10

1.1	Rights / Management / Governance	10

1.1.1	Intellectual Property Rights	10

1.1.2	CIM Object Models	11

1.1.3	Service Resource Definitions	11

1.2	Referenced Specifications	11

1.3	Referenced Guidance	11

1.4	Namespaces	11

2	Information Objects	12

2.1	Security	12

2.2	Message document format	12

3	Versioning	13

4	Extensibility	13

5	Functional Areas	13

5.1	Common	13

5.2	Information Object Details	13

5.2.1	Demand Response Asset	13

5.2.2	Demand Response Resource	16

5.2.3	Demand Response Event – Price	20

5.2.4	Demand Response Event – Price “Plus”	22

5.2.5	Demand Response Event – Direct Load Control	27

5.2.6	DR Event – Objectives	32

5.2.7	Demand Response Event – Opt Out	36

5.2.8	Asset Resource Status	39

6	Appendix A	40

6.1	Demand Response XSDs	40

List of Figures

Figure 1 : UML diagram showing the attributes, classes, and relationship required to support the Demand Response Asset message payload	16

Figure 2 : UML model of DR Resource message payload used to support the Register, Update, and Delete DR Resource use case scenarios.  Classes prefixed with IRC indicate those which came from the IRC reference model while other classes are from the CIM.  Red lines indicate association that are not in the CIM.	19

Figure 3 : UML diagram showing the attributes, classes, and relationship required to support the DR Event - Price message payload	22

Figure 4 : UML diagram showing the classes, relationships, and attributes required to support a DR Event - Price "Plus" message payload	27

Figure 5 : UML diagram showing the attributes, classes, and relationships required to support the DR Event - Direct Load Control message payload	32

Figure 6 : UML Showing the classes, relationship, and attributes required to support the DR Event - Objectives message payload	36

Figure 7 : UML showing the classes, relationships, and attributes required to support a DR Event Opt Out message payload	38

Figure 8 : UML diagram illustrating the contents and relationships within the AssetResourceStatus message payload	40

# Introduction

The Open Smart Grid Open Automated Demand Response (OpenADR) is an industry-led initiative under the Open Smart Grid (OpenSG) subcommittee within the UCA International Users Group (UCAIug).  The OpenADR Task Force defines systems requirements, policies and principles, best practices, and services, required for business and data requirements for standardizing control and pricing signals for Demand Response (DR) and Distributed Energy Resources (DER) as part of the Smart Grid implementation. OpenADR, as an open user group forum, is developing a set of utility-ratified requirements and specifications for utilities and 3rd Parties to adopt and implement.  The end-state of this effort will contribute to the development of open and interoperable Demand Response solutions.

The OpenADR Service Definition is based on the functional requirements, architectural principles and patterns, and common information requirements defined in the OpenADR 1.0 System Requirements Specification.

As the standards development organizations recommend alterations, stakeholders will decide how to handle these changes. If possible, all changes will be made as enhancements, so that existing implementations can continue to function or be upgraded independently of others.

It is the goal of OpenSG to promote interoperability by providing an easy to use, simple set of commonly available technologies. Toward this end, our direction is to define XML formats for payload data that could be used with either a resource-oriented architecture or service-oriented architecture.

Extensions to support on-demand access to resources using REST are contained in “OpenSG OpenADE SD – REST”. Extensions to support WS-I Basic Profile web service operations are contained in “OpenSG OpenADE SD – Web Services”. This document is focused on common authorization and payload definition.

The REST document contains more details, because REST is more of a style, not a specification, and so requires more definition, while web services are more formally specified, and also the WS document refers to the AMI-ENT IEC 61968-1-2 profile to drive naming patterns of operations and other aspects.

## Rights / Management / Governance

### Intellectual Property Rights

This document and the information contained herein is provided on an "AS IS" basis. UCAIug DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY OWNERSHIP RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

UCAIug requests any party that believes it has a patent claim that would necessarily be infringed by implementations of this UCAIug work, to notify UCAIug immediately, so that fair and reasonable licensing terms can be negotiated. UCAIug invites any party aware of applicable undisclosed patent claims to contact the UCAIug. UCAIug may include such claims on its website, but disclaims any obligation to do so.

UCAIug takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this UCAIug recommendation, can be obtained from the UCAIug. UCAIug makes no representation that any information or list of intellectual property rights will at any time be complete, or that any claims in such list are, in fact, Essential Claims.

### CIM Object Models

Information on the management of rights and governance for IEC can be found at the page below.
http://www.iec.ch/tctools/patent-guidelines.htm

The recommendations herein build on work owned by the IEC. Required extensions identified in this recommendation will be submitted to the IEC, and will be tracked for inclusion in the model.

### Service Resource Definitions

If necessary, UCAIug is willing to work with standards development organizations to incorporate additional aspects of this recommendation into a standard, including the specification of how to use profiled (restricted) CIM objects within different environments, and possibly the information object definitions themselves.

## Referenced Specifications

- [1] OpenADR SRS 1.0 - osgug.ucaiug.org Open Smart Grid - OpenSG > SG Systems > OpenADR > Shared Documents > SRS

- [2] IEC CIM (TC 57 61968/61970) - http://tc57.iec.ch

- [3] OAuth - http://tools.ietf.org/html/draft-hammer-oauth-10

- [4] IEC TC57 WG14 61968-1-2 – Profile for use of CIM with WS-I Basic Profile

## Referenced Guidance

- [G1] 3PDA – Security Profile for Third Party Data Access (ASAP-SG)

- [G2] OpenSG OpenADR SD – REST Extensions

- [G3] OpenSG OpenADR SD – WS-I Extensions

## Namespaces

The subject of namespaces is important, because the namespace identifies the domain managing the definitions of protocol resources and formats. OpenSG proposes to use the namespace below.

http://osgug.ucaiug.org/ns/2010/06/oadr

Namespaces already defined elsewhere and used directly within reference service definitions will remain where they are, and will reference the identified body. Extensions to the schema that are backwards and forwards compatible will not change the namespace, but will include a version number inside the definition.

# Information Objects

Information Objects refer to the collection of classes that define the payload that is to be exchanged to meet each of the integration requirements identified as part of the scope for OpenADR 1.0.  The integrations requirements identified as part of 1.0 scope include:

- Asset / Resource Status – used for monitoring either an Asset or a Resource

- Demand Response Asset - including the information required to register an Asset for DR Program, update DR Asset information, or removing an Asset from a DR Program

- Demand Response Resource - this represents an aggregate of DR Assets, and supports the ability to  register a Resource for DR Program, update a resource for DR Program, and remove a Resource from a DR Program

- DR Event - Direct Load Control Signal – used for direct interactions between a DR Controlling entity and a specific DR Asset

- DR Event - Price – used in the broadcast of Demand Response message in association with source of power or generation and is mainly used for volunteer or non-mission critical messages

- DR Event – PricePlus – a message that facilitates price information that may include an “uplift” on the pricing data

- DR Event – Dispatch – this message facilitates DR events that are outcome-based in terms of reducing system load

For each Information Object the payload elements will be defined, with schema definitions provided.  It is the intent that this common document will define these common payloads that can then be implemented using a variety of technologies, most typically web services and/or REST implementation profiles that will be defined in separate deliverables.

## Security

Because these services define information objects that could be used to cause damage, access must be restricted to only those data objects that have been authorized. The security guidance specified in [G1] 3PDA is addressed through the use of [4] Open Authorization, which is proposed as the method for requesting and acquiring these authorizations.

Implementers can support other mechanisms, as long as the result of the process is a shared key associated with user-specific resources.

## Message document format

“Message document” refers to the type of XML returned by service / resource requests.  The XML payloads used to support the OpenADR message exchange will be primarily based on CIM following the recommendation based on IEC 61968-1-2, with other inputs e.g. SEP 2.0, PAP09, PAP10, used to extend the CIM model.  The information objects correspond to the message document with the following information objects currently in the OpenADR 1.0 SRS scope.

# Versioning

As additional capabilities are added to the interface definition, the minor version number of the definition will be incremented. If compatibility with existing counterparts must be broken, the namespace and the major version number will be updated, as per [9] IEC 61968-1-2.

<xs:schema targetNamespace="http://osgug.ucaiug.org/ns/2010/06/oadr" xmlns:m="http://osgug.ucaiug.org/ns/2010/07/oadr" xmlns:xs="http://www.w3.org/2001/XMLSchema" elementFormDefault="qualified" version="1.0">

# Extensibility

To enable backwards and forwards compatibility, schema validation should be turned off in operational systems to allow new schema elements to pass without update or rebuild. These unrecognized elements shall be ignored.   Also, additional platform-specific handling features should be implemented to support compatibility.

# Functional Areas

## Common

The flows in this section represent general-purpose functions that are needed for all protected resource publications. Note that operations to support 3rd Party registration, certificate transfer, and test of configuration were decided to be premature for this initial version, since those steps will require manual processes anyway, and volume will be low. They may be specified in a future release.

Definitions of the methods to be used to transfer payload data are specified in REST and WS-I documents.

## Information Object Details

The resources described below are necessary to support authorization. Implementations shall conform to referenced specifications for details on these interfaces. Clarifications and refinements made to support these service resources are denoted where necessary.

### Demand Response Asset

This information object contains the data specific to a Demand Response asset.

A Demand Response Asset is defined as an end device that is capable of shedding load in response to Demand Response Events, Electricity Price Signals or other system events (e.g. under frequency detection). The data provided for a Demand Response Asset is for the purposes of Program Enrollment and to provide information on the Assets availability and capabilities to participate in Demand Response Events.

| Data Element | Comments | CIM/Extension Mapping |
| --- | --- | --- |
| DR Asset Identifier | The unique identifier and name of the DR Assets. | CIM : 61968.Metering.EndDeviceAsset.mRID |
| DR Asset Enrollment (Registration) Transaction Type | This indicates the type of report being issued by the Asset or Resource Owner. This is an enumerated value containing one of the following: • REGISTRATION (to register a new asset/resource) • CHANGE (refers to permanent changes) • RETIREMENT. | IRC : Enrollment.programEnrollmentStatus |
| DR Asset group ID | Grouping of Assets that can respond to the same DR Signal within a DR Resource. (See DR Resource Specification) bcb:grouping within a Resource EndDeviceGroup (added association to DRAsset) | CIM : 61968.Metering.EndDeviceAsset -> CIM : 61968.Metering.EndDeviceGroup |
| Asset Operator | The business entity that operates the DR assets bcb: added association OperatingParticipant-Asset | CIM:61970.Core.OperatingParticipant Association CIM : 61970.Core.OperatingParticipant -> CIM : 61968.Metering.EndDeviceAsset |
| Asset Owner | The business entity that owns the DR assets bcb: Added PersonPropertyRole and OrgPropertyRole and associated with OperatingParticipant | CIM:61968.InfLocations.PersonPropertyRole, CIM:61968.InfLocations.OrgPropertyRole |
| Asset Location Type | A value used to interpret the value contained in the Location element. Examples of Location-type include: Address Zone GPS Coordinates Grid Location / USNG Electrical Node Zip-code | CIM : 61968.Common.ServiceLocation |
| Asset Physical Location | The location of where the DR assets reside | Association EndDeviceAsset -> ServiceLocation (ServiceLocation inherits from Location) |
| Date of Registration and Last Update | Date of which the DR Assets registered for DR purpose. | Added enrollmentChangeDate to IRC : Enrollment class |
| State of Registration Process | The state/status of the registration process of the DR assets. | IRC : Enrollment.programEnrollmentStatus |
| DR Asset Availability | Run Status, Override status | IRC : Offer.commitStatus IRC : Offer. dispatchStatus |
| DR Asset State | Set point, etc (other state related characteristics |  |
| DR Asset Physical Capabilities | Ramp Up/Down Rate, Maximum Capacity | IRC : RampRate IRC : RampRateSegment IRC : OfferParameters Association from RampRate -> Offerparameters |
| DR Asset Product | Manufacturer, Model, Version, Date of Manufacturer | CIM : Metering.EndDeviceAsset.CorporateCode CIM : Metering.EndDeviceAsset.serialNumber CIM : Metering.EndDeviceAsset.manufacturedDate CIM : Metering.EndDeviceAsset.utcNumber |
| DR Asset Type | (DG, renewable, storage, curtailable or interruptible load) | CIM : 61968.Metering.EndDeviceAsset.category |
| DR Resources | The identifier of DR resources that the DR Assets belong to. An Asset can associate with multiple Resources, but with only one Resource for a DR Program. | IRC : Resource.mRID Association IRC : Resource -> CIM : 61968.Metering.EndDeviceAsset |

Figure 1 : UML diagram showing the attributes, classes, and relationship required to support the Demand Response Asset message payload

### Demand Response Resource

A Resource is an aggregation of one or more Demand Response Assets. A DR Resource as a logical entity is a group of Assets that represents a single dispatchable entity. The data provided for a Demand Response Resource is for the purposes of Program Enrollment and to provide information on the Resource’s availability and capabilities to participate in Demand Response Events.

| Data Element | Comments | CIM/Extension Mapping |
| --- | --- | --- |
| DR Resource Identifier | This identifies the DR Resource that is being registered. | IRC : Resource.mRID Association Resource -> Resource |
| Resource Type | Type of Resource. Valid types are: load reduction, generation, combination. | IRC : Resource.resourceType |
| Available-Capacity | The total amount of power (megawatts) available from the asset/resource, expressed in integer format representing the amount of kilowatts available. | IRC : Resource.resourceType Association IRC : Enrollment -> IRC : CapacityInfo (include all attributes) |
| DR Program Identifier | This identifies the DR program in which a DR Resource is participating. | Added CIM : 61968.Metering.DemandResponseProgram |
| DR Resource Operational Constraints | These are constraints that define the amount load that can be made available during a DR event and includes the following (offer parameter section 8): · Minimum load · Maximum load. From PAP 9 Wholesale Limits: Limit Value Limit Type Physical Min Gen Min Gen MW Ramp Rate Type Ramp Rate Segment Ramp Rate Direction | IRC: RampRate IRC : RampRateSegment IRC : CapacityInfo |
| DR Resource Schedule Constraints | These are a set of constraints that specify when the DR Resource will be available. It may contain such information as: · Time of day schedule constraints · Black out dates · Maximum consecutive days of participation · Maximum duration of DR event participation (covered separately below) · Minimum duration of DR event participation (covered separately below) · Max number of times per day the DR Resource may be called · Minimum advanced notification necessary. Provide details if DR asset or DR resource is in any other DR programs (wholesale and retail) | IRC : Schedule IRC : OfferParameters IRC : Offer Association from Resource -> Offer Association from Offer -> OfferParameters Association from Schedule -> Offer |
| Effective-Start-Date-Time | The start date and time which an asset/resource is available. | IRC : Enrollment.effectiveDate |
| Program Enrollment Status | Status of the Program Enrollment for the Facility or Resource | IRC : Enrollment.programEnrollmentStatus |
| Location | An identifier to indicate the location of the asset/resource. | CIM : 61968.Common.ServiceLocation |
| Location-type | A value used to interpret the value contained in the Location element. Examples of Location-type include: · Zone · Node · Zip-code. | CIM : MarketOperations.Pnode CIM : 61968.Common.ServiceLocation : StreetAddress |
| Maximum-Duration | The maximum amount of time the asset/resource is capable of delivering power (megawatts), this may be expressed in hours using decimal notation. For example, a value of 0.5 indicates a maximum duration of 30 minutes which the asset/resource can reduce power consumption by the level indicated in Available Capacity. | IRC : OfferParameters.constraintType |
| Minimum-Duration | The minimum amount of time that an Asset/Resource Owner is willing to allow the resource/asset to be utilized during a DR event. It may be expressed in decimal format representing hours. For example, a value of 1.5 indicates that an asset/resource must be utilized for no less than one hour and 30 minutes during any DR event. | IRC : OfferParameters.constraintType |
| Response-time (Ramp Time) | The amount of time before an asset/resource is capable of meeting its full performance, in response to a request by a Service Provider to shed load, expressed as minutes in decimal format. | IRC : RampRateSegment IRC : RampRate |
| Monthly-Capacity-Availability | The average capacity available for interruption by month for the period defined by the effective start/end date, expressed in Megawatts with appropriate precision. | IRC : OfferParameters.constraintType |
| Temporary Opt-Out | This is used to temporarily opt out of DR Events and to override the normal operational constraints. The opt-out can be specified using the following criteria: · All events in a program indefinitely · Specific DR Event · All events in a specific time period. · Other triggered programs for which an asset or DR resource is already called upon (reduce double counting of available capacity) | IRC : Offer.dispatchStatus IRC : Schedule.endTime |
| Removal Effective Date/time | Date/time when the DR resource is no longer available. Date of Termination of Enrollment | IRC : Enrollment.endDate |

Figure 2 : UML model of DR Resource message payload used to support the Register, Update, and Delete DR Resource use case scenarios.  Classes prefixed with IRC indicate those which came from the IRC reference model while other classes are from the CIM.  Red lines indicate association that are not in the CIM.

### Demand Response Event – Price

This message interaction leverages much of the work accomplished by SEP 2.0, with the majority of the message using the classes and attributes of the SEP 2.0 – Pricing Data Reference Model with the addition of information needed to identify the Demand Response Event.

| Data Element | Comments | CIM/Extension Mapping |
| --- | --- | --- |
| Demand Response Event |  | IRC : DemandResponseEvent.eventID |
| Charge | SEP2.0 | CIM : 61968.PaymentMetering.Charge |
| Consumption Tariff Interval | SEP2.0 | CIM : 61968.PaymentMetering.ConsumptionTariffInterval |
| Time Tariff Interval | SEP2.0 | CIM : 61968.PaymentMetering.TimeTariffInterval |
| Tariff Profile | SEP2.0 | CIM : 61968.PaymentMetering.TariffProfile |
| Tariff | SEP2.0 | CIM : 61968.Customers.Tariff Association 61968.Customers.Tariff -> 61968.PaymentMetering.ServiceSupplier Association 61968.Customers.Tariff -> 61968.Customers.CustomerAccount |
| Pricing Structure | SEP2.0 | CIM : 61968.Customers.PricingStructure |
| Customer Account |  | CIM : 61968.Customers.CustomerAccount |
| Service Supplier | SEP2.0 | CIM : 61968.PaymentMetering.ServiceSupplier |
| Service Category | SEP2.0 | CIM : 61968.Customers.ServiceCategory |
| Currency | Identifier used to interpret the price element. MUST follow ISO 4217 standard. | CIM : 61968.PaymentMetering.AccountUnit |
| Price | Expressed in decimal notation with a precision up to 6 decimal places. Prices MAY be either positive or negative. Single or multiple valued price (e.g., for energy, demand, etc.) Including association to CustomerAgreement in attempt to tie this to CustomerAccount from the SEP2.0 profile | CIM : 61968.PaymentMetering.AccountUnit.value CIM : 61968.Metering.EndDeviceControl.priceSignal |
| Unit-of-Measure | Indicates the unit of measure for which the price pertains. MUST be complaint with the International System of Units as defined by NIST SP 330, ref: http://physics.nist.gov/Pubs/SP330/sp330.pdf Examples of NIST compliant units of measure include: kWh MWh | CIM : 61968.PaymentMetering.AccountUnit.energyUnit |
| Interval End Time | The amount of time for which this price is valid, commencing at the Effective-Date-Time specified. A value of zero means price is valid until next price broadcast override. Specified in decimal notation where integers represent minutes and decimals represent fractions of minutes. | IRC : TariffInterval.endTime |
| Effective-Date-Time | The date and time which the price is in effect. In ISO 8601 standard format. The date and time interval which the price is in effect. Since the SEP2.0 profile already uses TimeTariffInterval.startDateTime we will stick with that | CIM : 61968.PaymentMetering.TimeTariffInverval.startDateTime |
| Product Type | Identifies the type of product to which this price pertains. Contains an enumeration of various products that may be offered. Extensibility MUST be supported in order to accommodate multiple jurisdictions and markets. Product types include the following: energy, regulation, spinning reserve. IRC uses this associated with a program and an enrollment There may be some differences here between wholesale/retail that need to be resolved in this payload | CIM : 61968.Customers.ServiceCategory |

Figure 3 : UML diagram showing the attributes, classes, and relationship required to support the DR Event - Price message payload

### Demand Response Event – Price “Plus”

This type of Demand Response Event sends a pricing signal but includes the capability to support an “uplift” by the DR Controlling Entity based on a Wholesale Price. It also can apply a percentage change or multiplier to the current price.

| Data Element | Comments | CIM/Extension Mapping |
| --- | --- | --- |
| DR Program Name | An identifier of the program for which a DR event was issued. | EndDeviceControl/name &/or EndDeviceControl/DemandResponseProgram/name - wrong map, remove CIM:DemandResponseProgram.name/mRID |
| Resource ID |  | IRC : Resource Association to Resources Association to CIM : Metering.EndDeviceAsset Association IRC : DemandResponseEvent -> IRC : Resouces |
| Asset ID |  | CIM : 61968.Metering.EndDeviceAsset.mRID |
| Service Provider ID | An identifier for the Service Provider issuing the DR event. | OpenADR:ServiceProvider.mRID |
| Event ID | An identifier for the DR event that was created when the DR event was first issued. | IRC : DemandResponseEvent.eventID Added Association TRC : DemandResponseEvent -> IRC : Schedule |
| Event Status | Gives the current status of an upcoming or active event ENUM: Initiated, Cancelled, Completed | IRC : DemandResponseEvent.status |
| Event Modification Number | A modification number for the DR event. This is used to indicate if the DR Event has been modified by the Utility. Each time it is modified, this number is incremented. | OpenADR:DemandResponseEvent.eventModNumber |
| Modification reason code | The reason the event was modified. (From Notify DR Event) | EndDeviceControl - > Status.reason OpenADR:DemandResponseEvent.eventModReason |
| Modification Effective date/time | The date and time a cancellation takes effect. | EndDeviceControl - > Status.dateTime OpenADR:DemandResponseEvent.eventModDateTime |
| Simple Signal Levels | Used as an alternate and simplified representation of the DR signal, whether it be price based or a dispatch. Takes on a small number of finite levels such as NORMAL, MODERATE, and HIGH, SPECIAL Characterization of the level, e.g. is it a HIGH, NORMAL, price, is it a HIGH, NORMAL load shed | Added enumeration to the SEP 2.0 EndDeviceControl used as part of the reference model (see repository) |
| Criticality Level | This field defines the level of criticality of this event. The action taken by load control devices for an event can be solely based on this value, or combination with other Load Control Event fields supported by this device. For example, additional fields such as Average Load Adjustment Percentage, Duty Cycle, Cooling Temperature Offset, Heating Temperature Offset, Cooling Temperature Set Point or Heating Temperature Set Point can be used in combination with the Criticality level. Level Description Participation 0 Reserved 1 Green Voluntary 2 1 Voluntary 3 2 Voluntary 4 3 Voluntary 5 4 Voluntary 6 5 Voluntary 7 Emergency Mandatory 8 Planned Outage Mandatory 9 Service Disconnect Mandatory 0x0A to 0x0F Utility Defined Utility Defined | If a DR control, EndDeviceControl/drProgramLevel (=0) for emergency If mandatory use drProgramMandatory SEP2 : EndDeviceControl.drProgramLevel SEP2 : EndDeviceControl.drProgramMandatory |
| Test Event Flag | This attribute signifies whether this is a test event or not. Test events may be issued by the Utility/ISO like other DR Events. | OpenADR:DemandResponseEvent.testEvent |
| Location Identifier | An identifier used to indicate an area which this price is in effect. A value of "null" indicates that the price is in effect for all areas. | Location tls: CIM:Location.corporateCode or CIM:ResourceGroup.mRID |
| Location-type | A value used to interpret the value contained in the Location. Examples of Location-type include: Postal Address Zone GPS Coordinates Grid Location / USNG Electrical Node Zip-code Weather Station Zone ID Zone (from CIM) Electrical Node ID Electrical Node Name Electrical Node Type PNode PNode ID, Competitive Choice Area Or Resource Identifier Or Asset Identifier | StreetAddress Zone PositionPoint CircuitSection Pnode PostalAddress.postalCode |
| Baseline Dates | Dates of days used to calculate the Energy Baseline. (From Notify DR Event) | IRC : Baseline.AbsoluteDateTime Association IRC : DemandResponseEvent |
| Baseline Exclusion Dates | Dates of days Excluded from the calculation of the Energy Baseline (From Notify DR Event) | IRC : BaselineExclusionDate.AbsoluteDateTime Association IRC : DemandResponseEvent |
| Energy Baseline Value | Calculated Energy Baseline (From Notify DR Event) | IRC : DemandResponseEvent.energyBaselineValue |
| Energy Baseline Timestamp | Timestamp of Energy Baseline (From Notify DR Event) | IRC : DemandResponseEvent.energyBaselineTimestamp |
| DR Dispatch Type | Identifies the type of the DR Price Plus Dispatch. PRICE_ABSOLUTE - Price number PRICE_RELATIVE - Change in price PRICE_MULTIPLE - Multiple of current price | OfferSegment.Product Price Factor |
| Currency | Identifier used to interpret the price element. MUST follow ISO 4217 standard. | OfferSegment.price.AccountingUnit.monetaryUnit |
| Price | Expressed in decimal notation with a precision up to 6 decimal places. Prices MAY be either positive or negative. Single or multiple valued price (e.g., for energy, demand, etc.) | IRC : TimeInterval.Price |
| Unit-of-Measure | Indicates the unit of measure for which the price pertains. MUST be complaint with the International System of Units as defined by NIST SP 330, ref: http://physics.nist.gov/Pubs/SP330/sp330.pdf Examples of NIST compliant units of measure include: kWh MWh | OfferSegmnetPrice.AccountingUnit.energyUnit |
| Value | Value of Price Relative or Price Multiple | IRC:TimeInterval.value |
| Interval Start Time | Start time of the dispatch interval. | IRC : TimeInterval.startTime Association IRC : Schedule |
| Interval End Time | Period of time the Control Command is in effect |  |
| End Date Time |  | IRC::Schedule.endtime |
| Product Type | Identifies the type of product to which this price pertains. Contains an enumeration of various products that may be offered. Extensibility MUST be supported in order to accommodate multiple jurisdictions and markets. Product types include the following: energy, regulation, spinning reserve. | CIM:MarketProduct.name and mRID |

Figure 4 : UML diagram showing the classes, relationships, and attributes required to support a DR Event - Price "Plus" message payload

### Demand Response Event – Direct Load Control

Direct Load Control is a Dispatch type that requests an Asset to be in a specific load control state (e.g., to turn it on or off or apply a SetPoint).

| Data Element | Comments | CIM/Extension Mapping |
| --- | --- | --- |
| DR Program Name | An identifier of the program for which a DR event was issued. | IRC : Program.programID IRC : Program.programName For utilities CIM : 61968.Metering.DemandResponseProgram.mRID CIM : 61968.Metering.DemandResponseProgram.name (DemandResponseProgram inherits from IRC : Program) |
| Resource | An event will be sent from a DR Controlling Entity to a Resource, so a Resource will need to be identified. | IRC : Resource Association IRC : Resource -> IRC : Resources Association IRC : Resource -> CIM:MarketOperations.Pnode Association IRC : Resource -> EndDeviceAsset Association IRC : Resource -> EndDeviceGroup Association IRC : Resource -> Zone |
| Service Provider ID | An identifier for the Service Provider issuing the DR event. | IRC : SP… |
| Event ID | An identifier for the DR event that was created when the DR event was first issued. | IRC : DemandResponseEvent.eventID OR IRC : DemandResponseEvent.mRID |
| Event Status | Gives the current status of an upcoming or active event ENUM: Initiated, Cancelled, Completed | IRC : DemandResponseEvent.status |
| Event Modification Number | A modification number for the DR event. This is used to indicate if the DR Event has been modified by the Utility. Each time it is modified, this number is incremented. | IRC : DemandResponseEvent.eventModNumber |
| Modification Effective date/time | The date and time a cancellation takes effect. | IRC : DemandResponseEvent.eventModDateTime |
| Modification reason code | The reason the event was modified. (From Notify DR Event) | IRC : DemandResponseEvent.cancellationReasonCode |
| Simple Signal Levels | Used as an alternate and simplified representation of the DR signal, whether it be price based or a dispatch. Takes on a small number of finite levels such as NORMAL, MODERATE, and HIGH, SPECIAL Characterization of the level, e.g. is it a HIGH, NORMAL, price, is it a HIGH, NORMAL load shed | SEP2 : EndDeviceControl.simpleSignalLevel (Added this attribute to the SEP 2 version of the EndDeviceControl class, see repository) |
| Criticality Level | This field defines the level of criticality of this event. The action taken by load control devices for an event can be solely based on this value, or combination with other Load Control Event fields supported by this device. For example, additional fields such as Average Load Adjustment Percentage, Duty Cycle, Cooling Temperature Offset, Heating Temperature Offset, Cooling Temperature Set Point or Heating Temperature Set Point can be used in combination with the Criticality level. Level Description Participation 0 Reserved 1 Green Voluntary 2 1 Voluntary 3 2 Voluntary 4 3 Voluntary 5 4 Voluntary 6 5 Voluntary 7 Emergency Mandatory 8 Planned Outage Mandatory 9 Service Disconnect Mandatory 0x0A to 0x0F Utility Defined Utility Defined | SEP: EndDeviceControl.drProgramLevel |
| Test Event Flag | This attribute signifies whether this is a test event or not. Test events may be issued by the Utility/ISO like other DR Events. | IRC : DemandResponseEvent.deploymentType |
| Location Identifier | An identifier used to indicate an area which this price is in effect. A value of "null" indicates that the price is in effect for all areas. | CIM : MarketOperations.ResourceGroup.mRID Association IRC : Resource |
| Location-type | A value used to interpret the value contained in the Location. Examples of Location-type include: Postal Address Zone GPS Coordinates Grid Location / USNG Electrical Node Zip-code Weather Station Zone ID Zone (from CIM) Electrical Node ID Electrical Node Name Electrical Node Type PNode PNode ID, Competitive Choice Area Or Resource Identifier Or Asset Identifier | CIM : 61968.Common.Location.Category CIM : MarketOperations.ResourceGroup.type (type is the new attribute) CIM : 61968.Common.Location.mainAddress : StreetAddress CIM : 61968.Informative.InfLocations.Zone CIM : 61968.Informative.InfGMLSupport.GMLPosition CIM : Informative.InfOperations.CircuitSection CIM : MarketOperations.PNode |
| Baseline Dates | Dates of days used to calculate the Energy Baseline. (From Notify DR Event) | IRC : Baseline.AbsoluteDateTime Association to IRC : DemandResponseEvent |
| Baseline Exclusion Dates | Dates of days Excluded from the calculation of the Energy Baseline (From Notify DR Event) | IRC : BaselineExclusionDate.AbsoluteDateTime Association to IRC : DemandResponseEvent |
| Energy Baseline Value | Calculated Energy Baseline (From Notify DR Event) | IRC : DemandResponseEvent.energyBaselineValue |
| Energy Baseline Timestamp | Timestamp of Energy Baseline (From Notify DR Event) | IRC : DemandResponseEvent.energyBaselineTimestamp |
| Direct Load Control Type | The type of DR Direct Load Control Command: e.g. Set Point, Open/Close, Heating Temperature -offset/setpoint Cooling Temperature -offset/setpoint Load adjustment offset | CIM : 61968.Metering.EndDeviceControl.type |
| Direct Load Control Value | Value associated with the Direct Load Control Type. | CIM : 61970.Meas.SetPoint SEP2 : DRLC.Offset.value Association from Offet -> EndDeviceControl |
| Interval Start Time | Start time of the dispatch interval. | SEP2 : DRLC.DateTimeInterval.start |
| Interval End Time | Period of time the Control Command is in effect. This was originally "duration" but has been changed to use SEP2 interval.end | SEP2 : DRLC.DateTimeInterval.end |
| Duty cycle | “Duty Cycle (optional): Defines the maximum On state duty cycle as a percentage of time. Example, if the value is 80, the device would be in an “on state” for 80% of the time for the duration of the event. Range of the value is 0 to 100. A value of 0xFF indicates the field is not used.” | SEP2 : DRLC.DutyCycle.name SEP2 : DRLC.DutyCycle.normalValue SEP2 : DRLC.DutyCycle.state Association from DutyCycle -> EndDeviceControl |
| Event control | Event Control options for randomized start or end times: 1= Randomize Start time, 0=Randomized Start not Applied 1= Randomize End time, 0=Randomized End not Applied. 5 | SEP2 : DRLC.Randomization Association from Randomization -> EndDeviceControl |

Figure 5 : UML diagram showing the attributes, classes, and relationships required to support the DR Event - Direct Load Control message payload

### DR Event – Objectives

DR Event Objectives refers to the Dispatch profile for a DR Event that sets Demand Response Objectives for a Resource. The objectives can be expressed as a Load Level, Load Amount, or Load Percentage.

| Data Element | Comments | CIM/Extension Mapping |
| --- | --- | --- |
| DR Program Name | An identifier of the program for which a DR event was issued. | IRC : Program.programID IRC : Program.programName For utilities CIM : 61968.Metering.DemandResponseProgram.mRID CIM : 61968.Metering.DemandResponseProgram.name (DemandResponseProgram inherits from IRC : Program) |
| Resource | An event will be sent from a DR Controlling Entity to a Resource, so a Resource will need to be identified. | IRC : Resource Association IRC : Resource -> IRC : Resources Association IRC : Resource -> CIM:MarketOperations.Pnode Association IRC : Resource -> EndDeviceAsset Association IRC : Resource -> EndDeviceGroup Association IRC : Resource -> Zone |
| Service Provider ID | An identifier for the Service Provider issuing the DR event. | IRC : SP… |
| Event ID | An identifier for the DR event that was created when the DR event was first issued. | IRC : DemandResponseEvent.eventID OR IRC : DemandResponseEvent.mRID |
| Event Status | Gives the current status of an upcoming or active event ENUM: Initiated, Cancelled, Completed | IRC : DemandResponseEvent.status |
| Event Modification Number | A modification number for the DR event. This is used to indicate if the DR Event has been modified by the Utility. Each time it is modified, this number is incremented. | IRC : DemandResponseEvent.eventModNumber |
| Modification reason code | The reason the event was modified. (From Notify DR Event) | IRC : DemandResponseEvent.eventModReason (cancellationReasonCode?) |
| Modification Effective date/time | The date and time a cancellation takes effect. | IRC : DemandResponseEvent.eventModDateTime |
| Simple Signal Levels | Used as an alternate and simplified representation of the DR signal, whether it be price based or a dispatch. Takes on a small number of finite levels such as NORMAL, MODERATE, and HIGH, SPECIAL | SEP2 : EndDeviceControl.simpleSignalLevel |
| Criticality Level | This field defines the level of criticality of this event. The action taken by load control devices for an event can be solely based on this value, or combination with other Load Control Event fields supported by this device. For example, additional fields such as Average Load Adjustment Percentage, Duty Cycle, Cooling Temperature Offset, Heating Temperature Offset, Cooling Temperature Set Point or Heating Temperature Set Point can be used in combination with the Criticality level. Criticality Level Level Description Participation 0 Reserved 1 Green Voluntary 2 1 Voluntary 3 2 Voluntary 4 3 Voluntary 5 4 Voluntary 6 5 Voluntary 7 Emergency Mandatory 8 Planned Outage Mandatory 9 Service Disconnect Mandatory 0x0A to 0x0F Utility Defined Utility Defined | If a DR control, EndDeviceControl/drProgramLevel (=0) for emergency If mandatory use drProgramMandatory SEP2 : EndDeviceControl.drProgramLevel SEP2 : EndDeviceControl.drProgramMandatory |
| Test Event Flag | This attribute signifies whether this is a test event or not. Test events may be issued by the Utility/ISO like other DR Events. | IRC : DemandResponseEvent.deploymentType |
| Location Identifier | An identifier used to indicate an area which this price is in effect. A value of "null" indicates that the price is in effect for all areas. | CIM : MarketOperations.ResourceGroup.mRID Association to IRC : Resource |
| Location-type | A value used to interpret the value contained in the Location. Examples of Location-type include: Postal Address Zone GPS Coordinates Grid Location / USNG Electrical Node Zip-code Weather Station Zone ID Zone (from CIM) Electrical Node ID Electrical Node Name Electrical Node Type PNode PNode ID, Competitive Choice Area Or Resource Identifier Or Asset Identifier | CIM : 61968.Common.Location.Category CIM : MarketOperations.ResourceGroup.type (type is the new attribute) CIM : 61968.Common.Location.mainAddress : StreetAddress CIM : 61968.Informative.InfLocations.Zone CIM : 61968.Informative.InfGMLSupport.GMLPosition CIM : Informative.InfOperations.CircuitSection CIM : MarketOperations.PNode |
| Baseline Dates | Dates of days used to calculate the Energy Baseline. (From Notify DR Event) | IRC : Baseline.AbsoluteDateTime Association IRC : DemandResponseEvent |
| Baseline Exclusion Dates | Dates of days Excluded from the calculation of the Energy Baseline (From Notify DR Event) | IRC : BaselineExclusionDate.AbsoluteDateTime Association IRC : DemandResponseEvent |
| Energy Baseline Value | Calculated Energy Baseline (From Notify DR Event) | IRC : DemandResponseEvent.energyBaselineValue |
| Energy Baseline Timestamp | Timestamp of Energy Baseline (From Notify DR Event) | IRC : DemandResponseEvent.energyBaselineTimestamp |
| DR Dispatch Type | Identifies the type of DR Objectives: • LOAD_LEVEL • LOAD_AMOUNT • LOAD_PERCENTAGE This indicates if the objective applies to: Load Level Value, Load Amount Value, or Load Percent Value. |  |
| Interval Start Time | Start time of the dispatch interval. | IRC : TimeInterval.startTime Association IRC : Schedule |
| Interval Duration | Period of time the Control Command is in effect. | IRC : TimeInterval.endTime |
| Load Level Value | Value of the load level to be achieved based on a set of enumerated values. | IRC:Schedule.LoadLevelValue or IRC:Schedule.DeploymentLevel |
| Load Amount Value | Fixed amount of load to shed in kW. | IRC:DemandResponseEvent.DeploymentMW |
| Load Percent Value | Percentage of load to shed. | IRC:DemandResponseEvent.DeploymentMW or new IRC:Schedule.LoadPercentValue (Deployment %) |
| DR Asset ID | An identifier of the DR Asset for which the control is intended. | CIM : 61968.Metering.EndDeviceAsset.mRID |

Figure 6 : UML Showing the classes, relationship, and attributes required to support the DR Event - Objectives message payload

### Demand Response Event – Opt Out

This is a specific message designed to a allow a Resource or Asset to notify a DR Controlling Entity that they may not be participating in a Demand Response Event, or they may be changing how they may be participating in the Demand Response Event, for example, changing the participating capacity for some portion of a scheduled event. The Opt Out could be for a single Event or for specific dates, date ranges, or indefinite number of days.

| Data Element | Comments | CIM/Extension Mapping |
| --- | --- | --- |
| DR Program Name | An identifier of the program for which a DR event was issued. | IRC : Program.programID IRC : Program.programName For utilities CIM : 61968.Metering.DemandResponseProgram.mRID CIM : 61968.Metering.DemandResponseProgram.name (DemandResponseProgram inherits from IRC : Program) |
| Event ID | An identifier for the DR event that was created when the DR event was first issued. | IRC : DemandResponseEvent.eventID OR IRC : DemandResponseEvent.mRID |
| Resource | An event will be sent from a DR Controlling Entity to a Resource, so a Resource will need to be identified. | IRC : Resource Association IRC : Resource -> IRC : Resources Association IRC : Resource -> EndDeviceAsset |
| DR Resource Schedule Constraints | These are a set of constraints that specify when the DR Resource will be available. It may contain such information as: · Time of day schedule constraints · Black out dates · Maximum consecutive days of participation · Maximum duration of DR event participation (covered separately below) · Minimum duration of DR event participation (covered separately below) · Max number of times per day the DR Resource may be called · Minimum advanced notification necessary. Provide details if DR asset or DR resource is in any other DR programs (wholesale and retail) | IRC : Schedule IRC : OfferParameters IRC : Offer Association from Resource -> Offer Association from Offer -> OfferParameters Association from Schedule -> Offer |
| DR Asset Identifier | The unique identifier and name of the DR Assets. | CIM : 61968.Metering.EndDeviceAsset.mRID |
| Contraint Type | Type of operational, schedule or offer constraint | IRC : Constraint.constraintType |
| Constraint Value | Value of the Constraint Type and Interval | IRC : Constraint.constraintValue |
| Constraint Interval | The timeframe over which the constraint type applies. | IRC : constraintInterval |
| DR Asset Availability | Run Status, Override status | IRC : Offer.commitStatus IRC : Offer. dispatchStatus |

Figure 7 : UML showing the classes, relationships, and attributes required to support a DR Event Opt Out message payload

### Asset Resource Status

Used for monitoring the state of a Demand Response Asset or Demand Response Resource as it applies to responding to DR Event requests.

| Data Element | Comments | CIM/Extension Mapping |
| --- | --- | --- |
| DR Resource ID | The identifier of the DR Resource. | IRC : Resource.mRID |
| DR Asset ID | The identifier of the DR Asset | CIM : 61968.Metering.EndDeviceAsset.mRID |
| Exception Conditions | This is used to report that the load controller may not behave as commanded because of a variety of conditions including: Faults in device, Customer override. | CIM : 61968.Common.Status.reason |
| Load Control State | The state of the load, which includes both commanded states and user settings. This may include a schedule of future states if a particular control algorithm for the load controller is being executed. Duplication of the above (exception conditions) row in terms of repository configuration | CIM : 61968.Metering.EndDeviceAsset CIM : 61968.Common.Status.reason |
| Operational Constraints | Constraints on how the load may be controlled. This may include limits on the state of the load controller as well as schedules upon those constraints. See attributes below, (type, value, interval) | Added Association from IRC:Offer -> IRC:Constraint |
| Contraint Type | Type of operational, schedule or offer constraint | IRC : Constraint.constraintType |
| Constraint Value | Value of the Constraint Type and Interval | IRC : Constraint.constraintValue |
| Constraint Interval | The timeframe over which the constraint type applies. | IRC : Constraint.constraintInterval |

Figure 8 : UML diagram illustrating the contents and relationships within the AssetResourceStatus message payload

# Appendix A

## Demand Response XSDs

The file embedded below contains the XML Schema Definition (XSD) described in this document, and the example.