OpenADR 1.0 Service Definition - Web Services implementation profile

Version: Draft v0.91

Release Date: 11/3/2010

Acknowledgements

The following individuals and their companies have contributed and/or provided support to the work of the OpenADR 1.0 Service Definition - Web Services Extension:

- Ed Koch from Akuacom

- Albert Chiu from Pacific Gas & Electric

- Gerald Gray from CIMple Integrations

- Mark Ortiz from Consumers Energy

- Shawn Hu from Xtensible Solutions

- Steve Van Ausdall from Xtensible Solutions

- Bruce Bartell from Xtensible Solutions

The OpenADR Task Force wishes to thank all of the contributors to OpenADR, especially the above-mentioned individuals and their companies for their support of this important endeavor as it facilitates the creation of a foundational element of an interoperable Smart Grid.

Document History

Revision History

Date of this revision: Apr. 15, 2010

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 0.1 | 07/23/2010 | Gerald R. Gray | Initial draft discussion version. | N |
| 0.2 | 08/10/2010 | Gerald R. Gray | Removed 4.8.1 – 4.8.3 from v1.0 scope | N |
| 0.3 | 08/13/2010 | Gerald R. Gray | Updated information objects to more closely align with SRS, (use case scenarios 4.6, 4.7.1, 4.7.2 | N |
| 0.4 | 08/23/2010 | Gerald R. Gray | Updated based on feedback from Service Definition team meeting, 8/19/2010; removing NAESB use case scenario numbering, consolidation of logical actors, removing ANSI C12.19 reference | Y |
| 0.5 | 09/02/2010 | Gerald R. Gray | Resolved DR Message issue and updated sequence diagrams to reflect information object changes, (DR Event Dispatch, DR Event Pricing, DR Event Direct Load Control) | Y |
| 0.6 | 09/13/2010 | Gerald R. Gray | Corrected some message names, updated example wsdls/xsd artifacts, and added an image showing the common reply.xsd structure | Y |
| 0.61 | 9/20/2010 | Gerald R. Gray | Changed DR Event-Pricing to reflect that this particular pricing message does not come from the system operator | Y |
| 0.7 | 9/27/2010 | Gerald R. Gray | Changed DR Event Pricing to reflect that it is “Price Plus” and added the DR Event – Pricing to reflect the “SEP 2-like” message. Added OptOpt service | Y |
| 0.9 | 10/22/2010 | Gerald R. Gray | Inserted completed artifacts zip file and updated release pending final review and approval | Y |
| 0.91 | 10/03/2010 | Gerald R. Gray | Updated based on OpenADR session feedback | Y |

Open Issues Log

Last updated: Apr. 8, 2010

| Issue | Issue Date | Provided By | Summary of the Issue |
| --- | --- | --- | --- |
| 1 | 08/13/2010 | GRGray | What is the content of the DRMessage Information Object for Use Case Scenario 4.4? Resolution: This was the PricePlus use case scenario. DRMessage has been replaced with DREventPricing as the information object. |
| 2 | 08/13/2010 | GRGray | Use case scenario 4.7.1 and 4.7.2 assume that the asset or resource periodically sends updated status. Is there a need for the DR Controlling Entity to ping the Asset or Resource? Resolution: This can be accommodated by creating a ReceiveAssetResourceStatus service with a GetAssetResource Status operation |

Contents

1	Introduction	7

1.1	Rights / Management / Governance	7

1.1.1	Intellectual Property Rights	7

1.1.2	CIM Object Models	7

1.1.3	Web Service Definitions	8

1.2	Referenced Specifications	8

1.3	Referenced Guidance	8

1.4	Namespaces	8

1.5	SCOPE	8

2	Web Services	9

1.1	Service Structure	9

1.2	Service Naming Convention	10

3	Service Discovery	11

4	Versioning	11

5	Demand Response Services Inventory	11

6	Functional Areas	13

6.1	DEMAND RESPONSE SERVICES	13

6.1.1	Register DR Resource	13

6.1.2	Update DR Resource	13

6.1.3	Remove DR Resource	14

6.1.4	Register DR Asset	14

6.1.5	Update DR Asset	15

6.1.6	Remove DR Asset	15

6.1.7	DR Event - PricePlus	16

6.1.8	DR Event – Price	17

6.1.9	DR Event - Objectives	18

6.1.10	DR Event - Direct Load Control	18

6.1.11	Monitor DR Event (DR Resource)	19

6.1.12	Monitor DR Event (DR Asset)	19

6.1.13	DR Event Opt Out	20

7	Appendix	20

7.1.1	OPENADR WSDLS	20

7.1.2	Reply.xsd Structure	22

List of Figures

Figure 1:  Example sequence diagram illustrating the convention used in this document, with both the service and operations shown on any given integration	11

Figure 2: Register DR Resource Sequence Diagram	13

Figure 3: Update DR Resource Sequence Diagram	14

Figure 5: Create a DR Asset Sequence Diagram	15

Figure 7: Remove DR Asset Sequence Diagram	16

Figure 13 : Sequence diagram illustrating the DREvent-Pricing interation with the assumption that the message payload is passed from the DR Resource to the DR Asset.	17

Figure 15: Monitor DR Event (DR Resource) Sequence Diagram	19

Figure 16: Monitor DR Event (DR Asset) Sequence Diagram	20

Figure 14 : DR Event Opt Out sequence diagram showing the interaction between a DR Asset and DR Resource with a DR Controlling Entity reflecting the ability to opt out of any given DR Event.	20

Figure 17 : Reply.xsd structure	23

List of Tables

Table 1:  Scope of OpenADR Services	8

Table 2:  Service Inventory List	10

# Introduction

This document contains the extensions to the OpenADR Common specification to build a WS-I Basic Profile 1.1 implementation of the OpenADR Requirements Specification.   The “OpenSG OpenADR SD – Common” document should be thought of as the parent of this document, filling in sections not addressed in the Common specification.

These extensions define a collection of services as a discoverable data service, using SOAP over HTTPS to send and receive requests and information in XML.  This architecture provides secure access to scalable methods and data resources hosted by the provider, while maintaining concurrency and integrity. All data is secured at the user level, so that access to individual user data can be provided or revoked to external services, and other users’ data will still be protected.

## Rights / Management / Governance

### Intellectual Property Rights

This document and the information contained herein is provided on an "AS IS" basis. UCAIug DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY OWNERSHIP RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

UCAIug requests any party that believes it has a patent claim that would necessarily be infringed by implementations of this UCAIug work, to notify UCAIug immediately, so that fair and reasonable licensing terms can be negotiated. UCAIug invites any party aware of applicable undisclosed patent claims to contact the UCAIug. UCAIug may include such claims on its website, but disclaims any obligation to do so.

UCAIug takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this UCAIug recommendation, can be obtained from the UCAIug. UCAIug makes no representation that any information or list of intellectual property rights will at any time be complete, or that any claims in such list are, in fact, Essential Claims.

### CIM Object Models

The recommendations herein build on work owned by the IEC. Required extensions identified in this recommendation will be submitted to the IEC, and will be tracked for inclusion in the model.

Information on the management of rights and governance can be found at the page below.
http://www.iec.ch/tctools/patent-guidelines.htm

### Web Service Definitions

If necessary, UCAIug is willing to work with standards development organizations to incorporate additional aspects of this recommendation into standards, including the specification of how to use profiled (restricted) CIM objects within the SOAP over HTTP environment, and possibly the web service definitions themselves.

## Referenced Specifications

- [1] IEC CIM (TC 57 61968/61970) - http://tc57.iec.ch

- [2] WS Basic Profile Version 1.0 http://www.ws-i.org/Profiles/BasicProfile-1.0-2004-04-16.html

- [3] OpenSG OpenADR SD – Common

- [4] UDDI: www.uddi.org

- [5] SOAP: http://www.w3.org/TR/SOAP/

- [6] IEC TC57 WG14 61968-1-2 – Profile for use of CIM with WS-I Basic Profile

## Referenced Guidance

- [G1] OpenADR SRS 1.0

- [G2] 3PDA – Security Profile for Third Party Data Access (ASAP-SG)

- [G3] Service Definitions Technical Guide

## Namespaces

The subject of namespaces is important, because the namespace identifies the domain managing the definitions of protocol resources and formats. OpenSG proposes to use a temporary namespace until the final destination is identified. In any case, namespaces already defined elsewhere and used directly within reference service definitions will remain where they are, and will reference the identified body.

The proposed temporary namespace for definitions to be used in early implementations is below. (Service definition will be updated with the final approved namespaces.)

http://osgug.ucaiug.org/ns/2010/06/wsoadr

## SCOPE

The use cases with their associated priority are defined in the OpenADR SRS, copied here for convenience:

Table 1:  Scope of OpenADR Services

| Use Case Scenario | Service Name | Functional Description of the Service | Priority |
| --- | --- | --- | --- |
| Administrate Customer for DR | DR Customer Agreement | Customer is Registered for, Updated or Removed from a DR Program. | 3 |
| Administrate DR Resource | DR Resource / DRAS Client | DR Resource is registered and associated with a DR Program and Customer. The Resource is updated and/or removed from DR Program. | 2 |
| Administrate DR Asset | DR Asset | DR Asset is registered and associated with a DR Resource. The Resource is updated and/or removed from DR Program. | 2 |
| Execute DR Event | Notify DR Event | DR Event information is sent to participants prior to the DR Event start based on defined intervals and is Updated, and/or Canceled. | 1 |
| Execute DR Event | DR Event | DR Event is a polymorphic message type that supports Direct Load Control, DR Instructions (Objectives), Price Schedule | 1 |
| Execute DR Event – Operational Coordination | Forecast Demand | Multiple levels of aggregated DR Demand and Telemetry data is provided for the purpose of coordinating a DR Event and to provide checks against circuit limits. | 6 |
| Execute DR - Event Monitoring / Confirmation | Asset / Resource Status (State) | The DR Resource or Asset (in the event of DLC) provides status for opt in / out or other state that impacts Demand Response. The Status message may be as a confirmation reply to a DR Signal or as an update resulting from a state/status change or in response to a Get message. | 1 |
| Post DR Event – M&V / Settlement | Meter Read & Billing | The process and messages used for settlement of a DR event are the same as defined in the Utility AMI AMI-ENT System Requirements Specification, Utility AMI-ENT Task Force. The meter read interval is determined by the interval of DR Event participation. | 4 |
| DR Bidding |  |  | 5 |

It is noted that for some use cases, such as 1.0 Administrate DR Program and 2.0 Administrate Customer, that with so many differences between regions that “it is unlikely that these will be automated”.  Assuming that once the differences in the business processes and data exchanges have been resolved these use case scenarios may be revisited.  Therefore the scope of the OpenADR 1.0 web services will be on those use cases and scenarios ranked with a priority of 1 or 2 in the table above.

# Web Services

The purpose of the section is to provide a set of recommendations for a Web Service definition based on OpenSG’s Service Definition design patterns and Web Services Description Language (WSDL) from W3C.  The audiences of the document are assumed to have basic knowledge of Web service and XML schema.

## Service Structure

W3C WSDL (v1.1) is followed to define OpenADR Web services. The services are made of two parts with following tags.

- definitions

- types

- message

- portType

- operation

- binding

- port

- service

The web service design practices are summarized below:

- Standard SOAP envelope is used to avoid extra message enveloping.

- XSD as data type is imported instead of being embedded for better version control

- Wrapped document WSDL style is used

- Operation name follows the Verb + Noun naming convention which can potentially avoid contend-based routing

## Service Naming Convention

Interfaces are defined using a specific set of verbs and nouns using Web service technology. Each service then has a subset of operations that are associated with information objects. Each operation is named following IEC 61968-1 verb + noun (information objects). The detail service and operation naming convention is covered in OpenSG Service Definition Technical Guide [G4].  In summary, the naming conventions are:

- Service name:

To follow <Service pattern name>+<Information Object> such as ReceiveDREvent

- Operation name:

To follow <Operation pattern name>+<Information Object> such as CreatedDREvent

Note: In the sequence diagrams an operation will be included in a service name as an argument e.g. CreatedDREvent(Cancel)

Figure 1:  Example sequence diagram illustrating the convention used in this document, with both the service and operations shown on any given integration

# Service Discovery

Universal Description, Discovery, and Integration (UDDI) is a specification designed to allow businesses to enter details about themselves and the services they provide in a registry. Searches can be typically be performed by company name, specific service, or types of service. This allows companies providing or needing web services to discover each other, define how they interact over the Internet, and share information in a standardized fashion.

Since a WSDL defines the XML grammar for describing services as collections of communication endpoints capable of exchanging messages, utilities and third parties can publish WSDLs for services they provide and links to the WSDLs are usually offered in a company’s profile in a UDDI registry.

# Versioning

As additional capabilities are added to the interface definition, the minor version number of the definition will be incremented. If compatibility with existing counterparts must be broken, the namespace and the major version number will be updated, as per [9] IEC 61968-1-2.

There are two types of updates in terms of version control:

- Major version update:

In this case major update has been made in an XSD and its backward compatibility has been broken as a result.

- Minor version update:

In this case backward compatibility is intact. One example of such minor update is a new element added but as an optional field.

A naming convention for version control is proposed here to use XSD targetNamespace, version attribute, and annotation as below:

- targetNamespace=“http://company.com/yyyy/mm /<Message Type Name>”

- version="<Major version>.<Minor version>".

Annotation added for detail description such as “Version 1.0 created in 2009/02”.

The version used in the first edition of these artifacts will thusly be:

<xs:schema targetNamespace="http://osgug.ucaiug.org/ns/2010/06/oadr" xmlns:m="http://osgug.ucaiug.org/ns/2010/07/oadr" xmlns:xs="http://www.w3.org/2001/XMLSchema" elementFormDefault="qualified" version="1.0">

# Demand Response Services Inventory

The following services have been identified as part of the OpenADR 1.0 scope detailing the service name, service consumer, and service provider.  The service naming convention in the table below includes the Verb + Information object pair, and includes the service operation in parentheses.

Table 2:  Service Inventory List

| Use Case & Scenario | Service Name : Operation Name | Service Provider | Service Consumer | Information Object |
| --- | --- | --- | --- | --- |
| Register DR Resource | ReceiveDRResource : CreatedDRResource | DR Controlling Entity | DR Asset | DR Resource |
| Update DR Resource | ReceiveDRResource : ChangedDRResource | DR Controlling Entity | DR Asset | DR Resource |
| Remove DR resource | ReceiveDRResource : DeletedDRResource | DR Controlling Entity | DR Asset | DR Resource |
| Register DR Asset | ReceiveDRAsset : CreatedDRAsset | DR Controlling Entity | DR Asset | DR Asset |
| Update DR Asset | ReceiveDRAsset : ChangedDRAsset | DR Controlling Entity | DR Asset | DR Asset |
| Remove DR Asset | ReceiveDRAsset : DeletedDRAsset | DR Controlling Entity | DR Asset | DR Asset |
| DR Resource Confirmation | ReceiveDRResource : CreatedDRResource | DR Controlling Entity | DR Resource / DRAS Client | DR Resource |
| Broadcast DR Message | ReceiveDREventPricePlus : CreatedDREventPricePlus | DR Resource | Load serving Entity | DREventPricePlus |
| Broadcast DR Message | ReceiveDREventPricePlus : CreatedDREventPricePlus | DR Resource | DR Controlling Entity | DREventPricePlus |
| Broadcast DR Message | ReceiveDREventPricePlus : CreatedDREventPricePLus | DR Controlling Entity | Load Serving Entity | DREventPricePlus |
| DR Event Pricing | ReceiveDREventPricing : CreatedDREventPricing | DR Resource | DR Controlling Entity | DREventPricing |
| DR Event Pricing | ReceiveDREventPricing : CreatedDREventPricing | DR Asset | DR Resource | DREventPricing |
| Dispatch DR Instructions | ReceiveDREventObjectives : CreatedDREventObjectives | DR Resource | DR Controlling Entity | DREventObjectives |
| Dispatch DR Instructions | SendDREventObjectives : CreatedDREventObjectives | DR Controlling Entity | DR Resource | DREventObjectives |
| Direct Load Control | ReceiveDREventDirectLoadControl : CreatedDREventDirectLoadControl | DR Asset | DR Controlling Entity | DREventDirectLoadControl |
| Monitor DR Event | SendAssetResourceStatus : CreatedAssetResourceStatus | DR Controlling Entity | DR Resource | AssetResourceStatus |
| Monitor DR Asset | SendAssetResourceStatus : CreatedAssetResourceStatus | DR Controlling Entity | DR Resource | AssetResourceStatus |
| DR Event Opt Out | SendDREventOptOut : CreatedDREventOptOut | DR Controlling Entity | DR Resource | DREventOptOut |
| DR Event Opt Out | SendDREventOptOut : CreatedDREventOptOut | DR Resource | DR Asset | DREventOptOut |

# Functional Areas

## DEMAND RESPONSE SERVICES

The flows in this section represent general-purpose functions that are needed for all protected resource publications, in addition to those specified in [4] OpenADR 1.0 SD - Common.

### Register DR Resource

A party with ownership, controlling interest or administrative responsibilities for an Asset or Resource communicates status related operational information about the Asset or Resource to a controlling entity.

For example the owner of a DR resource or asset may wish to declare their inability to shed load (an outage) due to summer shutdown or may wish to reduce the available capacity of a resource/asset due to equipment maintenance or other causes.

Figure 2: Register DR Resource Sequence Diagram

### Update DR Resource

Figure 3: Update DR Resource Sequence Diagram

### Remove DR Resource

The use case reflects the removal of a registered resource as an entity in the DR Controlling Entity’s system.  This will use the same Information object as the Register DR Resource and Update DR Resource use cases, simply with an action reflecting the removal.

Figure 4: Remove DR Resource Sequence Diagram

### Register DR Asset

The DR Asset registration process must capture the key identifiers to enable accurate tracking of DR Assets and their capabilities. A requirement for a System and Market Operator, Load Serving Entity, DR Aggregator, or other entity facilitating the registration process (hereafter called DR Controlling Entity) is to track assets. This is done through DR Asset registration and association of physical DR Assets to DR Resources, (each DR Asset will be associated with at least one DR Resource) in order to recognize the asset and its potential contribution as part of a DR Resource.  The DR Controlling Entity ultimately administers the DR Asset registration process to recognize DR Assets that can serve as part of a DR Resource, although the customer may be party to the registration process.

Figure 5: Create a DR Asset Sequence Diagram

### Update DR Asset

Once a DR Asset registration is completed, changes to elements of the registration may be required or desired. After identifying the specific required modification and verification of authorization to perform the update, each of the considerations identified in the DR Asset registration step should be followed to update the DR Asset information. The ability to update DR Asset information helps to ensure the asset information on record is up-to-date and complete.

Parties that are privy to and rely on the update should be notified of updates made and have access to review and in some cases approve/disapprove the update(s).

Figure 6: Update DR Asset Sequence Diagram

### Remove DR Asset

Removing a DR Asset must take into account any DR resource long term commitments in System and Market Operator programs, contractual obligations with DR Aggregators or Load Serving Entities.  In addition, State and or Federal regulatory agency filings and approvals must be considered prior to removing a customer enrollment from a DR program.

Figure 7: Remove DR Asset Sequence Diagram

### DR Event - PricePlus

Demand Response programs are designed to address different power system concerns caused by the imbalance between generation, transmission and consumption or environmental concerns. Some DR programs are conducted on a voluntary basis, where the customer can opt to maintain the level or load; some DR programs are mandatory, where either the customer loads will be curtailed under certain conditions or customer will incur financial penalties for noncompliance.

In retail market, certain “DR Pricing Messages” can be broadcasted to DR Resources either directly or through Service Providers.

Based on the OpenADR discussion, broadcasting function is mainly used for volunteer or non mission critical DR message, therefore, message acknowledgement or confirmation is optional.

DR Source of Power/Generation

Precondition:

The DR controlling entity sends the DR message to service providers. In the case of DR pricing, DR controlling entity calculates the wholesale price per location and communicates the appropriate price associated with the DR product to service providers.

Post Condition:

DR Resources received the DR pricing information, and may or may not act based on the DR agreement or contract.

Figure 12: Broadcast DR Event PricePlus Message Sequence Diagram

### DR Event – Price

This message interaction reflects a “SEP2”-like message payload, i.e. the message contains tariff, tariff interval, and tariff block information as well as price.  In this message interaction it is assumed that the DR Resource passes the DR Event Pricing information onto a DR Asset.

Figure 13 : Sequence diagram illustrating the DREvent-Pricing interation with the assumption that the message payload is passed from the DR Resource to the DR Asset.

### DR Event - Objectives

This interaction is used to dispatch DR Resources.  This type of interaction is used when the Controlling entity needs to achieve specific objectives from the DR Resources during DR events. This means that specific instructions will be given to the DR Resource with objectives (e.g. shed 100KW) for the load profile of the DR Resource.

Note: For the retail use cases a Dispatch is considered a special type of DR Notification and thus it is very similar in nature to the requirements given for that interaction.

Figure 13: DR Event Objectives Instructions Sequence Diagram

### DR Event - Direct Load Control

This use case covers direct interactions between the Controlling entity and a specific DR Asset for the purposes of putting that asset into a specific load control state (e.g. turn it on or off). In this case the DR Asset is a DR Resource with only one DR Asset and thus the interaction is directly with the DR Asset.

Figure 14: DR Event Direct Load Control Sequence Diagram

### Monitor DR Event (DR Resource)

This interaction is used to monitor A Resource's behavior. It may be executed as a result of the DR Resource receiving a DR signal or it may be conducted continuously.  Note that this service uses a one way MEP.

Figure 15: Monitor DR Event (DR Resource) Sequence Diagram

### Monitor DR Event (DR Asset)

This interaction is used to monitor the state of a DR Asset.  It may be executed as a result of the DR Asset receiving a DR signal or it may be conducted continuously.

Figure 16: Monitor DR Event (DR Asset) Sequence Diagram

### DR Event Opt Out

At time there may be a need for a DR Resource or a DR Asset to Opt Out of any particular DR Event.  This message interaction provides a way for the DR Asset to notify a DR Resource of an opt out, and in turn, the DR Resource may notify the DR Controlling Entity of an opt out.

Figure 14 : DR Event Opt Out sequence diagram showing the interaction between a DR Asset and DR Resource with a DR Controlling Entity reflecting the ability to opt out of any given DR Event.

# Appendix

### OPENADR Artifacts (WSDLs/XSDs)

Example WSDLs/XSDs for each of the service defined in this document.

The artifacts representing any given integration are made up of three parts, the WSDL itself, a message header.xsd for the associated WSDL and a Reply.xsd (for those integrations using a two-way message exchange pattern).

By way of example, examining the services to support the 1.0 scope will be made up of the following artifacts:

- ReceiveDRAsset.wsdl

  - DRAsset.xsd

  - MessageHeader.xsd

  - Reply.xsd

- ReceiveDRResource.wsdl

  - DRResource.xsd

  - MessageHeader.xsd

  - Reply.xsd

- SendAssetResourceStatus.wsdl

  - AssetResourceStatus.xsd

  - MessageHeader.xsd

- ReceiveDREventPricePlus.wsdl

  - DREventPricePlus.xsd

  - MessageHeader.xsd

- ReceiveDREventPrice.wsdl

  - DREventPrice.xsd

  - MessageHeader.xsd

  - Reply.xsd

- ReceiveDREventDirectLoadControl.wsdl

  - DREventDirectLoadControl.xsd

  - MessageHeader.xsd

  - Reply.xsd

- ReceiveDREventObjectives.wsdl

  - DREventObjectives.xsd

  - MessageHeader.xsd

  - Reply.xsd

- SendDREventOptOut

  - DREventOptOut.xsd

  - Message.xsd

  - Reply.xsd

### Reply.xsd Structure

The following is a visual representation of the xsd structure for the common reply that is used in all two-way message exchange patterns.

Figure 17 : Reply.xsd structure

# Text boxes

Concrete part

Abstract part