AMI-ENT Step-by-Step Modeling and Artifacts Generation Guidelines Document AMI-ENT Service Definition Sub-Team

July 23, 2009

Document Information and Revision History

| Version | Date | Author(s) | Revision Notes |
| --- | --- | --- | --- |
| 1.0 | 07/23/09 | Shawn Hu | First draft based on two previous documents: AMI Services Gap Analysis Approach.doc AMI Services Detail Design Approach.doc |
| 1.1 | 08/05/09 | GRGray | Added figure captions and some notes. Minor edits for clarity. |

Table of Contents

1.	Introduction	4

1.1.	Scope	4

1.2.	Assumptions	4

1.3.	Glossary	4

1.4.	References	4

2.	Service Design Overall Process	5

2.1.	Step 1 – Business Process Analysis	5

2.2.	Step 2 – Integration Requirements Detailed in Sequence Diagrams	9

2.3.	Step 3 – Service and Operation Pattern Applied	12

2.4.	Step 4 – Service and Information Object Identification and Harmonization	14

2.5.	Step 5 – Data Modeling and Artifacts Generation	15

2.6.	Step 6 – Artifacts Validation and Testing	18

2.7.	Step 7 – Artifacts Version Control and Issue Tracking	20

3.	Web Service Definition Templates	21

# Table of Figures

Figure 1.  Example: Original business process	6

Figure 2.  Example:  Updated business process after integration requirement identified	6

Figure 3.  Integration with ESB.	10

Figure 4.  Integration without ESB or transparent ESB	10

Figure 5.  Entity class diagram of MeterReading	15

Figure 6.  Property class diagram of MeterReading	16

# Introduction

## Scope

This document details an overall process to define services and message payloads. It provides the framework for developing interfaces and provides the guidelines for business process analysis, integration requirements identification, services harmonization and design, data modeling, artifacts generation and validation. Service Oriented Architecture (SOA) patterns and Web Service technology are employed in the process. Related information has been posted on SmartGridiPedia at http://www.smartgridipedia.org/index.php/AMI-ENT_Service_Definitions_Sub-Team

## Assumptions

SOA Web Service technology has been adopted by AMI-ENT Service Definition Task Force as the overarching design principle to provide interoperable and sustainable interface definitions. Both business processes and data information objects are modeled in UML using Sparx EA as a modeling tool. Model driven methodology is followed to generate design-phase artifacts using a semantic model that is mainly based on two reference models; IEC Common Information Model (CIM) and MultiSpeak v3.0.

## Glossary

- CIM – IEC Common Information Model

- EA – Enterprise Architect, a modeling tool from Sparx Systems

- ESB – Enterprise Service Bus

- UML – Unified Modeling Language

- WSDL – Web Service Description Language

- WS-I – Web Service Interoperability industry consortium

- WS-I Basic Profile – Basic Profile from WS-I for Web service interoperability guidance

- XSD – XML Schema

## References

The following documents and standards are referenced.

| Document No. | Document Name | Location |
| --- | --- | --- |
| 1 | W3C Web Service Description Language | http://www.w3.org/TR/wsdl |
| 2 | MultiSpeak – Web Service Online | http://www.multispeak.org/interface/30pb/ |
| 3 | WS-I Basic Profile Version 1.0 | http://www.ws-i.org/Profiles/BasicProfile-1.0-2004-04-16.html |
| 4 | IEC 61968-1: System Interfaces For Distribution Management – Part 1: Interface Architecture and General Requirements | IEC TC57 WG14 (61968) document |
| 5 | IEC 61968-9: System Interfaces For Distribution Management – Part 9: Interface Standard for Meter Reading and Control | IEC TC57 WG14 (61968) document |

# Service Design Overall Process

Major steps involved in the service design overall process are listed below:

- Business process analysis

- Integration requirements detailed in sequence diagrams

- Service and operation pattern applied

- Service and information object identification and harmonization

- Data modeling and artifacts generation

- Artifacts validation and testing

- Artifacts version control and issue tracking

AMI-ENT Use Case B1 – Scenario 1 (AMI meter completes scheduled read request) is used as an example for the steps listed below. Related data model, services, and design artifacts can be found at http://www.smartgridipedia.org/index.php/MeterReading

## Step 1 – Business Process Analysis

Business processes of AMI-ENT use cases are captured in UML activity diagrams. The processes are reexamined for gap analysis in terms of industry standards as well as integration requirements. These activity diagrams are the start point for detail service design. Two activity diagrams are shown below to illustrate the B1-S1 process before and after integration requirement is identified.

Integration requirements identified in B1 – Scenario 1

Figure 1.  Example: Original business process

Figure 2.  Example:  Updated business process after integration requirement identified

Notice in the updated activity diagram, a UML “control flow” activity relationship between Box 03 and Box 04 is replaced with an “object flow” relationship because information objects are involved. The object flow has two objects allocated at each side. These objects (■) are labeled with messages that are exchanged in this particular integration flow.

Note: This integration requirement is added because the information flow crosses the boundary between two actors that are considered in-scope for AMI-ENT service definition.  This is why no similar integration requirement is noted on the boundary between the meter and the head-end in this diagram.  It is assumed at this time that meters will not be hosting services.

The message (object) naming convention follows a verb-noun pair scheme with the verbs listed in Section 2.3, where the verb indicates the intended action of the message while noun indicates the content of the service (message payload).  In the example above, the verb is “Created” and the noun is “MeterReading” so the message name is “CreatedMeterReading”.  These objects are linked to the identified integration requirement (REQ-B1004) using UML dependency associations stereotyped <<trace>>. The linkage establishes traceability between business process and integration requirements. The integration requirement is then further detailed using sequence diagram (Section 2.2) with or without an integration layer.

Note:  Integration requirement naming convention is simply “REQ”, indicating that this is a requirement, “-“, the use case name, “B1”, and the instance of the identified requirement.  In this example this was the fourth integration requirement that was identified for the B1 use case.  Put it all together: REQ-B1004.

The swimlane Name:Classifier pair may also need to be updated during this step. At least the swimlane classifier name (“AMI Head End” in this case) should be aligned with the “Logical Component” name in AMI-ENT SRS Logical Systems Model.

Common elements that constitute an activity diagram are listed below:

Initial Node: An initial node (solid dot) indicates a start of an activity. This node should be always presented in an AMI-ENT activity diagram.

Control Flow: A control flow (line with an arrowhead) shows a flow of control from one action to the next.

Action: An action (round cornered rectangle) represents a single step within an activity. Note an activity box (not shown) is similar in shape in UML but it is used to specify a parameterized sequence of behavior which contains all actions, flows and other elements that make up the activity. Typically only Action box is used in AMI-ENT activity diagrams.

Object Flow: An object flow (an arrowed line with square boxes) has one or two objects on its ends to show object flow. An object box is used in AMI-ENT activity diagrams to indicate a message payload.

Final Node: Activity final node (circle with a dot inside) is typically used to indicate an end of an activity. Note there is another type of final node called flow final node (circle with a cross, not shown) to indicate an end of a single flow. The difference between the two node types is that the flow final node denotes the end of a single control flow; the activity final node denotes the end of all control flows within the activity. The activity final node should be always presented in an AMI-ENT activity diagram.

Decision & Merge Nodes: Decision and merge nodes have the same notation (diamond shape). Control flows come away from a decision node based on conditions. These flows can merge back to one flow using a merge node. These nodes are not included in the example activity diagram (B1-S1) shown above but used in other AMI END activity diagrams.

Fork & Join: Forks and joins have the same notation (horizontal or vertical bar). They indicate the start and end of concurrent threads of control. Note the key difference between a Fork and Decision is that a Fork leads concurrent multiple control flows and Decision leads a flow; either true to a condition or false to a condition but not both.

Swimlane: A swimlane can be either horizontal or vertical, but are typically horizontal for AMI-ENT activity diagrams. The swimlanes are used to separate actions within an activity based on logical systems. Note the Name:Classifier is used in a swimlane. The classifier should follow the SRS Logical System name. Note that the actor AMI Meter does not exist in SRS Logical Systems yet since AMI-ENT SRS scope does not go beyond AMI Head End.

## Step 2 – Integration Requirements Detailed in Sequence Diagrams

A sequence diagram provides a mechanism to describe integration between message providers and consumers in terms of message transaction in this example.  It presents messages in sequence based on integration requirements identified in Step 1).  Two sequence diagrams are listed below for two integration scenarios: with or without integration layer (such as an ESB).

Note the actors in the sequence diagrams below are the same as the swimlane classifiers in the activity diagram shown in Step 1). Again these actors should come from the AMI-ENT SRS Logical Systems list.

Figure 3.  Integration with ESB.

Figure 4.  Integration without ESB or transparent ESB

Note that the two messages in the integration scenario with an ESB are named the same “CreatedMeterReading” for flexible implementation at client application side. By doing so, an integration with or without ESB is irrelevant to a client application. The messages exchanged among the systems listed above are named following a service and operation pattern listed in the next section (Step 3).

Relevant elements that constitute an AMI-ENT sequence diagram are listed below:

Lifeline: A lifeline represents an individual participant in a sequence diagram. For AMI-ENT sequence diagrams, a lifeline typically has an actor element at its head such as “AMI Head End” for this case. A lifeline can also go with an object rectangle box, a boundary, a control, or an entity element which are rarely used for AMI-ENT sequence diagrams.

Messages: Messages are displayed as arrows. Messages can be synchronous (solid arrowhead) or asynchronous (line arrowhead). In the diagram above, the first message is a synchronous message; the second message is a synchronous return (dashed line). Note that a synchronous message usually implies a return meaning a return is not necessarily shown. However, for AMI-ENT sequence diagrams a synchronous return is always explicitly presented to indicate a return message name. This aligns with Web service definition well. The first message matches wsdl:input and the second matches wsdl:output. In summary, two messages are used to present a single synchronous call thread.

Note a return message in EA is displayed with a line arrowhead regardless whether it is synchronous or asynchronous.

## Step 3 – Service and Operation Pattern Applied

After Steps 1) and 2), a collection of interfaces can be identified.  These interfaces are defined as services. In particular, they are defined as Web Services which are described using W3C standard Web Service Description Language (WSDL).

These services typically have common patterns among them. For instance, some services are identified to “receive” data to process their functionality while other services are provided to be queried and “retrieve” data from their repositories. Also a web service can have multiple operations. Hence the pattern not only applies to a service level but to an operation level as well.

Service and operation patterns are critical to implement SOA architecture principles as they promote design quality and consistency.  To identify such patterns can streamline business process implementation, minimize the implementation effort, and reduce the duplication of work. The patterns are summarized below at two levels: service level and operation level.

This is a list of service patterns. These patterns are used for the web services naming convention.

- Send – to provide (send) information (business object) for public (enterprise) consumption. To be invoked by the system of record for the business object and only when the states of the business object has been changed.

- Receive – to consume (receive) information (business object).

- Request – to request another party to perform a specific service

- Execute – to run a service provided to the public, which may include a state change request or a query request.

- Reply – to reply with the result of the execution of a service (by the Execute service)

- Show – to provide (show) information (business object) for public (enterprise) consumption, when the state of the business object is not changed, by the system of record or other system that has a copy of the same business object.

- Retrieve – to request specific data of a business object to be provided.

- Publish – to provide (send) information (business object) for public (enterprise) consumption. To be invoked by the system of record for the business object and only when state of a business object has changed.

- Subscribe – to consume (receive) information (business object) from an external source.

Here is a list of operation naming patterns utilizing IEC 61989 verbs (See Reference list). These patterns are used for the operation naming convention.

- Create –  operation: used in Request, Execute services

- Change –  operation: used in Request, Execute services

- Cancel –  operation: used in Request, Execute services

- Close –  operation: used in Request, Execute services

- Delete –  operation: used in Request, Execute services

- Created –  operation: used in Send, Receive, Reply services

- Changed –  operation: used in Send, Receive, Reply services

- Closed –  operation: used in Send, Receive, Reply services

- Canceled –  operation: used in Send, Receive, Reply services

- Deleted –  operation: used in Send, Receive, Reply services

- Get – not used, equivalent to Retrieve service

- Show – used as the service level pattern.

- Reply – used as the service level pattern.

- Subscribe – used as the service level pattern.

- Unsubscribe – not used.

Using the two pattern lists above, service/operation naming convention is described as below:

- Service naming convention:

  - <Information Object>

    - if no ESB involved or ESB is “invisible” such as MeterReading

  - <Service pattern name> + <Information Object>

    - if ESB is involved such as ReceiveMeterReading

- Operation naming convention:

  - <Operation pattern name> + <Information Object>

    - for both integration scenarios such as CreatedMeterReading

## Step 4 – Service and Information Object Identification and Harmonization

Service identification is a critical step in the overall service design process. It is not just driven by the business process analysis in Step 1) but is also based on the data information model and in accordance with business functionality. Identified services are listed in a service inventory sheet (sample rows listed below) which organizes all identified services across business processes. This inventory sheet offers an opportunity to harmonize services so that granularity level of services and information objects can be better determined, overlapped services can be eliminated, services can be better aligned with business, and well-defined services can be achieved.

Based on the business process analysis (Step 1), the following information object (message payload) is identified for data exchange in B1-S1.

Information objects identified in B1 – Scenario 1

- MeterReading

There are two integration scenarios to exchange this information object, one without ESB and one with ESB. The integration without ESB is basically a point-to-point style integration. In this case, only one web service is identified as listed in the table below. The operation name follows the operation pattern in Step 3).

- Integration without ESB or invisible ESB

| Use Case & Scenario | Integration Requirement | Operation Pattern | Service Name | Service Operation | Service Consumer | Service Provider | Information Object |
| --- | --- | --- | --- | --- | --- | --- | --- |
| B1-S1 | REQ-B1004 | Created | MeterReading | CreatedMeterReading | Head End | MDMS | MeterReading |

If an ESB is involved, typically two services are involved and named after the service patterns listed in Step 3).

- Integration with ESB

| Use Case & Scenario | Integration Requirement | Operation Pattern | Service Name | Service Operation | Service Consumer | Service Provider | Information Object |
| --- | --- | --- | --- | --- | --- | --- | --- |
| B1-S1 | REQ-B1004 | Created | SendMeterReading | CreatedMeterReading | Head End | ESB | MeterReading |
| B1-S1 | REQ-B1004 | Created | ReceiveMeterReading | CreatedMeterReading | ESB | MDMS | MeterReading |

Note that these information as well as other identified services and information objects have been documented in the AMI-ENT Service Inventory Sheet.

## Step 5 – Data Modeling and Artifact Generation

Information objects documented after Step 4) are modeled in UML using Sparx EA. The UML model is created in the following layered structure:

- Reference Model

- Semantic Model

- Context Model

- Implementation Model

These layers are organized in UML packages. The Reference Model package contains two models: IEC CIM and MultiSpeak. IEC CIM is delivered in UML so it is directly imported into EA. MultiSpeak, however, is in XSD format so it is reverse engineered into UML model.

Classes and attributes in CIM and MultiSpeak are selected and transformed into Semantic Model based on the Information Objects identified. During this process, Reference Model classes are transformed into entity classes and attributes are transformed into property classes. By doing so, all classes and attributes are abstracted to a global level for explicit semantics. This is a key step in defining a semantic model.

Context Model package contains a number of context folders based on the information objects listed in the Service Inventory Sheet. Each context folder contains a single entity level class diagram and a number of property class diagrams. An entity class diagram lists all entities that are used to describe an information object.  A property class diagram contains a number of properties that are used to define an entity in a particular context. An entity class diagram and a property diagram are shown below.

Figure 5.  Entity class diagram of MeterReading

In total eight entity classes are included for the MeterReading information object. Each entity contains a list of property classes, for example MeterReading contains six property classes as shown below:

Figure 6.  Property class diagram of MeterReading

A model driven application tool can then be utilized to generate XSDs in an automated fashion. First of all, a semantic context model (Platform Independent Model – PIM) is transformed into an implementation model (Platform Specific Model – PSM) and stereotyped using an XSD profile. Once an implementation model is ready, a direct translation to XSD can be achieved. Note this translation leads to an explicit XSD generation with the help of the XSD profile applied to the implementation model. The XSD namespace follows a naming convention listed below:

- targetNamespace=“http://www.smartgridipedia.org/yyyy/mm/<Information Object>”

The string “yyyy/mm” is used for version control which will be detailed out in Section 2.7. A sample MeterReading XSD can be found at: http://www.smartgridipedia.org/index.php/Physical_Model_for_MeterReading_(XML_Schema_(XSD))

WSDLs are generated using templates documented in Section 3. The namespace follows a similar naming convention as the one used for XSDs:

- targetNamespace=“http://www.smartgridipedia.org/yyyy/mm/<Service Name>.wsdl”

AMI-ENT WSDLs can be used for integration with ESB or without ESB. Note the ones posted on SmartGridiPedia have the service name for integration without ESB. A logical representation of MeterReading service can be found at: http://www.smartgridipedia.org/index.php/MeterReading_Service

MeterReading artifacts package including all related WSDLs and XSDs can be downloaded at http://www.smartgridipedia.org/index.php/MeterReading

Common elements that constitute a class diagram are listed below:

Class: A class is an element that defines its attributes and behaviors that an object is able to generate. In AMI-ENT data modeling an effort on data semantics has been made to bring all items (classes and attributes) to global level. To do so, traditional object classes are stereotyped “Entity” classes and attributes are transformed into classes which are stereotyped “Property” classes.  An attribute that was duplicated in several places can now be eliminated and consolidated into a single semantic class. As a result, there is no attribute for classes but only Property classes.

Association: An association shows a relationship between elements such as classes. This relationship includes named roles at each end, cardinality, direction and constraints. In AMI-ENT data modeling, a directional association (line arrowhead) is typically used to imply a containment relationship such as MeterReading contains 0 to many MeterAsset in this particular context.

Generalization: A generalization relationship is used to show inheritance such as a MeterReading class is inherited from IdentifiedObject class. It means MeterReading class inherits the characteristics of IdentifiedObject including its attributes and relationships.

Aggregation & Composition:

An aggregation (white diamond arrowhead, not shown) is used to depict a relationship in which an element is made up of smaller components.

A composition (black diamond arrowhead) is a stronger form of aggregation. It is used where components can be included in a maximum of one composition at a time. It is used in AMI-ENT data modeling to present a relationship between an entity and a property.

## Step 6 – Artifact Validation and Testing

Generated XSDs/XMLs and WSDLs should be fully validated and tested before implementation. Validation and testing steps are described in this section.

XSD and XML validation

A message payload definition in XSD should be validated before it can be deployed. Typically a message validation process includes:

- Message schema (XSD) validation

- Message instance (XML) validation against XSD

The validation of a message schema includes both validity checking and validation against its imported schema(s). All message schemas in AMI-ENT service definition effort import a MessageHeader schema and as a result they should be validated with the header schema included.

Once an instance XML document is created the XML should be validated against its XSD as well as the well-formedness as recommended by the W3C.

WSDL Validation

The WSDL file is an XML document itself. Therefore it should be validated against generic W3C specification for an XML document. Secondly it should be validated against W3C specification for a WSDL document. Furthermore a validation based on WS-I Basic Profile should be conducted since this profile is adopted by AMI-ENT Service Definition Task Force. Thus, validation process for a WSDL document shall include two steps:

- WSDL well-formedness validation (both W3C XSD & WSDL)

- WSDL WS-I compliance validation

The XML well-formedness validation follows the W3C recommendations that can be found at http://www.w3.org/TR/2004/REC-xml-20040204. A number of XML tools can be utilized for the validation.

WS-I Basic Profile provides guidelines to develop interoperable Web services. WS-I also provides testing tools that evaluate Web services conformance to the Basic Profile. The Basic Profile can be found at http://www.ws-i.org/Profiles/BasicProfile-1.0-2004-04-16.html

Web Service Testing

After the validation step, Web services can then be created and tested according to their WSDL definitions using open source applications such as Apache Axis2. Service pattern name can then be updated and tested based on integration needs such as with or without an ESB.

- With ESB: <wsdl:service name=”SendMeterReading”>

Or

- Without ESB: <wsdl:service name=”MeterReading”>

## Step 7 – Artifact Version Control and Issue Tracking

Both XSDs and WSDLs need to be version controlled since both can be updated many times in the course of a service definition. In this section, the usage of both targetNamespace and version attribute is described for design-phase artifacts version control.

XSD version control:

There are two scenarios for an XSD version update:

- Major version update

It means major update has been made in an XSD and its backward compatibility has been broken as a result.

- Minor version update

It means its backward compatibility is held. One example of such minor update is a new element added but as optional.

By naming convention, XSD targetNamespace and version attribute are defined as:

- targetNamespace=“http://www.smartgridipedia.org/yyyy/mm/MeterReading”

- version="<Major version>.<Minor version>".

Here are two examples for major and minor XSD updates, respectively.

In this example a 2009/02 version has a major update, its targetNamespace and version should be changed from:

- targetNamespace=“http://www.smartgridipedia.org/2009/02/MeterReading” version=”1.0”

To

- targetNamespace=“http://www.smartgridipedia.org/2009/03/MeterReading” version=”2.0”

However if an update is minor, its targetNamespace and version will be changed from:

- targetNamespace=“http://www.smartgridipedia.org/2009/02/MeterReading” version=”1.0”

To

- targetNamespace=“http://www.smartgridipedia.org/2009/02/MeterReading” version=”1.1”

Note that the “version” attribute does not apply to XML validation against an XSD so its content change does not break validation against previous XSD version.

WSDL version control:

An XSD is imported in a WSDL for data type definition. As a result, at least two namespaces (XSD & WSDL) exist in a WSDL definition as shown below:

targetNamespace="http://www.smartgridipedia.org/2009/03/MeterReading.wsdl"

xmlns:typeOrig="http://www.smartgridipedia.org/2009/03/MeterReading"

By convention, WSDL targetNamespace needs to be updated whenever a change occurs to an XSD namespace. In other words, a major XSD update will result in a WSDL namespace change and minor XSD update (no namespace change) will have no impact on WSDL namespace.

Issue Tracking:

Issue reporting and tracking can be found at:

http://osgug.ucaiug.org/utilityami/AMIENT/Serivce%20Definitions%20Team/Lists/Service%20Definition%20issues/AllItems.aspx

# Web Service Definition Templates

A separate document has been created for Web Service Definition Templates. It is embedded below: