AMI-ENT Task Force

AMI-ENT Functional Requirements and Use Case Document

AMI-ENT Demand Response

Functional Requirements and Use Case Document

Version 1.0

| Version: | 1.0 |
| --- | --- |
| Created: | June 30, 2009 |
| Last Update: |  |
| Print Date: |  |
| By: | AMI ENT DR Use Case Team |
| Distribution: | Public |

Acknowledgements

The following individuals and their companies are members of the UCAiug OpenSG and have contributed and/or provided support to the work of the AMI ENT Demand Response Functional Requirements and Use Case Document:

Albert Chiu, Pacific Gas and Electric

Reggie Cole, Lockheed Martin

Kent Dickson, Tendril

Tray Fleming, SAIC Global Utility Sector

Gerald R. Gray, Consumers Energy

Erich Gunther, EnerNex

Greg Hinchman, Lockheed Martin

Doug Houseman, Capgemini

Alex Levinson, Lockheed Martin

Wayne Longcore, Consumers Energy

Randy Lowe, American Electric Power

John Mani, Converge

Stuart McCafferty, EnerNex

Jerry Melcher, EnerNex

Terry Mohn, Sempra Energy Utilities

Dave Owens, Lockheed Martin

Phil Montell, American Electric Power

Greg Robinson, Xtensible Solutions

Craig Rodine, Grid Net

Daniel J. Rogier, American Electric Power

Marc Rosson, Snohomish County PUD

Bob Roth, Sparx Systems

Jack. Shih, Southern California Edison

Deb Smith, Digi International

Kay Stefferud, Lockheed Martin

Eva Thomas, Corporate Systems Engineering, Inc

Bon Truong, San Diego Gas & Electric

Mark Van Den Broek, Lockheed Martin

Bud Vos, Converge

Xiaofeng Wang, GE Energy

Josh Wepman, SAIC

Joe Zhou, Xtensible Solutions

Table of Contents

1.0	INTRODUCTION	1

1.1	Purpose of Document	1

2.0	Application Overview	2

2.1	Scope	5

2.2	Context	6

2.3	Technical Environment	6

2.4	Terms and Definitions	6

2.5	Function Decomposition	11

3.0	DRMS Model	14

3.1	Business Process Models	14

3.1.1	Business Functions	14

3.1.2	Demand Response Business Process Model	15

3.1.3	Analyze Demand Response Scenario	16

3.1.4	Capture and Store Behavior Information on Demand Resources	17

3.1.5	Manage DR Program	17

3.1.6	Monitor and Store Real Time Network Information	18

3.1.7.1	Add DR Device	18

3.1.7.2	Remove DR Device	19

3.1.7.3	Manage Demand through Direct Load Control	19

3.1.8	Non-Functional Requirements	20

3.1.8.1	Performance Requirements	20

3.1.8.2	Performance	20

3.1.8.3	Scalability	21

3.1.8.3.1	Scalable for current markets	21

3.1.8.3.2	Scalable for future markets	21

3.1.8.4	Security	21

3.1.8.5	Transport	21

3.1.8.5.1	Compliant with IEC TC57 standards	22

3.1.9	Actors	22

3.1.9.1	Billing Agent	23

3.1.9.2	Customer	23

3.1.9.3	Demand Response Provider	23

3.1.9.4	Distributor	23

3.1.9.5	ISO	23

3.1.9.6	ISO or Grid Operator	23

3.1.9.7	Large C/I Customer and Co-Generator	24

3.1.9.8	Metering Agent	24

3.1.9.9	Regulator	24

3.1.9.10	Scheduling Agent	24

3.1.9.11	Settlement Agent	24

3.1.9.12	Small-Scale Merchant Generator	24

3.2	Manage Energy Resource	26

3.3	Manage Demand	26

3.4	Manage Demand for Economic Effect	26

3.5	Manage Demand through Direct Load Control	26

3.6	Manage Demand for Maintenance Purpose	27

3.7	Manage Demand in Respond to Pricing Signal	27

3.8	Manage DR Programs	27

3.8.1	Administer Program	28

3.8.2	Create DR Program	28

3.8.3	Delete DR Program	29

3.8.4	Enroll Customer	29

3.8.5	Dis-enroll Customer	29

3.8.6	Execute Program	30

3.8.7	Manage Program Customer	30

3.8.8	Measurement and Verification	30

3.8.9	Read DR Program	31

3.8.10	Supply Interruptible Resource	31

3.8.11	Supply Non-Interruptible Resource	32

3.8.12	Update DR Program	33

3.8.13	Manage Statistics	33

3.9	Manage DR Customer	34

3.10	Provision Demand Response Equipment	34

3.10.1	Add DR Device	34

3.10.2	Remove DR Device	35

3.10.3	Read DR Device Information	35

3.10.4	Update Active DR Device	35

3.11	Manage Supply	35

3.12	Manage Supplier	36

3.13	Manage Supply through Price Signal	36

3.14	Manage Supply through Direct Control	36

3.15	Provision Supply Response Equipment	36

4.0	DR Event Class	37

List of Figures

Figure 2-1.  Timing of a Demand Response Event	2

Figure 2-2.  Illustration of Baseline Concept	4

Figure 2-3.  Demand Response Service Types	5

Figure 2-4.  DRMS High-Level Functional Decomposition	11

Figure 2-5.  Manage Customer Programs Functional Decomposition	12

Figure 2-6.  DR Measurement and Verification Functional Decomposition	12

Figure 2-7.  Execution Event Resopnse Funcational Decomposition	13

Figure 3-1.  IEG-61968 IRM Business Functions	14

Figure 3-2.  Demand Response Business Process Model	15

Figure 3-3.  Analyze Demand Response Scenario	16

Figure 3-4.  Capture and Store Behavior Information on Demand Resources	17

Figure 3-5.  Manage DR Program	17

Figure 3-6.  Monitor and Store Real Time Network Information	18

Figure 3-7.  Add DR Device to Data Repository	18

Figure 3-8.  Remove DR Device From Data Repository	19

Figure 3-9.  Manage Demand through Direct Load Control	19

Figure 3-10.  Non-Functional Requirements	20

Figure 3-11.  Performance	20

Figure 3-12.  Scalability	21

Figure 3-13.  Transport	21

Figure 3-14.  Reference Architecture	22

Figure 3-15.  Actors	23

Figure 3-16.  Primary Use Case Diagram	25

Figure 3-17.  Manage DR Programs Use Case Diagram	27

Figure 3-18.  Supply Interruptible DR Resource	32

Figure 3-19.  Supply Non-Interruptible DR Resource	33

Figure 3-20.  Provision Demand Response Equipment	34

Figure 4-1.  DR Event Class Diagram	37

1.0	INTRODUCTION

Demand Response is the proactive management of electric and gas utility loads in order to more efficiently and reliably market, produce, transmit and deliver energy. Applications of demand response are as simple as the Utility interrupting load in response to severe grid transients or supply shortages (direct load control or active demand-side management), or as complex as millions of customers voluntarily reducing their consumption/load in response to price signals (passive demand-side management). With the exception of having to address emergencies, DR is generally used to flatten the demand peaks. In any case, the Utility must have a communications gateway to either directly control the consumer's loads, or provide a pricing signal to allow the consumer to manage their consumption directly by:

Making the decision when to use appliances/equipment

As input to a home/premise energy management system

Large Commercial and Industrial Customer DR Programs are not new. They have been in-place for more than 20 years. Demand Response systems have traditionally been utilized with large commercial and industrial customers because the individual loads are larger, requiring fewer controls and automation, in achieving the desired load reduction/shedding. However, as demand has continued to grow, there has been a noticeable shift in the overall makeup and magnitude of the energy demand peak. Residential consumers now make up about 60% of the peak, with unprecedented growth occurring, such as 17% growth in the last three years in the U.S. Mid-Atlantic states. Additional DR will have to come primarily from residential consumers. There currently are successful, residential DR programs – Florida Power and Light (FP&L) Company has about 750,000 residential customers enrolled with the capability to shed ~1,000 Mw of load.

To clarify terms, this document describes:

Energy Efficiency – Reduce total kilowatt of load with permanent and efficient technologies

Demand Response – Temporary reduction of peak energy usage for a defined duration. Curtailment events are triggered either by reliability events or pricing signals.

Load Shifting – Flattening the peak by using off-peak power in place of on-peak power. This is often a permanent peak shift driven by combining technologies and time-of-use rates. An example includes thermal energy storage.

1.1	Purpose of Document

The Purpose of this Document is to define the Use Cases and functional requirements for a Demand Response Management System (DRMS) deployable anywhere in the world. The desired system will be developed using open non-proprietary standards, will be scalable to any geographic area, and will be designed to be upwardly compatible with future enhancements,

2.0	Application Overview

Demand Response systems curtail load to maintain grid reliability and to reduce demand during peak load periods.  Demand Response systems manage load by issueing Demand Response Events.

The illustration below (Figure 2-1) from the Recommendation to the NAESB Executive Committee represents the terms for timing events and time durations applicable to a Demand Response Event.  The definitions of the ten elements in the illustration are the basis for describing the Timing of a Demand Response Event.  The applicablity of these elements to a Demand Response Service is dependent on the Service type.  The Grid Operator shall specify whether any or all of the elements illustrated in the Timing Demand Response Event figure are applicable.  In some cases, some elements will not be applicable; the inclusion of the elements establish a requirement for said elements.

Source: Recommendation to the NAESB Executive Committee DSM-EE Subcommittee dated December 2, 2008

Figure 2-1.  Timing of a Demand Response Event

The following terms refer to the above Figure 2-1.

| Term | Definition |
| --- | --- |
| Advance Notification(s) | One or more communications to Demand Resources of an impending Demand Response Event in advance of the actual event. |
| Deployment | The time at which a Demand Resource begins reducing Demand on the system in response to an instruction. |
| Deployment Period | The time in a Demand Response Event beginning with the Deployment and ending with the Release/Recall. |
| Normal Operations | The time following Release/Recall at which a System Operator may require a Demand Resource to have returned its Load consumption to normal levels, and to be available again for Deployment. |
| Ramp Period | The time between Deployment and Reduction Deadline, representing the period of time over which a Demand Resource is expected to achieve its change in Demand. |
| Recovery Period | The time between Release/Recall and Normal Operations, representing the window over which Demand Resources are required to return to their normal Load. |
| Reduction Deadline | The time at the end of the Ramp Period when a Demand Resource is required to have met its Demand Reduction Value obligation. |
| Release/Recall | The time when a System Operator or Demand Response Provider notifies a Demand Resource that the Deployment Period has ended or will end. |
| Sustained Response Period | The time between Reduction Deadline and Release/Recall, representing the window over which a Demand Resource is required to maintain its reduced net consumption of electricity. |

A Baseline is an estimate of the electricity that would have been consumed by a Demand Resource in the absence of a Demand Response Event. The Baseline is compared to the actual metered electricity consumption during the Demand Response Event to determine the Demand Reduction Value.  Depending on the type of Demand Response product or service, Baseline calculations may be performed in real-time or after-the-fact.  The Grid Operator may offer multiple Baseline models and may assign a Demand Resource to a model based on the characteristics of the Demand Resource's Load or allow the Demand Resource to choose a performance evaluation model consistent with its load characteristics from a predefined list.  A baseline model is the simple or complex mathematical relationship found to exist between Baseline Window demand readings and Independent Variables.  A baseline model is used to derive the Baseline Adjustments which are part of the Baseline, which in turn is used to compute the Demand Reduction Value.  Independent variable is a parameter that is expected to change regularly and have a measureable impact on demand.  Figure 2-2 illustrates the concept of Baseline relative to a Demand Response Event.

Source: Recommendation to the NAESB Executive Committee DSM-EE Subcommittee dated December 2, 2008

Figure 2-2.  Illustration of Baseline Concept

DR Services define the typical services that a Grid Operator can request or correspondingly that a Demand Response Provider can supply.

Figure 2-3.  Demand Response Service Types

2.1	Scope

Demand Response (DR) systems are currently being considered for adoption and expansion in a number of markets.  Existing DR systems have been successfully deployed by organizations including ISO New England, co-ops and others using AMR meters, and through numerous programs controlling air conditioners with wireless signals.

Newer DR systems will ideally build upon features of existing systems while providing for future enhancements via open standards which anticipate technology advancements including smart meters, increased local generation, e.g., microgrids, and other SmartGrid infrastructure enhancements.

The specific DR system covered by this document is anticipated to be used by public utilities, coops, government-owned utilities and direct access providers.  In order to leverage both existing and future vendor investments in DR system development, the intent of the DR functionality described here is to be compatible with existing technology, and to be compliant with IEC electrical standards, specifically with IEC 61968.

2.2	Context

This document is targeted to utilities, regional transmission operators, third party aggregators and large demand response providers.  A Demand Response Management Systems (DRMS) is envisioned that will evolve over time to accomplish many tasks including:

DR program design, operations, and enrollment

DR event execution including forecasting, bidding and scheduling

DR performance evaluation including measurement and validation based on baseline methodology

DR event billing and settlement

All these DR activities result in a need for implementation of business processes that are derived from a solid set of functional requirements. These activities will result in integration with utilities' internal systems as well as external clients.  Information exchange will be a fundamental requirement to successful deployment of a DRMS.

2.3	Technical Environment

We envision this new system to integrate with at least the following existing systems: Customer Billing, Outage Management, Meter Data Management, Customer Relationship Management and Financial.

2.4	Terms and Definitions

This subsection provides the definition of terms in general use:

| Term | Definition |
| --- | --- |
| Adjustment Window | The period of time prior to a Demand Response Event used for calculating a Baseline adjustment. |
| Advanced Metering | Technology which allows two way communications between the utility and the meter. This communication enables the ability to analyze energy consumption resulting in more efficient demand response systems. |
| Advanced Metering Infrastructure (AMI) | The infrastructure built around advanced metering allowing the utility and consumer to communicate in real time with respect to energy consumption. Based on the information collected the utility is able to obtain an accurate reading of demands, while consumers are able to modify their usage to save energy. |
| Aggregated Demand Resource | A group of independent Load facilities that provide Demand Response services as a single Demand Resource. |
| After-the-Fact Metering | Interval meter data separate from Telemetry that is used to measure Demand Response. May not apply to Demand Resources under Baseline Type II (Non-Interval Meter). |
| Automated Meter Reading | Automated meter reading is a subcategory of AMI which allows for communication devices to transfer data from a meter to the utility or from a meter to the data management provider. |
| Baseline | A Baseline is an estimate of the electricity that would have been consumed by a Demand Resource in the absence of a Demand Response Event. The Baseline is compared to the actual metered electricity consumption during the Demand Response Event to determine the Demand Reduction Value. Depending on the type of Demand Response product or service, Baseline calculations may be performed in real-time or after-the-fact. The Grid Operator may offer multiple Baseline models and may assign a Demand Resource to a model based on the characteristics of the Demand Resource’s Load or allow the Demand Resource to choose a performance evaluation model consistent with its load characteristics from a predefined list. A baseline model is the simple or complex mathematical relationship found to exist between Baseline Window demand readings and Independent Variables. A baseline model is used to derive the Baseline Adjustments which are part of the Baseline, which in turn is used to compute the Demand Reduction Value. Independent variable is a parameter that is expected to change regularly and have a measureable impact on demand. |
| Baseline Adjustment | An adjustment that modifies the Baseline to reflect actual conditions immediately prior to or during a Demand Response Event to provide a better estimate of the energy the Demand Resource would have consumed but for the Demand Response Event. The adjustments may include but are not limited to weather conditions, near real time event facility Load, current Demand Resource operational information, or other parameters based on the System Operator’s requirements. |
| Baseline Type-I (Interval Metered) | A Baseline performance evaluation methodology based on a Demand Resource’s historical interval meter data which may also include other variables such as weather and calendar data. |
| Baseline Type-II (Non-Interval Metered) | A Baseline performance evaluation methodology that uses statistical sampling to estimate the electricity consumption of an Aggregated Demand Resource where interval metering is not available on the entire population. |
| Baseline Window | The window of time preceding and optionally following, a Demand Response Event over which the electricity consumption data is collected for the purpose of establishing a Baseline. The applicability of this term is limited to Meter Before/Meter After, and Baseline Type-I and Type-II. |
| Business Intelligence | A term describing the extraction and presentation of data to provide business value. |
| Business Service Provider | Software delivered over the internet as web services. The platform for integrating these web services is the enterprise service bus. |
| Capacity Service | A type of Demand Response service in which Demand Resources are obligated over a defined period of time to be available to provide Demand Response upon deployment by the System Operator. |
| Communicate | Interact and cooperate with people or organizations (groups of people). |
| Control | Monitor and regulate the supply (of electricity or other commodity) |
| Daily Consumption | The amount of energy a customer uses in a 24 hour period. This information is used to drive business intelligence solutions. |
| Demand | The rate at which electric energy is delivered to or by a system or part of a system, generally expressed in kilowatts or megawatts, at a given instant or averaged over any designated interval of time; and the rate at which energy is being used by the customer (NERC Definition). |
| Demand Billing | The energy demand of a customer upon which billing is calculated. This is often based on peak demand or some other demand related measurement. |
| Demand Interval | The interval of time between demand queries to the meter. This is typically in 15, 30, and 60 minute intervals. |
| Demand Reduction Value | Quantity of reduced electrical consumption by a Demand Resource, expressed as MW or MWh. |
| Demand Resource | A Load or aggregation of Loads capable of measurably and verifiably providing Demand Response. |
| Demand Response | An agreement between customer and utility that states that the customer agrees to allow the utility to manage their energy consumption when the utility deems necessary. Often times this result in the utility increasing or reducing energy distribution based on supply based metrics. Demand response mechanisms typical operate in on or off whereas dynamic response mechanisms may passively curtail energy usage as the mechanism senses stress on the grid. |
| Demand Response Provider | The entity that is responsible for delivering Demand reductions from Demand Resources and is compensated for providing such Demand Response products in accordance as specified by the System Operator. |
| Distributed Generation | Electricity generation from small energy sources allowing for more efficient energy distribution. This approach allows for energy to be generated closer to the source of the consumption which reduces the distance the generated energy has to travel. |
| Energy Data Acquisition | Obtaining meter data by way of handheld devices. Essentially a non automated meter reading typically administered by a utility worker. |
| Energy Data Management | Analyzing meter data for consumption by backend systems. Often times these back end systems will measure load, calculate demand response, billing intervals, etc. |
| Energy Service | A type of Demand Response service in which Demand Resources are compensated solely based on their performance during a Demand Response Event. |
| Enterprise Resource Planning | Integrating all back and front office data and process into one unified enterprise system. |
| ESB | Enterprise Service Bus. The ESB provides the features necessary for a service oriented architecture implementation by providing a place to host all of the web services. |
| Highly-Variable Load | A Load with a fluctuating or unpredictable electricity consumption pattern. |
| IEC | The International Electrotechnical Commission (IEC). The IEC TC57 maintains an electric utility focused information model called CIM (Common information model). |
| IEC 61968 | International standards for Energy Distribution Managements Systems, respectively, specify a Common Information Model (CIM) for utility data exchange, Applications Programming Interfaces (API) for application integration (GID), and XML messaging standards. |
| Load | An end-use device or customer that receives power from the electric system (NERC Definition). |
| Load Shedding | Reducing a customer's demand in order to maintain integrity of the grid. Load shedding in utility operations, is monitoring electric usage continuously (usually by automated instrumentation) and shutting down certain pre-arranged electric loads or devices if a certain upper threshold of electric usage is approached. |
| Logical Data Model | A representation of an organization's data based upon entities and attributes of those entities. A logical data model is often a logical representation of a business' integration or business requirements. |
| Maintain | Keep up to date information on, typically associated with data storage. |
| Manage | Control and effectively handle devices or processes. |
| Maximum Base Load | A performance evaluation methodology based solely on a Demand Resource’s ability to reduce to a specified level of electricity Demand, regardless of its electricity consumption or Demand at Deployment. |
| Meter Before/ Meter After | A performance evaluation methodology where electricity Demand over a prescribed period of time prior to Deployment is compared to similar readings during the Sustained Response Period. |
| Meter Bus (M-bus) | Allows for the interconnecting of many different utility measuring units (i.e. gas, electric, water, etc.) The M-Bus acts as the central station for these different utilities to communicate with. |
| Meter Data Management | A system for storing, processing, consuming and analyzing large quantities of meter data. |
| Meter Data Recording Interval | The time between electricity meter consumption recordings. |
| Metering Date Reporting Deadline | The maximum allowed time from the end of a Demand Response Event (Normal Operations) to the time when meter data is required to be submitted for performance evaluation and settlement. The Meter Data Reporting Deadline may be either relative (a number of hours/days after Normal Operations) or fixed (a fixed calendar time, such as end-of-month). |
| Metering Generator Output | A performance evaluation methodology, used when a generation asset is located behind the Demand Resource’s revenue meter, in which the Demand Reduction Value is based on the output of the generation asset. |
| Performance Window | The period of time in a Demand Response Event analyzed by the System Operator to measure and verify the Demand Reduction Value for a Demand Resource. |
| Price Signals | Messages sent to consumers which specify a commodity price. |
| Provide | Feature/possess the capability to. System has the ability to perform the specified function. |
| Ramp Rate | The rate, expressed in megawatts per minute, that a generator changes its output. (NERC Definition) Demand Resource ramp rate is the rate, expressed in megawatts per minute, that a Demand Resource changes its Load. |
| Real Time Metering | Meter readings taken almost in real time to allow for adjustments to be made as the energy market fluctuates. |
| Regulation Service | A type of Demand Response service in which a Demand Resource increases and decreases Load in response to real-time signals from the System Operator. Demand Resources providing Regulation Service are subject to dispatch continuously during a commitment period. Provision of Regulation Service does not correlate to Demand Response Event timelines, deadlines and durations. |
| Receive | Accept messages from devices. |
| Reserve Service | A type of Demand Response service in which Demand Resources are obligated to be available to provide Demand reduction upon deployment by the System Operator, based on reserve capacity requirements that are established to meet applicable reliability standards. |
| SLA | Service Level Agreement: the part of a service contract where the level of the services are agreed upon between two systems. |
| Smart Grid | The term smart grid represents the digital upgrade of our distribution and long distance transmission grid allowing for increased energy efficiency as well as a boost in optimization of current systems. |
| Smart Meters | Meters with extra functionality that allow for more accurate and useful meter readings. This extra functionality allows the meter to collect usage data and transmit this data back to the utility over a network. |
| SOA | Service oriented architecture - The concept of grouping business functionality around business processes. These services are than packaged as interoperable services. A SOA architecture allows for the transmission of data between multiple systems as they participate in multiple business processes. |
| SOAP | Simple Object Access Protocol (XML protocol) - A protocol for exchanging xml messages for web services in a service oriented architecture implementation. |
| Supervisory Control and Data Acquisition (SCADA) | SCADA systems monitor and control the electric power generation, transmission, and distribution. |
| Supply Resources | Devices which have the capability to supply electricity. |
| System Operator | A System Operator is a Balancing Authority, Transmission Operator, or Reliability Coordinator whose responsibility is to monitor and control an electric system in real time (based on NERC definition). The System Operator is responsible for initiating Advance Notifications, Deployment, and Release/Recall instructions. |
| Telemetry | Real-time continuous communication between a Demand Resource or Demand Response Provider and the System Operator. |
| Telemetry Interval | The time unit between communications between a Demand Resource or Demand Response Provider and a System Operator. |
| Transmit | Send messages to devices. |
| UML | Unified Modeling Language is a general purpose modeling language commonly used for object/data modeling. |
| Utility Sub Metering | An implementation that allows for a multi tenant property to bill tenants for individual energy usage. This is most commonly implemented in apartments and condominiums. |
| Validation, Editing and Estimation | The process of taking raw meter data and performing validation and, as necessary, editing and estimation of corrupt or missing data, to create validated data. (VEE guidelines are published in the Edison Electric Institute’s Uniform Business Practices for Unbundled Electricity Metering, Volume Two, Published 12/05/00, http://www.naesb.org/REQ/req_form.asp). |
| WSDL | Web Services Description Language is a xml format used to describe web services and the messages that interface with the web services. |
| XML | Extensible Markup Language – general purpose markup language for creating custom mark-up languages. |
| XSD | A description describing a specific xml document focusing primarily on the restraints and structure of that xml document. |

2.5	Function Decomposition

Functional decompositions define a system in terms of its main activities. For the DRMS, the main activities have been defined in  three main areas:

Manage Customer Programs

Execute DR Event Response and

DR Measurement and Verification.

The three main functional areas were then further broken down into subfunctions as shown in Figures 2-4, 2-5, 2-6 and 2-7.

Figure 2-4.  DRMS High-Level Functional Decomposition

Figure 2-5.  Manage Customer Programs Functional Decomposition

Figure 2-6.  DR Measurement and Verification Functional Decomposition

Figure 2-7.  Execution Event Resopnse Funcational Decomposition

3.0	DRMS Model

3.1	Business Process Models

3.1.1	Business Functions

Figure 3-1.  IEG-61968 IRM Business Functions

3.1.2	Demand Response Business Process Model

Figure 3-2.  Demand Response Business Process Model

3.1.3	Analyze Demand Response Scenario

Figure 3-3.  Analyze Demand Response Scenario

3.1.4	Capture and Store Behavior Information on Demand Resources

Figure 3-4.  Capture and Store Behavior Information on Demand Resources

3.1.5	Manage DR Program

Figure 3-5.  Manage DR Program

3.1.6	Monitor and Store Real Time Network Information

Figure 3-6.  Monitor and Store Real Time Network Information

3.1.7.1	Add DR Device

Figure 3-7.  Add DR Device to Data Repository

3.1.7.2	Remove DR Device

Figure 3-8.  Remove DR Device From Data Repository

3.1.7.3	Manage Demand through Direct Load Control

Figure 3-9.  Manage Demand through Direct Load Control

3.1.8	Non-Functional Requirements

Figure 3-10.  Non-Functional Requirements

3.1.8.1	Performance Requirements

Performance requirements define parameters such as transactions per second, network latency, form load times and other measurable aspects of the system that govern overall speed and responsiveness.

3.1.8.2	Performance

Figure 3-11.  Performance

3.1.8.3	Scalability

Figure 3-12.  Scalability

3.1.8.3.1	Scalable for current markets

The DR solution shall scale to up to Current market size includes known programs with 10,000,000 meters with up to 50,000,000 devices.

3.1.8.3.2	Scalable for future markets

Future markets may contain entities with up to a 1000 number of participants in a single geographic location.

3.1.8.4	Security

The DR solution shall be in compliance with the AMI System Security Requirements and Guidelines, version 1.0, approved at the January 8, 2009 AMI-SEC meeting held in Palo Alto, California.

3.1.8.5	Transport

Figure 3-13.  Transport

3.1.8.5.1	Compliant with IEC TC57 standards

The DR solution shall be compliant with the latest IEC TC57 Reference Architecture.  See the reference architecture in Figure 14.

Figure 3-14.  Reference Architecture

3.1.9	Actors

Actors are the users of the system being modeled. Each Actor will have a well-defined role, and in the context of that role have useful interactions with the system.

A person may perform the role of more than one Actor, although they will only assume one role during one use case interaction.

An Actor role may be performed by a non-human system, such as another computer program.

Figure 3-15.  Actors

3.1.9.1	Billing Agent

The billing agent determines the cost including applicable credits for customers.  Typically costs vary among different classes of customers.

3.1.9.2	Customer

A customer of a utility, including customers who provide more power than they consume.

3.1.9.3	Demand Response Provider

An entity responsible for delivering demand reductions which is compensated in accordance with policy.

3.1.9.4	Distributor

A system which transfers energy from generation systems to consumers.

3.1.9.5	ISO

An Independent System Operator (ISO).

3.1.9.6	ISO or Grid Operator

An organization which manages the grid.

3.1.9.7	Large C/I Customer and Co-Generator

A customer whose usage typically exceeds a threshold and which is capable of providing electricity to the grid.

3.1.9.8	Metering Agent

Records the DR meter information during the time of the DR event onto persistent media.  Provides DR event meter data to the MDMS. Typically a smart meter.

3.1.9.9	Regulator

Public commission that approves demand response programs.

3.1.9.10	Scheduling Agent

Sometimes is an IOU and sometimes is independent operator who provides an estimate of system demand.

3.1.9.11	Settlement Agent

A system which provides the accounting services necessary to determine payments and bills for customers and energy providers including 3rd party aggregators.

3.1.9.12	Small-Scale Merchant Generator

A customer whose usage typically exceeds a threshold and which is capable of proving electricity to the grid.

Figure 3-16.  Primary Use Case Diagram

3.2	Manage Energy Resource

3.2-1	The DR solution shall manage demand resources.

3.2-2	The DR solution shall manage supply resources.

3.2-3	The DR solution shall manage resources which combine characteristics of supply and demand resources.  Resources which combine characteristics of both supply and demand include devices which can be controlled to either take or discharge load such as energy storage, pumped storage hydroelectricity, PEV batteries, compressed air systems, and new systems not yet developed.

3.2-4	The DR solution shall communicate with organizations that manage the grid. Organizations which manage the grid include ISOs, RTOs, and corporations such as TVA, BPA, and others.

3.2-5	The DR solution shall provide for load control provided by independent service providers.

3.2-6	The DR solution shall provide for load control provided by third party Aggregator of Retail Customers (ARC).

3.3	Manage Demand

3.3-1	The DR solution shall provide the capability to manage demand for grid reliability purposes.

3.3-2	The DR solution shall provide the capability to manage demand for economic reasons.

3.3-3	The DR solution shall provide the capability to manage demand for maintenance purposes.

3.3-4	The DR solution shall provide the capability to manage demand in response to price signals.

3.3-5	The DR solution shall provide the capability to specify the availability of resources for demand management on a daily basis.

3.4	Manage Demand for Economic Effect

3.4-1	 The DR solution shall provide the ability to manage economic effect programs. Economic effect is defined as the ability to reduce overall energy cost for example by trading load generation with load reduction.

3.4-2	The DR solution shall manage the transmission of economic cost information to third party aggregators.

3.4-3	The DR solution shall interact with customers to convey carbon usage information.

3.5	Manage Demand through Direct Load Control

3.5-1	The DR solution shall provide the ability to manage direct load control programs.

3.5-2	The DR solution shall manage the transmission of direct load control actions to direct-load-control-enabled devices.

3.5-3	The DR solution shall interact with customers to provide direct load control event notification. Studies indicate that customers want to know when direct load control measures are in effect.

3.5-4	The DR solution shall interact with customers to convey direct load control information.

3.6	Manage Demand for Maintenance Purpose

3.6-1	The DR solution shall provide the ability to manage load reduction to support maintenance programs. Load reduction to support maintenance programs reduces demand when resources, typically a circuit, are taken off-line and demand needs to be reduced to facilitate maintenance in the field.

3.7	Manage Demand in Respond to Pricing Signal

3.7-1	 The DR solution shall provide the ability to manage pricing signal programs designed to reduce load. Pricing signals are any type of dynamic pricing information including time-of-use (TOU), real-time pricing (RTP), and critical peak pricing (CPP) data distributed to customers either a day ahead or periodically during the day.

3.7-2	The DR solution shall manage the transmission of price signal information to DR-enabled devices.

3.7-3	The DR solution shall provide interact with customers to convey price signal information. Studies indicate that customers who understand the cost of electricity reduce their usage, especially when prices are high.

3.8	Manage DR Programs

Figure 3-17.  Manage DR Programs Use Case Diagram

3.8-1	The DR solution shall provide the ability to manage multiple DR programs.

3.8-2	The DR solution shall provide the ability to support customizable programs.

3.8-3	The DR solution shall provide the ability to manage programs which control demand.

3.8-4	The DR solution shall provide the ability to manage programs which control supply.

3.8-5	The DR solution shall communicate with the DR program administrator(s).

3.8-6	The DR solution shall manage existing demand response programs.

3.8-7	The DR solution shall manage new demand response programs.

3.8-8	The DR solution shall manage existing supply response programs.

3.8-9	The DR solution shall manage new supply response programs.

3.8-10	The DR solution shall manage existing load shifting programs. An example of a load shifting program includes pre-cooling air conditioning system. e DR solution shall manage existing load shifting programs.

3.8-11	The DR solution shall manage new load shifting response programs.

3.8.1	Administer Program

3.8.1-1	The DR solution shall manage multiple programs.

3.8.1-2	The DR solution shall allow customers to be in multiple programs.

3.8.1-3	The DR solution shall allow a program to be applied for all customers.

3.8.1-4	The DR solution shall allow a program to be applied to all members of a class of customers.

3.8.1-5	The DR solution shall allow a program to be applied for some but not all classes of customers.

3.8.1-6	The DR solution shall not force enrollment in any program.

3.8.1-7	The DR solution shall allow a program to be the default program for all customers.

3.8.1-8	The DR solution shall allow a program to be the default program for some but not all classes of customers.

3.8.1-9	The DR solution shall allow a program to be the default program for a class of customers.

3.8.2	Create DR Program

3.8.2.1	The DR solution shall support the creation of new DR programs. The DR program administer typically performs these steps to create a new program:

Determine the need for program

Do an analysis of the current load

Consider effects of regulations/coop rules /city board issues

Determine goals of program

Design DR program

Simulate the effect of the new program

Brief Senior Management & Acquire DR Prog. Approval

Brief regulators (PUC) /City board (city) /Owner board & USDA (coops) to receive approval

3.8.2.3	The DR solution shall simulate the predicted effect of a new program.   A typical sequence of steps used to simulate predicted effects of a new program is:

Determine need for program Do analysis of current load Consider effects of regulations/coop rules/city board issues Determine goals of program Design DR program Simulate effect of program Brief Senior Management & Acquire DR Prog. Approval Brief Regulators/City Board (city)/Owner board & USDA for Coops & receive approval

3.8.3	Delete DR Program

3.8.3-1	The DR solution shall support the removal of a DR program.

3.8.4	Enroll Customer

3.8.4-1	The DR Solution shall provide the capability to enroll customers in DR programs.

3.8.4-2	The DR Solution shall provide the ability to communicate with customers via multiple methods to enroll them in DR programs.  Typically, customers communicate with a customer service representative or a web portal interface to enroll in a program.

3.8.4-3	The DR solution shall communicate with the DR Program Administration to verify program enrollment eligibility.

3.8.4-4	The DR solution shall communicate with the DR Program Administration to request program enrollment eligibility.

3.8.4-5	The DR solution shall communicate with the DR Program Administration to check program enrollment eligibility.

3.8.5	Dis-enroll Customer

3.8.5-1	The DR Solution shall provide the capability to dis-enroll customers in DR programs.

3.8.5-2	The DR Solution shall provide the ability to communicate with customers via multiple methods to dis-enroll them in DR programs.  Typically, customers communicate with a customer service representative or a web portal interface to dis-enroll in a program.

3.8.5-3	The DR solution shall communicate with the DR Program Administration to verify program dis-enrollment eligibility.

3.8.5-4	The DR solution shall communicate with the DR Program Administration to request program dis-enrollment eligibility.

3.8.5-5	The DR solution shall communicate with the DR Program Administration to check program dis-enrollment eligibility.

3.8.6	Execute Program

3.8.6-1	The DR solution shall manage load reduction program execution.

3.8.6-2	The DR solution shall manage load shifting program execution. An example of load shifting includes thermal energy storage.

3.8.6-3	The DR solution shall manage programs which increase energy supply. Examples of programs which increase supply include auxiliary generators and discharging PEV batteries.

3.8.6-4	The DR solution shall manage programs which decrease the energy supply.

3.8.7	Manage Program Customer

3.8.7-1	The DR solution shall provide the capability to manage multiple customers.

3.8.7-2	The DR solution shall provide the capability to manage classes of customers.  Typical customer classes include industrial, commercial, agricultural and residential.

3.8.7-3	The DR solution shall provide the capability to add new classes of customers.

3.8.7-4	The DR solution shall provide the capability to delete a class of customers.

3.8.7-5	The DR solution shall provide the capability for customers in different customer classes to enroll in the same program.

3.8.7-6	The DR solution shall provide the capability to restrict programs to particular customer classes.

3.8.8	Measurement and Verification

3.8.8-1	The DR solution shall provide the ability to measure the load reduction from DR program execution.

3.8.8-2	The DR solution shall be able to estimate the predicted amount of load reduction for a DR program event.

3.8.8-3	The DR solution shall be able to calculate baseline usage for DR program participants.

3.8.8-4	During DR event execution, the DR solution shall be able to calculate the actual load reduction for some programs on a customer by customer basis.

3.8.8-5	During DR event execution, the DR solution shall be able to calculate the difference between the actual load reduction and the predicted load reduction for a geographic area.

3.8.8-6	During DR event execution, the DR solution shall be able to calculate the difference between the actual load reduction and the predicted load reduction for some individual customers.

3.8.8-7	During DR event execution, the DR solution shall be able to calculate the difference between the actual load reduction and the predicted load reduction at step down transformers.

3.8.8-8	During DR event execution, the DR solution shall be able to calculate the difference between the actual load reduction and the predicted load reduction at branch circuits.

3.8.8-9	During DR event execution, the DR solution shall be able to calculate the difference between the actual load reduction and the predicted load reduction at distribution feeders.

3.8.8-10	During DR event execution, the DR solution shall be able to calculate the difference between the actual load reduction and the predicted load reduction at substations.

3.8.8-11	The DR solution shall validate settlement in non-real time to correctly bill customers.

3.8.8-12	The DR solution shall provide the ability to validate the actual load reduction from DR program execution.

3.8.8-13	The DR solution shall provide the ability to store the load reduction from DR program execution on a customer by customer basis.

3.8.8-14	The DR solution shall provide the ability to determine the credit earned by customers enrolled in DR programs.

3.8.8-15	The DR solution shall provide the ability to determine penalties for customers who fail to meet specified levels of load reduction.

3.8.8-16	The DR solution shall provide the ability to determine the credit earned by customers who are by default covered by programs not requiring enrollment.

3.8.9	Read DR Program

3.8.9-1	The DR solution shall support reading of the DR program parameters.

3.8.10	Supply Interruptible Resource

3.8.10-1	The DR solution shall be capable of reducing load by providing interruptible power. Interruptible power is typically produced by generators.

A typical sequence of events to supply interruptible resources is:

1. ISO/Grid Operator releases event

2. ISO/Grid Operator selects DR resource to activate

3. ISO/Grid Operator submits to Scheduling Agent selected DR resource

4. Scheduling Agent posts schedule for DR resource

5. DR resource Provider executes DR event (provides)

6. DR resource Provider notifies customer of DR event

7. Customer acknowledges DR event

8. Customer provides DR resource

9. Customer reports DR resource status to DR resource provider

10. DR event ends (timeout or DR resource provider terminates event)

Figure 3-18.  Supply Interruptible DR Resource

3.8.11	Supply Non-Interruptible Resource

3.8.11-1	The DR solution shall have the capability to reduce load using non-interruptible resources.  Non-interruptible resources include geothermal, solar and wind. Non-interruptible resources are also called non-dispatchable resources.

A typical sequence of events to supply non-interruptible resources is:

1. DR provider submits DR bid to Scheduling Coordinator

2. Scheduling Coordinator validates DR bid

3. Scheduling Coordinator posts DR bid to ISO/grid operator

4. ISO awards and schedules DR resource

5. Scheduling Coordinator notified DR resource provider of award and schedule

6. DR resource Provider executes DR event (provides)

7. DR resource Provider notifies customer of DR event

8. Customer acknowledges DR event

9. Customer provides DR resource

10. Customer reports DR resource status to DR resource provider

11. DR event ends (timeout or DR resource provider terminates event)

Figure 3-19.  Supply Non-Interruptible DR Resource

3.8.12	Update DR Program

3.8.12-1	The DR solution shall support modifying of the DR program parameters.

3.8.12-2	The DR solution shall support common program parameters such as TOD, % reduction, amount paid to customers, maximum number of events which can be called, kWh to be reduced, credits earned per unit of reduction, etc.

A typical sequence of events to update a DR program is:

Determine need for changes Do analysis of current load Consider effects of regulations/coop rules /city board issues Determine goals of program Design DR program Simulate effect of program Brief Senior Management & Acquire DR Prog. Approval Brief Regulators/City Board (city)/Owner board & USDA for Coops & receive approval

3.8.13	Manage Statistics

3.8.13-1	The DR solution shall manage the collection of the percent of active devices which responded to a DR event.

3.8.13-2	The DR solution shall manage the collection of the percent of customers who responded to a DR event.

3.8.13-3	The DR solution shall manage the collection of the percent of customers who opted out of a DR event.

3.8.13-4	The DR solution shall manage the collection of the average response latency to a DR event.

3.8.13-5	The DR solution shall calculate statistics for the collected data.

3.8.13-6	The DR solution shall calculate statistics for the collected data including standard deviations.

3.9	Manage DR Customer

3.9-1	The DR solution shall manage customers for DR purposes.

3.9-2	The DR solution shall communicate with customers.

3.9-3	The DR solution shall manage existing customers.

3.9-4	The DR solution shall manage new customers.

3.10	Provision Demand Response Equipment

3.10-1	The DR solution shall manage the provisioning of active DR equipment.

Figure 3-20.  Provision Demand Response Equipment

3.10.1	Add DR Device

3.10.1-1	The DR solution shall manage the provisioning of new active DR devices.

3.10.1-2	If a DR device is capable of self-configuring on a network, then the DR solution shall be capable of commissioning the device into the DR program.

3.10.1-3	The DR solution shall maintain a database of all active DR devices.

3.10.1-4	The DR solution shall manage the provisioning of existing active DR devices.

3.10.1-5	The DR Solution shall validate the location of DR devices.

3.10.1-6	The DR solution shall manage the provisioning of new types of future DR devices.

3.10.1-7	The DR Solution shall be capable of adding DR device types.

3.10.2	Remove DR Device

3.10.2-1	 The DR solution shall maintain records of all active DR devices removed for a time period as defined by a regulatory agency.

3.10.2-2	The DR solution shall manage the decommissioning of existing DR devices.

3.10.2-3	The DR solution shall manage the removal of existing DR devices from a program.

3.10.2-4	The DR solution shall manage the removal of existing DR devices from a customer.

3.10.2-5	The DR solution shall manage the removal of existing DR devices from a list of premise equipment.

3.10.2-6	The DR Solution shall be capable of removing obsolete DR device types.

3.10.3	Read DR Device Information

3.10.3-1	 The DR solution shall read information from active DR devices.

3.10.3-2	The DR solution shall maintain the information read from active DR devices.

3.10.3-3	The DR solution shall manage changing the recording rate of selected meters on selected programs.

3.10.3-4	The DR solution shall manage changing the reporting rate of selected meters on selected programs.

3.10.4	Update Active DR Device

3.10.4-1	The DR solution shall be capable of updating active DR device information.

The DR solution shall maintain up-to-date information for all active DR devices.

3.10.4-2	The DR solution shall manage the updating of existing active DR devices.

3.10.4-3	The DR solution shall be capable of remotely updating active DR devices from the utility.

3.10.4-4	The DR solution shall be capable of remotely updating DR devices.

3.10.4-5	The DR solution shall validate updates of remote devices.

3.10.4-6	The DR solution shall be capable of updating the attached load.

3.11	Manage Supply

3.11-1	The DR solution shall manage the available supply of energy.  Attributes of energy supply include type of supply energy capacity, reliability, regulation amount of supply in mW, duration, number of times per day that it can be supplied.

3.11-2	The DR solution shall provide the capability to manage supply through price signals.

3.11-3	The DR solution shall provide the capability to manage supply through direct load control.

3.12	Manage Supplier

3.12-1	The DR Solution shall allow commercial customers to supply electricity to the grid.

3.12-2	The DR solution shall allow residential customers to supply energy to the grid.

3.13	Manage Supply through Price Signal

3.13-1	The DR solution shall provide the ability to manage pricing signal programs designed to increase supply.

3.13-2	The DR solution shall manage the transmission of price signal information to enabled devices.

3.13-3	The DR solution shall interact with customers to convey price signal information.

3.14	Manage Supply through Direct Control

3.14-1	The DR solution shall provide the ability to manage direct supply control programs.

3.14-2	The DR solution shall manage the transmission of direct supply control actions to direct-control-enabled devices.

3.14-3	The DR solution shall provide interact with customers to convey direct supply control information.

3.14-4	The DR solution shall interact with customers to provide supply event notification.

3.15	Provision Supply Response Equipment

3.15-1	The DR solution provisions equipment designed to increase supply. An example of equipment designed to increase supply is an additional meter which measures the output from a customer’s system which provides electricity to the grid. Another example would be a backup generator.

3.15-2	The DR solution shall be capable of adding a supply resource to a DR program.

3.15-3	The DR solution shall be capable of managing a supply resource.

3.15-4	The DR solution shall be capable of measuring a supply resource response to a DR event.

3.15-5	The DR solution shall be capable of verifying a supply resource response to a DR event.

3.15-6	The DR solution shall have the capability to manage multiple meters on a single customer site.

4.0	DR Event Class

This DR Event Class diagram shows the association between the main classes in one potential DRMS system decomposition.

Figure 4-1.  DR Event Class Diagram