Description:

Energy Management System integrates with the respective Home Area Network (HAN), and the Utility AMI system, and responds to commands to drop load for grid reliability, price responsive programs.

Use case business rules and assumptions:

See also “HAN Use Case - General Definitions, Assumption, Actors” document.

The EMS is aware of or can retrieve the types of HAN device types and the status of those devices connected to the HAN and upon registration or change-out. (e.g., fridge on/off)

EMS controls production, consumption and storage within the HAN. (e.g. Controls charging/discharging of an Electric Vehicle)

The EMS can be pre-programmed to respond to utility signals and commands. (e.g., reliability event)

Use case does not imply the utility’s preferred configuration or communication for reliability programs. (e.g., utility may still require HAN device registration)

Definitions:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

Actors:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

Scenario 1 (Price Response and Reliability Event):

Utility calls a DR event and controls load by communicating with the EMS through the Utility AMI gateway.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| The utility determines the need for a demand response event. | Energy Management System (EMS) | The Installation Use Cases are successfully completed. The Registration Use Cases are successfully completed. | EMS curtails load until event is concluded. |

Steps for this scenario

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | Utility | Utility sends notification of event and for price response case, the appropriate pricing information to the EMS. |
| 2 | EMS | The EMS sends a signal to all connected HAN devices and attempts to control consumption or production. |
| 3 | EMS | The EMS responds back with an acknowledgment message (e.g. customer override, load successfully dropped by x%, etc) to the AMI system. |
| 4 | AMI system | The AMI system sends a restore signal to the Utility AMI Gateway upon conclusion of the event. |
| 5 | Energy Management System | The EMS is restored to the pre-event state. |