Description:

The FHDMC connects with the premise Home Area Network (HAN), identifies itself and the account it is properly associated with the utility, where premise owner’s charges are reconciled.  This use case also describes the scenario documented in The Load and Energy Management Use Cases, in that the FHDMC may behave according to that use case. The following scenario is defined: bi-directional metering (i.e. distributed generation) and third-party (i.e. gas meter).

Use Case Business Rules and Assumptions:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

FHDMC have a certification process for meter accuracy as required by the utility or jurisdiction.

FHDMC may supply capabilities beyond basic metering (e.g. measurement, monitoring, and device state information).

AMI system may provide data to the FHDMC.

Definitions:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

FHDMC stands for “Fixed HAN Devices with Metering Capability”.

Use Case Actors:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

| Actor Name | Actor Type | Actor Description |
| --- | --- | --- |
| FHDMC | HAN device | A fixed-location child-metering device, downstream from the meter (i.e. point of service meter), that is communicated to via the HAN |
| Meter | Utility/HAN device | The point of service meter permanently associated with the unique premise applicable to this use case. |
| Premise | Location | The premise location where the meter is permanently located and where the FHDMC is located during the execution of this use case |

Scenarios (sequenced):

Scenario The following scenario addresses FHDMC, where bi-directional electric and third-party metering takes place.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| FHDMC is connected and enabled | FHDMC | The Installation Use Cases are successfully completed. The Registration Use Cases are successfully completed. | Device owner meters the device and gets billed for the appropriate amount on their electricity bill or other third-party bill. |

Steps for this scenario

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | FHDMC | Device indicates positive status of the communication link with the appropriate Utility AMI Gateway. |
| 2 | FHDMC | Device provides the customer (end user) with the appropriate information. (e.g. current rate of consumption, etc) |
| 3 | FHDMC | Device accumulates usage (delivered or received) and returns the information to the utility AMI gateway. |
| 4 | FHDMC | (optional) The device provides the utility AMI gateway with additional state information if applicable (e.g. state of charge of a storage device). |