Description:

The MHDMC connects with the premise Home Area Network (HAN), identifies itself and the account it is properly associated with the utility. MHDMC’s and premise owner’s charges are reconciled, as applicable.  This use case also describes the scenario documented in The Load and Energy Management Use Cases, in that the MHDMC may behave according to that use case.  The mobile (e.g. any customer PHEV/EV) scenario is defined in this document.

Use Case Business Rules and Assumptions:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

MHDMC has a certification process for meter accuracy as required by the utility or jurisdiction.

The MHDMC and premise are properly authorized to operate within the jurisdiction and utility.

AMI system may provide data to the MHDMC.

MHDMC records bi-directional MHDMC usage for audit purposes.

Definitions:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

MHDMC stands for “Mobile HAN Devices with Metering Capability”.

Use Case Actors:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

| Actor Name | Actor Type | Actor Description |
| --- | --- | --- |
| MHDMC | HAN device | A mobile child-metering device, downstream from the meter (i.e. point of service meter), that is communicated to via the HAN |
| Meter | Utility/HAN device | The point of service meter permanently associated with the unique premise applicable to this use case. |
| MHDMC Owner | Consumer | The person or organization responsible for MHDMC account |
| Premise | Location | The premise location where the meter is permanently located and where the MHDMC is located during the execution of this use case |

Scenarios (sequenced):

Scenario The following scenario addresses MHDMC, where bi-directional electric metering takes place.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| MHDMC is connected and enabled temporarily | MHDMC | The Installation Use Cases are successfully completed. The Registration Use Cases are successfully completed. | MHDMC owner and premise owner bills are properly reconciled. |

Steps for this scenario

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | MHDMC | Device indicates positive status of the communication link with the appropriate Utility AMI Gateway. |
| 2 | MHDMC | (optional) Device provides the customer (end user) with the appropriate information. (e.g. % of charge, current rate of consumption, etc) |
| 3 | MHDMC | Device indicates to the user whether the MHDMC is recognized by the utility (i.e. for billing purposes) |
| 4 | MHDMC | Device accumulates usage (delivered or received) and returns the information to the utility AMI gateway. |
| 5 | MHDMC | (optional) The device provides the utility AMI gateway with additional state information if applicable (e.g. state of charge of a storage device). |