| 366 | Zahra Makoui, PG&E | 54 | 1 | Shouldn't App.measure.7 be BF for AMI meter or Utility ESI and HAN meter? |  |
| --- | --- | --- | --- | --- | --- |

App.Measure.7 HAN Device shall allow interval configuration (e.g. 15 minutes).

Add the following new requirement:

App.Measure. xx HAN Device shall make its measurements available to other Registered HAN devices.

Doc editing team is Ok with these changes

The question arose this morning " did we state explicitly that logical ESI networks are distinct/independent?".  Some statements support that they are distinct but are perhaps not sufficiently explicit.  My research & suggested minor clarifications.

- ESI definition:  add to end:  Each ESI defines an independent logical network.

- Note: Registration definition is correct: " and among other devices Registered to that ESI"

- 2.2.1
The ESI provides a particular logical function in the HAN.  It is an interface which enables Secure Communications between authorized parties (e.g. Utility, Consumer, non-Utility Service Providers, EMS, etc.) and all HAN Devices that are Commissioned and Registered to it. The HAN architecture allows for more than one ESI in a Consumer premises. The Each ESI creates an independent logical segmentation within the premises.  This logical segmentation can be viewed as separate independent networks, each with its own security.:  the Utility network and all other networks. HAN Devices (e.g. EMS, internet gateway, etc.) which are active on multiple networks must have a logical separation between those networks. This does not preclude implementation of multiple logical networks existing on a common single physical network

- 2.2.2
The Registration process is a further step involving Mutual Authentication and authorizing a Commissioned HAN device to exchange secure information with a specific ESI and other HAN Devices Registered devices and with an to that ESI.  Registration creates a trust relationship between the HAN dDevice and thethat ESI and governs the rights granted to the HAN device in that ESI's network.

- Registration, p42 line 20
Initialization –The process of making the HAN device information (e.g. MAC address, security codes, etc.) available to the authentication service utilized by that ESI

- There may be additional Security items that inttersect with this issue but I see none that are in conflict.