Table __: Security Accountability Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Security.Account.1 | HAN Device shall alert the ESI of all detected, security-related activities, including access control, authentication, and integrity violations. | S | S | S | NA | S | S | S | S | S | S | S |
| Comments | What is the ESI going to do with the information? The device should take appropriate action if it detects a violation.( e.g. shut off communications for a period of time, notify consumer of attack and that energy info is not current) |  |  | NA | NA | NA | NA |  |  | NA | NA | NA |
| Security.Account.2 | HAN Device shall audit and store all security-related activities, including access control violations, authentication activities, etc. | S | S | NA | NA | S | NA | NA | NA | NA | NA | NA |
| Comments | This only makes sense it #1 makes sense. |  |  | NA | NA | NA | NA |  |  | NA |  |  |
| Security.Account.3 | HAN Device shall provide, at a minimum, the following information for all detected security events: date and time of the event, type of event, device/user identity. | S | S | S | NA | S | S | S | S | S | S | S |
| Comments | This only makes sense it #1 makes sense. |  |  | NA | NA | NA | NA |  |  | NA |  |  |
| Security.Account.4 | HAN Device shall provide the ESI access to audit data. | S | S | S | NA | S | S | S | S | S | S | S |
| Comments | This only makes sense it #1 makes sense. |  |  | NA | NA | NA | NA |  |  | NA |  |  |
| Security.Account.5 | HAN Device shall provide the ability to perform searches, sorts and filters of audit data based on date and time, type and/or user identity. | S | S | NA | NA | S | NA | NA | NA | NA | NA | NA |
| Comments | Most devices have limited UI therefore this is not |  |  | NA | NA | O | NA |  |  | NA |  |  |
| Security.Account.6 | HAN Device shall provide the capability to identify mandatory and configurable audit elements (In this context, mandatory refers to audit elements which are always enabled and configurable refers to audit elements which can be enabled or disabled at the discretion of the Consumer or Service Provider). | S | S | NA | NA | S | NA | NA | NA | NA | NA | NA |
| Comments | What is an audit element? |  |  | NA | NA | O | NA |  |  | NA |  |  |
| Security.Account.7 | ESI shall provide non-repudiation that a message was sent from the ESI to a HAN device.. | S | S | S | S | S | S | S | S | S | S | S |
| Comments |  |  |  | BS | BS | BS | NA |  |  | BS |  |  |
| Security.Account.8 | ESI shall provide non-repudiation that a reply was received from a HAN device back to the ESI. | S | S | S | S | S | S | S | S | S | S | S |
|  |  |  |  | BS | BS | BS |  |  |  | BS |  |  |
| Security.Account.9 | ESI shall provide a mechanism for source identification of data (e.g., HAN and AMI System data). | S | S | NA | NA | S | NA | NA | NA | NA | NA | NA |
|  |  |  |  | BS | BS | BS |  |  |  | BS |  |  |
| Security.Account.10 | ESI shall provide the capability to audit system policies. | S | S | NA | NA | S | NA | NA | NA | NA | NA | NA |
|  | What are the policies? |  |  |  |  |  |  |  |  |  |  |  |

# Comments

Assuming all items which require validation that data is genuine should receive an S, but only those involving control would alert the ESI.

PCT has load control

I don’t believe most end user devices need to log.

ESI should confirm message sends

ESI does not need to confirm all replies. Reply required for control elements and north bound systems.

OPT-IN/OPT-OUT Messaging may require this.

Required for Northbound systems and coordinators.