UCAIug Home Area Network System Requirements Specification

A Work Product of the OpenHAN Task Force of the SG Systems Working Group under the Open Smart Grid (OpenSG) Technical Committee of the UCA® International Users Group

Version 2.0 – ______   , 2010

© Copyright, UCA® International Users Group, All Rights Reserved

DISCLAIMER OF WARRANTIES AND LIMITATION OF LIABILITIES

THIS DOCUMENT WAS PREPARED BY A TASK FORCE OF THE UCA® INTERNATIONAL USERS GROUP COMPRISED OF INDIVIDUAL MEMBERS FROM MULTIPLE ORGANIZATIONS NAMED BELOW.  NEITHER THE UCA® INTERNATIONAL USERS GROUP, ANY MEMBER OF THE UCA® INTERNATIONAL USERS GROUP, THE PERSONS OR ORGANIZATION(S) NAMED BELOW, NOR ANY PERSON ACTING ON BEHALF OF ANY OF THEM:

(A)  MAKES ANY WARRANTY OR REPRESENTATION WHATSOEVER, EXPRESS OR IMPLIED, (I) WITH RESPECT TO THE USE OF ANY INFORMATION, APPARATUS, METHOD, PROCESS, OR SIMILAR ITEM DISCLOSED IN THIS DOCUMENT, INCLUDING MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE, OR (II) THAT SUCH USE DOES NOT INFRINGE ON OR INTERFERE WITH PRIVATELY OWNED RIGHTS, INCLUDING ANY PARTY'S INTELLECTUAL PROPERTY, OR (III) THAT THIS DOCUMENT IS SUITABLE TO ANY PARTICULAR USER'S CIRCUMSTANCE; OR

(B)  ASSUMES RESPONSIBILITY FOR ANY DAMAGES OR OTHER LIABILITY WHATSOEVER (INCLUDING ANY CONSEQUENTIAL DAMAGES, EVEN IF THE UCA INTERNATIONAL USERS GROUP OR ANY UCA® INTERNATIONAL USERS GROUP REPRESENTATIVE OR MEMBER HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES RESULTING FROM YOUR SELECTION OR USE OF THIS DOCUMENT OR ANY INFORMATION, APPARATUS, METHOD, PROCESS, OR SIMILAR ITEM DISCLOSED IN THIS DOCUMENT.

THE CONTENTS OF THIS DOCUMENT REPRESENT THE OPENHAN TASK FORCE MEMBERS BEST UNDERSTANDING OF THE HAN AT THE TIME OF COMPLETION.  THIS UNDERSTANDING EITHER COLLECTIVELY OR BY INDIVIDUAL MEMBERS MAY CHANGE OVER TIME.

Authors

The following individuals and their companies participated in the OpenHAN 2.0 Task Group and contributed substantially to the drafting of this document:

Acknowledgements

Ratification and Endorsement

Document History

Revision History

| Revision Number | Revision Date | Revision By | Summary of Changes | Changes marked |
| --- | --- | --- | --- | --- |
| 1.9 | 1-30-10 | Document Editing Team | Revisions were made to v1.04 by incorporating requirements from SEP2.0 MRD and Retail DR requirements from NAESB use cases | Yes for added requirements |
| 1.91 | 3-22-10 | Document Editing Team | Includes comments from BC Hydo, Itron, CenterPoint Energy, Oncor, People Power. Cisco, Google, Reliant Energy, I’m in Control, Trilliant, and GE | Yes |
| 1.915 | 4-28-10 | Document Editing Team | Includes comments from BC Hydo, CenterPoint Energy, Oncor, People Power. Google, Reliant Energy, I’m in Control, Trilliant, PG&E, Enernex, LBNL & DRRC, and GE | Yes; v1.91 comments reviewed and included in 1.915 up through Section 3.4.3 Processing |
| 1.95 | 5-21-10 | Document Editing Team | Added changes from the 2Q OpenSG F2F meeting and remaining v1.91 comments | Yes |

Contents

1.	Introduction	9

1.1	Purpose	10

1.2	Scope	11

1.3	Acronyms and Abbreviations	13

1.4	Definitions	13

1.5	Other Considerations and References	21

1.6	Security in the HAN Environment	23

1.7	Overview	25

2.	Overall Description	26

2.1	Guiding Principles	26

2.2	Architectural Considerations	33

2.2.1	Energy Services Interface (ESI)	33

2.2.2	Commissioning, Registration, Enrollment	34

2.2.3	Device Ownership	35

2.2.5	Cohabitation	36

2.2.6	Deregulated Electric Markets	36

2.2.7	External Interfaces	37

2.2.8	Special Applications	37

2.2.9	Architectural Scenarios	42

3.	OpenHAN System Requirements	46

3.1	Requirements Mapping to Logical Devices	46

3.1.1	Mapping Categories	46

3.1.2	Logical Device Types	46

3.2	Requirements Framework	47

3.3	Requirements Assumptions	53

3.4	Application Requirements	54

3.4.1	Control	54

3.4.2	Measurement and Monitoring	59

3.4.3	Processing	64

3.4.4	Human-Machine Interface	76

3.5	Communication Requirements	81

3.5.1	Commissioning	81

3.5.2	Control	86

3.6	Security Requirements	91

3.6.1	Access Controls and Confidentiality	91

3.6.2	Integrity	93

3.6.3	Accountability	94

3.6.4	Registration	96

3.6.5	Enrollment	102

3.7	Performance Requirements	104

3.8	Operations, Maintenance, and Logistics Requirements	112

3.8.1	Manufacturing and Distribution	112

3.8.2	Installation	116

3.8.3	Manage, Maintain	118

4.	Appendices	123

4.1	Use Cases	123

4.1.1	Other Use Cases and Documents Reviewed	123

4.1.2	UCAIug OpenHAN Task Force Use Cases	124

4.1.3	Definitions / Assumptions / Actors	125

4.1.4	Use Case Assumptions	125

4.1.5	Load and Energy Management	127

4.1.6	Energy Management System	134

4.1.7	User Information	136

4.1.8	Energy Storage and Generation	138

4.1.9	Fixed HAN Devices with Metering Capability	139

4.1.10	Mobile HAN Device with Metering Capability	140

4.1.11	System Configuration and Management	142

4.2   HAN Security Considerations	155

# Introduction

In 2007, the UtilityAMI established the OpenHAN Task Force to develop guiding principles, use cases, and platform independent requirements for the utility Advanced Metering Infrastructure (“AMI”) home-area-network (“HAN”). The core development team included more than a dozen investor-owned North American utilities serving more than 28 million electric and gas customers in 17 states and provinces, as well as contributors from EnerNex Corporation, Tendril Networks, Mulligan Labs, LLC, Itron, and Silver Spring Networks.  The OpenHAN Task Force collaborated throughout 2007 and 2008 to draft the UtilityAMI 2008 Home Area Network System Requirements Specification and received ratification of v1.04 in August 2008 (“UtilityAMI 2008 HAN SRS”).

Since August 2008, additional HAN related use cases were developed and the UCAIug OpenSG Technical Committee re-established the OpenHAN Task Force under the SG Systems Working Group in October 2009.  The OpenHAN Task Force was directed to begin work on the next version of the HAN SRS document, i.e. UCAIug HAN SRS v2.0. The work to produce this document was a collaborative effort with meetings open to all interested parties.  Those that participated in developing this document include utilities, energy service providers, vendors, appliance manufacturers, software developers, etc.

The following conceptual diagram provides a high-level perspective of the Smart Grid providing a tool for identifying actors and possible communications paths. The red circle represents the area of focus for this OpenHAN SRS document.

Figure 1 NIST Conceptual Reference Diagram for Smart Grid Information Networks

This document consists of four sections:  Introduction, Overall Description, System Requirements, and Appendices.

Section 1 describes the purpose, scope, and policy directives that have shaped the HAN SRS.  Section 1 also includes a comprehensive list of acronyms and definitions to help the reader interpret the HAN SRS.

Section 2 describes the overall premises energy ecosystem, the guiding principles for the system and architectural considerations relevant to understanding the system.

Section 3 gives context for and lists all platform-independent OpenHAN system requirements by category but does not map them to specific logical devices.  The requirements categories are:

- Application

- Communication

- Security

- Performance

- Operations, Maintenance, and Logistics

Section 4 contains the appendices, which include high-level system use cases, requirements mappings to logical HAN Devices, and deployment scenario examples.

Although this document is a system requirements specification, it follows the IEEE 830-1998 Recommended Practice for Software Requirements Specifications given the focus on Home Area Network (HAN) applications for utilities and consumers.

## Purpose

One of the key outcomes of Smart Grid deployments is enabling informed participation by end-use consumers in retail and wholesale electricity markets. When consumers are given timely information about their electrical usage, this will empower them to manage their electricity usage, promote energy efficiency, and lower overall energy costs. Home Area Networks will play a role in achieving these goals by giving consumers more information than they have ever had before on how they use electricity and the cost of their usage. In addition, by using interoperable standards utilities, device manufactures, vendors, and energy service providers can develop innovative and cost effective solutions and products which help consumers manage, optimize, and control their electricity usage.

To reach these goals and to bring the benefits of the Smart Grid to consumers, the OpenHAN Task Force undertook the development of the initial version of the OpenHAN SRS, the UtilityAMI 2008 Home Area Network System Requirements Specification v1.04 (“UtilityAMI 2008 HAN SRS”).  By providing common architectures, language, and requirements, the use of the UCAIug OpenHAN SRS 2.0 will ensure a competitive market place by driving down costs, increasing interoperability, and maximizing longevity and maintainability.

Utilities interested in AMI deployments with two-way communication into the premises are encouraged to use and include sections of this document when evaluating or procuring AMI systems that interact with HANs.

The purpose of this HAN SRS is to:

- Define the system requirements for an open standard Home Area Network system

- Promote open standards-based HANs that are interoperable

- Provide the vendor community with a common set of principles and requirements around which to build products

- Ensure reliable and sustainable HAN platforms

- Support various energy policies in a variety of states, provinces, and countries

- Empower consumers  to manage their electricity consumption by giving them the information and control they need to make decisions on their energy use and to effectively control their  energy consumption

The audience for this HAN SRS is:

- Utilities considering deploying AMI systems that interact with HANs

- Vendors that make AMI systems for Utilities that interact with HANs

- Vendors that make consumer products (e.g. programmable communicating thermostats, energy management systems, load control switches, in-home displays, smart appliances, PEVs, distributed energy resources, etc.)

- Service Providers developing smart grid enabled programs for consumers (e.g. demand response, energy management, pre-pay, PEV programs, distributed energy resources , etc.)

- Policy makers looking to understand how Utility AMI deployments benefit  consumers

- Industry alliances and standards organizations

- NIST Smart Grid Interoperability Panel (SGIP) activities (e.g. Smart Grid Architectural Committee (SGAC), Cyber Security Working Group (CSWG), Smart Grid Testing and Certification Committee (SGTCC), etc.)

As AMI and HAN systems continue to evolve, the UCAIug OpenHAN TF maintains an open door policy and encourages all interested parties (e.g. utilities, regulators, service providers, software vendors, original equipment manufacturers, etc.) to join the discussion.

## Scope

This document includes Guiding Principles, Use Cases, System Requirements, Architectural Drawings, and Logical Device Mappings for platform-independent HAN Devices regardless of the ownership of the devices. This document provides platform-independent requirements and systems that Service Providers, Utilities, and vendors can use regardless of the technology they select.

This SRS does not apply to, but has inherent implications for, certain Utility Enterprise Systems (e.g. Utility AMI communications network, Meter Data Collection and Management Systems, etc.), which are beyond the Customer domain.  It also does not apply to devices in the premises that are not part of the Home Area Network, as defined in this document (described in more detail in Section 2.2 – Architectural Considerations).  Some examples of these devices not covered in the scope of this specification are home automation, home health monitoring, and security system products.

While the residential consumer has the most to gain from the HAN SRS, the requirements in this SRS are applicable and may be used by commercial and industrial consumers as well.

As developed through Guiding Principles, Use Cases, and System Requirements, this SRS establishes the initial requirements and framework for the development of well managed and secure HAN communications systems.  This is important and necessary given the increased risk to the electricity grid by the installation of in-premises HAN Devices (e.g. gateway, Energy Management System, etc.) that can engage in two-way communications using more than one communication media (e.g. Utility AMI network, internet, cell phone network, etc.) and may be commissioned to multiple ESIs (e.g. Utility ESI, third party ESI).  As part of the Utilities’ mandate to ensure a reliable electricity supply, security requirements have been included in this specification.

## Acronyms and Abbreviations

This subsection provides a list of all acronyms and abbreviations used in this document.

.

| AMI | Advanced Metering Infrastructure |
| --- | --- |
| CPP | Critical Peak Pricing |
| CSS | Customer Service System |
| DER | Distributed Energy Resources |
| EMS | Energy Management System |
| ESI | Energy Services Interface |
| ESU | Energy Supplying Unit |
| EUMD | End-Use Measurement Device |
| EVSE | Electric Vehicle Supply Equipment |
| FHDMC | Fixed Home Area Network Devices with Metering Capability |
| HAN | Home Area Network |
| HMI | Human / Machine Interface |
| IHD | In-Home Display |
| ISO | Independent System Operator |
| MHDMC | Mobile Home Area Network Devices with Metering Capability |
| PCT | Programmable Communicating Thermostat |
| PEV | Plug-in Electric Vehicle |
| SRS | System Requirements Specification |
| TOU | Time of Use |

## Definitions

This subsection provides the definitions of all terms used in this document.

| Active Event | Refers to an event (e.g. demand response, price, emergency, etc.) that is underway |
| --- | --- |
| Advanced Metering Infrastructure (AMI) | Advanced Metering Infrastructure refers to systems that measure, collect, and analyze energy usage from advanced devices (e.g. electricity meters, gas meters, and/or water meters), through various communication media on request (i.e. on-demand) or on a pre-defined schedule. This infrastructure includes hardware, software, communications, Customer Service Systems, meter data management software, metering system, network distribution business systems, Utility Energy Services Interface, etc. In some jurisdictions this may be call the Advanced Metering System (AMS) |
| Audit | A methodical examination or review of a condition or situation within a Home Area Network Device |
| Capacity Billing Rates | Demand charges based in the rate of consumption (e.g. kWh demand, cubic feet per minute) |
| Charging Interval | The period of time that is bound by a start and stop of charging |
| Commissioning | The process by which a HAN device obtains access to a specific physical network and allows the device to be discovered on that network. The process may involve the exchange of link keys or other security related information required to establish network coordination, assign device addresses and to route packets. Admission to the network allows the HAN device to communicate with peer devices on a network and receive public broadcast information from an ESI, but not secured information. |
| Consumer | A person who consumes electricity, natural gas, water, or other utility and who has the greatest potential to conserve and manage the consumption of those utilities. The Consumer may participate in Service Provider programs (e.g., Demand Response, pricing, PEV programs, pre-pay, pricing, etc.). Consumers may also manage demand response events and daily usage by controlling HAN Devices manually or via other devices (e.g. EMS, etc.). Consumers are distinct from Customers because the Consumer of the Service Provider isn’t always the Service Provider Customer that pays for the consumption or enrolls in a program. |
| Consumer Override | Refers to a consumer adjusting the functional behavior of a device to ignore or modify a Service Provider’s control messages |
| Control Signal | A signal from an authorized party (e.g. Utility, Service Providers, EMS, Consumers, etc.) that requests a change in the operational state of a device (e.g. on, off, cycle, energy saving mode, etc.) for a configurable time interval. |
| Critical Peak Pricing | A monthly or seasonal schedule of energy charges which vary based upon a predetermined schedule of hours of the day and days of the week. In addition, the Consumer receives real-time notification of critical hours subject to special higher prices for a small percentage of the hours in the year. |
| Customer Representative | Person or intelligent system with which the Consumer interacts to work with a business (e.g., Utility, Service Provider, demand response aggregator, etc.) |
| Customer Service System | A system (e.g. system used by the call center) that provides Service Provider employees the ability to view Consumer-specific information (e.g. account information, billing, tariffs, programs, metering, interval usage, etc.). In some case this system is also called a CIS (Customer Information System). |
| Demand Response | A temporary change in electricity consumption by a demand resource (e.g. PCT, smart appliance, pool pump, PEV, etc.) in response to a control signal which is issued due to market or reliability conditions. For purposes of this document, Demand Response does not include energy efficiency or permanent Load reduction. |
| Direct Load Control / remote load control | A Demand Response activity by which the Service Provider remotely shuts down, cycles, or reduces the load of a consumer’s electrical equipment (e.g. air conditioner, water heater, smart appliances, etc.). |
| Distributed Energy Resources (DER) | Small, modular, energy generation and storage technologies that provide electric capacity or energy where it is needed. May also be referred to as Distributed Generation. |
| Dynamic Pricing | Time-varying retail pricing of electricity that usually involves the capabilities of advanced meters and reflects fluctuations in grid conditions or the wholesale electricity prices on short notice, such as an hour or day in advance. |
| Electric Vehicle Supply Equipment (EVSE) | The physical electrical cord and connectors that are specified by applicable SAE (Society of Automotive Engineers) standards that provide transfer of electric energy from the charging point to the PEV. The PEV connects to the electricity supply using an EVSE. The EVSE may contain HAN communications capability. |
| Emergency Event | An Independent System Operator or Utility initiated reliability event requesting consumers to reduce peak load (e.g. high priority request prior to a system outage). |
| End-Use Measurement Device (EUMD) | The device that measures energy usage from an end-device (e.g. PEV, DER, appliance, etc.) |
| Energy Cost Application | Calculates HAN Device energy consumption cost. The application may use information from multiple sources including: AMI meter(s), the AMI System, other application(s), other Home Area Network Device(s), Human Machine Interface(s), etc. |
| Energy Management System (EMS) | An application used for controlling multiple energy-controllable devices (e.g., pool pump, Programmable Communicating Thermostat, light switches, PEV charging, etc.). This application may reside within a HAN Device (e.g. Programmable Communicating Thermostat, In-Home Display, computer, cable set-top box, other computing device, etc.). This application may also control other devices or systems in the home providing integrated automated services for the Consumer. |
| Energy Services Interface (ESI) | A secure interface to a premises communications network which facilitates relevant energy applications (e.g. remote load control, demand response, monitoring and control of DER, in-premises display of customer usage, reading of energy and non-energy meters, PEV charging and roaming coordination, and integration with energy management systems, etc.), provides auditing / logging functions that record transactions to and from HAN Devices, and, often, coordination functions that enable secure transactions between the HAN Devices Commissioned and Registered on its network and Enrolled in a Service Provider program. Note: There may be more than one ESI in a premises or more than one ESI in a HAN Device. |
| Energy Supplying Unit (ESU) | An energy storage device (e.g., battery storage unit, electric vehicle battery) capable of providing power to a premises or the electric grid |
| Enrollment | The process by which a Consumer enrolls a HAN device in a Service Provider’s program (e.g. demand response, energy management, pre-pay, PEV programs, distributed generation programs, pricing, messaging, etc.) and gives certain rights to the Service Provider to communicate with their HAN device. |
| External Interface | Provides the HAN with access to a communication network outside of the customer domain. A Utility ESI, third-party ESIs, and gateways that connect to external communication networks (e.g. Utility AMI communication network, internet, cell phone network, etc.) are examples of external interfaces. |
| Fixed Home Area Network Devices with Metering Capability | A HAN device which does not have mobility (i.e. DER, etc.) and includes measuring capability. |
| Home Area Network (HAN) | Within the scope of this SRS, a HAN is an energy related network used for communicating with devices within the premises. HANs do not necessarily require connectivity outside the premises, but may be connected to one or more external communication networks (e.g. Utility AMI, internet, cell phone network, etc.) using gateways, bridges and interfaces. |
| Home Area Network Device (HAN Device) | Within the scope of this specification, any device that communicates on the HAN |
| HAN System | A collection of devices, actions, communications capability and processes which enable a HAN to operate in a premises. |
| Dynamic Energy Rate | Energy charges based upon market conditions which vary on an hourly or less than hourly basis. This may include real-time pricing or Dynamic Pricing |
| In-Home Display | A HAN Device that receives and displays data. |
| Independent System Operator | Coordinates controls and monitors the operation of the electrical power system, usually within a single US State, but often encompassing multiple states |
| Installer | The entity who installs and at a minimum Commissions a Home Area Network Device in the Consumer’s premises; Installer may be a 3rd party or the Consumer |
| Labeling | Compliance, safety, and standards labeling |
| Least Privilege | The concept of least privilege is to operate using the least set of privileges necessary to complete a given task. The ultimate goal is to eliminate damage that can occur from accidental errors or malicious intent. |
| Manufacturer | Defined broadly to include Original Equipment Manufacturers, Distributors, and Value-added retailers and is accountable for ensuring proper out-of-box operation of the HAN device |
| Measure | Determination of dimension, quantity, or capacity |
| Meter | A device whose primary function is to measure, record, and communicate usage and/or production of a commodity (e.g. electricity, water, gas, etc.) for an individual device or the customer’s premises. |
| Mobile Home Area Network Devices with Metering Capability (MHDMC) | A mobile end-use meter, downstream from the premises’ electric meter (i.e., point of service meter), that is communicated to via the Home Area Network (e.g.,PEV with an onboard EMUD) |
| Mobile Home Area Network Devices with Metering Capability Owner | A Consumer who is the person or organization responsible for Mobile Home Area Network Devices with Metering Capability account |
| Mode | A condition of the operational state (e.g., charging, discharging, power save) of a device |
| Monitor | A device or arrangement for observing, detecting, or recording the operation of a machine or system |
| Mutual Authentication | A process in which both entities in a communications link authenticate each other |
| Network Management | The ability to remotely diagnose system components, and to monitor and control the communication system |
| Orphaned Charge | A billing charge that is incurred by a Mobile Home Area Network Device with Metering Capability at a premises other than its registered, “home” premises, which has yet to be reconciled through the Service Provider billing system and associated with the proper customer account (e.g., a PEV that charges at a grocery store or at a friend’s house). |
| Pending Event | Refers to an event (e.g. demand response, emergency, etc.) that is scheduled but has not yet happened |
| Plug-in Electric Vehicle (PEV) | An electric vehicle that may solely rely on electric propulsion (EV) or may include an alternative source of propulsion power (PHEV). |
| Pool Pump Controller | The controller is a separate device that resides between the timer and the pool pump, has minimal intelligence, and sends and receives signals through the Home Area Network |
| Pre-Commissioning | Custom configuration of a device done prior to HAN device installation |
| Premises | A geographical location (e.g., house, apartment, building, etc.) with which the meter is permanently associated. |
| Price Event | An event (e.g. demand response, emergency, etc.) based upon price |
| Programmable Communicating Thermostat (PCT) | A thermostat that can communicate with the HAN |
| Rate Tiers/Blocks | Energy charges which vary based on the accumulated consumption / production during a period of time |
| Registration | The process by which a Commissioned HAN device is authorized to communicate on a logical network. This involves the exchange of security credentials with an ESI. The registration process is required for the exchange of secure information between a Registered device and the ESI and among other devices Registered to that ESI. |
| Remote Upgrade | The ability to correct defects, enable new features and applications, change recording and reporting intervals, refresh security, and optimize network operation from an external location in a secure manner |
| Secure Communications |  |
| Security | Those measures that protect and defend information and information systems by assuring their confidentiality, integrity, access controls, availability, and accountability |
| Service Point Location | Uniquely identifies the service delivery point |
| Service Provider | An entity (e.g. Utility, retail electric provider, demand response aggregator, etc.) which provides energy services to Consumers |
| Smart Appliance | A white good or household appliance, that has HAN communication capability and is capable of receiving signals from authorized parties (e.g. Utility, Service Provider, EMS, Consumer, etc.) and of adjusting its operational mode based on Consumer preferences (e.g. energy saving mode, delayed turn on/off) |
| State | A condition of the device (i.e., on/off) |
| System Operator | The entity responsible for operation and control of the electricity grid for a specific and defined geographic / service area |
| Time of Use Rates | Energy charges which vary based upon a predetermined schedule of hours of the day and days of the week |
| Time of Day Demand Rates | Demand charges which vary based upon a predetermined schedule of hours of the day, days of the week, and seasons of the year |
| Utility Public Broadcast Channel | Utility Public Broadcast Channel is one-way communication to HAN devices of information which is publicly available and of general interest to all consumers (e.g. energy conservation, environmental awareness, etc.) |
| Utility | The electric service provider, which, at a minimum, is responsible for reading the electric meter, providing HAN access to the meter, and delivering energy to the consumer. This may be an integrated electric utility or a Transmission and Distribution utility. |
| Utility Enterprise System | Includes Advanced Metering Infrastructure system, Distributed Automation, and all other enabling technologies of the Utility operation |
| Utility Energy Services Interface | An ESI, owned by the Utility, which enables secure interactions between HAN Devices commissioned on its network and the Utility AMI. |

## Other Considerations and References

The development of the UtilityAMI 2008 HAN SRS was motivated by legislative and regulatory policy directives and the proliferation of multiple technology standards for HANs. Regulatory policy directives played a key role in pushing Utilities to deploy AMI systems that provide consumers with more detailed energy consumption information and demand-reduction capabilities, including the California Public Utilities Commission Energy Action Plan and AMI Directives, the California Energy Commission J45 Reference Design for Programmable Communicating Thermostats (PCTs), the Public Utility Commission of Texas (PUCT) Advanced Metering rule, and the Michigan 21st Century Energy Plan. Another motivating factor driving the development of the UtilityAMI 2008 HAN SRS was to guide and direct the alliances who are responsible for developing HAN technology standards by providing a standard set of requirements. The UtilityAMI OpenHAN TF also leveraged the work of Electric Power Research Institute and the GridWise Architecture Council. These organizations provided a template and a foundation which was used to approach the development of the UtilityAMI 2008 HAN SRS.

Since the ratification of the UtilityAMI 2008 HAN SRS in August 2008, the national focus and attention on the Smart Grid, especially as it relates to enabling informed participation by end-use customers, has been intensified. The Energy Independence and Security Act of 2007 (ESIA) made the development of a Smart Grid a national policy goal. ESIA authorized DOE to solicit applications for the Smart Grid Investment Grant Program (SGIG) and assigned the National Institute of Standards and Technology (NIST) the responsibility to coordinate the development of an interoperability framework between Smart Grid devices and systems that is “flexible, uniform and technology neutral”. In February 2009, the U.S. Congress passed the American Recovery and Reinvestment Act (“ARRA”), which provided funding for DOE Smart Grid grants, other DOE incentives, and NIST for NIST to fulfill its ESIA obligations.

In 2009 NIST began its work and by January 2010 NIST published the NIST Framework and Roadmap for Smart Grid Interoperability Standards, Release 1.0. In this framework document, NIST recognized the UtilityAMI 2008 HAN SRS as a set of requirements for the Smart Grid data communications interface to customer devices.  The UtilityAMI 2008 HAN SRS sets forth the requirements for secure communication between the Distribution and Customer domains and between the Service Provider and Customer domains as graphically depicted in Figure 2 of the NIST conceptual reference model.

Figure 2 Interaction of actors in different Smart Grid Domains through Secure Communication Flows and Electrical Flows.

In mid 2009, DOE issued the Smart Grid Investment Grant (SGIG) Program Funding Opportunity with specific goals including enabling informed participation by consumers in retail and wholesale electricity markets, enabling new products, services, and markets, and optimizing asset utilization and operating efficiency of the electric power system. Reimbursement for project expenditures was contingent upon a project’s compliance with relevant technical standards and the project’s support for and compatibility with NIST’s emerging smart grid framework for standards and protocols. DOE selected 100 projects to fund and many of those projects include providing customers usage information, dynamic pricing, demand response programs, smart appliances, and in home displays.  Use of the OpenHAN SRS by these utilities and vendors will help them meet the DOE standards requirement, to further the development of Smart Grid functions, and bring the benefits of the Smart Grid to consumers.

The Department of Energy has also funded projects to demonstrate advanced Smart Grid technologies and integrated systems that will help build a smarter, more efficient, more resilient electrical grid. The Smart Grid Demonstration Grants (SGDGs) provided funding for thirty two demonstration projects, which include large-scale energy storage, smart meters, distribution and transmission system monitoring devices, and a range of other smart technologies. These projects are to act as models for deploying integrated Smart Grid systems on a broader scale.

## Security in the HAN Environment

The Smart Grid enables the two-way flow of information between devices in a Consumer’s premises, which are connected to an energy Home Area Network (HAN), and a Service Provider’s network.  This type of communication is a new technology being introduced to the electric power grid through the deployment of Advanced Metering Infrastructure (AMI) systems, including smart meters, and HAN devices. Since bi-directional communication with HAN devices involves the flow of information through various networks it is necessary to have proper security measures in place to reduce the risk of intrusion, eavesdropping, and transmitting unwanted content. In addition, each HAN device as a node on the network has the potential to host, transmit, and receive unwanted content. Security in the HAN is a balance between securing the bi-directional communications, ensuring Consumer privacy while allowing access to the relevant stakeholders, and manufacturing cost effective HAN devices. Emerging threat and attack vectors make cyber security an ongoing evolutionary process. Due to the ever-changing landscape within cyber security, it will be necessary to review and modify standards and controls regularly.

When determining the appropriate security requirements, the Smart Grid Interoperability Panel (SGIP) Cyber Security Working Group (CSWG) recommends performing a security risk assessment, including identifying vulnerabilities, impacts, and threats, from a high-level overall functional perspective. The primary goal, as stated by CSWG, should be on prevention.  The output of this type of risk assessment becomes the basis for the selection of security requirements and the identification of security requirements gaps. The OpenHAN Task Force (TF), in conjunction with UCAIug SG Security Working Group, evaluated the security risks associated with the HAN to determine if adequate security requirements are included in the OpenHAN SRS (see Appendix 4.2). The results of this evaluation provide justification for the selection of security controls that support cyber security objectives as defined by stature:

Confidentiality

“Preserving authorized restrictions on information access and disclosure, including means for protecting personal privacy and proprietary information…” [44 U.S.C., Sec. 3542]

A loss of confidentiality is the unauthorized disclosure of information.

Integrity

“Guarding against improper information modification or destruction, and includes ensuring information non-repudiation and authenticity…” [44 U.S.C., Sec. 3542]

A loss of integrity is the unauthorized modification or destruction of information.

Availability

“Ensuring timely and reliable access to and use of information…” [44 U.S.C., SEC. 3542]

A loss of availability is the disruption of access to or use of information or an information system.

The levels of potential impact for each security objective are denoted as low, moderate, or high and are defined in FIPS 199. In addition, the OpenHAN TF and the UCAIug SG Security Working Group reviewed the security requirements identified by the CSWG as applicable to the HAN and compared them with the OpenHAN SRS security requirements to determine if any gaps existed.

## Overview

This document follows a top-down approach to system decomposition and conforms to the GridWise Architecture Council’s framework as shown in the figure below: This figure also provides the layout for the rest of this specification following the top-down approach.

# Overall Description

The UCAIug HAN SRS provides the foundation of the home energy ecosystem in which HAN Devices operating within a premises are able to engage with the Service Provider as much or as little as the Consumer wishes. The HAN may be deployed in different physical environments (e.g. multi-dwelling units, large single or two story house, strip mall, etc.).

This section defines the Guiding Principles the OpenHAN Task Force adopted to frame the capabilities and constraints of the system, the Architecture for HAN Device interaction with the Service Provider that permits a highly adaptable and flexible system depending on consumer preference, and the assumptions for the system used as a starting point for drafting the Use Cases and Requirements found in Appendix 4.1 and Section 3, respectively.

## Guiding Principles

The Guiding Principles represent high level expectations used to guide and frame the development of the functional and technical requirements in this document.  These expectations include the capabilities which are necessary to support policy directives, interoperability, and smart grid functionality.

The principles are authoritative and define the HAN implementation starting point. A complete implementation will provide technical methods and processes which meet or exceed a stated capability and adhere to the stated constraints.  These principles, as stated, drive and define the functional characteristics and are the basis for the HAN Use Cases.

- Secure Two-way Communication Between HAN Devices and Service Provider(s)

Description

HAN devices, including AMI meters, must be capable of connecting to a communications network. By utilizing an Energy Services Interface (ESI), HAN devices and Service Provider(s) gain the ability to engage in secure two-way communications.

As such, the ESI and communications network may carry various types of data, including sensitive, confidential, and control data. Security and privacy protections are paramount; therefore appropriate levels of protection must be provided for these types of communications.

Rationale

Fundamental HAN capabilities (e.g. real-time monitoring, dynamic pricing, demand response programs, PEV programs, etc.) are possible when a secure two-way communication path between Service Provider(s) and HAN devices is present. The ESI is the critical component that makes this secure communication possible.

- Supports Load Control Integration

Description

Load control is the concept of load being managed (e.g. deferred, eliminated, cycled, reduced, etc.). A load control device (e.g. PCT, Smart Appliance, pool pump controller, EMS, etc.) has the capability to reduce the peak power consumption of the equipment under its control. These devices within the Consumer’s premises can be used to reduce load through direct and indirect control.  Control signal execution should not in anyway compromise safety systems built into HAN Devices or compromise the ability of the HAN Device to complete the task previously initiated.

Rationale

A capability to interface and integrate with load control systems improves the operational efficiency of the electrical distribution system, and as such, it is critical that this capability be enabled within the HAN. This also enables the Service Provider to offer various programs that help consumers adjust their energy usage based on events external to the consumer (such as grid demand stress or generation failure). Enabling load control integration via the HAN will provide consumers with more choices with respect to energy management and energy management services.

- The AMI meter provides the HAN with direct access to Consumer-specific usage data

Description

The AMI meter provides the HAN with access to Consumer-specific usage data (e.g. instantaneous usage, interval usage, volts, Amps, VAr, Power Factor, etc.)which enables a new class of energy services and products.

Rationale

One of the main requirements for energy management and conservation is a better informed Consumer.  By providing Consumers with more timely and detailed usage information, Consumers will be able to make informed choices about when and how they consume energy. Applications may use the usage data to automatically optimize premises consumption (e.g. EMS, PEV programs, pool pump, PCT, etc.). With direct access to usage data, Consumers need not wait until the end of the month to get an indication of how their bill is affected by their choices in energy consumption.  Since the energy usage from the AMI meter is recorded in shorter time intervals, the Consumer can more readily observe the impact of changing energy usage patterns.

- Provides a Growth Platform for Future Products Which Leverage the HAN and Meter Data

Description

A growth platform is typically an opportunity identified as providing value to consumers and thereby providing business opportunities.  The HAN is an example of a strategic growth platform. Strategic growth platforms are longer term initiatives where the initiative and results span years.  While AMI enables the Utility to exchange information with a HAN via the Utility ESI, the growth platform is not limited to the Utility, but extends to any organization that wants to develop products or services leveraging the HAN and meter data.

Rationale

The HAN environment enables a new class of energy services and products and  is expected to support many innovative applications and devices, including the next generation of applications (e.g. DER, PEV programs, Smart Appliances, EMS, other energy applications, etc.) as the technology, information, and communication capabilities of the HAN mature.  By supporting open standards (see Principle 9), it is expected that many Service Providers and vendors will be able to expand the capabilities of the HAN by developing innovative products for this emergent HAN market.

- Supports Three Types of Messaging: Public, Consumer-Specific, and Control

Description

To support the anticipated growth in the HAN market, the system must provide for various types of messaging.  These message types may include public, consumer-specific, and control messaging.  Public messaging is the communication of material which is publicly available and of general interest to all or a large identifiable subset of consumers. Consumer-specific messaging is information which is specific to a consumer. Contents of these types of messages might include usage, pricing, billing, load control, etc..  Control Messaging is used to support applications such as load-reduction, demand response, load limiting, etc. (see Principle 2).

Rationale

Each message type is required to support the HAN as a growth platform (see Principle 4).  Each message type warrants individual security and privacy analysis and treatment. Consumer-specific information messaging implies a level of privacy and additional privacy measures and methods are warranted.  Demand Response messaging for load control is a special use of the system and as such, requires robust handling methods.  This capability expectation is based on Service Provider accountability for reliable and secure delivery of the control signal.

- Supports End-Use Metering and other Utility Meters

Description

End-use metering is when an additional meter may be installed in the premises to record DER production or to measure discrete loads (e.g. PEV, etc.). DER systems are small-scale power generation technologies used to provide an alternative to or an enhancement of the traditional electric power system.

Additionally, the OpenHAN architecture does not presume use of only electric meters.  The Utility ESI may also communicate with gas and water meters and transmit their data through the HAN (e.g., to an IHD) or through a backhaul network (e.g. AMI network, internet, etc.) for transfer to an appropriate entity (e.g., an electric utility could gather water meter information and pass that information to the water utility).

Rationale

The ability to support communication to multiple HAN Devices provides greater value to the Consumer and Service Provider by facilitating automation and reducing redundancy in the systems required to capture metering information. As more homes and business become “green” it is anticipated that the HAN will need to support DER sources such as solar panels, small wind turbines, or PEVs that may discharge energy back into the grid.  In addition, non-revenue grade metering of end-use devices can provide consumers with additional information on the energy and cost associated with end-uses such as individual circuits, appliances, or plug loads.

- Supports Distributed Energy Generation

- Consumer Owns the HAN

Description

The Consumer owns and controls the HAN.  For various reasons and under designated conditions, the Consumer may cede control of specific HAN devices and functions in accordance with a Service Provider's program. A Service Provider can not manage a Consumer’s registered HAN device without receiving permission from the Consumer. The Consumer gives a Service Provider this permission by enrolling a registered HAN Device in the Service Provider’s program.

Rationale

Service Providers and vendors may offer Consumers innovative applications, programs, and devices which utilize the HAN and the AMI meter data. However, the Consumer decides which applications, products, information, programs, devices, etc. are best suited to meet the Consumer’s energy goals and needs.

- HAN Devices Present Additional Security Considerations

Description

The ESI manages the boundary between a HAN and a Service Provider’s network (e.g. Utility AMI Network). As such, ESI implementers and Service Providers must carefully consider the security implications of device tampering and compromised devices/networks when designing their systems and programs. It should be expected that certain individuals will attempt to use compromised HAN Devices and networks to launch attacks on a Utility AMI Network or to defraud a Service Provider’s program. It should also be expected that a HAN device may not perform the requested action (e.g. reduce load).

Rationale

HAN Devices are under the physical control of the Consumer and are typically located inside the Consumer Premises. Just like existing in-home networks, the Consumer bears responsibility for the security and integrity of their network and its attached devices. It should be expected that HAN devices may be tampered with inside the home, and that external parties may find ways to compromise devices on the HAN. It is important that appropriate security measures are taken so that the HAN does not comprise the Service Provider network's integrity and vice-versa.

- The HAN is enabled by Open and Interoperable Standards

Description

The HAN is enabled by open and interoperable standards.

Open specification: standards should be developed and maintained through a collaborative, consensus-driven process that is open to participation by all relevant and materially affected parties and not dominated by, or under the control of, a single organization or group of organizations. As important, the standards resulting from this process should be readily and reasonably available to all for Smart Grid applications.

Interoperability: The capability of two or more networks, systems, devices, applications, or components to directly exchange and readily use information—securely, effectively, and with little or no inconvenience to the user.

Rationale

The use of open and interoperable standards is a key to accessibility, availability, innovation, and wide-spread adoption.  Standards provide for (1) cyber security that protects systems and data, (2) interoperable components that protect investments in technology and enable growth in the HAN ecosystem, (3) competition among consumer products companies, which drives down costs while increasing choices for Consumers, (4) reduced maintenance and support costs caused by proprietary solutions, and (5) a common understanding of information exchange.

## Architectural Considerations

The architectural consideration section is not binding. That is, this section of the document is not considered “requirements.”  Rather, this section of the document provides context to the OpenHAN task force architectural considerations during the development of this HAN SRS document. In general, this HAN SRS is architecture agnostic.  The requirements are targeted at logical devices.  The following sections simply provide additional clarifications and context.

In November 2009, NIST formed the Smart Grid Interoperability Panel (SGIP) and seated the initial SGIP Governing Board (SGIPGB). The HAN has been a topic of interest and the SGIPGB formed a HAN Task Force to make recommendations to the SGIPGB on the issue of HAN Architecture.  Since the view of HAN architecture is evolving, it is expected that this OpenHAN SRS v2.0 will require updating as the SGIPGB HAN Task Force and the Smart Grid Architecture Committee (SGAC) complete their work on HAN architecture.

### Energy Services Interface (ESI)

The ESI provides a particular logical function in the HAN.  It is an interface which enables Secure Communications between authorized parties (e.g. Utility, Consumer, non-Utility Service Providers, EMS, etc.) and all HAN Devices that are Commissioned and Registered to it. The HAN architecture allows for more than one ESI in a Consumer premises. The ESI creates logical segmentation within the premises.  This logical segmentation can be viewed as separate networks:  the Utility network and all other networks. HAN Devices (e.g. EMS, internet gateway, etc.) which are active on multiple networks must have a logical separation between those networks. This does not preclude implementation of multiple logical networks existing on a common single physical network.

An important ESI is the Utility ESI which enables secure interactions between HAN Devices Commissioned and Registered to it and the Utility AMI.  Security on this interface is robust and comprehensive in order to protect Utility assets (e.g. electric grid, AMI, etc.). This ESI is the unique interface providing real-time energy usage information from the AMI meter to HAN Devices and is protected with cryptographic methods. Who (e.g. Utility, Consumer, non-utility Service Provider, etc.) has access to communicate with the Utility ESI is a matter of law or regulatory policy.  In addition, the type of access an authorized party has is subject to the program in which the HAN Device is Enrolled.  Additional ESIs may be installed in the Consumer premises to create additional logical HANs (e.g. EMS, a Service Provider program, etc.). These ESIs must provide security to protect Consumer assets and data. Communication to HAN Devices Commissioned and Registered to these ESIs may be through alternative communication networks (e.g. internet, cell phone network, EMS, etc.).

In some jurisdictions, the Utility ESI may provide for two modes of communication to the premises, one which requires Registration for two-way communication over the Utility AMI communication network and another which does not require Registration and only allows on-way communication (i.e. public broadcast).

### Commissioning, Registration, Enrollment

### To create a home-area network, devices must at a minimum scan for networks to join, request admission, and exchange device parameters. This initial process is called Commissioning and allows devices to exchange a limited amount of information (e.g. network keys, device type, device ID, initial path, etc.) and to receive public broadcast information. This process is initiated by the Installer powering on the device and following the manufacturer’s instruction. Once a HAN device has completed the Commissioning process it may go through an additional process called Registration.

### The Registration process is a further step involving Mutual Authentication and authorizing a Commissioned HAN device to exchange secure information with other Registered devices and with an ESI.  Registration creates a trust relationship between the HAN device and the ESI and governs the rights granted to the HAN device. This process is more complex than Commissioning and requires coordination between the Installer and the Service Provider.  In some jurisdictions Commissioning and Registration are combined into one process called Provisioning.

### The final process is Enrollment.  This process is only applicable when the Consumer wants to sign up their HAN Device for a specific Service Provider program (e.g. demand response, PEV special rate, pre-pay, etc.).  In this process the Consumer selects a Service Provider program and grants the Service Provider certain rights to communicate with or control their HAN device.  A HAN device must be Commissioned and Registered prior to initiating the Enrollment process.  This process requires coordination between the Consumer and the Service Provider. Each of these processes is discrete but they may be combined by a Service Provider in order to provide a seamless customer experience.

### Device Ownership

The HAN SRS as a whole is agnostic to device ownership.  OpenHAN recognizes consumer rights, and this sentiment is stated explicitly in the Guiding Principles section of this document. With that being said, the architecture section does touch on additional aspects of ownership and control.  The architecture section makes a further assumption beyond the Guiding Principle that devices in the premises can be supplied by the Utility, a non-utility Service Provider, or the Consumer. This HAN SRS provides for architecture flexibility and supports any desired configuration.

    - Utility Public Broadcast Channel

Some jurisdictions may require a public broadcast channel to supply a limited amount of public information to the consumer premises.  This is a one way communication channel that requires Commissioning of the HAN device but not Registration. That is to say, this interface has a fair amount of vulnerabilities and should be used only for general conservation information.

### Cohabitation

Some HAN Devices may reside on a third party network and may also be Commissioned and Registered to the Utility ESI. Since there can be vulnerabilities related to HAN Devices, the Utility ESI should start with the assumption that a HAN Device should not be trusted and it must provide a means for protecting the Utility AMI including the AMI meter.

### Deregulated Electric Markets

The electric market structure varies from jurisdiction to jurisdiction and country to country.  In certain deregulated markets, retail energy sales and the actual delivery of electricity are segmented.  In such markets the Utility is the entity which delivers the electricity and the Service Provider is the entity which provides Consumer programs for HAN devices and may or may not provide retail energy sales to the Consumer.  In addition, in some jurisdictions metering may be a competitive service. This HAN SRS is agnostic to electric market structure and may be used regardless of the market structure.

    - External Interfaces

The HAN SRS was written to support external interfaces to the HAN.  The ESI requirements specified in the HAN SRS do not presuppose an architecture in which the only interface to the HAN is the Utility ESI.  Pricing information, control signals, and messaging may be provided from a non-Utility Service Provider (e.g. Retail Energy Provider, Demand Response Aggregator, etc.).  In this model, the AMI meter would continue to provide premises consumption information (e.g., real-time metrology) through the Utility ESI and would be part of the HAN.  Customers may also have an external interface (e.g. internet, cell phone network, etc.) to communicate with devices on their HAN to enable remote configuration, monitoring, and other applications.

### Special Applications

- PEV

PEVs are a unique HAN device because they combine mobility with numerous applications (e.g. demand response, pricing, energy management, energy storage, metering, etc.).  This version of OpenHAN SRS focuses primarily on charging a PEV at the primary residence. It also includes requirements dealing with energy storage and mobility, however, comprehensive and robust requirements dealing with the complex nature of the bi-directional flow of energy and charging at locations other than the primary residence will be left to future versions of the OpenHAN SRS once the technology, policy, and market design are more fully developed.

From an architectural perspective, a PEV application includes two functions that involve HAN communications and these functions may or may not be included within a single HAN device. These functions are the Electric Vehicle Supply Equipment (EVSE) and End-Use-Measurement Device (EUMD). The EVSE is the apparatuses (e.g. PEV connectors, attachment plugs, power outlets, etc.) specified by applicable SAE standards (e.g., SAE J2293, J1772 ™, J2836 & J2847.) that provide for the safe transfer of electrical energy from premises wiring to the PEV battery.  This can be 120V or 240V AC depending upon the connection. The EVSE is generally found in two configurations: (1) a specialized cord set or (2) a wall or pedestal mounted box.  The EUMD measures the energy consumed by a PEV and communicates the information.

The requirements in this OpenHAN SRS related to PEVs are based upon the following assumptions:

- The EVSE contains the HAN communications capabilities.

- The EUMD may contain HAN communications capabilities.

- The PEV may contain HAN communications capabilities.

- The PEV, EVSE, and EUMD are logically separate functions.  The EVSE is located off board the vehicle.  The EVSE and EUMD may be co-located in a single device or located in physically separate devices.   The PEV and EUMD may be co-located in a single device or located in physically separate devices.

- If EVSE and EUMD are a single physical device, a single representative HAN communications is anticipated; however dual communications in the single physical device may exist.

There are several PEV technical aspects related to implementation that influence the PEV interaction with the HAN.  The location of the EVSE may be a fixed installation in the premises (e.g. permanently installed in a garage, etc.) or it could be a portable device connected with the PEV. The metering accuracy of the EMUD may or may not be revenue grade.  In addition, the EMUD may be a sub-meter in the Consumer premises or it may be a separate meter dedicated to measuring only the PEV consumption.

The way the PEV is technically implemented inside the Consumer premises leads to the following architectural scenarios:

- Scenario A

    - PEV has integrated EUMD.

    - HAN has periodic connectivity to EVSE, as PEV is utilized by driver - i.e. network connectivity is not constant.

- Scenario B

- Vehicle only has J1772 receptacle.

- Consumer premises has a single HAN device with integrated EVSE and EUMD.

- Scenario C

a.	Vehicle only has J1772 receptacle.

b.	Consumer premises has two separate physical devices, an EVSE and an EUMD.

5.   Scenario D

  - Consumer premises has two separate physical devices, an EVSE and an EUMD

  - EVSE is connected to an Energy Management System (EMS) that is Commissioned and Registered to the Utility ESI.

- Energy Management System (EMS)

In this OpenHAN SRS, an EMS is a logical function to manage energy consumption in the premises.  Physically, it may reside in another hardware device (such as a PCT, In-Home Display, computer, cable set-top box) or it may be a separate and independent device.  At its simplest, the EMS may manage a few devices based on simple rules or enable the Consumer to access devices in the premises remotely from mobile phones. A more complex EMS may optimize energy usage or costs for devices within the premises, utilizing algorithms that manipulate many objectives and aspects of the current state of the grid and premises.  These varied EMSs will also have a wide range of communications capabilities: some, but not all, will communicate outside the premises; some will exchange information and control messages with one or more ESIs in the premises; some will control HAN Devices which are also enrolled in Service Provider programs.

This SRS recognizes the evolving architectures for premises energy management and the role of the EMS over the installed lifetime of the HAN Devices.  An EMS is not a required function in a HAN; however, as the Consumer adds more smart devices (e.g. PCT, smart appliance, PEV, etc.) to their premises and desires a more sophisticated and automated HAN ecosystem, an EMS may be installed. The EMS may provide conservation-related local control of HAN devices using various inputs (e.g. instantaneous usage obtained from the AMI meter, weather information available on the Internet, Consumer preferences, etc.). This type of control could begin with inexpensive HAN Devices such as light dimmers and pump relays which are controlled only by an EMS for local energy management. Over time, this could extend to those devices enrolled in Service Provider programs. As even more smart devices are purchased, an EMS may perform advanced optimization for the entire premises, balancing Consumer preferences with Service Provider program requirements and energy production from DER.

- Distributed Energy Resources (DER)

Distributed Energy Resources (DER) are small, modular, energy generation and storage technologies that are located at a customer’s service delivery point. DERs generate electricity which may provide for all or a portion of the premises’ electrical needs. A DER may be interconnected to the Utility electric distribution system and any net energy flowing on to the electric grid may be recorded in a separate channel on the AMI meter.  For purposes of the HAN SRS, a DER is a HAN device with functionality that measures and communicates its full energy production.  The DER production may also be managed by an EMS which optimizes the premises energy consumption.

### Architectural Scenarios

Figure 3:  Scenario One (Inception) – Utility interacts with a registered (Voluntary) PCT.  The Public Broadcast Channel interface is used to provide price signals and grid event messages to the Consumer’s unregistered Smart Appliance.  The ESI is located in the meter under glass.

Figure 4:  Scenario Two (Consumer Choice Example) – Consumer has placed the PCT and other devices on a third party network but chosen to register a load control device with the Utility.  The Utility is also using the HAN for communications to a gas meter.  The Utility Public Broadcast Channel is available but not used.

Figure 5:  Scenario Three (Mature System) - Several Consumer and Utility devices, several of which are registered with the Utility.  HAN Devices are accessible to the external interface/gateway (Internet).  The Utility Public Broadcast Channel is available but not used.

Figure 6:  Scenario Four (Deregulated Example) - All devices sit on the third party network.  The electric distribution company provides information through its Energy Services Interface.  The distribution company’s accountability boundary ends at the Utility ESI.  The Utility Public Broadcast Channel is available but not used.

# OpenHAN System Requirements

The OpenHAN System Requirements are the main focus of this document and provide the most important information to the various HAN stakeholders.  They define and constrain the HAN to enable successful functionality for Consumers, Utilities, Service Providers, and vendors.

## Requirements Mapping to Logical Devices

The OpenHAN SRS requirements are written with the key word “shall”, however, different HAN devices may include only a subset of these requirements to provide the device functionality. In order to provide guidance to Service Providers and vendors, the OpenHAN Task Force mapped each set of requirements to functional HAN devices in a table provided at the end of each section.  The tables indicate which requirements the OpenHAN Task Force considered Basic for Commissioning (BC), Basic for Registration (BR), Basic for application functionality (BF), Optional (O), or Not Applicable (NA).  These tables may be used as a template or starting point for Service Providers in their discussions with vendors and in their procurement process.  Vendors may use these tables as a guidance for producing devices and software which enables basic HAN functionality and for providing additional functionality in order to provide competitive differentiation. The tables are for reference only and should not limit the needs of Service Providers nor limit vendor innovation.

    - Mapping Categories

    - The categories used for the mapping of the requirements to the logical device types are defined below

- BC or Basic Commissioning – Minimum requirement for the Commissioning process.  These requirements are mandatory and must be included to support the process of Commissioning a HAN device on the HAN.

- BC or Basic Registration - Minimum requirement for the Registration process. These requirements are mandatory and must be included to support the process of Registering a HAN device on the ESI.

- BF or Basic Functionality – Minimum requirement that the OpenHAN TF recommends is needed to support the basic functionality of the logical HAN device.

- O or Optional – An optional requirement that may be included to support a Service Provider program or allow a vendor to differentiate their product.

- NA or Not Applicable - This requirement is not applicable to this logical HAN Device.

    - Logical Device Types

The list of logical devices chosen by the OpenHAN TF was limited to devices that were the most common at the time this document was written and is by no means exhaustive.  This list is intended to expand and grow as new classes of devices are available and new Service Provider programs are developed.  The logical HAN Devices are listed along with their primary functionality in the following Table 1.  These devices may include multiple functions but for simplicity sake the mapping was done by primary function.

Table 1: Logical HAN Device Types

|  | Logical Device | Primary Functionality |
| --- | --- | --- |
| 1 | Energy Services Interface (ESI) | Network Control and Coordination |
| 2 | Utility ESI | Network Control and Coordination |
| 3 | Programmable Communicating Thermostat (PCT) | HVAC Control |
| 4 | In-Home Display (IHD) | Display of Energy Information |
| 5 | Energy Management System (EMS) | Controlling end-device energy |
| 6 | Load Control | Resource Control |
| 7 | AMI meter | Energy Measurement |
| 8 | HAN Non-Electric Meter | Resource Measurement |
| 9 | Smart Appliance | Energy Awareness |
| 10 | Electric Vehicle Supply Equipment (EVSE) | Charging a PEV |
| 11 | End-Use Measurement Device (EUMD) | Metering of an end-device load |

## Requirements Framework

In creating the requirements, the OpenHAN Task Force considered a number of categories, such as:

- HAN Applications

- Communications

- Security

- Performance

- Operations-Maintenance-Logistics

HAN Applications are one of the most important categories from the Utility, Service Provider, vendor, and Consumer’s perspective. Any application that is enabled through the HAN will have one or more of the following characteristics: Control, Measurement and Monitor, Processing, and Human-Machine Interface (HMI).

Control applications respond to control signals. The simplest control application is direct control, which turns loads on or off. Control applications can also cycle, which means they turn the load on and off at configurable time intervals.  More sophisticated control applications can limit the load of a device (e.g. Smart Appliance, etc.) based on configurable thresholds. Control may also be exerted from within the HAN to fulfill Consumer objectives (e.g. manual, EMS, etc.).

Measurement and Monitor applications generally provide internal data and status.  These applications include DER functionality where local energy input and output is measured and monitored.  It can also have end-use metering functionality to measure and monitor device-specific energy consumption or production.  A Consumer PEV, for example, can have end-use metering functionality as well as DER.  Applications can be as simple as measuring and monitoring the environmental state or whether a device is on or off.

Processing applications consume, process, and act on external and internal data.  These applications accept data from external systems and HAN measurement and monitoring applications.  Applications with processing capability are generally more complex and costly.  The following applications require processing:

- Energy Cost - Calculates current and overall energy cost

- Energy Consumption - Calculates current and overall energy consumption

- Energy Production - Calculates current and overall energy production

- Energy Optimization - Utilizes external and HAN data to determine desired response based on a consumer-configurable profile

- Energy Demand Reduction - Uses external and HAN data to reduce load based on a consumer configurable profile (e.g. profiles based on various triggers such as  occupancy (home/away/vacation), schedule (day/night/weekend), price (low/med/high), demand response requests (voluntary/mandatory)

- Environmental Impact - Calculates environmental impact of current energy consumption (e.g. based on the CO2 emission profile of a  generation portfolio)

Human Machine Interface (HMI) – Most applications will need an HMI in order to provide local user input and/or output.  These applications are based on the data type.

- User Input - Provides Consumers with a means to input data into an application (e.g., touch screen, keypad, mobile phone, computer, etc.)

- User Output - Provides an Application with a means to output data to the Consumer (e.g., message, browser, mobile phone, display, etc.)

Communications is one of the most challenging categories for the HAN. The OpenHAN Task Force has identified communications criteria for commissioning and control.

Commissioning is the network process of adding a HAN device on the HAN to allow the device to communicate with other devices. This process is decoupled from Utility registration. Commissioning involves the following:

- Network scanning – Identifying candidate networks the device could elect to join.

- Network selection – Selection of the network the device will attempt to join

- Network admission – Inclusion of the device onto one of the candidate networks. This may include providing a network key.

- Network configuration - Establishing network specific device parameters (e.g., network ID, initial path, bindings)

Control of a node is enabled by the platform specific technology and it involves:

- Self-Organization – network must be self-forming and self-organizing

- Optimization - Path selection

- Mitigation - Ability to adapt and work in response to interference or range constraints

Security goes hand-in-hand with Communications. Introduction of a communications technology for the home requires enhanced security in the Utility ESI to protect the overall AMI system. The OpenHAN Task Force expects the UCAIug AMI Security Task Force to address the security requirements of the AMI system in greater detail. However, due to the importance of this category, the OpenHAN Task Force addresses specific security criteria that pertain to the ESI (e.g. Utility ESI, other ESI). The security categories addressed are: Access Control and Confidentiality, Registration, Enrollment, Integrity, and Accountability.

Access Controls and Confidentiality address levels of data protection based on data type. All data will have some level of access control, but there are various requirements associated with data-at-rest and data-in-transit based on data type.

- Public Controls (low robustness) - Protection methods for publicly available information (e.g., conservation messages, etc.)

- Private Controls (medium robustness) -  Protection methods for confidential or sensitive data (e.g., Consumer usage)

- Utility Controls (high robustness) - Protection methods for Utility accountable data (e.g., load control, other premises metering data)

Registration is the network process to authenticate and authorize HAN device participation with an ESI. Once a HAN device is Commissioned, it is part of the network. However, the device must go through the Registration process to privately send and receive information with other devices registered to a common ESI. Therefore, Registration involves the following:

- Initialization –The process of making the HAN device information (e.g. MAC address, security codes, etc.) available to the authentication service

- Authentication – The process of verifying the application / device as a trusted device (i.e. verifies the application’s / device’s identity) This may include mutual authentication.

- Correlation – Creates a trust relationship between the HAN device and the ESI (e.g. exchanging security keys)

- Authorization – Governs rights granted to devices.

- De-register – the process of removing a device that has been Registered (i.e. removing the correlation and authorization)

Enrollment is the process by which a Consumer enrolls a HAN device in a Service Provider’s program (e.g. demand response, energy management, pre-pay, PEV programs, distributed generation, pricing, messaging, etc.) and gives certain rights to the Service Provider to communicate with their HAN device.

Integrity preserves the HAN operating environment through:

- Resistance – Methods which prevent changes to the application or application’s data (e.g., tamper and compromise resistance)

- Recovery – Restores an application or the application’s data to a previous or desired state (e.g., reloading an application, resending corrupted communications)

Accountability will allow for monitoring malicious activities through:

- Audit – Application log detected compromise attempts

- Non-repudiation – Applications and application operators are responsible for actions (e.g., can not deny receipt or response)

Performance requirements ensure applications or other factors do not limit the performance of the system.  Since the OpenHAN SRS is written at a platform-independent level, these criteria are higher level than the others found in this document.  The requirements associated with these criteria are also less detailed than others for the same reason that, depending on  technology selection, their performance requirements will differ.  Performance of the system is usually dependent on the following:

Availability - The applications and devices are consistently reachable

Reliability - The applications and devices are designed and manufactured to be durable and resilient

Maintainability - The applications and devices are designed to be easily diagnosed and managed

Scalability - The system supports a reasonable amount of growth in applications and devices

Upgradeability - The applications and devices have a reasonable amount of remote upgradeability (e.g., patches, updates, enhancements)

Quality - The applications and devices will perform as advertised

Latency - The applications will respond in an appropriate amount of time

Operations, Maintenance and Logistics criteria address the challenges around deploying HAN Devices in a new market segment. The OpenHAN Task Force’s goal is to make the design, maintenance, and operation of the system as easy and cost effective as possible while not compromising security and performance. There are many activities involved in reaching this goal:

Manufacturing and Distribution - Vendor’s pre-installation activities

- Pre-commissioning - Depot level configuration setting

- Application configuration - Any required Service Provider specific configurations or applications

- Labeling - compliance and standards labeling

- Purchasing - Supports multiple distribution channels (e.g., retail, wholesale, Service Provider, etc.)

Installation - Physical placement of the device

- Documentation - Installation materials and manuals (e.g. how to install, how to operate, how to commission, etc.)

- Support Systems - Installation support systems including web support, help line, other third party systems

Manage, Maintain

- Alarming and logging - Event driven notifications

- Testing - System and device testing

- Device reset - Resets the device to the installation state

- Monitoring – device and application heartbeat

Please refer to the Figure 7 on the following page to see a hierarchical illustration of the Requirements Framework and system decomposition.

Figure 7 Requirements Framework

## Requirements Assumptions

This section documents the assumptions on which the requirements are based.  It will be helpful to refer back to these throughout the rest of the specification.

- Service Providers are granted access rights to HAN Devices in a Consumer premises by the Consumer.

- Service Providers expect vendor differentiation and innovation in the marketplace.

- Assume orderly shutdown of operations during control signal execution (e.g., shutdown could be delayed until current process completes, shutdown is such that it does not compromise safety systems built into HAN Devices, etc.).

- HAN device does not presume source of message (e.g., authorized users, Consumer, EMS, etc.).

- Does not cover the consequences or incentives associated with demand response participation or compliance (e.g., overriding mandatory control signals).

- EMS may proxy as the controller (e.g. Utility, Service Provider, Consumer, etc.).

- EMS devices are viewed as aggregating functions within the system and may aggregate data from multiple sources.

- Rate and consumption information can pass from the ESI (e.g. Utility ESI, or other ESI) to the Energy Cost application.

- Energy Cost applications are not intended to reconcile costs displayed on HAN Devices with bills generated by a Service Provider billing system.  There are other elements associated with billing and revenue-grade metering that are outside the scope of these requirements (e.g., revenue-grade certification, Utility rate recovery).

- The Energy Cost applications may be components of an Energy Management System.

- Existence of alarm features may be part of separate energy optimization applications (e.g., signal an alarm when the accumulated cost for the month is greater than $100).

- For authentications to be considered secure they must not be able to be reversed with modern computing technology in the amount of time for which they are valid.

- The HAN provides secure communication with multiple HAN Devices and different device types to support scalability and growth.

- The HAN device may have default configurations that allow the Consumer to use the HAN device following installation and Commissioning to the greatest degree possible (e.g. smart appliance or PCT operates even if it is not Registered or Enrolled in a program, etc.).

- Dynamic pricing information may need to be communicated to HAN Devices in such a way that the HAN Device can group the information according to Consumer set price thresholds (e.g. prices over a threshold require a certain smart appliance reaction)

- Authorized users (e.g. Utility, Consumer, Service Provider, etc.) shall be provided secure two-way access to HAN Devices Enrolled in Service Provider programs.

The requirements listed in these sections are not prioritized by criticality or sophistication and include some fairly advanced functional capabilities that may be beyond the current state of the market.  This is intentional.

## Application Requirements

Application requirements are the heart of HAN interactions and define what HAN Devices do.  These applications include: Control, Measurement & Monitoring, Processes, and Human-to-machine interfaces and are broadly described here. Other functions and programs supported by applications include: demand response, messaging, bi-directional consumption sharing (metering data) and price delivery, off-the-shelf HAN device installation and configuration by Consumers, multi-dwelling unit (MDU) deployments, consumer energy conservation, control, etc.)

### Control

Control applications respond to control signals from authorized parties (e.g. Utility, Service Providers, EMS, Consumers, etc.).  Control signals typically tell a device to turn ON or OFF at configurable time intervals or thresholds or enter into an energy saving mode.

Requirements:

App.Control.1 HAN Device shall accept control signals from one or more authorized parties (e.g. Utility, Service Provider, EMS, Consumer, etc.)

App.Control.2 HAN Device shall respond to requests to cease operational state (e.g. open contact).

App.Control.3 HAN Device shall respond to requests to resume operational state (e.g. close contact).

App.Control.4 HAN Device shall acknowledge receipt of control signal.

App.Control.5 HAN Device shall acknowledge execution of control signal.

App.Control.6 HAN Device shall acknowledge execution failure of control signal (i.e. exceptions).

App.Control.7 HAN Device shall communicate any consumer or device -initiated overrides or delays in response (e.g. all events in a program, specific demand response event, all events in a specific time period, partial overrides, etc.).

App.Control.8 HAN Device shall respond to request to cease operation state at a specific time.

App.Control.9 HAN Device shall respond to request to resume operation state based at a specific time.

App.Control.10 HAN Device shall delay restoration of operational state based on a pre-configured time (e.g., random number).

App.Control.11 HAN Device shall respond to request to cycle operational state (i.e. duty cycle).

App.Control.12 HAN Device shall respond to request to change operational mode (e.g. on, off, cycle, charging, discharging, power save, etc.) taking into account thresholds, set-points, or triggers (e.g. price points, device safety configurations, relative price (high, medium, low), demand limits, etc.).

App.Control.13 HAN Device shall respond to requests for variable output (e.g. load limiting, energy savings mode, etc.)

App.Control.14 The HAN Device shall support local and remote active management by authorized parties (e.g., Consumer, Utility, Service Provider, EMS, etc.) of HAN Device applications (e.g., Consumer-configurable preferences for load control, etc.).

App.Control.15 HAN Device shall appropriately respond to a cancellation of an advanced scheduled event (e.g. demand response, price event, PEV charging session, etc.).

App.Control.16 The HAN device shall appropriately respond to a cancellation of a demand response event which is either in progress or has not yet started.

Table 2: Control Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| App.Control.1 | HAN Device shall accept control signals from one or more authorized parties (e.g. Utility, Service Provider, EMS, Consumer, etc.) | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.2 | HAN Device shall respond to requests to cease operational state (e.g., open contact). | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.3 | HAN Device shall respond to requests to resume operational state (e.g., close contact). | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.4 | HAN Device shall acknowledge receipt of control signal. | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.5 | HAN Device shall acknowledge execution of control signal. | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.6 | HAN Device shall acknowledge execution failure of request (i.e., exceptions). | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.7 | HAN Device shall communicate any consumer or device-initiated overrides or delays in response (e.g. all events in a program, specific demand response event, all events in a specific time period, partial overrides, etc.). | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.8 | HAN Device shall respond to request to cease operation state at a specific time. | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.9 | HAN Device shall respond to request to resume operation state at a specific time. | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.10 | HAN Device shall delay restoration of operational state based on a pre-configured time (e.g., random number). | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.11 | HAN Device shall respond to request to cycle operational state (i.e., duty cycle). | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.12 | HAN Device shall respond to request to change operational mode (e.g. on, off, cycle, charging, discharging, power save, etc.) taking into account thresholds, set-points, or triggers (e.g. price points, device safety configurations, relative price (high, medium, low), demand limits, etc.). | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.13 | HAN Device shall respond to requests for variable output (e.g. load limiting, energy savings mode, etc.) | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.14 | The HAN Device shall support local and remote active management by authorized parties (e.g., Consumer, Utility, Service Provider, EMS, etc.) of HAN Device applications (e.g., Consumer-configurable preferences for load control, etc.). | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.15 | HAN Device shall appropriately respond to a cancellation of an advanced scheduled event (e.g. demand response, price event, PEV charging session, etc.). | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |
| App.Control.16 | The HAN device shall appropriately respond to a cancellation of a demand response event which is either in progress or has not yet started. | NA | NA | BF | NA | BF | BF | NA | NA | O | BF | NA |

### Measurement and Monitoring

Measurement and monitoring applications provide data and status from HAN devices.  These are functional requirements on the device.  They do not speak to the organization of the system (e.g., net versus sub).  The applications covered are DER (e.g., solar, fuel cell, wind), metering of devices within the premises (e.g., Consumer PEV), monitoring of local conditions (e.g., temperature, humidity, time, airflow, ambient light level, motion), and monitoring of a device’s state.  These applications provide input to the HAN system and enable processing and action based upon that input. Appropriate levels of security to protect consumer privacy must be observed by the receiving entity of each of these data.

Requirements:

App.Measure.1 HAN Device shall measure instantaneous demand (e.g., W).

App.Measure.2 HAN Device shall measure accumulated consumption (e.g. Wh) for a variety of time periods (e.g. 15 minutes, hour, day, month, configurable period, year, etc.) and price periods (e.g. TOU-Peak period, TOU-Shoulder period, CPP period, etc.).

App.Measure.3 HAN Device shall measure accumulated production (e.g. Wh) for a variety of time periods (e.g. 15 minutes, hour, day, month, configurable period, year, etc.) and price periods  (e.g. TOU-Peak period, TOU-Shoulder period, CPP period, etc.).

App.Measure.4 HAN Device shall measure consumption per interval (e.g. Wh, BTU, HCF).

App.Measure.5 HAN Device shall measure production per interval (e.g. Wh).

App.Measure.6 HAN Device shall store intervals measurements (e.g., 30 days of interval reads).

App.Measure.7 HAN Device shall allow interval configuration (e.g. 15 minutes).

App.Measure.8 HAN Device shall monitor energy state (e.g. state of charge, Watt-hour).

App.Measure.9 HAN Device shall measure available capacity (e.g. Watts, Volt-Amps).

App.Measure.10 HAN Device shall monitor the end-device state (e.g. operational, stand-by, maintenance).

App.Measure.11 HAN Device shall measure power quality (e.g. frequency, neutral voltage, harmonic content).

App.Measure.12 HAN Device shall monitor environmental state (e.g. temperature, motion, wind).

App.Measure.13 HAN Device shall monitor the operational mode of other HAN devices (e.g. duty cycle, charging, discharging, etc.).

App.Measure.14 The application shall support multiple measurement standards (e.g. metric, US, Imperial) for energy applications.

App.Measure.15 HAN Device shall measure Peak Demand per time of use/Critical Peak Pricing period and Peak Demand per configurable period.

App.Measure.16 The application shall support other metrology information as provided from the meter (e.g. Volts, Amps, VAr, Power Factor, etc.)

App.Measure.17 The application shall support temperature information.

App.Measure.18 The application shall support billing Information (e.g. rate label, Service Provider name or ID, etc)

App.Measure.19 The application shall provide the ability to measure discrete HAN Device loads for specific programs, (i.e. billing PEV charging at preferential rates).

App.Measure.20 The HAN Device shall measure or monitor and display status indicators related to pricing and billing status (e.g. current TOU period, current Block Pricing Tier, CPP Event, etc.)

Table 3: Measurement and Monitoring Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| App.Measure.1 | HAN Device shall measure instantaneous demand (e.g., W). | NA | NA | NA | NA | O | NA | BF | BF | O | NA | BF |
| App.Measure.2 | HAN Device shall measure accumulated consumption (e.g. Wh) for a variety of time periods (e.g. 15 minutes, hour, day, month, configurable period, year, etc.) and price periods (e.g. TOU-Peak period, TOU-Shoulder period, CPP period, etc.). | NA | NA | NA | NA | O | NA | BF | BF | O | NA | O |
| App.Measure.3 | HAN Device shall measure accumulated production (e.g. Wh) for a variety of time periods (e.g. 15 minutes, hour, day, month, configurable period, year, etc.) and price periods (e.g. TOU-Peak period, TOU-Shoulder period, CPP period, etc.). | NA | NA | NA | NA | O | NA | BF | BF | O | NA | O |
| App.Measure.4 | HAN Device shall measure consumption per interval (e.g., Wh, BTU, CCF, HCF). | NA | NA | NA | NA | O | NA | BF | BF | O | NA | O |
| App.Measure.5 | HAN Device shall measure production per interval (e.g., Wh). | NA | NA | NA | NA | O | NA | BF | BF | O | NA | O |
| App.Measure.6 | HAN Device shall store intervals measurements (e.g., 30 days of interval reads). | NA | NA | NA | O | O | NA | BF | BF | O | NA | O |
| App.Measure.7 | HAN Device shall allow interval configuration (e.g., 15 Minutes). | NA | NA | NA | O | O | NA | O | O | O | NA | O |
| App.Measure.8 | HAN Device shall monitor energy state (e.g. state of charge, Watt-hour). | NA | NA | O | O | O | O | NA | NA | O | O | O |
| App.Measure.9 | HAN Device shall measure available capacity (e.g., Watts, Volt-Amps). | NA | NA | NA | NA | O | NA | NA | NA | O | NA | O |
| App.Measure.10 | HAN Device shall monitor the end-device state (e.g., operational, stand-by, maintenance). | NA | NA | O | NA | O | BF | NA | NA | O | O | NA |
| App.Measure.11 | HAN Device shall measure power quality (e.g., frequency, neutral voltage, harmonic content). | NA | NA | NA | NA | NA | NA | O | NA | O | NA | O |
| App.Measure.12 | HAN Device shall monitor environmental state (e.g., temperature, motion, wind). | NA | NA | O | NA | O | NA | NA | NA | O | NA | NA |
| App.Measure.13 | HAN Device shall monitor the operational mode of other HAN devices (e.g. duty cycle, charging, discharging, etc.). | NA | NA | NA | NA | BF | NA | NA | NA | O | NA | NA |
| App.Measure.14 | Application shall support multiple measurement standards (e.g. metric, US, Imperial) for energy applications. | NA | NA | NA | O | O | NA | NA | NA | O | NA | NA |
| App.Measure.15 | HAN Device shall measure Peak Demand per time of use/Critical Peak Pricing period and Peak Demand per configurable period. | NA | NA | NA | O | O | NA | O | O | O | NA | O |
| App.Measure.16 | Application shall support other metrology information as provided from the meter (e.g. Volts, Amps, VAr, Power Factor, etc.) | NA | NA | NA | O | O | NA | NA | NA | O | NA | NA |
| App.Measure.17 | Application shall support temperature information. | NA | NA | O | NA | O | NA | NA | NA | O | NA | NA |
| App.Measure.18 | Application shall support billing Information (e.g. rate label, Service Provider name or ID, etc) | NA | NA | NA | O | O | NA | NA | NA | O | NA | NA |
| App.Measure.19 | Application shall provide the ability to measure discrete HAN Device loads for specific programs, (i.e. billing PEV charging at preferential rates). | NA | NA | NA | NA | O | NA | NA | NA | O | NA | BF |
| App.Measure.20 | The HAN Device shall measure or monitor and display status indicators related to pricing and billing status (e.g. current TOU period, current Block Pricing Tier, CPP Event, etc.) | NA | NA | NA | O | O | NA | NA | NA | O | NA | NA |

### Processing

Processing are applications that consume, process, and act on external (e.g. data coming from outside the HAN, rate, billing, etc.) and internal data (e.g. data from within the HAN environment).  These applications accept data from external systems and HAN measurement & monitoring applications.  In general, these applications have a higher level of complexity and cost.

Requirements:

App.Process.1 The application shall calculate a HAN Device’s cost of accumulated energy consumption as monetary value (e.g., $/kWh * accumulated kWh = $).

App.Process.2 The application shall calculate a HAN Device’s energy cost of instantaneous power consumption as a monetary value per time interval, (e.g., $/Wh * instantaneous W= $/hr).

App.Process.3 The application shall calculate a HAN Device’s cost for Dynamic Energy rates for the appropriate time interval.

App.Process.4 The application shall calculate a HAN Device’s energy cost for rate tiers/energy blocks.

App.Process.5 The application shall calculate a HAN Device’s energy cost for Time-of-Use (TOU) energy rates.

App.Process.6 The application shall calculate a HAN Device’s cost for Critical Peak Pricing (CPP).

App.Process.7 The application shall calculate a HAN Device’s cost for capacity billing rates.

App.Process.8 The application shall calculate costs for other billing determinants (e.g., monthly consumer charges, taxes & franchise fee, surcharges, discounts, ratcheted demand, bond charges).

App.Process.9 The application shall accept aggregated consumption, billing, and rate information from user-configurable sources (e.g., AMI System, EMS, HMI, etc.).

App.Process.10 The application shall calculate and forecast a HAN Device’s consumption based on user-defined parameters (e.g., estimated kWh/month).

App.Process.11 The application shall calculate and forecast a HAN Device’s production based on user-defined parameters (e.g., estimated kWh/month).

App.Process.12 The application shall forecast a HAN Device’s estimated cost calculation based on user-defined parameters (e.g., monthly consumption at current rate/usage).

App.Process.13 The application shall calculate a HAN Device’s consumption based on user-defined parameters (e.g., historical reporting).

App.Process.14 The application shall calculate and/or predict a HAN Device’s environmental impact based on user-defined parameters (e.g., historical carbon footprint, forecasted carbon credits earned).

App.Process.15 The application shall supply a method for local billing resolution and true-up to approximate Service Provider billing amounts (e.g., orphaned billing charge, consumption debits/credits).

App.Process.16 The application shall manage and/or make suggestions related to energy consumption and costs for load devices under its control (e.g., PCT, lights, PEV, pool pump , smart appliances, etc.) based on the consumer's rate structure (e.g. CPP, TOU, real-time pricing, demand rates, etc.), Service Provider program parameters (e.g. demand response, etc.), and Consumer-defined parameters (e.g., demand limit, PCT thresholds, lighting settings, pool pump cycling, PEV charging schedule, household schedule, payment objective, etc.).

App.Process.17 The application shall calculate a HAN Device’s relative efficiency (e.g., comparison can be based on historical data, baseline at install, manufacturer’s parameters, industry/governmental standards, other devices, other premises).

App.Process.18 The application shall calculate available load for demand reduction based on user-defined parameters (e.g., percentage of load available for various response scenarios, minimum load, maximum load, etc).

App.Process.19 The application shall accumulate  consumption, production, and cost and measure it against user-defined thresholds (e.g., if aggregated consumption reaches a certain level an alert is generated, PEV is charged for 20 miles of driving, etc.).

App.Process.20 The application shall accept a simple, relative price signal (e.g., low, medium, high, critical, etc.) [Note:  the customer may be the one who determines what is low, medium, high or critical]

App.Process.21 The application shall support multiple rate structures (e.g. time-of-use, inclining block tiers, critical peak pricing events, Peak Time Rebate, Real Time Pricing, all combinations thereof, etc.)

App.Process.22 The application shall send an acknowledgement of receipt of message only upon request.

App.Process.23 HAN device shall have the ability to be assigned to a group.

App.Process.24 The application shall support comparisons of energy consumption and cost information to externally supplied values (e.g. average user comparisons, comparisons with a baseline, track progress toward a target, etc.)

App.Process.25 The application shall support configurable periods.

App.Process.26 The application shall make available Peak Demand per time of use /Critical Peak Pricing period and Peak Demand per configurable period (e.g. EMS, IHD, etc.)

App.Process.27 The application shall provide methods to support negotiation of an energy request with ESI (e.g. for PEV charging purposes). This might include requested charge amount (in KWh) requested charge time, charging start and end time(s), available charge amount, charging rate, etc.

App.Process.28 The application shall support on-board PEV calculations (e.g. cost per distance). [Note: consumer may want this information displayed on another HAN Device, (e.g. EMS); EMS may want to request this information so consumer can make charging decisions.]

App.Process.29 The application shall provide method for communicating constraints when the HAN device (i.e. a demand response asset) is available for load shed (e.g. time of day schedule constraints, black out dates, maximum consecutive days of participation, maximum duration of demand response event participation, minimum duration of demand response event participation, maximum number of times per day demand response resource may be called, minimum advanced notification necessary, etc.).

App Process.30 The application shall calculate the load overridden by consumer during a demand response event

App.Process.31 The application shall communicate effective starting date and time when the HAN device is expected to comply with the demand response obligation.

App.Process.32 The application shall accept a decimal representation of the expected duration of the demand response event with integers representing hours and decimal positions representing fraction of hours (e.g. 1.5 indicates duration of 1 hour and 30 minutes from the effective-start-date-time)

App.Process.33 The application shall accept a unique identifier for the demand response event (eg. a URI in accordance with http://www.w3.org/TR/uri-clarification/#uri-schemes) to manage the most recent information.

App.Process.34 The application shall record the date and time a message was received and returns that date and time in the acknowledgment message.

App.Process.35 The application shall cancel an active demand response event when notified of a cancellation beginning with the date and time the cancellation is effective.

App.Process.36 The application shall accept a ramp time (potentially randomized).

App.Process.37 The application shall accept a demand response event end date/time and respond appropriately.

App.Process.38 The application shall respond appropriately to changes in events (e.g. demand response, PEV charging, etc.) and ensure execution of the most recent information.

App.Process.39 The application shall respond to a price for the duration the price is valid. The prices may be published on a frequency interval.

App.Process.40 The application shall accept a price expressed in decimal notation with a precision up to 6 decimal places.  Prices may be either positive or negative.

App.Process.41 The application shall accept the unit of measure for which the price pertains. Must be compliant with the International System of Units as defined by NIST SP 330, ref: http://physics.nist.gov/Pubs/SP330/sp330.pdf (e.g. kWh, MWh).

App.Process.42 The application shall calculate the load deferred during the demand response event.

App.Process.43 The application shall send any override messages to the Service Provider, when an override occurs during a demand response event, which is in progress.

App.Process.44 The application shall determine the device operation mode or state using both a price and relative price signal (e.g., low, medium, high, critical, etc.)

App.Process.45 The application shall inform (e.g. display, text message, email, etc.) the authorized user (e.g. Consumer, Service Provider, etc.) of the initiation and termination of a charging session (e.g. PEV, etc.)

App.Process.46 The application shall calculate and make available either locally or remotely the current state of the storage (e.g. PEV battery charge level, etc.) in a user configured format (e.g. travel miles available, kwh available, etc.).

Table 4: Process Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| App.Process.1 | Application shall calculate a HAN Device’s cost of accumulated energy consumption as monetary value (e.g., $/kWh * accumulated kWhrs = $). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.2 | Application shall calculate a HAN Device’s energy cost of instantaneous power consumption as a monetary value per time interval, (e.g., $/Wh * instantaneous W= $/hr). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.3 | Application shall calculate a HAN Device’s cost for Dynamic Energy rates for the appropriate time interval. | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.4 | Application shall calculate a HAN Device’s energy cost for rate tiers/energy blocks. | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.5 | Application shall calculate a HAN Device’s energy cost for Time-of-Use (TOU) energy rates. | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.6 | Application shall calculate a HAN Device’s cost for Critical Peak Pricing (CPP). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.7 | Application shall calculate a HAN Device’s cost for capacity billing rates. | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.8 | Application shall calculate costs for other billing determinants (e.g., monthly Consumer charges, taxes & franchise fee, surcharges, discounts, ratcheted demand, bond charges). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.9 | Application shall accept aggregated consumption, billing, and rate information from user-configurable sources (e.g., AMI System, EMS, HMI, etc,). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.10 | Application shall calculate and forecast a HAN Device’s consumption based on user-defined parameters (e.g., estimated kWh/month). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.11 | Application shall calculate and forecast a HAN Device’s production based on user-defined parameters (e.g., estimated kWh/month). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.12 | Application shall forecast a HAN Device’s estimated cost calculation based on user-defined parameters (e.g., monthly consumption at current rate/usage). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.13 | Application shall calculate a HAN Device’s consumption based on user-defined parameters (e.g., historical reporting). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.14 | Application shall calculate and/or predict a HAN Device’s environmental impact based on user-defined parameters (e.g., historical carbon footprint, forecasted carbon credits earned). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.15 | Application shall supply a method for local billing resolution and true-up to approximate Service Provider billing amounts (e.g., orphaned billing charge, consumption debits/credits). | NA | NA | NA | O | O | NA | NA | NA | O | NA | O |
| App.Process.16 | Application shall calculate and suggest methods to optimize energy consumption and cost based on user-defined parameters (e.g., PCT thresholds, lighting settings, pool pump cycling). | NA | NA | NA | NA | O | NA | NA | NA | NA | NA | NA |
| App.Process.17 | Application shall calculate a HAN Device’s relative efficiency (e.g., comparison can be based on historical data, baseline at install, manufacturer’s parameters, industry/governmental standards, other devices, other premises). | NA | NA | NA | NA | O | NA | NA | NA | O | NA | NA |
| App.Process.18 | Application shall calculate available load for demand reduction based on user-defined parameters (e.g., percentage of load available for various response scenarios). | NA | NA | O | NA | O | O | NA | NA | O | NA | O |
| App.Process.19 | Application shall accumulate consumption, production, and cost and measure it against user-defined thresholds (e.g., if aggregated consumption reaches a certain level an alert is generated, PEV is charged for 20 miles of driving, etc.). | NA | NA | NA | O | O | NA | NA | NA | NA | NA | NA |
| App.Process.20 | Application shall accept a simple, relative price signal (e.g., low, medium, high, critical, etc.) | NA | NA | O | O | O | O | NA | NA | BF | O | NA |
| App.Process.21 | Application shall support multiple rate structures (e.g. time-of-use, inclining block tiers, critical peak pricing events, Peak Time Rebate, Real Time Pricing, all combinations thereof, etc.) | NA | NA | NA | O | O | NA | NA | NA | O | O | NA |
| App.Process.22 | Application shall send an acknowledgement of receipt of message only upon request. | BF | BF | O | O | O | O | NA | NA | O | O | O |
| App.Process.23 | HAN device shall have the ability to be assigned to a group. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| App.Process.24 | Application shall support comparisons of energy consumption and cost information to externally supplied values (e.g. average user comparisons, comparisons with a baseline, track progress toward a target, etc.) | NA | NA | NA | O | O | NA | NA | NA | NA | NA | NA |
| App.Process.25 | Application shall support configurable periods. | BF | BF | BF | BF | BF | BF | NA | NA | BF | O | NA |
| App.Process.26 | Application shall make available Peak Demand per time of use /Critical Peak Pricing period and Peak Demand per configurable period (e.g. EMS, IHD, etc.) | NA | NA | O | O | O | NA | NA | NA | O | O | NA |
| App.Process.27 | Application shall provide methods to support negotiation of an energy request with ESI (e.g. for PEV charging purposes). This might include requested charge amount (in KWh) requested charge time, charging start and end time(s), available charge amount, charging rate, etc. | NA | NA | O | NA | O | O | NA | NA | O | O | NA |
| App.Process.28 | Application shall support on-board PEV calculations (e.g. cost per distance). [Note: consumer may want this information displayed on another HAN Device, (e.g. EMS); EMS may want to request this information so consumer can make charging decisions.] | NA | NA | NA | NA | O | NA | NA | NA | NA | O | NA |
| App.Process.29 | Application shall provide method for communicating constraints when the HAN device (i.e. a demand response asset) is available for load shed (e.g. time of day schedule constraints, black out dates, maximum consecutive days of participation, maximum duration of demand response event participation, minimum duration of demand response event participation, maximum number of times per day demand response resource may be called, minimum advanced notification necessary, etc.). | NA | NA | O | NA | O | O | NA | NA | O | O | NA |
| App.Process.30 | Application shall calculate the load overridden by consumer during a demand response event | NA | NA | O | NA | O | O | NA | NA | O | O | NA |
| App.Process.31 | Application shall communicate effective starting date and time when the HAN device is expected to comply with the demand response obligation. | NA | NA | O | NA | O | O | NA | NA | O | O | NA |
| App.Process.32 | Application shall accept a decimal representation of the expected duration of the demand response event with integers representing hours and decimal positions representing fraction of hours (e.g. 1.5 indicates a duration of 1 hour and 30 minutes from the effective-start-date-time) | NA | NA | BF | NA | BF | BF | NA | NA | BF | BF | NA |
| App.Process.33 | Application shall accept a unique identifier for the demand response event (eg. a URI in accordance with http://www.w3.org/TR/uri-clarification/#uri-schemes) to manage the most recent information. | NA | NA | BF | NA | BF | BF | NA | NA | BF | BF | NA |
| App.Process.34 | Application shall record the date and time a message was received and returns that date and time in the acknowledgment message. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| App.Process.35 | Application shall cancel an active demand response event when notified of a cancellation beginning with the date and time the cancellation is effective. | NA | NA | BF | NA | BF | BF | NA | NA | BF | BF | NA |
| App.Process.36 | Application shall accept a ramp time (potentially randomized). | NA | NA | O | NA | O | O | NA | NA | O | O | NA |
| App.Process.37 | Application shall accept a demand response event end date/time and respond appropriately. | NA | NA | BF | NA | BF | BF | NA | NA | BF | BF | NA |
| App.Process.38 | Application shall respond appropriately to changes in demand response events and ensure execution of the most recent information. | NA | NA | BF | NA | BF | BF | NA | NA | BF | BF | NA |
| App.Process.39 | Application shall respond to a price for the duration the price is valid. The prices may be published on a frequency interval. | NA | NA | BF | NA | BF | BF | NA | NA | BF | BF | NA |
| App.Process.40 | Application shall accept a price expressed in decimal notation with a precision up to 6 decimal places. Prices may be either positive or negative. | NA | NA | BF | BF | BF | BF | NA | NA | BF | BF | NA |
| App.Process.41 | Application shall accept the unit of measure for which the price pertains. Must be compliant with the International System of Units as defined by NIST SP 330, ref: http://physics.nist.gov/Pubs/SP330/sp330.pdf (e.g. kWh, MWh). | NA | NA | BF | BF | BF | BF | NA | NA | BF | BF | NA |
| App.Process.42 | Application shall calculate the load deferred during the demand response event. | NA | NA | O | NA | O | O | NA | NA | O | O | NA |
| App.Process.43 | Application shall send any override messages to the Service Provider, when an override occurs during a demand response event, which is in progress. | BF | BF | BF | NA | BF | BF | NA | NA | BF | BF | NA |
| App.Process.44 | Application shall determine the device operation mode or state using both a price and relative price signal (e.g., low, medium, high, critical, etc.) | NA | NA | O | NA | O | O | NA | NA | BF | O | NA |
| App.Process.45 | The application shall inform (e.g. display, text message, email, etc.) the authorized user (e.g. Consumer, Service Provider, etc.) of the initiation and termination of a charging session (e.g. PEV, etc.) | NA | NA | NA | O | O | NA | NA | NA | NA | O | NA |
| App.Process.46 | The application shall calculate and make available either locally or remotely the current state of the storage (e.g. PEV battery charge level, etc.) in a user configured format (e.g. travel miles available, kwh available, etc.). | NA | NA | NA | O | O | NA | NA | NA | NA | O | NA |

### Human-Machine Interface

Human-Machine Interface are applications that provide local user input and/or output.  These applications may be limited and may be depend upon the device type.  They provide a method for users to interact with the HAN, enter preferences, configure the HAN and its devices, and obtain useful information from the HAN and its devices.

Requirements:

App.HMI.1 HAN Device shall provide visual indicators which indicate operational state (e.g., commissioned, registered, event status, device state, etc.).

App.HMI.2 HAN Device shall provide a power cycle input, which reboots the device.

App.HMI.3 HAN Device shall provide a user reset input, which returns the device to its pre-installation state (e.g., button).

App.HMI.4 HAN Device shall provide an alphanumeric display which indicates operational state (e.g., LCD screen).

App.HMI.5 HAN Device shall provide non-visual sensory feedback (e.g., motion, vibration, audible).

App.HMI.6 HAN Device shall provide a sight and hearing impaired interface.

App.HMI.7 HAN Device shall provide a user-configurable display.

App.HMI.8 HAN Device shall accept user configurations.

App.HMI.9 HAN Device shall accept user preferences (e.g., Celsius/Fahrenheit, color, language).

App.HMI.10 HAN Device shall provide alarm notifications (e.g., price threshold, event messages).

App.HMI.11 HAN Device shall accept Utility data source configurations (e.g., Energy Services Interface, other HAN Devices).

App.HMI.12 HAN Device shall display Utility data source configurations (e.g., Energy Services Interface, other HAN Devices).

App.HMI.13 HAN Device shall display application-specific information (e.g., cost, consumption, environmental impact, payment credit, remaining account credit).

App.HMI.14 HAN Device shall accept application-specific configurations (e.g., preconfigured periods (e.g., hour, day, week), configurable periods (e.g., interval length, TOU period), variable periods (e.g., Critical Peak Price period).

App.HMI.15 For battery-powered devices, HAN Device shall provide a battery life indicator.

App.HMI.16 HAN Device shall accept payment data from the consumer.

App.HMI.17 The application shall support multiple languages and shall accept user preference of language.

App.HMI.18 HAN devices shall accept user preference to display values in a currency with an appropriate number of decimal places or rounded to the nearest full currency unit.

App.HMI.19 The HAN device shall display a description of the demand response event that is occurring.

App.HMI.20 The HAN device shall display information using units that are common to the Consumer in the Consumer's local.

App.HMI.21 The HAN device shall provide abilities for the Consumer to a) reset the HAN device to a default state and, or, b) to erase all Consumer information (e.g. usage, billing, pricing, etc.).

Table 5: Human Machine Interface Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| App.HMI.1 | HAN Device shall provide visual indicators which indicate operational state (e.g., commissioned, registered, event status, device state, etc.). | NA | NA | O | O | O | NA | NA | NA | NA | O | NA |
| App.HMI.2 | HAN Device shall provide a power cycle input, which reboots the device. | NA | BF | BF | BF | BF | BF | NA | NA | BF | BF | BF |
| App.HMI.3 | HAN Device shall provide a user reset input, which returns the device to its pre-installation state (e.g., button). | NA | BF | BF | BF | BF | BF | NA | NA | BF | BF | BF |
| App.HMI.4 | HAN Device shall provide an alphanumeric display which indicates operational state (e.g., LCD screen). | NA | NA | BF | BF | O | NA | NA | NA | O | O | BF |
| App.HMI.5 | HAN Device shall provide non-visual sensory feedback (e.g., motion, vibration, audible). | NA | NA | O | O | O | O | NA | NA | O | O | NA |
| App.HMI.6 | HAN Device shall provide a sight and hearing impaired interface. | NA | NA | O | O | O | O | NA | NA | O | O | NA |
| App.HMI.7 | HAN Device shall provide a user-configurable display. | NA | NA | O | O | O | O | NA | NA | O | O | NA |
| App.HMI.8 | HAN Device shall accept user configurations. | NA | NA | O | O | O | O | NA | NA | O | O | O |
| App.HMI.9 | HAN Device shall accept user preferences (e.g., Celsius/Fahrenheit, color, language). | NA | NA | O | O | O | O | NA | NA | O | O | O |
| App.HMI.10 | HAN Device shall provide alarm notifications (e.g., price threshold, event messages). | NA | NA | O | O | O | O | NA | NA | O | O | NA |
| App.HMI.11 | HAN Device shall accept Utility data source configurations (e.g., Energy Services Interface, other HAN Devices). | BR | BR | BR | BR | BR | BR | NA | NA | BR | BR | BR |
| App.HMI.12 | HAN Device shall display Utility data source configurations (e.g., Energy Services Interface, other HAN Devices). | NA | NA | O | O | O | O | NA | NA | O | O | O |
| App.HMI.13 | HAN Device shall display application-specific information (e.g., cost, consumption, environmental impact, payment credit, remaining account credit). | NA | NA | O | BF | O | O | NA | NA | O | O | O |
| App.HMI.14 | HAN Device shall accept application-specific configurations (e.g., preconfigured periods (e.g., hour, day, week), configurable periods (e.g., interval length, TOU period), variable periods (e.g., Critical Peak Price period). | NA | NA | BF | BF | BF | BF | NA | NA | BF | BF | BFNA |
| App.HMI.15 | For battery-powered devices, HAN Device shall provide a battery life indicator. | NA | NA | O | O | O | NA | NA | O | NA | NA | NA |
| App.HMI.16 | HAN Device shall accept payment data from the consumer. | NA | NA | NA | O | O | NA | NA | NA | NA | O | NA |
| App.HMI.17 | HAN Device shall support multiple languages and shall accept user preference of language. | NA | NA | O | O | O | NA | NA | NA | NA | O | NA |
| App.HMI.18 | HAN devices shall accept user preference to display values in a currency with an appropriate number of decimal places or rounded to the nearest full currency unit. | NA | NA | O | O | O | NA | NA | NA | O | O | NA |
| App.HMI.19 | The HAN device shall display a description of the demand response event that is occurring | NA | NA | O | O | O | O | NA | NA | O | O | NA |
| App.HMI.20 | The HAN device shall display information using units that are common to the Consumer in the Consumer's local. | NA | NA | BF | BF | O | NA | NA | NA | O | O | NA |
| App.HMI.21 | The HAN device shall provide abilities for the Consumer to a) reset the HAN device to a default state and, or, b) to erase all Consumer information (e.g. usage, billing, pricing, etc.). | BF | BF | BF | BF | BF | BF | NA | NA | BF | BF | BF |

## Communication Requirements

Communication requirements of OpenHAN are designed to provide reliable message transmissions between the authorized parties (e.g. Utility, Service Provider, EMS, etc.) and the consumer’s HAN Devices.  These requirements cover Commissioning, Control,  Commissioning requirements describe how a new HAN Device is added to the communication network.  Control requirements detail how the communication network and HAN Device work together to maintain a reliable communication network.

### Commissioning

Commissioning is defined as the network process of identifying and adding a node on the HAN with the expectation that the system is self-organizing (i.e., initial communication path configuration).  This process is decoupled from Registration and Enrollment.

Requirements:

Comm.Commission.1 HAN Device shall accept network configuration data which allows for admission to an existing network or the establishment of a new network (e.g., network ID, etc.)

Comm.Commission.2 HAN Device shall accept Commissioning configuration data by the manufacturer (e.g., link key).

Comm.Commission.3 When a HAN Device is triggered (e.g. Power-on, button, etc.), HAN Device shall be capable of providing the HAN with device-specific information (e.g. device ID, device type, networking details, network ID, gateway ID, etc.) needed for Commissioning.

Comm.Commission.4 ESI shall acknowledge successful Commissioning requests (i.e., provide acknowledgement to the requesting HAN Device).

Comm.Commission.5 When a HAN Device is communicating with the ESI, HAN Device shall indicate link connectivity.

Comm.Commission.6 HAN Device shall provide notification to the Installer of the Commissioning status (e.g. successful, unsuccessful, in process, etc.).

Comm.Commission.7 ESI shall be uniquely identified (e.g. meter number, Service Point Location, customer id, ESI ID, etc.)

Comm.Commission.8 HAN Device shall be uniquely identified (e.g. networking details, MAC Address, etc.)

| Table 6: Commissioning Requirements MappingRequirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Comm.Commission.1 | HAN Device shall accept network configuration data which allows for admission to an existing network or the establishment of a new network (e.g., network ID, etc.) | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC |
| Comm.Commission.2 | HAN Device shall accept Commissioning configuration data by the manufacturer (e.g., link key). | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC |
| Comm.Commission.3 | When a HAN Device is triggered (e.g. Power-on, button, etc.), HAN Device shall be capable of providing the HAN with device-specific information (e.g. device ID, device type, networking details, network ID, gateway ID, etc.) needed for Commissioning. | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC |
| Comm.Commission.4 | ESI shall acknowledge successful Commissioning requests (i.e., provide acknowledgement to the requesting HAN Device). | O | O | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Comm.Commission.5 | When a HAN Device is communicating with the ESI, HAN Device shall indicate link connectivity | NA | NA | O | O | O | O | O | O | O | O | O |
| Comm.Commission.6 | HAN Device shall provide notification to the Installer of the Commissioning status (e.g. successful, unsuccessful, in process, etc.). | NA | NA | O | O | O | O | O | O | O | O | O |
| Comm.Commission.7 | ESI shall be uniquely identified (e.g. meter number, Service Point Location, customer id, ESI ID, etc.) | BC | BC | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Com.Commission.8 | HAN Device shall be uniquely identified (e.g. networking details, MAC Address, etc.) | NA | NA | BC | BC | BC | BC | BC | BC | BC | BC | BC |

### Control

Autonomous functions enabled by the platform-specific technology.  These requirements speak to the efficient functioning of HAN communications and are intended to provide robust and reliable communication paths in the HAN.

Requirements:

Comm.Control.1 HAN Device shall accept network organization messages from the Energy Services Interface (e.g., gateway location, routing table, address).

Comm.Control.2 HAN Device shall accept network organization messages from peer devices (e.g., hidden node).

Comm.Control.3 The HAN shall use reliable communication paths (e.g., based on signal strength/quality) and have the ability to overcome interference on the communications medium (e.g., channel hopping, channel avoidance, etc.).

Comm.Control.4 HAN Device shall have the ability to automatically adapt to communications interference through detection and analysis of environmental conditions (e.g., channel hopping, channel avoidance, signal-to-noise ratio).

Comm.Control.5 HAN Device shall include a data integrity mechanism for all communications (e.g., checksum).

Comm.Control.6 Energy Services Interface shall have the ability to activate and deactivate its HAN communication.

Comm.Control.7 HAN Device shall have a configurable availability communication (i.e., heartbeat) frequency to the Energy Services Interface.

Comm.Control.8 HAN shall support broadcast messaging to all HAN devices.

Comm.Control.9 The HAN shall support multiple communication paths into the premises (e.g., Utility AMI network, public network, internet, other private network, etc.).

Comm.Control.10 The HAN shall support utility-secured and public broadcast communication channels.

Comm.Control.11 The HAN Device shall support more than one physical layer and shall be extensible to more than one physical layer.

Comm.Control.12 HAN Device shall be able to attach to one or more ESIs, temporarily, habitually, etc. (e.g. PEV mobility, EMS, gateway, etc.).

Comm.Control.13 HAN Device shall have the ability to communicate directly or indirectly with another HAN Device within the HAN (subject to security policies).

Comm.Control.14 HAN Device shall be able to initiate communication with the ESI (e.g. override of event by PCT, etc).

Comm.Control.15 The ESI shall support time stamp logging of communication to/from HAN Devices.

Comm.Control.16 The HAN shall support bridging between communications media (e.g. wireless HAN and wired HAN), while maintaining compatibility and security requirements.

Comm.Control.17 Authorized users (e.g. Utility, Consumer, Service Provider, EMS, etc.) shall be provided secure two-way access to Registered or Enrolled HAN Devices.

Comm.Control.18 HAN shall support messaging to individual HAN Devices.

Comm.Control.19 HAN shall support messaging to groups of HAN Devices.

Comm.Control.20 ESI shall resend a message upon failure of a requested confirmation from HAN Device and the HAN Device shall appropriately handle receipt of retries.

Comm.Control.21 ESI shall provide the communication availability (i.e., heartbeat) of the devices that are Registered to it.

Table 7: Control Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Comm.Control.1 | HAN Device shall accept network organization messages from the Energy Services Interface (e.g., gateway location, routing table, address). | NA | NA | BC | BC | BC | BC | BC | BC | BC | BC | BC |
| Comm.Control.2 | HAN Device shall accept network organization messages from peer devices (e.g., hidden node). | NA | NA | BC | BC | BC | BC | BC | BC | BC | BC | BC |
| Comm.Control.3 | The HAN shall use reliable communication paths (e.g., based on signal strength/quality) and have the ability to overcome interference on the communications medium (e.g., channel hopping, channel avoidance, etc.). | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC |
| Comm.Control.4 | HAN Device shall have the ability to automatically adapt to communications interference through detection and analysis of environmental conditions (e.g., channel hopping, channel avoidance, signal-to-noise ratio). | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC |
| Comm.Control.5 | HAN Device shall include a data integrity mechanism for all communications (e.g., checksum) | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC |
| Comm.Control.6 | Energy Services Interface shall have the ability to activate and deactivate its HAN communication. | BF | BF | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Comm.Control.7 | HAN Device shall have a configurable availability communication (i.e., heartbeat) frequency to the Energy Services Interface. | NA | NA | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Comm.Control.8 | HAN shall support broadcast messaging to all HAN devices. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Comm.Control.9 | The HAN shall support multiple communication paths into the premises (e.g., Utility AMI network, public network, other private network, etc.). | NA | O | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Comm.Control.10 | The HAN shall support utility-secured and public broadcast communication channels. | O | O | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Comm.Control.11 | The HAN Device shall support more than one physical layer and shall be extensible to more than one physical layer. | O | O | O | O | O | O | O | O | O | O | O |
| Comm.Control.12 | HAN Device shall be able to attach to one or more ESIs, temporarily, habitually, etc. (e.g. PEV mobility, EMS, gateway, etc.). | NA | NA | O | O | O | O | NA | NA | O | O | O |
| Comm.Control.13 | HAN Device shall have the ability to communicate directly or indirectly with another HAN Device within the HAN (subject to security policies). | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Comm.Control.14 | HAN Device shall be able to initiate communication with the ESI (e.g. override of event by PCT, etc). | NA | NA | O | NA | O | O | NA | NA | O | O | NA |
| Comm.Control.15 | The ESI shall support time stamp logging of communication to/from HAN Devices. | BF | BF | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Comm.Control.16 | The HAN shall support bridging between communications media (e.g. wireless HAN and wired HAN), while maintaining compatibility and security requirements. | O | O | O | O | O | O | O | O | O | O | O |
| Comm.Control.17 | Authorized users (e.g. Utility, Consumer, Service Provider, etc.) shall be provided secure two-way access to Registered or Enrolled HAN Devices. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Comm.Control.18 | HAN shall support messaging to individual HAN Devices. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Comm.Control.19 | HAN shall support messaging to groups of HAN Devices. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Comm.Control.20 | ESI shall resend a message upon failure of a requested confirmation from HAN Device and the HAN Device shall appropriately handle receipt of retries. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Comm.Control.21 | ESI shall provide the communication availability (i.e., heartbeat) of the devices that are Registered to it. | BF | BF | NA | NA | NA | NA | NA | NA | NA | NA | NA |

## Security Requirements

The OpenHAN security requirements are designed to help ensure that HAN communications are used for their intended purposes.  These security requirements help to verify users’ identities, maintain user privacy, and assure responsible use.  These security requirements are divided into four sections: Access Controls and Confidentiality, Integrity, Accountability, Registration and Enrollment.

### Access Controls and Confidentiality

The goal of access control is to prevent the unauthorized use of HAN resources. Access control includes resource control; for example, preventing logon to local HAN Devices. For the purposes of this discussion, access control is not concerned with denying physical access. Access control is applied to an entity based on an identity or an authorization. An identity may represent an actual user, a process with its own identity (e.g., a program making a remote access connection), or a number of users represented by single identity (e.g., role-based access control).

Confidentiality refers to the security services, which prevent unauthorized disclosure of data (both stored and communicated). Confidentiality services prevent disclosure of data in transit and data at rest. Confidentiality services also include “anonymity”, a service which prevents disclosure of information which leads to the identification of the source or end-user of the information. Because of its role in limiting authorized disclosure of information, confidentiality services are closely linked with access control services.

Requirements:

Security.Access.1 Energy Services Interface shall provide access control (i.e., logical segmentation) to Service Provider applications, data, and services (e.g., control data, consumer-specific consumption data).

Security.Access.2 HAN Device shall control access to persistent HAN data (data at rest).

Security.Access.3 HAN Device shall control access to transmitted HAN data (data in transit).

Security.Access.4 HAN Device shall provide protection of HAN data while being processed (data in processing) (e.g., trusted processor).

Security.Access.5 HAN Device shall control access to data in accordance with a managed security policy when logically linking one or more networks (e.g., users, applications, devices, data access-read/write, EMS, etc.).

Security.Access.6 ESI shall provide mechanisms to enforce a policy based on least privilege (i.e., explicit authorization) for communications with the ESI.

Security.Access.7 ESI shall have the ability to enforce policy periods (time constraints) for security policy elements (e.g., maintenance/firmware window) for communications with the ESI.

Security.Access.8 HAN Device shall provide methods to query and report access control data settings.

Security.Access.9 HAN Device shall provide access control methods which prevent known attacks, including replay, man-in-the-middle, delay, spoofing, sequence change, and deletion attacks.

Security.Access.10 HAN Device shall implement mechanisms to prevent unintended disclosure of source/originator data to unauthorized principals.

Security.Access.11 HAN Device shall implement controls which limit access to audit information.

Security.Access.12 HAN Device shall support confidentiality and access controls that employ cryptographic operations (e.g., digital signatures).

Security.Access.13 HAN Device shall support confidentiality and access controls that employ cryptographic keys (e.g., encryption authentication, or digital certificates).

Security.Access.14 The application shall provide a means for authorized users to configure HAN Devices to communicate with one or more HANs (e.g., authorized users can select which portions of an application are available to devices not commissioned to the Utility ESI).

Security.Access.15 The HAN shall follow NIST SP 800-57, Recommendation for Key Management. (Note: This Recommendation provides guidance when using the cryptographic features of current systems. It is intended to help system administrators and system installers adequately secure applications based on product availability and organizational needs, and to support organizational decisions about future procurements. The guide also provides information for end users regarding application options left under their control in the normal use of the application).

Security.Access.16 Utility ESI shall comply with UtilityAMI System Security Requirements Specification v1.0.

Security.Access.17 Only HAN Devices that are Registered with the ESI will be able to communicate directly with the ESI.

Security.Access.18 The ESI will be the clear information boundary between the secure provider network (e.g. AMI, internet, broadband, local area network, gateway to local devices, etc.) and the HAN Device(s) that are commissioned to it.

### Integrity

The integrity security service addresses prevention of unauthorized modification of data (both stored and communicated).  Modification of both stored and communicated data may include changes, insertions, deletions or duplications. Additional potential modifications that may result when data is exposed to communications channels include sequence changes.  The integrity service also addresses the problem of ensuring that communicating components can correctly identify those that they are communicating with.

Requirements:

Security.Integrity.1 HAN Device shall protect the integrity of the HAN system (e.g., shall not adversely impact the operations of the HAN system by introducing malicious or unintended activity).

Security.Integrity.2 ESI shall provide a configurable filtering function (e.g. message structural integrity, message rate, message type, etc.) that filters messages transmitted bi-directionally between HAN devices and the Service Provider through the ESI.

Security.Integrity.3 HAN Device shall detect unauthorized modification of security-related data during storage.

Security.Integrity.4 HAN Device shall detect unauthorized modification of data during network transit (e.g., check sums and hashes).

Security.Integrity.5 HAN Device shall detect unauthorized modification of data attributes (e.g., modification to a message type).

Security.Integrity.6 HAN Device shall attempt to correct unauthorized modification of data attributes (e.g., NAK, resend).

Security.Integrity.7 HAN Device shall accept data from authorized trusted sources (e.g., ESI, EMS, other HAN Devices, etc.).

Security.Integrity.8 HAN Device shall protect the HAN from malicious code (e.g., buffer overflow protection, limit executable code exposure).

Security.Integrity.9 HAN Device shall separate security critical functionality and data from non-security critical system data.

Security.Integrity.10 HAN Device shall validate the source of HAN security policy.

Security.Integrity.11 HAN Device shall detect unauthorized modification of HAN security policy.

Security.Integrity.12 HAN Device shall detect unauthorized modification of audit data.

Security.Integrity.13 HAN Device shall validate the integrity of all software updates, including source, structure, and version.

Security.Integrity.14 HAN Device shall use tamper-resistant hardware (e.g., epoxy, etc.).

Security.Integrity.15 HAN Device shall support open source security methods.

Security.Integrity.16 HAN Device shall provide multiple security methods.

Security.Integrity.17 The ESI shall be configurable to detect and take appropriate action towards Registered HAN devices that are impairing the performance of the ESI (e.g. repeatedly sending degraded (Error) messages or repetitive messages at a high rate).

### Accountability

Accountability can be considered a special type of non-repudiation.  The accountability security service holds each network entity responsible for its actions on that network.

Depending upon the type of device or the Service Provider program, certain devices may require functions that detect and audit events related to security violation and tampering. Device security requirements should provide a reasonable measure of protection for the Consumer and the Service Provider.  The device security requirements are not intended to be the sole measure of protection and the entire environment should never be dependent upon the security measures implemented in end devices—they are simply one part, and an essential part, of the security program.

Requirements:

Security.Account.1 HAN Device shall alert the ESI of all detected, security-related activities, including access control, authentication, and integrity violations.

Security.Account.2 HAN Device shall audit and store all security-related activities, including access control violations, authentication activities, etc.

Security.Account.3 HAN Device shall provide, at a minimum, the following information for all detected security events: date and time of the event, type of event, device/user identity.

Security.Account.4 HAN Device shall provide the ESI access to audit data.

Security.Account.5 HAN Device shall provide the ability to perform searches, sorts and filters of audit data based on date and time, type and/or user identity.

Security.Account.6 HAN Device shall provide the capability to identify mandatory and configurable audit elements (In this context, mandatory refers to audit elements which are always enabled and configurable refers to audit elements which can be enabled or disabled at the discretion of the Consumer or Service Provider).

Security.Account.7 ESI shall provide non-repudiation that a message was sent from the ESI to a HAN device.

Security.Account.8 ESI shall provide non-repudiation that a reply was received from a HAN device back to the ESI.

Security.Account.9 ESI shall provide a mechanism for source identification of data (e.g., HAN and AMI System data).

Security.Account.10 ESI shall provide the capability to audit system policies.

### Registration

The registration and authenticating requirements are used in conjunction with most other security services. The first step of most security services is to determine the identities of one or more of the parties participating in an action. A trusted identity must be used for access control decisions and to provide accountability evidence. Knowing the identity of an entity and the existence of a peer relationship is also fundamental to establishing communication with confidentiality and integrity. If the identity of the peer in a secure communications path is not properly established, it leaves open the possibility that an unauthorized principal (an adversary) could masquerade as an authorized principal, exposing the data to disclosure or manipulation.

Requirements:

Security.Reg.1 HAN Device shall support Mutual Authentication.

Security.Reg.2 HAN Device shall provide a mechanism which allows for multiple and configurable authentication materials (e.g., device ID, device type, key, serial key, device configuration, certificate, etc.).

Security.Reg.3 HAN Device shall be configured with authentication materials (e.g., certificate, key).

Security.Reg.4 HAN Device shall not store or send authentication materials over the network in an insecure fashion (e.g., do not transmit passwords or keys in the clear).

Security.Reg.5 HAN Device shall support a defined Registration process.

Security.Reg.6 HAN Device shall provide a means to update (i.e., change, reconstitute, rollover) authentication materials.

Security.Reg.7 ESI shall allow de-registration for Registered HAN Devices.

Security.Reg.8 ESI shall support a configurable Registration and expiration period (e.g., Registration timeout, Registration persistence).

Security.Reg.9 HAN Device shall use security services (i.e., cryptographic services) which are either FIPS-approved or NIST-recommended.

Security.Reg.10 HAN Device shall support a Registration method that employs cryptographic operations (e.g., digital signatures).

Security.Reg.11 ESI shall provide an authentication mechanism which proxies for the Service Provider (e.g., negotiates on behalf of the Service Provider).

Security.Reg.12 HAN Device shall provide notification to the Installer of the Registration status (e.g. successful, pending, failed, etc.).

Security.Reg.13 ESI shall enable remote network and security configuration/control including the ability to remotely configure the rules (i.e., policies) which governs its logical network and interactions with its Registered devices.

Security.Reg.14 The HAN device shall be uniquely identified for the Registration process (e.g., Vehicle Identification Number, Electronic Serial Number, MAC address, networking details, Installation codes, Service Point Location, meter number, ESI security credentials, ESI ID, etc.)

Security.Reg.15 ESI shall accept Registration configuration from the Installer.

Security.Reg.16 When ESI is triggered (e.g., Allow Join Command), HAN Device location-/contact-specific data shall be provided to other HAN Devices in the premises.

Security.Reg.17 ESI shall have the ability to accept or reject a Registration request based on device type and ID.

Security.Reg.18 ESI shall have the ability to accept or reject device requests based on Service Provider-specific information (e.g., network ID, gateway ID, or Service Provider ID).

Security.Reg.19 ESI shall maintain a current list of Registered HAN Devices and make that list available upon request.

Security.Reg.20 An authorized user shall be able to Register a HAN Device either locally or remotely (e.g. through a Web Portal or other 3rd Party registration service [i.e. retail store, depot, or other]).

Security.Reg.21 ESI shall send an error message to the Service Provider when a request to Register a HAN Device has not been successfully completed within a configurable amount of time.

Security.Reg.22 ESI shall transmit the status of the HAN Device Registration (e.g. successful, pending, failed, etc.) to the party who is requesting the device Registration.

Security.Reg.23 An authorized user (e.g. Utility, Service Provider, Consumer, etc.) shall be able to remotely or locally de-Register a HAN Device.

Table 8: Registration Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Security.Reg.1 | HAN Device shall support Mutual Authentication. | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.2 | HAN Device shall provide a mechanism which allows for multiple and configurable authentication materials (e.g., device ID, device type, key, serial key, device configuration, certificate, etc.). | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.3 | HAN Device shall be configured with authentication materials (e.g., certificate, key). | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.4 | HAN Device shall not store or send authentication materials over the network in an insecure fashion (e.g., do not transmit passwords or keys in the clear). | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.5 | HAN Device shall support a defined Registration process. | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.6 | HAN Device shall provide a means to update (i.e., change, reconstitute, rollover) authentication materials. | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.7 | ESI shall allow de-registration for Registered HAN Devices. | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.8 | ESI shall support a configurable Registration and expiration period (e.g., Registration timeout, Registration persistence). | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.9 | HAN Device shall use security services (i.e., cryptographic services) which are either FIPS-approved or NIST-recommended. | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.10 | HAN Device shall support a Registration method that employs cryptographic operations (e.g., digital signatures). | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.11 | ESI shall provide an authentication mechanism which proxies for the Service Provider (e.g., negotiates on behalf of the Service Provider). | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.12 | HAN Device shall provide notification to the Installer of the Registration status (e.g. successful, pending, failed, etc.). | O | O | O | O | O | O | O | O | O | O | O |
| Security.Reg.13 | ESI shall enable remote network and security configuration/control including the ability to remotely configure the rules (i.e., policies) which governs its logical network and interactions with its Registered devices. | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.14 | The HAN device shall be uniquely identified for the Registration process (e.g., Vehicle Identification Number, Electronic Serial Number, MAC address, networking details, Installation codes, Service Point Location, meter number, ESI security credentials, ESI ID, etc.) | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.15 | ESI shall accept Registration configuration from the Installer. | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.16 | When ESI is triggered (e.g., Allow Join Command), HAN Device location-/contact-specific data shall be provided to other HAN Devices in the premises. | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.17 | ESI shall have the ability to accept or reject a Registration request based on device type and ID. | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.18 | ESI shall have the ability to accept or reject device requests based on Service Provider-specific information (e.g., network ID, gateway ID, or Service Provider ID). | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.19 | ESI shall maintain a current list of Registered HAN Devices and make that list available upon request. | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.20 | An authorized user shall be able to Register a HAN Device either locally or remotely (e.g. through a Web Portal or other 3rd Party registration service [i.e. retail store, depot, or other]). | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| Security.Reg.21 | ESI shall send an error message to the Service Provider when a request to Register a HAN Device has not been successfully completed within a configurable amount of time. | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg.22 | ESI shall transmit the status of the HAN Device Registration (e.g. successful, pending, failed, etc.) to the party who is requesting the device Registration. | BR | BR | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Security.Reg,23 | An authorized user (e.g. Utility, Service Provider, Consumer, etc.) shall be able to remotely or locally de-Register a HAN Device. | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |

    - Enrollment

Enrollment is the process by which a Consumer enrolls a Registered HAN device in a Service Provider’s program (e.g. demand response, energy management, pre-pay, PEV programs, distributed generation programs, pricing, messaging, etc.) and gives certain rights to the Service Provider to communicate with their HAN device.  This process creates a program relationship between the HAN device and the Service Provider’s back office.

Requirements:

Security.Enroll.1 HAN Device shall authenticate the source of all control signals.

Security.Enroll.2 HAN Device shall accept Enrollment configuration (e.g. Service Provider ID, program ID, etc.) either remotely or locally.

Security.Enroll.3 HAN Devices shall be individually addressable.

Security.Enroll.4 Authorized users (e.g. Utility, Consumer, Service Provider, etc.) shall be provided secure two-way access to Enrolled HAN Devices.

Security.Enroll.5. A HAN device shall have the ability to be assigned to a group.

Security.Enroll.6 ESI shall allow for un-enrolling a HAN Device in a Service Provider program.

## Table 9: Enrollment Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Security.Enroll.2 | HAN Device shall accept Enrollment configuration (e.g. Service Provider ID, program ID, etc.) either remotely or locally. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Security.Enroll.3 | HAN Devices shall be individually addressable. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Security.Enroll.4 | Authorized users (e.g. Utility, Consumer, Service Provider, etc.) shall be provided secure two-way access to Enrolled HAN Devices. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Security.Enroll.5 | A HAN device shall have the ability to be assigned to a group. | O | O | O | O | O | O | O | O | O | O | O |
| Security.Enroll.6 | ESI shall allow for un-enrolling a HAN Device in a Service Provider program. | BF | BF | NA | NA | NA | NA | NA | NA | NA | NA | NA |

## Performance Requirements

The OpenHAN performance requirements are intended to maintain the quality of the HAN communications over the short and long term. Often performance of a system is characterized by reliability, availability and scalability.

Performance requirements are designed to insure HAN applications and devices are:

- consistently reachable,

- designed and manufactured to be durable and resilient,

- easy to diagnose and manage,

- expandable to support future growth,

- remotely upgradeable (e.g., patches, updates, enhancements) without a field visit, and

- performing as advertised (i.e., quality).

Requirements:

Perf.1 HAN Device shall supply functionality that maintains communications availability to the Energy Services Interface.

Perf.2 HAN Device shall supply functionality that maintains application availability to the ESI (e.g., software/hardware application watchdog).

Perf.3 After loss of power, HAN Device shall return to its post-configuration state (i.e., shall persist communication and registration configurations).

Perf.4 HAN Device shall supply adequate computational performance (i.e., Device shall not hamper overall operational state of the HAN)

Perf.5 HAN Device shall supply adequate communications performance (e.g., bandwidth and throughput).

Perf.6 HAN Device shall supply accurate time keeping and counter functions.

Perf.7 HAN Device shall not act on expired signals (e.g., message validity duration or sequence).

Perf.8 HAN Device shall provide configurable communications such that system is scalable (e.g., heartbeat and request frequency).

Perf.9 For battery-powered HAN Devices, HAN Device shall function for a minimum of 1 year without requiring replacement of the battery.

Perf.10 HAN Device shall supply a field-programmable software upgrade function (i.e., firmware upgrade).

Perf.11 HAN Device shall supply a remote software upgrade function (i.e., firmware upgrade, application upgrade).

Perf.12 HAN Device shall meet the quality, interoperability, and testing (i.e., certification) requirements of its respective technology platform body.

Perf.13 HAN Device shall accept a reference time from the ESI.

Perf.14 ESI and HAN shall accept and utilize a reference time from a Service Provider-approved source (i.e. a shared understanding of time).

Perf.15 Shall support secondary and peripheral services which enable smart energy networking (e.g., management, bridging, registration, etc.).

Perf.16 HAN device shall support remote configuration.

Perf.17 The application shall use a structured, extensible information message schema.

Perf.18 HAN Devices shall support discrete (self contained) data.

Perf.19 HAN Devices shall support unordered data exchange.

Perf.20 HAN Devices shall support self-describing data across versions (e.g. device types, device attributes, device functions, etc.). Note: requirements 18-20 are necessary in order to ensure forward compatibility.

Perf.21 The application shall support the local currency for energy applications.

Perf.22 The application shall provide configurable sampling rate for application data (e.g., 5 seconds, 15 minutes, hourly, charging session, daily, etc.).

Perf.23 The application shall support a valid date/time/duration for each piece of information or message and shall not respond to expired messages. Configuration data for date/time/duration shall be in a standard and self-describing format. Also used for displaying new information based on scheduled changes to information. For messages with time boundaries they must have an expiration to provide graceful failures.

Perf.24 The application shall support variable length text messages (e.g., freeform messages conveying information, configuration, status, control).

Perf.25 The HAN shall provide adequate communications performance (e.g., bandwidth, throughput, range, latency, reliability, etc.) from the ESI  to the HAN Device for multiple deployment scenarios (e.g. large single or two story house, medium apartment, small apartment, multi-dwelling unit, strip mall store, etc.).

Perf.26 The application shall support multiple deployment scenarios (e.g. large single story house, medium two story house, medium apartment, small apartment, multi-dwelling unit, strip mall store, etc.).

Perf.27 The application shall provide adequate feedback in a reasonable amount of time (e.g., 0.1 second, 1.0 second, 10 second requirements found at: http://www.useit.com/papers/responsetime.html>)

Perf.28 HAN Devices (including ESI) shall not modify priority of messages.

Perf.29 HAN Devices (including ESI) shall be able to support delivery of messages in near real-time within the HAN .

Perf.30 ESI shall accept mean and operational tolerances for time resolution and time synchronization of messages and data from the authorized provider's time source.

Perf.31 ESI shall report the failure to deliver HAN messages to the requesting party.

Perf.32 HAN Devices (including ESI) shall provide sufficient standard error messages for a range of device and communication failures (e.g., unrecognized message, out of range/low signal strength, low battery level, feature not supported, meter faults, HAN device faults, communication errors, etc) that facilitate effective troubleshooting by the authorized user (e.g. Utility, Installer, third party, or automated systems)

Table 10: Performance Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Perf.1 | HAN Device shall supply functionality that maintains communications availability to the Energy Services Interface. | NA | NA | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.2 | HAN Device shall supply functionality that maintains application availability to the ESI (e.g., software/hardware application watchdog). | NA | NA | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.3 | After loss of power, HAN Device shall return to its post-configuration state (i.e., shall persist communication and registration configurations). | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.4 | HAN Device shall supply adequate computational performance (i.e., Device shall not hamper overall operational state of the HAN) | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.5 | HAN Device shall supply adequate communications performance (e.g., bandwidth and throughput). | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.6 | HAN Device shall supply accurate time keeping and counter functions. | BF | BF | O | O | O | O | BF | BF | O | O | O |
| Perf.7 | HAN Device shall not act on expired signals (e.g., message validity duration or sequence). | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.8 | HAN Device shall provide configurable communications such that the system is scalable (e.g., heartbeat and request frequency). | O | O | O | O | O | O | O | O | O | O | O |
| Perf.9 | For battery-powered HAN Devices, HAN Device shall function for a minimum of 1 year without requiring replacement of the battery. | NA | NA | O | O | O | O | NA | NA | O | O | O |
| Perf.10 | HAN Device shall supply a field-programmable software upgrade function (i.e., firmware upgrade). | BF | BF | O | O | O | O | BF | O | O | O | O |
| Perf.11 | HAN Device shall supply a remote software upgrade function (i.e., firmware upgrade). | BF | BF | O | O | O | O | BF | O | O | O | O |
| Perf.12 | HAN Device shall meet the quality, interoperability, and testing (i.e., certification) requirements of its respective technology platform body. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.13 | HAN Device shall accept a reference time from the ESI. | NA | NA | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.14 | ESI and HAN shall accept and utilize a reference time from a Service Provider-approved source (i.e. a shared understanding of time). | BF | BF | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Perf.15 | Shall support secondary and peripheral services which enable smart energy networking (e.g., management, bridging, registration, etc.). | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.16 | HAN device shall support remote configuration. | BF | BF | O | O | O | O | BF | O | O | O | O |
| Perf.17 | The application shall use a structured, extensible information message schema. | O | O | O | O | O | O | O | O | O | O | O |
| Perf.18 | HAN Devices shall support discrete (self contained) data. | O | O | O | O | O | O | O | O | O | O | O |
| Perf.19 | HAN Devices shall support unordered data exchange. | O | O | O | O | O | O | O | O | O | O | O |
| Perf.20 | HAN Devices shall support self-describing data across versions (e.g. device types, device attributes, device functions, etc.). Note: requirements 18-20 are necessary in order to ensure forward compatibility. | O | O | O | O | O | O | O | O | O | O | O |
| Perf.21 | The application shall support the local currency for energy applications. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.22 | The application shall provide configurable sampling rate for application data (e.g., 5 seconds, 15 minutes, hourly, charging session, daily, etc.). | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.23 | The application shall support a valid date/time/duration for each piece of information or message and shall not respond to expired messages. Configuration data for date/time/duration shall be in a standard and self-describing format. Also used for displaying new information based on scheduled changes to information. For messages with time boundaries they must have an expiration to provide graceful failures. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.24 | The application shall support variable length text messages (e.g., freeform messages conveying information, configuration, status, control). | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.25 | The HAN shall provide adequate communications performance (e.g., bandwidth, throughput, range, latency, reliability, etc.) from the ESI to the HAN Device for multiple deployment scenarios (e.g. large single or two story house, medium apartment, small apartment, multi-dwelling unit, strip mall store, etc.). | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.26 | The application shall support multiple deployment scenarios (e.g. large single story house, medium two story house, medium apartment, small apartment, multi-dwelling unit, strip mall store, etc.). | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.27 | The application shall provide adequate feedback in a reasonable amount of time (e.g., 0.1 second, 1.0 second, 10 second requirements found at: http://www.useit.com/papers/responsetime.html>) | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.28 | HAN Devices (including ESI) shall not modify priority of messages. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.29 | HAN Devices (including ESI) shall be able to support delivery of messages in near real-time within the HAN. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| Perf.30 | ESI shall accept mean and operational tolerances for time resolution and time synchronization of messages and data from the authorized provider's time source. | O | O | O | O | O | O | O | O | O | O | O |
| Perf.31 | ESI shall report the failure to deliver HAN messages to the requesting party. | BF | BF | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| Perf.33 | HAN Devices (including ESI) shall provide sufficient standard error messages for a range of device and communication failures (e.g., unrecognized message, out of range/low signal strength, low battery level, feature not supported, meter faults, HAN device faults, communication errors, etc) that facilitate effective troubleshooting by the authorized user (e.g. Utility, Installer, third party, or automated systems) | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |

## Operations, Maintenance, and Logistics Requirements

OpenHAN requirements for operations, maintenance, and logistics speak to supply chain standards for HAN Devices, including manufacturing, configuring, labeling, and packaging as well as standards for installation assistance, user manuals, online support, and device self-testing and troubleshooting.

### Manufacturing and Distribution

These requirements speak to a vendor’s pre-installation activities, including manufacture, depot, distribution, and point-of-sale.  The goal of these requirements is to clearly establish responsibilities and enable the widest diversity of supply chain options for Utilities and their customers.

Requirements:

OML.ManuDist.1 Prior to installation (e.g., factory, depot), HAN Device shall support placement of commissioning data (e.g., pre-placed device credentials).

OML.ManuDist.2 Prior to installation (e.g., factory, depot), HAN Device shall support placement of Registration data (e.g., pre-placed registration credentials).

OML.ManuDist.3 HAN device shall support pre-placed methods or materials that support Commissioning and Registration by multiple Service Providers (does not imply simultaneous registration).

OML.ManuDist.4 HAN Device shall support pre-placement of application-specific configurations (e.g., cost, consumption, environmental impact, configurable time/rate intervals, etc.).

OML.ManuDist.5 HAN Device shall have and display appropriate certification (e.g., electrical, safety, and communications requirements) on its packaging or body.

OML.ManuDist.6 HAN Device shall have and display appropriate Commissioning and Registration information on its packaging and body (e.g., serial number, installation code, MAC IDs for network interfaces, etc.).

OML.ManuDist.7 HAN Device shall display its HAN network technology compatibility on its outside packaging and body.

OML.ManuDist.8 HAN device shall display, on its packaging, any secondary device requirements (e.g., required EMS, bridge device, gateway, etc.).

OML.ManuDist.9 HAN Device shall be manufactured to support multiple distribution channels (e.g., retail, direct Utility, Service Provider, etc.).

OML.ManuDist.10 HAN device shall display, on its packaging, any power requirements (e.g. battery powered, plug in, etc.)

Table 11: Manufacturing and Distribution Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| OML.ManuDist.1 | Prior to installation (e.g., factory, depot), HAN Device shall support placement of commissioning data (e.g., pre-placed device credentials). | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC | BC |
| OML.ManuDist.2 | Prior to installation (e.g., factory, depot), a HAN Device shall support placement of registration data (e.g., pre-placed registration credentials). | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR | BR |
| OML.ManuDist.3 | HAN device shall support pre-placed methods or materials that support Commissioning and Registration by multiple Utilities (does not imply simultaneous registration). | BC, BR | BC | BR | BC | BR | BC | BR | BC | BR | BC | BR |
| OML.ManuDist.4 | HAN Device shall support pre-placement of application-specific configurations (e.g., cost, consumption, environmental impact, configurable time/rate intervals). | NA | NA | BF | BF | BF | BF | NA | NA | BF | BF | BF |
| OML.ManuDist.5 | HAN Device shall have and display appropriate certification (e.g., electrical, safety, and communications requirements) on its packaging or body. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| OML.ManuDist.6 | HAN Device shall have and display appropriate Commissioning and Registration information on its packaging and body (e.g., serial number, registration code,). | NA | BF | BF | BF | BF | BF | NA | NA | BF | BF | BF |
| OML.ManuDist.7 | HAN Device shall display its HAN network technology compatibility on its outside packaging and body. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| OML.ManuDist.8 | The HAN device shall display, on its packaging, any secondary device requirements (e.g., required EMS, bridge device). | NA | O | O | O | O | O | NA | O | O | O | O |
| OML.ManuDist.9 | HAN Device shall be manufactured to support multiple distribution channels (e.g., retail, direct Utility, Service Provider, etc.). | NA | O | O | O | O | O | NA | O | O | O | O |
| OML.ManuDist.10 | HAN device shall display, on its packaging, any power requirements (e.g. battery powered, plug in, etc.) | NA | O | O | O | O | O | NA | O | O | O | O |

### Installation

These requirements speak to vendor responsibilities in support of physical placement of the HAN Device.  The goal of these requirements is to ensure a smooth installation process regardless of the Installer with a minimum need for Consumer support from the Manufacturer and the Service Provider.

Requirements:

OML.Install.1 HAN Device Manufacturer or supplier shall include installation documentation that includes instructions for installation (e.g., placement, need for batteries, etc.) and commissioning, including any external dependencies.

OML.Install.2 HAN Device Manufacturer or supplier shall include a HAN Device user’s manual in the Device packaging.

OML.Install.3 HAN Device Manufacturer or supplier shall include Manufacturer contact information in the Device packaging.

OML.Install.4 HAN Device Manufacturer or supplier shall supply technical support services (e.g., help desk, web site, etc.).

Table 12: Installation Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| OML.Install.1 | HAN Device Manufacturer shall include installation documentation that includes instructions for installation (e.g., placement), commissioning, and registration, including any external dependencies. | NA | NA | BF | BF | BF | BF | NA | NA | BF | BF | BF |
| OML.Install.2 | HAN Device Manufacturer shall include a HAN Device user’s manual in the Device packaging. | NA | NA | BF | BF | BF | BF | NA | NA | BF | BF | BF |
| OML.Install.3 | HAN Device Manufacturer shall include Manufacturer contact information in the Device packaging. | NA | NA | BF | BF | BF | BF | NA | NA | BF | BF | BF |
| OML.Install.4 | HAN Device Manufacturer shall supply technical support services (e.g., help desk, web site). | NA | NA | O | O | O | O | NA | NA | O | O | O |

### Manage, Maintain

These requirements speak to vendor responsibilities for customer support.  They ensure HAN Devices enable diagnostic, management, and troubleshooting capabilities.  The goal of these requirements is to grant Service Providers the ability to remotely resolve problems with HAN Devices to quickly determine whether a Consumer needs to contact the Manufacturer’s customer support for further assistance.

Requirements:

OML.Maintain.1 HAN Device shall have a self-check (initialization) function that notifies the Installer the HAN Device is functioning properly.

OML.Maintain.2 Energy Services Interface shall have a configurable ability (e.g. retention policy, etc.) to log all ESI-to-HAN System communications.

OML.Maintain.3 When the HAN Device is rebooted (e.g. power cycled, turned off, off due to power outage, etc.), HAN device shall return to its state prior to losing connectivity (i.e., post-installation Commissioning, Registration, and Enrollment, if applicable) state and shall reestablish communication with the ESI.

OML.Maintain.4 HAN Device shall have a user-operable testing function that is equivalent to the self-testing function.

OML.Maintain.5 HAN Device shall supply a maintenance port for field diagnostics.

OML.Maintain.6 HAN Device shall simulate events for diagnostic purposes.

OML.Maintain.7 HAN Device shall supply network management functions for diagnostic purposes.

OML.Maintain.8 For battery-powered devices, HAN Device shall communicate low battery state to the Consumer and Service Provider, if the HAN Device is Enrolled in a Service Provider program.

OML.Maintain.9 HAN Device Manufacturer shall supply and support a flaw remediation process.

OML.Maintain.10 HAN Device shall support a communications feedback mechanism.

OML.Maintain.11 HAN Device shall provide methods to service communication components, which are transparent to the consumer (e.g., AMI Meter or other ESI replacement, device communication card replacement) – that is, don't require manual re-Commissioning and re-Registering of HAN Devices with the ESI.

OML.Maintain.12 HAN Device shall support remote methods to manage and update authentication materials (e.g. digital certificates) in HAN Devices requiring no Consumer intervention.

OML.Maintain.13 Application shall support diagnostic messages when errors (e.g. HAN device faults, communications errors, etc.) are detected (Note: Need an additional requirement on what diagnostic messages may be received from the meter (i.e. C12.19 data))

OML.Maintain.14 ESI shall provide methods and information needed for the Service Provider to troubleshoot where a communication fault occurred between an Enrolled device and the ESI.

OML.Maintain.15 The HAN Device shall provide maintenance details (e.g., current date and time stamp for firmware revision number and one prior date and time stamp for firmware revision number).

Table 13: Manage, Maintain Requirements Mapping

| Requirement ID | OpenHAN System Requirements | Utility ESI | ESI | PCT | IHD | EMS | Load Control | AMI Meter | HAN Meter (non-electric) | Smart Appliance | EVSE | EUMD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| OML.Maintain.1 | HAN Device shall have a self-check (i.e., initialization) function that notifies the Installer that the HAN Device is functioning properly. | NA | NA | O | O | O | O | NA | NA | O | O | O |
| OML.Maintain.2 | Energy Services Interface shall have a configurable ability (e.g. retention policy, etc.) to log all ESI-to-HAN System communications. | BF | BF | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| OML.Maintain.3 | When the HAN Device is rebooted (e.g. power cycled, turned off, off due to power outage, etc.), HAN device shall return to its state prior to losing connectivity (i.e., post-installation Commissioning, Registration, and Enrollment, if applicable) state and shall reestablish communication with the ESI. | NA | NA | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| OML.Maintain.4 | HAN Device shall have a user-operable testing function that is equivalent to the self-testing function. | O | O | O | O | O | O | O | O | O | O | O |
| OML.Maintain.5 | HAN Device shall supply a maintenance port for field diagnostics. | O | O | O | O | O | O | O | O | O | O | O |
| OML.Maintain.6 | HAN Device shall simulate events for diagnostic purposes. | O | O | O | O | O | O | O | O | O | O | O |
| OML.Maintain.7 | HAN Device shall supply network management functions for diagnostic purposes. | O | O | O | O | O | O | O | O | O | O | O |
| OML.Maintain.8 | For battery-powered devices, HAN Device shall communicate low battery state to the Consumer and Service Provider, if the HAN Device is Enrolled in a Service Provider program. | O | O | O | O | O | O | O | O | O | O | O |
| OML.Maintain.9 | HAN Device Manufacturer shall supply and support a flaw remediation process. | O | O | O | O | O | O | O | O | O | O | O |
| OML.Maintain.10 | HAN Device shall support a communications feedback mechanism. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| OML.Maintain.11 | HAN Device shall provide methods to service communication components, which are transparent to the consumer (e.g., Meter or other ESI replacement, device communication card replacement) – that is, don't require manual re-Commissioning and re-Registering of HAN Devices with the ESI. | BF | NA | NA | NA | NA | NA | BF | NA | NA | NA | NA |
| OML.Maintain.12 | HAN Device shall support remote methods to manage and update authentication materials (e.g. digital certificates) in HAN Devices requiring no Consumer intervention. | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| OML.Maintain.13 | Application shall support diagnostic messages when errors (e.g. HAN device faults, communications errors, etc.) are detected (Note: Need an additional requirement on what diagnostic messages may be received from the meter (i.e. C12.19 data)) | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |
| OML.Maintain.14 | ESI shall provide methods and information needed for the Service Provider to troubleshoot where a communication fault occurred between an Enrolled device and the ESI. | BF | BF | NA | NA | NA | NA | NA | NA | NA | NA | NA |
| OML.Maintain.15 | The HAN Device shall provide maintenance details (e.g., current date and time stamp for firmware revision number and one prior date and time stamp for firmware revision number). | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF | BF |

# Appendices

## Use Cases

### Other Use Cases and Documents Reviewed

In addition to the use cases included in this SRS, the OpenHAN TF reviewed the following use cases to identify any gaps in the OpenHAN requirements.

- ZigBee+HomePlug Joint Working Group Smart Energy Profile Marketing Requirements Document (MRD)

- J2836/1™ Use Cases for Communication between Plug-in Vehicles and the Utility Grid (Surface Vehicle Information Report).

- J2836/2™ Use Cases for Communication between Plug-in Vehicles and the Supply Equipment (EVSE) (Surface Vehicle Information Report).

- J2836/3™ Use Cases for Communication between Plug-in Vehicles and the Utility Grid for Reverse Power Flow (Surface Vehicle Information Report).

- Draft Requirements Specifications for Common Electricity Product and Pricing Definition – for NIST PAP03

- Draft Requirements Specifications for Common Scheduling Mechanism for Energy Transactions – for NIST PAP04

- Draft Requirements Specifications for Retail Standard DR Signals – for NIST PAP09

- Energy Information Standards (EIS) Alliance Customer Domain Use Cases v1.0

- California Energy Commission Requirements Engineering for the Advance Metering Infrastructure and the Home Automation Network (AMI-HAN) interface – February 2008

- Smart Grid White Paper: The Home Appliance Industry’s Principles & Requirements for Achieving a Widely Accepted Smart Grid  (AHAM White Paper)

- Distributed Energy Resources Contribution to OpenHAN;  EPRI/DOE PV/Storage Communiction Project

- Summary of Use Cases:  For Demand Responce Appliances Interface (EPRI Adapters)

### UCAIug OpenHAN Task Force Use Cases

The UCAIug OpenHAN Task Force developed these use cases as a way to bound the development of the system decomposition and requirements.  They are written at a very high level and are by no means comprehensive.  They are highly dependent on other back office systems and processes that are assumed to exist and be in place.  Each utility looking to implement a HAN or Service Provider wanting to offer HAN enabled programs will want to expand upon these use ases.

#### Methodology

These use cases focus on functional capabilities rather than device-specific capabilities.  Use case actors and scenarios may refer to a device, but the working group generally strove to describe the use case by its function.

#### Use Case Categories

Use cases are broken into four general use case categories:

- Load (kW) and Energy (kWh) Management

  - Voluntary Load Reduction

  - Mandatory Load Reduction

  - Energy Management System

- User Information

  - Complex Interactive

  - Simple One-way

- In-premises Metering

  - Energy Storage and Generation

  - Fixed HAN Device with Metering Capability

  - Mobile HAN Device with Metering Capability

- System Configuration and Management

- HAN Installation & Commissioning

- HAN Utility Registration (e.g. application/devices)

- HAN Device Remote Diagnostics and Troubleshooting

- HAN Device Diagnostics and Maintenance

- HAN Device Depot Configuration (optional)

#### Use Case Template

The template for use cases is as follows:

- Use Case Title

- Use Case Description

- Use Case Business Rules and Assumptions

- Use Case Scenarios (sequenced)

### Definitions / Assumptions / Actors

| Actor Name | Actor Type |
| --- | --- |
| Consumer | Person |
| HAN Devices | Devices |
| AMI | System |
| Metering System | System |
| Energy Services Interface (ESI) | Function |
| Customer Service System (CSS) | System |
| AMI and/or HAN Trust Center | System |
| Automated Data Collection System | System |
| Utility HAN | Devices |
| Consumer HAN | Devices |
| Pool Pump Controller | Devices |
| Customer Representative | Person or System |
| HAN Device Registration Application | Application |
| In-Home Display (IHD) | Device |
| Energy Management System (EMS) | Application |

### Use Case Assumptions

This section documents the assumptions on which the use cases are based.  It will be helpful to refer back to these throughout the rest of the specification.

- The Utility AMI-to-HAN interface exists.

- All communications between the Utility AMI network and HAN Devices pass through the ESI.

- A process exists to connect/bind the Consumer’s HAN Devices to the ESI.

- HAN communications are limited to the Consumer’s HAN Devices connected and bound to the ESI.

- HAN Devices have been safety tested and are approved by a well recognized test facility (Manufacturers to determine).

- HAN Devices comply with all applicable regional regulatory requirements (e.g., electrical, safety, and communications requirements).

- Additional certifications may be needed based on geographic and political boundaries.

- The original equipment manufacturer will provide operating manuals and technical support for HAN Devices to the end-use Consumer. This includes installing, operating, and troubleshooting materials.

- If net metering, the premises’ electric panel upgrade has occurred and the electrical circuits and wiring can handle the discharging process.

- For Mobile HAN Devices with Metering Capability (e.g., PEV), the vehicle has some onboard intelligence and communication capability.

- Consumers can override a non-emergency curtailment request (e.g., pricing events).

- Non-Interoperable HAN Devices will not participate in Utility-sponsored rates and programs.

- In order for Consumer HAN Devices to communicate with the Utility’s AMI network, suitable and appropriate security methods (including privacy protection) and capabilities within the AMI and HAN devices are implemented.

- The HAN SRS requirements apply to all Consumers, specifically to those under 200kW in demand.

- The ISO (i.e., transmission operator) and Utility have determined that demand response programs and events (e.g., Critical Peak Pricing) are necessary for grid management.

- Load control device(s) at the Consumer site will take action based on price or specific event (dependent on presence of the control devices and compliance with Utility requirements).

- The Consumer shall have the ability to pre-program the load control device at their site to respond to event messages and/or pricing.

- Consumers must Enroll their HAN Device in a demand response program to enable demand response communications between the Service Provider and the HAN Devices.

- Consumers may, but do not have to, negotiate another communication method (e.g., Internet) for price, consumption, load, event messages between their HAN devices and the Service Provider.

- Consumers will have the choice of which HAN Devices participate in any offered demand response program (subject to technical conformance with the offered demand response program from the Service Provider).  For example, the Consumer may have door open/close sensors attached to the same HAN as their lights and thermostat but may choose to only Enroll the lights and thermostat in the demand response program.

- If a HAN Device requires Registration with the ESI, the device is expected to contain volatile and non-volatile memory.  A portion of the non-volatile memory will retain Registration information in case there is a loss of power.  Once power and communication is restored to the device, it will automatically re-Register itself based upon the last known “good” registration.

- The HAN Device is compatible and able to interoperate with the Utility’s AMI system.

- The AMI System supports meter device-specific, Consumer-specific and location-specific rates/billing. (e.g. PEV).

- Display options are supported as required for the specific application including, but not limited to, display of Utility-provided data.

- FHDMC have a certification process for meter accuracy as required by the Utility or jurisdiction.

- FHDMC may supply capabilities beyond basic metering (e.g., measurement, monitoring, and device state information).

- AMI System may provide data to the FHDMC.

- MHDMC has a certification process for meter accuracy as required by the Utility or jurisdiction.

- The MHDMC and premises are properly authorized to operate within the jurisdiction and Utility.

- AMI System may provide data to the MHDMC.

- MHDMC records bi-directional MHDMC usage for audit purposes.

- Any required installation will meet the appropriate building and safety codes.

- Individual Service Providers may only require a subset or additional requirements from those provided in this document.

- This is not a static document and the list of requirements may be updated from time to time.

- Specific examples given in the document are exactly that. Innovation in the market place is always encouraged.

- While specific requirements may not be economically appropriate in today’s market, it is assumed that these will become more viable over time as technology and availability improve.

### Load and Energy Management

#### Voluntary Use Case for Registered HAN Devices

Description

A major benefit of the HAN is that it supports Consumer awareness of his instantaneous kWh electricity pricing, consumption, projected costs, rate tiers, and voluntary load reduction program events, and it can support Service Providers in the achievement of load reduction needs. As Utilities see increased electricity demand on the grid, energy shortages may result, therefore triggering the need for Service Providers to reduce energy consumption in support of grid stability. The Service Provider will help facilitate load reduction at the consumer’s site by communicating instantaneous kWh pricing and voluntary load reduction program events to the Consumer and to various enabling devices Registered to the ESI, each of which contains the requisite  functionality at the Consumer’s site.  Voluntary load reduction events may be scheduled with a large amount of advanced notice (24 hrs) or near real-time.  For the Service Provider to receive the desired Consumer response, it must provide timely pricing, event, and usage information.

Related to this scenario is the measurement of the response to financial incentives, energy price adjustments, and other voluntary demand response programs. The Consumer responses will be used to determine how and/or if Consumers have responded to a pricing event, if the Service Provider needs to launch other demand response events to achieve the needed demand reduction, and help the Service Provider determine how to structure future voluntary load reduction programs, to ensure the Service Provider receives the best Consumer response.

This scenario includes the actual mechanism to distribute price signals and voluntary load reduction events to Consumers (direct electronic delivery to the Consumer meter or display device within the home/business, automated telephone calls, e-mail, pager, commercial broadcast radio, newspapers, etc.).  It includes the mechanism by which the HAN will display current pricing and voluntary load reduction event information within the consumer’s home/business.  The Service Provider will initiate automatic load reduction at the Consumer’s premises by communicating event and pricing information to Consumer HAN Devices, which will take action based on the Consumer’s predefined settings.  The Consumer will be able to program their load control specifications and refuse Service Provider load reduction requests. The Consumer will also be able to manually curtail load based upon informational messages communicated to them from a Service Provider.

This scenario also includes the actual Home Area Network functionality for Consumer HAN Devices and describes the scenario for separate HAN Devices classes and AMI-related behavior of the HAN Devices.

Troubleshooting for installation, registration, and event failure should refer to the HAN Use Case – Maintenance

Use Case Business Rules and Assumptions

- If the HAN Device offers a display, it is capable of displaying actual price of power for a unit of time and/or providing an indication of relative price (e.g., low, medium, high, critical).

- The HAN Device is capable of differentiating between emergency/reliability and/or price-response event signals.

- If the HAN Device offers a display, it is able to display messages comprised of alphanumeric characters, as delivered or triggered remotely from the Service Provider.

- Certain HAN Devices can distinguish or support various event types and take appropriate action based on the event.

- The Consumer must Enroll their device in a Service Provider demand response program or tariff and the HAN device must be Registered with the ESI for the HAN Device to confirm its successful actuation of the event.

Use Case Scenario

Service Provider initiates a voluntary demand response event (e.g., Critical Peak Pricing Event).

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| The Service Provider determines the need for a demand response event. | HAN Device | The Installation use case is successfully completed. The Commissioning use case is successfully completed. The Registration use cases is successfully completed. The HAN device has either been pre-programmed to respond appropriately to price, consumption, load or event messages and/or the Consumer has manually programmed the HAN Device. | The Consumer will have been notified of an event, the event will have been autonomously launched by the Service Provider’s system, the HAN Devices will have actuated and the event will have ended and the Consumer equipment returned to its original state. |

Steps for this scenario

These steps apply for both event actuation and restoration to initial HAN Device state.

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | Service Provider | Service Provider sends a message to the Consumer’s display device and/or control equipment, via ESI for Consumer viewing, that an event start time has arrived. |
| 2 | ESI/HAN Devices | TThe Consumer’s HAN Device receives the message, update the event status (e.g. to active) and the HAN Device will take Consumer preprogrammed action (e.g. raise thermostat by 4 degrees, lower thermostat to original state) reacting to pricing and/or event type. |
| 3 | Consumer | Consumer may choose not to participate in economic or pricing event. Consumer overrides the automatic HAN Device actuation sequence. |
| 4 | ESI/HAN Devices | The Consumer's HAN Device may send a receipt that it received the event message to the Service Provider (dependent on type of Consumer equipment), via the ESI. If a message is sent to the ESI by the HAN Device, the message includes the device ID, message received date/time (in UTC time) by the display/control equipment and action taken (e.g. receive event info, raised thermostat by 4 degrees, A/C off) and date/time action taken. The HAN Device may also log events for future Consumer analysis and audit or send events to a different HAN Device to log events. If the Consumer overrode the event, the message will signify message received but overridden by Consumer. |
| 5 | Service Provider | Curtailment period ends and Service Provider sends the command to restore HAN Devices to previous state. |
| 6 | HAN Devices | HAN Devices may restore load on a random restoration schedule so as to create minimal impact to the distribution system. |
| 7 | HAN Devices | HAN Devices respond back to the ESI confirming the receipt of event end notification. |

#### Mandatory Use Case

Description

The mandatory load and energy management use case refers to demand response resources dispatched for reliability purposes. These events are mandatory due to the potential of the demand for power exceeding supply as a result of unexpected power plants going offline or congestion in transmission and/or distribution lines. The Consumer may be (1) Enrolled in, or (2) as condition of service, be defaulted on a mandatory demand response program used for grid management. For voluntary Enrollment in a Service Provider’s program, the Consumer is generally compensated with a credit on her monthly bill.

Control of a Consumer’s HVAC can be accomplished via a PCT Enrolled in a Service Provider program. Other HAN Devices may include an EMS, a pool pump controller, A/C switch, or even a passive device (one that does not actually shed load) such as an IHD that warns of potential power shortages in the near future or a load shed event in progress. The PCT may act as both a load shedding and passive/informational device. The ESI will forward curtailment messages to the HAN Device(s) capable of receiving this.  Upon receipt and successful execution of the load shed, the HAN Device(s) may return an acknowledgement back to the ESI, including logging and device status.

Mandatory/emergency load and energy management events may not allow Consumers the option to override the load shed request. The Service Provider relies on firm load shed to avert rotating outages. Giving Consumers the option to override a mandatory load shed request increases the possibility a complete power outage. For public safety purposes, the Service Provider must be able to immediately remove a Consumer off the program due to a medical emergency and restore operation to the HVAC as soon as possible.

The Service Provider will be informed by at least two levels of advanced warning:

- Long term (24 hours) and short term (few hours notice) predicted energy shortages

- Emergency shortage (few minutes notice)

The following is a list of use case scenarios:

- Predicted mandatory load curtailment for grid management – Warnings are issued for possible electrical system overload or potential lack of generation resources.

- Consumer requests an immediate opt-off due to a medical emergency.

Use Case Business Rules and Assumptions

- Medical Opt-out devices are pre-registered or may register upon Consumer contacting the Service Provider to exclude their HAN device from mandatory events.

Use Case Scenarios

Scenario 1

Service Provider initiates a mandatory demand response event due to a possible electrical system overload or potential generation/demand imbalance.  Warnings issued to Consumers are optional.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| The Service Provider determines the need for a demand response event. | HAN Device | The Installation use cases are successfully completed. The Commissioning use cases are successfully completed. The Registration Use Cases are successfully completed. The HAN Device has been programmed by the Service Provider or Consumer to shed load on command. | The Consumer may have been notified of an event, the event will have been autonomously launched by the Service Provider’s System, the HAN Devices will have actuated and the event will have ended and the Consumer equipment returned to its original state. |

Steps for this scenario

These steps apply for both event actuation and restoration to initial HAN Device state.

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1a | Service Provider | Service Provider anticipates the need to dispatch a mandatory curtailment program. |
| 1b | Service Provider | Service Provider anticipates the need to dispatch a mandatory curtailment program and sends a warning message to the Consumer. |
| 2 | HAN Devices | HAN Devices receive the warning message that a mandatory event occurred and displays the appropriate message (e.g., lights the appropriate LED) (** optional step **) |
| 3 | Service Provider | Service Provider sends a mandatory load shed message. |
| 4 | HAN Devices | HAN Devices receive the mandatory load shed notification of the scheduled curtailment. |
| 5 | HAN Devices | Han Devices enter appropriate “off” and/or “energy minimum” state(s). |
| 6 | HAN Devices | HAN Devices respond back to the ESI, confirming the receipt of the mandatory load shed notification. |
| 7 | Service Provider | Curtailment period ends and Service Provider sends the command to restore HAN Devices to previous state. |
| 8 | HAN Devices | HAN Devices restore load on a random restoration schedule so as to create minimal impact to the distribution system. |
| 9 | HAN Devices | HAN Devices respond back to the ESI, confirming the receipt of event end notification. |

Scenario 2

Utility initiates a mandatory demand response event due to a possible electrical system overload or potential lack of generation resources.  Consumer calls the Utility to opt-out of the program due to a medical emergency.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| The Service Provider determines the need for a demand response event. | HAN Device | The Installation use cases are successfully completed. The Commissioning use cases are successfully completed. The Registration use cases are successfully completed. The HAN Device has been programmed by the Service Provider or Consumer to shed load on command. | The Consumer is opted-out of the program and the HAN device being controlled is restored to the initial state. |

Steps for this scenario

These steps apply for both event actuation and opting the Consumer out of the program.

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | HAN Devices | HAN Devices receive the notification from the Service Provider to start the curtailment. |
| 2 | HAN Devices | HAN Devices enter appropriate “off” and/or “energy minimum” state(s). |
| 3 | HAN Devices | HAN Devices respond back to the ESI, confirming the receipt of the mandatory load shed notification. |
| 4 | Consumer | Consumer contacts the Service Provider to restore load. |
| 5 | Service Provider | Service Provider sends the message to restore load to the appropriate HAN Devices. |
| 6 | HAN Devices | HAN Devices immediately restore load. |
| 7 | HAN Devices | HAN Devices respond back to the ESI, confirming the device has received the command to restore load. |
| 8 | HAN Devices | HAN Devices un-Enroll from mandatory load and energy management program. |

### Energy Management System

Description

Energy Management System (EMS) integrates with the respective HAN, Enrolls in a Service Provider’s program, and responds to commands to drop load for grid reliability or price responsive programs.

Use Case Business Rules and Assumptions

- The EMS is aware of or can retrieve the types of HAN Devices and the status of those devices connected to the HAN upon Registration or change-out. (e.g., fridge on/off).

- EMS controls production, consumption, and storage within the HAN (e.g., Controls charging/discharging of an Electric Vehicle).

- The EMS can be pre-programmed to respond to Service Provider signals and commands (e.g., reliability event).

- Use case does not imply the Service Provider’s preferred configuration or communication for reliability programs (e.g., Service Provider requires HAN device Registration and Enrollment).

Use Case Scenario

Service Provider calls a demand response event and controls load by communicating with the EMS through the ESI.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| The Service Provider determines the need for a demand response event. | EMS | The Installation use cases are successfully completed. The Commissioning use cases are successfully completed. The Registration use cases are successfully completed. | EMS curtails load until event is concluded. |

Steps for this scenario

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | Service Provider | Service Provider sends notification of event and for price response case, the appropriate pricing information to the EMS. |
| 2 | EMS | The EMS sends a signal to all HAN devices under its control and attempts to control consumption or production. |
| 3 | EMS | The EMS responds back with an acknowledgment message (e.g., Consumer override, load successfully dropped by x%, etc) to the ESI. |
| 4 | Service Provider | The Service Provider sends a restore signal to the ESI upon conclusion of the event. |
| 5 | EMS | The EMS is restores HAN device load to the pre-event state. |

### User Information

Consumer receives Service Provider initiated messages and electric usage updates via an In Home Display (IHD)

Description

An IHD is Commissioned and Registered with the Utility ESI and is Enrolled in a Service Provider program.  The Service Provider provides usage information and sends messages to the Consumer. The AMI meter provides real-time usage data to the IHD.

Use Case Scenarios

A simple IHD provides basic display of Service Provider-generated price and Consumer-specific usage information

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| Consumer obtains IHD. | Consumer | The Installation use cases are successfully completed. The Commissioning use cases are successfully completed. The Registration use cases are successfully completed Installer installs IHD in the premises The IHD has either been pre-programmed to respond appropriately to price, consumption, load or event messages and/or the Consumer has manually programmed the IHD. | none |

Steps for this scenario

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | IHD | The IHD indicates the status of the communication link with the ESI. |
| 2 | IHD | Displays Service Provider-generated messages. (e.g. emergency event) |
| 3 | IHD | The Registered IHD requests Consumer-specific real-time data (e.g., demand, electric energy usage) from the AMI meter |
| 4 | AMI meter | AMI meter provides usage data as requested. (e.g., demand (watts) every 6 seconds) |

### Energy Storage and Generation

Consumer uses a storage or generation unit to provide energy to their home or the grid.

Description

The Energy Supplying Unit (ESU) connects with the premises HAN, the ESI, and the electric system (home, vendor, or Utility’s). The ESU identifies itself and the account it is associated with, and provides energy to the home or grid. This use case also describes the scenarios documented in The Sub Metering Use Case and The Load and Energy Management Use Cases, in that the ESU behaves according to these use cases.

Use Case Business Rules and Assumptions

- Energy Supplying Unit (ESU) already contains energy.

- All Utility safety measures and rules are in place to provide power to the grid.

Use Case Scenario

The following scenario addresses storage and generation for the purpose of providing energy to the home or grid.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| Incentives or Utility requirements are in place for providing energy to the home or grid. | ESU | The Installation use cases are successfully completed. The Commissioning use cases are successfully completed. The Registration use cases are successfully completed. Units are transfer ready and properly connected. | Energy is successfully transferred. |

Steps for this scenario

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | EMS, ESI, other entity, ESU (Consumer acts on EMS or ESU) | Signals ESU to transfer energy. |
| 2 | ESU | Performs a self-check for sufficient capacity and generation readiness. |
| 3 | ESU | Transfers energy. |
| 4 | EMS, ESI, other entity, ESU (Consumer acts on EMS or ESU) | Signals to end transfer event. (e.g., due to drop in price, inadequate energy availability, Consumer preference, or Utility preference) |
| 5 | ESU | Ceases transfer of energy. |

### Fixed HAN Devices with Metering Capability

Description

The FHDMC connects with the premises HAN and identifies itself and the account it is properly associated with to the Service Provider, where premises owner’s charges are reconciled.  This use case also describes the scenario documented in The Load and Energy Management Use Cases, in that the FHDMC may behave according to that use case. The following scenario is defined: bi-directional metering (i.e., DER) and third-party (i.e., gas meter).

Use Case Scenario

The following scenario addresses FHDMC, where bi-directional electric and third-party metering takes place.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| FHDMC is connected and enabled | FHDMC | The Installation use cases are successfully completed. The Commissioning use cases are successfully completed. The Registration use cases are successfully completed. | Device owner meters the device and gets billed for the appropriate amount on their electricity bill or other third-party bill. |

Steps for this scenario

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | FHDMC | Device indicates positive status of the communication link with the appropriate ESI. |
| 2 | FHDMC | Device provides the Consumer (end user) with the appropriate information. (e.g. current rate of consumption, etc) |
| 3 | FHDMC | Device accumulates usage (delivered or received) and returns the information to the ESI. |
| 4 | FHDMC | (optional) The device provides the ESI with additional state information if applicable (e.g. state of charge of a storage device). |

### Mobile HAN Device with Metering Capability

Description

The MHDMC connects with the premises Home Area Network (HAN), identifies itself and the account it is properly associated with the Service Provider. MHDMC’s and premises owner’s charges are reconciled, as applicable.  This use case also describes the scenario documented in The Load and Energy Management Use Cases, in that the MHDMC may behave according to that use case.  The mobile (e.g. any Consumer PEV) scenario is defined in this document.

Use Case Scenario

The following scenario addresses MHDMC, where bi-directional electric metering takes place.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| MHDMC is connected and enabled temporarily | MHDMC | The Installation use cases are successfully completed. The Commissioning use cases are successfully completed. The Registration use cases are successfully completed. The MHDMC is enrolled in a Service Provider program | MHDMC owner and premises owner bills are properly reconciled. |

Steps for this scenario

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | MHDMC | Device indicates positive status of the communication link with the appropriate ESI. |
| 2 | MHDMC | (optional) Device provides the Consumer (end user) with the appropriate information. (e.g., percentage of charge, current rate of consumption, etc) |
| 3 | MHDMC | Device indicates to the user whether the MHDMC is recognized by the Service Provider (i.e., for billing purposes) |
| 4 | MHDMC | Device accumulates usage (delivered or received) and returns the information to the ESI. |
| 5 | MHDMC | (optional) The device provides the ESI with additional state information if applicable (e.g., state of charge of a storage device). |

### System Configuration and Management

#### HAN Installation and Commissioning

Description

The installation and commissioning use cases covers the activities associated with physical installation and Commissioning.   Commissioning establishes the communication path to the ESI.  Once this process is complete then a HAN device can be Registered with the ESI. The Registration and Commissioning processes are actually discrete operations.

This use case covers all HAN Devices including, but not limited to, PEV, PCT, pool pump controller, EMS, etc.  Premises commissioning ignores mobility related functions (e.g., PEV moving from premises to premises).  That is, Mobility is an aspect of Enrollment.

The Installer may perform other diagnostics that the meter and HAN Devices cannot perform by itself.  These steps are specific to the underlying technology and not covered in the high level use of the system.

It is important to note this use case covers all the staging scenarios, including HAN Devices (e.g., PCT), Service Provider delivers additional HAN Devices and Commissions to the existing HAN at time of meter installation, and Consumer Commissions the HAN Devices to the ESI after installation of an AMI System.

Use Case Business Rules and Assumptions

- For control devices, device is installed in-line at the appropriate control point (e.g., in series with the information or energy flow).

- All appropriate safety precautions are taken (e.g., qualified electrician is required for certain installation routines).

- Devices and applications are procured or provided through multiple distribution channels (e.g., retail, Utility-provided, etc.).

- Devices meet all applicable electrical, safety, and communications laws.

- Pre-commissioning routines have been successfully executed (e.g., pre-placed network key has been loaded).

Use Case Scenario

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| Consumer takes possession of HAN Device. | Consumer or Installer | ESI with two-way communications capability is present. | The Consumer device has been added to the local HAN network and has established communications with the ESI (i.e., the HAN has been established). |

| Step | Actor | Description of the Step | Additional Notes |
| --- | --- | --- | --- |
| 1 | Installer | Installer locates appropriate installation point. | Appropriate installation point considerations includes: signal strength at location, appropriate control point, etc.) |
| 2 | Installer | Device is installed. | Installation includes removing previous equipment and connecting the device to external power (if necessary) |
| 3 | HAN Device | HAN Device performs self-check and reports results to installer. | In certain installation instances, a field tool can assist in the device initialization and configuration. |
| 4 | Installer | InstallIInstaller inputs any required pre-commissioning materials (e.g., physical location, LAT/LONG, etc), |  |
| 5 | Installer | Installer enters commissioning data (e.g., network key) or performs any necessary commissioning actions (e.g., proximity) |  |
| 6 | HAN Device | HAN Device notifies the ESI or other network coordinator of its presence on the network. | This process is part of the technology-specific beaconing and discovery process. If a third-party device performs the actual commissioning, then the ESI needs to be notified through a separate process. |
| 7 | ESI | ESI acknowledges notification and authenticates network credentials | Authentication failures should be logged and a notification sent to authorized user. This is necessary due to possible security implications |
| 8 | ESI | Sends HAN Device any necessary configuration data (e.g., preferred communication paths, updates, etc.) |  |
| 9 | ESI | Device is added to the network. |  |
| 10 | HAN Device | HAN device notifies the Installer (successful Commissioning) |  |
| 11 | Consumer | Consumer contacts Service Provider and Service Provider provides Consumer the registration instructions *Optional* | This is so the Consumer can register their HAN Device in a Service Provider program |

#### HAN Device Registration

Description

The Registration use case covers device–to-ESI Registration.  As a prerequisite to the use case, the device has already been Commissioned to the local network.  Whereas, the installation and commissioning use case resulted in admission to the local HAN, the Registration use case covers the steps necessary to Register a HAN Device on the ESI.  This implies that Registration is a higher level function.

The Registration process establishes a directional trust (i.e. Mutual Authentication) between the ESI and the HAN device.  The Registration use case does not cover details associated with Enrollment.  These back office steps, while necessary, are outside the scope of this activity.

Use Case Business Rules and Assumptions

- Local HAN commissioning establishes the base communication capability, Registration rides on top of this commissioning and Enrollment rides on top of Registration.

Use Case Scenario

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| Consumer wants HAN devices to participate in two-way communications with the ESI and other HAN devices | HAN Device | The Installation and Commissioning use cases have been successfully completed. | The Consumer device will be registered with the ESI. All communications with the device will be protected, authenticated and acknowledged. |

Steps for this scenario

| Step | Actor | Description of the Step | Additional Notes |
| --- | --- | --- | --- |
| 1 | Consumer | Consumer makes decision to join their HAN device to the Utility ESI to enable the HAN device to receive energy information from the AMI meter. |  |
| 2 | Customer Representative | Customer Representative receives notification from Consumer that Consumer is ready to have one (or more) of their HAN Devices Registered with the Utility ESI. | This process can be automated through a web based interface. (i.e., the web application is the Customer Representative) |
| 5 | Customer Representative | Customer Representative gets appropriate Consumer information (address, verification information, etc) and locates Consumer information from CSS |  |
| 6 | Customer Representative | Customer Representative activates HAN Device Registration process |  |
| 7 | HAN Device Registration process | HAN Device Registration initiates the HAN discovery process which identifies the Consumer’s HAN Device. | If this process fails then the device has not been commissioned. |
| 8 | Consumer | Consumer provides unique Registration information from HAN Device (e.g., registration key, serial number). |  |
| 9 | HAN Device Registration process | HAN Device Registration process attempts to create an authenticated link with HAN Device using registration information. | This step can be staged. . |
| 10 | HAN Device Registration process | HAN Device Registration process sends appropriate registration, configuration, and initiation messages to all applicable HAN and ESI devices. |  |
| 11 | HAN Device(s) | HAN Device(s) acknowledges activation and readiness state(s) to HAN Device Registration process. |  |
| 12 | HAN Device Registration process | HAN Device Registration process communicates all necessary information to CSS and other applicable systems for storage and any required internal registrations |  |
| 13 | Customer Representative | Customer Representative confirms with the Consumer that HAN Devices have now been Registered. |  |
| 14 | HAN Device | HAN Device provides notification to the Installer of its successful Registration | The HAN device is now eligible to Enroll in a Service Provider program and to receive authorized information (e.g. meter usage data, etc.) |

#### HAN Device Remote Diagnostics and Troubleshooting

Description

This use case discusses the scenario associated with remote Service Provider diagnostics.  This use case does not cover all resolution scenarios.  Resolution scenarios are specific to the underlying technology and based on warranties, ownership and accountability.  These discussions are outside the scope of the base use case.

Use Case Business Rules and Assumptions:

- The scope of Service Provider responsibility for diagnostics and maintenance is limited.

- Accountability for troubleshooting is driven by several factors not addressed in these use cases.

Use Case Scenario

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| A HAN device fails to receive Service Provider communications. | HAN Device | The Installation Commissioning and Registration Use Cases have been successfully completed. | The Consumer device is returned to an operational state. |

Steps for this scenario

| Step | Actor | Description of the Step | Additional Notes |
| --- | --- | --- | --- |
| 1 | Consumer | Contacts Customer Representative. |  |
| 2 | Customer Representative | Identifies Consumer (verifies) and records Consumer issue. |  |
| 3 | Customer Representative | Retrieves Consumer account (e.g., billing data, device registrations, program registrations, etc.) |  |
| 4 | Customer Representative | Validates account status |  |
| 5a | Customer Representative | Corrects account or registration information (e.g., updates billing, updates program participation) and ends call. |  |
| 5b | Customer Representative | Starts remote diagnostics application. |  |
| 6 | Remote Diagnostics application | Retrieves device commissioning data from ESI. |  |
| 7 | Remote Diagnostic Application | Attempts to connect to HAN Device |  |
| 8a | Remote Diagnostic Application | Connection successful – commissioning confirmed, |  |
| 8b | Remote Diagnostic Application | Connection unsuccessful – repeat installation commissioning use case |  |
| 9 | Customer Representative | Notifies Consumer that the Service Provider can or can not communicate with the HAN Device |  |
| 10a | Customer Representative | Schedules onsite maintenance | See HAN Device Diagnostics and Maintenance use case |
| 10b | Customer Representative | Starts Registration Diagnostics Application |  |
| 11 | Remote Diagnostic Application | Check application layer communication (e.g., send registered control signal) |  |
| 12 | Customer Representative | Notifies the Consumer that the device is functioning or is not functioning correctly |  |
| 13a | Customer Representative | Registration communication unsuccessful – execute registration use case | See HAN Device Diagnostics and Maintenance use case |
| 13b | Customer Representative | Schedules onsite maintenance | See HAN Device Diagnostics and Maintenance use case |

#### HAN Device Diagnostics and Maintenance

Description

This use case discusses the scenario associated with Service Provider maintenance and onsite diagnostics.  This use cases does not cover all resolution scenarios.  Resolution scenarios are specific to the underlying technology and based on warranties, ownership, and accountability.  These discussions are outside the scope of the base use case.

Use Case Business Rules and Assumptions

- The scope of Service Provider responsibility for diagnostics and maintenance is limited.

- Accountability for troubleshooting is driven be several factors not addressed in these use cases.

Use Case Scenario

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| A HAN device fails to communicate with the Service Provider | HAN Device | The Installation, Commissioning and Registration use cases have been successfully completed or attempted | The Consumer device is returned to an operational state. |

Steps for this scenario

| Step | Actor | Description of the Step | Additional Notes |
| --- | --- | --- | --- |
| 1 | HAN Device | HAN Device(s) cannot communicate with the Service Provider. |  |
| 2 | HAN Device | HAN Devices notifies installer of communication failure. |  |
| 3 | Consumer or Installer | Installer or Consumer uses field tool or HAN Device diagnostic capabilities to test network communication. |  |
| 4a | Consumer or Installer | Installer validates whether device is faulty. |  |
| 4b | Consumer or Installer | Installer validates adequate HAN network connectivity exists. |  |
| 5a | Consumer or Installer | Installer replaces HAN Devices, if appropriate. |  |
| 5b | Consumer or Installer | Customer Reports marginal coverage if appropriate. |  |
| 6 | Consumer or Installer | Performs problem and device specific resolution (e.g., installs a bridging device to mitigate poor signal strength, installs a higher power or more capable device, etc.) |  |

#### HAN Device Depot Configuration (optional)

Description

The device depot configuration use case discusses the steps associates with the preparation of the HAN Device (e.g., required certifications, pre-placed materials, or support modes).  The depot (e.g., factory) steps show any necessary Utility to manufacturer interactions.

Use Case Business Rules and Assumptions

- HAN Devices can be configured prior to installation.

- Compliance implies compatibility.

Use Case Scenario

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| A HAN Device has been produced. | Manufacturer | Device supports required configurations and materials. | The HAN device is ready for installation and Commissioning. |

Steps for this scenario

| Step | Actor | Description of the Step | Additional Notes |
| --- | --- | --- | --- |
| 1 | Manufacturer | Checks registration and authentication requirements (UtilityAMI). |  |
| 2 | Manufacturer | Determines any special destination-specific configurations (Optional) |  |
| 3 | Manufacturer | Request commissioning and registration materials (e.g., Keys, certificates, methods/functions) |  |
| 4 | Manufacturer | Adds registration specific materials/methods. |  |
| 5 | Manufacture | Adds appropriate compliance/certification labeling. |  |
| 6 | Manufacturer | Notifies or provides destination Utility with materials (e.g., keys) (Optional) |  |

4.2   HAN Security Considerations

This section considers the potential impact of HAN security compromise in the context of four categories of compromise scope. These categories provide rough orders of magnitude with which the security engineer may associate tangible undesirable outcomes and therefore justify certain costs associated with the implementation of controls. For each scope of compromise the tables below display possible impact to the different stakeholders surrounding a Home Area Network (HAN). The impact definitions can be found in the Federal Information Processing Standards (FIPS) Publication number 199 and are listed below:

The potential impact is LOW if—

− The loss of confidentiality, integrity, or availability could be expected to have a limited adverse effect on organizational operations, organizational assets, or individuals.

AMPLIFICATION: A limited adverse effect means that, for example, the loss of confidentiality, integrity, or availability might: (i) cause a degradation in mission capability to an extent and duration that the organization is able to perform its primary functions, but the effectiveness of the functions is noticeably reduced; (ii) result in minor damage to organizational assets; (iii) result in minor financial loss; or (iv) result in minor harm to individuals.

The potential impact is MODERATE if—

− The loss of confidentiality, integrity, or availability could be expected to have a serious adverse effect on organizational operations, organizational assets, or individuals.

AMPLIFICATION: A serious adverse effect means that, for example, the loss of confidentiality, integrity, or availability might: (i) cause a significant degradation in mission capability to an extent and duration that the organization is able to perform its primary functions, but the effectiveness of the functions is significantly reduced; (ii) result in significant damage to organizational assets; (iii) result in significant financial loss; or (iv) result in significant harm to individuals that does not involve loss of life or serious life threatening injuries.

The potential impact is HIGH if—

− The loss of confidentiality, integrity, or availability could be expected to have a severe or catastrophic adverse effect on organizational operations, organizational assets, or individuals.

AMPLIFICATION: A severe or catastrophic adverse effect means that, for example, the loss of confidentiality, integrity, or availability might: (i) cause a severe degradation in or loss of mission capability to an extent and duration that the organization is not able to perform one or more of its primary functions; (ii) result in major damage to organizational assets; (iii) result in major financial loss; or (iv) result in severe or catastrophic harm to individuals involving loss of life or serious life threatening injuries.

Table 14: Scope of Compromise

| Scope of Compromise | Concerns |
| --- | --- |
| Singular device within a single HAN | Magnitude of associated load or energy supply | Can the associated load or energy supply be manipulated? |
|  | Credential / key information | Can the credential or key information be obtained and re-used by unauthorized entities? |
|  | False / misleading messages for humans as well as other devices | Can humans and/or other devices be misled (i.e. tricked) into taking undesirable actions? |
|  | Metrology / revenue information | Can metrology or revenue information be falsified? |
|  | Personally Identifiable information (PII) theft | Can PII be exposed to unauthorized entities? |
|  | Loss / destruction of device functionality (includes human safety) | Can a device’s physical capabilities be turned against itself, other devices, or humans? |
|  | Impact Ratings |
|  | Stakeholder | Impact |
|  | Utility / Service Provider | Low |
|  | Consumer | Moderate |
|  | Premise owner | Low |
|  | Vendor | Low |
|  | Regulator / policy-maker | Low |
| Scope of Compromise | Concerns |
| Multiple devices within a single HAN, up to and including all devices within a single HAN | Amplification of concerns for a single device | Can the associated load or energy supply be manipulated? |
|  | Impact Ratings |
|  | Stakeholder | Impact |
|  | Utility / Service Provider | Low |
|  | Consumer | High |
|  | Premise owner | Low |
|  | Vendor | Low |
|  | Regulator / policy-maker | Low |

| Scope of Compromise | Concerns |
| --- | --- |
| Multiple devices within multiple HANs (single neighborhood scale) | Service availability to neighbors (i.e. Transformer fuse) | Can enough load be shed or energy supplied to blow the transformer fuse for the associated neighborhood? |
|  | Disruption of HAN functionality /Loss of consumer confidence/ Loss of reputation | Can enough devices be caused to misbehave such that the collective behavior causes a nuisance or that the public (or a portion thereof) loses trust in the technology. |
|  | Damage to a distribution system asset | Can enough load be shed, energy supplied, or fluctuation be introduced (i.e. cycling) to damage a distribution asset or otherwise shorten its life expectancy? |
|  | Synchronistic events (e.g. resource contention) | Can devices be manipulated by timing of normal otherwise normal operations in such a way as to overload system resources? |
|  | Impact Ratings |
|  | Stakeholder | Impact |
|  | Utility / Service Provider | Moderate |
|  | Consumer | High |
|  | Premise owner | Moderate |
|  | Vendor | Low |
|  | Regulator / policy-maker | Low |
| Scope of Compromise | Concerns |
| Large number of HANs (multiple neighborhoods) | Denial of service to wide areas | Can capabilities/benefits of the technology be blocked for a substantial geographic area? |
|  | Damage to a distribution system asset | Can enough load be shed, energy supplied, or fluctuation be introduced (i.e. cycling) to damage a distribution asset or otherwise shorten its life expectancy? |
|  | Loss of revenue | Can the technology be manipulated in such a way as to prevent an organization from being able to realize fiscal benefit of their investment or meet contractual obligations? |
|  | Misuse / abuse of system | Can the technology be manipulated in such a way as to create widespread undesirable effects? |
|  | Breach of sensitive information (e.g., PII, corporate sensitive information, etc.) | Can a large-scale breach expose sensitive information to unauthorized entities? |
|  | Impact Ratings |
|  | Stakeholder | Impact |
|  | Utility / Service Provider | High |
|  | Consumer | High |
|  | Premise owner | High |
|  | Vendor | High |
|  | Regulator / policy-maker | High |

| Scope of Compromise | Concerns |
| --- | --- |
| Extension into a network beyond the HAN | Compromise of command and control | Can the ESI be used as a conduit to facilitate usurpation of command and control (i.e. operation of the AMI network or capabilities such as remote disconnect)? |
|  | Using the end point gateway to affect denial of service to a significant area | Can the ESI be leveraged to launch a wide-scale attack on a substantial portion of the AMI network? |
|  | Malicious use of devices upstream, route malicious payload upstream, affect or alter command and control upstream, or affect/alter back-end office systems upstream | Can a connection to a 3rd party service provider be leveraged to compromise said service provider? Can the technology and communication channels be used as a conduit for attacks against other utility/service provider systems? |
|  | Damage to a distribution system asset | Can enough load be shed, energy supplied, or fluctuation be introduced (i.e. cycling) to damage a distribution asset or otherwise shorten its life expectancy? |
|  | Loss of revenue | Can the technology be manipulated in such a way as to prevent an organization from being able to realize fiscal benefit of their investment or meet contractual obligations? |
|  | Misuse / abuse of system | Can the technology be manipulated in such a way as to create widespread undesirable effects? |
|  | Breach of sensitive information | Can a large-scale breach expose sensitive information to unauthorized entities? |
|  | Impact Ratings |
|  | Stakeholder | Impact |
|  | Utility / Service Provider | High |
|  | Consumer | High |
|  | Premise owner | High |
|  | Vendor | High |
|  | Regulator / policy-maker | High |

# Footnotes

NIST Framework and Roadmap for Smart Grid Interoperability Standards, Release 1.0, page 35

NIST Framework and Roadmap for Smart Grid Interoperability Standards, Release 1.0, page 35

Definition of DER provided by the Department of Energy, http://www1.eere.energy.gov/femp/pdfs/31570.pdf

U.S. Department of Energy Office of Electricity Delivery and Energy Reliability Smart Grid Investment Grant Program: DE-FOA-0000058, page 22

Section 1306 of the Energy Independence and Security Act of 2007, Public Law 110-140 (EISA)

EISA Title Xiii, Section 1305

NIST Framework and Roadmap for Smart Grid Interoperability Standards, Release 1.0., page 33

U.S. Department of Energy Office of Electricity Delivery and Energy Reliability Smart Grid Investment Grant Program: DE-FOA-0000058, page 7

Second Draft NISTIR 7628 Smart Grid Cyber Security Strategy and Requirements – Feb 2010, page 12 and NIST Framework and Roadmap for SG Interoperability Standards, Release 1.0, page 112

Ibid

Ibid

Ibid, page 76

FIPS 199, Standards for Security Categorization of Federal Information and Information Systems, February 2004, pages 2-3

Ibid, Table 3.5 – Allocation of Technical Requirements to the Logical Interface Categories pages 93-95

Adapted from Southern California Edison (SCE) Edison SmartConnect’s™ Lifecycle Hierarchy

NIST Framework and Roadmap for Smart Grid Interoperability Standards, Release 1.0. http://www.nist.gov/public_affairs/releases/upload/smartgrid_interoperability_final.pdf

Recovery Act Financial Assistance, Funding Opportunity Announcement. U. S. Department of Energy, Office of Electricity Delivery and Energy Reliability, Smart Grid Investment Grant Program Funding Opportunity Number: DE-FOA-0000058.

Recovery Act Financial Assistance, Funding Opportunity Announcement. U. S. Department of Energy, Office of Electricity Delivery and Energy Reliability, Smart Grid Investment Grant Program Funding Opportunity Number: DE-FOA-0000058.

Adapted from Southern California Edison (SCE) Edison SmartConnect™

Adapted from Southern California Edison (SCE) Edison SmartConnect™

Adapted from Southern California Edison (SCE) Edison SmartConnect™

Adapted from Southern California Edison (SCE) Edison SmartConnect™

FIPS Publication 199, Standards for Security Categorization of Federal Information Systems, February 2004, pages 2-3