Consumer uses a storage or generation unit to provide energy to their home or the grid.

Description:

The Energy Supplying Unit (ESU) connects with the premise Home Area Network (HAN), the Utility AMI system and the electric system (home, vendor or utility’s). The ESU identifies itself and the account it is associated with, and provides energy to the home or grid. This use case also describes the scenarios documented in The Sub Metering Use Case and The Load and Energy Management Use Cases, in that the ESU behaves according to these use cases.

Use Case Business Rules and Assumptions:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

Energy Supplying Unit (ESU) already contains energy.

All utility safety measures and rules are in place to provide power to the grid.

Definitions:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

Energy Supplying Unit (ESU) can be an energy storage device (e.g., electric vehicle battery) or an energy generation device (e.g., photovoltaic array or backup generator).

Use Case Actors:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

| Actor Name | Actor Type | Actor Description |
| --- | --- | --- |
| Energy Supplying Unit (ESU) | HAN device | Stores or Generates Energy |

Scenarios

Scenario (Power Upload)

The following scenarios address storage and generation for the purpose of providing energy to the home or grid.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| Incentives or utility requirements are in place for providing energy to the home or grid. | ESU | The Installation Use Cases are successfully completed. The Registration Use Cases are successfully completed. Units are transfer ready and properly connected. | Energy is successfully transferred. |

Steps for this scenario

| Step # | Actor | Description of the Step |
| --- | --- | --- |
| 1 | EMS, Utility, other entity, ESU (Consumer acts on EMS or ESU) | Signals ESU to transfer energy. |
| 2 | ESU | Performs a self-check for sufficient capacity and generation readiness. |
| 3 | ESU | Transfers energy. |
| 4 | EMS, Utility, other entity, ESU (Consumer acts on EMS or ESU) | Signals to end transfer event. (e.g., due to drop in price, inadequate energy availability, customer preference, or utility preference) |
| 5 | ESU | Ceases transfer of energy. |