System Configuration and Management

PHEV – document the bindings for vehicle and user account.

HAN Installation and Provisioning

Description:

Use case business rules and assumptions:

For control devices, device is installed in-line with at the appropriate control point (e.g., in series with the information or energy flow).

All appropriate safety precautions are taken (e.g., Qualified electrician is required fro certain installation routines).

Devices and applications are procured or provided through multiple distribution channels (e.g., retail, utility provided, etc.).

Devices meet all applicable state and federal laws (e.g., FCC).

Pre-commissioning routines have been successfully executed (e.g., pre-place network key has been loaded).

Scenario:

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| Customer takes position of HAN device. | Customer or Installer | Meter or other Utility AMI Gateway with two way communications capability is present. | The customer device has been added to the local network and has established communications with the Utility’s AMI Gateway (i.e., the HAN interface has been established). |

| Step | Actor | Description of the Step | Additional Notes |
| --- | --- | --- | --- |
| 1 | Customer or Installer | Installer locates appropriate installation point. | Appropriate installation point considerations includes: signal strength at location, appropriate control point, etc.) |
| 2 | Customer or Installer | Device is installed. | Installation includes removing previous equipment and connecting the device to external power (if necessary) |
| 3 | HAN Device | HAN Devices performs self-check and reports results to installer. | In certain installation instances a filed tool can asset in the device initialization and configuration. |
| 4 | Customer of Installer | InstallIInstaller inputs any required pre-commissioning materials (e.g., Physical location, LAT/LONG, etc), |  |
| 5 | Customer or Installer | Installer enters commissioning data (e.g., network key) or performs any necessary commissioning actions (e.g., proximity) |  |
| 5 | HAN Device | HAN Device notifies the AMI Utility Gateway or other network coordinator. | This process is part of the technology specific beckoning and discovery process. If a third part device performs the actual commissioning then the Utility AMI Gateway needs to be notified. |
| 6 | Utility AMI Gateway | Gateway acknowledge notification and authenticates network credentials |  |
| 7 | Utility AMI Gateway | Sends HAN Device any necessary configuration data (e.g., preferred communication paths, updates, etc.) |  |
| 8 | Utility AMI Gateway | Device is added to the network. The device is added the UtilityAMI list of available devices. |  |
| 9 | HAN Device | HAN device notifies the installer (successful installation) |  |
| 10 | Utility AMI Gateway | Gateway provides registration instruction *Optional* |  |

Utility Registration (e.g. application/devices)

Description:

Customer registers a device with the utility.

Self-test on start-up, automated provisioning, and remote health check capability reduces installation and maintenance labor costs. The Installer may perform other diagnostics that the meter and HAN Devices cannot perform by itself.

Based on its configuration, the meter and HAN Devices delivered by the utility ensure communications between the AMI and any additional customer-site equipment that will expand the size/scope of the HAN Devices have been established. It is important to note in this Use Case that a variety of HAN Device installation and provisioning scenarios exist, including a) utility delivers the only HAN Devices (e.g. a PCT), b) utility delivers additional HAN Devices and attaches to the existing customer HAN devices at time of meter installation and c) Customer connects HAN Devices to AMI after utility installation of AMI system.  The registration process needs to recognize these various scenarios.

TBD – describe PHEV/EV association for billable records.

Use case business rules and assumptions:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

Command and control communications (e.g., load control) require utility participation and imply accountability (i.e. require registration).

Customer specific communications (e.g., consumer consumption) require utility participation and imply accountability (i.e. require registration).

Local HAN commissioning establishes the base communication capability, utility registration rides on top of this commissioning.

Actors:

See “HAN Use Case - General Definitions, Assumption, Actors.doc”

Scenario:

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| The utility determines the need for authenticated device communications. | HAN Device | The Installation and Network Provisioning Use Cases have been successfully completed. | The customer device will be registered with the utility. All communications with the device will be protected, authenticated and acknowledged. |

| Step | Actor | Description of the Step | Additional Notes |
| --- | --- | --- | --- |
| 1 | Customer | Customer procures or is provided HAN equipment that is compatible with AMI system. |  |
| 2 | Customer | Customer installs HAN Devices per manufacturer’s instructions. | There maybe additional commissioning related steps associated with the device commissioning (See commissioning use case) |
| 3 | Customer | Customer makes decision to participate in utility AMI-related programs. | Potential regulatory involvement could force use. |
| 4 | Customer Representative | Customer Representative receives notification from Customer that Customer is ready to have one (or more) of their HAN Devices connected to the AMI for program purposes. | This process can be automated through a web based interface. (i.e., the web application is the Customer Representative) |
| 5 | Customer Representative | Customer Representative gets appropriate Customer information (address, verification information, etc…) and locates Customer information from CCS |  |
| 6 | Customer Representative | Customer Representative activates HAN Device Registration Application. |  |
| 7 | HAN Device Registration Application | HAN Device Registration Application initiates Utility AMI HAN discovery process which identifies the customer’s HAN Device. | If this process fails then the device has not been commissioned. |
| 8 | Customer | Customer provides unique registration information from HAN device (e.g., registration key, serial number). |  |
| 9 | Customer Representative | Customer Representative either decides or negotiates, with the Customer, the appropriate program(s) the Customer and the HAN Devices will participate. | This sequencing could occur prior to step 8. |
| 10 | HAN Device Registration Application | HAN Device Registration Application attempts to create an authenticated link with HAN Device using registration information. | This step can be staged. Depending on several performance and design constraints the Utility AMI Gateway can participate in the registration. |
| 12 | HAN Device Registration Application | HAN Device Registration Application sends appropriate registration, configuration and initiation messages to all applicable HAN and Utility AMI Gateway devices. | To reduce AMI load, the meter can be updated and act on behalf of the utility (e.g., registration materials are pushed down to the Utility AMI Gateway) |
| 13 | HAN Devices | HAN Devices acknowledge activation and readiness state(s) to HAN Device Registration Application. |  |
| 14 | HAN Devices Provisioning Tool | HAN Device Registration Application communicates all necessary information to CSS and other applicable systems for storage and any required internal registrations |  |
| 15 | Customer Representative | Customer Representative confirms with the Customer that HAN Devices have now been initialized into the AMI and the applicable program(s) are now activated. |  |

HAN Device Remote Diagnostics and Troubleshooting

Description:

Use case business rules and assumptions:

The scope of utility responsibility for diagnostics and maintenance is limited.  Accountability for troubleshooting is driven be several factors not addressed in these use cases.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| A utility owned or configured device fails or does not initialize | HAN Device | The Installation and Network Provisioning and Registration Use Cases have been successfully completed. | The customer device is returned to an operational state. |

| Step | Actor | Description of the Step | Additional Notes |
| --- | --- | --- | --- |
| 1 | Customer | Calls contacts customer service. |  |
| 2 | Customer Service Representative | Identifies customer (verifies) and records customer issue. |  |
| 3 | Customer Service Representative | Retrieves customer account (e.g., billing data, device registrations, program registrations, etc.) |  |
| 4 | Customer Service Representative | Validates account status |  |
| 5 | Customer Service Representative | Corrects account or registration information (e.g., updates billing, updates program participation) and ends call. |  |
| 5a | Customer Service Representative | Starts remote diagnostics application. |  |
| 6 | Remote Diagnostics application | Retrieves device commissioning data from Utility AMI gateway. |  |
| 7 | Remote Diagnostic Application | Attempts to connect to HAN device |  |
| 8a | Remote Diagnostic Application | Connection successful – commissioning confirmed, |  |
| 8b | Remote Diagnostic Application | Connection unsuccessful – repeat installation commissioning use case |  |
| 9 | Customer Service Representative | Notifies customer that the Utility can or can not communicate with the HAN Device |  |
| 10a | Customer Service Representative | Schedules onsite maintenance | See HAN Device Diagnostics and Maintenance use case |
| 10b | Customer Service Representative | Starts Registration Diagnostics Application |  |
| 10 | Remote Diagnostic Application | Check application layer communication (e.g., send registered control signal) |  |
| 11 | Customer Service Representative | Notifies the customer that the device is functioning or is not functioning correctly |  |
| 12a | Customer Service Representative | Registration communication unsuccessful – execute registration use case | See HAN Device Diagnostics and Maintenance use case |
| 12b | Customer Service Representative | Schedules onsite maintenance | See HAN Device Diagnostics and Maintenance use case |

HAN Device Diagnostics and Maintenance

Description:

Use case business rules and assumptions:

The scope of utility responsibility for diagnostics and maintenance is limited.  Accountability for troubleshooting is driven be several factors not addressed in these use cases.

| Triggering Event | Primary Actor | Pre-Condition | Post-Condition |
| --- | --- | --- | --- |
| A utility owned or configured device fails or does not initialize | HAN Device | The Installation/Provisioning and Registration Use Cases have been successfully completed or attempted | The customer device is returned to an operational state. |

| Step | Actor | Description of the Step | Additional Notes |
| --- | --- | --- | --- |
| 1 | HAN Device | HAN Devices cannot communicate with AMI system to self-register. |  |
| 2 | HAN Device | HAN Devices notifies installer of communication failure. |  |
| 3 | Customer or Installer | Installer or Customer uses field tool or HAN device diagnostic capabilities to test network communication. |  |
| 4a | Customer or Installer | Installer validates whether device is faulty. |  |
| 4b | Customer or Installer | Installer validates adequate HAN network coverage exists. |  |
| 5a | Customer or Installer | Installer replaces HAN Devices, if appropriate. |  |
| 5b | Customer or Installer | Customer Reports marginal coverage if appropriate. Installer may leave site at this point. |  |
| 6 | Customer or Installer | Performs problem and device specific resolution (e.g., installs a bridging device to mitigate poor signal strength, installs a higher power or more capable device, etc.) |  |