AMI Risk Assessment

Produced by the AMI-SEC (Advanced Metering Infrastructure Security) Task Force

Authors:

R. Eric Robinson (eric.robinson@itron.com)

Jeremy McDonald (jeremy.mcdonald@sce.com)

Brad Singletary (brad@enernex.com)

Bobby Brown (bobby@enernex.com)

Darren Highfill (darren@enernex.com)

Neil Greenfield (ngreenfield@aep.com)

Matt Gillmore (mkgillmore@cmsenergy.com)

Geoff Mulligan (geoff@mulligan.com)

Ray Bell (ray@grid-net.com)

Team Members:

John Lilley (jlilley@sempra.com)

Eric Rehberg (elrehberg@aep.com)

Nader Attar (nader@grid-net.com)

James Pace (pace@silverspringnet.com)

Matt Thomson (matt.thomson@ge.com)

Bill Menter (bill.menter@viasat.com)

Mike St. Johns (mstjohns@comcast.net)

Matt Carpenter (mcarpenter@intelguardians.com)

Abstract

Advanced metering infrastructure systems promise to deliver support for dynamic pricing models, and to improve both the stability and reliability of the electric grid, but with a greater need for strong security throughout the architecture. In this paper, we identify the security threats to be considered in advanced metering systems. Additionally, we use qualitative metrics to rank the threats so that mitigations can be applied both effectively and efficiently. Finally, in the appendix, we present an extended set of common criteria threat material for inclusion into an advanced metering system level protection profile.

1	Introduction	5

1.1	Overview	5

1.2	Scope	5

1.3	Assumptions about AMI Security	6

2	Methodology	7

2.1	Risk Assessment Steps	7

2.2	Mapping Risk through Security Domains	7

2.3	Asset Identification Methodology	9

2.3.1	Asset Identification Inputs	9

2.3.2	Asset Identification Outputs	9

2.4	Threat Assessment	11

2.4.1	Threat Model Development	12

2.4.2	Threats and Threat Agents	13

2.4.3	Threat Agent: Motive	14

2.4.4	Threat Agent: Means (Capability)	16

2.4.5	Threat Agent: Opportunity	17

2.5	Vulnerability	17

2.6	Risk Determination	18

2.6.1	AMI-SEC Likelihood Interpretation Policy	18

2.6.2	AMI-SEC Consequence Interpretation Policy	19

2.6.3	AMI-SEC Risk Interpretation Policy	19

3	Risk Assessment	21

3.1	Introduction	21

3.2	Vulnerabilities	21

3.3	Assets	21

3.4	Attacks	22

3.5	Scenarios and Prioritization	22

4	Conclusion	25

5	References	26

APPENDIX A:	aSSET iDENTIFICATION sUPPORT	27

A.1	Summary	27

APPENDIX B:	Threat Model Support	28

B.1	Summary	28

B.2	Assumptions	28

B.3	Threat Descriptions	30

B.3.1	Administrative Threats	30

B.3.2	Audit Threats	32

B.3.3	Crypto Threats	34

B.3.4	Download Threats	34

B.3.5	Eavesdropping Threats	36

B.3.6	Flawed Implementation Threats	37

B.3.7	Identification & Authentication Threats	38

B.3.8	Information System Threats	39

B.3.9	Initialization Threats	40

B.3.10	Insider Threats	40

B.3.11	Key Management Threats	42

B.3.12	Malicious Code Threats	44

B.3.13	Network Threats	47

B.3.14	Operational Denial of Service Threats	48

B.3.15	Operational Disclosure Threats	50

5.1.1	Operational Integrity Threats	53

B.3.16	Operational Non-Repudiation Threats	53

B.3.17	Physical Threats	55

B.3.18	Social Engineering Threats	59

B.3.19	Trust Threats	60

B.4	Organizational Security Policies	62

B.4.1	Security Objectives for Target	63

B.4.2	Security Objectives of the Environment	66

B.5	Coverage	68

B.5.1	Coverage of Administrative Threats	68

B.5.2	Coverage of Audit Threats	75

B.5.3	Coverage of Crypto Threats	77

B.5.4	Coverage of Download Threats	78

B.5.5	Coverage of Eavesdropping Threats	79

B.5.6	Coverage of Flawed Implementation Threats	80

B.5.7	Coverage of I&A Threats	81

B.5.8	Coverage of Information Systems Threats	81

B.5.9	Coverage of Initialization Threats	82

B.5.10	Coverage of Insider Threats	83

B.5.11	Coverage of Key Management Threats	84

B.5.12	Coverage of Malicious Code Threats	85

B.5.13	Coverage of Network Threats	88

B.5.14	Coverage of Operational Denial of Service Threats	89

B.5.15	Coverage of Operational Disclosure Threats	93

B.5.16	Coverage of Operational Integrity Threats	97

B.5.17	Coverage of Operational Non-Repudiation Threats	100

B.5.18	Coverage of Physical Threats	101

B.5.19	Coverage of Social Engineering Threats	104

B.5.20	Coverage of Trust Threats	104

B.5.21	Coverage of Assumptions	106

B.5.22	Coverage of Policy	110

B.5.23	Coverage of Objectives for Target	113

5.1.2	Coverage of Objectives for the Environment	149

APPENDIX C:	Vulnerability Analysis Support	156

# Introduction

## Overview

Advanced Metering Infrastructure (AMI) is a transforming technology that has broad impact on the energy market and its consumers. AMI allows utilities to balance supply, demand, and capacity making a smarter, more efficient, grid by pushing aspects of grid monitoring and control out to the endpoints of delivery. Stakeholders are implementing the systems and technologies required to deploy AMI today.

Advanced metering infrastructure systems promise to provide advanced energy monitoring and recording, sophisticated tariff/rate program data collection, and load management command and control capabilities. Additionally, these powerful mechanisms will enable consumers to better manage their energy usage, and allowing the grid to be run more efficiently from both a cost and energy deliver perspective. These advanced capabilities will also allow utilities to provision and configure the advanced meters in the field, offering new rate programs, and energy monitoring and control. With the advanced functionality, however, comes great responsibility.  It is the purpose of the Advanced Metering Infrastructure Security Task Force (AMI-SEC) to provide utilities with sufficient guidance to build security into the basic fabric of this deployment.

In this document, we develop a qualitative methodology for identifying key AMI assets, their threats, vulnerabilities, and risks to support security control development. While many such methods exist for information technology and industrial control systems today, no method is adapted for the needs presented by the increased exposure of the AMI field systems. The method used proceeds by characterizing critical assets and their security concerns, system threats, critical asset vulnerability, and concludes with a method for analyzing risk. We next apply the method to a representative high level set of AMI assets.

This Security Risk Assessment (SRA) is a tool to help stakeholders identify the risk values in each AMI security domain, and in turn make effective decisions about how to mitigate those risks.

## Scope

This document provides guidance for conducting the SRA in support of AMI architecture development. Organizations involved with AMI deployments will find this document to be a valuable resource in understanding AMI system risk. This assessment is designed to address the specific security needs, organizational objectives, utility products and services, and processes and specific practices in regard to utility AMI deployment.

Security issues are elicited and aggregated for AMI critical assets from Premise Edge Services to Utility Operations. This assessment does not address non-AMI utility networks.

AMI-SEC has defined and tailored a risk assessment methodology specifically for AMI that includes:

- Identification of security domains,

- Identification of key AMI assets for each security domain,

- Description of security concerns for each asset,

- Identification of threats and threat agents,

- Evaluation of vulnerabilities associated with assets and security domains,

- Consideration of attack likelihood, and

- Evaluation of successful attack consequences.

The valuation of asset security concerns is considered input to the risk assessment methodology utilities may use to determine asset exposure and ultimately, control selection. This document does not advise mitigating measures or prescribe controls against risk determination. Control recommendations are conducted in a separate document.

## Assumptions about AMI Security

The following assumptions are listed to better clarify the scope of the risk assessment problem within the advanced metering infrastructure system [SPP05].

- AMI is a new application domain for system stakeholders, requiring new application of risk assessment, and subsequent security controls prescription.

- Consumers of this document have the ability to identify inputs to the risk assessment process.

- Consumers of this document are responsible for mapping and adapting its tenets to the protection of the value of their individual business values.

- An AMI system security design should incorporate principles of system survivability.

- Stakeholders for this document give preference to openness in security standards, guidelines, methodologies, and ultimately technology.

# Methodology

## Risk Assessment Steps

There are many definitions of risk, but each has different implications for the nature of the AMI security problem. We leverage two definitions of risk that match the AMI community concerns

- A systems definition of Risk:  The level of impact on organizational operations (including mission, functions, image, or reputation, organizational assets, or individuals resulting from the operation of an information system given the potential impact of a threat and the likelihood of that threat occurring. [NIST800-53 Rev2]

- How to compute Qualitative Risk:  a function of the likelihood of a given threat-source’s exercising a particular potential vulnerability, and the resulting impact of that adverse event on the organization. [NIST800-30]

We adapt a methodology of understanding AMI critical system asset risk. The risk assessment is presented in terms of a static assessment in this document, but must become part of a recurring risk management process for utilities implementing AMI-SEC recommendations to make it compliant with a goal of system survivability.

The following steps are taken directly from NIST 800-30 as a reasonable process for determining and documenting qualitative asset risk:

- Step 1 – System Characterization (Asset Identification for the purposes of AMI)

- Step 2 – Threat Identification

- Step 3 – Vulnerability Identification

- Step 4 – Control Analysis [not considered by this document]

- Step 5 – Likelihood Determination

- Step 6 – Impact Analysis

- Step 7 – Risk Determination

- Step 8 – Control Recommendations[not considered by this document]

- Step 9 – Results Documentation

For the purposes of the initial assessment, Steps 4 and 8 of the NIST SP 800-30 process are not addressed, but rather deferred to a future design document as this document presumes no specific system architecture. As an organization matures and systems are deployed, the utility can easily incorporate existing mitigations into their process. Note Steps 2, 3, 4 and 6 may be done in parallel after step 1 is completed. We will describe AMI specific policies for assessing risk in each of these steps below.

## Mapping Risk through Security Domains

In the interest of approaching risk assessment in a way that is manageable, scalable and traceable, this document utilizes the IntelliGrid concept of Security Domains to aggregate logically cohesive system security requirements. A Security Domain (SD) represents a set of resources (e.g. network, computational, and physical) that is governed/secured and managed through a consistent set of security policies and processes. Thus each Security Domain that might be considered for AMI-SEC is responsible for its own general security process (e.g. Assessment, Policy, Deployment, Monitoring, and Training).

A Security Domain provides a well-known set of security functions that are used to secure transactions and information within that domain. We scale our risk assessment process by grouping AMI assets into Security Service Domains and subsequently treating risk by domain. This approach manages the explosion of relationships possible across the number of assets, threats, and vulnerabilities, and allows the mapping of Security Objectives (sometimes called Security Functional Requirements) to Security Service Domains. The rationale and design of the AMI security domains is given in a separate document.

Figure 1 - Risk Assessment Element Mapping illustrates relationships considered for mapping approach.

AMI-SEC utilizes the following definitions from NIST IR 7298 for purposes of the mapping process:

Asset: A major application, general support system, high impact program, physical plant, mission critical system, or a logically related group of systems. (Note: this is a systems definition of the term “asset,” which is appropriate for this level of analysis. Other uses of the term in this document are accompanied by explanation or definition.)

Threat: Any circumstance or event with the potential to adversely impact organizational operations (including mission, functions, image, or reputation), organizational assets, or individuals through an information system via unauthorized access, destruction, disclosure, modification of information, and/or denial of service.

Vulnerability: Weakness in an information system, system security procedures, internal controls, or implementation that could be exploited or triggered by a threat source.

Security Objective: Requirements levied on an information system that are derived from laws, executive orders, directives, policies, instructions, regulations, or organizational (mission) needs to ensure the confidentiality, integrity, and availability of the information being processed, stored, or transmitted.

Additionally, AMI-SEC utilizes the following definition in the mapping process

Security Service Domain: A set of assets with common security concerns and requirements.

This model captures the fact that threat agents (especially when malicious) do not always directly attack the end-target asset. The threat agent is not limited to the particular set of vulnerabilities associated with the end-target asset, but can instead exploit any vulnerability belonging to any asset within the same security service domain. The threat agent may subsequently leverage any existing and legitimate trust relationship within the domain to compromise the end-target asset. Thus, evaluation of the legitimacy or probability of a threat exploiting a specific vulnerability becomes moot.

The mapping process most importantly results in the ability to link security objectives (requirements) with security service domains. This link may subsequently be traced back through individual assets to determine appropriate mitigating controls for vulnerabilities within a specific domain.

## Asset Identification Methodology

Assets are things of business value to the stakeholder that it desires to protect and sustain. The asset identification phase within the SRA is the first step in the assessment of critical infrastructure. Each asset identified will have a degree of due diligence applied to its risk assessment output. It is important to limit assets considered by risk management efforts to those with true value to the AMI system. Any culling of assets should occur at this early stage. To help determine asset risk, we attempt to identify its context of use, its value, its impact, and specific security concerns it may have for its use context.

### Asset Identification Inputs

Inputs into the Asset Identification process can include just about anything contributing value or considered for protection. However, we are most concerned with assets having high likelihood of being compromised, high consequences resulting from compromise, or sufficient combination thereof. The list will cover assets such as:

- Business Values

- Hardware

- Software

- System Interfaces

- Data and Information

- People

- System Mission

### Asset Identification Outputs

Outputs of the Asset Identification process will include:

- Description

  - Name

  - Security requirements domain

  - Asset type

  - Contexts of use

- Security Profile

  - Security concerns

  - Value

  - Impact & consequence

#### Description

Each asset will be described by name, the security service domain in which it resides, asset type (e.g.: information, equipment, etc…), and any contextual use information that helps situate it in the AMI architecture.

#### Security Concerns

Protection concerns are varied as they are derived from the security attributes required by a particular system. Depending on role, location, and context an asset will have different sensitivities for each of the security attributes. These security attributes include confidentiality, integrity, availability, authentication, access control, and accounting.

#### Value Concerns

At the highest, most abstract level, assets are traced through business functions to organizational mission and values. The value of an individual system-level asset is ultimately derived from its role and criticality in an organization achieving said mission by the enablement of associated business functions.

#### Impact & Consequence Concerns

Consequence is the result of an unwanted incident, caused either deliberately or accidentally, which affects the assets. The consequences could be the destruction of certain assets, damage to the IT system, and loss of confidentiality, integrity, availability, accountability, authenticity or reliability. Possible indirect consequences include financial losses, and the loss of market share or company image.

Impact is a measurement of the magnitude of influence associated with results of an unwanted incident. The measurement of impacts permits a balance to be found between the results of an unwanted incident and the cost of the safeguards to protect against the unwanted incident. [SSE-CMM v.3]

The following table highlights a suggested classification of consequence severity due to expected asset impact based on an ANZ 4360:2004 example:

Table 1 – Example policy for consequence severity determination

|  | Consequence Types |
| --- | --- |
|  | Project Cost | Financial Impact | Customer Impact | Regulatory and Compliance Impact |
| Severity Level | High | $3M or more | $50M or more | 10,000 or more | Substantial financial penalties |
|  | Medium | $1M - $3M | $1M-$49M | 1,000 to 9,999 | Limited financial penalties |
|  | Low | $1M or less | $1M or less | Less than 1,000 | No regulatory or compliance issues |

These consequences are provided as an example. Each utility will need to define its own thresholds for severity and impact.

Mission criticality is defined as the extent to which a system is an integral, functioning part of the business and mission of the organization. NIST has identified three categories of criticality that can be assigned to specific systems. Criticality can be interpreted as the impact on the system operation, on human lives, on operational cost and other critical factors, when a leveraged function is compromised, modified, or unavailable in the operational environment.

Table 2 – Criticality Categories

| Category | Definition | Criteria |
| --- | --- | --- |
| Mission Critical | Systems that would preclude an organization from accomplishing its core business functions if they fail. | Supports a core business function. Single-source of mission-critical data. May cause immediate business failure upon system failure |
| Important | Systems that would preclude an organization in the short term from accomplishing its core business functions if they fail. | Backup source for critical data. Extended period of time. |
| Supportive | Effectiveness and efficiency issues. Failures affect day-to-day business operations. | Cause loss of business efficiency and effectiveness. Tracks/calculates data for convenience. |

## Threat Assessment

A threat can be defined as a potential violation of a security mechanism. It is possible to classify threats into four broad classes [SHIREY00]:

- Disclosure – Unauthorized access to information

- Deception – Acceptance of false data

- Disruption – Interruption or prevention of correct information

- Usurpation – Unauthorized control of some part of the system

The following security services counter these threats [BISHOP02]:

- Authentication – Ensures that device, system, or user access is strongly mutually authenticated.

- Authorization – Ensures that access levels are authorized based upon strong mutual authentication. (This function is addressed within the AMI-SEC security service of Access Control.)

- Confidentiality - Ensures that data is shared only with authorized individuals on a need-to-know basis, and that intentional or unintentional disclosure of the data does not occur.

- Integrity - Ensures that data is authentic, correct and complete, and provides assurance that the data can be trusted.

- Availability - Ensures that data, applications and systems are available to those who need them when they need them.

Sometimes, non-repudiation is also included as a component of information security [PARKER02]. Non-repudiation refers to the assurance that a person who claims or is claimed to have created, modified, or transmitted data is in fact that person, and is unable to deny that they are responsible for the data’s content or transmission.

In essence, non-repudiation is about tying a specific actor to a specific action in an undeniable manner. This function is accommodated by the AMI-SEC security service of Accounting.

### Threat Model Development

A threat model is a description of a set of possible attacks to consider when designing a system. Furthermore, the threat model can be used to assess the probability, severity, and reasoning of certain attacks and allow for designers to implement proper controls for mitigation purposes. The development of a threat model includes listing the security assumptions, threat agents, motivations, threats, vulnerabilities, controls, and assets in the system of interest. Figure 2 - A Generic Threat Model shows the interaction of some of these functions.

Figure 2 - A Generic Threat Model

### Threats and Threat Agents

Threat agents are characterizations of entities that may have the motivation, opportunities, or means for compromising an advanced metering system. Threat agents are used to represent individuals or groups that can manifest a threat [OWASP]. These agents may be classified using four criteria:

- Objectives – The end-goal(s) of the threat agent.

- Access – The ability of the attacker to gain physical or logical proximity to the system, as well as any inherent trust assumptions.

- Resources – The financial, temporal, or manpower assets available to the threat agent.

- Expertise – The threat agent’s understanding or expertise in the advanced metering infrastructure system, the electric power system, and/or the network technologies deployed by such systems.

- Risk Aversion Profile – The threat agent’s tolerance for consequences that differ from the general population (e.g.: arrest, publicity, safety, etc…).

The following table gives examples of some possible threat agents [OWASP]:

| Threat Agents |
| --- |
| Non-Target Specific | Non-Target specific Threat Agents are Computer Viruses, Worms, Trojan Horses and Logic Bombs. |
| Employees | Staff, Contractors, Operational and Maintenance Staff, Security Guard who are annoyed with the company. |
| Organized Crime and Criminals | Criminals target information that is of value to them, such as bank accounts, credit cards or intellectual property that can be converted into money. Criminals will often make use of insiders to help them. |
| Corporations | Companies engaged in offensive Information Warfare. Partners and Competitors come under this category. |
| Human Unintentional | Accidents, Carelessness |
| Human Intentional | Insider, Outsider |
| Natural | Flood, Fire, Lightning, Meteor, Earthquakes |

Additionally, other non-deliberate threat agents are possible including natural disasters, environmental and mechanical failure, as well as inadvertent actions of an authorized user may be considered [NIST80082]. This study will not consider these from an information systems security viewpoint, but should be examined in the disaster recovery and business continuity planning.

Threats are the means through which the ability or intent of a threat agent to adversely affect the goals and objectives of the advanced metering infrastructure system can be carried out [SHIREY00]. Threats are different from threat agents in that they do not necessarily imply intent. Possible threats include:

- Brute Force - Performing an exhaustive search of all possible values for a security credential or attribute (e.g. key, password or passphrase)

- Bypass - Bypassing system security functions and mechanisms.

- Destruction - Causing the destruction of system data, business data or configuration information.

- Disclosure - Losing data confidentiality.

- Denial of Service - Overloading the network and/or system resources.

- Hijack - Commandeering one-side of an existing authenticated connection.

- Malware - Deploying malicious software developed for the purposes of doing harm to a computer system or network (e.g. viruses, Trojan horses, backdoors, etc).

- Man In the Middle - Inserting undetected between two connections, where the attacker can read, insert and modify messages at will.

- Physical - Causing physical damage to or destruction of an asset.

- Privilege Escalation - Causing an unauthorized elevation of privilege.

- Replay – Creating an unauthorized replay of captured traffic.

- Repudiate - Refuting an action or association with an action.

- Sniff - Performing unauthorized traffic analysis.

- Social Engineering - Manipulating knowledgeable entities to gain privileged information or access.

- Spoof - Impersonating an authorized user or asset.

- Tamper - Modifying, in an unauthorized manner, system data, business data or configuration information.

Three steps to analyzing threats are:

Step 1 - determine threat-sources.

Step 2 - determine if threat sources have motivation, resources, and capabilities to carry out a successful attack.

Step 3 - apply a qualitative value to a successful attack (results of Step 2) taking into account likelihood of occurrence and impact per occurrence.

### Threat Agent: Motive

Motivation can be defined as an attacker’s purpose or intent to cause a desired effect on the advanced metering system. There are a variety of attacker ‘attitudes’ that impact individual motives, and thus vary the risk to the advanced metering system. The lack of motive reduces the likelihood that an attack will be executed. Possible motivations include:

- Profit

    - Avoid Billing

    - Derive Revenue

    - Directly Profit

        - Resell AMI Hosted BotNet

    - Manipulate the Energy Market

    - Manipulate Unrelated Market

    - Manipulate the Economy

- Revenge

    - Defame Individual

    - Degrade Revenue

    - Degrade Corporate Image

    - Degrade Service Delivery

    - Degrade Infrastructure

    - Extortion

    - Degrade Billing Integrity

- Privacy / Secrecy

    - Maintain Confidentiality

    - Become Anonymous

    - Mask Behavior

    - Spoof Behavior

    - Become Unobservable

    - Deter Meter Deploy

    - Delay Meter Deploy

- War

    - Degrade Infrastructure

    - Degrade Dependent Infrastructure

    - Degrade Service Delivery

    - Degrade Economy

- Ego

    - Achieve Bragging Rights

    - Prove Something

    - Publish

- Spying

    - Degrade Confidentiality

    - Reconnaissance

        - Capability Assessment

        - Economic

        - Technological

    - Determine Operational Advantage

    - Determine Market Advantage

- Curiosity

    - Explore

    - Understand

- Civil Disobedience

    - Degrade Infrastructure

    - Vandalism

- Activism

    - Exploit

        - Manipulate Attention to Specific Issue

        - Manipulate Attention to Broad Issue

        - Manipulate Attention to Unrelated Issue

    - Degrade Service Delivery

    - Vandalism

### Threat Agent: Means (Capability)

A threat agent must possess the means or capability in order to carry out a successful attack.  Several factors should be considered in evaluating threat agent capabilities from attack cost to special skills required.

Attack cost – involves the resources necessary in order to perform a successful attack including money, time and people. A government or activist group would likely have more resources than an individual by comparison.

Complexity of attack – it is desirable to make complexity high in order for a threat agent to compromise a system. Complexity is gained through adding controls and performing defense in-depth practices. Complexity for an attacker means they will have to be knowledgeable in several areas of the system, possibly need more time to execute, and require more cost. On the other hand if a system is easy to attack, likelyhood is that it will be attacked.

Exploit availability – availability of known exploits to platforms increases the likelyhood that it will be used in order to degrade the system.

Time factors of attack – time plays a role in when a system may be vulnerable to attack. For example, banks usually get robbed during the day when they are open for business, but not after hours when the vaults are sealed and no one is around to open them.

Special skills required to carry out the attack – involve special knowledge and ability in order to compromise a system. An example may be that the attacker would have to understand how to use special equipment to intercept signals and then write special programming in order to infiltrate the system.

### Threat Agent: Opportunity

AMI security should be configured and implemented in such a way as to diminish opportunity for threat agents to conduct an attact.

Access requirements:

Physical Proximity Required – the likelihood of an attack increases considerably the closer a threat agent is to an asset; conversely, the further a threat agent is from an asset the less likely a compromise in security will occur. An example of proximity

Trust requirements – a threat agent (human or another system) may require some level of trust to be granted in order for the opportunity to exploit a vulnerability.

Circumstantial requirements – Some vulnerabilities may be exploited only if the proper conditions exist.

Current Treatment of Vulnerability – the current treatment of a vulnerability can expose an opportunity of attack.

## Vulnerability

Vulnerabilities are weaknesses in the AMI system assets which increase asset exposure to attacks. Vulnerabilities stem from requirements, design, or implementation defects in the AMI system. Many general application vulnerabilities are available at the [OWASP] site.

- 3rd Party Network - Unauthorized access to the advanced metering system via a 3rd party network.

- Abuse – misuse by a valid user

- API Abuse - The most common forms of API abuse are caused by the returner failing to honor its end of this contract, returning erroneous data.

- Authentication - Weakness in the authentication mechanisms.

- Coarse Access Control - Access controls that do not allow for proper separation of duties or desired granularity.

- Code Permission - Software that requires unnecessarily elevated privileges for normal operation.

- Code Quality - Poor code quality that leads to unpredictable behavior, poor usability, and low assurance.

- Cryptographic Vulnerability – insecure, incorrect, or improperly implemented algorithms

- Dangerous API - Use of an Application Programming Interface that has known vulnerabilities, is no longer supported, or does not meet system requirements.

- Enforcement – lack of policy enforcement / assurance

- Error Handling - Improper error handling that can or does cause unintended or unpredictable behavior.

- Fail-Open: Systems should fail only into secured states (fail-secure), and never fail-open.

- Input Validation - Input that is not validated for proper formatting and content.

- Logging and Auditing - Poor or inadequate recording, retention, and handling of events of interest.

- Misconfiguration – gap between having security features and using them properly / effectively

- Protocol - Use of unknown/unproven protocols or protocols with known weaknesses inappropriate for system design.

- Sensitive - Inadequate protection of data value in transit, storage, and processing.

- Seperation of Privileges – Failure to use privilege seperation

- Services - Unnecessary services enabled on system components.

- Synchronization and Timing – improper design leads to weakness in synchronization and timing subsystems. E.g. clock manipulation

- Session Management - Inadequate session identifiers, often leading to replay attacks.

## Risk Determination

System stakeholders are highly concerned with denying or handling consequence of specific attacks on system assets. To understand the risk associated with a given concern, various factors may be taken into consideration including monetary value. The likelihood and consequence of attack to the asset stakeholder should be the primary concerns to the system builder. At high levels, these factors are easily and effectively described through subjective ranking factors and are easily derived from asset protection and classification requirements.

We provide a first rough qualitative assessment of risk due to attack or perceived vulnerability by assessing summary attack likelihood and attack consequences. Additional considerations or tables may be made to derive summary likelihood or consequence; however, in the risk assessment, the summary rating of a threat event against a specific asset is used.

Likelihood is summarized on a subjective scale from A to E with A being the most certain and E being rare. Consequence is summarized on a subjective scale from 1 to 5 with 1 being negligible consequence and 5 being severe consequence. Certain combinations of likelihood and consequence result in a subjective risk rating selected from low (L), medium (M), High (H), and extreme (E). A policy is first deployed for interpreting the component subjective values and subsequent assignment of risk ratings to various likelihood/consequence combinations. See Table 1 for an example subjective rating interpretation policy. See Table 2 for an example risk assignment policy.  It is expected that specific risk ratings generate minimal due-diligence requirements for management of controls against the threat and threat sources.

### AMI-SEC Likelihood Interpretation Policy

Likelihood is determined qualitatively by determining the threat agent’s means, motive, and opportunism. This matrix below shows an example of a possible means for determining a likelihood interpretation policy. Note that if any one component of motive, means or opportunity does not exist then likelihood is negligible. Controls are the mechanisms developed to mitigate risks. Removing motive, means or opportunity from a threat agent during the control development process significantly reduces the likelihood of of a successful attack occureing.

| Motive | Means | Opportunity | Likelihood |
| --- | --- | --- | --- |
| Low | Low | Low | Rare |
| Low | Low | High | Possible |
| Low | High | Low | Possible |
| Low | High | High | Likely |
| High | Low | Low | Possible |
| High | Low | High | Likely |
| High | High | Low | Likely |
| High | High | High | Almost Certain |

### AMI-SEC Consequence Interpretation Policy

### Consequences can also be interpreted quailitatively as a measure of impact that a successful attack would produce. We have given a rating example of 1 to 5 where (1) equals negligable impact on the low end to (5) sever consequence of impact on the high end. Refer to Table 3 – Qualitative Risk Assessment Interpretation. The rating is based against impact to accomplishing organizational goals and objectives.

### AMI-SEC Risk Interpretation Policy

### In a qualitative analysis interpretation of risk for our purposes will be calculated by scoring consequence against likelihood. As shown in Table 4, Risk is scored from (L) Low Risk to (E) Extreme Risk. Risk levels are assigned to security assets within the AMI domain. The body of the matrix may be adjusted to an organizaion’s specific exposure to risk. In general low risk assets map to the lower left corner where likelihood is low and consequence to impact of an attack is negligible; and extreme risk assets map to the upper right of the matrix where likelihood of a successful attack is high and the resulting consequence is a sever impact on performing organizational functions to reach goals and objectives.

Table 3 – Example: Qualitative Risk Assessment Interpretation

Table 4 - Example Risk Rating Policy

# Risk Assessment

## Introduction

Neither the clients nor providers of AMI can afford to have it fail or become compromised. The concern of loss or degredation of AMI drives the need for the risk assessment process. Stakeholders in AMI do not want to become the authors of a Greek tragedy; to find that in their effort to provide better service gives an enemy a new platform to which they can wage attacks. As mentioned earlier, a risk assessment serves as a tool to help stakeholders identify the risk value in order to make effective decisions about how to mitigate risk concerns.

## A risk assessment is the first step in the risk management process and should be an iterative process. The need to revisit the risk assessment process is made necessary by the emergence of new technologies, availability of new exploits, and new threats arise as time progresses.

## Vulnerabilities

## The initial phase of categorizing vulnerabilities for assets is generic. The goal is to relate vulnerabilities to AMI Security Domains through assets. The goal is to group theats by known categories and then apply them to assets during the asset definition phase. One or more vulnerabilities will map to a single asset (refer to Figure 1 - Risk Assessment Element Mapping). Appendix B3 catalogs threats by category and provides a detailed decription of each.

## Assets

Assets are the items of protection, the target of threats, the possessors of exposures, and the beneficiaries of controls [JAQUITH07]. System assets can be defined as any software, hardware, data, administrative, physical, communications, or personnel resource within an information system [CNSS4009]. Similarly, it is possible to define assets as information, resources, or services. For the purposes of AMI, assets are considered as business services that provide value streams for the organization. To accomplish this we aggregate the components required to provide a service and arrive at an abstract value stream. The value streams are what the organization wishes to protect at a context level risk assessment.

- Information Assets

  - Audit Data

  - Information Object

  - Policy

  - Other Configuration Information

  - Locally Protected Information

  - Traffic Flow

- Resource Assets

  - AMI Virtual Network

  - AMI components

    - Software

    - AMI applications

    - Operating System

    - Hardware

  - Tokens

- Service Assets

  - Order Key Service

  - Deliver Key Service

  - Track and Control Keys Service

  - Membership Management Service

  - Initialization Service

  - Software Download Service

  - Configured Cryptographic Element Interface Service

  - Policy Imposition Service

  - Trust Anchor Service

  - Network Infrastructure Services

  - Primary Security Services

    - Access Control Services

    - Integrity Services

    - Confidentiality Services

    - Accountability Services

    - Identification, Authentication, and Authorization Services

    - Availability Services

    - Audit Services

  - System Enrollment Services

It is important to note that each of the above assets include user data and the protection mechanisms.

## Attacks

An attack is an attempt to gain unauthorized access to an information system’s services, resources, or information, or the attempt to compromise an information system’s integrity, availability or confidentiality. An attack implies intent due to the definition as an attempt. However, not all attempts are malicious.

Attacks upon the security functions themselves are called direct attacks. All assets are subject to this type of attack. Most malicious direct attacks (other than denial of service attacks) target authentication and access control mechanisms first, since defeating those mechanisms may yield additional system privileges and may provide a platform from which to launch additional attacks.

Attacks upon external entities that occur over advanced metering interfaces are called forwarded attacks. For example, an external entity floods the advanced metering network with more traffic than was allocated to the particular component—this may result in a denial of service on the network.

A third type of attack is a system attack. This sort of attack happens when the system itself, without prompting from an external user, attacks internal or external assets. This would usually occur only in the case of a malicious developer or serious hardware/software failure.

Adding security controls to an advanced metering system does not mean that the system will not be attacked, nor does it mean that the system will be impossible to compromise. An adversary with the necessary time, funding, and expertise can often compromise the most secure system.

## Scenarios and Prioritization

Developing a set of attack scenarios allows for efficient application of security controls to help mitigate the defined attack vectors. The sole purpose of these controls is to reduce both the likelihood, and the impact of a successful attack. The likelihood of an attack refers the probability that this attack vector would be used. The impact of an attack refers the financial, reputation, or other business impact a successful penetration would have.

It is often beneficial to qualitatively sort possible attacks in terms of risk using both the likelihood and severity of the attack.

Each threat is given a severity, which is one of the following: Low, Medium, or High. The severity indicates the level of harm to the system if this threat were to succeed. A Low severity should result in no disclosure of information but, for example, might create an improperly or inconveniently configured system. A potential disclosure of information is an example of a Medium threat to the system security. A potential continuing disclosure of information is an example of a High threat.

Each threat is also given a likelihood, which is one of the following: Unusual, Unlikely, or Likely. In the case of a non-malicious threat, the likelihood is purely a probability of the threat occurring. In the case of malicious threats, the likelihood includes motivation to attack this way, whether the attack is coming from a user that some trust is placed in, and the gain from a successful attack. For malicious attacks, likelihood is less related to probability directly, since an attacker will attack a system at its weak point. Note that the likelihood is assigned before any protections are put in place. So, a threat of enrolling a user through unauthorized mechanisms is a Likely threat, simply because an attacker would be highly motivated to do it. In neither case does the likelihood include any mitigation factors implemented by the system or the environment. An unusual likelihood has an extremely low probability of occurrence. Unlikely threats have a low probability of occurrence. Likely threats are expected to be encountered and therefore require the strongest mitigation based on severity.

Some threats have a narrower focus than other threats. These threats were made specific because they have important implications in the system. The top threats were realized by combining threat components with assets to create threat statements. The following list of threat statements should be considered most apropos:

The following attacks are considered HIGH risk with a HIGH severity if realized and a LIKELY degree of likelihood:

- A threat agent may attempt to shut off large population of meters.

- A threat agent may hijack or spoof one or more trusted systems.

- A threat agent may craft a denial of service attacks at the utility back-office.

The following attacks are considered MEDIUM risk with a HIGH severity if realized and an UNLIKELY degree of likelihood:

- A threat agent may try to obtain key material from the system.

- A threat agent may craft a denial of service attacks to a large population of meters.

The following attacks are considered MEDIUM risk with a MEDIUM severity if realized and a LIKELY degree of likelihood:

- A threat agent may try to obtain key material from a meter.

- A threat agent may attack the system using test development software or other field tools typically used by technicians or manufacturers.

- A threat agent may try to spoof the meter using stolen key material or as a man in the middle attack.

The following attacks are considered LOW risk:

- A threat agent may try to sniff messages in order to maliciously control or alter functionality.

- A threat agent may try to tamper with application protocols to maliciously control or alter functionality.

- A threat agent may try to physically modify a meter to steal power.

# Conclusion

Advanced Metering Infrastructure systems offer a tremendous amount of potential, yet it introduces the requirements for industry proven, strong, robust, scalable, and open standards-based security. The goal of this working group is to define an exhaustive list of the potential security threats to the systems, and to perform detailed analysis of each threat to determine the threat levels and risks that it presents. The goal through this discovery process is to deliver information necessary to implement proper controls that will mitigate the security concerns surrounding AMI. The AMI-SEC team’s desire is that utilities find these tools and processes useful in the rigourous process of incorporating security to this developing field.

# References

[BISHOP02] Bishop M.A. The Art and Science of Computer Security, Addison-Wesley Longman Publishing Co., Inc., Boston, MA, 2002

[CNSS4009] National Information Assurance (IA) Glossary, May 2003.

[JAQUITH07] Jaquith, A. Security Metrics: Replacing Fear, Uncertainty, and Doubt, Addison Wesley Professional Co., Inc., Boston, MA, 2007.

[LANDWEHR94] Landwehr C.E., A. R. Bull, J. P. McDermott, and W. S.Choi. “A taxonomy of computer program security flaws”. ACM Computing Surveys (CSUR), 26(3):211–254, September 1994.

[LEMAY07] LeMay M., G. Gross, C. Gunter, and S. Garg. "Unified Architecture for Large-Scale Attested Metering". HICSS, p. 115b,  40th Annual Hawaii International Conference on System Sciences (HICSS'07),  2007.

[NISTSP800-30] NIST SP 800-30 Risk Management Guide for Information Technology Systems, July 2002.

[NISTSP800-53] NIST SP 800-53 Rev. 2. Recommended Security Controls for Federal Information Systems. December 2007.

[NISTSP800-82] NIST SP 800-82 2nd Draft Special Publication 800-82, Guide to Industrial Control Systems (ICS) Security, 2007.

[NISTIR7298] NIST IR 7298. Glossary of key information security terms. April 25, 2006.

[OWASP] http://www.owasp.org/index.php/Category:Vulnerability

[PARKER02] Parker, D.P. “Toward a New Framework for Information Security”, The Computer Security Handbook 4th Edition., John Wiley & Sons, 2002.

[SALEH07] Saleh, M. S., Alrabiah, A., and Bakry, S. H. “Using ISO 17799: 2005 information security management: a STOPE view with six sigma approach”. Int. J. Netw. Manag. 17(1):85-97, January 2007.

[SHIREY00] Shirey R.,  "Internet Security Glossary", RFC 2828, May 2000.

[SPP05] System Protection Profile – Critical Infrastructure Process Control Systems, June 2005.

aSSET iDENTIFICATION sUPPORT

## Summary

The spreadsheet associated with System Asset Identification is embedded below, or available at the following location: <INSERT ALTERNATE LOCATION>

The spreadsheet contains several tabs covering the following areas:

- System Asset Identification

- System Interfaces

- System Messages

- System Logical Architecture

Threat Model Support

## Summary

The Common Criteria considers both threats and the technical remedies needed to counter those threats doing so in a more formal language. The following is an extended set of common criteria threat material for inclusion into an advanced metering system level protection profile.

Advanced Metering Infrastructure (AMI) is another name for an advanced metering system. It refers to any system that measures, collects, and/or analyzes resource consumption from advanced devices such as electricity meters, gas meters, and/or water meters.

An entity is defined as a device (e.g., meter, relay, switch, router, collector), system (e.g., metering system, load control system), person (e.g., utility employee, customer), or a self-contained piece of data that can be referenced as a unit within the Advanced Metering Infrastructure system.

Threats to the Advanced Metering Infrastructure system are listed below by category:

The spreadsheet associated with this section is embedded below, or available at the following location: <INSERT ALTERNATE LOCATION>

## Assumptions

Assumptions are items that the security functions of the AMI system itself cannot implement or enforce. Assumptions do not specify functional requirements on the environment; that is done with a threat or policy statement.

Assumption Table 1 describes relevant assumptions, which may contribute to satisfying portions of the identified policies and will modify the impact of these policies on identified security objectives.

Assumption Table 1

| Assumption Name | Description |
| --- | --- |
| A.Admin_Available | At least one Security Administrator is available at all times to respond to TOE security incidents, alerts, and alarms. |
| A.Audit_Analysis | Mechanisms exist outside the TOE but within the TSE to perform sophisticated audit analysis (e.g., audit reduction and trend analysis) to augment TOE capability. |
| A.Back_Up | Backups of TOE files and configuration parameters are performed as required in accordance with site security policy. They are sufficient to restore TOE operation in the event of a failure or security compromise. |
| A.Clearance | All authorized users and administrators with access to the TOE will be authorized by their government to have access to, and the need-to-know, specified categories of TOE information. |
| A.Comms_Available | Communication capability with adequate service levels exists between TOE physical environments and is not part of the TOE. |
| A.Environment | This Problem Profile addresses the security environment of the TOE but specifically excludes the definition of the physical environmental tolerances (temperature, shock, vibration, etc.) |
| A.External_Networks | External networks that interface with the TOE are single-level attributed networks. |
| A.KeyMat_Source | Key material for the TOE will be supplied from external sources. |
| A.KeyMat_Source_Trust | The source of key material, after authentication, will be trusted. |
| A.Backhaul_Network_Errors | The Backhaul Network will report error indications to the TOE. |
| A.Personnel_Untrusted | Users (operational and management, local and remote) are not trusted to operate within their allocated authority. |
| A.Physical_Protection | The environment is capable of physically protecting the TOE by signaling the occurrence of fire, flood, power loss, and environmental control failures that might adversely affect TOE operations. |
| A.Partial_Physical_Security | Some TOE components are located within controlled access areas that provide protection against unauthorized physical access and tampering by unauthorized agents. |
| A.Policy_MoA | The U.S. negotiates multinational information sharing policy with the partner nations and all member nations enforce it. |
| A.Printer_Security | The printer outputs of TOE components are protected from observation by unauthorized personnel. |
| A.TOE_Design | The TOE is designed, manufactured, installed, and configured in accordance with its evaluated configuration and conforms to applicable security policies. |
| A.TOE_Maintenance | The TOE will be maintained by the System Administrator or by designated maintenance personnel who have been properly cleared and trained, and who perform under the supervision of the System Administrator. |
| A.TOE_Operation | The TOE is operated, maintained, and managed in accordance with its accredited configuration and conforms to applicable security policies. |
| A.TOE_User | TOE users will be either U.S. or coalition nation personnel who have been specifically authorized to participate in the operation or mission. |
| A.Trained | All users, administrators, and maintainers are appropriately trained. |
| A.Trusted_Source | A trusted source for key material, policy and software exists external to the TOE. |
| A.Visual_Security | The visible outputs of TOE components are protected from observation by unauthorized persons. |

## Threat Descriptions

## Administrative Threats

Administrative threats are those threats that are caused by malicious or negligent administrators. These threats are listed below in Table 1.

Table 1. Administrative Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Admin.Cred.1 |  |  | An entity gives access to information assets to inappropriate users |
| T.Admin.Cred.2 |  |  | An AMI entity with proper access gives access to resource assets to inappropriate users |
| T.Admin.Cred.3 |  |  | An AMI entity with proper access gives access to service assets to inappropriate users |
| T.Admin.Enroll.1 |  |  | An AMI entity with proper access enrolls a user with inappropriate levels of access control. . |
| T.Admin.Lockout.1 |  |  | An entity uses the Lockout service asset in an unauthorized manner to lock out a user. |
| T.Admin.Lockout.2 |  |  | An entity uses the Lockout service asset in an unauthorized manner to unlock a locked out a user. |
| T.Admin.Policy.4 |  |  | An entity gains unintentional access to objects in another system due to information sharing between the two information systems. |
| T.Admin.Policy.5 |  |  | An AMI entity with access creates a large policy causing an exhaustion of storage space. |
| T.Admin.Policy.7 |  |  | An AMI entity without proper access exploits policy flaws to gain improper (unintended) access to assets. |
| T.Admin.Policy.9 |  |  | An AMI entity with access enters/modifies AMI policy incorrectly, due to a lack of understanding of the policy system. |
| T.Admin.Policy.10 |  |  | An AMI entity with access enters/modifies AMI policy incorrectly, due to a lack of understanding of the current policy. |
| T.Admin.Policy.11 |  |  | An AMI entity with access enters/modifies AMI policy maliciously to cause information disclosure or loss. |
| T.Admin.Policy.12 |  |  | An AMI entity with access enters inconsistent AMI policy. |
| T.Admin.Policy.13 |  |  | An AMI entity with access imports a malicious AMI organizational policy. |
| T.Admin.Policy.14 |  |  | A policy authority provides a malicious AMI organizational policy. |
| T.Admin.Policy.17 |  |  | Required organizational policies are inconsistent resulting in denial of service. |

## Audit Threats

Audit threats are those threats that involve the AMI audit logs. The specific threats are listed below in Table 2.

Table 2. Audit Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Audit.1 | Medium | Likely | An entity creates a large number of auditable events in order to cause the AMI audit logs to run out of resource space. |
| T.Audit.2 | Medium | Likely | An AMI entity with proper access to the audit logs fails to clear enough space for the logs, causing the AMI audit logs to run out of resource space. |
| T.Audit.3 | Medium | Likely | An entity causes the AMI auditing function to fail, allowing an entity to perform non-recorded auditable actions. |
| T.Audit.4 | High | Likely | An entity reads AMI audit logs when it does not have authorization to read any audit logs. |
| T.Audit.5 | Medium | Likely | An entity reads AMI audit logs with a security attribute it does not possess. |
| T.Audit.6 | High | Likely | An entity modifies AMI audit logs to hide other actions. |
| T.Audit.7 | High | Likely | An entity deletes AMI audit logs it does not have authorization to delete. |
| T.Audit.8 | Low | Likely | An AMI entity with proper access misinterprets audit data, and thus cannot detect inappropriate actions of other principals. |
| T.Audit.9 | Low | Likely | An AMI entity with proper access cannot find the desired audit data within the AMI audit logs, and thus cannot detect inappropriate actions of other principals. |
| T.Audit.10 | Medium | Unlikely | An AMI entity with proper access is not provided enough information by the AMI audit logs to detect inappropriate actions of other principals. |
| T.Audit.11 | Medium | Unlikely | An AMI entity with proper access is not provided enough information by the AMI audit logs to identify principals who take inappropriate actions. |

## Crypto Threats

Crypto threats are those threats that directly involve the cryptography of the system. These threats include brute force attacks, mathematical attacks, etc. The specific threats are listed below in Table 3.

Table 3. Crypto Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Crypto.Break.1 | High | Unusual | An entity breaks the cryptographic mechanisms that protect assets through mathematical means. |
| T.Crypto.Break.2 | High | Unusual | An entity breaks the cryptographic mechanisms that protect assets through brute force computational means. |
| T.Crypto.Invalid_Keys.1 | Medium | Unusual | An AMI entity with access uses invalid cryptographic keys causing the system to enter a non-operational state. |
| T.Crypto.Invalid_Keys.2 | High | Unusual | An AMI entity with access uses invalid cryptographic keys causing the system to enter an insecure state. |
| T.Crypto.Weak_Keys.1 | High | Unlikely | An entity breaks the cryptographic mechanisms that protect assets because of the use of weak keys. |

## Download Threats

Download threats are those threats that directly involve the download source interface. The specific threats are listed below in Table 4.

Table 4. Download Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Download.1 | Medium | Unusual | An entity performs a denial of service attack that prevents the Download service asset from being able to download. This may lead to failure of a critical upgrade and continued exploitation of a weakness. |
| T.Download.2 | High | Unusual | An AMI entity with access to the Software Download service asset provides faulty software/configuration information to the AMI component resource asset. |
| T.Download.3 | Low | Likely | An AMI entity with proper access to the Download service asset loads software/configuration into an AMI component resource asset out of sequence. |
| T.Download.4 | Low | Likely | An AMI entity with access to the Download Software service asset loads software/configuration into the wrong AMI component resource asset. |
| T.Download.5 | Medium | Unusual | A non-AMI entity without access to the Download Software service asset replays download messages to cause a denial of service. |

## Eavesdropping Threats

Eavesdropping threats are those threats that involve network or communication eavesdropping. The specific threats are listed below in Table 5

Table 5. Eavesdropping Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Eavesdrop.Apps.1 | Medium | Unlikely | An entity eavesdrops on the Applications Interface (e.g. via logger process) in an attempt to read policy, information content, or information attributes information assets. |
| T.Eavesdrop.Comm.1 | Medium | Likely | An entity eavesdrops on the Backhaul network in an attempt to read an information asset (e.g., in order to receive covert channel communications or perform traffic analysis). |
| T.Eavesdrop.Comm.2 | Medium | Likely | An AMI entity eavesdrops on the AMI Virtual Network in an attempt to read an information asset (e.g., in order to receive covert channel communications or perform traffic analysis). |
| T.Eavesdrop.Comm.3 | Low | Likely | An entity eavesdrops on the Policy Authority Interface in an attempt to read a policy, policy mechanism, or traffic flow information asset. |
| T.Eavesdrop.Comm.4 | Medium | Likely | An entity eavesdrops on the AMI Systems Interface in an attempt to read information content, information attributes, policy, policy mechanism, or traffic flow information assets. |
| T.Eavesdrop.Comm.5 | Medium | Likely | An entity eavesdrops on the non-AMI Systems Interface in an attempt to read information content, information attributes, or traffic flow information assets. |
| T.Eavesdrop.Comm.6 | Low | Unlikely | An entity eavesdrops on the Download Source Interface in an attempt to diagnose AMI configuration and derive attacks on other AMI systems that weren’t upgraded yet. |
| T.Eavesdrop.Comm.7 | High | Likely | An entity eavesdrops on the Key Management Systems Interface in an attempt to read policy, policy mechanisms, or traffic flow information assets. |
| T.Eavesdrop.HMI.1 | Medium | Likely | An entity eavesdrops on the Users Interface (e.g. via a camera or a tap in the monitor cable) in an attempt to read policy, information content, or information attributes information assets. |
| T.Eavesdrop.HMI.2 | Medium | Likely | A valid AMI user leaves the workstation unattended, does not logout, and leaves the AMI Token in the workstation. An entity sits at the unattended workstation and improperly accesses information assets. |
| T.Eavesdrop.HMI.3 | Low | Unlikely | An entity sits at the unattended, inactive workstation, and attempts to access information assets. |
| T.Eavesdrop.HMI.4 | Medium | Likely | An entity eavesdrops on the Users Interface because an authorized user viewed information assets in an unauthorized area. |

## Flawed Implementation Threats

Flawed implementation threats are those threats that arise due to an incorrect or insecure implementation of AMI. Specific threats are listed below in Table 6.

Table 6. Flawed Implementation Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Flawed_Imp.Backdoor.1 | High | Unusual | An entity gains improper access to assets via a backdoor mechanism. |
| T.Flawed_Imp.Developer.1 | Medium | Likely | An entity exploits flaws in the AMI component [software, hardware] resource assets to gain improper access to assets. |
| T.Flawed_Imp.Developer.2 | Medium | Likely | An entity exploits flaws in the AMI component [software, hardware] resource assets to perform a denial of service attack. |
| T.Flawed_Imp.Developer.3 | Medium | Likely | An entity exploits flaws in the AMI component [software, hardware] resource assets to exfiltrate an information asset. |

## Identification & Authentication Threats

I&A threats are those threats that involve the user identification and authentication process. The specific threats are listed below in Table 7.

Table 7. I&A Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Ident_Auth.1 | High | Likely | An entity discovers user authentication information from a AMI component resource asset. |
| T.Ident_Auth.2 | High | Likely | An entity discovers user authentication information by external methods (i.e. human intelligence). |
| T.Ident_Auth.3 | Low | Likely | An AMI entity forgets its passphrase. |
| T.Ident_Auth.4 | High | Likely | An AMI entity attempts to crack I&A mechanisms through brute force methods (e.g., a password cracker). |
| T.Ident_Auth.5 | High | Likely | An entity is able to guess a passphrase because the passphrase was too simple (e.g., too short, it is “password”, etc.) |
| T.Ident_Auth.6 | High | Unlikely | An entity spoofs the I&A process to gain access to the user authentication information assets. |
| T.Ident_Auth.7 | High | Unlikely | An entity has access to a user’s AMI Token, and attempts to login to a AMI Workstation. |
| T.Ident_Auth.8 | High | Unlikely | An entity steals or borrows a valid user’s AMI Token, and duplicates it with the intent of using it for access by a different individual, or returning it modified to the original user. |

## Information System Threats

Information system threats are those threats that involve other information systems, whether those systems are other AMI System security domains or non-AMI systems. The specific threats are listed below in Table 8.

Table 8. Information System Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.InfoSys.1 | High | Likely | An entity installs a secret trapdoor into another information system so as to gain access to AMI. |
| T.InfoSys.2 | Medium | Likely | An entity changes the dissemination of an object to which he had access after it has been moved to another information system. |
| T.InfoSys.Filter.1 | Medium | Likely | A AMI entity with access makes use of an ineffective filter (e.g., dirty word filter) at the information system interface. |
| T.InfoSys.Printer.1 | Medium | Likely | An entity waits for a AMI entity with access to an information asset to print that information asset to a printer the entity has access to, and gains access to the information asset via the printout. |

## Initialization Threats

Initialization threats are those threats that occur during initialization of AMI components and during distribution of AMI components. The specific threats are listed below in Table 9.

Table 9. Initialization Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Initialize.Configuration.1 | High | Unusual | A AMI entity with access to the Initialization service asset provides faulty configuration information to the AMI component resource asset. |
| T.Initialize.Configuration.2 | High | Unusual | A AMI entity with access to the Initialization service asset provides faulty trust anchors to the AMI component resource asset. |
| T.Initialize.Configuration.3 | High | Unusual | A AMI entity with access to the Initialization service asset provides faulty hardware as a AMI component resource asset. |
| T.Initialize.Distribution.1 | High | Likely | An entity intercepts distribution of AMI components, and replaces AMI hardware with malicious hardware. |
| T.Initialize.Distribution.2 | High | Likely | An entity intercepts distribution of AMI components, and replaces AMI software with malicious software. |

## Insider Threats

Insider threats are those threats that directly involve authorized users of the system operating maliciously or negligently. The specific threats are listed below in Table 10.

Table 10. Insider Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Insider.Aggregation.1 | Low | Unusual | An AMI entity with access browses files to collect information (aggregation attack). |
| T.Insider.Confusion.1 | Medium | Likely | An AMI entity with access configures the system incorrectly because the system is too complex. |
| T.Insider.Confusion.2 | Medium | Likely | An AMI entity with access performs some insecure actions because the system is too complex. |
| T.Insider.Confusion.3 | Medium | Likely | A non-English speaking AMI entity performs insecure actions due to confusion about how to use the system securely. |
| T.Insider.Misinfo.1 | High | Unusual | An AMI entity with access improperly enters, edits, or imports content resulting in misinformation. |
| T.Insider.Mislabel.1 | Medium | Likely | An AMI entity with access creates, enters, edits, or imports content and labels it with incorrect security attributes resulting in unauthorized disclosure. |
| T.Insider.Mislabel.2 | Medium | Likely | An entity enters, edits unauthorized values in the information attributes resulting in exfiltration of information assets. |
| T.Insider.Misuse.Info.1 | Medium | Likely | An AMI entity with access to an information asset attempts to exfiltrate that information asset to a potential covert channel. |
| T.Insider.Misuse.Info.2 | Medium | Likely | An AMI entity with access to an information asset prints that asset and discloses it to an inappropriate individual. |
| T.Insider.Misuse.Res.1 | Low | Unlikely | An AMI entity with access to a resource asset attempts to access greater than its quota of that resource asset (e.g., bandwidth quota or data repository quota). |

## Key Management Threats

Key Management threats are those threats that involve the Key Management Systems with which AMI is interfacing. The specific threats are listed below in Table 11.

Table 11. Key Management Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.KeyMan.Deliver.1 | High | Likely | An AMI entity with proper access to the Deliver Keys service asset downloads duplicate keys with different attributes. This can lead to unauthorized access to assets. |
| T.KeyMan.Deliver.2 | High | Likely | An AMI entity with proper access to the Deliver Keys service asset downloads weak keys that can be broken. This can lead to unauthorized access to assets. |
| T.KeyMan.Deliver.3 | High | Likely | An AMI entity with proper access to the Deliver Keys service asset downloads keys with inappropriate attributes. This can lead to unauthorized access to assets. |
| T.KeyMan.Deliver.4 | Medium | Unlikely | An entity performs a denial of service attack that prevents the Deliver Keys service asset from being able to deliver keys. |
| T.KeyMan.Membership.1 | Medium | Likely | An AMI entity with access to the Membership Management service asset fails to report an individual whose keys should be revoked. |
| T.KeyMan.Membership.2 | Low | Unusual | An AMI entity with access to the Membership Management service asset reports revocation of individual whose keys should not have been revoked. |
| T.KeyMan.Membership.3 | Low | Unusual | An AMI entity with access to the Membership Management service asset delivers Membership Management information with inappropriate attributes for users. |
| T.KeyMan.Obsolescence.1 | Medium | Likely | Key Management services evolve in ways that are not backwardly compatible with AMI (may be included in KMS). |
| T.KeyMan.Order.1 | Medium | Unusual | An AMI entity with proper access to the Order Keys service asset annoys the Key Management Systems with nuisance orders causing the Key Management Systems to stop services to that AMI System security domain. |
| T.KeyMan.Order.2 | Medium | Unlikely | An AMI entity with proper access to the Order Keys service asset orders the wrong keys from the Key Management System and causes a failure to share information. |
| T.KeyMan.Order.3 | Medium | Unlikely | An entity performs a denial of service attack that prevents the Order Keys service asset from being able to order keys, creating an inability to access or verify information assets. |
| T.KeyMan.TrackControl.1 | Low | Unlikely | An entity performs a denial of service attack that prevents the Tracking and Control service asset from being able to report the correct information. This may lead to incomplete analysis and may cause: Inappropriate compromise recovery actions Damage assessment errors |

## Malicious Code Threats

Malicious code threats are those threats that involve malicious code execution or implantation. The specific threats are listed below in Table 12.

Table 12. Malicious Code Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Malicious_Code.App.1 | High | Likely | An entity implants malicious code in an application in order to modify the operating system, other applications, or data leading to disclosure of information assets, modification of information assets, denial of service, repudiation. |
| T.Malicious_Code.App.2 | High | Likely | An entity implants malicious code in an application in order to modify the operating system, other applications, or data leading to exfiltration of information assets to potential covert channels. |
| T.Malicious_Code.App.3 | High | Unlikely | An entity implants malicious code in an application in order to receive covert channel communication to direct the application to modify the operating system, other applications, or data. (See T.Malicious_Code.App.1 and T.Malicious_Code.App.2) |
| T.Malicious_Code.App.4 | High | Likely | An entity implants malicious code in an application in order to attack external entities through a AMI interface. |
| T.Malicious_Code.Info.1 | Medium | Likely | An entity implants malicious code in an information asset in order to gain access to an asset it is not authorized to access. |
| T.Malicious_Code.Info.2 | Medium | Likely | An entity implants malicious code in an information asset in order to exfiltrate information assets to a potential covert channel. |
| T.Malicious_Code.Info.3 | Medium | Likely | An entity implants malicious code in a AMI component information asset in order to modify information assets. |
| T.Malicious_Code.Info.4 | Low | Unlikely | An entity implants malicious code in a information asset in order to launch a denial of service attack. |
| T.Malicious_Code.Info.5 | Medium | Likely | An entity causes a user to execute malicious code in a AMI component information asset in order to modify information assets. |
| T.Malicious_Code.Info.6 | Medium | Likely | An entity causes a user to execute malicious code in an information asset in order to gain access to an asset. |
| T.Malicious_Code.Info.7 | Medium | Likely | An entity causes a user to execute malicious code in an information asset in order to exfiltrate information assets to a potential covert channel. |
| T.Malicious_Code.Info.8 | Low | Unlikely | An entity causes a user to execute malicious code in an information asset in order to launch a denial of service attack. |
| T.Malicious_Code.Proxy.1 | Medium | Unlikely | An entity implants malicious code in an AMI system security domain component to enable an authorized entity to act as a proxy for him. |
| T.Malicious_Code.Res.1 | Medium | Likely | An entity implants malicious code in an AMI component resource asset in order to gain access to an asset. |
| T.Malicious_Code.Res.2 | High | Likely | An entity implants malicious code in an AMI component resource asset in order to exfiltrate information assets to a potential covert channel. |
| T.Malicious_Code.Res.3 | High | Likely | An entity implants malicious code in an AMI component resource asset in order to modify information assets. |
| T.Malicious_Code.Res.4 | Medium | Unlikely | An entity implants malicious code in an AMI component resource asset in order to launch a denial of service attack. |
| T.Malicious_Code.Res.5 | Medium | Likely | An entity causes a user to execute malicious code in an AMI component resource asset in order to gain access to an asset it is not authorized to access. |
| T.Malicious_Code.Res.6 | Medium | Likely | An entity causes a user to execute malicious code in an AMI component resource asset in order to exfiltrate information assets to a potential covert channel. |
| T.Malicious_Code.Res.7 | Low | Unlikely | An entity causes a user to execute malicious code in an AMI component resource asset in order to launch a denial of service attack. |

## Network Threats

Network threats are those threats that directly involve the network in some manner other than eavesdropping (which is covered in the Eavesdropping Threats section). The specific threats are listed below in Table 13.

Table 13. Network Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Network.Denial.1 | High | Likely | An entity performs a denial of service attack on the Backhaul network (e.g. jamming, malicious code, distributed denial-of-service) resulting in a denial of service for assets. |
| T.Network.Filter.1 | High | Likely | An entity uses IP-level access to a Backhaul network and uses the AMI system security domain network interface to gain IP-level access to another Backhaul network that the AMI system security domain is interfacing with. |
| T.Network.Modify.1 | High | Likely | An entity modifies data on the Backhaul network in an attempt to modify that information asset. |
| T.Network.Modify.2 | High | Likely | An AMI entity without proper access to an information asset inserts data onto the AMI Virtual Network in an attempt to modify that information asset. |
| T.Network.Replay.1 | Medium | Likely | An entity attempts to replay a previous AMI network message sent over the Backhaul network. |
| T.Network.Replay.2 | Medium | Likely | An entity attempts to replay a previous AMI network message sent over the AMI Virtual Network. |
| T.Network.Unauth.1 | High | Likely | An AMI entity with access adds unauthorized network interfaces to AMI system security domain. |

## Operational Denial of Service Threats

Operational denial of service threats are those threats that affect availability of the system and may be caused by operational users of the system. The specific threats are listed below in Table 14

Table 14. Operational Denial of Service Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Op.Denial.1 | Low | Likely | An entity enters access control attributes related to specific content resulting in denying access to consumers who should be authorized for that information object. |
| T.Op.Denial.2 | Low | Likely | An entity enters improper value in the priority attribute related to specific content resulting in reduced distribution efficiency for that information object. |
| T.Op.Denial.3 | High | Likely | An entity creates excessive volume of information objects resulting in resource exhaustion (e.g., storage space) resulting in a denial of service. |
| T.Op.Denial.4 | Medium | Likely | An entity removes or changes endorsements on an information object in an unauthorized manner with the intent to stop the publication of the information object. |
| T.Op.Denial.5 | High | Unusual | An entity creates excessive volume of endorsements resulting in resource exhaustion (e.g., storage space) resulting in a denial of service. |
| T.Op.Denial.6 | High | Unlikely | An entity copies the information object to an excessive volume of ownership types resulting in resource exhaustion (e.g., storage space). |
| T.Op.Denial.7 | High | Unlikely | An entity copies an excessive volume of the information object to the same ownership type resulting in resource exhaustion (e.g., storage space, processor resources [race condition]). |
| T.Op.Denial.8 | Low | Likely | An entity enters (regrades to) incorrect values in the access control attributes that overly restrict access to the information content resulting in denial of service. Incorrect values could be as a result of: Negligence Hidden or malicious content Content different than what was displayed |
| T.Op.Denial.9 | High | Unlikely | An entity publishes the information object to an excessive volume of ownership types resulting in resource exhaustion (e.g., storage space). |
| T.Op.Denial.10 | High | Unlikely | An entity publishes an excessive volume of the information object to the same ownership type resulting in resource exhaustion (e.g., storage space, processor resources [race condition]). |
| T.Op.Denial.11 | Medium | Likely | An entity deletes an object it is not authorized to delete resulting in denial of service. |
| T.Op.Denial.12 | Low | Likely | An AMI entity deletes an object it is authorized to delete resulting in denial of service. |
| T.Op.Denial.13 | Low | Unlikely | An AMI entity mounts an attack against AMI computing resources that results in task overloading. |
| T.Op.Denial.14 | Medium | Unlikely | An entity prevents the decryption of information objects resulting in no information being displayed, resulting in denial of service. |
| T.Op.Denial.15 | Medium | Unusual | An entity prevents display content from being displayed resulting in denial of service. |
| T.Op.Denial.16 | Low | Unusual | An entity causes an authorized user to view an improper/incorrect AMI directory structure resulting in denial by failing to connect to the intended AMI directory. |

## Operational Disclosure Threats

Operational disclosure threats are those threats that affect confidentiality of the system and may be caused by operational users of the system. The specific threats are listed below in Table 15.

Table 15. Operational Disclosure Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Op.Disclosure.1 | Medium | Likely | An entity views an information asset it is not authorized to view. |
| T.Op.Disclosure.2 | Medium | Likely | An entity enters, edits, or imports content with attributes it does not have access to resulting in unauthorized disclosure. |
| T.Op.Disclosure.3 | Medium | Likely | An entity improperly copies to the wrong ownership resulting in disclosure to a different set of entities prior to obtaining authorization to disseminate. |
| T.Op.Disclosure.4 | Medium | Likely | An entity regrades to incorrect values in the access control attributes resulting in the unauthorized access to the information content resulting in disclosure. Incorrect values could be as a result of: Negligence Hidden or malicious content Content different than what was displayed |
| T.Op.Disclosure.5 | Medium | Likely | An entity improperly publishes a document resulting in disclosure or exfiltration of information assets. |
| T.Op.Disclosure.6 | Medium | Likely | An AMI entity improperly publishes a document to the wrong location resulting in disclosure or exfiltration of information assets. |
| T.Op.Disclosure.7 | Medium | Likely | An AMI entity fails to delete all copies of an information object resulting in disclosure of information that may have been distributed (e.g., after publishing a document with incorrect information, he tries to delete, but the genie is out of the bottle; or had a bad delete list; or user forgot to select all objects that he intended to delete). |
| T.Op.Disclosure.8 | High | Likely | An entity collects (e.g., signals intelligence SIGINT) unprotected (plaintext) content and unprotected object attributes and endorsements resulting in unauthorized disclosure. |
| T.Op.Disclosure.9 | Medium | Likely | An entity executes a view function (decryption) on an object they are not authorized to access resulting in unauthorized disclosure. |
| T.Op.Disclosure.10 | High | Likely | An entity collects (e.g., signals intelligence SIGINT, human intelligence HUMINT) unprotected (plaintext) content and unprotected object attributes and endorsements resulting in unauthorized disclosure. |
| T.Op.Disclosure.11 | Medium | Likely | An entity executes an export function on an information object they are not authorized to export resulting in unauthorized disclosure. |
| T.Op.Disclosure.12 | Medium | Likely | An entity executes an export function on an information object they are authorized to export to the wrong non-AMI network resulting in unauthorized disclosure. |
| T.Op.Disclosure.13 | High | Likely | An AMI entity with access in a remote information system attempts to access AMI information objects in an unauthorized manner. |
| T.Op.Disclosure.14 | Low | Unusual | An entity views unauthorized AMI directory structure resulting in unauthorized disclosure. (e.g. an unauthorized user is presented unauthorized directory names) |
| T.Op.Disclosure.15 | Medium | Likely | An entity views an information asset it is not authorized to view because an authorized user viewed the information on an unauthorized component. |

### Operational Integrity Threats

Operational integrity threats are those threats that affect integrity of the system or information in the system and may be caused by operational users of the system. The specific threats are listed below in Table 16.

Table 16. Operational Integrity Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Op.Integrity.1 | High | Likely | An entity modifies an information asset it is not authorized to modify. |
| T.Op.Integrity.2 | Medium | Likely | An entity modifies information content it is not authorized to modify (see T.Integrity.1). |
| T.Op.Integrity.3 | High | Likely | An entity modifies access control attributes when it does not have regrade function access (see T.Integrity.1). |
| T.Op.Integrity.4 | High | Likely | An entity modifies information attributes it is not authorized to modify (see T.Integrity.1). |
| T.Op.Integrity.5 | High | Likely | An entity modifies policy it is not authorized to modify (see T.Integrity.1). |
| T.Op.Integrity.6 | High | Unusual | An entity modifies display signals resulting in incorrect information being displayed. |
| T.Op.Integrity.7 | High | Likely | An AMI entity with access in a remote information system attempts to modify AMI information objects in an unauthorized manner. |
| T.Op.Integrity.8 | High | Likely | An entity modifies a AMI component software or operating system resource asset in an unauthorized manner. |

## Operational Non-Repudiation Threats

Operational non-repudiation threats are those threats that affect the ability to perform non-repudiation of information in the system and may be caused by operational users of the system. The specific threats are listed below in Table 17.

Table 17. Operational Non-Repudiation Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Op.Non-Repudiation.1 | Medium | Likely | An entity enters, edits unauthorized values in the information attributes resulting in false attribution of the content creator. |
| T.Op.Non-Repudiation.2 | Low | Unlikely | An entity improperly enters, edits unauthorized values in the information attributes resulting in false repudiation of the content endorser. (X deletes X or Y signatures) |
| T.Op.Non-Repudiation.3 | Low | Unlikely | An entity enters, edits unauthorized values in the information attributes resulting in repudiation of the information object copier. (X says X did not do it) |
| T.Op.Non-Repudiation.4 | Medium | Likely | An entity enters, edits unauthorized values in the information attributes resulting in false attribution of the information object copier. (X says Y did it) |
| T.Op.Non-Repudiation.5 | Low | Unlikely | An entity enters, edits unauthorized values in the information attributes resulting in repudiation of the information object publisher. (X says X did not do it) |
| T.Op.Non-Repudiation.6 | Low | Unlikely | An entity enters, edits unauthorized values in the information attributes resulting in false attribution of the information object publisher. (X says Y did it). |
| T.Op.Non-Repudiation.7 | Medium | Likely | An entity improperly enters, edits unauthorized values in the information attributes resulting in false attribution of the content endorser. (X says Y signed it). |

## Physical Threats

Physical threats are those threats that directly involve the physical hardware/software of the system. The specific threats are listed below in Table 18.

Table 18. Physical Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Physical.Capture.1 | High | Likely | Without warning, an entity captures (e.g., with troops) a AMI System security domain in order to access assets. |
| T.Physical.Capture.2 | High | Likely | With warning, an entity captures (e.g., with troops) a AMI System security domain in order to access assets. |
| T.Physical.Denial.1 | Medium | Likely | An entity causes the physical to cease functioning (e.g., cables are cut, a router fails, a network component loses power) causing a denial of service. |
| T.Physical.Destruction.IA.1 | Low | Likely | An entity destroys a AMI token resource asset. (see T.Physical.Destruction.Res.1 and T.Physical.Destruction.Res.2) |
| T.Physical.Destruction.IA.2 | Low | Likely | An entity renders a AMI biometric source unusable (e.g., a body part is lost or damaged). |
| T.Physical.Destruction.Info.1 | Medium | Unusual | A natural disaster destroys the media that contains an information asset. |
| T.Physical.Destruction.Info.2 | Medium | Likely | An entity destroys the media that contains an information asset. |
| T.Physical.Destruction.Res.1 | Medium | Likely | A natural disaster destroys a resource asset. |
| T.Physical.Destruction.Res.2 | Medium | Likely | An entity destroys a resource asset. |
| T.Physical.Destruction.Serv.1 | Medium | Likely | A natural disaster renders a service asset physically inoperable. |
| T.Physical.Destruction.Serv.2 | Medium | Likely | An entity renders a service asset physically inoperable. |
| T.Physical.Destruction.Total.1 | High | Unusual | A natural disaster destroys a AMI System security domain. |
| T.Physical.Destruction.Total.2 | High | Likely | An entity destroys a AMI System security domain. |
| T.Physical.Extract.IA.1 | High | Likely | An entity gains physical access to an AMI token resource asset containing a user authentication information in order to extract that information via intrusive physical means. |
| T.Physical.Extract.IA.2 | High | Likely | An entity eavesdrops on compromising emanations from a AMI token resource asset to discover user authentication information. |
| T.Physical.Extract.NonAMI.1 | High | Likely | An entity collects emanations from the unprotected side of the non-AMI interface to discover information assets. |
| T.Physical.Extract.Res.1 | High | Likely | An entity gains physical access to an AMI component resource asset containing an information asset in order to extract that information asset via intrusive physical means. |
| T.Physical.Extract.Res.2 | High | Likely | An entity eavesdrops on compromising emanations from a AMI component resource asset to discover an information asset (e.g., to learn information content or perform traffic analysis). |
| T.Physical.Extract.Res.3 | High | Likely | An entity eavesdrops on compromising emanations from a AMI component resource asset to receive covert channel communications. |
| T.Physical.HWFailure.1 | Medium | Likely | An AMI component resource asset experiences a hardware failure that places AMI in a non-operational state. |
| T.Physical.HWFailure.2 | Medium | Likely | An AMI component resource asset experiences a hardware failure that places AMI in an insecure state. |
| T.Physical.HWFailure.3 | Medium | Likely | An AMI component resource asset experiences a hardware failure that alters an information asset. |
| T.Physical.MechFailure.1 | Medium | Likely | An AMI component resource asset experiences a mechanical failure that places AMI in a non-operational state. |
| T.Physical.Modification.Info.1 | Medium | Unlikely | An entity gains physical access to an AMI component resource asset containing an information asset in order to modify that information asset via physical means. |
| T.Physical.Modification.Input.1 | High | Likely | An entity installs a recording device into a user’s input device so as to gain the user’s access or discover information. |
| T.Physical.Modification.Res.1 | High | Likely | An entity physically modifies a AMI component resource asset in order to gain access to an asset. |
| T.Physical.Modification.Res.2 | High | Likely | An entity physically modifies a AMI component resource asset to exfiltrate information assets to a potential covert channel. |
| T.Physical.Obsolete.1 | High | Likely | AMI component hardware resource assets become obsolete and are no longer in production. |
| T.Physical.Obsolete.2 | High | Likely | AMI component software resource assets become obsolete and are no longer available, resulting in denial of service. |
| T.Physical.ReverseEng.1 | Medium | Likely | An entity procures a piece of AMI hardware to perform reverse engineering so as to capture advanced technology. |
| T.Physical.ReverseEng.2 | Medium | Likely | An entity procures a piece of AMI hardware to perform reverse engineering to exploit discovered flaws. |
| T.Physical.ReverseEng.3 | Medium | Likely | An entity with physical access to AMI equipment at the remote AMI system reverse engineers the AMI equipment to improve that country’s technology. |
| T.Physical.ReverseEng.4 | Medium | Likely | An entity with physical access to AMI equipment at the remote AMI system reverse engineers the AMI equipment to use it against us. |
| T.Physical.SWFailure.1 | Medium | Likely | An AMI component resource asset experiences a software failure that places AMI in a non-operational state. |
| T.Physical.SWFailure.2 | Medium | Likely | An AMI component resource asset experiences a software failure that places AMI in an insecure state. |

## Social Engineering Threats

Social engineering threats are those threats that involve human-to-human breaches in security. Specific threats are listed below in Table 19.

Table 19. Social Engineering Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Social_Eng.Access.1 | High | Likely | An entity co-opts a AMI user to grant the entity system access. |
| T.Social_Eng.Access.2 | High | Likely | An entity persuades a user of a non-AMI system with some level of access to AMI to divulge his AMI credentials. |
| T.Social_Eng.Access.3 | High | Likely | An entity persuades a user of a different AMI system with some level of access to the AMI to divulge his AMI credentials. |
| T.Social_Eng.AdminLeak.1 | High | Likely | An entity persuades an administrator of a non-AMI system to reveal information about system operational procedures, auditing or known flaws so as to enable the entity to access AMI. |
| T.Social_Eng.Authorize.1 | Medium | Likely | An AMI entity co-opts a AMI user to grant the entity authorization to an asset. |
| T.Social_Eng.Info.1 | Medium | Likely | An entity co-opts a AMI user to access information assets. The attacking entity may then access the information via the co-opted user (e.g., read over the shoulder of user, have user verbally tell content). |
| T.Social_Eng.Info.2 | High | Likely | An entity co-opts a AMI user to exfiltrate information assets to a potential covert channel. |
| T.Social_Eng.Info.3 | High | Likely | An entity co-opts a AMI user to modify information assets. |
| T.Social_Eng.Info.4 | High | Likely | An entity attempts to guess a user passphrase based upon knowledge of the user. |

## Trust Threats

Trust threats are those threats which involve either impersonation of a known entity or creation of trusted assets. Specific threats are listed below in Table 20.

Table 20. Trust Threats

| Threat Name | Severity | Likelihood | Description |
| --- | --- | --- | --- |
| T.Trust.Impersonate.1 | High | Likely | An entity impersonates a policy authority entity and is recognized by the AMI System security domain as a valid policy authority. |
| T.Trust.Impersonate.2 | High | Likely | An entity impersonates the Key Management System and is recognized by the AMI System security domain as the Key Management System. |
| T.Trust.Impersonate.3 | High | Likely | An entity impersonates a known AMI System and is recognized by the AMI System security domain as that AMI System. |
| T.Trust.Impersonate.4 | High | Likely | An entity impersonates a known non-AMI System and is recognized by the AMI System security domain as that non-AMI System. |
| T.Trust.Impersonate.5 | High | Likely | An entity impersonates the Download Source and is recognized by the AMI System security domain as the Download Source. |
| T.Trust.Impersonate.6 | High | Likely | An entity impersonates a user and is recognized by the AMI System security domain as that user. |
| T.Trust.Impersonate.7 | High | Likely | An entity impersonates an application, and that application is recognized by the AMI System security domain as a valid application. |
| T.Trust.Impersonate.8 | Medium | Unlikely | An entity impersonates the network infrastructure in order to analyze or affect IP datagrams transmissions. |
| T.Trust.Info.1 | High | Likely | An entity creates trusted information assets in an unauthorized manner. |
| T.Trust.Res.1 | High | Likely | An entity creates trusted resource assets in an unauthorized manner. |
| T.Trust.Serv.1 | High | Likely | An entity is able to impersonate trusted service assets in an unauthorized manner. |

## Organizational Security Policies

The following statements identify and explain organizational policies that are relevant to AMI. These policies define the operation, management, personnel responsibilities, and guidelines that must be used to provide security for the AMI system. Table 21 describes these policies.

Table 21. Organizational Security Policies

| Policy Name | Definition |
| --- | --- |
| P.Access | Access to TOE information will be limited to authorized users within the limits of their credentials and need-to-know. |
| P.Accountability | Authorized administrators and users are held accountable for security relevant actions they perform. |
| P.Admin_Security | A Security Administrator interprets, maintains, and oversees site security policy and develops and implements procedures assuring secure operation of the TOE. |
| P.Admin_Split | Administrative responsibilities are split between System Administrator and Security Administrator roles that together competently administer the TOE. The assignment of split administrative authorization is established in order to prevent unrestricted system control and to provide for “checks and balances”. |
| P.Admin_System | A System Administrator is responsible for installing, configuring, managing, and monitoring the performance of the TOE in accordance with its evaluated configuration and ensuring its conformance to applicable security policies. |
| P.Audit_Review | Administrators will review audit reports and take appropriate action. |
| P.Cross_Domain_Filtering | Information domains will not be directly connected without application of appropriate cross-domain filtering techniques. |
| P.Distribution | A Security Administrator will issue security relevant TOE hardware and software, and will maintain all records regarding distribution of these items. |
| P.Due_Care | The level of security afforded the TOE will be in accordance with what is considered prudent by the organization’s accrediting authority. |
| P.Info_Senders | TOE users and processes must be explicitly authorized to transfer information outside the TOE. |
| P.Info_Sources | U.S. and partner personnel and processes that transfer information into the TOE must be explicitly authorized to do so. |
| P.Integrity | Data collected and produced by the TOE will be protected from modification. |
| P.Protect | The TOE will be protected from unauthorized accesses and disruptions of TOE data and functions. |
| P.Security_Admin_Restricted | Only authorized System Administrators, Security Administrators, and their representatives may administer or repair security mechanisms in the TOE. |
| P.Users | Only personnel authorized by the sponsoring U.S. Command, Service, Agency, or Coalition Organization may have access to or utilize TOE resources. |

## Security Objectives for Target

This section defines the security objectives of the AMI system and its supporting environment. Security objectives reflect the stated intent to counter identified threats and/or comply with any organizational security policies identified.

Table 22. Security Objectives of the System

| Objective Name | Description |
| --- | --- |
| O.Admin_Roles_Access | Design administrative functions such that administrative responsibilities of the system will be well defined and compartmentalized such that administrators do not automatically have access to assets, except for necessary exceptions. |
| O.Audit | Record in audit records: date and time of action, location of the action, and the entity responsible for the action. |
| O.Audit_Log_Maintenance | The audit log will be maintained in such a way as to prevent unauthorized access, modification, deletion or overflow conditions. |
| O.Trusted_Path&Channel | Provide a trusted path and channel between the system and a remote trusted system for the performance of security-critical operations. |
| O.Confidentiality | Provide high assurance that information is not disclosed to unauthorized individuals, processes, or devices. |
| O.Crypto_Comm_Channel | Provide secure session establishment between the system and remote systems using NSA approved confidentiality, integrity, authentication and non-repudiation of network transmissions. Restrict user access to cryptographic IT assets in accordance with a specified user access control policy. Provide complete separation between plaintext and encrypted data and between data and keys. |
| O.Crypto_Storage | Provide NSA approved confidentiality, integrity, authentication and non-repudiation of stored information content. |
| O.Crypto_Import_Export | Protect cryptographic data assets when they are being transmitted to and from the TOE, either through intervening untrusted components or directly to/from human users. |
| O.Import_Export_Control | Provide security services and labels on import/export data that is consistent with policy (i.e. user, data source, data content, and intended audience). |
| O.Fault_Tolerant | Provide fault tolerant operations for critical components and continue to operate in the presence of specific failures in one or more system components. |
| O.Integrity_Checks | Provide periodic integrity checks on system data, user data, and hardware/software functionality. |
| O.I&A | Uniquely identity and robustly authenticate each user that will support accountability and authorization. |
| O.Integ_Data | Ensure the integrity of system data, user data, and security attributes transferred or replicated within the system. |
| O.Emanantions | Limit system-produced unintended emanations (intelligible or not) to within a specified limit. |
| O.Isolate_Executables | Run executable code in a protected domain where the code's potential errors or malicious code will not significantly impact other system functions of other valid users of the system. |
| O.Maintain_Online | Provide online maintenance role with a limited capability to observe the usage of specified services or resources as necessary. |
| O.NonRepudiation | Provide accountability and nonrepudiation of information transfer between entities. |
| O.Obj_Attr | Maintain object security attributes with integrity. |
| O.Priority_Of_Service | Control access to resources so that lower-priority activities do not unduly interfere with or delay higher-priority activities. |
| O.Resource_Quotas | Use resource quotas to limit user and service use of system resources to a level that will prevent degradation or denial of service to other critical users and services. |
| O.Rollback | Recover from user operations by undoing some user operations (i.e., “rolling back”) to restore a previous known state. |
| O.SW_Download | Provide the ability to update the TOE software program to patch discovered security flaws or other flaws in the program that could be exploited by the adversary. SW download is implemented with High Robustness. |
| O.Session_Protection | Provide protection of a user or admin session to prevent an unauthorized user from using an unattended computer where a valid user has an active session. |
| O.Secure_State | Maintain and recover to a secure state without security compromise after power cycle, addition or removal of components, system error or other interruption of system operation. |
| O.Security_Mgt | Manage the initialization of, limits on, and allowable operations on security attributes, security-critical data, and security mechanisms. |
| O.Security_Roles | Maintain security-relevant roles and the association of users with those roles. |
| O.Sys_Assur_HW/SW/FW | Ensure that security-relevant software, hardware, and firmware are correctly functioning through features and procedures. |
| O.Tamper | Provide system features that prevent, detect, and resist physical tampering of a system component, and use those features to limit security breaches. |
| O.User_Attributes | Maintain a set of security attributes (which may include group membership, clearance, access rights, etc.) associated with individual users in addition to user identity. |
| O.Secure_via_Cryptography | Ensure the protection provided to data in the system is predicated on the secrecy of the keys not in the secrecy of the design. |
| O.Malicious_Code | Incorporate malicious code prevention procedures and mechanisms. |
| O.Comp_Attributes | Maintain a set of security attributes associated with individual components in addition to component identity. |
| O.Attr_based_Policy | Provide policy based access control via security attributes on Users, Components, and Objects. |

## Security Objectives of the Environment

Security Objectives of the Environment encompass environment countermeasures that are necessary to protect assets. The environment is defined as the “aggregate of external procedures, conditions, and objects affecting the development, operation, and maintenance of an information system” or alternatively environment can also be defined as that which is not being built.

Security objectives of the environment can contribute to overall defense-in-depth strategies that result in high-assurance protections with respect to privacy, integrity, availability, and authenticity. The AMI system is being specified to result in only modest levels for environment countermeasures, and therefore, the security objectives of the environment can be identified by addressing broad categories of countermeasures with only modest needs for environment countermeasures (e.g., a remote AMI User should be able to operate on sea, land, or air in a boat, tent, or small airborne vehicle).

Table 23. Security Objectives of the Environment

| Objective Name | Description |
| --- | --- |
| OE.Admin_Guidance | Deter administrator errors by providing adequate administrator guidance. |
| OE.Config_Management | Implement a configuration management plan. Implement configuration management to assure storage integrity, identification of system connectivity (software, hardware, and firmware), and identification of system components (software, hardware, and firmware). |
| OE.Crypto_Key_Man | Fully define cryptographic components, functions, and interfaces. Ensure appropriate protection for cryptographic keys throughout their lifecycle, covering generation, distribution, storage, use, and destruction. |
| OE.Secure_Configuration | Manage and update system security policy data and enforcement functions, and other security-relevant configuration data, in accordance with organizational security policies. |
| OE.Evaluated_System | Evaluate system via Common Criteria methods for proper implementation including examination for accidental or deliberate flaws in code made by the developer. The accidental flaws could be lack of engineering detail or bad design. Where the deliberate flaws would include building trapdoors for later entry as an example. |
| OE.Sys_Backup_Procs | Provide backup procedures to ensure that the system can be reconstructed. |
| OE.User_Auth_Management | Manage and update user authorization and privilege data in accordance with organizational security and personnel policies. |
| OE.User_Guidance | Provide documentation for the general user. |
| OE.Component_Engineering | Manage lifecycle maintenance such that when component hardware becomes obsolete the AMI hardware/software is redesigned to support production |
| OE.Admin_Available | Provide at least one Security Administrator (authorized by the U.S. or the host country) to respond to administrative issues including fixing enrollment/I&A issues. |
| OE.Trusted_Facility | Provide a trusted facility for initialization. |
| OE.Physical_Security | Provide an appropriate level of physical security. |
| OE.BackhaulSLA | Negotiate an SLA with the Backhaul network that meets the operational needs of the mission. This includes required fault-tolerant aspects of the Backhaul’s system including but not limited to routers, switch, and even “back-hoe” protection. |
| OE.Enrollment_Process | Provide a registration/enrollment procedure that includes both a chain of trust of user identity to enroll (e.g. DoD PKI or a US Passport) plus a chain of trust of access and authorization to those domains to grant access. |

## Coverage

## Coverage of Administrative Threats

| Threats | Objectives |
| --- | --- |
| T.Admin.Cred.1 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Session_Protection O.Security_Mgt O.Security_Roles O.Attr_based_Policy OE.Secure_Configuration |
| T.Admin.Cred.2 | O.Admin_Roles_Access O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Cred.3 | O.Admin_Roles_Access O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Enroll.1 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Security_Mgt O.Security_Roles OE.User_Auth_Management OE.Enrollment_Process |
| T.Admin.Enroll.2 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Security_Mgt O.Security_Roles OE.User_Auth_Management OE.Enrollment_Process |
| T.Admin.Enroll.3 | O.Admin_Roles_Access O.Rollback O.Security_Mgt O.Security_Roles OE.User_Auth_Management OE.Enrollment_Process |
| T.Admin.Enroll.4 | O.Admin_Roles_Access O.Rollback O.Security_Mgt O.Security_Roles OE.User_Auth_Management OE.Enrollment_Process |
| T.Admin.Enroll.5 | O.Admin_Roles_Access O.Confidentiality O.I&A O.Rollback O.Session_Protection O.Security_Mgt O.Security_Roles O.Attr_based_Policy OE.User_Auth_Management |
| T.Admin.Enroll.6 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Security_Mgt O.Security_Roles OE.User_Auth_Management OE.Enrollment_Process |
| T.Admin.Enroll.7 | O.Admin_Roles_Access O.Security_Mgt O.Security_Roles OE.User_Auth_Management OE.Enrollment_Process |
| T.Admin.Lockout.1 | O.Admin_Roles_Access O.I&A O.Rollback O.Session_Protection O.Security_Mgt O.Security_Roles O.Attr_based_Policy OE.User_Auth_Management |
| T.Admin.Lockout.2 | O.Admin_Roles_Access O.I&A O.Rollback O.Session_Protection O.Security_Mgt O.Security_Roles O.Attr_based_Policy OE.User_Auth_Management |
| T.Admin.Policy.1 | O.Admin_Roles_Access O.Confidentiality O.I&A O.Session_Protection O.Security_Mgt O.Security_Roles O.Attr_based_Policy OE.User_Auth_Management |
| T.Admin.Policy.2 | O.Admin_Roles_Access O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.3 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.4 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Rollback O.Session_Protection O.Security_Mgt O.Security_Roles O.Attr_based_Policy OE.Secure_Configuration |
| T.Admin.Policy.5 | O.Admin_Roles_Access O.Resource_Quotas O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.6 | O.Admin_Roles_Access O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.7 | O.Admin_Roles_Access O.Confidentiality O.Security_Mgt O.Security_Roles |
| T.Admin.Policy.8 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Session_Protection O.Security_Mgt O.Security_Roles O.Attr_based_Policy OE.Secure_Configuration |
| T.Admin.Policy.9 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.10 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.11 | O.Admin_Roles_Access O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.12 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.13 | O.Admin_Roles_Access O.Confidentiality O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.14 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.NonRepudiation O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.15 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.NonRepudiation O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.16 | O.Admin_Roles_Access O.Confidentiality O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.Policy.17 | O.Admin_Roles_Access O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.PolicyImp.1 | O.Admin_Roles_Access O.Fault_Tolerant O.Rollback O.Security_Mgt O.Security_Roles OE.Secure_Configuration |
| T.Admin.PolicyImp.2 | O.Admin_Roles_Access O.Confidentiality O.I&A O.Rollback O.Session_Protection O.Security_Mgt O.Security_Roles O.Attr_based_Policy OE.Secure_Configuration |

## Coverage of Audit Threats

| Threats | Objectives |
| --- | --- |
| T.Audit.1 | O.Audit_Log_Maintenance O.Import_Export_Control O.Maintain_Online |
| T.Audit.2 | O.Audit_Log_Maintenance O.Import_Export_Control O.Maintain_Online |
| T.Audit.3 | O.Audit_Log_Maintenance O.Import_Export_Control O.Maintain_Online |
| T.Audit.4 | O.Audit O.Confidentiality O.Import_Export_Control O.I&A O.Maintain_Online O.Attr_based_Policy |
| T.Audit.5 | O.Audit O.Confidentiality O.Import_Export_Control O.Maintain_Online O.Attr_based_Policy |
| T.Audit.6 | O.Audit O.Import_Export_Control O.Maintain_Online O.Attr_based_Policy |
| T.Audit.7 | O.Audit O.Audit_Log_Maintenance O.Import_Export_Control O.I&A O.Maintain_Online O.Attr_based_Policy |
| T.Audit.8 | O.Audit O.Import_Export_Control O.Maintain_Online OE.Admin_Guidance |
| T.Audit.9 | O.Audit O.Import_Export_Control O.Maintain_Online OE.Admin_Guidance |
| T.Audit.10 | O.Audit O.Import_Export_Control O.Maintain_Online |
| T.Audit.11 | O.Audit O.Import_Export_Control O.Maintain_Online |

## Coverage of Crypto Threats

| Threats | Objectives |
| --- | --- |
| T.Crypto.Break.1 | O.Confidentiality O.Crypto_Comm_Channel O.Crypto_Storage |
| T.Crypto.Break.2 | O.Confidentiality O.Crypto_Comm_Channel O.Crypto_Storage |
| T.Crypto.Invalid_Keys.1 | O.Trusted_Path&Channel O.Confidentiality OE.Crypto_Key_Man |
| T.Crypto.Invalid_Keys.2 | O.Trusted_Path&Channel O.Confidentiality OE.Crypto_Key_Man |
| T.Crypto.Weak_Keys.1 | O.Trusted_Path&Channel O.Confidentiality O.Crypto_Comm_Channel O.Crypto_Storage OE.Crypto_Key_Man |

## Coverage of Download Threats

| Threats | Objectives |
| --- | --- |
| T.Download.1 | O.Fault_Tolerant O.Import_Export_Control O.Integrity_Checks O.SW_Download |
| T.Download.2 | O.Confidentiality O.Import_Export_Control O.Integrity_Checks O.SW_Download |
| T.Download.3 | O.Import_Export_Control O.Integrity_Checks O.SW_Download |
| T.Download.4 | O.Confidentiality O.Import_Export_Control O.Integrity_Checks O.SW_Download O.Comp_Attributes |
| T.Download.5 | O.Import_Export_Control O.Integrity_Checks O.SW_Download |

## Coverage of Eavesdropping Threats

| Threats | Objectives |
| --- | --- |
| T.Eavesdrop.Apps.1 | O.Confidentiality O.Import_Export_Control |
| T.Eavesdrop.Comm.1 | O.Confidentiality O.Crypto_Comm_Channel O.Import_Export_Control |
| T.Eavesdrop.Comm.2 | O.Confidentiality O.Crypto_Comm_Channel O.Import_Export_Control |
| T.Eavesdrop.Comm.3 | O.Confidentiality O.Crypto_Comm_Channel O.Import_Export_Control |
| T.Eavesdrop.Comm.4 | O.Confidentiality O.Crypto_Comm_Channel O.Import_Export_Control |
| T.Eavesdrop.Comm.5 | O.Confidentiality O.Crypto_Comm_Channel O.Import_Export_Control |
| T.Eavesdrop.Comm.6 | O.Confidentiality O.Crypto_Comm_Channel O.Import_Export_Control |
| T.Eavesdrop.Comm.7 | O.Confidentiality O.Crypto_Comm_Channel O.Import_Export_Control |
| T.Eavesdrop.HMI.1 | O.Confidentiality O.Import_Export_Control O.Session_Protection |
| T.Eavesdrop.HMI.2 | O.Confidentiality O.Session_Protection |
| T.Eavesdrop.HMI.3 | O.Confidentiality O.Session_Protection |
| T.Eavesdrop.HMI.4 | O.Security_Mgt O.Comp_Attributes OE.Physical_Security |

## Coverage of Flawed Implementation Threats

| Threats | Objectives |
| --- | --- |
| T.Flawed_Imp.Backdoor.1 | O.Confidentiality O.SW_Download O.Malicious_Code OE.Evaluated_System |
| T.Flawed_Imp.Developer.1 | O.Confidentiality O.SW_Download O.Malicious_Code OE.Evaluated_System |
| T.Flawed_Imp.Developer.2 | O.SW_Download O.Malicious_Code OE.Evaluated_System |
| T.Flawed_Imp.Developer.3 | O.Confidentiality O.SW_Download O.Malicious_Code OE.Evaluated_System |

## Coverage of I&A Threats

| Threats | Objectives |
| --- | --- |
| T.Ident_Auth.1 | O.Confidentiality O.I&A |
| T.Ident_Auth.2 | O.Confidentiality O.I&A |
| T.Ident_Auth.3 | OE.Admin_Available |
| T.Ident_Auth.4 | O.Confidentiality O.I&A |
| T.Ident_Auth.5 | O.Confidentiality O.I&A |
| T.Ident_Auth.6 | O.Confidentiality O.I&A |
| T.Ident_Auth.7 | O.Confidentiality O.I&A |
| T.Ident_Auth.8 | O.Confidentiality O.I&A |

## Coverage of Information Systems Threats

| Threats | Objectives |
| --- | --- |
| T.InfoSys.1 | O.Confidentiality OE.Evaluated_System |
| T.InfoSys.2 | O.Confidentiality O.Import_Export_Control O.I&A O.NonRepudiation |
| T.InfoSys.Filter.1 | O.Confidentiality OE.Evaluated_System |
| T.InfoSys.Printer.1 | O.Confidentiality O.User_Attributes OE.User_Guidance OE.Physical_Security |

## Coverage of Initialization Threats

| Threats | Objectives |
| --- | --- |
| T.Initialize.Configuration.1 | O.Confidentiality OE.Trusted_Facility |
| T.Initialize.Configuration.2 | O.Confidentiality OE.Trusted_Facility |
| T.Initialize.Configuration.3 | O.Confidentiality O.SW_Download |
| T.Initialize.Distribution.1 | O.Confidentiality O.Integrity_Checks O.SW_Download |
| T.Initialize.Distribution.2 | O.Confidentiality O.Integrity_Checks O.SW_Download O.Malicious_Code |

## Coverage of Insider Threats

| Threats | Objectives |
| --- | --- |
| T.Insider.Aggregation.1 | O.Audit O.Confidentiality O.User_Attributes |
| T.Insider.Confusion.1 | O.Confidentiality O.Rollback |
| T.Insider.Confusion.2 | O.Confidentiality O.Import_Export_Control |
| T.Insider.Confusion.3 | O.Confidentiality O.Import_Export_Control O.Rollback |
| T.Insider.Misinfo.1 | O.Import_Export_Control |
| T.Insider.Mislabel.1 | O.Confidentiality O.Import_Export_Control |
| T.Insider.Mislabel.2 | O.Confidentiality O.Import_Export_Control O.I&A |
| T.Insider.Misuse.Info.1 | O.Confidentiality O.Import_Export_Control |
| T.Insider.Misuse.Info.2 | O.Confidentiality OE.Physical_Security |
| T.Insider.Misuse.Res.1 | O.Maintain_Online O.Priority_Of_Service O.Resource_Quotas |

## Coverage of Key Management Threats

| Threats | Objectives |
| --- | --- |
| T.KeyMan.Deliver.1 | O.Confidentiality OE.Admin_Guidance OE.Crypto_Key_Man |
| T.KeyMan.Deliver.2 | O.Confidentiality OE.Admin_Guidance OE.Crypto_Key_Man |
| T.KeyMan.Deliver.3 | O.Confidentiality OE.Admin_Guidance OE.Crypto_Key_Man |
| T.KeyMan.Deliver.4 | O.Fault_Tolerant OE.Crypto_Key_Man |
| T.KeyMan.Membership.1 | O.Admin_Roles_Access O.Confidentiality OE.Admin_Guidance OE.User_Auth_Management |
| T.KeyMan.Membership.2 | O.Admin_Roles_Access OE.Admin_Guidance OE.User_Auth_Management |
| T.KeyMan.Membership.3 | O.Admin_Roles_Access O.Confidentiality OE.Admin_Guidance OE.Crypto_Key_Man OE.User_Auth_Management |
| T.KeyMan.Obsolescence.1 | OE.Crypto_Key_Man |
| T.KeyMan.Order.1 | OE.Admin_Guidance OE.Crypto_Key_Man |
| T.KeyMan.Order.2 | OE.Admin_Guidance OE.Crypto_Key_Man |
| T.KeyMan.Order.3 | O.Fault_Tolerant OE.Admin_Guidance OE.Crypto_Key_Man |
| T.KeyMan.TrackControl.1 | O.Fault_Tolerant OE.Admin_Guidance OE.Crypto_Key_Man |

## Coverage of Malicious Code Threats

| Threats | Objectives |
| --- | --- |
| T.Malicious_Code.App.1 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.App.2 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.App.3 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.App.4 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Info.1 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Info.2 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Info.3 | O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Info.4 | O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Info.5 | O.Integrity_Checks O.Isolate_Executables O.Malicious_Code |
| T.Malicious_Code.Info.6 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code |
| T.Malicious_Code.Info.7 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code |
| T.Malicious_Code.Info.8 | O.Integrity_Checks O.Isolate_Executables O.Malicious_Code |
| T.Malicious_Code.Proxy.1 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Res.1 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Res.2 | O.Confidentiality O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Res.3 | O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Res.4 | O.Integrity_Checks O.Isolate_Executables O.Malicious_Code O.Attr_based_Policy |
| T.Malicious_Code.Res.5 | O.Integrity_Checks O.Isolate_Executables O.Malicious_Code |
| T.Malicious_Code.Res.6 | O.Integrity_Checks O.Isolate_Executables O.Malicious_Code |
| T.Malicious_Code.Res.7 | O.Integrity_Checks O.Isolate_Executables O.Malicious_Code |

## Coverage of Network Threats

| Threats | Objectives |
| --- | --- |
| T.Network.Denial.1 | O.Trusted_Path&Channel O.Fault_Tolerant O.Maintain_Online O.Resource_Quotas |
| T.Network.Filter.1 | O.Confidentiality O.Trusted_Path&Channel O.Maintain_Online |
| T.Network.Modify.1 | O.Crypto_Comm_Channel |
| T.Network.Modify.2 | O.Crypto_Comm_Channel O.Maintain_Online |
| T.Network.Replay.1 | O.Maintain_Online |
| T.Network.Replay.2 | O.Maintain_Online |
| T.Network.Unauth.1 | O.Admin_Roles_Access O.Confidentiality O.Audit O.User_Attributes OE.Admin_Guidance OE.User_Guidance |

## Coverage of Operational Denial of Service Threats

| Threats | Objectives |
| --- | --- |
| T.Op.Denial.1 | O.Import_Export_Control O.I&A O.Integrity_Checks O.Integ_Data O.NonRepudiation O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy OE.User_Guidance |
| T.Op.Denial.2 | O.Import_Export_Control O.I&A O.NonRepudiation O.Priority_Of_Service O.Session_Protection O.User_Attributes O.Attr_based_Policy OE.User_Guidance |
| T.Op.Denial.3 | O.I&A O.NonRepudiation O.Resource_Quotas O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.4 | O.Import_Export_Control O.I&A O.Integrity_Checks O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.5 | O.Import_Export_Control O.I&A O.Obj_Attr O.Resource_Quotas O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.6 | O.Import_Export_Control O.I&A O.Obj_Attr O.Resource_Quotas O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.7 | O.I&A O.Obj_Attr O.Resource_Quotas O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.8 | O.Import_Export_Control O.I&A O.Integrity_Checks O.Obj_Attr O.Session_Protection O.User_Attributes OE.User_Guidance O.Attr_based_Policy |
| T.Op.Denial.9 | O.Import_Export_Control O.I&A O.Obj_Attr O.Resource_Quotas O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.10 | O.Import_Export_Control O.I&A O.Obj_Attr O.Resource_Quotas O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.11 | O.I&A O.Integrity_Checks O.Obj_Attr O.Priority_Of_Service O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.12 | O.I&A O.NonRepudiation O.User_Attributes OE.User_Guidance O.Attr_based_Policy |
| T.Op.Denial.13 | O.I&A O.Integrity_Checks O.Resource_Quotas O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.14 | O.I&A O.Integrity_Checks O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.15 | O.I&A O.Integrity_Checks O.Obj_Attr O.User_Attributes O.Attr_based_Policy |
| T.Op.Denial.16 | O.I&A O.Integrity_Checks O.Obj_Attr O.User_Attributes O.Attr_based_Policy |

## Coverage of Operational Disclosure Threats

| Threats | Objectives |
| --- | --- |
| T.Op.Disclosure.1 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Disclosure.2 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Integrity_Checks O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Disclosure.3 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy OE.User_Guidance |
| T.Op.Disclosure.4 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy OE.User_Guidance |
| T.Op.Disclosure.5 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy OE.User_Guidance |
| T.Op.Disclosure.6 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy OE.User_Guidance |
| T.Op.Disclosure.7 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr OE.User_Guidance |
| T.Op.Disclosure.8 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Emanations O.User_Attributes O.Attr_based_Policy |
| T.Op.Disclosure.9 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Disclosure.10 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.Emanations |
| T.Op.Disclosure.11 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Disclosure.12 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.User_Attributes OE.User_Guidance O.Attr_based_Policy |
| T.Op.Disclosure.13 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr |
| T.Op.Disclosure.14 | O.Admin_Roles_Access O.Confidentiality O.Import_Export_Control O.I&A O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Disclosure.15 | O.Sys_Assur_HW/SW/FW O.Comp_Attributes OE.Config_Management OE.Evaluated_System |

## Coverage of Operational Integrity Threats

| Threats | Objectives |
| --- | --- |
| T.Op.Integrity.1 | O.I&A O.Integrity_Checks O.Integ_Data O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Integrity.2 | O.I&A O.Integrity_Checks O.Integ_Data O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Integrity.3 | O.I&A O.Integrity_Checks O.Integ_Data O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Integrity.4 | O.I&A O.Integrity_Checks O.Integ_Data O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Integrity.5 | O.I&A O.Integrity_Checks O.Integ_Data O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Integrity.6 | O.I&A O.Integrity_Checks O.Integ_Data O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Integrity.7 | O.I&A O.Integrity_Checks O.Integ_Data O.Obj_Attr O.Session_Protection |
| T.Op.Integrity.8 | O.I&A O.Integrity_Checks O.Integ_Data O.Obj_Attr O.Session_Protection O.User_Attributes O.Attr_based_Policy |

## Coverage of Operational Non-Repudiation Threats

| Threats | Objectives |
| --- | --- |
| T.Op.Non-Repudiation.1 | O.Import_Export_Control O.I&A O.NonRepudiation O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Non-Repudiation.2 | O.Import_Export_Control O.I&A O.NonRepudiation O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Non-Repudiation.3 | O.Import_Export_Control O.I&A O.NonRepudiation O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Non-Repudiation.4 | O.Import_Export_Control O.I&A O.NonRepudiation O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Non-Repudiation.5 | O.Import_Export_Control O.I&A O.NonRepudiation O.Session_Protection O.User_Attributes O.Attr_based_Policy |
| T.Op.Non-Repudiation.6 | O.Import_Export_Control O.I&A O.NonRepudiation O.Session_Protection O.User_Attributes O.Attr_based_Policy |

## Coverage of Physical Threats

| Threats | Objectives |
| --- | --- |
| T.Physical.Capture.1 | O.Confidentiality O.Fault_Tolerant O.Secure_State O.Tamper |
| T.Physical.Capture.2 | O.Confidentiality O.Fault_Tolerant O.Secure_State O.Tamper |
| T.Physical.Denial.1 | O.Secure_State |
| T.Physical.Destruction.IA.1 | O.Fault_Tolerant O.I&A OE.Admin_Available |
| T.Physical.Destruction.IA.2 | O.Fault_Tolerant O.I&A OE.Admin_Available |
| T.Physical.Destruction.Info.1 | O.Secure_State OE.Sys_Backup_Procs |
| T.Physical.Destruction.Info.2 | O.Secure_State OE.Sys_Backup_Procs |
| T.Physical.Destruction.Res.1 | O.Secure_State |
| T.Physical.Destruction.Res.2 | O.Secure_State |
| T.Physical.Destruction.Serv.1 | O.Secure_State |
| T.Physical.Destruction.Serv.2 | O.Secure_State |
| T.Physical.Destruction.Total.1 | O.Secure_State |
| T.Physical.Destruction.Total.2 | O.Secure_State |
| T.Physical.Extract.IA.1 | O.Confidentiality O.Tamper |
| T.Physical.Extract.IA.2 | O.Confidentiality O.Emanations |
| T.Physical.Extract.NonAMI.1 | O.Confidentiality O.Emanations |
| T.Physical.Extract.Res.1 | O.Confidentiality O.Tamper |
| T.Physical.Extract.Res.2 | O.Confidentiality O.Emanations |
| T.Physical.Extract.Res.3 | O.Confidentiality O.Emanations |
| T.Physical.HWFailure.1 | O.Secure_State O.Sys_Assur_HW/SW/FW |
| T.Physical.HWFailure.2 | O.Confidentiality O.Secure_State O.Sys_Assur_HW/SW/FW |
| T.Physical.HWFailure.3 | O.Secure_State O.Sys_Assur_HW/SW/FW |
| T.Physical.MechFailure.1 | O.Secure_State O.Sys_Assur_HW/SW/FW |
| T.Physical.Modification.Info.1 | O.Tamper |
| T.Physical.Modification.Input.1 | O.Confidentiality O.Tamper |
| T.Physical.Modification.Res.1 | O.Confidentiality O.Tamper |
| T.Physical.Modification.Res.2 | O.Confidentiality O.Tamper |
| T.Physical.Obsolete.1 | OE.Component_Engineering |
| T.Physical.Obsolete.2 | OE.Component_Engineering |
| T.Physical.ReverseEng.1 | O.Confidentiality O.Secure_via_Cryptography |
| T.Physical.ReverseEng.2 | O.Confidentiality O.Secure_via_Cryptography |
| T.Physical.ReverseEng.3 | O.Confidentiality O.Secure_via_Cryptography |
| T.Physical.ReverseEng.4 | O.Confidentiality O.Secure_via_Cryptography |
| T.Physical.SWFailure.1 | O.Secure_State O.Sys_Assur_HW/SW/FW |
| T.Physical.SWFailure.2 | O.Confidentiality O.Secure_State O.Sys_Assur_HW/SW/FW |

## Coverage of Social Engineering Threats

| Threats | Objectives |
| --- | --- |
| T.Social_Eng.Access.1 | O.Confidentiality O.I&A OE.Physical_Security |
| T.Social_Eng.Access.2 | O.Confidentiality |
| T.Social_Eng.Access.3 | O.Confidentiality |
| T.Social_Eng.AdminLeak.1 | O.Confidentiality OE.Secure_Configuration OE.Evaluated_System |
| T.Social_Eng.Authorize.1 | O.Confidentiality O.I&A OE.Physical_Security |
| T.Social_Eng.Info.1 | O.Confidentiality O.User_Attributes OE.User_Auth_Management OE.Physical_Security |
| T.Social_Eng.Info.2 | O.Confidentiality OE.User_Auth_Management OE.Secure_Configuration OE.User_Auth_Management |
| T.Social_Eng.Info.3 | OE.User_Auth_Management OE.Secure_Configuration OE.User_Auth_Management |
| T.Social_Eng.Info.4 | O.Confidentiality O.I&A OE.User_Auth_Management |

## Coverage of Trust Threats

| Threats | Objectives |
| --- | --- |
| T.Trust.Impersonate.1 | O.Confidentiality O.I&A |
| T.Trust.Impersonate.2 | O.Confidentiality O.I&A OE.Crypto_Key_Man |
| T.Trust.Impersonate.3 | O.Confidentiality O.I&A |
| T.Trust.Impersonate.4 | O.Confidentiality O.I&A |
| T.Trust.Impersonate.5 | O.Confidentiality O.I&A |
| T.Trust.Impersonate.6 | O.Confidentiality O.I&A |
| T.Trust.Impersonate.7 | O.Confidentiality O.I&A O.Session_Protection |
| T.Trust.Impersonate.8 | O.Confidentiality O.I&A |
| T.Trust.Info.1 | O.I&A O.Session_Protection |
| T.Trust.Res.1 | O.Confidentiality O.I&A O.Session_Protection |
| T.Trust.Serv.1 | O.Confidentiality O.I&A O.Session_Protection |

## Coverage of Assumptions

| Assumptions | Objectives |
| --- | --- |
| A.Admin_Available | O.Admin_Roles_Access |
| A.Audit_Analysis | O.Audit O.Maintain_Online OE.Admin_Guidance |
| A.Back_Up | O.Admin_Roles_Access |
| A.Clearance | OE.Admin_Guidance |
| A.Comms_Available | O.Fault_Tolerant OE.Config_Management |
| A.Environment | O.Secure_State |
| A.External_Networks | O.Fault_Tolerant |
| A.KeyMat_Source | OE.Crypto_Key_Man |
| A.Personnel_Untrusted | O.Audit O.Crypto_Comm_Channel O.Crypto_Storage O.Crypto_Import_Export O.Import_Export_Control O.I&A O.Isolate_Executables O.NonRepudiation O.Obj_Attr O.Priority_Of_Service O.Resource_Quotas O.Rollback O.Session_Protection O.Security_Mgt O.Security_Roles O.Sys_Assur_HW/SW/FW O.Tamper O.User_Attributes O.Malicious_Code O.Comp_Attributes O.Attr_based_Policy OE.Config_Management OE.Crypto_Key_Man OE.Secure_Configuration OE.Evaluated_System OE.Sys_Backup_Procs OE.User_Auth_Management OE.Physical_Security |
| A.Physical_Protection | O.Secure_State OE.Physical_Security |
| A.Partial_Physical_Security | O.Tamper OE.Physical_Security |
| A.Policy_MoA | O.Audit O.Crypto_Comm_Channel O.Crypto_Storage O.Crypto_Import_Export O.Import_Export_Control O.I&A O.Isolate_Executables O.NonRepudiation O.Obj_Attr O.Priority_Of_Service O.Resource_Quotas O.Rollback O.Session_Protection O.Security_Mgt O.Security_Roles O.Sys_Assur_HW/SW/FW O.Tamper O.User_Attributes O.Malicious_Code O.Comp_Attributes O.Attr_based_Policy OE.Config_Management OE.Crypto_Key_Man OE.Secure_Configuration OE.Evaluated_System OE.Sys_Backup_Procs OE.User_Auth_Management OE.Physical_Security |
| A.Printer_Security | OE.User_Guidance OE.Physical_Security |
| A.TOE_Design | OE.Admin_Guidance OE.Config_Management OE.Crypto_Key_Man OE.Secure_Configuration OE.Evaluated_System OE.Sys_Backup_Procs OE.User_Auth_Management OE.User_Guidance OE.Component_Engineering OE.Admin_Available OE.Trusted_Facility OE.Physical_Security OE.BackhaulSLA |
| A.TOE_Maintenance | O.I&A O.Maintain_Online OE.Admin_Guidance OE.Secure_Configuration |
| A.TOE_Operation | O.I&A O.Maintain_Online OE.Admin_Guidance OE.Secure_Configuration OE.BackhaulSLA |
| A.TOE_User | O.I&A OE.Secure_Configuration OE.User_Auth_Management OE.User_Guidance |
| A.Trained | O.I&A OE.User_Auth_Management OE.User_Guidance |
| A.Trusted_Source | OE.Crypto_Key_Man OE.Trusted_Facility |
| A.Visual_Security | OE.Secure_Configuration OE.Physical_Security |

## Coverage of Policy

| Policy | Objectives |
| --- | --- |
| P.Access | O.Admin_Roles_Access O.I&A |
| P.Accountability | O.Admin_Roles_Access O.Audit O.I&A O.NonRepudiation OE.Admin_Guidance |
| P.Admin_Security | O.Admin_Roles_Access O.I&A O.Maintain_Online |
| P.Admin_Split | O.Admin_Roles_Access |
| P.Admin_System | O.Admin_Roles_Access O.I&A O.Maintain_Online |
| P.Audit_Review | O.Admin_Roles_Access O.Audit O.Audit_Log_Maintenance O.Maintain_Online OE.Admin_Guidance |
| P.Cross_Domain_Filtering | O.Import_Export_Control O.I&A OE.Admin_Guidance |
| P.Distribution | O.Integrity_Checks O.Integ_Data O.Maintain_Online |
| P.Due_Care | O.Trusted_Path&Channel OE.Admin_Guidance OE.Config_Management |
| P.Info_Senders | O.Import_Export_Control O.I&A |
| P.Info_Sources | O.Import_Export_Control O.I&A |
| P.Integrity | O.Integrity_Checks O.Integ_Data O.Obj_Attr |
| P.Protect | O.Trusted_Path&Channel O.Crypto_Comm_Channel O.Crypto_Storage O.Obj_Attr OE.Crypto_Key_Man |
| P.Security_Admin_Restricted | O.Admin_Roles_Access O.I&A OE.Admin_Guidance |
| P.Users | O.Import_Export_Control O.I&A |

## Coverage of Objectives for Target

| Objectives | Threats / Policies / Assumptions |
| --- | --- |
| O.Admin_Roles_Access | T.Admin.Cred.1 T.Admin.Cred.2 T.Admin.Cred.3 T.Admin.Enroll.1 T.Admin.Enroll.2 T.Admin.Enroll.3 T.Admin.Enroll.4 T.Admin.Enroll.5 T.Admin.Enroll.6 T.Admin.Enroll.7 T.Admin.Lockout.1 T.Admin.Lockout.2 T.Admin.Policy.1 T.Admin.Policy.2 T.Admin.Policy.3 T.Admin.Policy.4 T.Admin.Policy.5 T.Admin.Policy.6 T.Admin.Policy.7 T.Admin.Policy.8 T.Admin.Policy.9 T.Admin.Policy.10 T.Admin.Policy.11 T.Admin.Policy.12 T.Admin.Policy.13 T.Admin.Policy.14 T.Admin.Policy.15 T.Admin.Policy.16 T.Admin.Policy.17 T.Admin.PolicyImp.1 T.Admin.PolicyImp.2 T.KeyMan.Membership.1 T.KeyMan.Membership.2 T.KeyMan.Membership.3 T.Network.Unauth.1 |
| O.Admin_Roles_Access (cont.) | T.Op.Disclosure.1 T.Op.Disclosure.2 T.Op.Disclosure.3 T.Op.Disclosure.4 T.Op.Disclosure.5 T.Op.Disclosure.6 T.Op.Disclosure.7 T.Op.Disclosure.8 T.Op.Disclosure.9 T.Op.Disclosure.10 T.Op.Disclosure.11 T.Op.Disclosure.12 T.Op.Disclosure.13 T.Op.Disclosure.14 A.Admin_Available A.Back_Up P.Access P.Accountability P.Admin_Security P.Admin_Split P.Admin_System P.Audit_Review P.Security_Admin_Restricted |
| O.Audit | T.Audit.4 T.Audit.5 T.Audit.6 T.Audit.7 T.Audit.8 T.Audit.9 T.Audit.10 T.Audit.11 T.Insider.Aggregation.1 T.Network.Unauth.1 A.Audit_Analysis A.Personnel_Untrusted A.Policy_MoA P.Accountability P.Audit_Review |
| O.Audit_Log_Maintenance | T.Audit.1 T.Audit.2 T.Audit.3 T.Audit.7 P.Audit_Review |
| O.Trusted_Path&Channel | T.Crypto.Invalid_Keys.1 T.Crypto.Invalid_Keys.2 T.Crypto.Weak_Keys.1 T.Network.Denial.1 T.Network.Filter.1 P.Due_Care P.Protect |
| O.Confidentiality | T.Admin.Cred.1 T.Admin.Enroll.1 T.Admin.Enroll.2 T.Admin.Enroll.5 T.Admin.Enroll.6 T.Admin.Policy.1 T.Admin.Policy.2 T.Admin.Policy.3 T.Admin.Policy.4 T.Admin.Policy.7 T.Admin.Policy.8 T.Admin.Policy.9 T.Admin.Policy.10 T.Admin.Policy.12 T.Admin.Policy.13 T.Admin.Policy.14 T.Admin.Policy.15 T.Admin.Policy.16 T.Admin.PolicyImp.2 T.Audit.4 T.Audit.5 |
| O.Confidentiality (cont.) | T.Crypto.Break.1 T.Crypto.Break.2 T.Crypto.Invalid_Keys.1 T.Crypto.Invalid_Keys.2 T.Crypto.Weak_Keys.1 T.Download.2 T.Download.4 T.Eavesdrop.Apps.1 T.Eavesdrop.Comm.1 T.Eavesdrop.Comm.2 T.Eavesdrop.Comm.3 T.Eavesdrop.Comm.4 T.Eavesdrop.Comm.5 T.Eavesdrop.Comm.6 T.Eavesdrop.Comm.7 T.Eavesdrop.HMI.3 T.Flawed_Imp.Backdoor.1 T.Flawed_Imp.Developer.1 T.Flawed_Imp.Developer.3 T.Ident_Auth.1 T.Ident_Auth.2 T.Ident_Auth.4 T.Ident_Auth.5 T.Ident_Auth.8 T.InfoSys.1 T.InfoSys.2 T.InfoSys.Filter.1 T.InfoSys.Printer.1 T.Initialize.Configuration.1 T.Initialize.Configuration.2 T.Initialize.Configuration.3 T.Initialize.Distribution.1 T.Initialize.Distribution.2 |
| O.Confidentiality (cont.) | T.Insider.Aggregation.1 T.Insider.Confusion.1 T.Insider.Confusion.2 T.Insider.Confusion.3 T.Insider.Mislabel.1 T.Insider.Mislabel.2 T.Insider.Misuse.Info.1 T.Insider.Misuse.Info.2 T.KeyMan.Deliver.1 T.KeyMan.Deliver.2 T.KeyMan.Deliver.3 T.KeyMan.Membership.1 T.KeyMan.Membership.3 T.Malicious_Code.App.1 T.Malicious_Code.App.2 T.Malicious_Code.App.3 T.Malicious_Code.App.4 T.Malicious_Code.Info.1 T.Malicious_Code.Info.2 T.Malicious_Code.Info.6 T.Malicious_Code.Info.7 T.Malicious_Code.Proxy.1 T.Malicious_Code.Res.1 T.Malicious_Code.Res.2 T.Malicious_Code.Res.5 T.Malicious_Code.Res.6 T.Network.Filter.1 T.Network.Unauth.1 |
| O.Confidentiality (cont.) | T.Op.Disclosure.1 T.Op.Disclosure.2 T.Op.Disclosure.3 T.Op.Disclosure.4 T.Op.Disclosure.5 T.Op.Disclosure.6 T.Op.Disclosure.7 T.Op.Disclosure.8 T.Op.Disclosure.9 T.Op.Disclosure.10 T.Op.Disclosure.11 T.Op.Disclosure.12 T.Op.Disclosure.13 T.Op.Disclosure.14 T.Physical.Capture.1 T.Physical.Capture.2 T.Physical.Extract.IA.1 T.Physical.Extract.IA.2 T.Physical.Extract.NonAMI.1 T.Physical.Extract.Res.1 T.Physical.Extract.Res.2 T.Physical.Extract.Res.3 T.Physical.HWFailure.2 T.Physical.Modification.Input.1 T.Physical.Modification.Res.1 T.Physical.Modification.Res.2 T.Physical.ReverseEng.1 T.Physical.ReverseEng.2 T.Physical.ReverseEng.3 T.Physical.ReverseEng.4 T.Physical.SWFailure.2 |
| O.Confidentiality (cont.) | T.Social_Eng.Access.1 T.Social_Eng.Access.2 T.Social_Eng.Access.3 T.Social_Eng.AdminLeak.1 T.Social_Eng.Authorize.1 T.Social_Eng.Info.1 T.Social_Eng.Info.2 T.Social_Eng.Info.4 T.Trust.Impersonate.1 T.Trust.Impersonate.2 T.Trust.Impersonate.3 T.Trust.Impersonate.4 T.Trust.Impersonate.5 T.Trust.Impersonate.6 T.Trust.Impersonate.7 T.Trust.Impersonate.8 T.Trust.Res.1 T.Trust.Serv.1 |
| O.Crypto_Comm_Channel | T.Crypto.Break.1 T.Crypto.Break.2 T.Crypto.Weak_Keys.1 T.Eavesdrop.Comm.1 T.Eavesdrop.Comm.2 T.Eavesdrop.Comm.3 T.Eavesdrop.Comm.4 T.Eavesdrop.Comm.5 T.Eavesdrop.Comm.6 T.Eavesdrop.Comm.7 T.Network.Modify.1 T.Network.Modify.2 A.Personnel_Untrusted A.Policy_MoA P.Protect |
| O.Crypto_Storage | T.Crypto.Break.1 T.Crypto.Break.2 T.Crypto.Weak_Keys.1 A.Personnel_Untrusted A.Policy_MoA P.Protect |
| O.Crypto_Import_Export | A.Personnel_Untrusted A.Policy_MoA |
| O.Fault_Tolerant | T.Admin.PolicyImp.1 T.Download.1 T.KeyMan.Deliver.4 T.KeyMan.Order.3 T.KeyMan.TrackControl.1 T.Network.Denial.1 T.Physical.Capture.1 T.Physical.Capture.2 T.Physical.Destruction.IA.1 T.Physical.Destruction.IA.2 A.Comms_Available A.External_Networks |
| O.Import_Export_Control | T.Admin.Policy.4 T.Admin.Policy.14 T.Admin.Policy.15 T.Audit.1 T.Audit.2 T.Audit.3 T.Audit.4 T.Audit.5 T.Audit.6 T.Audit.7 T.Audit.8 T.Audit.9 T.Audit.10 T.Audit.11 T.Download.1 T.Download.2 T.Download.3 T.Download.4 T.Download.5 |
| O.Import_Export_Control (cont.) | T.Eavesdrop.Apps.1 T.Eavesdrop.Comm.1 T.Eavesdrop.Comm.2 T.Eavesdrop.Comm.3 T.Eavesdrop.Comm.4 T.Eavesdrop.Comm.5 T.Eavesdrop.Comm.6 T.Eavesdrop.Comm.7 T.Eavesdrop.HMI.1 T.InfoSys.2 T.Insider.Confusion.2 T.Insider.Confusion.3 T.Insider.Misinfo.1 T.Insider.Mislabel.1 T.Insider.Mislabel.2 T.Insider.Misuse.Info.1 T.Op.Denial.1 T.Op.Denial.2 T.Op.Denial.4 T.Op.Denial.5 T.Op.Denial.6 T.Op.Denial.8 T.Op.Denial.9 T.Op.Denial.10 T.Op.Disclosure.1 T.Op.Disclosure.2 T.Op.Disclosure.3 T.Op.Disclosure.4 T.Op.Disclosure.5 T.Op.Disclosure.6 T.Op.Disclosure.7 T.Op.Disclosure.8 T.Op.Disclosure.9 T.Op.Disclosure.10 T.Op.Disclosure.11 T.Op.Disclosure.12 T.Op.Disclosure.13 T.Op.Disclosure.14 |
| O.Import_Export_Control (cont.) | T.Op.Non-Repudiation.1 T.Op.Non-Repudiation.2 T.Op.Non-Repudiation.3 T.Op.Non-Repudiation.4 T.Op.Non-Repudiation.5 T.Op.Non-Repudiation.6 A.Personnel_Untrusted A.Policy_MoA P.Cross_Domain_Filtering P.Info_Senders P.Info_Sources P.Users |
| O.I&A | T.Admin.Enroll.5 T.Admin.Lockout.1 T.Admin.Lockout.2 T.Admin.Policy.1 T.Admin.Policy.4 T.Admin.PolicyImp.2 T.Audit.4 T.Audit.7 T.Ident_Auth.1 T.Ident_Auth.2 T.Ident_Auth.4 T.Ident_Auth.5 T.Ident_Auth.6 T.Ident_Auth.7 T.Ident_Auth.8 T.InfoSys.2 T.Insider.Mislabel.2 |
| O.I&A (cont.) | T.Op.Denial.1 T.Op.Denial.2 T.Op.Denial.3 T.Op.Denial.4 T.Op.Denial.5 T.Op.Denial.6 T.Op.Denial.7 T.Op.Denial.8 T.Op.Denial.9 T.Op.Denial.10 T.Op.Denial.11 T.Op.Denial.12 T.Op.Denial.13 T.Op.Denial.14 T.Op.Denial.15 T.Op.Denial.16 T.Op.Disclosure.1 T.Op.Disclosure.2 T.Op.Disclosure.3 T.Op.Disclosure.4 T.Op.Disclosure.5 T.Op.Disclosure.6 T.Op.Disclosure.7 T.Op.Disclosure.8 T.Op.Disclosure.9 T.Op.Disclosure.10 T.Op.Disclosure.11 T.Op.Disclosure.12 T.Op.Disclosure.13 T.Op.Disclosure.14 T.Op.Integrity.1 T.Op.Integrity.2 T.Op.Integrity.3 T.Op.Integrity.4 T.Op.Integrity.5 T.Op.Integrity.6 T.Op.Integrity.7 T.Op.Integrity.8 |
| O.I&A (cont.) | T.Op.Non-Repudiation.1 T.Op.Non-Repudiation.2 T.Op.Non-Repudiation.3 T.Op.Non-Repudiation.4 T.Op.Non-Repudiation.5 T.Op.Non-Repudiation.6 T.Physical.Destruction.IA.1 T.Physical.Destruction.IA.2 T.Social_Eng.Access.1 T.Social_Eng.Authorize.1 T.Social_Eng.Info.4 T.Trust.Impersonate.1 T.Trust.Impersonate.2 T.Trust.Impersonate.3 T.Trust.Impersonate.4 T.Trust.Impersonate.5 T.Trust.Impersonate.6 T.Trust.Impersonate.7 T.Trust.Impersonate.8 T.Trust.Info.1 T.Trust.Res.1 T.Trust.Serv.1 A.Personnel_Untrusted A.Policy_MoA A.TOE_Maintenance A.TOE_Operation A.TOE_User A.Trained P.Access P.Accountability P.Admin_Security P.Admin_System P.Cross_Domain_Filtering P.Info_Senders P.Info_Sources P.Security_Admin_Restricted P.Users |
| O.Integrity_Checks | T.Download.1 T.Download.2 T.Download.3 T.Download.4 T.Download.5 T.Initialize.Distribution.1 T.Initialize.Distribution.2 T.Malicious_Code.App.1 T.Malicious_Code.App.2 T.Malicious_Code.App.3 T.Malicious_Code.App.4 T.Malicious_Code.Info.1 T.Malicious_Code.Info.2 T.Malicious_Code.Info.3 T.Malicious_Code.Info.4 T.Malicious_Code.Info.5 T.Malicious_Code.Info.6 T.Malicious_Code.Info.7 T.Malicious_Code.Info.8 T.Malicious_Code.Proxy.1 T.Malicious_Code.Res.1 T.Malicious_Code.Res.2 T.Malicious_Code.Res.3 T.Malicious_Code.Res.4 T.Malicious_Code.Res.5 T.Malicious_Code.Res.6 T.Malicious_Code.Res.7 T.Op.Denial.1 T.Op.Denial.4 T.Op.Denial.8 T.Op.Denial.11 T.Op.Denial.13 T.Op.Denial.14 T.Op.Denial.15 T.Op.Denial.16 |
| O.Integrity_Checks (cont.) | T.Op.Disclosure.2 T.Op.Integrity.1 T.Op.Integrity.2 T.Op.Integrity.3 T.Op.Integrity.4 T.Op.Integrity.5 T.Op.Integrity.6 T.Op.Integrity.7 T.Op.Integrity.8 P.Distribution P.Integrity |
| O.Integ_Data | T.Op.Denial.1 T.Op.Integrity.1 T.Op.Integrity.2 T.Op.Integrity.3 T.Op.Integrity.4 T.Op.Integrity.5 T.Op.Integrity.6 T.Op.Integrity.7 T.Op.Integrity.8 P.Distribution P.Integrity |
| O.Isolate_Executables | T.Malicious_Code.App.1 T.Malicious_Code.App.2 T.Malicious_Code.App.3 T.Malicious_Code.App.4 T.Malicious_Code.Info.1 T.Malicious_Code.Info.2 T.Malicious_Code.Info.3 T.Malicious_Code.Info.4 T.Malicious_Code.Info.5 T.Malicious_Code.Info.6 T.Malicious_Code.Info.7 T.Malicious_Code.Info.8 T.Malicious_Code.Proxy.1 T.Malicious_Code.Res.1 T.Malicious_Code.Res.2 T.Malicious_Code.Res.3 T.Malicious_Code.Res.4 T.Malicious_Code.Res.5 T.Malicious_Code.Res.6 T.Malicious_Code.Res.7 A.Personnel_Untrusted A.Policy_MoA |
| O.Maintain_Online | T.Audit.1 T.Audit.2 T.Audit.3 T.Audit.4 T.Audit.5 T.Audit.6 T.Audit.7 T.Audit.8 T.Audit.9 T.Audit.10 T.Audit.11 T.Insider.Misuse.Res.1 T.Network.Denial.1 T.Network.Filter.1 T.Network.Modify.2 T.Network.Replay.1 T.Network.Replay.2 A.Audit_Analysis A.TOE_Maintenance A.TOE_Operation P.Admin_Security P.Admin_System P.Audit_Review P.Distribution |
| O.NonRepudiation | T.Admin.Policy.14 T.Admin.Policy.15 T.InfoSys.2 T.Op.Denial.1 T.Op.Denial.2 T.Op.Denial.3 T.Op.Denial.12 T.Op.Non-Repudiation.1 T.Op.Non-Repudiation.2 T.Op.Non-Repudiation.3 T.Op.Non-Repudiation.4 T.Op.Non-Repudiation.5 T.Op.Non-Repudiation.6 A.Personnel_Untrusted A.Policy_MoA P.Accountability |
| O.Obj_Attr | T.Op.Denial.1 T.Op.Denial.4 T.Op.Denial.5 T.Op.Denial.6 T.Op.Denial.7 T.Op.Denial.8 T.Op.Denial.9 T.Op.Denial.10 T.Op.Denial.11 T.Op.Denial.15 T.Op.Denial.16 T.Op.Disclosure.1 T.Op.Disclosure.2 T.Op.Disclosure.3 T.Op.Disclosure.4 T.Op.Disclosure.5 T.Op.Disclosure.6 T.Op.Disclosure.7 T.Op.Disclosure.8 T.Op.Disclosure.9 T.Op.Disclosure.10 T.Op.Disclosure.11 T.Op.Disclosure.12 T.Op.Disclosure.13 T.Op.Disclosure.14 T.Op.Integrity.1 T.Op.Integrity.2 T.Op.Integrity.3 T.Op.Integrity.4 T.Op.Integrity.5 T.Op.Integrity.6 T.Op.Integrity.7 T.Op.Integrity.8 A.Personnel_Untrusted A.Policy_MoA P.Integrity P.Protect |
| O.Priority_Of_Service | T.Insider.Misuse.Res.1 T.Op.Denial.2 T.Op.Denial.11 A.Personnel_Untrusted A.Policy_MoA |
| O.Resource_Quotas | T.Admin.Policy.5 T.Insider.Misuse.Res.1 T.Network.Denial.1 T.Op.Denial.3 T.Op.Denial.5 T.Op.Denial.6 T.Op.Denial.7 T.Op.Denial.9 T.Op.Denial.10 T.Op.Denial.13 A.Personnel_Untrusted A.Policy_MoA |
| O.Rollback | T.Admin.Cred.1 T.Admin.Cred.2 T.Admin.Cred.3 T.Admin.Enroll.1 T.Admin.Enroll.2 T.Admin.Enroll.3 T.Admin.Enroll.4 T.Admin.Enroll.5 T.Admin.Enroll.6 T.Admin.Lockout.1 T.Admin.Lockout.2 T.Admin.Policy.2 T.Admin.Policy.3 T.Admin.Policy.4 T.Admin.Policy.5 T.Admin.Policy.6 T.Admin.Policy.8 T.Admin.Policy.9 T.Admin.Policy.10 T.Admin.Policy.11 T.Admin.Policy.12 T.Admin.Policy.13 T.Admin.Policy.14 T.Admin.Policy.17 T.Admin.PolicyImp.1 T.Admin.PolicyImp.2 T.Insider.Confusion.1 T.Insider.Confusion.3 A.Personnel_Untrusted A.Policy_MoA |
| O.SW_Download | T.Download.1 T.Download.2 T.Download.3 T.Download.4 T.Download.5 T.Flawed_Imp.Backdoor.1 T.Flawed_Imp.Developer.1 T.Flawed_Imp.Developer.2 T.Flawed_Imp.Developer.3 T.Initialize.Configuration.3 T.Initialize.Distribution.1 T.Initialize.Distribution.2 |
| O.Session_Protection | T.Admin.Cred.1 T.Admin.Enroll.5 T.Admin.Lockout.1 T.Admin.Lockout.2 T.Admin.Policy.1 T.Admin.Policy.4 T.Admin.Policy.8 T.Admin.PolicyImp.2 T.Eavesdrop.HMI.1 T.Eavesdrop.HMI.2 T.Eavesdrop.HMI.3 T.Op.Denial.1 T.Op.Denial.2 T.Op.Denial.3 T.Op.Denial.4 T.Op.Denial.5 T.Op.Denial.6 T.Op.Denial.7 T.Op.Denial.8 T.Op.Denial.9 T.Op.Denial.10 T.Op.Denial.11 T.Op.Denial.13 T.Op.Disclosure.1 T.Op.Disclosure.2 T.Op.Disclosure.3 T.Op.Disclosure.4 T.Op.Disclosure.5 T.Op.Disclosure.6 T.Op.Disclosure.9 T.Op.Disclosure.10 T.Op.Disclosure.11 T.Op.Disclosure.12 T.Op.Disclosure.14 |
| O.Session_Protection (cont.) | T.Op.Integrity.1 T.Op.Integrity.2 T.Op.Integrity.3 T.Op.Integrity.4 T.Op.Integrity.5 T.Op.Integrity.6 T.Op.Integrity.7 T.Op.Integrity.8 T.Op.Non-Repudiation.1 T.Op.Non-Repudiation.2 T.Op.Non-Repudiation.3 T.Op.Non-Repudiation.4 T.Op.Non-Repudiation.5 T.Op.Non-Repudiation.6 T.Trust.Impersonate.7 T.Trust.Info.1 T.Trust.Res.1 T.Trust.Serv.1 A.Personnel_Untrusted A.Policy_MoA |
| O.Secure_State | T.Physical.Capture.1 T.Physical.Capture.2 T.Physical.Denial.1 T.Physical.Destruction.Info.1 T.Physical.Destruction.Info.2 T.Physical.Destruction.Res.1 T.Physical.Destruction.Res.2 T.Physical.Destruction.Serv.1 T.Physical.Destruction.Serv.2 T.Physical.Destruction.Total.1 T.Physical.Destruction.Total.2 T.Physical.HWFailure.1 T.Physical.HWFailure.2 T.Physical.HWFailure.3 T.Physical.MechFailure.1 T.Physical.SWFailure.1 T.Physical.SWFailure.2 A.Environment A.Physical_Protection |
| O.Security_Mgt | T.Admin.Cred.1 T.Admin.Cred.2 T.Admin.Cred.3 T.Admin.Enroll.1 T.Admin.Enroll.2 T.Admin.Enroll.3 T.Admin.Enroll.4 T.Admin.Enroll.5 T.Admin.Enroll.6 T.Admin.Enroll.7 T.Admin.Lockout.1 T.Admin.Lockout.2 T.Admin.Policy.1 T.Admin.Policy.2 T.Admin.Policy.3 T.Admin.Policy.4 T.Admin.Policy.5 T.Admin.Policy.6 T.Admin.Policy.7 T.Admin.Policy.8 T.Admin.Policy.9 T.Admin.Policy.10 T.Admin.Policy.11 T.Admin.Policy.12 T.Admin.Policy.13 T.Admin.Policy.14 T.Admin.Policy.15 T.Admin.Policy.16 T.Admin.Policy.17 T.Admin.PolicyImp.1 T.Admin.PolicyImp.2 T.Eavesdrop.HMI.4 A.Personnel_Untrusted A.Policy_MoA |
| O.Security_Roles | T.Admin.Cred.1 T.Admin.Cred.2 T.Admin.Cred.3 T.Admin.Enroll.1 T.Admin.Enroll.2 T.Admin.Enroll.3 T.Admin.Enroll.4 T.Admin.Enroll.5 T.Admin.Enroll.6 T.Admin.Enroll.7 T.Admin.Lockout.1 T.Admin.Lockout.2 T.Admin.Policy.1 T.Admin.Policy.2 T.Admin.Policy.3 T.Admin.Policy.4 T.Admin.Policy.5 T.Admin.Policy.6 T.Admin.Policy.7 T.Admin.Policy.8 T.Admin.Policy.9 T.Admin.Policy.10 T.Admin.Policy.11 T.Admin.Policy.12 T.Admin.Policy.13 T.Admin.Policy.14 T.Admin.Policy.15 T.Admin.Policy.16 T.Admin.Policy.17 T.Admin.PolicyImp.1 T.Admin.PolicyImp.2 A.Personnel_Untrusted A.Policy_MoA |
| O.Sys_Assur_HW/SW/FW | T.Op.Disclosure.15 T.Physical.HWFailure.1 T.Physical.HWFailure.2 T.Physical.HWFailure.3 T.Physical.MechFailure.1 T.Physical.SWFailure.1 T.Physical.SWFailure.2 A.Personnel_Untrusted A.Policy_MoA |
| O.Tamper | T.Physical.Capture.1 T.Physical.Capture.2 T.Physical.Extract.IA.1 T.Physical.Extract.Res.1 T.Physical.Modification.Info.1 T.Physical.Modification.Input.1 T.Physical.Modification.Res.1 T.Physical.Modification.Res.2 A.Personnel_Untrusted A.Partial_Physical_Security A.Policy_MoA |
| O.Emanations | T.Op.Disclosure.8 T.Op.Disclosure.10 T.Physical.Extract.IA.2 T.Physical.Extract.NonAMI.1 T.Physical.Extract.Res.2 T.Physical.Extract.Res.3 |
| O.User_Attributes | T.InfoSys.Printer.1 T.Insider.Aggregation.1 T.Network.Unauth.1 T.Op.Denial.1 T.Op.Denial.2 T.Op.Denial.3 T.Op.Denial.4 T.Op.Denial.5 T.Op.Denial.6 T.Op.Denial.7 T.Op.Denial.8 T.Op.Denial.9 T.Op.Denial.10 T.Op.Denial.11 T.Op.Denial.12 T.Op.Denial.13 T.Op.Denial.14 T.Op.Denial.15 T.Op.Denial.16 T.Op.Disclosure.1 T.Op.Disclosure.2 T.Op.Disclosure.3 T.Op.Disclosure.4 T.Op.Disclosure.5 T.Op.Disclosure.6 T.Op.Disclosure.8 T.Op.Disclosure.9 T.Op.Disclosure.11 T.Op.Disclosure.12 T.Op.Disclosure.14 T.Op.Integrity.1 T.Op.Integrity.2 T.Op.Integrity.3 T.Op.Integrity.4 T.Op.Integrity.5 T.Op.Integrity.6 T.Op.Integrity.8 |
| O.User_Attributes (cont.) | T.Op.Non-Repudiation.1 T.Op.Non-Repudiation.2 T.Op.Non-Repudiation.3 T.Op.Non-Repudiation.4 T.Op.Non-Repudiation.5 T.Op.Non-Repudiation.6 T.Social_Eng.Info.1 A.Personnel_Untrusted A.Policy_MoA |
| O.Secure_via_Cryptography | T.Physical.ReverseEng.1 T.Physical.ReverseEng.2 T.Physical.ReverseEng.3 T.Physical.ReverseEng.4 |
| O.Malicious_Code | T.Flawed_Imp.Backdoor.1 T.Flawed_Imp.Developer.1 T.Flawed_Imp.Developer.2 T.Flawed_Imp.Developer.3 T.Initialize.Distribution.2 T.Malicious_Code.App.1 T.Malicious_Code.App.2 T.Malicious_Code.App.3 T.Malicious_Code.App.4 T.Malicious_Code.Info.1 T.Malicious_Code.Info.2 T.Malicious_Code.Info.3 T.Malicious_Code.Info.4 T.Malicious_Code.Info.5 T.Malicious_Code.Info.6 T.Malicious_Code.Info.7 T.Malicious_Code.Info.8 T.Malicious_Code.Proxy.1 T.Malicious_Code.Res.1 T.Malicious_Code.Res.2 T.Malicious_Code.Res.3 T.Malicious_Code.Res.4 T.Malicious_Code.Res.5 T.Malicious_Code.Res.6 T.Malicious_Code.Res.7 A.Personnel_Untrusted A.Policy_MoA |
| O.Comp_Attributes | T.Download.4 T.Eavesdrop.HMI.4 T.Op.Disclosure.15 A.Personnel_Untrusted A.Policy_MoA |
| O.Attr_based_Policy | T.Admin.Cred.1 T.Admin.Enroll.5 T.Admin.Lockout.1 T.Admin.Lockout.2 T.Admin.Policy.1 T.Admin.Policy.4 T.Admin.Policy.8 T.Admin.PolicyImp.2 T.Audit.4 T.Audit.5 T.Audit.6 T.Audit.7 T.Malicious_Code.App.1 T.Malicious_Code.App.2 T.Malicious_Code.App.3 T.Malicious_Code.App.4 T.Malicious_Code.Info.1 T.Malicious_Code.Info.2 T.Malicious_Code.Info.3 T.Malicious_Code.Info.4 T.Malicious_Code.Proxy.1 T.Malicious_Code.Res.1 T.Malicious_Code.Res.2 T.Malicious_Code.Res.3 T.Malicious_Code.Res.4 T.Op.Denial.1 T.Op.Denial.2 T.Op.Denial.3 T.Op.Denial.4 T.Op.Denial.5 T.Op.Denial.6 T.Op.Denial.7 T.Op.Denial.8 T.Op.Denial.9 |
| O.Attr_based_Policy (cont.) | T.Op.Denial.10 T.Op.Denial.11 T.Op.Denial.12 T.Op.Denial.13 T.Op.Denial.14 T.Op.Denial.15 T.Op.Denial.16 T.Op.Disclosure.1 T.Op.Disclosure.2 T.Op.Disclosure.3 T.Op.Disclosure.4 T.Op.Disclosure.5 T.Op.Disclosure.6 T.Op.Disclosure.8 T.Op.Disclosure.9 T.Op.Disclosure.11 T.Op.Disclosure.12 T.Op.Disclosure.14 T.Op.Integrity.1 T.Op.Integrity.2 T.Op.Integrity.3 T.Op.Integrity.4 T.Op.Integrity.5 T.Op.Integrity.6 T.Op.Integrity.8 T.Op.Non-Repudiation.1 T.Op.Non-Repudiation.2 T.Op.Non-Repudiation.3 T.Op.Non-Repudiation.4 T.Op.Non-Repudiation.5 T.Op.Non-Repudiation.6 A.Personnel_Untrusted A.Policy_MoA |

### Coverage of Objectives for the Environment

| Objectives | Threats / Policies / Assumptions |
| --- | --- |
| OE.Admin_Guidance | T.Audit.8 T.Audit.9 T.KeyMan.Deliver.1 T.KeyMan.Deliver.2 T.KeyMan.Deliver.3 T.KeyMan.Membership.1 T.KeyMan.Membership.2 T.KeyMan.Membership.3 T.KeyMan.Order.1 T.KeyMan.Order.2 T.KeyMan.Order.3 T.KeyMan.TrackControl.1 T.Network.Unauth.1 A.Audit_Analysis A.Clearance A.TOE_Design A.TOE_Maintenance A.TOE_Operation P.Accountability P.Audit_Review P.Cross_Domain_Filtering P.Due_Care P.Security_Admin_Restricted |
| OE.Config_Management | T.Op.Disclosure.15 A.Comms_Available A.Personnel_Untrusted A.Policy_MoA A.TOE_Design P.Due_Care |
| OE.Crypto_Key_Man | T.Crypto.Invalid_Keys.1 T.Crypto.Invalid_Keys.2 T.Crypto.Weak_Keys.1 T.KeyMan.Deliver.1 T.KeyMan.Deliver.2 T.KeyMan.Deliver.3 T.KeyMan.Deliver.4 T.KeyMan.Membership.3 T.KeyMan.Obsolescence.1 T.KeyMan.Order.1 T.KeyMan.Order.2 T.KeyMan.Order.3 T.KeyMan.TrackControl.1 T.Trust.Impersonate.2 A.KeyMat_Source A.Personnel_Untrusted A.Policy_MoA A.TOE_Design A.Trusted_Source P.Protect |
| OE.Secure_Configuration | T.Admin.Cred.1 T.Admin.Cred.2 T.Admin.Cred.3 T.Admin.Policy.2 T.Admin.Policy.3 T.Admin.Policy.4 T.Admin.Policy.5 T.Admin.Policy.6 T.Admin.Policy.8 T.Admin.Policy.9 T.Admin.Policy.10 T.Admin.Policy.11 T.Admin.Policy.12 T.Admin.Policy.13 T.Admin.Policy.14 T.Admin.Policy.15 T.Admin.Policy.16 T.Admin.Policy.17 T.Admin.PolicyImp.1 T.Admin.PolicyImp.2 T.Social_Eng.Access.2 T.Social_Eng.Access.3 T.Social_Eng.AdminLeak.1 A.Personnel_Untrusted A.Policy_MoA A.TOE_Design A.TOE_Maintenance A.TOE_Operation A.TOE_User A.Visual_Security |
| OE.Evaluated_System | T.Flawed_Imp.Backdoor.1 T.Flawed_Imp.Developer.1 T.Flawed_Imp.Developer.2 T.Flawed_Imp.Developer.3 T.InfoSys.1 T.InfoSys.Filter.1 T.Op.Disclosure.15 T.Social_Eng.AdminLeak.1 A.Personnel_Untrusted A.Policy_MoA A.TOE_Design |
| OE.Sys_Backup_Procs | T.Physical.Destruction.Info.1 T.Physical.Destruction.Info.2 A.Personnel_Untrusted A.Policy_MoA A.TOE_Design |
| OE.User_Auth_Management | T.Admin.Enroll.1 T.Admin.Enroll.2 T.Admin.Enroll.3 T.Admin.Enroll.4 T.Admin.Enroll.5 T.Admin.Enroll.6 T.Admin.Enroll.7 T.Admin.Lockout.1 T.Admin.Lockout.2 T.Admin.Policy.1 T.KeyMan.Membership.1 T.KeyMan.Membership.2 T.KeyMan.Membership.3 T.Social_Eng.Access.2 T.Social_Eng.Access.3 T.Social_Eng.Info.1 T.Social_Eng.Info.2 T.Social_Eng.Info.3 T.Social_Eng.Info.4 A.Personnel_Untrusted A.Policy_MoA A.TOE_Design A.TOE_User A.Trained |
| OE.User_Guidance | T.InfoSys.Printer.1 T.Network.Unauth.1 T.Op.Denial.1 T.Op.Denial.2 T.Op.Denial.8 T.Op.Denial.12 T.Op.Disclosure.3 T.Op.Disclosure.4 T.Op.Disclosure.5 T.Op.Disclosure.6 T.Op.Disclosure.7 T.Op.Disclosure.12 A.Printer_Security A.TOE_Design A.TOE_User A.Trained |
| OE.Component_Engineering | T.Physical.Obsolete.1 T.Physical.Obsolete.2 A.TOE_Design |
| OE.Admin_Available | T.Ident_Auth.3 T.Physical.Destruction.IA.1 T.Physical.Destruction.IA.2 A.TOE_Design |
| OE.Trusted_Facility | T.Initialize.Configuration.1 T.Initialize.Configuration.2 A.TOE_Design A.Trusted_Source |
| OE.Physical_Security | T.InfoSys.Printer.1 T.Insider.Misuse.Info.2 T.Eavesdrop.HMI.4 T.Social_Eng.Access.1 T.Social_Eng.Authorize.1 T.Social_Eng.Info.1 A.Personnel_Untrusted A.Physical_Protection A.Partial_Physical_Security A.Policy_MoA A.Printer_Security A.TOE_Design A.Visual_Security |
| OE.BackhaulSLA | A.TOE_Design A.TOE_Operation |
| OE.Enrollment_Process | T.Admin.Enroll.1 T.Admin.Enroll.2 T.Admin.Enroll.3 T.Admin.Enroll.4 T.Admin.Enroll.6 T.Admin.Enroll.7 |

Vulnerability Analysis Support

| Vulnerability Name | Description | Assets Impacted (eg meter) | Nature of the vulnerability (e.g. Proximity, access) | Cost | Complexity | Type of compromise | trust level required | Business Impact | Frequency | Severity | Consequences descripition | Rating (Low, Med, High) | Comments | Provided by (Your Name) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SPP-ICS Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| V.PLAINTEXT | Use of clear text protocols - The use of clear text protocols and the transmission of business and control data unencrypted over insecure communication channels (e.g. FTP, TELNET). |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| V.SERVICES | Unnecessary services enabled on system components - The presence of unnecessary system services on key AMI system components and subsystems that may be exploited to negatively impact on system security (e.g. sendmail, finger services). |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| V.REMOTE | Remote access vulnerabilities - Uncontrolled external access to the corporate network (e.g. through the Internet) allowing unauthorized entry to the interconnected AMI system network. Also includes vulnerabilities introduced through poor VPN configuration, exposed wireless access points, uncontrolled modem access (e.g. through networked faxes) and weak remote user authentication techniques. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| V.ARCHITECTURE | Poor system architecture designleading to weaknesses in system security posture - Business and operational requirements impacting on the effectiveness of deployed or planned security measures to protect the confidentiality, integrity and availability of the AMI system and its components. Poor security architecture may also lead to the bypass and tamper of AMI system security functions. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| V.DEVELOPMENT | Poor system development practices leading to weakness in system implementation - Lack of quality processes (e.g. configuration management, quality testing) leading to errors in system implementation and third party products such as buffer overflows and errors in control algorithms. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| V.NOPOLICIES | Inadequate system security policies, plans and procedures - Lack of formal system policies, plans and procedures (e.g. weak password policies, no incident response plans, irregular compliance audits, poor configuration management policies and procedures, poor system auditing practices, backup procedures etc). |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| V.SPOF | Single Points of Failure - Poor security architecture design leading to one or more single points of failure in the AMI system and resulting in system unavailability. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| V.NOTRAINING | Inadequate user training - Inadequate training on system security issues leading to poor user security awareness. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| V.3RDPARTY | Unauthorized access to AMI system via 3rd party network - Unauthorized user access to the AMI system or its components via a 3rd party network connection. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| V.NORISK | Lack of risk assessment - Inadequate risk assessment activities performed on critical assets leading to a poor understanding of the security posture of the AMI system and the security controls needed to counter security risks to the organization. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Policy and Procedure Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inadequate security policy for the AMI system | Vulnerabilities are often introduced into AMI system due to inadequate policies or the lack of policies specifically for control system security. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| No formal AMI system security training and awareness program | A documented formal security training and awareness program is designed to keep staff up to date on organizational security policies and procedures as well as industry cyber security standards and recommended practices. Without training on specific AMI system policies and procedures, staff cannot be expected to maintain a secure AMI system environment. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Inadequate security architecture and design | Control engineers have historically had minimal training in security and until relatively recently vendors have not included security features in their products |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| No specific or documented security procedures were developed from the security policy for the AMI system | Specific security procedures should be developed and employees trained for the AMI system. They are the roots of a sound security program. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Absent or deficient AMI system equipment implementation guidelines | Equipment implementation guidelines should be kept up to date and readily available. These guidelines are an integral part of security procedures in the event of an AMI system malfunction. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Lack of administrative mechanisms for security enforcement | Staff responsible for enforcing security should be held accountable for administering documented security policies and procedures. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Few or no security audits on the AMI system | Independent security audits should review and examine a system’s records and activities to determine the adequacy of system controls and ensure compliance with established AMI system security policy and procedures. Audits should also be used to detect breaches in AMI system security services and recommend changes as countermeasures which may include making existing security controls more robust and/or adding new security controls. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| No AMI system specific continuity of operations or disaster recovery plan (DRP) | A DRP should be prepared, tested and available in the event of a major hardware or software failure or destruction of facilities. Lack of a specific DRP for the AMI system could lead to extended downtimes and production loss. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Lack of AMI system specific configuration change management | A process for controlling modifications to hardware, firmware, software, and documentation should be implemented to ensure an AMI system is protected against inadequate or improper modifications before, during, and after system implementation. A lack of configuration change management procedures can lead to security oversights, exposures, and risks. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| OS and vendor software patches may not be developed until significantly after security vulnerabilities are found | Because of the complexity of AMI system software and possible modifications to the underlying OS, changes must undergo comprehensive regression testing. The elapsed time for such testing and subsequent distribution of updated software provides a long window of vulnerability |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Platform Configuration Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| OS and application security patches are not maintained | Out-of-date OSs and applications may contain newly discovered vulnerabilities that could be exploited. Documented procedures should be developed for how security patches will be maintained. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| OS and application security patches are implemented without exhaustive testing | OS and application security patches deployed without testing could compromise normal operation of the AMI system. Documented procedures should be developed for testing new security patches. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Default configurations are used | Using default configurations often leads to insecure and unnecessary open ports and exploitable services and applications running on hosts. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Critical configurations are not stored or backed up | Procedures should be available for restoring AMI system configuration settings in the event of accidental or adversary-initiated configuration changes to maintain system availability and prevent loss of data. Documented procedures should be developed for maintaining AMI system configuration settings. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Data unprotected on portable device | If sensitive data (e.g., passwords, dial-up numbers) is stored in the clear on portable devices such as laptops and PDAs and these devices are lost or stolen, system security could be compromised. Policy, procedures, and mechanisms are required for protection. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Lack of adequate password policy | Password policies are needed to define when passwords must be used, how strong they must be, and how they must be maintained. Without a password policy, systems might not have appropriate password controls, making unauthorized access to systems more likely. Password policies should be developed as part of an overall AMI system security program taking into account the capabilities of the AMI system to handle more complex passwords. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| No password used | Passwords should be implemented on AMI system components to prevent unauthorized access. Password-related vulnerabilities include having no password for: • System login (if the system has user accounts) • System power-on (if the system has no user accounts) • System screen saver (if an AMI system component is unattended over time) Password authentication should not hamper or interfere with emergency actions for AMI system. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Password disclosure | Passwords should be kept confidential to prevent unauthorized access. Examples of password disclosures include: • Posting passwords in plain sight, local to a system • Sharing passwords to individual user accounts with associates • Communicating passwords to adversaries through social engineering • Sending passwords that are not encrypted through unprotected communications |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Password guessing | Poorly chosen passwords can easily be guessed by humans or computer algorithms to gain unauthorized access. Examples include: • Passwords that are short, simple (e.g., all lower-case letters), or otherwise do not meet typical strength requirements. Password strength also depends on the specific AMI system capability to handle more stringent passwords • Passwords that are set to the default vendor supplied value • Passwords that are not changed on a specified interval |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Inadequate access controls applied | Poorly specified access controls can result in giving an AMI system user too many or too few privileges. The following exemplify each case: • System configured with default access control settings gives an operator administrative privileges • System improperly configured results in an operator being unable to take corrective actions in an emergency situation Access control policies should be developed as part of an AMI system security program. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Platform Hardware Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inadequate testing of security changes | Many AMI system facilities, especially smaller facilities, have no test facilities, so security changes must be implemented using the live operational systems |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Inadequate physical protection for critical systems | Access to the control center, field devices, portable devices, media, and other AMI system components needs to be controlled. Many remote sites are often not staffed and it may not be feasible to physically monitor them. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Unauthorized personnel have physical access to equipment | Physical access to AMI system equipment should be restricted to only the necessary personnel, taking into account safety requirements, such as emergency shutdown or restarts. Improper access to AMI system equipment can lead to any of the following: • Physical theft of data and hardware • Physical damage or destruction of data and hardware • Unauthorized changes to the functional environment (e.g., data connections, unauthorized use of removable media, adding/removing resources) • Disconnection of physical data links • Undetectable interception of data (keystroke and other input logging) |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Insecure remote access on AMI system components | Modems and other remote access capabilities that enable control engineers and vendors to gain remote access to systems should be deployed with security controls to prevent unauthorized individuals from gaining access to the AMI system. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Dual network interface cards (NIC) to connect networks | Machines with dual NAMI system connected to different networks could allow unauthorized access and passing of data from one network to another. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Undocumented assets | To properly secure an AMI system, there should be an accurate listing of the assets in the system. An inaccurate representation of the control system and its components could leave an unauthorized access point or backdoor into the AMI system. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Radio frequency and electro-magnetic pulse (EMP) | The hardware used for control systems is vulnerable to radio frequency electro-magnetic pulses (EMP). The impact can range from temporary disruption of command and control to permanent damage to circuit boards. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Lack of backup power | Without backup power to critical assets, a general loss of power will shut down the AMI system and could create an unsafe situation. Loss of power could also lead to insecure default settings. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Loss of environmental control | Loss of environmental control could lead to processors overheating. Some processors will shut down to protect themselves; some may continue to operate but in a minimal capacity, producing intermittent errors; and some just melt if they overheat. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Lack of redundancy for critical components | Lack of redundancy in critical components could provide single point of failure possibilities |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Platform Software Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Buffer overflow | Software used to implement an AMI system could be vulnerable to buffer overflows; adversaries could exploit these to perform various attacks. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Installed security capabilities not enabled by default | Security capabilities that were installed with the product are useless if they are not enabled or at least identified as being disabled. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Denial of service (DoS) | AMI system software could be vulnerable to DoS attacks, resulting in the prevention of authorized access to a system resource or delaying system operations and functions. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Mishandling of undefined, poorly defined, or “illegal” conditions | Some AMI system implementations are vulnerable to packets that are malformed or contain illegal or otherwise unexpected field values. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| OLE for Process Control (OPC) relies on Remote Procedure Call (RPC) and Distributed Component Object Model (DCOM) | Without updated patches, OPC is vulnerable to the known RPC/DCOM vulnerabilities. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Use of insecure industry-wide AMI system protocols | Distributed Network Protocol (DNP) 3.0, Modbus, Profibus, and other protocols are common across several industries and protocol information is freely available. These protocols often have few or no security capabilities built in. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Use of clear text | Many AMI system protocols transmit messages in clear text across the transmission media, making them susceptible to eavesdropping by adversaries. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Unneeded services running | Many platforms have a wide variety of processor and network services defined to operate as a default. Unneeded services are seldom disabled and could be exploited. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Use of proprietary software that has been discussed at conferences and in periodicals | Proprietary software issues are discussed at international IT, AMI system and “Black Hat” conferences and available through technical papers, periodicals and listservers. Also, AMI system maintenance manuals are available from the vendors. This information can help adversaries create successful attacks against AMI system. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Inadequate authentication and access control for configuration and programming software | Unauthorized access to configuration and programming software could provide the ability to corrupt a device. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Intrusion detection/prevention software not installed | Incidents can result in loss of system availability; the capture, modification, and deletion of data; and incorrect execution of control commands. IDS/IPS software may stop or prevent various types of attacks, including DoS attacks, and also identify attacked internal hosts, such as those infected with worms. IDS/IPS software must be tested prior to deployment to determine that it does not compromise normal operation of the AMI system. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Logs not maintained | Without proper and accurate logs, it might be impossible to determine what caused a security event to occur. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Incidents are not detected | Where logs and other security sensors are installed, they may not be monitored on a real-time basis and therefore security incidents may not be rapidly detected and countered. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Platform Malware Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Malware protection software not installed | Malicious software can result in performance degradation, loss of system availability, and the capture, modification, or deletion of data. Malware protection software, such as antivirus software, is needed to prevent systems from being infected by malicious software. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Malware protection software or definitions not current | Outdated malware protection software and definitions leave the system open to new malware threats. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Malware protection software implemented without exhaustive testing | Malware protection software deployed without testing could impact normal operation of the AMI system. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Network Configuration Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Weak network security architecture | The network infrastructure environment within the AMI system has often been developed and modified based on business and operational requirements, with little consideration for the potential security impacts of the changes. Over time, security gaps may have been inadvertently introduced within particular portions of the infrastructure. Without remediation, these gaps may represent backdoors into the AMI system. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Data flow controls not employed | Data flow controls, such as access control lists (ACL), are needed to restrict which systems can directly access network devices. Generally, only designated network administrators should be able to access such devices directly. Data flow controls should ensure that other systems cannot directly access the devices. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Poorly configured security equipment | Using default configurations often leads to insecure and unnecessary open ports and exploitable network services running on hosts. Improperly configured firewall rules and router ACLs can allow unnecessary traffic. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Network device configurations not stored or backed up | Procedures should be available for restoring network device configuration settings in the event of accidental or adversary-initiated configuration changes to maintain system availability and prevent loss of data. Documented procedures should be developed for maintaining network device configuration settings. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Passwords are not encrypted in transit | Passwords transmitted in clear text across transmission media are susceptible to eavesdropping by adversaries, who could reuse them to gain unauthorized access to a network device. Such access could allow an adversary to disrupt AMI system operations or to monitor AMI system network activity. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Passwords exist indefinitely on network devices | Passwords should be changed regularly so that if one becomes known by an unauthorized party, the party has unauthorized access to the network device only for a short time. Such access could allow an adversary to disrupt AMI system operations or monitor AMI system network activity. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Inadequate access controls applied | Unauthorized access to network devices and administrative functions could allow a user to disrupt AMI system operations or monitor AMI system network activity. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Network Hardware Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inadequate physical protection of network equipment | Access to network equipment should be controlled to prevent damage or destruction. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Unsecured physical ports | Unsecured universal serial bus (USB) and PS/2 ports could allow unauthorized connection of thumb drives, keystroke loggers, etc. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Loss of environmental control | Loss of environmental control could lead to processors overheating. Some processors will shut down to protect themselves, and some just melt if they overheat. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Non-critical personnel have access to equipment and network connections | Physical access to network equipment should be restricted to only the necessary personnel. Improper access to network equipment can lead to any of the following: • Physical theft of data and hardware • Physical damage or destruction of data and hardware • Unauthorized changes to the security environment (e.g., altering ACLs to permit attacks to enter a network) • Unauthorized interception and manipulation of network activity • Disconnection of physical data links or connection of unauthorized data links |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Lack of redundancy for critical networks | Lack of redundancy in critical networks could provide single point of failure possibilities |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Network Perimeter Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| No security perimeter defined | If the control network does not have a security perimeter clearly defined, then it is not possible to ensure that the necessary security controls are deployed and configured properly. This can lead to unauthorized access to systems and data, as well as other problems. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Firewalls nonexistent or improperly configured | A lack of properly configured firewalls could permit unnecessary data to pass between networks, such as control and corporate networks. This could cause several problems, including allowing attacks and malware to spread between networks, making sensitive data susceptible to monitoring/eavesdropping on the other network, and providing individuals with unauthorized access to systems. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Control networks used for non-control traffic | Control and non-control traffic have different requirements, such as determinism and reliability, so having both types of traffic on a single network makes it more difficult to configure the network so that it meets the requirements of the control traffic. For example, non-control traffic could inadvertently consume resources that control traffic needs, causing disruptions in AMI system functions. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Control network services not within the control network | Where IT services such as Domain Name System (DNS),and/or Dynamic Host Configuration Protocol (DHCP) are used by control networks, they are often implemented in the IT network, causing the AMI system network to become dependent on the IT network that may not have the reliability and availability requirements needed by the AMI system. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Network Monitoring and Logging Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inadequate firewall and router logs | Without proper and accurate logs, it might be impossible to determine what caused a security incident to occur. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| No security monitoring on the AMI system network | Without regular security monitoring, incidents might go unnoticed, leading to additional damage and/or disruption. Regular security monitoring is also needed to identify problems with security controls, such as misconfigurations and failures. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Communications Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Critical monitoring and control paths are not identified | Rogue and/or unknown connections into the AMI system can leave a backdoor for attacks. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Standard, well-documented communication protocols are used in plain text | Adversaries that can monitor the AMI system network activity can use a protocol analyzer or other utilities to decode the data transferred by protocols such as telnet, File Transfer Protocol (FTP), and Network File System (NFS). The use of such protocols also makes it easier for adversaries to perform attacks against the AMI system and manipulate AMI system network activity. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Authentication of users, data or devices is substandard or nonexistent | Many AMI system protocols have no authentication at any level. Without authentication, there is the potential to replay, modify, or spoof data or to spoof devices such as sensors and user identities. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Lack of integrity checking for communications | There are no integrity checks built into most industrial control protocols; adversaries could manipulate communications undetected. To ensure integrity, the AMI system can use lower-layer protocols (e.g., IPsec) that offer data integrity protection. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Wireless Connection Vulnerabilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inadequate authentication between clients and access points | Strong mutual authentication between wireless clients and access points is needed to ensure that clients do not connect to a rogue access point deployed by an adversary, and also to ensure that adversaries do not connect to any of the AMI system’s wireless networks. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |
| Inadequate data protection between clients and access points | Sensitive data between wireless clients and access points should be protected using strong encryption to ensure that adversaries cannot gain unauthorized access to the unencrypted data. |  |  |  |  |  |  |  |  |  |  |  |  | Neil Greenfield |

# Comments

Definition taken from EPRI IECSA Architecture Volume IV Appendix A

Ref. SSE-CMM v3 – Prioritize Capabilities section p.127

Missing Authentication, and Authorization. Most of the disclosure and usurpation attacks are based on compromising either or both of A&A.

Non repudiation is generally considered part of Integrity and only called out separately as a highlight or refinement of integrity protections. (Generally a combination of authentication and integrity)

In general, incomplete – especially when considering the funding aspect. Any or all of these can be compromised (e.g. subverted into being an ageng of a third party) by a third party with substantial resources.

Some additional roles – each of these has a unique motivation and generally will focus on specific things of interest within the system.

Contract Insider – An insider with a limited relationship to the AMS, authorized to do certain limited tasks, but able to use that access to do other unauthorized activities

Outsider (Retail Attacks) – An outsider whose primary interest relates to attacks that affect a small number (e.g. approximately 1) of customers

Outsider (Wholesale Attacks) – An outsider whose primary interest relates to attacks that affect a broad number (e.g. neighborhood, substation branch, system) of customers generally for the purposes of disruption, or subversion of the system for other purposes.

Outsider (National) – An outsider whose primary interests are related to its national security and who may consider the use of attacks on the AMI grid as legitimate means for advancing its interests.

Customer (Wholesale) – A customer who has customers to which it distributes energy and may or may not have a subsidiary AMI relationship with.

This type of matrix needs to be generated from the specific threat analysis; it is meaningless and inaccurate in its current form…

Why not?  The system should provide mechanism to fail safe inadvertent actions that can have catastrophic effects…

Brute force is an exploit not a threat. The threat is compromise of the credential

Exploit. Threat is Intrusion or data insertion.

Exploit. Threat is subversion of the system. [This one is hard – malware is a vector for getting control of the system – its not so much deploying the malware as the AMS being convinced to run or install it.]

Exploit. Threat is to confidentiality, integrity or subverting the system

Exploit. Threat is too generic here – it feeds into mechanisms to use other exploits to subvert the system, read data, or analyze the control structures for points of weakness.

Exploit.

Yes, if one requires strong authentication to join the AMI network…

Is this just a form of failed authentication?

Is this just a form of failed authentication?

Hmmm…  On a published API, what is your point here???

See comment above; I don’t get the threat???

Add in “Personnel – use of untrusted or unvetted operators, installers, or administrators”

This is a good asset description but the following list needs better clarification and details added.

What does this refer to? Security tokens?

Assume these refer to Security Keys?

Is the is the service interface on the device?

What do you mean by “the system”?  Malicious code is not “part of the system”, it is code that has been injected into the system…

What is missing from this discussion is the likelihood of the attack based on cost (e.g., if the cost to implement is low, then the likelihood of occurrence is high)…

Depending upon the key management scheme used; the keys may be dynamically generated by each of the mutually authenticated device/system – e.g., by the Meter and the AAA server…

This would only be relevant if one stored it in the meter – which would be “brain dead”; not to mention a very weak security model;

I hope this does not refer to the current proposals floating around to use the C12.19 Application passwords as cryptographic key material, or as network identity credentials…

The first item would be bad practice; the second item is not a threat if the field tool has authenticated / authorized access to the device…

The exact reason one should use ephemeral cryptographic keys, that are generated by a method that protects against this type of attack…

The above examples are not even close to being a advanced metering infrastructure threat matrix; and they should not be presented as such…

What Common Criteria do these refer to?  The nomenclature does not appear to map to ISO/IEC 15408 Common Criteria for Information Technology Security Evaluation, which is the common security industry reference when referring to the phrase “Common Criteria”. Link: http://www.commoncriteriaportal.org/index.php

Entity appears to have a greater meaning than an atomic unit of data

How were the Severity & Likelihood values determined, and by whom?

I don’t believe we can accept them at “face value”

T.Admin.Enroll.2-.5 are the same as revised T.Admin.Enroll.1

How is this a threat scenario?

Items T.Admin.Policy.1-.3 are the same as revised T.Admin.Enroll.1

This may be out of scope if the “other system” is not part of the AMI System…

same as revised T.Admin.Enroll.1

what is an organizational policy?

Presupposes a particular system design

Presupposes a particular system design

Presupposes a particular system design

Presupposes a particular system design

# Text boxes

Figure 1 - Risk Assessment Element Mapping