| Summary of Comments on the Security Profile for Advanced Metering Infrastructure |  |
| --- | --- |
|  | Prepared for: The UtiliSec Working Group (UCAIug) |  |
|  | Prepared by: |  |
|  | Managed by: 620 Mabry Hood Road Knoxville, TN 37923 USA (865) 218-4600 www.enernex.com |  |
|  | November 3, 2009 |

Table of Contents

1	Introduction	1

2	Control Additions/Removals in Version 0.49	2

2.1	Removed Controls	2

2.2	Added Controls	3

3	Comments Not Addressed in Version 0.49	4

3.1	General Document Comments	4

3.2	Control Specific Comments	6

DHS-2.8 System and Communication Protection	6

DHS-2.8.2 Management Port Partitioning	6

DHS-2.8.3 Security Function Isolation	7

DHS-2.8.4 Information Remnants	8

DHS-2.8.5 Denial-of-Service Protection	8

DHS-2.8.6 Resource Priority	8

DHS-2.8.7 Boundary Protection	8

DHS-2.8.8 Communication Integrity	9

DHS-2.8.9 Communication Confidentiality	9

DHS-2.8.10 Trusted Path	9

DHS-2.8.11 Cryptographic Key Establishment and Management	10

DHS-2.8.12 Use of Validated Cryptography	10

DHS-2.8.13 Collaborative Computing N/A	11

DHS-2.8.14 Transmission of Security Parameters	11

DHS-2.8.15 Public Key Infrastructure Certificates	11

DHS-2.8.16 Mobile Code	11

DHS-2.8.17 Voice-Over Internet Protocol	11

DHS-2.8.18 System Connections	12

DHS-2.8.19 Security Roles	12

DHS-2.8.20 Message Authenticity	12

DHS-2.8.21 Architecture and Provisioning for Name/Address Resolution Service	12

DHS-2.8.22 Secure Name / Address Resolution Service (Authoritative Source)	13

DHS-2.8.23 Secure Name/Address Resolution Service (Recursive or Caching Resolver)	13

ASAP-2.8.24 Secure Name/Address Resolution Service (Address Resolution Tampering)	13

DHS-2.9 Information and Document Management	13

DHS-2.9.4 Information Classification	13

DHS-2.9.5 Information Exchange	14

DHS-2.9.7 Information and Document Retrieval	14

DHS-2.9.8 Information and Document Destruction	14

DHS-2.9.9 Information and Document Management Review	15

DHS-2.9.10 Automated Marking	15

DHS-2.10 System Development and Maintenance	15

DHS-2.10.1 System Maintenance Policy and Procedures	15

DHS-2.10.2 Legacy System Upgrades	15

DHS-2.10.3 System Monitoring and Evaluation	16

DHS-2.10.4 Backup and Recovery	16

DHS-2.10.6 Periodic System Maintenance	16

ASAP-2.10.7 Field Tools	17

DHS-2.10.8 Maintenance Personnel	17

DHS-2.10.9 Remote Maintenance	17

DHS-2.12 Incident Response	18

DHS-2.12.1 Incident Response Policy and Procedures	18

DHS-2.12.2 Continuity of Operations Plan	18

DHS-2.12.4 Incident Response Training	18

DHS-2.12.5 Continuity of Operations Plan Testing	19

DHS-2.12.6 Continuity of Operations Plan Update	19

DHS-2.14 System and Information Integrity	19

DHS-2.14.1 System and Information Integrity Policy and Procedures	19

DHS-2.14.2 Flaw Remediation	20

DHS-2.14.3 Malicious Code Protection	20

DHS-2.14.4 System Monitoring Tools and Techniques	21

DHS-2.14.5 Security Alerts and Advisories	22

DHS-2.14.6 Security Functionality Verification	22

DHS-2.14.7 Software and Information Integrity	23

DHS-2.14.8 Spam Protection	23

DHS-2.14.10 Information Input Accuracy, Completeness, Validity, and Authenticity	24

DHS-2.14.11 Error Handling	24

DHS-2.15 Access Control	25

DHS-2.15.1Access Control Policy and Procedures	25

DHS-2.15.2 Identification and Authentication Policy and Procedures	25

DHS-2.15.3 Account Management	26

DHS-2.15.4 Identifier Management	27

DHS-2.15.5 Authenticator Management	27

DHS-2.15.6 Supervision and Review	27

DHS-2.15.7 Access Enforcement	28

DHS-2.15.8 Separation of Duties	29

DHS-2.15.9 Least Privilege	29

DHS-2.15.10 User Identification and Authentication	29

DHS-2.15.11 Permitted Actions without Identification or Authentication	30

DHS-2.15.12 Device Identification and Authentication	30

DHS-2.15.13 Authenticator Feedback	30

DHS-2.15.14 Cryptographic Module Authentication	31

DHS-2.15.15 Information Flow Enforcement	31

DHS-2.15.16 Passwords	31

DHS-2.15.17 System Use Notification	31

DHS-2.15.19 Previous Logon Notification	32

DHS-2.15.20 Unsuccessful Login Attempts	32

DHS-2.15.22 Remote Session Termination	32

DHS-2.15.24 Remote Access	32

DHS-2.15.25 Access Control for Portable and Mobile Devices	33

DHS-2.15.26 Wireless Access Restrictions	33

DHS-2.15.27 Personally Owned Information	33

DHS-2.15.28 External Access Protections	33

DHS-2.15.29 Use of External Information Control Systems	34

ASAP-2.15.30 Unauthorized Access Reporting	34

DHS-2.16 Audit and Accountability	34

DHS-2.16.2 Auditable Events	34

DHS-2.16.3 Content of Audit Records	35

DHS-2.16.4 Audit Storage Capacity	36

DHS-2.16.5 Response to Audit Processing Failures	36

DHS-2.16.7 Audit Reduction and Report Generation	36

DHS-2.16.8 Time Stamps	36

ASAP-2.16.13 Audit Tools	37

# Introduction

This document serves as a collection point for all comments received from review of the AMI Security Profile, version 0.46 and is intended to be a companion document to the AMI Security Profile, version 0.49. These comments have been received from several sources, particularly including Cisco and the NIST CSCTG. Additionally, some comments have also been included from the ASAP-SG Architectural Team. The ASAP-SG Usability Analysis Team has also provided a summary of findings, which may be found in a separate document titled “Usability Analysis Team Preliminary Results Oct 1 2009.”

# Control Additions/Removals in Version 0.49

## Removed Controls

The following controls which were part of the AMI Security Profile, version 0.46 have been removed in version 0.49. These controls were determined to be organizational related which will be dealt with separately from the AMI Security Profile.

DHS-2.12.6 Continuity of Operations Plan Update

DHS-2.12.7 Incident Handling

DHS-2.12.8 Incident Monitoring

DHS-2.12.9 Incident Reporting

DHS-2.12.10 Incident Response Assistance

DHS-2.12.11 Incident Response Investigation and Analysis

DHS-2.12.12 Corrective Action

DHS-2.12.13 Alternate Data Storage Sites

DHS-2.12.14 Alternate Command/Control Methods

DHS-2.12.15 Alternate Control Center

ASAP-2.12.16 Business Data Backup

DHS-2.12.17 Control System Recovery and Reconstitution

DHS-2.12.18 Fail-Safe Response

ASAP-2.15.31 Unauthorized Access

DHS-2.15.23 Remote Access Policy and Procedures

DHS-2.16.1 Audit and Accountability Policy and Procedures

DHS-2.16.6 Audit Monitoring, Analysis, and Reporting

DHS-2.16.10 Audit Record Retention

DHS-2.16.11 Conduct and Frequency of Audits

DHS-2.16.14 Security Policy Compliance

## Added Controls

The following controls which were not part of the AMI Security Profile, version 0.46 have been added in version 0.49.

ASAP-2.17.1 Delay of Remote Connect/Disconnect

# Comments Not Addressed in Version 0.49

## General Document Comments

- The early sections of the document discuss a reasonable AMI architecture and component interfaces.  Subsequent sections discuss various security mechanisms.  What is missing are the associations between the two.

- Security mechanisms are discussed in isolation, and not tied back to specific interfaces and components in the AMI network.   The high level AMI architecture is discussed. The low level security mechanisms are discussed.  There is little discussion re: which mechanisms should be applied, where, and under what conditions.

- There is a tendency to designate various protocols as not suitable for an AMI network. Little justification is provided. For example:

  - DHS-2.8.21.2 Do not use DNS.  The document makes several contradictory statements re: DNS.

  - DHS-2.8.16.2 HTTP Web interface should not be used for configuration and management of AMI aggregator.

  - DHS-2.8.13 States that voice, video, IM cannot be secured.

The ability to securely deploy any of the above services is dependent upon the specifics of the deployed AMI network.  The decision to deploy or not should be left entirely up to the AMI provider.  When deployed, appropriate security mechanisms should be applied.

- Normative language.

  - Document could be worded much more specifically if standard normative terms are used.  Recommend using RFC 2119 or similar.

  - Section 5 normative structure is not clear.  One would expect normative requirements to be explicitly listed under the Requirements and Requirements Enhancements sub headings.  One would also expect informal, non-normative, clarifying descriptions in the Supplemental Guidance sub heading.  Yet there seems to be normative text within the Supplemental Guidance sections (example: DHS 2.18.12.2) which is not reflected in the requirements sections.  Recommendation is that all normative text be placed in requirements sections only.

- Section 4 makes many technical references to section 2.x.  These references do not exist.

- Figure 2: it is not clear why there are two alternate paths between AMI meter and AMI head end.  Should not all the communication be passing through the AMI communication network device? If the intent is to depict Internet as a path via the HAN, this should be made explicit (but later text makes it clear that HAN should not be commanding the meter).

  - Same issues for 3rd party meter and non electric meter.  They are depicted as communicating directly with the AMI head end, bypassing the AMI communication device.

- Table 1.  There seems an assumption that meter reading will be polled.  This will not be the general case (text explicitly discusses request/response).

- 4.2 end of section.  Unless there is a compelling reason to do otherwise, combine the AMI meter management system and AMI network management system.

- Section 4.3.  Controls discussed in later sections of the document are not associated with interfaces or components discussed here.  For example, the term HAN is used extensively in the controls section but is not listed as a component or domain.

- Section 4.3.7 - DRAACS will also need the ability to collect shed-able load from the premises.

- Section 4.4 - The security domain concepts discussed here are barely used within section 5.  When used, they are used in a confusing manner.  For example, “enterprise domain” is variously referred to enterprise network, enterprise system enterprise, business system, etc.  “Automated network” is mentioned once.  “Managed network” not at all.

- Section 4.4 - Second paragraph on page 19.  Reference to section 3 makes no sense.

- Section 4 seems a non sequitur to the rest of the document. Section 5 content needs to be mapped back to the security domains, or remove section 4.4 for clarity.

- Section 5. Terminology is frequently undefined.  Vague wording within an “actionable” specification will lead to confusion down the road.  Are these terms defined in the DHS documents or elsewhere?  If so, sources need to be cited.

Examples … trusted path, trusted base computing, mobile code, flaw, etc.

## Control Specific Comments

### DHS-2.8 System and Communication Protection

Comments:

- I am not clear about the definition of AMI component.  I make comments throughout on this because I am not sure components have the capability to implement many of the controls.  I typically think of a component as a device.

#### DHS-2.8.2 Management Port Partitioning

###### DHS-2.8.2.1 Requirement:

Comments:

- Is the reference to “AMI Components” in the first sentence appropriate?  See comment #1 in Section 2.8.

- Move the following text from Supplemental Guidance to Requirements sections “The AMI system management port needs to be physically or logically separated from telemetry/data acquisition services and information storage and management services (e.g., database management) of the system.”

###### DHS-2.8.2.2 Supplemental Guidance:

Comments:

- Move text as per comment #2 in 2.8.2.1.

- Add new text to end of this section as follows: “Such precautions reduce the risk of allowing access to a data acquisition server and can help limit the damage of a compromised system. Configuration and testing ports for AMI components should be disabled when not in use. 
Depending on the criticality of the system it may be advised that a device be physically disconnected. “

- "different network addresses or protocol port (e.g., TCP ports)" - That doesn't seem like much of a separation if they are both on the same host, but seem acceptable if they are on multiple hosts. For example if mail and web running on one server, compromise one and you can probably compromise the other.  Perhaps a better or extra addition would be different user permissions on the system per application so if one is compromised (and it's not root/admin) it forces the attacker to also escalate privs. To (fully) compromise the other services on the box.

#### DHS-2.8.3 Security Function Isolation

###### DHS-2.8.3.1 Requirement:

Comments:

- Is the reference to “AMI Components” in the first sentence appropriate?  See comment #1 in Section 2.8.

- Is FIPS compliance sufficient to meet this or is there something more?

###### DHS-2.8.3.2 Supplemental Guidance:

Comments:

- Change the beginning of the first sentence in this section from “AMI components must isolate” to “AMI components shall isolate”

- Change the beginning of the second sentence in this section from “The AMI system maintains” to “The AMI system shall maintain”

- How do we want to handle the last sentence of the first paragraph if organizational controls are not part of the AMI Security Profile? “Some AMI components may not implement this capability. In situations where it is not implemented, the organization details its risk acceptance and mitigation in the AMI system security plan

- Move the last paragraph and list of five items to Requirements Enhancements (DHS-2.8.3.3)

###### DHS-2.8.3.3 Requirement Enhancements:

Comments:

- Move text from Supplemental Guidance (See comment #4 in Section DHS-2.8.3.2)

- Change first sentence from “The AMI system must employ” to “The AMI system shall employ”

#### DHS-2.8.4 Information Remnants

###### DHS-2.8.4.1 Requirement:

Comments:

- Underline the word “components” in the first sentence.

- Is FIPS compliance sufficient to meet this or is there something more?

#### DHS-2.8.5 Denial-of-Service Protection

###### DHS-2.8.5.1 Requirement:

Comments:

- Underline the word “components” in the first sentence.

###### DHS-2.8.5.2 Supplemental Guidance:

Comments:

- The three items in the list are requirements. Move to Requirements Enhancements section (DHS 2.8.5.3)

#### DHS-2.8.6 Resource Priority

###### DHS-2.8.6.1 Requirement:

Comments:

- Underline the word “components” in the first sentence.

#### DHS-2.8.7 Boundary Protection

###### DHS-2.8.7.1 Requirement:

Comments:

- Do boundaries align at all with domains from section 4?  The HAN is most likely connected to the internet.  What does it mean to push data to the HAN?  Is it just transit?  Or can AMI data be interpreted by other components in the HAN?  If other components in the HAN want to interact with the AMI system how do they do it?

- I found this description of the requirement to be somewhat confusing.  This is really about establishing boundaries on trust.

###### DHS-2.8.7.2 Supplemental Guidance:

Comments:

- The items in the list that begins with “The following guidance also applies:” are requirements. Move to the Requirements Enhancements section (DHS-2.8.7.3)

###### DHS-2.8.7.3 Requirement Enhancements:

Comments:

- Move list of items from Supplemental Guidance section (see comment #2 under DHS-2.8.7.2)

#### DHS-2.8.8 Communication Integrity

###### DHS-2.8.8.1 Requirement:

Comments:

- Change “must” to “shall” in the first sentence of this section.

- How is communication integrity different than authentication when cryptographic protection is applied?  What interfaces require integrity?  Is a definition for the various levels of data sensitivity provided for the AMI system?

###### DHS-2.8.8.3 Requirement Enhancements:

Comments:

- #3 "must not create a denial of service of rail to an unprotected open state" - This seems to contradict (maybe in wording alone) the "availability" mentioned later in that paragraph.  It seems if it doesn't fail in open state it would fail to a closed state and not work.  However, I see the argument that it shouldn't be unprotected, perhaps there should be a note that the implementer should take into account the criticality of the system.

#### DHS-2.8.9 Communication Confidentiality

###### DHS-2.8.9.1 Requirement:

Comments:

- Shouldn’t confidentiality have similar concerns as integrity with respect to data sensitivity etc?

#### DHS-2.8.10 Trusted Path

###### DHS-2.8.10.1 Requirement:

Comments:

- Underline the word “components” in the first sentence.

###### DHS-2.8.10.2 Supplemental Guidance:

Comments:

- This section needs to be rewritten both here and in the DHS Catalog.  The terminology is old (from the orange book) and referencing clearances is really not appropriate.

#### DHS-2.8.11 Cryptographic Key Establishment and Management

###### DHS-2.8.11.1 Requirement:

Comments:

- This control is somewhat bothersome to me. Requiring automation has more to do with usability than security. I think the purpose is really to ensure that key establishment and management is protected. An encryption scheme only provides as much protection as is afforded to its components.

###### DHS-2.8.11.2 Supplemental Guidance:

Comments:

- Reference to an “effective” random number generator. Where is [effective] defined?

#### DHS-2.8.12 Use of Validated Cryptography

###### DHS-2.8.12.1 Requirement:

Comments:

- This one is a borderline organizational issue.

###### DHS-2.8.12.2 Supplemental Guidance:

Comments:

- Meeting the FIPS 140-2 standards is not the same as being validated. Recommend changing this to being “validated”.

- Is FIPS 140 required or just recommended?  Is certification required?

###### DHS-2.8.12.3 Requirement Enhancements:

Comments:

- I don’t understand this requirement. This is in reference to requirement #2 in this section which states: “The organization selects cryptographic hardware with remote key management capabilities”.

#### DHS-2.8.13 Collaborative Computing N/A

###### DHS-2.8.13.1 Requirement:

Comments:

- The intent of the collaborative computing section is not clear.  For starters, it states that voice, video, IM cannot be secured, etc.  The wholesale banning of a particular technology seems draconian.  If the technology supports appropriate controls it should be permitted.  If additional controls are necessary then they should be enumerated.

#### DHS-2.8.14 Transmission of Security Parameters

###### DHS-2.8.14.2 Supplemental Guidance:

Comments:

- I am not clear what “explicitly” or “implicitly” means.

#### DHS-2.8.15 Public Key Infrastructure Certificates

###### DHS-2.8.15.1 Requirement:

Comments:

- Does registration authorization need to be a manual process?

- Not sure how to define appropriate here.

#### DHS-2.8.16 Mobile Code

###### DHS-2.8.16.1 Requirement:

Comments:

- Not clear what point is being made. When is code considered mobile or not?  What’s the spectrum versus an executable image run directly on the HW or interpreted at a higher level? Signed images/code eliminates the security concerns. Also states that HTTP interfaces should not be used for configuration or management.

###### DHS-2.8.16.2 Supplemental Guidance:

Comments:

- The url referenced is not valid.

#### DHS-2.8.17 Voice-Over Internet Protocol

###### DHS-2.8.17.1 Requirement:

Comments:

- The last sentence (starting with “Given the current state of this technology”) of this section is not a requirement.

- There are security mechanisms for VOIP.  If it can be secured using the controls in this document then why not permit its use?  If additional controls are necessary then they should be defined.

#### DHS-2.8.18 System Connections

###### DHS-2.8.18.1 Requirement:

Comments:

- Underline the word “components” in the first sentence.

#### DHS-2.8.19 Security Roles

###### DHS-2.8.19.2 Supplemental Guidance:

Comments:

- This doesn’t make sense to me.  Shouldn’t roles be defined for job descriptions and/or individuals?

#### DHS-2.8.20 Message Authenticity

###### DHS-2.8.20.1 Requirement:

Comments:

- Device-to-device communication? When is communication considered not device to device? Also, what specifically is meant by “at the protocol level” and why is it singled out?

###### DHS-2.8.20.3 Requirement Enhancements:

Comments:

- I am not clear on this requirement.

#### DHS-2.8.21 Architecture and Provisioning for Name/Address Resolution Service

###### DHS-2.8.21.1 Requirement:

Comments:

- Should “AMI components” be “AMI devices”?

###### DHS-2.8.21.2 Supplemental Guidance:

Comments:

- This section needs to be heavily reviewed and edited. I do not believe all the information is accurate.

- Singles out AMI name/address resolution services as requiring fault tolerance.  Then recommends that DNS not be used, instead use host based resolution mechanisms.  Then described how to deploy DNS and requires authentication and integrity checking (referring to NIST 800-81).   This section is not at all clear.  Host based name resolution for several million NAN endpoints will not be practical.

#### DHS-2.8.22 Secure Name / Address Resolution Service (Authoritative Source)

###### DHS-2.8.22.2 Supplemental Guidance:

Comments:

- This section needs to be heavily reviewed and edited. I do not believe all the information is accurate.

#### DHS-2.8.23 Secure Name/Address Resolution Service (Recursive or Caching Resolver)

###### DHS-2.8.23.2 Supplemental Guidance:

Comments:

- In reference to the second and third sentences of this section: This needs to be heavily reviewed and edited. I do not believe all the information is accurate.

#### ASAP-2.8.24 Secure Name/Address Resolution Service (Address Resolution Tampering)

Comments:

- I am not sure what this requirement addresses.

###### ASAP-2.8.24.3 Requirement Enhancements:

Comments:

- "ARP spoofing and similar attacks may allow an attack to subvert natural automated network behavior in order to allow the attacker to get "in the middle" of valid communication". Change all to "allow".  Although I don't think I'm entirely clear on "natural automated network behavior" means. Seems like a lot of words for the network structure, or something equally simplistic.

### DHS-2.9 Information and Document Management

#### DHS-2.9.4 Information Classification

Comments:

- Who defines the information classification for the information communicated over the various interfaces?  It seems that at least a base level should be defined so requirements can be defined and controls applied appropriately.

###### DHS-2.9.4.1 Requirement:

Comments:

- I don’t agree that this applies to components.

###### DHS-2.9.4.2 Supplemental Guidance:

Comments:

- Underline the word “components” in the first sentence of this section.

#### DHS-2.9.5 Information Exchange

###### DHS-2.9.5.3 Requirement Enhancements:

Comments:

- Is a component a “device”?

#### DHS-2.9.7 Information and Document Retrieval

###### DHS-2.9.7.1 Requirement:

Comments:

- The first sentence in section DHS-2.9.7.2 (starting with “The organization shall employ appropriate measures”) is a requirement. Move it to this section.

###### DHS-2.9.7.2 Supplemental Guidance:

Comments:

- Move the first sentence of this section to Requirements Section (see comment #1 in DHS-2.9.7.1)

- Relating to the second sentence of this section (starting with “Any legal or regulatory requirements”). Not sure what his has to do with document retrieval.

- Delete the last sentence of the paragraph (starting with “The organization must take special care”).

#### DHS-2.9.8 Information and Document Destruction

###### DHS-2.9.8.1 Requirement:

Comments:

- Move the first sentence in DHS-2.9.8.2 (starting with “The organization shall develop policies and procedures detailing destruction”) to this section.

###### DHS-2.9.8.2 Supplemental Guidance:

Comments:

- Move the first sentence of this section to Requirements Section (see comment #1 in DHS-2.9.8.1)

#### DHS-2.9.9 Information and Document Management Review

###### DHS-2.9.9.1 Requirement:

Comments:

- Move the first sentence in DHS-2.9.8.2 (starting with “The organization shall regularly review compliance”) to this section.

###### DHS-2.9.9.2 Supplemental Guidance:

Comments:

- Move the first sentence of this section to Requirements Section (see comment #1 in DHS-2.9.9.1)

#### DHS-2.9.10 Automated Marking

Comments:

- This is very different from the DHS requirement.  I recommend renaming this is an ASAP requirement and changing the requirement name.

### DHS-2.10 System Development and Maintenance

#### DHS-2.10.1 System Maintenance Policy and Procedures

###### DHS-2.10.1.1 Requirement:

Comments:

- Add “and associated system maintenance controls” to the end of the sentence in the second (#2) item.

###### DHS-2.10.1.2 Supplemental Guidance:

Comments:

- Change “components of the AMI system” to “AMI systems” in the last sentence of this section.

#### DHS-2.10.2 Legacy System Upgrades

###### DHS-2.10.2.1 Requirement:

Comments:

- I believe this requirement should really address the AMI system.  Why are you mandating upgrading all legacy components?

###### DHS-2.10.2.2 Supplemental Guidance:

Comments:

- Change “components” to “systems” in the first sentence of this section.

#### DHS-2.10.3 System Monitoring and Evaluation

###### DHS-2.10.3.1 Requirement:

Comments:

- Why are you updating or replacing all components?

###### DHS-2.10.3.2 Supplemental Guidance:

Comments:

- Change the last sentence of this section to read: “These reviews must be carefully planned and documented in accordance with the organization’s configuration maintenance policies and procedures to identify any changes to the system.”

#### DHS-2.10.4 Backup and Recovery

###### DHS-2.10.4.1 Requirement:

Comments:

- Underline the word “components” in the first and second sentences of this section.

- Where is “reasonable” defined?

###### DHS-2.10.4.2 Supplemental Guidance:

Comments:

- Underline the word “components” in the first and second sentences of this section.

#### DHS-2.10.6 Periodic System Maintenance

###### DHS-2.10.6.1 Requirement:

Comments:

- Why were DHS catalog requirements 2-4 deleted?

###### DHS-2.10.6.3 Requirement Enhancements:

Comments:

- Make this a number list (3 items).

#### ASAP-2.10.7 Field Tools

Comments:

###### Same reference as DHS requirement.  Some of the text is the same – some is different.  Should this have a different number?

###### ASAP-2.10.7.3 Requirement Enhancements:

Comments:

- Why are DHS 1, 4, and 5 not included?

- Relating to list item #2, second part of the sentence (beginning with “if the equipment cannot be sanitized”). Does this really make sense?

- Add item #3 as follows (this is moved from section DHS-2.10.8.2):

“Maintenance personnel shall have appropriate access authorization when maintenance activities allow access to organizational information that could result in a future compromise of availability, integrity, or confidentiality.”

- Add item #4 as follows(this is moved from section DHS-2.10.8.2):

“When maintenance personnel do not have required access authorizations, organizational personnel with appropriate access authorizations shall supervise maintenance personnel during the performance of maintenance activities.”

#### DHS-2.10.8 Maintenance Personnel

###### DHS-2.10.8.1 Requirement:

Comments:

- Add “on the AMI system” to the end of the first sentence.

###### DHS-2.10.8.2 Supplemental Guidance:

Comments:

- Move these items to section DHS-2.10.7.3 (see comments #3, and #4 in DHS-2.10.7.3)

#### DHS-2.10.9 Remote Maintenance

###### DHS-2.10.9.1 Requirement:

Comments:

- Why are 2, 3, and 5 not included?

- Make this a numbered list

- Move the following from DHS-2.10.9.2:

“The use of remote maintenance and diagnostic tools shall be consistent with organizational policy and documented in the security plan. “

“The organization shall maintain records for all remote maintenance and diagnostic activities.”

###### DHS-2.10.9.2 Supplemental Guidance:

Comments:

- Move the last two sentences to DHS-2.10.9.1 (see comment #3 in DHS-2.10.9.2)

###### DHS-2.10.9.3 Requirement Enhancements:

Comments:

- Make this a numbered list.

### DHS-2.12 Incident Response

#### DHS-2.12.1 Incident Response Policy and Procedures

###### DHS-2.12.1.1 Requirement:

Comments:

- Make this a numbered list.

#### DHS-2.12.2 Continuity of Operations Plan

###### DHS-2.12.2.2 Supplemental Guidance:

Comments:

- Change “components of the AMI system” to “AMI system operations”.

###### DHS-2.12.2.3 Requirement Enhancements:

Comments:

- Why is 1 not included?

#### DHS-2.12.4 Incident Response Training

###### DHS-2.12.4.1 Requirement:

Comments:

- Change the beginning of the second sentence from “ The organization provides” to “The organization shall provide”.

###### DHS-2.12.4.3 Requirement Enhancements:

Comments:

- Change this from a “DHS” to an “ASAP” control designation.

- Why are DHS 1 and 2 not included?

#### DHS-2.12.5 Continuity of Operations Plan Testing

###### DHS-2.12.5.1 Requirement:

Comments:

- Move the following from DHS-2.12.5.2 to this section (with minor revisions. i.e. “must” changed to “shall”):

“The organization shall maintain a list of incident response activities and mitigations for the utility and its customers in accordance with the provisions of the organization incident response policy and procedures.”

“Following the preparation of the various plans, a schedule shall be developed to review and test each plan and ensure that each still meets the objectives.”

###### DHS-2.12.5.2 Supplemental Guidance:

Comments:

- Move first and last sentences to DHS-2.12.5.1 (see comment #1 in DHS-2.15.5.1)

###### DHS-2.12.5.3 Requirement Enhancements:

Comments:

- Why are DHS 1, 2, and 3 not included?

#### DHS-2.12.6 Continuity of Operations Plan Update

###### DHS-2.12.6.3 Requirement Enhancements:

Comments:

- Change designation of this control from “DHS” to “ASAP”.

### DHS-2.14 System and Information Integrity

#### DHS-2.14.1 System and Information Integrity Policy and Procedures

###### DHS-2.14.1.1 Requirement:

Comments:

- “Formal” is not consistently used. I don’t see where it adds value and recommend deleting it.

- Move the following sentence of DHS-2.14.1.2:

“The organization shall ensure the system and information integrity policy and procedures are consistent with applicable federal laws, directives, policies, regulations, standards, and guidance.”

###### DHS-2.14.1.2 Supplemental Guidance:

Comments:

- Move the first sentence in this section to DHS-2.14.1.1 (see comment #2 under DHS-2.14.1.1)

- Relating to the last two sentences in this section (beginning with “The system and information integrity policy”). These statements are sometimes included in the policy statements, and sometimes not. It should be consistent throughout this document.

#### DHS-2.14.2 Flaw Remediation

###### DHS-2.14.2.1 Requirement:

Comments:

- What are requirements 2 and 3 from the DHS catalog not included?

- Move the following from DHS-2.14.2.2

“The organization shall identify AMI systems and system components containing software affected by recently announced flaws (and potential vulnerabilities resulting from those flaws).”

“The organization (or the software developer/vendor for software developed and maintained by a vendor/contractor) shall promptly evaluate newly released security-relevant patches, service packs, and hot fixes and tests them for effectiveness and potential impacts on the organization’s AMI system before installation.”

###### DHS-2.14.2.2 Supplemental Guidance:

Comments:

- Move the first two sentences to DHS-2.14.2.1 (see comment #2 under DHS-2.14.2.1).

- What is the specific definition of “flaw”?

#### DHS-2.14.3 Malicious Code Protection

###### DHS-2.14.3.1 Requirement:

Comments:

- Why isn’t requirement 2 from the DHS catalog included?

- Change “must” to “shall”

- Move the following from DHS-2.14.3.2:

“From a system perspective, malicious code protection mechanisms must be deployed in such a manner as to limit the impact of the attack to a small geographical area prior to detection and eradication.

Additionally, what does “to a small geographical area” mean?

###### DHS-2.14.3.2 Supplemental Guidance:

Comments:

- Relating to the paragraph starting with “From a host device perspective. This assumes a specific architecture.

###### DHS-2.14.3.3 Requirement Enhancements:

Comments:

- Why are DHS catalog requirements 1-6 not included.

- Relating to item #2: Why is “centralized managed” necessary?

- Relating to item #3: How is this related to malicious code detection?

- Relating to item #4: How is this related to malicious code detection?

- Relating to items 7-10: Why are these requirements here?

- Relating to item #16.2: How is this done?

- Relating to item #16.3: What does “host hardening” mean?

#### DHS-2.14.4 System Monitoring Tools and Techniques

###### DHS-2.14.4.1 Requirement:

Comments:

- Add DHS catalog requirements 2 and 3.

- Change the sentence from “shall log and report” to “shall detect, log, and report”.

###### DHS-2.14.4.2 Supplemental Guidance:

Comments:

- Change the sentence from “security events” to “security events and anomalies” in the first paragraph.

- Underline the word “components” in the first and third paragraphs.

- Relating to the last sentence of the second paragraph: Do you really want to log all communication events? This could be significant.

###### DHS-2.14.4.3 Requirement Enhancements:

Comments:

- Why were 1-11 from the DHS catalog not included?

- Relating to item #5. Change to read as follows:

“The AMI system component shall provide a mechanism by which accessed, missing and modified logs are detected.”

- SYSLOG “ format” cited.  Is the intent that the AMI system specifically use the full SYSLOG protocol (RFC 3164 is cited)?  DHS-2.16.2.2 also states centralized log management system is required.  Is the intent here that it be SYSLOG?

#### DHS-2.14.5 Security Alerts and Advisories

###### DHS-2.14.5.1 Requirement:

Comments:

- Change the first item to read:

“Receives and/or generates AMI system security alerts/advisories regularly and in response to system-based occurrences;”

- Move the following from DHS-2.14.5.2:

“The organization shall maintain contact with special interest groups (e.g., information security forums) that:

- Facilitate sharing of security-related information (e.g., threats, vulnerabilities, and latest security technologies);

- Provide access to advice from security professionals;

- Improve knowledge of security best practices.”

#### DHS-2.14.6 Security Functionality Verification

###### DHS-2.14.6.1 Requirement:

Comments:

- Not sure what “independently and in concert with the AMI management system” means.

###### DHS-2.14.6.2 Supplemental Guidance:

Comments:

- The first sentence is a killer and seems to do a lot of hand waving and not say much of anything with a lot of words.  I'm not too sure what to offer as a suggestion, but it seems to say "It supports the functions that it does securely". So maybe it should say "The AMI management system should be designed with security in mind, such that AMI devices will require proper security to function"?

###### DHS-2.14.6.3 Requirement Enhancements:

Comments:

- Why were DHS catalog requirement 1 and 2 not included?

- Changed designation for this control from “DHS” to “ASAP”.

#### DHS-2.14.7 Software and Information Integrity

###### DHS-2.14.7.1 Requirement:

Comments:

- Change the first sentence to read:

“The AMI system shall monitor and detect unauthorized changes to software, firmware and data.”

- Move the following from DHS-2.14.7.2 to this section:

“The organization shall employ integrity verification techniques on the AMI system to look for evidence of information tampering, errors, and/or omissions. The organization shall employ good software engineering practices with regard to commercial-off-the-shelf integrity mechanisms (e.g., parity checks, cyclical redundancy checks, cryptographic hashes) and uses tools to automatically monitor the integrity of the IT systems, AMI components, and the applications they host.”

###### DHS-2.14.7.3 Requirement Enhancements:

Comments:

- Why was requirement 4 from the DHS catalog not included?

- Change item 1 to read:

“The organization shall reassess the integrity of software, firmware and data by performing integrity scans of the AMI system;”

#### DHS-2.14.8 Spam Protection

###### DHS-2.14.8.1 Requirement:

Comments:

- Move the following from DHS-2.14.8.2

“The organization shall employ spam protection mechanisms at critical AMI system entry points (e.g., firewalls, electronic mail servers, remote-access servers) and at workstations, servers, and/or mobile computing devices on the network.”

- Specific definition of spam?  Why would email servers be running in the AMI network?  Seems email servers would be restricted to enterprise domain?  Or is the intent that all bogus traffic on the AMI network be indentified and mitigated?

###### DHS-2.14.8.2 Supplemental Guidance:

Comments:

- Relating to the last paragraph in this section (starting with “For an AMI system, the organization should”). This seems to conflict with the previous paragraph.

#### DHS-2.14.10 Information Input Accuracy, Completeness, Validity, and Authenticity

###### DHS-2.14.10.1 Requirement:

Comments:

- Change “must” to “shall” in the first sentence.

###### DHS-2.14.10.2 Supplemental Guidance:

Comments:

- Change designation from “DHS” to “ASAP”.

#### DHS-2.14.11 Error Handling

###### DHS-2.14.11.1 Requirement:

Comments:

- Why were requirements 3 and 4 not included?

###### DHS-2.14.11.2 Supplemental Guidance:

Comments:

- Relating to the last sentence (beginning with “Details AMI system component”). This is requirement 3 from the DHS catalog.

###### ASAP-2.14.11.3 Requirement Enhancements:

Comments:

- Relating to item #1. How does a component perform this?

- Underline “components” in the first item.

### DHS-2.15 Access Control

#### DHS-2.15.1Access Control Policy and Procedures

Comments:

###### This section should reference the domains, components and interfaces from section 4.

###### DHS-2.15.1.1 Requirement:

Comments:

- Change “must” to shall in the paragraph starting with “Access control policies and procedures”.

- Relating to the paragraph starting with “Access control policies and procedures”: This is the first reference to multi-factor authentication. Do you really want to require it?

- Move the following text from DHS-2.15.1.2:

“The organization shall ensure that access control policy and procedures are consistent with applicable federal laws, directives, policies, regulations, standards, and guidance.”

- HAN passes no control to the NAN.  What is specifically meant by “control” and “informational” traffic from the HAN?  For example, I can see a HAN device wanting to read the meter, how is this classified?  This also appears elsewhere in the controls.

###### DHS-2.15.1.2 Supplemental Guidance:

Comments:

- Relating to the paragraph starting with “It is recommended that the access control policy”: Based on the previous requirement, these are really requirements. If so, they should be moved up.

#### DHS-2.15.2 Identification and Authentication Policy and Procedures

###### DHS-2.15.2.1 Requirement:

Comments:

- Where is “strongly” defined?

- Move the following text from DHS-2.15.2.2

“The organization shall ensure the identification and authentication policy and procedures are consistent with applicable federal laws, directives, policies, regulations, standards, and guidance.”

#### DHS-2.15.3 Account Management

###### DHS-2.15.3.1 Requirement:

Comments:

- Why are requirements 1-4 and 7-9 from the DHS catalog not included?

- Change the first sentence to read:

“The organization shall manage AMI system accounts, including authorizing, establishing, activating, modifying, reviewing, disabling, and removing accounts.”

- Move the following text from DHS-2.15.3.2:

“The organization shall identify authorized users of the AMI system and specifies access rights and privileges; i.e., access control list.”

“Intended system use. The organization shall require proper identification for requests to establish AMI system accounts and must approve all such requests. The organization specifically authorizes and monitors the use of guest/anonymous accounts and removes, disables, or otherwise secures unnecessary accounts. The organization ensures that account managers for the AMI system are notified when users are terminated or transferred and associated accounts are removed, disabled, or otherwise secured. Account managers are also notified when users’ AMI system usage or need-to-know/need-to-share changes. In cases where accounts are role-based, i.e., the workstation, hardware, and/or field devices define a user role, access to the AMI system includes physical security policies and procedures based on organization risk assessment. In cases where physical access to the workstation, hardware, and/or field devices predefine privileges, the organization must implement physical security policies, and procedures based on organization risk assessment.”

###### DHS-2.15.3.3 Requirement Enhancements:

Comments:

- Why are requirements 5 and 6 from the DHS catalog not included?

- Relating to the second sentence of list item #1 (starting with “For some AMI components (e.g., field devices”): This is not a requirement.

- Change the list item #2 to read:

“The AMI system must automatically terminate temporary and emergency accounts after a defined time period for each type of account.”

- Change “must” to “Shall” in list item #4.

- Relating to list item #5 (“The organization must ensure default passwords are changed.”): This is listed as a main requirement elsewhere, why is this only an enhancement here?

#### DHS-2.15.4 Identifier Management

###### DHS-2.15.4.1 Requirement:

Comments:

- Move the following text from DHS-2.15.4.2:

“Failure of identification system should not fail to an open unprotected state.  It should fail to a protected, recoverable backup state.”

#### DHS-2.15.5 Authenticator Management

###### DHS-2.15.5.1 Requirement:

Comments:

- Why aren’t requirements 1,3,6,8, and 9 from the DHS catalog included?

- Move the following text from DHS-2.15.5.2:

“Users take reasonable measures to safeguard authenticators including maintaining possession of their individual authenticators, not loaning or sharing authenticators with others, and reporting lost or compromised authenticators immediately.”

“Passwords shall not be embedded into tools, source code, scripts, aliases or shortcuts. Many AMI components and software are shipped with factory default authentication credentials to allow for initial installation and configuration.”

###### DHS-2.15.5.3 Requirement Enhancements:

Comments:

- Change list item #2 under asymmetric/PKI-based authentication to read:

“Enforces authorized access to the corresponding private key;”

#### DHS-2.15.6 Supervision and Review

###### DHS-2.15.6.1 Requirement:

Comments:

- Change designation of this control from “DHS” to “ASAP”

- Change “must” to “shall” in the first sentence of this section.

- Move the following text from DHS-2.15.6.2:

“The organization shall review audit records (e.g., user activity logs) for inappropriate activities in accordance with organizational procedures. The organization shall investigate any unusual AMI system-related activities and periodically review changes to access authorizations. The organization shall review the activities of users with significant roles and responsibilities for the AMI system more frequently.”

“The organization shall have in place policies and procedures that deal specifically with breaches in security, that detail specifically what actions are to occur to secure the breach and investigate any damage. “

###### DHS-2.15.6.3 Requirement Enhancements:

Comments:

- Why are DHS catalog requirements 2-4 not included?

#### DHS-2.15.7 Access Enforcement

###### DHS-2.15.7.1 Requirement:

Comments:

- Change “must” to “shall” in the first sentence of this section.

- Move the following text from DHS-2.15.6.2:

“The organization shall consider the implementation of a controlled, audited, and manual override of automated mechanisms in the event of emergencies or other serious events.”

“The functionality of field tools and other systems which perform managed services shall be limited to the bare minimum to perform the needed task. E-mail and web functions should be removed or limited to access only an approved list. Other applications not required to perform the functions shall be removed.”

###### DHS-2.15.7.3 Requirement Enhancements:

Comments:

- Change “must” to “shall” in list item #2.

- Change “should” to “shall” in list items #2 and #6

#### DHS-2.15.8 Separation of Duties

###### DHS-2.15.8.1 Requirement:

Comments:

- Move the following text from DHS-2.15.8.2:

“Access control software needs to be on the AMI system that prevents users from having all of the necessary authority or information access to perform fraudulent activity without collusion.”

“The organization shall establish appropriate divisions of responsibility and separate duties as needed to eliminate conflicts of interest in the responsibilities and duties of individuals.”

#### DHS-2.15.9 Least Privilege

###### DHS-2.15.9.1 Requirement:

Comments:

- Relating to the fist sentence in this section: Not clear how these restrictions should apply to workstations.

- Move the following text from DHS-2.15.9.2:

“The organization shall employ the concept of least privilege for specific duties and AMI components (including specific ports, protocols, and services) in accordance with risk assessments as necessary to adequately mitigate risk to organizational operations, organizational assets, and individuals.”

#### DHS-2.15.10 User Identification and Authentication

###### DHS-2.15.10.1 Requirement:

Comments:

- Move the following text from DHS-2.15.10.2:

“Users shall be uniquely identified and authenticated for all accesses other than those accesses explicitly identified and documented by the organization in accordance with security control.  Authentication of user identities shall be accomplished through the use of passwords, tokens, biometrics, or in the case of multifactor authentication, some combination of these.”

###### DHS-2.15.10.3 Requirement Enhancements:

Comments:

- Change the sentence in this section to read:

“Remote user access to AMI system components shall only be enabled when necessary, approved, and authenticated.”

#### DHS-2.15.11 Permitted Actions without Identification or Authentication

###### DHS-2.15.11.1 Requirement:

Comments:

- Move the following text from DHS-2.15.11.2:

“The use of anonymous accounts, public accounts, and guest accounts is prohibited.”

“AMI components that perform management services (e.g. Field Tool) shall not be permitted to perform any actions without identification or authentication.”

#### DHS-2.15.12 Device Identification and Authentication

Comments:

###### Shouldn’t identifier management 2.15.4 cover devices as well?

###### DHS-2.15.12.1 Requirement:

Comments:

- Change “must” to “shall” in the first sentence.

- Move the following text from DHS-2.15.12.2 and change “must” to “shall”:

“Field devices shall have the capability to support authentication mechanisms.”

###### DHS-2.15.12.3 Requirement Enhancements:

Comments:

- Why were DHS catalog requirements 1 and 2 not included?

#### DHS-2.15.13 Authenticator Feedback

###### DHS-2.15.13.1 Requirement:

Comments:

- Is “obfuscate” the correct term?

- Move the following text from DHS-2.15.13.2:

“The AMI component/system shall obscure feedback of authentication information during the authentication process (e.g., displaying asterisks when a user types in a password).”

“AMI components involved in authentication shall not at any time pass key or token information in an unencrypted format.”

#### DHS-2.15.14 Cryptographic Module Authentication

###### DHS-2.15.14.1 Requirement:

Comments:

- Relating to the term “must comply with”: What does this mean? Does this mean must be validated to?

###### DHS-2.15.14.3 Requirement Enhancements:

Comments:

- Change “must” to “shall” in this section.

#### DHS-2.15.15 Information Flow Enforcement

###### DHS-2.15.15.3 Requirement Enhancements:

Comments:

- Relating to list item #3: I’m not sure what this requirement means.

#### DHS-2.15.16 Passwords

###### DHS-2.15.16.1 Requirement:

Comments:

- Change the first paragraph of this section to read as follows:

“The organization develops and enforces policies and procedures for control system users concerning the generation and use of passwords. The AMI components that support passwords shall enforce a level of complexity based on the criticality level of the device/system. Default passwords of applications, operating systems, etc must be changed immediately. Passwords shall be changed regularly and systems should enforce an expiration policy based on the criticality level of the AMI component/system. Passwords shall not to be embedded into tools, source code, scripts, aliases or shortcuts.”

- Move all 9 list items from DHS-2.15.16.2 to this section.

#### DHS-2.15.17 System Use Notification

###### DHS-2.15.17.1 Requirement:

Comments:

- Move all text from DHS-2.15.17.2 to this section.

#### DHS-2.15.19 Previous Logon Notification

###### DHS-2.15.19.1 Requirement:

Comments:

- Delete the second paragraph of this section (starting with “The AMI system notifies user”).

#### DHS-2.15.20 Unsuccessful Login Attempts

###### DHS-2.12.20.3 Requirement Enhancements:

Comments:

- Change “must” to “shall”

#### DHS-2.15.22 Remote Session Termination

###### DHS-2.15.22.3 Requirement Enhancements:

Comments:

- Why is this included for remote session termination?

#### DHS-2.15.24 Remote Access

###### DHS-2.15.24.1 Requirement:

Comments:

- Change “must” to “shall”

- Move the following text from DHS-2.15.24.2 to this section:

“The organization shall document, monitor, and manage all methods of remote access (e.g., dialup, Internet, physical) to the AMI system. Appropriate authentication methods are required to adequately secure remote access.”

“The organization shall restrict access achieved through dial-up connections (e.g., limiting dial-up access based upon source of request) or protects against unauthorized connections or subversion of authorized connections (e.g., using virtual private network technology).”

###### DHS-2.15.24.3 Requirement Enhancements:

Comments:

- Why are DHS catalog requirements 5-12 not included?

- Change “encryption” to “cryptography” in list item #2.

#### DHS-2.15.25 Access Control for Portable and Mobile Devices

###### DHS-2.15.25.1 Requirement:

Comments:

- Organizational – Could be modified for field devices, but would take more time.

- Change “must” to “shall”

- Move the following text from DHS-2.15.25.2 to this section:

“Organizations shall disable unused or unnecessary I/O ports.”

#### DHS-2.15.26 Wireless Access Restrictions

Comments:

- Scans should be conducted even if wireless is not deployed.

###### DHS-2.15.26.1 Requirement:

Comments:

- Change “must” to “shall”

- Move the following text from DHS-2.15.26.2 to this section:

“The organization shall use authentication and cryptography or enhanced defense mechanisms to protect wireless access to the AMI system. “

###### DHS-2.15.26.3 Requirement Enhancements:

Comments:

- Change “encryption” to “cryptography”

#### DHS-2.15.27 Personally Owned Information

###### DHS-2.15.27.1 Requirement:

Comments:

- Organizational control.

- Change “must” to “shall”

- Relating to list item #3: What is a personally owned AMI component?

#### DHS-2.15.28 External Access Protections

###### DHS-2.15.28.1 Requirement:

Comments:

- Move the following text from DHS-2.15.28.2:

“The organization shall explicitly allow necessary network protocols in the DMZ; blocks or filters unnecessary protocols, configure firewalls to block inbound connections, limits outbound connections to only those specifically required for operations, and eliminates network connections that bypass perimeter protection mechanisms (e.g. firewall, VPN, DMZ).”

#### DHS-2.15.29 Use of External Information Control Systems

###### DHS-2.15.29.1 Requirement:

Comments:

- Organizational control.

- Move the following text from DHS-2.15.29.3 to list item #3 of this section:

“The organization shall establish terms and conditions for the use of external information systems in accordance with organizational security policies and procedures. The terms and conditions address, as a minimum the types of applications that can be accessed on the organizational information system from the external information system.”

#### ASAP-2.15.30 Unauthorized Access Reporting

###### ASAP-2.15.30.1 Requirement:

Comments:

- Do you really want to log every unsuccessful attempt?

### DHS-2.16 Audit and Accountability

Comments:

- Should NIST SP800-92, “Guide to Computer Security Log Management” be referenced somewhere in this section?

#### DHS-2.16.2 Auditable Events

###### DHS-2.16.2.1 Requirement:

Comments:

- Change “must” to “shall” in the first and second paragraphs.

- Relating to the list of three items: How does this list match 2.15.30?

- Move the following text from DHS-2.16.2.2:

The organization shall specify which AMI system components carry out auditing activities and ensure that certain events are included or excluded from the set of auditable events based on specified attributes.

The organization defines auditable events that are adequate to support after-the-fact investigations of security incidents.

The targeted security functionality shall be able to generate an audit record of:

- Startup and shutdown of the audit functions;

- Successful and failed logins

- Failed authentications of signed or encrypted requests

- Change in access control or privilege

- Changes to security settings

- Creation, deletion, or modifications of users, password, tokens, and security keys

- Triggering of tamper sensors

The organization shall maintain a centralized log management system for long term storage and log correlation. This system shall:

- Provide the capability to compile audit records from multiple components throughout the system into a system wide (logical or physical), time-correlated audit trail.

- Provide the capability to manage the selection of events to be audited by individual components of the system.

- Provide the organization the ability to periodically review and update the list of organization-defined auditable events.

#### DHS-2.16.3 Content of Audit Records

###### DHS-2.16.3.1 Requirement:

Comments:

- Move the following text from DHS-2.16.3.2:

Two types of audits shall be tracked:

- General quality assurance audits of the configuration and operation of the AMI system that verify compliance with organization’s security plan;

- Audits of operational events encountered by the AMI system when the system operates outsides its normal operating parameters.

All AMI components shall provide the capability to include additional, more detailed information in the records for audit events identified by type, location, or subject. All AMI systems and components shall provide the capability to centrally manage the content of audit records generated by individual components throughout the AMI system.

#### DHS-2.16.4 Audit Storage Capacity

###### DHS-2.16.4.1 Requirement:

Comments:

- Not clear what “auditing verbosity” means.

- Relating to the second paragraph: Where is the discussion of “outside normal usage conditions”?

- The time referenced for the Central Log Management System might need to be extended if NERC CIP is applicable in this space. This might need to be increased to a 2 -3 year timeframe.

#### DHS-2.16.5 Response to Audit Processing Failures

###### DHS-2.16.5.1 Requirement:

Comments:

- What is the action taken if one of the events referenced occurs? Definition of “alert”?

#### DHS-2.16.7 Audit Reduction and Report Generation

###### DHS-2.16.7.3 Requirement Enhancements:

Comments:

- Why is requirement 2 from the DHS catalog not included?

#### DHS-2.16.8 Time Stamps

###### DHS-2.16.8.1 Requirement:

Comments:

- Move the following text from DHS-2.16.8.2:

“Time stamps of audit records shall be generated using internal system clocks synchronized across all of the AMI components.”

#### ASAP-2.16.13 Audit Tools

###### ASAP-2.16.13.1 Requirement:

Comments:

- Move the following text from ASAP-2.16.13.2:

“For new AMI components, system auditing utilities shall to be incorporated into the design. Appropriate security audit practices for legacy systems require appropriate precautions be taken before assessing the AMI system. For AMI system audits to determine inappropriate activity, information custodians ensure that AMI system monitoring tools are installed to log system activity and security events.”